## Slide 1
CESG LunaNet Interoperability Spec
(LNIS) v5
Top-Level Issues
CCSDS Feedback
The Hague, Netherlands
27 Nov 2023

## Slide 2: CCSDS Top Level LNIS Issues p. 1 of 3
Maturity
  Document has 5 pages of TBDs many for major aspects of the specification
  Substantial improvement needed to arrive at implementable specifications
End-to-end Architecture
  Document needs an end-to-end architecture or a sufficiently accurate definition of Earth user to LNSP, Space user to LNSP, service interfaces including application, network, link layer, and physical layer features
  Now it only has highly abstract diagrams and physical or link layer details
  Proposed end to end protocol stack diagrams are attached
DTN / IP Interoperability
  Unclear on how to offer DTN, end-to-end, internetworking services and to integrate “islands of IP” using DTN for a long-haul backbone
  Integration of these two different protocol families must be engineered, and the specification is silent on both issues and how it might be handled

## Slide 3: CCSDS Top Level LNIS Issues p. 2 of 3
Inconsistencies
  Scope of LNSP (Earth User to space node, or just in space)
  Scope of services (all in space or end to end)
  Nature of services (single hop, multi-hop, link or network layer security)
  Details of newly offered services vs use of existing ones
Security Features
  Needs a security architecture that specifies how all entities that operate within it will be named, addressed, and identified
  Must address link and network layer security and key management
  Must address
    registration of BP (& LTP) nodes
    IP addresses
    registration of SCID
    spacecraft and node names
    service provider elements and the services that they offer

## Slide 4: CCSDS Top Level LNIS Issues p. 3 of 3
Secure LNSP Interoperability
  Document must clearly specify interoperable and secure interfaces at the boundaries between two separate LNSPs
Use of CCSDS Standards
  References ~13 CCSDS standards at link layer & below, but is missing another 25 essential and useful standards from Applicable Documents
    A key one for rigorous systems architecture descriptions, is the Space Communication Cross Support Architecture Requirements Document (SCCS-ARD), CCSDS 901.1-M-1. updated version in preparation

## Slide 5: Graphical Examples
Example Protocol Stack diagrams for a single LunaNet Service Provider as input for discussion for level of detail that is needed for the LNIS specification
Please note that the boundaries of the LunaNet Service Provider need to be CCSDS compliant to ensure interoperability and cross support, i.e. the Inter-Spacecraft Protocol and the Ground-Ground Protocol.
  The “internals” of the LunaNet Service Provider(relay node and ground station) are shown here also as CCSDS compliant, however – while this is encouraged – it is not mandatory

## Slide 6: LunaNet Service Provider (blue) and User (green) as CCSDS Protocol Stack – Example Forward File Delivery
CCSDS
Inter Spacecraft
Protocols
Terrestrial
WAN
Ground Station
CCSDS Space-Ground
Protocols
X-band
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
S-Band
Prox-1
Bundle Agent (Router/S&F)
BP
USLP
ENCAP
BP
LTP
C & S
USLP
X-band
To
VC X&Z
Space User Node
From
VC Z
USLP
S-Band
Prox-1
Space File Application
BP
CFDP
IP-based Network
Terrestrial
WAN
To
VC X
User File Application
IP
BP
CFDP
TCP
Earth User Node
To
VC Z
User File Application
IP
TCP
BP
CFDP
Space Routing Node MOC
From
VC X
Space File Application
CFDP
CCSDS Ground-Ground Protocols
ENCAP
ENCAP
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
6

## Slide 7: LunaNet Service Provider (blue) and User (green) as CCSDS Protocol Stack – Example Return Message Delivery
CCSDS Inter Spacecraft Protocol
Terrestrial
WAN
Ground Station
CCSDS Ground-Ground
Protocols
X-band
IP
TCP
C & S
SLE - RCF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
S-band
Prox-1
Bundle Agent (Router/S&F)
BP
USLP
ENCAP
BP
LTP
C & S
USLP
X-band
From
VC X&Z
Space User Node
To
VC Z
USLP
S-band
Prox-1
Space Message Application
BP
AMS
IP-based Network
From
VC X
User File Application
IP
BP
CFDP
TCP
Earth User Node
From
VC Z
User Message Application
IP
TCP
BP
AMS
Space Routing Node MOC
To
VC X
Space File Application
CFDP
CCSDS Space-Ground
Protocols
ENCAP
ENCAP
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
7

## Slide 8: CCSDS Proposal
A Joint LNIS/CCSDS in person workshop
In Jan/Feb 2024 timeframe
  Alt. 1: 8 May 2024 after LunaNet Developer’s Forum
  Alt. 2: 3 May 2024 at the end of CCSDS technical meetings
CCSDS has prepared a more detailed comment form, that will be made available after initial discussions