Draft Recommendation for
Space Data System Standards

Voice and Audio Communications

PROPOSED Recommended Standard

CCSDS 766.2-R-0

Red Book

March 2014

AUTHORITY

|  | Issue: | Red Book, Issue 1 |  |
| --- | --- | --- | --- |
|  | Date: | March 2014 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies. The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-3), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

STATEMENT OF INTENT

(WHEN THIS PROPOSED RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members. Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

- Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

- Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

- Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than three years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible. It is the responsibility of each member to determine when such standards or implementations are to be modified. Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

This document is a technical Recommendation for use in determining which voice and audio industry standards should be used for interoperability between spacecraft, astronaut-to-spacecraft, spacecraft-to-ground, ground-to-spacecraft, and ground-to-ground applications. The voice and audio communications described herein are intended for missions that are cross-supported between Agencies of the CCSDS.

The international voice and audio industries have many standards and interfaces for acquiring, recording, and distributing live and recorded audio. That flexibility can lead to complexity when attempting to share or monitor voice or audio from acquisition to monitoring or recording locations. This Recommendation provides system designers with a subset of the larger industry set of standards from which to choose, depending on the application and purpose of the voice system.

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. CCSDS shall not be held responsible for identifying any or all such patent rights.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur. This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-3). Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

Austrian Space Agency (ASA)/Austria.

Belgian Federal Science Policy Office (BFSPO)/Belgium.

Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

China  Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

Chinese Academy of Sciences (CAS)/China.

Chinese Academy of Space Technology (CAST)/China.

Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

Danish National Space Center (DNSC)/Denmark.

Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

European Telecommunications Satellite Organization (EUTELSAT)/Europe.

Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

Hellenic National Space Committee (HNSC)/Greece.

Indian Space Research Organization (ISRO)/India.

Institute of Space Research (IKI)/Russian Federation.

KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

Korea Aerospace Research Institute (KARI)/Korea.

Ministry of Communications (MOC)/Israel.

National Institute of Information and Communications Technology (NICT)/Japan.

National Oceanic and Atmospheric Administration (NOAA)/USA.

National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

National Space Organization (NSPO)/Chinese Taipei.

Naval Center for Space Technology (NCST)/USA.

Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

South African National Space Agency (SANSA)/Republic of South Africa.

Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

Swedish Space Corporation (SSC)/Sweden.

Swiss Space Office (SSO)/Switzerland.

United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard. Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations. However, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 766.2-R-0 | Voice and Audio Communications, Proposed Recommended Standard, Issue 1 | April 2014 | Current draft |

CONTENTS

Section	Page

1	Introduction	1-1

1.1	Purpose	1-1

1.2	Scope	1-1

1.3	Applicability	1-1

1.4	Rationale	1-2

1.5	Document Structure	1-2

1.6	Definitions	1-3

1.6.1	Definitions from G.711	1-3

1.6.2	Terms	1-3

1.6.3	Nomenclature	1-4

1.7	References	1-5

2	Overview	2-1

2.1	Voice Data Exchange	2-1

2.1.2	Transport Technologies	2-2

2.1.3	Protocols Used for Voice Transmission	2-3

2.1.4	CODECS	2-4

2.2	Voice and Audio Communication REQUIREMENTS	2-4

2.3	Voice and Audio Communication Services	2-5

2.3.1	Lip Synchronization (Lip Sync) for Public Affairs	2-5

2.3.2	Voice Recording/Playback	2-5

2.3.3	Voice-to-Text Conversion	2-6

2.4	Voice and Audio Communication Security	2-7

2.5	VOiCE SYSTEM: Parameter Considerations	2-7

3	Case 1: Terrestrial (Ground) Communication Systems	3-1

3.1	Overview	3-1

3.2	Terrestrial Communication Systems within an MCC	3-1

3.2.1	Background	3-1

3.2.2	Discussion: Example of VoIP Implementation	3-2

3.2.3	VoIP Transmission Using IP or PSTN Networks	3-3

3.3	Terrestrial Communication between MCCs	3-4

3.3.1	Discussion	3-4

3.4	Terrestrial Communication between an MCC and External Entities	3-7

3.4.1	Discussion	3-7

3.5	Terrestrial Voice Systems: Recommended Standards	3-7

4	Case 2: Space-to-Ground Voice Systems	4-1

4.1	Discussion	4-1

4.2	Short-distance Voice Communication	4-2

4.2.1	Voice and Audio Data Format Standards	4-2

4.2.2	Voice and Audio Data Transmission	4-2

4.2.3	Voice and Audio Data Formats for Files	4-3

4.3	Long-distance Audio Communication	4-3

4.3.1	Overview	4-3

4.4	Telepresence	4-3

4.5	Space-to-Ground Voice Systems: Recommended Standards	4-3

5	Case 3: Emergency Voice Communication	5-1

5.1	Overview	5-1

5.2	Emergency Voice Communication: Recommended Standards	5-2

6	Case 4: ISS Rendezvous, Proximity, And Docking Operations Voice Communications	6-1

6.1	Overview	6-1

6.1.1	Rendezvous	6-1

6.1.2	Proximity	6-1

6.1.3	Docking	6-1

6.2	Rendezvous, Proximity, and Docking Operations: REcommended Standards	6-1

7	Case 5: Search and Rescue Voice Communications	7-1

7.1	Discussion	7-1

7.1.1	Cospas-Sarsat	7-1

7.1.2	Soyuz Search and Rescue Case Scenario	7-1

7.2	Search and Rescue Voice Communication: Recommended Standards	7-2

Figure

Figure 3-1: Example of Voice Connections between MCCs	3-2

Figure 3-2: IVoDS Functionality Schema inside an MCC and to External Facilities	3-3

Figure 3-3: Example of Voice Connections inside of an MCC	3-4

Table

Table 2-1: Protocols Used for Voice Transmission	2-3

# Introduction

## Purpose

The purpose of this Voice and Audio Communications Proposed Recommended Standard is to specify the technologies, services, and service interfaces for real-time or near real-time voice and audio communications among terrestrial facilities and space systems in support of the mission operations of space flight.

Non-real-time communications are handled by exchange of audio files and are not covered in this Recommendation.

As with any other CCSDS Blue book, this Blue book is written for experts of this particular subject. If more basic explanations of voice communication are needed, please read the corresponding Voice Communications Green book (reference [C1]) or consult a voice expert.

## Scope

This Proposed Recommended Standard presents recommendations for voice and audio data communications in terms of:

- the exchange of voice and audio data between terrestrial facilities;

- the exchange of voice and audio data between terrestrial and space-borne facilities;

- emergency voice communications;

- rendezvous, proximity, and docking operations voice communications;

- search and rescue (SAR) voice communications.

- audio embedded in video feeds and special payload audio are considered a part of cases a) and b).

This recommendation does not specify:

- individual implementations;

- the methods to perform the communication;

- the management activities required to configure and control the voice systems;

## Applicability

This Proposed Recommended Standard applies to any terrestrial and space voice and audio communications systems said to be interoperable through adherence to CCSDS Recommended Standards and for use in mission operations.

This book is heavily oriented to voice communications of manned space missions. Unmanned space missions are less complex than manned ones, and can be seen as a subset of the recommendations needed for human space flight. For this reason in this book the term MCC (Mission Control Center) is used and not the commonly used  MOC (Mission Operations Center) as mentioned in others CCSDS books.

Voice communication is applicable for relatively short distances, spanning at most a planet and its moon(s). For longer distances, audio files exchange should be used.

## Rationale

The goal of this Proposed Recommended Standard is to promote interoperability and development reuse through interagency standardization. By having interoperable and compatible voice systems, intensive testing and voice communications issues can be avoided, thus reducing costs and improving interoperability.

## Document Structure

This document consists of several sections and four annexes:

a)	section 1 presents the purpose, scope, applicability, and rationale of this document and lists the definitions and references used throughout the document;

b)	section 2 provides an overview of voice and audio communications;

c)	section 3 provides requirements for recommended voice and audio data in terrestrial voice systems (ground communication systems);

- section 4 provides requirements for recommended voice and audio data in exchange of voice data between spacecraft and ground systems;

- section 5 provides requirements for recommended voice and audio data in emergency voice communication;

- section 6 provides requirements for recommended voice and audio data in rendezvous, proximity, and docking operations voice communications;

- section 7 provides requirements for recommended voice and audio data in SAR voice communications;

- annexes A–D include a Protocol Implementation Conformance Statement (PICS) proforma, security considerations, a list of acronyms and abbreviations, and a list of informative references.

## Definitions

### Definitions from G.711

This Recommended Standard makes use of the following terms defined in reference [1]:

- A-Law: companding logarithmic algorithm used in Europe and rest of the World. Encodes 13 bits linear Pulse Code Modulation (PCM) samples to logarithmic 8-bit samples. The G.711 encoder will create a 64 kbits/sec bitstream for a signal sampled at 8 KHz. The European system provides more quantization levels at lower signal levels.

- μ-Law: companding logarithm algorithm used in North America and Japan. Encodes 14 bits linear PCM samples to logarithmic 8-bit samples. The G.711 encoder will create a 64 kbits/sec bitstream for a signal sampled at 8 KHz. The North American system tends to give more resolution to higher range signals.

### Terms

A list of acronyms used within this document is provided in annex C. For the purposes of this document, the following definitions apply:

Bandwidth, BW: The bit rate available for data communications expressed in bits per seconds or multiples of it (Kbps, Mbps, Gbps).

encoding: analog-to-digital conversion or compression of digitally represented data.

ENCAP: Encapsulation.

IVoDS: Internet Voice Distribution System.

LDAP: Lightweight Directory Access Protocol.

MCC: Mission Control Center.

Mission Operations Voice Enhancement, MOVE: a NASA project designed to replace existing voice systems utilizing a standardized commercial off-the-shelf approach.

MOC: Mission Operations Center.

NOTE	–	This book uses MCC because is the term used for human space flight. MOC is used primarily for satellite missions and is thus used in many CCSDS books.

PDH: Plesiochronous Digital Hierarchy. Network technology for moving large amounts of data between systems that have independent clocks.

Packet Switched Network, PSN:  A common technology used in telecommunications to transport large amounts of data over digital networks.

Pseudowire, PW: emulates a point-to-point connection over a packet switching network.

Quality of Experience, QoE or QX: the subjective measure of a user experience with a service, in this case a space mission voice system.

Quality of Service, QoS: ability of a communication system to provide predictable and differentiated services.

Quindars: the ‘beeps’ heard intermittently during space-to-ground voice communications in space missions. It was originally used by the Apollo missions to indicate the in-band signaling used to simulate Push-To-Talk (PTT) buttons.

S/G: Space-to-Ground

Summation: the mixing of multiple voice sources into a single conference loop.

Voice Format: a collection of voice loops grouped together to meet the requirements of a particular situation or mode of operation. Voice formats are typically negotiated between two MCCs to prioritize loop connectivity to best match communication needs with the available channels.

NOTE	–	Because in each MCC there are many more internal voice loops than available circuits to transport the voice loops between the MCCs, different operations modes  must be defined by different voice formats. Each format contains a limited number of voice loops matched to the available channels for a specific operational aspect between MCCs. These formats are interchangeable and really dynamic; they need to be clearly defined between MCCs. Examples of voice formats are Joint Simulation and System Test Format. It is extremely important to reserve a number of channels in each format to maintain normal operations during a test or simulation.

### Nomenclature

#### Normative Text

The following conventions apply for the normative specifications in this document:

a)	the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

b)	the word ‘should’ implies an optional, but desirable, specification;

c)	the word ‘may’ implies an optional specification;

d)	the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

#### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

–	Overview;

–	Background;

–	Rationale;

–	Discussion.

## References

The following publications contain provisions which, through reference in this text, constitute provisions of this document. At the time of publication, the editions indicated were valid. All publications are subject to revision, and users of this Proposed Recommended Standard are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below. The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Pulse Code Modulation (PCM) of Voice Frequencies. G.711. International Telecommunication Union-Telecommunication Standardization Sector (ITU-T), November 1988.

[2]	Standard for Telecommunications—Network-to-Customer Installation. ANSI T1.403-1989. ANSI, 1989.

[3]	Synchronous Frame Structures Used at 1544, 6312, 2048, 8448 and 44 736 kbit/s Hierarchical Levels. G.704. ITU-T, October 1998 and Characteristics of Primary PCM Multiplex Equipment Operating at 2048 kbit/s. G.732. ITU-T, November 1988.

[4]	Coding of Speech at 8 kbit/s Using Conjugate-Structure Algebraic-Code-Excited-Linear Prediction (CS-ACELP). G.729. ITU-T, June 2012.

[5]	J. Postel. User Data Diagram Protocol (UDP). RFC 768. ISI, August 1980.

[6]	H. Schulzrinne, et al. RTP: A Transport Protocol for Real-Time Applications. RFC 3550. ISOC, July 2003.

[7]	M. Baugher, et al. The Secure Real-time Transport Protocol (SRTP). RFC 3711. ISOC, March 2004.

[8]	V. Cerf, Y. Dalal, and C. Sunshine. Specification of Internet Transmission Control Program. RFC 675. December 1974.

[9]	J. Rosenberg, et al. SIP: Session Initiation Protocol. RFC 3261. ISOC, June 2002.

[10]	Packet-based Multimedia Communications Systems. H.323. ITU-T, December 2009.

[11]	F. Andreasen and B. Foster. Media Gateway Control Protocol (MGCP). RFC 3435. ISOC, January 2003.

[12]	N. Greene, et al. Media Gateway Control Protocol Architecture and Requirements. RFC 2805. ISOC, April 2000.

[13]	Coding of Speech at 16 kbit/s Using Low-delay Code Excited Linear Prediction. G.728. ITU-T, June 2012.

[14]	Information Technology—Generic Coding of Moving Pictures and Associated Audio Information—Part 7: Advanced Audio Coding (AAC). International Standard, ISO/IEC 13818-7:2006. 4th ed. Geneva: ISO, 2006.

[15]	Information Technology—Coding of Audio-Visual Objects—Part 3: Audio. International Standard, ISO/IEC 14496-3:2009. 4th ed. Geneva: ISO, 2009.

[16]	IP over CCSDS Space Links. Recommendation for Space Data System Practices, CCSDS 702.1-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, September 2012.

[17]	CCSDS File Delivery Protocol (CFDP). Recommendation for Space Data System Standards, CCSDS 727.0-B-4. Blue Book. Issue 4. Washington, D.C.: CCSDS, January 2007.

[18]	Licklider Transmission Protocol (LTP) for CCSDS. Draft Recommendation for Space Data System Standards, CCSDS 734.1-R-2. Draft Blue Book. Issue 2. Washington, D.C.: CCSDS, forthcoming.

[19]	CCSDS Bundle Protocol Specification. Draft Recommendation for Space Data System Standards, CCSDS 734.2-R-2. Draft Blue Book. Issue 2. Washington, D.C.: CCSDS, forthcoming.

[20]	Proximity-1 Space Link Protocol—Physical Layer. Recommendation for Space Data System Standards, CCSDS 211.1-B-4. Blue Book. Issue 4. Washington, D.C.: CCSDS, December 2013.

[21]	Proximity-1 Space Link Protocol—Data Link Layer. Recommendation for Space Data System Standards, CCSDS 211.0-B-5. Blue Book. Issue 5. Washington, D.C.: CCSDS, December 2013.

[22]	Proximity-1 Space Link Protocol—Coding and Synchronization Sublayer. Recommendation for Space Data System Standards, CCSDS 211.2-B-2. Blue Book. Issue 2. Washington, D.C.: CCSDS, December 2013.

[23]	Information Technology—Open Systems Interconnection—The Directory: Public-key and attribute certificate frameworks. International Standard, ISO/IEC 9594-8:2008. 6th ed. Geneva: ISO, 2008-2014.

[24]  AOS Space Data Link Protocol. Recommendation for Space Data System Standards, CCSDS 732.0-B-2.

[25]	Television—SDTV Digital Signal/Data—Serial Digital Interface.  SMPTE ST 259:2008.  White Plains, New York: SMPTE, 2008.

[26]	Digital Interfaces for HDTV Studio Signals.  ITU-R BT.1120-8.  Geneva: ITU, 2012.

# Overview

Voice and audio communications in space missions serve all the supporting personnel as well as the astronauts. The astronauts live and work in various space facilities developed and launched by different countries. The supporting personnel belong to different agencies and private companies as well. For mission safety and success, interoperability of voice communications is crucial. For purposes of this document, the following descriptions apply:

- voice is defined as the transport of human voice using low BW resources for transmission (typically 300-3000Hz);

- audio may contain human voice, experiments’ noises, sounds, or music, all of which need more quality and more BW to be transmitted (typically 20-20kHz);

- audio files either may contain recorded human voice or any kind of audio. Because they are files, they are transmitted like any other files, using file transfer standards.

## Voice Data Exchange

Voice communications was once the realm of analog technology; now voice is encoded and exchanged in digital form. This Proposed Recommended Standard discusses exchange of voice data in five challenging domains, presented here as cases, that are applicable to internationally interoperable mission voice communications. The five cases defined in this book are the exchange of voice and audio data in the following situations:

- between different terrestrial facilities;

- between terrestrial and space-borne facilities;

- for emergency voice communications;

- for rendezvous, proximity, and docking operations;

- for SAR voice communications.

The exchange of voice data between ground-based personnel working in space missions can be achieved by commercial telecom services such as leased circuits like PDH (E1/T1) (references [2], [3]) or Voice over Internet Protocol (VoIP). Both technologies either can be combined inside and outside of an MCC, or they can be used for terrestrial or other kinds of communications as described in the five cases presented in this book. Carriers on the ground can use Multi-Protocol Label Switching (MPLS), Asynchronous Transfer Mode (ATM), or Integrated Services Digital Network (ISDN); however, current international communications are increasingly migrating to MPLS.

When VoIP is used, the originating voice codec should be maintained through network links. An example would be IP/UDP/RTP/G.711 or IP/UDP/RTP/G.729.

If real-time voice communications either are impossible or not needed, audio files should be exchanged using file transfer such as File Transfer Protocol (FTP), CCSDS File Delivery Protocol (CFDP [17]) over Delay-Tolerant Networking (DTN), or other approved standards.

CFDP supports two classes. Each of the classes can be supported over the DTN Bundle Protocol (reference [19]) and DTN Licklider Transport Protocol (LTP) (reference [18]).

- Class 1—Unreliable CFDP Transfer (if over reliable DTN "UT layer" stack);

- Class 2—Reliable CFDP Transfer (if over unreliable DTN "UT layer" stack);

#### DTN

There are three classes or modes of voice and audio transmission under DTN:

- Mode 1 – Real Time Delivery, Best Effort;

- Mode 2 – Delayed Delivery, With Packet Restoration.

- Mode 3 – Reassembly with best-effort real time delivery.

Annex C presents a narrative of the classes of real-time voice transmission still under development by the DTN working group.

### Transport Technologies

Digital voice is transported using packets (VoIP) or frames (E1/T1). For ground communications there are currently two major possibilities: using DTM with E1/T1 interfaces or VoIP (over E1/T1 or Internet). These technology options are described here:

- Time Division Multiplexing (TDM): Each voice sample time slot in the TDM frame is called a ‘channel’. In European systems, TDM frames contain 30 digital voice channels (E1); in American/Japanese systems, the frames contain 24 channels (T1). Both standards (E1/T1) also contain extra bits (or bit time slots) for signaling and synchronization bits.

  - TDM using PDH is still the more commonly used technology to transport voice  with E1/T1 carriers (references [2], [3]).

  - TDM over Internet Protocol (TDMoIP) is the emulation of TDM over a PSN. TDMoIP is a type of pseudowire.

- VoIP is the emerging technology for new voice systems. VoIP can run over Internet or over dedicated networks (see next section).

- S/G Voice communication primarily uses Radio Frequency (RF) links, with different frequencies (S-band, Ku-band, and Ultra High Frequency [UHF]).

### Protocols Used for Voice Transmission

Depending of which kind of voice system will be implemented in the control center and the system’s functionality, one or a combination of the following protocols shown in table 2-1shall be used.

Table 2-1: Protocols Used for Voice Transmission

| Protocol | Notes | Where Defined | Ref # |
| --- | --- | --- | --- |
| UDP (User Datagram Protocol) | None. | RFC 768 (STD 6) | [5] |
| RTP (Real-time Transport Protocol) | RTP is used for MCC and space communications. | RFC 3550 (STD 64) | [6] |
| RTCP (Real-time Control Protocol) | RTCP’s primary function is to provide feedback on the QoS. | RFC 3550 (STD 64) | [6] |
| SRTP (Secure Real-time Transport Protocol) | SRTP has a sister protocol called Secure RTCP (SRTCP) | ECP 3711 | [7] |
| TCP/IP (Transmission Control Protocol/Internet Protocol) | TCP/IP is appropriate for exchange of audio files. TCP/IP is NOT recommended for voice communications. | RFC 675 | [8] |
| E1/T1 | E1/T1 protocols support 30 (E1) or 24 (T1) digital channels simultaneously using TDM. | ANSI T1 ITU-T G.704/G.732 | [2], [3] |
| VoIP Signaling Protocols |  |  |  |
| Session Control Protocols | Session Initiation Protocol (SIP) | SIP is designed to serve VoIP services over Internet Protocol (IP). SIP is an Application-Layer protocol that can operate over UDP or TCP. SIP is currently (2014) at version 2. | RFC 3261 | [9] |
|  | H.323 | H.323 is an ITU-T recommendation for call signaling and control, multimedia transport and control, and BW control for point-to-point and multi-point conferences for any packet network. | ITU-T H.323 | [10] |
| Media Control Protocols | Media Gateway Control Protocol (MGCP) | MGCP is one implementation for controlling media gateways on IP networks and the Public Switched Telephone Network (PSTN). | RFC 3435 | [11] |
|  | Megaco (H.248) | H.248 follows the guidelines of the Application Programming Interface (API) MGCP architecture and requirements described in RFC 2805. | RFC 2805 | [12] |

### CODECS

#### G.711

G.711 (reference [1]) is also known as PCM (pulse code modulation). It is an ITU-T standard that uses lossless data compression to reduce BW usage. G.711 maintains full audio quality at a relative high BW compared to other codecs. G.711 uses µ-law North America and Japan, and A-law in other countries. It uses 64 kbits/s bitrate (8 KHz sampling frequency x 8 bits per sample).

If there are no BW limitations, G.711 should be used for communications between MCCs or for S/G communications.

#### G.728

G.728 (reference [13]) is an ITU-T standard operating at 16 kbits/s. It is a low-delay codec with linear prediction and low BW and is used commonly for communication between spacecraft, or S/G with low BW (like S-band).

#### G.729

G.729 (reference [4]) is an ITU-T standard providing an audio data compression algorithm for voice that compresses digital voice in packets of 10 msec duration. It is mostly used in VoIP and operates at a bit rate of 8 kbits/s.

## Voice and Audio Communication REQUIREMENTS

Voice communication is the exchange of voice and audio data between different users. During a human space flight mission, a voice communication system should provide the following:

- point-to-point voice communication;

- voice loop or voice conference (These are implemented by voice summation, which is the mixing of multiple voice sources into a single conference [voice] loop);

- voice switch (or voice matrix);

- voice recording and playback of audio files in a standard format such as Advance Audio Coding (AAC) (reference [14]);

- voice/text conversion;

- keysets.

NOTE	–	A keyset provides capabilities for selection of loops, as well as for audio input and output. Interaction with the keyset for loop selection is usually a physical interaction by pressing buttons. The interaction components of the device may be dedicated hardware buttons for each loop, or a software user interface shown as a touchscreen. Physical interaction is preferred for higher user awareness. For actual audio input, the physical interaction is done by actively pressing a PTT button to activate the microphone of the keyset for transmission of the voice signals to the selected loop. The keyset may be either an integrated or multipiece separated unit, or it can be a software application (soft keyset). The complete device will be called a keyset and provide all necessary functionality for end-user interaction with the voice conferencing core.

## Voice and Audio Communication Services

### Lip Synchronization (Lip Sync) for Public Affairs

For public-relations events, an external facility communicates with the astronauts in space. The voice path normally uses S-band, and video uses Ku-band. The paths are different and need to be synchronized.

The final synchronization is  done manually. The astronauts and the MCC test the whole path a few minutes before the event starts. The video personnel on the ground synchronize the video with the audio using the predefined values of the encoders. The personnel then either add or subtract steps of 10 milliseconds at a time to the encoder configuration until the lips are synchronized with the audio.

An automatic lip sync can be made possible if timestamps are used in the video and voice systems; however, this requires special equipment. Ideally, the synchronization of the video and audio should be done onboard and sent embedded from space.

Some of the new cameras are already using embedded audio (HD-SDI or SD-SDI) on the ISS.

### Voice Recording/Playback

Voice recording and playback are an essential part of space missions. Classic uses of recording are to store voice data for post analysis during failure investigation, for reconstruction of issues, for public relations activities, and for training purposes. A common use is short-term playback of unclear communication to avoid misunderstandings and frequent repetition over the channels.

Based on the use cases, three different types of recording are used: user-specific recording, loop-specific recording, and interface-specific recording.

#### User-specific Recording (Keyset Recording)

User-specific/keyset recording is the sum of all audio traffic for a specific user and is dependent on the user’s loop selection. User-specific recording represents the presence of all audio signals at a user position.

Keyset recording and playback of a user position is used for a short time span only. In this way a user is able to replay the last minutes of all audio arriving at the keyset. It is mainly used for replays of unclear communication.

#### Loop-specific Recording (Loop Recording)

Loop recording is defined as the sum of all audio traffic for a specific loop. It is user independent. Loop recording represents the presence of an audio signal within a loop.

Loop recording is the most common recording for space mission operations. All audio of a loop is stored separately within the recording system. This way, loop-specific investigations are possible (e.g., dialog between different positions).

Loop recording is very demanding in terms of storage capacity and correct time-tagging to allow replays of specific events based on a given time span.

#### Interface-specific Recording (Interface Recording)

Interface recording represents the presence of an audio signal at an interface and is able to identify the direction of the signal (outgoing/incoming)

Interface recording is a technical support recording to verify audio sources within loops. It is aligned to loop assignments of channels.

Interface recording is mainly used to identify failure sources such as noise bursts within a loop, open microphone conditions, or other audible misalignments.

### Voice-to-Text Conversion

Voice-to-text, also known as Automatic Speech Recognition (ASR) or text-to-speech (TTS), is nowadays a standard application for many smartphones, browsers, cars, and dictation devices.

When long transmission time becomes an issue, voice-to-text software should be considered; voice should be converted to text and sent to the MCC as an audio file. The reply could be sent in the same way and could optionally be converted back to voice.

NOTE	–	There are several voice-to-text and TTS software products available. Product selection is beyond the scope of this book.

## Voice and Audio Communication Security

Security concerns in voice and audio communication are voice privacy, audio data integrity, and source authentication:

- Voice privacy means that the voice loop should not be heard by any other than the intended recipient(s). It can be achieved by employing protected data transport at lower layers, restricting distribution, or using cryptographic techniques.

- Audio data integrity means that the content of the audio/voice should not be altered.

- Source authentication is the requirement that the audio should be attributable to a known origin. It can be achieved together with the privacy implementation.

A detailed description is found in annex B: Security Considerations.

## VOiCE SYSTEM: Parameter Considerations

Voice communication and audio data exchange are essential services for supporting space mission operations. They are especially important in a cooperative international environment in human space flight programs like the International Space Station (ISS). Between humans, one of the most common information exchanges is voice communication. In human space flight, the primary function of voice communication is to support the mission executed by astronauts, cosmonauts, taikonauts, and other space travelers.

This document describes the setup of voice communication in a space mission context, points out special requirements and operational approaches, and defines the transmission, coding, interface, and quality parameters needed for space mission support.

Different parameters are required for each of the five voice communication cases defined in this book. Each of the five cases presented in this document identifies the parameters applicable to the case being presented. In some cases only some parameters are applicable. Best-practice recommendations are presented in normative text.

The following parameters must be taken into account in the definition and implementation of a voice system:

- packet-switched versus circuit-switched systems (the current tendency is to use packet-switched systems);

- users and permissions associated with the login (e.g., the roles Talk/Listen/Monitor [T/L/M]);

- voice formats and activation procedures, a common case when more voice loops are needed than available circuits to transmit them;

NOTE	- voice formats must be clearly defined and agreed in advance between the MCCs. Voice loops changes into a format is a dynamic task, a good coordination is mandatory.

- PTT;

- codecs selections and settings (including lossless, lossy, and eventually effects of packet drops);

- minimization of codec conversions;

- synchronization;

- latency requirements (e.g., 10 to 200 msec for VoIP systems inside of one control room);

NOTE	–	The latency requirements for a system running inside of a control room must be as low as possible. For systems communicating with external locations or different rooms inside of a facility, it is not a problem to have a higher latency.

- frequencies and channelization;

- signaling; CAS (Channel Associated Signaling) or CCS (Common Channel Signaling).

- voice encryption and voice private channel setup.

- quality monitoring (Depending on the case, QoS and/or QoE will be needed. If the Internet is used for the voice transmission, quality cannot be guaranteed.);

- etiquette and protocol (roles and positions to talk);

- alternative methods (consider secondary paths such as IP telephony—e.g., Skype, VSee—in the ISS for voice conference which use different protocols and etiquette).

# Case 1: Terrestrial (Ground) Communication Systems

## Overview

Terrestrial communication systems can be divided into three cases:

- within an MCC;

- between MCCs;

- between an MCC and other external entities.

## Terrestrial Communication Systems within an MCC

### Background

The voice system in an MCC uses a dedicated system, with dedicated network lines, and high availability. This assures a high voice quality, very high reliability of the communications, and good overview and control over the system functionality. All of these features make the MCC voice system a unique application.

MCCs employ centralized, high-performance, fault-tolerant, and high-capacity voice conference systems to provide voice communications for flight operations and support personnel. The required level of performance is typically achieved through dedicated TDM-based systems or loop-based systems connected to keysets located in flight-control and support rooms. E1/T1 provides the necessary interface to other MCCs for voice communications.

The following context diagram (figure 3-1) illustrates E1/T1, Private Automated Branch Exchange (PABX), VoIP, and analog connections between different MCCs. Keysets are connected internally via T1 or VoIP interfaces.

As mentioned in section 2.1.1, the current development of the technology is moving toward VoIP. In many systems there is a combination of VoIP (for internal distribution in an MCC) and E1/T1 interfaces for external or internal distribution, or a combination of VoIP for external keysets as well.

The advantages of VoIP are the low infrastructure and network costs. The disadvantage is the quality of service.

Figure 3-1: Example of Voice Connections inside of an MCC

Figure 3-1 shows a voice system inside an MCC having a PDH switch and a VoIP one, with the connections to the external world.

### Discussion: Example of VoIP Implementation

An example of a VoIP implementation is the NASA Marshall Space Flight Center’s (MSFC’s) use of the Local Internet Voice Distribution System (Local IVoDS or LVoDS).

IVoDS is based on a conference server/gateway server concept. The conference server contains the user loop configuration database (voice groups). Once authenticated with a conference server, users can monitor/talk (based on user permissions) within the loops for which they are privileged.

The conference servers are affiliated with gateway servers, which provide a matrix of voice transport circuit channels (e.g., E1/T1), accept multiple TDM circuits, and break down the voice channels for conference access.

IVoDS is scalable based on voice transport circuit quantity/type (gateway), as well as soft client quantity (conference). IVoDS is also scalable so as to be capable of providing fault-tolerant voice services for the real-time flight control team within the MCC.

IVoDS authentication is compatible with two-factor authentication, as well as X.500 management (reference [23]). IVoDS provides encrypted sessions between client and server, although it can be configured to operate unencrypted. Additionally, traditional network techniques such as access control lists and Virtual Private Network (VPN) can be used to better protect voice access to the required level.

Figure 3-2 shows the configuration schema of IVoDS and LVoDS in the next page.

### VoIP Transmission Using IP or PSTN Networks

VoIP can be transmitted using IP or PSTN networks. For this communication technology, some extra considerations must be taken into account:

Security concerns, including authentication and authorization, must be addressed, especially for remote access. X.500 (reference [23])/LDAP authentication, firewall border control, VPN access, and/or two-factor authentication may be required.

Soft switch is typically used to control connections at the interface between circuit-switched and packet-switched networks.

NOTE	–	Soft switch is a cheaper compared to a standard gateway, but  has the disadvantages of requiring software running on a computer.

Media Proxy is a media relay for RTP/RTCP and UDP streams that work in tandem with OpenSIP to provide Network Address Translation (NAT) traversal capability for media streams from SIP user agents located behind a NAT.

NOTE	–	The disadvantage is that peer-to-peer applications like VoIP have severe problems working behind a NAT.

Encryption between the external client and the MCC should be included in the VoIP switch.

Figure 3-2: IVoDS Functionality Schema inside an MCC and to External Facilities

## Terrestrial Communication between MCCs

### Discussion

There are different voice system transport media that can carry the audio signals and audio files between the different MCCs. These transport media could be MPLS, IP, and / or satellite links:

- MPLS is an efficient and cheap network technology (e.g., leased line or commercial carrier). It is widely used, but has some problems for voice transmission:

- Interruptions in the voice system for several seconds must be accepted. Interruptions can be produced due to the rerouting generated when a big company is connected to the network or important maintenance takes place somewhere in the world. In spite of the best class (voice class) being used, these problems can cause interruptions up to 30 seconds. This is an important factor, as the applications must be more robust in order to survive these ‘normal’ issues.

- Clocking can be an issue and should be taken into account.

- IP: IPv4 and IPv6 protocols work quite well inside of the MPLS network, having the same mentioned limitations. Public Internet can also be used; it works well but does not provide QoS.

- Satellite links are occasionally used for transmission of compressed voice data (e.g. IP [16] over satellite links).

Figure 3-3: Example of Voice Connections between MCCs

## Terrestrial Communication between an MCC and External Entities

### Discussion

In many cases temporary voice loops are needed for some tests, public relations events, or special work with external facilities. In most of the systems it is possible to patch one or more phones into a voice loop (or several loops) to establish external communication.

An example of an extension of an MCC to external entity is the Remote IVoDS system. Remote IVoDS provides a complete voice package for end users (e.g., universities) via any available IP-supported network (e.g., the Internet) and an MCC circuit matrix as shown in figure 3-2.

There are other similar applications like external soft keysets connected to the MCC via the Internet. Due to the many communications problems of soft keysets, like stability issues, loss of connection, re-login due to unexpected disconnections, they are NOT recommended to use them for real-time operations.

PSTN dial-in is used widely for public relations events, especially when the event takes place outside of the closed voice system. Normally the user makes a phone call to a number on a PABX and the call is patched to a voice loop. In those cases there are several clasic problems:

a)	the user does not have PTT capabilities: the device can be a microphone or black phone (hardwired telephony communications);

b)	the user does not have experience/training/etiquette to talk in a voice loop;

c)	in communication using video, lip synchronization must be included.

Another possibility is to use a mobile phone to call a gateway, and with a passcode, access some voice loops from the mobile phone.

As a general definition a POTS (Plain Old Telephone System) should be used.

## Terrestrial Voice Systems: Recommended Standards

A packet-switched network (MPLS/IP) should be used, in spite of the communication problems (packet loss).

NOTE	–	The quality is good enough and the costs considerably lower than circuit-switched alternatives or dedicated lines (e.g. ISDN).

A well-considered schema for restricting access and roles (T/L/M) for various voice loops should be defined in advance. X.500 (e.g., LDAP) authentication should be used.

NOTE	–	Maintaining appropriate access controls can be quite labor intensive since the user information and role assignment can be very dynamic.

Voice format changes for different activities (e.g Mission, test or simulations) must be well defined and agreed upon in advance between the MCCs.

PTT should be implemented in all kinds of keysets (manual or automatic). If VOX (Voice Level Detection or Voice Activity Level or Voice Operated eXchange) is used, enough time shall be expended to have a reliable configuration of the VOX tested with different users.

NOTE	–	PTT can be implemented physically via a button or pedal, or via VOX, where the voice level is monitored and the PTT is activated automatically.

G.711 should be used for communications between MCCs or S/G if there are not BW limitations.

The codec shall not be changed during the transition through network links. Lossy voice codecs should be employed carefully, and voice encoding should occur only once (ideally) between end points; multiple encode/decode cycles significantly affect voice quality and add latency.

NOTE	–	Examples of a protocol and codec stack would be IP/UDP/RTP/G.711 from end to end or IP/UDP/RTP/G.729 from end to end.

Synchronization: The clocking between the MCC voice systems must be well synchronized.

NOTE	–	Jitter and latency should both be, less than 200 msec. If not a clock fallback solution should be implemented .

Latency: There shall be no more than 10 msec latency for communications inside of a control room and 200 msec for connections to other rooms or facilities.

Channelization shall be used to refer to which loop is assigned to which channel, e.g., S/G to Flight Director (FD). Enough time shall be invested in the definition of channels between the MCCs.

Signaling: In analog systems signaling is always present. In digital systems an open line may be used without signaling, but for important loops like S/G, signaling is required. Important channels and signaling requirements should be defined between MCCs. CAS  signaling which is often called “robbed bit” in the America’s on the T1’s and CCS signaling for the PABX.

Voice recording shall be used for important loops in an MCC.

NOTE	–	Voice recording is mandatory in human space missions.

Lip sync equipment shall be used for public relations events.

Timestamps should be used in the video and voice systems if possible to enable an automatic lip sync (requires special equipment).

Video and audio should be sent embedded (HD-SDI[26]) from space and synchronized onboard if possible.

VoIP technology should be used for new system development and connectivity in line with industry trends.

High-performance voice conferencing systems using TDM with G.711 µ-law or A-law voice encoding shall be used in an MCC.

Voice quality should not be sacrificed in deference to BW usage. End-to-end configuration must be considered (e.g., use G.729 instead of G.711).

Voice encryption should be implemented if VoIP is used.

If E1/T1 or MPLS are used, even though the data are encrypted over the external network, encryption shall be used for the internal network.

Voice channel privatization may be required for medical-related communications or for astronauts’ family loops also called PFC (Private family conference).

Quality monitoring should be used, either QoS or QoE, depending on the case.

NOTE	–	If Internet is used (VoIP) for the voice transmission, quality cannot be guaranteed. In either case, a voice recorder is needed as described in section 2.3.2

Users shall follow a clear and well-defined etiquette and protocol (roles and positions to talk) and shall receive etiquette and protocol training.

Cisco IP telephony is used by most of the space agencies and should be used for IP telephony.

VSee video conference and screen share software shall be used for secure video chat.

Soft keysets should not be used for real-time operations with an MCC.

Recorded audio shall be transmitted as files.

Redundancy of the network and voice system (matrix or switch) should be implemented for voice communications between MCCs.

# Case 2: Space-to-Ground Voice Systems

## Discussion

Within the frame of manned space flight missions, voice communication is the most important part among all types of S/G communications. Voice is considered mission critical.

There are two types of S/G communications: short-distance communications, and long-distance communications.

- Short-distance communications are confined to the Earth/Moon or other planetary systems. A short-distance voice communication system implies real-time communications and the use of S/G voice loops.

- Long-distance communications include interplanetary or deep-space communications. As distance imposes communication delays beyond approximately 30 seconds, file transfer may be used rather than real-time communication.

The exchange of voice and audio communications between vehicles in space and Earth-bound control centers necessarily involves satellites and ground stations as well as the space and deep-space networks. S/G voice communications uses the following assets:

- Voice communication primarily uses Radio Frequency (RF) links, with different frequencies (S-band, Ku-band, and Ultra High Frequency [UHF]).

- During launch, the Soyuz vehicle uses VHF1 to communicate to MCC-Moscow (MCC-M): Uplink: 130.167 MHz; Downlink: 121.750 MHz for communications to the ISS and S/G, the VHF2 is used for docking operations for direct communications to the ISS.

- Zhengzhou uses similar systems to Soyuz vehicle.

- Space X uses G.729 for communications between ISS and the Dragon capsule. It also uses RF links for S/G communications.

- Other vehicles like ATV, HTV, Progress or Cygnus  (are not manned and have only extensions of the ISS voice system when they are docked to the station).

- For Extra Vehicular Activities (EVA), UHF (414.2 MHz) is used with a direct link to the spacecraft. The communication to the Earth uses the spacecraft’s system, which is usually S-band.

- On the ISS, Internet is available over the Ku-band. Various Internet applications can be used by the astronauts. The connection uses Tracking and Data Relay Satellite System (TDRSS).

- The voice loops S/G 1 and 2 use Modified Residual Excited Linear Predictive Coding, a proprietary Motorola Protocol (via S-band). The new S/G loops, like 3 and 4, use G.729 (via Ku-band).

## Short-distance Voice Communication

### Voice and Audio Data Format Standards

For voice and audio data formats, one of the following standards should be used:

- ITU-T G.729/G.729A;

- ITU-T G.711;

- AAC: ISO/IEC 13818-7 or ISO/IEC 14496-3 (references [14], [15]).

G.729/G.729A may be used in all kinds of ground-to-space communication links, while G.711 and AAC shall be used in the communication links with adequate BW availability.

AAC may be used if high-quality audio transmission is required in real-time voice communication.

AAC uses variable bit rates from 8 kbit/s to 529 kbit/s depending on the BW limitations of the communication link between ground and spacecraft. For good voice and audio quality, at least 128 kbit/s should be used.

### Voice and Audio Data Transmission

#### Overview

Short-distance transmission mechanisms for voice and audio data between ground and spacecraft include voice over CCSDS data links and VoIP.

#### Voice over CCSDS Data Links

While the frames of voice and audio data have fixed size and are produced with fixed rate, any isochronous service provided by CCSDS data link protocols is applicable to transmit them.

Advanced Orbiting Systems (AOS) Virtual Channel Access (VCA), AOS [24]   Bitstream, and AOS [24]  Insert services should be used to transmit voice and audio data.

#### Voice over IP

The IP network covering the ground and spacecraft shall be implemented with standards conforming to reference [16].

The RTP/UDP/IP/ENCAP/AOS [24] protocol stack should be used in VoIP for ground-to-space voice systems.

### Voice and Audio Data Formats for Files

The coding and compression mechanism for non-real-time audio file transmission shall conform to the AAC specification.

NOTES

- MP3 (ISO/IEC 13818-3) (reference [C2]) is not recommended because it is a legacy format; however, MP3 is still used in many audio files and probably will continue to be used for some years. However the recommendation is to migrate to AAC.

- Due to the common characteristics between audio files and other kinds of files in space missions, the transmission mechanism for non-real-time audio files is not specified in this book.

## Long-distance Audio Communication

### Overview

As distance imposes communication delays beyond approximately 30 seconds, the mission could choose to use file transfer rather than real-time communication.

The coding and compression mechanism for audio file transmission shall conform to AAC or MP3

If using speech-to-text and text-to-voice conversion, a standard application should be used.

Audio file transmission should be scheduled with high priority.

Files may be transmitted by any general file transmission protocol, e.g., via CFDP Class 1 or Class 2 (reference [17]), over CCSDS links or over DTN protocol (references [18] and [19]).

For long-distance missions like Mars and beyond, DTN technology should be used.

## Telepresence

Public and private tele/videoconferences using commercial products, like NetMeeting, VSee, or Skype, are used by the astronauts to communicate from the international space station to the ground and vice versa, using IP via a proxy.

## Space-to-Ground Voice Systems: Recommended Standards

Real-time audio should be encoded according to G.729 for low BW delivery, and with G.711 if enough BW is available. In the particular case of the ISS, Ku- and S-band may be used. For this reason, G.711 may be used with the high-BW of the Ku-band. G.729 should be used for S/G voice loops and communications with vehicles where S-band is used.

Users and permissions (roles, e.g., T/L/M) associated to the login should be used on the ground segment.

For long distance, file-based transfer, AAC format files should be used via the CFDP Class 1 or Class 2 (reference [17]), over CCSDS links or over DTN protocol (references [18] and [19]).

PTT in S/G should be implemented. If automatic detection is used, it must be calibrated with different voice levels.

NOTE	–	Quindars are still used as part of the communication, but they are not an ongoing requirement.

Frequencies and channelization: If a direct space link to spacecraft is available or if the MCC communicates using a space link to other MCC, the CCSDS standard frequency (reference [20][21][22]) should be used.

Signaling: In analog systems signaling is always present. In digital systems an open line may be used without signaling .

Signaling must be used for important loops like S/G.

Channels and the kind of signaling should be well defined in advance.

Security restrictions must be taken into account if commercial products are used, especially using the Internet.

Encryption and channel privatization must be used for medical conferences and experiments using medical data.

Quality monitoring should be used, either QoS or QoE, depending on the case.

NOTE	–	If the Internet is used (e.g., VoIP) for the voice transmission, quality cannot be guaranteed.

Voice recording equipment is needed as described in section 2.3.2.

S/G communications should follow a clear and well-defined etiquette and protocol (roles and positions to talk).

Personnel should be trained in etiquette, protocol, voice formats, their use, and notification of changes.

Cisco IP Communicator should be used if the station laptops are used for IP telephony. On the ground any IP device compatible with Cisco IP Communicator may be used.

When designing a crewed mission, alternate conferencing or IM systems such as NetMeeting, VSee, or Skype should be taken into account.

VSee should be the first option used for telepresence.

NOTE	–	A high-BW link (e.g., Ku-band) would be required for this application.

Multiple voice channels (redundancy) must be available due to the importance of voice communication in space missions.

# Case 3: Emergency Voice Communication

## Overview

Emergency communications is normally performed between MCCs using a black phone, a mobile phone connected to a commercial cellular service, or a satellite phone. The ground controllers must have access to a list of telephone numbers for the console positions they need to contact in the event of an emergency communication situation where the primary voice communication system is unavailable.

In Space, when normal means of voice communication are not available from the primary vehicle as a result of an emergency situation, noncritical systems (including primary radio equipment) should be powered down to conserve power and BW. Low-power communications equipment could then be used to transmit voice and a limited amount of command/telemetry. In these emergency situations, voice communications should be encoded as G.729 data and transmitted over CCSDS AOS VCA (virtual channel access) service with no IP/UDP/RTP protocol wrapping (BW 10.5 Kbps).

Support for unscheduled NASA Very High Frequency (VHF) ground stations will be for spacecraft contingency and/or spacecraft emergency conditions, when S-band S/G communication is unavailable due to S-band communication failures caused by problems such as:

- ISS/Soyuz fire;

- ISS/Soyuz depressurization;

- ISS/Soyuz crew medical emergencies;

- extended SHO (scheduled order) gaps during any complications on the ISS.

During this type of emergency, ISS VHF1, VHF2 and Soyuz VHF systems will be activated simultaneously to maximize communications coverage to ensure contact with the crew during an emergency ingress of Soyuz.

Examples of configurations used during an emergency situation with the Russian and U.S. ground segments are listed below:

- ISS VHF1: Used for S/G communication over Russian ground stations (RS ISS S/G 1 MH21) and also used as an alternate link for S/G communications when ISS is over NASA VHF ground stations. Uplink: 139.208 MHz; Downlink: 143.625 MHz.

- Soyuz VHF2: Used for S/G over Russian ground stations (RS ISS S/G 2 MH24) and space-to-space communication. This is the only VHF frequency pair carried on Soyuz. Soyuz VHF2 communication through NASA VHF ground stations is authorized for emergency use only per Flight Rule (D3-1). Uplink: 130.167 MHz; Downlink: 121.750 MHz.

- Goddard Voice will configure DFRC and WSC S/G circuits. MCC-M will configure RS ISS S/G 1 MH21 (ISS VHF1) and/or RS ISS S/G 2 MH24 (Soyuz VHF2).

- The ISS VHF transmitter will be constant keyed, which is necessary to verify signal reception and link integrity, as well as to ensure minimum required link margin is used.

Orion and Space X use CCSDS standards for emergency communications.

In cases involving landers, rovers, orbiting constellations, and orbiting relays, proximity links should be considered (references [20], [21], [22].) This protocol uses a frequency band in the 400 MHz band so as to reduce complexity of the vehicle: 437.1000 MHz, 440.7425 MHz, 444.3850 MHz, and 448.0275 MHz.

In the specific case of an astronaut using an Extravehicular Mobility Unit (EMU), a communications carrier assembly leverages two (redundant) UHF channel transmitters and three single-channel receivers to provide voice (and limited telemetry) communication.

## Emergency Voice Communication: Recommended Standards

The voice system in an MCC should be highly available:

Redundant voice systems on diversified power supply feeds should be available.

Alternate routes should be available to patch around disrupted connections between MCCs.

Every console position should have access to a black phone, mobile phone, or satellite phone.

Emergency procedures should be simulated on a regular basis to allow ground personnel to have adequate training.

NOTE	–	The ISS program has a requirement that allows for 30 minutes of crew time per month for VHF emergency communications checkouts, which allows for two 15-minute checkouts monthly.

Emergency channel voice should be encoded as G.729 and transmitted over CCSDS AOS VCA service using 8 KHz with no IP/UDP/RTP or VoIP protocol wrapping.

PTT should be required on the ground.

Signaling, or loops keyed should be used from the spacecraft.

Voice, cautions, and warnings should have the highest priority in the communications channels.

NOTE	–	All the other parameters defined in section 2.5 are not applicable here.

# Case 4: ISS Rendezvous, Proximity, And Docking Operations Voice Communications

## Overview

Space rendezvous of an active, or ‘chaser’, spacecraft with an (assumed) passive spacecraft can be divided into several phases and typically starts with the two spacecraft in separate orbits; the spacecraft are typically separated by more than 10,000 km (6,200 mi). For the voice and audio communications covered in this book, the phases are only important due to the voice system used in each case. It must be clear that the vehicles are manned and have voice systems.

### Rendezvous

Rendezvous occurs when two spacecraft have the same orbit, e.g., a vehicle and the ISS. It can take hours to days to complete the rendezvous. Vehicles communicate with each other using their S/G voice systems. In the case of line-of-sight, they can contact one another directly vehicle to vehicle, using S/G as backup. S/G is also used to inform the operations personnel on ground.

### Proximity

Proximity occurs when two spacecraft are very close to each other, e.g., around 300 m. (1–2 hours of operations till docking). Vehicles use direct links for voice communications and S/G to keep the operations teams on the ground up to date (for Soyus start at 200 km). In some cases only direct communication is used in order to avoid any interference.

### Docking

Docking is considered to be between around 300 m and docking completion(from several minutes up to 1 hour of operations). Vehicles use direct links for voice communications and S/G to keep the operations teams on the ground up to date.

NOTE	–	VHF is used for near-field, vehicle-to-vehicle communication.

## Rendezvous, Proximity, and Docking Operations: REcommended Standards

For a rendezvous, standard S/G communications should be used.

For proximity and docking, the normal S/G voice loop should be used, plus spacecraft-to-spacecraft communication.

NOTE	–	This is a direct connection using VHF or S-band communication channels, going to the ground almost simultaneously. That is a similar system to what is used for EVA. The communication is between the EVA crewman and the vehicle, using the vehicle’s voice system.

The ISS/spacecraft voice system should be radiated down the S/G communication link.

For communication to the ground, ground stations (ground telemetry station) or TDRSS are used.

NOTE	–	Soyuz, when approaching proximity operations manually, severs the connection to the ground and uses only the VHF/S-band connection from spacecraft to spacecraft.

PTT,  signaling,  voice encryption, QoS, and etiquette have the same requirements as in section 3.

NOTE	–	All the other parameters defined in section 2.5 are not applicable here.

# Case 5: Search and Rescue Voice Communications

## Discussion

At the moment (2014) and for the next few years, on the ISS the only rescue vehicle is the Russian Soyuz capsule. For this reason, this section is strongly oriented to the Russian capsule.

SAR voice communication concerns messaging between spacecraft crew and rescue teams.

Voice communications are crucial in a rescue. During rescue operations, it is essential that standardized communication procedures are used.

The primary means of communication in a rescue is the survival radio or satellite telephone supplied with the survival equipment. Each crew member must be familiar with the radio operations.

In addition to the Automatic Direction Finder (ADF) capability, the U.S. government also uses satellites that monitor guard frequencies for emergency locator transmitter broadcasts. For example, a AN/PRC-149 Rescue Radio includes a Global Positioning System (GPS) and a Cospas-Sarsat beacon. It operates on 121.5 MHz, 243.0 MHz, and 406.025 MHz.

### Cospas-Sarsat

The International Cospas-Sarsat Program is a satellite-based SAR distress, alert-detection, and information-distribution system, established in 1979 by Canada, France, the U.S., and the former Soviet Union. It is best known as the system that detects and locates emergency beacons activated by aircraft, ships, and backcountry hikers in distress. Over the years, many countries have joined the project, either as providers of ground segments or as user states. The system consists of a ground segment and a space segment.

More recently, the Cospas-Sarsat system has been designed to detect only alerts transmitted by 406 MHz beacons that incorporate GPS receivers. Such beacons transmit highly accurate positions of distress almost instantly to SAR agencies via the GEOSAR satellites.

### Soyuz Search and Rescue Case Scenario

The Soyuz commander or the FDs of MCC-M and MCC-Houston (MCC-H) are authorized to formally declare a Soyuz spacecraft emergency which requires an emergency landing. If this were to occur, the following notification requirements will immediately be met:

- Depending on whether the landing area is within Russia or territories of the former Soviet Union, or in North America, the ISS or MCC-H FD must inform the corresponding SAR personnel.

- In America, the ISS FD shall notify the Air Force Rescue Coordination Center (AFRCC) in Langley, Virginia, and the MCC-H Trajectory Operations Officer (TOPO).

- AFRCC and TOPO shall notify USSPACECOM, the Department of Defense (DoD) manned spaceflight group, and other U.S. agencies/organizations, as required.

- Once notified, the AFRCC shall coordinate the efforts of the local SAR organization that will locate, assist the crew, and transport them to definitive medical care as required. The AFRCC shall provide the SAR team with checklists and pictures of hazards associated with the Soyuz and how to remove the crew. AFRCC shall inform the DoD Manned Space Flight Support (DDMS).

- The DDMS shall coordinate and provide command and control for all required DoD assets. The MCC-H Landing Support Officer (LSO) shall provide coordination with these external agencies. If LSO is not on console, TOPO provides coordination.

NOTE	–	The Soyuz contingency landing areas must be evaluated with respect to terrain, experience of the landing support personnel, SAR capabilities, access to definitive medical care, and in-place international support agreements. However, since Soyuz requires a ballistic reentry with a g-load near 8–10 g’s, the assumption is the decision to perform an emergency landing is made only in the direst of circumstances.

- To mitigate the risk from the above factors, the MCC-H Spaceflight Meteorology Group forecasts GO/NO GO conditions. Once a decision is made to land the Soyuz at an emergency site, the ISS FD, upon concurrence with MCC-M, may call in the MCC-H Spaceflight Meteorology Group to update the wind forecasts if time permits. This assumes MCC-H/M will receive the updated forecasts before a final landing area decision is required.

- In Russia, MCC-M coordinate directly with the rescue teams. The crew uses a Satellite telephone to communicate with the rescue teams.

NOTES

- Splashdown was used by the Apollo missions and will be used by Space-X Dragon and Orion in the near future. From the voice point of view, there are no differences between a landing on the water or on the land.

- Chinese Zhengzhou spacecraft lands normally on the ground, but Russian Soyuz can be also land on water.

- Soyuz and Zhengzhou have in the capsule a Cospas-Sarsat radio and a Iridium satellite phone.

## Search and Rescue Voice Communication: Recommended Standards

For SAR the standard S/G voice system should be used as long as possible.

After landing, unnecessary equipment should be shut down; only communications should be active.

The crew should use an emergency radio or satellite telephone.

The SAR radio in the vehicle should be a battery-powered radio, like PRC-112G or PRC-149, having UHF, VHF, GPS, satellite radio, and a Cospas-Sarsat beacon.

NOTE	–	All other parameters are not applicable here.

Protocol Implementation Conformance
 Statement (PICS) Proforma

(NORMATIVE)

Introduction

Overview

      - Columns

        - General

In order to reduce the size of tables in the PICS proforma, notations have been introduced that have allowed the use of a multi-column layout, where the columns are headed ‘Status’ and ‘Support’. The definition of each of these follows.

        - Status Column

The ‘Status’ column indicates the level of support required for conformance to the standard. The values are as follows:

M		Mandatory support is required.

O		Optional support is permitted for conformance to the standard.  If implemented, it must conform to the specifications and restrictions contained in the standard.  These restrictions may affect the optionality of other items.

O.n		The item is optional, but support of at least one of the options labeled with the same number n is mandatory.  The definitions for the qualification statements used in this annex are written under the tables in which they first appear.

C.n		The item is conditional (where n is the number which identifies the applicable condition). The definitions for the conditional statements used in this annex are written under the tables in which they first appear.

n/a		The item is not applicable.

        - Support Column

The ‘Support’ column is completed by the supplier or implementer to indicate the level of implementation of each feature. The proforma has been designed such that the only entries required in the ‘Support’ column are:

Y		Yes, the feature has been implemented.

N		No, the feature has not been implemented.

–		The item is not applicable.

      - Item Reference Numbers

Within the PICS proforma, each line that requires implementation detail to be entered is numbered at the left hand edge of the line. This numbering is included as a means of uniquely identifying all possible implementation details within the PICS proforma. The need for such unique referencing has been identified by the testing bodies.

The means of referencing individual responses is to specify the following sequence:

- a reference to the smallest subclause enclosing the relevant item;

- a solidus character, ‘/’;

- the reference number of the row in which the response appears;

- if, and only if, more than one response occurs in the row identified by the reference number, then each possible entry is implicitly labeled a, b, c, etc., from left to right, and this letter is appended to the sequence.

  - Completion of the PICS

The implementer shall complete all entries in the column marked ‘Support’. In certain clauses of the PICS proforma, further guidance for completion may be necessary. Such guidance shall supplement the guidance given in this clause and shall have a scope restricted to the clause in which it appears. In addition, other specifically identified information shall be provided by the implementer where requested. No changes shall be made to the proforma except the completion as required. Recognizing that the level of detail required may, in some instances, exceed the space available for responses, a number of responses specifically allow for the addition of appendices to the PICS.

Voice formats should be specified between the Agencies in order to carry out the testing. For cases 3, 4 and 5 the dedicated voice loops and the frequencies used must be specified if more than one Agency is involved.

  - REFERENCED BASE STANDARDS

Voice and Audio Communications (V&A in this document and in the yellow book) is the only base standard referenced in the PICS. In the tables below, numbers in the Reference column refer to applicable subsections within this document.

  - GENERAL INFORMATION

    - IDENTIFICATION OF the PICS

| Date of statement (yyyy-mm-dd) |  |
| --- | --- |
| PICS version |  |
| System Conformance Statement cross-reference |  |
| Other information |  |

    - Identification of the system supplier / test laboratory client

| Organization name |  |
| --- | --- |
| Contact name |  |
| Address |  |
| Telephone |  |
| E-mail |  |
| Other information |  |

    - IDENTIFICATION OF the IMPLEMENTATION UNDER TEST

| Implementation name |  |
| --- | --- |
| Implementation version |  |
| Voice system |  |
| Codec used |  |
| Type of keyset (hard, soft-keyset, etc) |  |
| Type of transport layer |  |
| Special configuration (port, IP addresses, etc) |  |
| Voice loops definition (Voice loops used) |  |
| Voice format |  |
| Other information (e.g.PaBX numbers, patched loop) |  |

Note: To test cases 3, 4, and 5, a separated PICs will be needed. Since these cases have been used operationally for decades with very clear established communication rules between RSA and NASA, the PICs for these cases will be not included in this book

    - Equipment Configuration for VOICE System  In detail

| Source Device IP address / Ports / PABX number |  |
| --- | --- |
| Source Device Netmask (VOIP) |  |
| Source Device Gateway (VOIP) |  |
| Source Device (T1 or E1) |  |
| Destination Device (T1 or E1) |  |
| Destination IP Addresses / Ports /PABX number |  |
| Network Protocol |  |
| Source /destination UDP ports (if any) |  |
| Codec (G.711, G.728, etc) |  |
| Voice loop Name (s) |  |
| Other information (e.g. micro or telephone with mute function) |  |

    - Global statement of conformance

| Are all mandatory features implemented? (Yes or No) |  |
| --- | --- |

NOTE	–	If a positive response is not given to this box, then the implementation does not conform to the standard.

  - INTERFACES

| Item | Transport Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | T1 (TDM) | 2.1.2 | O.1 |  |
| 2 | E1(TDM) | 2.1.2 | O.1 |  |
| 3 | VOIP | 2.1.2 | O.1 |  |
| 4 | Phone line (POTS) | 3.4.1 | O.1 |  |

Note: the O.1 options specify the interface used to the communication between the Agencies or to externals. When one option is chosen it becomes mandatory for the communication. But is possible to have also more than one communication interface.

  - Supported PARAMETERS

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | MPLS /IP network | 3.3.1 | O.2 |  |
| 2 | Internet /IP network | 3.3.1 | O.2 |  |
| 3 | Compatible Voice Formats | 1.6.2 /2.5 | O.3 |  |
| 4 | Common Voice loops | 2.2 | M |  |
| 5 | PTT | 2.5 | M |  |
| 6 | Common Codec | 2.1.4 | O.3 | If not, converters |
| 7 | Synchronization (E1/T1) | 2.1.2 | M |  |
| 8 | Synchronization (VoIP) | 2.1.2 | N/A |  |
| 9 | Latency | 2.5 | O | As little as possibe |
| 10 | Channelization (voice Format) | 3.5.9 | O.3 |  |
| 11 | Signaling | 2.5 | O.3 | M if (S/G) |
| 12 | Voice Recording | 3.5.11 | M |  |
| 13 | Etiquette and protocol | 3.5.22 | M |  |
| 14 | Redundancy | 3.5.27 | O.2 |  |
| 15 | Audio file format | 4.2.3 | O.4 | If not converters |
| 16 | User role assignment and security | 2.5 /2.4 | M |  |
| 17 | Keyset type | 2.2 | M |  |
| 18 | Others ?? |  |  |  |

Note: The O.2 options are related to the communication link,  O.3 to the parameters needed to establish the communication between voice systems, and O.4 to audio file format.

  - Interoperability

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | Real time voice | 2.2 | M |  |
| 2 | Playback voice and audio | 2.3.2 | M |  |
| 3 | End User Capabilities | 2 | O |  |

  - PRotocols

| 1 | RTP | 2.1.3 | O.3 |  |
| --- | --- | --- | --- | --- |
| 2 | RTCP | 2.1.3 | O.3 |  |
| 3 | SRTP | 2.1.3 | O.3 |  |
| 4 | E1/T1 | 2.1.3 | O.3 |  |
| 5 | TCP/IP | 2.1.3 | O.3 |  |
| 6 | UDP | 2.1.3 | O.3 |  |
| item | VOIP |  |  |  |
| 7 | SIP | 2.1.3 | O.3 |  |
| 8 | H.323 | 2.1.3 | O.3 |  |
| 9 | MGPC | 2.1.3 | O.3 |  |
| 10 | MEGACO (H.248) | 2.1.3 | O.3 |  |
| Item | Codec |  |  |  |
| 11 | G.711 | 2.1.4 | O.4 |  |
| 12 | G.729 | 2.1.4 | O.4 | (S/G CNSA) |
| 13 | G.728 | 2.1.4 | O.4 | (S/G) |
| Item | Audio files transmission |  |  |  |
| 14 | AAC | 4.2.1 | O.5 |  |
| 15 | MP3 | 4.2.3 | O.5 |  |
| 16 | DTN | 2.1 | O |  |
| 17 | CFDP | 2.1 | O |  |

Note: the O.3 options are related to the interface used to communication between voice systems, O.4 to the preferred codec, and O.5 to the audio codec.

  - Supported Operations

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | MCC to MCC | 3.3 | M |  |
| 2 | MCC to the Public Affairs | 3.4 | M |  |
| 3 | MCC to S/G | 4.1 | O |  |
| 4 | Emergency communications | 5.1 | O |  |
| 5 | Docking / Rendezvous communications | 6.1 | O |  |
| 6 | SAR | 7.1 | O |  |
| 7 | Audio and Data file transfer | 4.2 | M |  |

Note – in this case, the optional items can be achieved through terrestrial connections between MCCs, e.g. S/G trough NASA or RSA.

  - PRIVACY

    - General

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | Data Privacy | B2.1 | M |  |
| 2 | Data Integrity | B2.2 | M |  |
| 3 | Authentication of communicating entities | B2.3 | M |  |
| 4 | Control of access of resources | B2.4 | M |  |

    - Encryption Procedures FOR PRIVATE VOice

Encryption procedures are applicable for private or medical voice.  Encryption is typically peer-to-peer based on the application being used.  Tests are not required for PICS proforma.  Tests of individual application are to be performed prior to use in flight.

Security Considerations

(Informative)

  - INTRODUCTION

Security concerns specific to audio communications exist where there are requirements to ensure that transmitted audio not be disclosed, altered, spoofed, nor redistributed without authorization.

Manned space systems frequently have requirements to provide capabilities for private audio communications between flight crew and ground operations personnel, physicians, families, and/or news media outlets. Ground systems that receive and/or redistribute such audio have both similar privacy requirements and additional threats and countermeasures.

The focus of this section is on the specific protocols and methods recommended earlier in this document. It may be necessary to implement security services at other layers within the protocol stack to account for a) audio and voice distribution, b) different classes of audio data or end users, or c) protection of data during unprotected portions of the complete end-to-end transmission (e.g., across ground networks for public relations events). The specification of security services at other layers is outside the scope of this document.

  - SECURITY CONCERNS With REspect to this CCSDS Document

The most common method of applying security to digital audio is through the use of multimedia container formats. Containers provide a file-based mechanism for exchanging, processing, and storing interleaved fragments of audio, metadata, and/or other content (e.g., annotations added to a recording). Most container files may be read or written by ordinary computer systems in the same manner as other files.

For the transmission of voice in real time, as is needed for operations, the security is implemented using codecs (as described previously in this book) and encrypting the data over the network as is done in MPLS or the E1/T1 interfaces.

For voice communication, it is necessary that the person who is speaking or listening in a voice loop have the required access permissions (role) and have a user ID and password controlled by the system, permitting logging into the voice system as well.

If VoIP is used, the transmission of the voice data must fulfill the same security requirements as the transmission of data in an IP network. For VoIP transmission, Internet Protocol Security/VPN tunnels are recommended.

Typical VoIP protocols (e.g., SIP, RTP, Cisco VoIP, Skype, or Asterisk) have their own security features, but are less suitable for space business and transmission over the Internet. More information about VoIP security can be found in Voice over IP Security Alliance (VoIPSA) recommendations (see https://www.voipsa.org).

    - DATA PRIVACY

The first major area of security concern is privacy, the requirement that the audio not be heard by any other than the intended recipient(s).

Limited privacy can be achieved by employing protected data transport at lower layers and restricting distribution. Virtual channel assignment over CCSDS RF links is not, by itself, an effective method of ensuring privacy.

Better privacy can be achieved using cryptographic techniques, which may be applied to all or part of a container format. Since any transcoding or decoding system must be able to read and pass metadata in order to process the stream, audio metadata must be readable at these points. It is therefore highly desirable to have the capability to perform selective encryption of container file fields (e.g., audio but not metadata).

VoIP data commonly uses RTP (reference [6]) as a transport layer together with UDP (reference [5]), regardless of which codecs are used at the application layer. SRTP (reference [7]) is an RTP protocol extension which can be used to encrypt RTP data streams.

For PDH, as in the E1/T1 voice systems (see references [2], [3]), the authentication described in section B2 must be taken into account.

      - Metadata Flags

Metadata flags, commonly used in the music industry (MPEG3 ID3V2.X), can be used for the description of voice data. Flags could indicate type of conversation (e.g., family or medical conference).

Another type of metadata is time stamps. The best way to do lip sync is to use a common time source for video and audio.

In general, the metadata flags must be protected like the rest of the voice data transmitted. The same requirements are applicable here.

      - IP/Port Configuration

A default port number should be used rather than an arbitrary port assignment, e.g., Skype. If commercial applications are used (e.g., NetMeeting, VSee, or Skype), the installation of the commercial software must fulfill the security requirements of the respective space agency (e.g., NASA HQ Skype Configuration and Appropriate Use Guidelines). These sorts of applications are commonly used for public relations and educational events.

    - DATA INTEGRITY

The second major area of security concern is data integrity. Data integrity requires that the audio not be altered, whether to introduce false audio or to interfere with decoding. Integrity verification mechanisms can be used for data validation to prevent security problems due to noncompliant or malignant data.

Like privacy, data integrity is commonly provided at other layers of the protocol stack or through a container format.

For VoIP data streams, the SRTP (reference [7]) is an RTP protocol extension which can be used to provide data integrity and replay protection.

For PDH using the E1/T1 voice communication systems, the transmission should be encrypted at least in the network transport layer (like in MPLS).

    - AUTHENTICATION OF COMMUNICATING ENTITIES

Source authentication is the requirement that the audio be attributable to a known origin. Closely related to data integrity, it can also be used for data validation.

Source authentication, if provided, is commonly provided at other layers of the protocol stack or through a container format.

For VoIP data streams, SRTP (reference [7]) is an RTP protocol extension which can be used to provide message authentication.

Using PDH systems, the source can be identified with the role. Each person and the assigned role is saved in an LDAP database or similar data bank, where the source can be identified.

The keyset can be identified as well, and because of the role, the manning roster or the shift plan allows identification of the person logged in.

    - CONTROL OF ACCESS TO RESOURCES

The fourth major area of security concern is access control, the requirement that the voice data be restricted from unauthorized further use by the recipient(s).

In an MCC, the user is identified by role, and the access and loop permissions are defined using X.500 (reference [23]). For users outside of an MCC (for supporting experiments or for special events) two-factor authentication and a VPN should be used to have acceptable access control.

To have access to a voice system, each user must have a user ID and a password and/or a token code. User login will give the user a predefined role with restricted permissions to their specific role.

Each role has listen, talk, or monitoring capabilities, and the role cannot be changed by the users themselves.

Access control can be provided at other layers of the protocol stack. Various methods also exist for attempting access control through the inclusion of proprietary metadata in a container format, although it should be noted that many similar techniques in the past have been defeated by determined attackers.

    - AVAILABILITY OF RESOURCES

Voice communication is the most essential resource in human space. The voice equipment must be maintained for emergency cases as well as for EVA and operations.

The access to a control room in an MCC must be restricted, and access to remote users must be controlled (see section B2.4). Access to voice equipment and the configuration management terminals must be under strict control.

Redundant equipment should be available in case of a hacker attack or failure, especially in space and in the MCC. Different communication channels and frequencies should be used in order to support communication in emergency cases (section 5).

User education is an important factor. Using VoIP implies many risks, as is described in this book. Regular user-awareness training should be done in a similar way to mandatory security training for Internet access, e-mails, phishing, etc.

    - AUDITING OF RESOURCE USAGE

User access to voice recording and audio data should be logged using X.500 or other methods.

Auditing a voice system is quite easy. Each loop is recorded, and the system records the users logged in using the different loops. Doing a playback is possible to identify the source and recipients as described before. It is a common practice to identify problems by reviewing the loops to know who said what and when. That helps especially in time-critical situations to identify problems or errors, and to have lessons learned to improve the communications during operations.

Accessing audio files inside an MCC is easy to control because files are transmitted using FTP or other protocols requiring a user ID and password. Control room access is also restricted; however, outside of an MCC, a pen drive or other methods of copying files could be used, which is out of the control of the MCC.

  - POTENTIAL THREATS AND ATTACK SCENARIOS

Especially during public affairs events where external equipment is used, there is a risk of inadvertent or malicious content being injected into one or more voice loops, or that the loop content could be made public.

Another risk is that someone could enter to the voice system using someone else’s role or credentials. This could cause confusion, damage, or loss of data.

  - CONSEQUENCES OF NOT APPLYING SECURITY TO THE TECHNOLOGY

If confidentiality is not implemented, audio communications might be heard by unauthorized entities, resulting in disclosure of sensitive or private information.

Without source authentication or integrity verification, valid audio communications could be corrupted, or invalid audio could be substituted in its place.

Without access controls, authorized entities might be able to redistribute sensitive or proprietary information to unauthorized third parties.

Acronyms and Abbreviations

(Informative)

Term	Meaning

AAC	Advance Audio Coding/Codec

AFRCC	Air Force Rescue Coordination Center

AOS	Advanced Orbiting Systems

API	Application Programming Interface

ASR	Automatic Speech Recognition

ATM	Asynchronous Transfer Mode

BW	Bandwidth

CCSDS	Consultative Committee for Space Data Systems

CFDP	CCSDS File Delivery Protocol

CODEC	Code-Decode

DDMS	Department of Defense Manned Space Flight Support

DFRS	NASA's Dryden Flight Research Center has been officially

redesignated as the NASA Armstrong Flight Research Center.

DoD	U.S. Department of Defense

DTN	Delay-Tolerant Networking

EMU	Extravehicular Mobility Unit

EVA	Extra Vehicular Activities

FD	Flight Director

FL/RL Comms	wide band TDM communication equipment (forward link / return link)

FTP	File Transfer Protocol

GPS	Global Positioning System

HOSC	Huntsville Operations Support Center

IP	Internet Protocol

ISDN	Integrated Services Digital Network

ISS	International Space Station

ITU-T	International Telecommunication Union-Telecommunication Standardization Sector

IVoDS	Internet Voice Distribution System

LDAP	Lightweight Directory Access Protocol

LIVoDS	Local Internet Voice Distribution System

LSO	Landing Support Officer

MCC	Mission Control Center

MCC-H	Mission Control Center-Houston

MCC-M	Mission Control Center-Moscow

MGCP	Media Gateway Control Protocol

MOC	Mission Operations Center

MOVE	Mission Operations Voice Enhancement

MPLS	Multi-Protocol Label Switching

MSFC	NASA Marshall Space Flight Center

NAT	Network Address Translation

PABX	Private Automated Branch Exchange

PCM	Pulse Code Modulation

PDH	Plesiochronous Digital Hierarchy

PIP 	Private Internet Protocol

POIC	Payload Operations Integration Center

PSN	Packet Switched Network

PSTN	Public Switched Telephone Network

PTT	Push-To-Talk

PW	Pseudowire

QoE or QX	Quality of Experience

QoS	Quality of Service

RF	Radio Frequency

RFC	Request for Comment

RTCP	Real-time Transport Control Protocol

RTP	Real-time Transport Protocol

RVoDS	Remote Internet Voice Distribution System

SAR	Search and Rescue

S/G	Space-to-Ground

SHO	Scheduled Order

SIP	Session Initiation Protocol

SRTCP	Secure Real-time Transport Control Protocol

SRTP	Secure Real-time Transport Protocol

TCP	Transmission Control Protocol

TCP/IP	Transmission Control Protocol/Internet Protocol

TDM	Time Division Multiplexing

TDMoIP	TDM over IP

TDRSS	Tracking and Data Relay Satellite System

T/L/M	Talk/Listen/Monitor

TOPO	Trajectory Operations Officer

TTS	Text-To-Speech

UDP	User Datagram Protocol

UHF	Ultra High Frequency

VCA	Virtual Channel Access

VHF	Very High Frequency

VoIP	Voice over IP

VoIPSA	Voice over IP Security Alliance

VOX	Voice Level Detection or Voice Activity Level

VPN	Virtual Private Network

WSC	White Sands Complex

DTN Bundle Protocol for Voice and audio Transmission

  - Mode 1 Real Time Delivery, Best Effort

Mode 1 provides best-effort delivery of data and should be used for unicast or multicast data delivery when the data is to be utilized immediately upon arrival (perhaps for near–real-time decision making).  The data will be forwarded using the DTN Bundle Protocol without custody transfer and will be available to the receiving CODEC/application on a best-effort basis.  Therefore the data will be ‘played’ in the order it is received.  Missing, damaged, or out-of-order packets will be ignored with subsequent CODEC responses being typical.  Additional items such as excessive latency or jitter may be deleterious to the CODEC response.

  - Mode 2 DELAYED Delivery, WITH Packet RESTORATION

Mode 2 provides delivery of data with the prospect of no packets dropped and should be used for single or multi-transport of data when the data can be utilized after a sufficient latency to allow reassembly of the data.  The data will be available to a CODEC/application once the underlying protocol has sufficient time to reassemble the data stream.

Therefore the data will be ‘played’ in its entirety subject to data being wholly lost on a frame basis.  Missing and damaged bundles will be forwarded prior to reassembly with out-of-order bundles to be made available to the end CODEC/application.  Additional items such as excessive latency or jitter will not affect CODEC/application response.

  - Store and Forward Issues

The Delay Tolerant Networking Bundle Protocol (DTN-BP) enables store and forward operation when multiple hops or links are required to send data from source to receiver. There is an additional space link reliability protocol available known as Licklider Transmission Protocol (LTP), which will note loss of DTN bundles (which would contain 1-n video frames depending on system design) and request retransmission of missing bundles.

Use of the LTP reliability mechanism will result in delivery of out-of-order video frames to the application layer (because of the lag in retransmitting missing bundles). This may or may not be acceptable to the end-user application, and consideration of this out-of-order condition must be made.

In current lab experiments, it has been seen that an effective use of DTN to transmit video is to transmit bundles unreliably, accept the consequences of missing data for the real-time viewing of the video stream, and use another mechanism for recovery of missing data. This mechanism could be an application buffer to store retransmitted bundles separately for later reconstruction of the video stream in non–real time, or to record the video on board and later transmit as a video file for playback after the file is completely received without errors.  Further experimentation is required to provide definite parameters for the transmission of voice and files transmission using DTN.

Informative References 

(Informative)

[C1]	Voice Communications. Informational Report, CCSDS 706.0-G-1. Green Book. Issue 1. Washington, D.C.: CCSDS, September 2010.

[C2]	Information Technology—Generic Coding of Moving Pictures and Associated Audio Information--Part 3:Audio. International Standard. ISO/IEC 13818-3:1995. April 1998.

[C3]	Digital Audio Interface—Part 3: Consumer Applications. Ed. 3.1 Consol. with am1. IEC 60958-3. Geneva: IEC, 2009.

[C4]	J. Postel. User Datagram Protocol. STD 6. Reston, Virginia: ISOC, August 1980.

[C5]	J. Postel. Internet Protocol. STD 5, September 1981. [RFC 791, RFC 950, RFC 919, RFC 922, RFC 792, RFC 1112].

[C6]	Space Link Extension—Internet Protocol for Transfer Services. Recommendation for Space Data System Standards, CCSDS 913.1-B-1. Blue Book. Issue 1. Washington, D.C.: CCSDS, September 2008.

[C7] ITU MOS (Mean Opinion Score) ITU-T P.800 (August 1996) and ITU-T PESQ P.862 (VoIP). February 2001.

# Footnotes

As this is refined, it will be added to the Voice and audio specifications.