## Slide 1
CCSDS Name & Number Registries
Issues & Proposed Fixes
Peter Shames, SEA AD
Erik Barkley, CSS AD
26 May 2015
V11: Updated post 11 May 2015 telecon

## Slide 2: Overview
  Over time CCSDS has created a number of different registries, registry policies, and registration organizations, most in the SANA
    SCID Registry
    MACAO Registry
    SANA Registries
    CCSDS web site agency, observer & affiliate lists
  The early “registries”, were flat files but had documented registry policies and organizational structure; more recent ones tend to be more casually specified, but …
    SCID, CCSDS 320x0: defines the SCID registry, Agency & Agency Head of Delegation (HoD), and Agency Representatives (AR)
    CAO & MACAO, CCSDS 630x0: defines the Control Authority Agent, Member Agency CAO, and SFDU registries
    Various protocol “magic number” registries: defined in Blue Books, CLCW ID, Encap PID, MAP IDs, IP Extension Header; registration policy is Blue Book change (or not stated)
    Different XML schema registries: defined in Blue Books, Nav XML schema, DAI XML schema; registration policy is Blue Book change (or not stated)
    CCSDS Object Identifier (OID) registry: ISO derived, largely SLE, CSTS, and SM; registration policy is SSG
    CCSDS Glossary & Terms: as defined in all CCSDS Blue & Magenta Books (and many Green Books), last updated 12/12/2012; uses an on-line registration form
    SIS AMS Transport Service and LTP Engine Identifiers: defined in Blue Books, but allocated from IANA; registration policy is “CCSDS Agency Representative”, but this just points to the Agencies on the CCSDS website, which lists the CMC members
  Most, but not all, include some sort of Review Authority which is usually the WG itself, which may, or may not, persist over time.

## Slide 3: Current CCSDS Registry Situation
Recommendation A
SANA Registry A1, A2..
Recommendation N
SANA Registry N1, N2..
Can lead to real problems:
1) A1, N1,etc may overlap in varying degrees;
2) A1, N1, may be named differently but really mean the same thing. Examples: "Originator" vs. "Originating Organization" , Spacecraft Identifiers,
Ground Station Identifiers,
Antenna Identifiers
3) Also possible that various registries contain slightly different criteria for inclusion but no formal statement of such criteria
There is no defined CCSDS process in place to check or manage this.
.
.
.
Each WG defines its own registries, without regard to existing registries or to others that might be related …

## Slide 4: Top Level CCSDS Registry Issue
The CCSDS registries, counting both the SANA and the CCSDS Web Site, now include the following;
  Ten separate "organization" type registries (member, observer, affiliate, operator, originator) with different levels of completeness and accuracy, ranging from a full spec to a "1024 character string"
    Two more "organization type registries” were just proposed by SOIS and CSS, with weak “1024 character string” type specs, more are surely on the way
  Four different "contacts" registries (contacts, PoC, HoD) with different levels of completeness and accuracy
    Two new, weakly specified, ”contact" type registries were just proposed by SOIS and CSS, more are surely on the way
  Two different antenna and station registries (plus future optical assets and a new, weakly specified, station registry from CSS)
There is little real guidance for creators of new registries, and none about re-use of existing ones

## Slide 5: Observations
CCSDS has transitioned from separate documents (registries of sorts), managed via different organizations and processes, to one where the major registries are managed in one central location, the SANA.
Various WG have identified various ways to manage registries and have assigned responsibility to (often to themselves) using quite different policies.
Some of the SANA Considerations sections of these documents define what are, in effect, identical registries of “agencies” or “providers” or “users” …
A number of new registries are already in discussion, some managed centrally, some supporting WGs, some for new protocols, and some delegated, somewhat haphazardly, to “space agency” or “agency representatives” who remain weakly defined and with unclear procedures or roles.

## Slide 6: Observations, contd
The following new registries have been identified:
  Sponsored agencies and service / data providers (by agency?)
  Unique (and singular) S/C, antenna, station identifiers (by agency?)
  CSS MD-CSTS functional resources (by OID / type)
  SOIS RFID assigning agencies
  (and there are probably others in work)
  And references to outside registries and info sources (QUDV, IAU celestial sources, global S/C lists, …)
Questions to be answered:
  Do we continue this random walk or do we try and bring some order to the process … now?
  How do we handle cross cutting or multi-WG (or area) registries?
    Agencies? Agency Representatives? Sponsored organizations?
    OIDs?, XML schema?, Terminology?
  For those registries where a WG is listed do we continue down that path or assign responsibility to the more long lived Areas or the CESG?

## Slide 7: SEA Registry Proposal
Identify a specific set of categories of registries with some well defined policies
Initial set of categories:
  Registries with information managed (or requested) by agencies
  Registries with cross-cutting information that is managed at CESG level by one or more Expert Groups
  Registries with information that is local and managed by Areas (or WG)
Require WGs to re-use existing well specified registries instead of inventing new, weakly specified, ones:
  Add new organizations and contacts as needed
  Add new roles and other attributes as needed
Following charts describe the SANA roles and these categories in more detail along with some examples

## Slide 8: Current SANA Registry Policies
Current SANA YB, CCSDS 313x0y1, defines Registration Rules:
The CCSDS document requesting the creation of a new registry must define which one of the following registration rules is to be used for adding new entries or for making changes to the registry:
    a) Change requires a CCSDS approved document.
    b) Change requires an engineering review by a designated expert (or group). The expert for that registry is assigned by the CESG based on the WG recommendation.
    c) Change requires no engineering review, but the request must come from the official representative of a space agency that is a member of the CCSDS. The official representative of an agency may differ for each registry.
    d) Change requires no review; assignments are done on a first-come, first-served basis.
SANA Registry Roles:
  Review Authority (which org is involved in controlling changes to the registry)
  Registration Policy
    Registration updates (how updates are requested and processed)
    Authorized updaters (who can make changes)
Key proposed new rule changes:
  A CCSDS Working Group that identifies a need for a new registry shall first review the existing SANA registries to determine if a suitable one already exists.
  If a requirement may be met by an existing registry by simple addition of some new field, such as role, permission, or identifier, the WG should describe the proposed extension and then discuss it with the SANA Operator and the identified Review Authority.
  Who the “official representative of a space agency” is must be formalized.

## Slide 9: SEA Proposal – “Agency Registries”
For any registry where the owner of the data is really an agency or other service provider, re-purpose and extend the SCID (CCSDS 320x0b6) and CAO / MACAO (CCSDS 630x0b1) registry structures and processes to provide a structure for managing the valid updates:
  Member Agency registry (includes sponsored agencies & other service providing organizations)
  Agency (or Org) Primary Point of Contact (Agency PoC) registry
  Agency (Org) Representative registry (for assignments, role based with different members & roles for different registries)
This should serve for:
  The agencies & representatives themselves …
  Observers and other service provider organizations
  SCIDs (for different protocols, plus names & aliases)
  Unique S/C identifiers (unique OID for each separate S/C, plus names & aliases)
And, (lower priority)
  Antennas (and stations)
  Service provider ports, catalogs, commitment offices
  Service provider/user identity/credentials
  Data provider identity/credentials
  Other “agency” assigned identifiers: LTP Engines, BP agents, SM&C services, AMS nodes, etc (now flat namespaces)

## Slide 10: Agency / Representative Model
CCSDS Agency /
Secretariat
Affiliate Agency (or Organization)
Spacecraft
SCID / OID
Org Primary
HoD or PoC
Sponsors (0…*)
Org has (1)
Appoints (1..*)
Org
Representative
Svc / Data Providers
Sites / Antennas
Service Access Pts
Service
Catalog
User / Provider Credentials
Has Role (1..*)
Manages
own data
Requests
All of these registries are created and managed by SANA, with their own specific policies. Derived from CCSDS 320x0b6.
Manages
own data
Org has (1..*)

## Slide 11: SEA Proposal – “Cross Cutting Registries”
For all registries where the scope cross-cuts more than one Area assign responsibility at the CESG level and delegate management as needed for operational purposes:
  URN Namespace (requested by WGs, managed by proposed XML Expert Group)
  XML registries (created / updated by WGs, managed by proposed XML Expert Group)
  CCSDS ISO OID top level registry – engineered (SSG ?)
  SANA as a whole (SSG)
  CCSDS Glossary, Terms, and Abbreviations (created / updated by WGs, managed by some new Terminology / Ontology Expert Group)
Expert Groups would be chartered and approved by the CESG, work largely via email and telecon, and be staffed by existing CCSDS experts in the subject matter. See later discussion.

## Slide 12: SEA Proposal – “Area / Local Registries”
For any registry where the creator / owner of the data is really a WG (or Area), assign responsibility for updates to the Area:
  Protocol identifiers, extensions, and version numbers (defined in a BB and often “fixed”)
  Catalogs, source lists, other locally managed information even if it is globally accessed (defined in a BB)
  WG specific data items (such as Nav 6-DOF & quaternions)
  Any ISO OID sub-registry specifically allocated to a WG (defined in a BB)
  Management may be “delegated down” to the WG by the Area as needed, which handles issues such as when a WG goes dormant

## Slide 13: Registry Category Management Model
CCSDS Agencies
Affiliate Organization
Spacecraft
SCID / ID
Agency
HoD
Agency
Representative
Svc / Data Providers
Manage data
CCSDS Expert Group(s)
XML
Registries
ISO OID
Top-level
Registry
SANA
Registries
CCSDS Glossary
URN Namespace
Manage data
CCSDS Area / WG
WG Catalogs
Delegated ISO OID Sub-tree registry
Protocol Identifiers
WG Source List
WG Local Registries
Manage data
Agency
Resources

## Slide 14: “Re-Purposing” the SCID Registry Structure
The SCID "registry structure" defines the following:
  Member Agency registry (all CCSDS member agencies, actually from MACAO) - we do not have a list for observer agencies or other “sponsored organizations”, except what is on the CCSDS web site, and we need them in SANA
  Agency Head of Delegation registry (the person the agency has delegated as HoD) - essentially the CMC for CCSDS member agencies
  Agency Representative registry (AR, for SCID assignments) - this list may have more than one entry per agency (multiple centers) and also entries for observer agencies (and others, sponsored by the Member Agencies) – probably should used role-based controls
The SCID doc (CCSDS 320x0b6) describes registry entries and the process for adding new ARs or affiliates, approved by the relevant CCSDS member agency (same country) or the Secretariat.
The MACAO describes Control Authorities (CA) and adding “descendant” / delegated authorities.
These, taken together, could provide a manageable framework for adding new "Agency Reps" and for handling requests for ”sponsored agency or service provider” type assignments.
Revise and extend this framework, with agreement, to cover situations where agencies or other service provider organizations have control over the content.
Revise registry and process to include truly unique, permanent, “spacecraft identifier”, i.e. OID, with spacecraft name, abbreviation, and aliases

## Slide 15: Expert Group Background
The SANA YB (CCSDS 313x0y1) introduced the term "designated expert" for a registry:
  "designated expert. The expert for that registry is assigned by the CESG based on the WG recommendation”
  This “expert” could be a group, it just needs to have a well defined policy and point of contact
The term "expert group" was specifically introduced in the draft XML Namespace Policy document (CCSSDS 315x1y0), but it has broader potential applicability:
"This document defines a CCSDS XML Expert Group to review the requests. This group is composed of XML experts nominated by the CESG with no pre-determined terms. CESG may choose to change the group as it see fits."
The intent, in both of these instances, was to identify an expert, or group of experts, who would have continuing cognizance over the management of some CCSDS resource (XML namespace, SANA registry) separate from the WG that created it.

## Slide 16: Expert Group Proposed Definition
SEA recommends definition of an new CCSDS entity called an "Expert Group", with the following characteristics:
  Created at request of a WG, SIG, Area, or the CESG itself
  Creation is approved by the CESG
  Role is to provide long term curation or management for contents of one or more registries
  Registries are managed in the SANA, the Expert Group supports SANA operations of the registry as stated in CCSSDS 315x1y0
  Membership and chair proposed by the creating group and approved by the CESG
  Membership is required to have expertise in the technical topic that is the subject of the registry
  Expert Group may be disbanded by the CESG
This definition of Expert Group is rather specific to the SANA and it could be defined in a revision to the SANA YB (draft update proposed)
There are not expected to be a lot of these Expert Groups and they will be regulated by the CESG.
Any Expert Group will operate using electronic communications such as email or the occasional telecons, as needed.
Expert Groups are not intended to require significant resources nor meeting rooms at bi-annual meetings, but might occasionally need a ½ day meeting.

## Slide 17: Current CCSDS OID Registry (CSS CCSDS 921x1r – CSTS Framework )
Object Identifier Label Assignment Policy for
the sub-tree (NULL)
1 iso
1.3 identified-organization
1.3.112 standards-producing-organization
1.3.112.4 ccsds
1.3.112.4.1 control-authority-registration-authority
1.3.112.4.2 control-authority-authority-description
1.3.112.4.3 space-link-extension
1.3.112.4.3.1 sle-transfer-services
1.3.112.4.4 csts
1.3.112.4.4.1 framework
1.3.112.4.4.2 services
CCSDS-MONITORED-DATA-OBJECT-IDENTIFIERS {iso identified-organization (3) standards-producing- organization(112) ccsds(4) css (4) csts(1) services (2) serviceIdentifiers(2) monitoredData (1) monitoredDataModules (4) identifiers (1)
Maintenance of the registry of the Functional Resource types, parameters, events, and directives under the crossSupportFunctionalities subnode is under the purview of the CCSDS Cross Support Services Area
Maintenance of the registry of the Functional Resource types, parameters, events, and directives under the agencyFunctionalities subnode is under the purview of designated Agency-level control authorities.
CCSDS-MONITORED-DATA-OBJECT-IDENTIFIERS module defined in annex B is registered with SANA. Maintenance of the SANA registry of this module and the OIDs contained within occurs as a result of changes in the published version of the Recommended Standard.

## Slide 18: Proposed Future CCSDS OID Registry (SANA)
Object Identifier Label Assignment Policy for
the sub-tree (NULL)
1 iso
1.3 identified-organization
1.3.112 standards-producing-organization
1.3.112.4 ccsds
1.3.112.4.1 organization, was control-authority-registration-authority
1.3.112.4.1.1 uniqueOrgOID
1.3.112.4.1.1.1 organizationName
1.3.112.4.1.1.2 organizationAddress, etc
1.3.112.4.2 persons, was control-authority-authority-description
1.3.112.4.2.1 uniquePersonOID
1.3.112.4.2.1.1 personName
1.3.112.4.2.1.2 personAddress, etc
1.3.112.4.3 space-link-extension
1.3.112.4.3.1 sle-transfer-services
1.3.112.4.4 css
1.3.112.4.4.1 csts
1.3.112.4.4.1.1 framework (modules, attributes, operations, proceduresExtensions, ` fwProceduresFunctionalities, serviceGenericIdentifiers)
1.3.112.4.4.1.2 services
1.3.112.4.4.1.2.1 serviceIdentifiers
1.3.112.4.4.1.3 externallyDefinedTypeAndValueExtension
1.3.112.4.4.2 crossSupportResources
1.3.112.4.4.2.1 crossSupportFunctionalities
1.3.112.4.4.2.2 agencyFunctionalities
1.3.112.4.5 serviceProviders
1.3.112.4.5.1 organizationReference
1.3.112.4.5.1… serviceProviderName, Location, Catalog, ServiceList
1.3.112.4.6 groundStationsAndAntennas
1.3.112.4.6.1 organizationReference
1.3.112.4.6.1… groundStationSite, Name, Location, antennaList
1.3.112.4.7 spacecraft
1.3.112.4.7.1 organizationReference
1.3.112.4.7.1… spacecraftName, Abbreviation, AliasList
1.3.112.4.8 agencyAssigned
1.3.112.4.8.1 agencyReference
1.3.112.4.8.1… agencyUnique

## Slide 19: Proposed Registry Management Update Process
Review and vet proposed Registry Management approach
Revise the SANA YB to align with new approach and clarify registry type / role / ownership processes
  Define and document Expert Group process & rules, define the needed ones and assign responsibility
  Add new registry request / creation procedure to clarify what is expected of the WGs
  Include SANA Expert Group section
  Require that the SSG, which includes the SANA Operator, be in the review path for any docs that include new registries
  Require that any new registries use existing registries for agencies, organizations, persons instead of haphazardly creating new ones
Augment SANA Agency, Observer, Provider and Expert registries as needed to cover new functions and fields, working closely with Areas WGs, and Agency Reps as necessary
  Coordinate with Secretariat technical staff
  Engineer the CCSDS OID registry structures and create new policy that supports all of the known and assumed future uses
  Revise the existing “Agency” registries to align with new approach
  Identify Agency (and other provider) PoCs, Reps, and Roles
Create a CCSDS Registry Management Policy YB to define the new approach and identify global, cross-cutting, registry type / role / ownership rules, policies, and processes
Revise the SCID registry document (CCSDS 320x0b6) to align with new features
Revise the MACAO registry document (CCSDS 630x0b6) to align with new features

## Slide 20: BACKUP SLIDES

## Slide 21: SCID Agency / Representative View
CCSDS Agency /
Secretariat
Affiliate Agency (or Organization)
Spacecraft
SCID / OID
Org Primary
HoD or PoC
Sponsors (0…*)
Org has (1)
Appoints (1..*)
Org
Representative
Has Role (1..*)
Requests
All of these registries are created and managed by SANA, with their own specific policies. Derived from CCSDS 320x0b6.
Org has (1..*)

## Slide 22: MACAO Agency / Representative View
CCSDS Agency /
Secretariat
Affiliate Agency (or Organization)
Org Primary
HoD or PoC
Sponsors (0…*)
Org has (1)
Appoints (1..*)
Org
Representative
Agency 1 Primary MACAO
Has Role (1..*)
Manages
Establishes (0..*)
All of these registries are created and managed by SANA, with their own specific policies. Derived from CCSDS 320x0b6 and CCSDS 630x0b2.
Org has (0..1)
CA Agent
(SANA)
Agency 1 Descendant MACAO
Agency 2 Primary MACAO
Agency 2 Descendant MACAO
Establishes (1..*)
Establishes (0..*)
Requests

## Slide 23: SCID Registry Features
CCSDS GSCID assignment procedures (CCSDS 320x0b6).
Defines Agency Representative, assigned by Agency Head of Delegation (Agency HoD), to manage the requesting and relinquishing of CCSDS Spacecraft Identifiers.
The CCSDS member agencies (or observer agency) creates an Agency Rep. There is no guidance for adding observer agencies or other service providers.
"CCSDS SCID assignment and management, on an international basis, must be viewed as a cooperative effort among the CCSDS Agencies, with each constituent acting as agent for the users under its cognizance."
The Secretariat has overall responsibility for managing this registry, and that has now been delegated to the SANA, along with the registry of Agency HoD and Agency Representatives. The SANA Operator acts as the "expert" for assigning SCIDs.

## Slide 24: CAO / MACAO Features
Part of CCSDS SFDU specifications (CCSDS 630x0b1)
Defines a CCSDS Control Authority Agent (CA Agent) and the Member Agency Control Authority Office (MACAO).
Defines a hierarchy of CAOs rooted in the CCSDS Secretariat and the CA Agent. The CA Agent was at WDC-A, but that has been defunct for a while.
There is an explicit process for adding “descendent MACAOs”, below agency level
It's intended purpose when it was set up was to provide the means to “manage transfer and usage of SFDUs by providing data description registration, revision, and dissemination services".
SFDUs are still in use, as are the MACAO's, and this set of registries are tied in a hierarchical fashion to space agencies as the ”authorities”.
The “registries” tend to be specified as flat files on a web page and they are often out of date.

## Slide 25: NDM XML Features
CCSDS Navigation specifications in XML (CCSDS 505x0).
Defines a CCSDS Common set of terms and a Nav WG common set of terms across all Nav WG schema.
Includes a definition “originator” that suggests “agency”, but apparently may be of any form, various ones are used in examples.
The original non-XML specs, such as CCSCS 502x0, defined originator as “Creating agency or operator (value should be specified in an ICD). The country of origin should also be provided where the originator is not a national space agency.”
Its intended purpose is to specify a format for use in exchanging spacecraft navigation data. Such exchanges are used for distributing attitude, orbit, and tracking data between space agencies.
The XML schema are in a set of SANA registries and these are referenced in the spec.
The Nav XML schema also define a set of “Common” terms that really belong in some higher level, CCSDS global, registry.

## Slide 26: Service Management (SM) Features
The current CCSDS SM spec (CCSDS 910x11) includes a set of XML schema.
Defines Supported and Supporting Agency, but these are just 256 character strings, there is no defined registry. The XML schema themselves are defined in a separate CCSDS document (CCSDS-910.11-B-1_XML_schemas).
The CSSM is now being de-defined as a set of separate documents, each with their own data formats that probably will use XML schema for exchange, as does NDM XML (CCSDS 902x0).
The concept of Supported and Supporting Agency persists, but these are just 256 character strings, there is not yet a defined registry.
CSSM requires XML schema registries, as well as some form of supported / supporting agency registry. This is likely to be similar (at least conceptually) to what is referenced in NDM XML.
CSSM (and other services still in work MD-CSTS and SC-CSTS) are planning on using ISO defined OIDs to reference a new class of entities called Functional Resources. These will have type definitions in the CCSDS Object Identifier Tree:
  { iso identified-organization(3) standards-producing-organization(112) ccsds(4) css(4) crossSupportResources(2) crossSupportFunctionalities(1)}

## Slide 27: Some simple practical steps?
Adjust procedures manual to recommend check of SANA registries for semantic overlaps, etc, not just update policy
  Update mandatory SANA Considerations section in pubs manual, etc
  Update to boot-camp slides as well
CESG to consider what a coordinated policy for registry updates looks like
  Current “laissez-faire” approach (each recommendation defines whatever it wants for registry content/update policies) is probably not okay?
  How much change is needed and can be supported?
    Means to resolve registry overlaps prior to poll (in affect this has already happened re a CSS recommendation, but CSS Area can not remove the condition on its own)
Suggest that overall management be folded into SE architecture and/or ontology work and that SE Area take the lead in determining proper approach
  As part of overall information architecture for CCSDS ?

## Slide 28: Near-term Adjustment?
WGs Develop Recommendations and Check Registries
ADs/DADs Oversight
CESG Agency Review Poll
CESG Check
AD signs off on registry management as part of requesting CESG release polls
CESG checks and request proper remedial work if overlapping registry definitions exist