## Slide 1: Cross Support, Mission Operations and Spacecraft On-board Services & Interfaces
Peter Shames
8 July 2015

## Slide 2: CCSDS CSS, MOIMS (SM&C) and SOIS
CCSDS has two sets of “services & interfaces” that have been identified as having a possible overlap:
  Cross Support Services (CSS: SLE, CSTS, SM)
  Spacecraft Monitor and Control (SM&C: mission operations).
The CSS services are specifically designed for interoperable space link cross support, they are quite mature and the SLE services have been in use for years, implemented by many agencies.
  The relationships between CSS, SLS, SIS and SEA are already very well documented in the SCCS-ARD (CCSDS 901x1m1) and ADD (CCSDS 901x0g1)
The SM&C application layer services are designed in a general fashion for mission operations. Parts of them have been prototyped over the years, using bi-lateral ICDs, and they are just now developing an interoperable set of specifications but they do not have any application layer services comparable to SLE or SM.
SOIS has a set of abstract on-board services that are largely application support, device and local communications services. There is not yet a solid SOIS to MOIMS mapping.
  There are only some older SM&C / SOIS mappings (MoU) and other study materials to draw upon in this context.
This quick overview drawn from existing materials explores this in more detail.

## Slide 3: Partial Standards Relationship Sketch (CSS Area Point of View – an example)
Specify links to Communicate with
Specify control of on-board activities of
Space Link &
Cross Support
Mission
Operations

## Slide 4: CSS and MOIMS Interface Alignment (from London Fall 2014 discussions)
MO Services are uniformly defined to use the MAL as a common data messaging layer.
MAL must be mapped “into a specific and unambiguous encoding of the messages and to a defined and unambiguous mapping to a specific data transport” using a MAL technology mapping and transport adapter.
The key technology mapping relevant for space links is the MAL to SPP adapter.
The standard, interoperable, cross-supported, means for transporting SPP over CCSDS space links is to insert SPP formatted data into TC, TM, or AOS frames and to use the SLE (F-CLTU, RAF, RCF) services to transfer them from a MOC to an ESLT.
The standard, interoperable, cross-supported, means for planning, scheduling, configuring and monitoring CCSDS space link services in an ESLT is to use CCSDS SM (& CSSM)
Other space link related data types (monitor, radiometric, and future service control) have CSTS cross-support service interfaces in process. The CSTS framework is mature.
SM&C may embed CSS service user interfaces within the relevant MO functions, or it may develop interface adapters that conform to CSS service user interfaces on one side and MO/MAL interfaces on the other.
Either approach is completely compliant with CCSDS cross support and interoperability standards and interfaces and provides a straightforward means of interfacing the whole SM&C suite to any agency’s space link services.

## Slide 5: Relationship of SM&C MO to other CCSDS Standards (from CCSDS 520.0-G-3)
CSS (SLE, CSTS, CSSM)
SLS (link & lower layers)
SOIS Services

## Slide 6: SCCS-ADD Figure 5‑1: Generic ABA Building Block and Functions
Each generic Link-Layer ABA node type contains these functions, Mission Operations functions are inside the pink function ovals.
Generic ABA Node
Application 1
Application 2
Element Management
Data
Store
Data Forwarding
Link Type A
Link Type B
Link B Processing
Link A Processing
Mission
Operations
Space Link &
Cross Support
Notes: 12/12: We reference “Node” in the figure, but the caption/figure title reflects “Building Block”—are we using the terms interchangeably? They should probably at least match between figure and figure title.

## Slide 7
SCCS-ARD (CCSDS 901x1m1) - Figure 7-4:
SSI Secure End-to-End Forward: SSI Agency Supporting SSI Agency
Earth-Space
Link Terminal
Earth User Node
Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
SSI
SSI
SSI
VC X
CMD
VC X
AOS/TC
RF & Mod
C & S
CFDP
ENCAP
Space Msg
Application
Space File Application
BP
AMS
LTP
RF & Mod
IP
C & S
F-Frame
Mux F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
AOS/TC
BP
To VC X
User File Application
IP
TCP
BP
User Msg
Application
CMD
CFDP
AMS
IPSEC
File Secure
SBSP
File Secure
SBSP
SBSP
SBSP
IPSEC
TCP
MOIMS SM&C
Apps
MOIMS SM&C
Apps
Notes: 12/12/12: New slide from Peter. Figure title in document is shown above. PPT original figure title is “SSI Secure Single Link Cross Support – Forward
(File, Frame & Message all DTN)
7

## Slide 8: SCCS-ARD (CCSDS 901x1m1) - Figure 7-2: SSI End-to-End Forward: All DTN
Earth-Space
Link Terminal
Earth User Node
Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
SSI
SSI
SSI
VC Z
VC X, Y, & Z
Prox-1
UHF
C & S
ENCAP
Space File Application
BP
CFDP
RF & Mod
IP
TCP
C & S
F-Frame
Mux F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
AOS/TC
BP
To
VC Z
User File Application
IP
TCP
BP
CFDP
Space Routing Node MOC
SSI
To
VC X
To
VC Y
User File Application
IP
BP
User Pkt
Application
CMD
CFDP
EP or SP
F-Frame
TCP
Space Routing Node
SSI
UHF
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
Prox-1 Link
RF & Mod
ENCAP
BP
LTP
VC Y
CMD
EP or SP
Space Pkt
Application
C & S
AOS/TC
VC X
Space File Application
CFDP
Proximity Space
CCSDS Protocols
AOS/TC
Notes: 12/12/12: Figure title here on slide is what’s in the document. Original figure title in PPT file is “ABCBA SSI Agency supported by SSI Agency - Forward, with legacy commanding”
8

## Slide 9: Cross Support / Mission Operations Interactions using Standard SLE / SM Services
ABA
ESLT
Earth User
Node
User Service Management Application
(Planning & Scheduling)
User Application
(Packet Processing)
User RCF Application
(Frame Processing)
User Radiometric
Data Processing
User Service Monitor Data Processing
User F-CLTU Application
(CLTU Processing)
Service
Delivery (SD)
Interfaces
Service
Management (SM) Interface (I/F)
Flight
Dynamics
Planning
Schedule
Execution
Monitor &
Control
SM over HTTP
F-CLTU over TCP
R-CF over TCP
MD-CSTS over TCP
TD-CSTS over TCP
SLE F-CLTU
Processing
SLE RCF
Processing
(Frame De-Muxing)
TD-CSTS
Processing
(Real-time Radiometric Data)
Service Management Processing
(Monitor Data)
Service Management Processing
(Scheduling)
SM&C MO Applications
(MAL Compliant)
MAL & Transport Adapter for SPP
Notes: I changed the lines here from dashed to solid.
7/25: Changed to ESLT now that the term is defined before this graphic.
Note that Earth-Space Link Terminals, while shown here, isn’t mentioned in the document until section 3. In part, that’s why I’ve not adjusted the term to show as “ESLT”.

## Slide 10: Pietras’ SM&C and CSS diagram 8 March 2007 Telecon Notes
Onboard Software Management
Onboard Data Product Management
Onboard
M&C
Onboard
Schedule
Execution
Complex
Management
(CM) (CS)
SL Comm & Transfer Services
Time & Location (MO) / Radiometric (CS) & Transfer Services
Flight Dynamics
Planning (MO) / UM (CS)
Schedule Execution
M&C (MO) / UM (CS)
Software Management
Payload Software Management
Data Product Management
Payload
M&C
Payload
Planning
Space Element (CS) /
Flight Segment (spacecraft) (MO)
Ground Element (CS) /
Ground Segment (MO)
Mission Data Operations System (CS)
Payload Operations Centre (MO)
Mission Control Centre (MO)
SLE Complex (MO) /
Ground Station (MO)

## Slide 11: Mission Operations Services Overview (from MOSC 520x0g3)
CSS (SLE, CSTS, CSSM) and
SLS (link, coding, modulation)
live in here (not shown)
SOIS lives in here
(not shown)

## Slide 13: MOIMS SM&C Abstract Service Model (from MORM 520x1m1)

## Slide 14: Activity Relay Model w/ AMS & MTS (from COM 521x1b1)

## Slide 15: MAL Abstract Service (from MAL 521x0b2)

## Slide 16: SOIS S/C On-Board Services
SOIS has a set of on-board services at “network” layer and below, for communication and device management, and at application layer
SOIS has a high level view of their on-board services
There are also evolving views of the abstract details of the insides of these services
  Figures from the latest SOIS EDS document, 876x0r0
There is little material showing the relationship between MOIMS and SOIS

## Slide 17: SOIS Service Architecture Focus on C&DA (from 876x0r0)
MOIMS SM&C O/B Services
are some of these

## Slide 18: “Plug and Play” View of SOIS Architecture (from 850x0g1)
SM&C MO Applications
(MAL Compliant)
MAL
MTS / AMS?

## Slide 19: SOIS C&DA Service Internals (from 876x0r0)

## Slide 20: SOIS DVS / DAS & EDS Functions Relationship to MCS (from 876x0r0)

## Slide 21: SOIS and MOIMS Services
The inter-relationship between SOIS and SM&C was studied back in 2003, when SM&C was just getting started
The attached materials, including those from the SOIS MOIMS MOU, are probably still relevant

## Slide 22
SOIS – MOIMS MoU
Service | Description
SM&C | Core Monitoring and Control service.
Automation | Activity automation management.
Scheduling | Activity scheduling.
Interaction | Operator notification and interaction.
Planning | Constraint and resource planning.
Flight Dynamics | Orbit determination, flight plan generation, and manoeuvre generation.
Time | Time correlation and modification.
Location | Tracking, ranging, and position services
Data Product Management | File management and transfer, both ground based and onboard.
Software Management | Software versioning, patching, and release.
The MOIMS Services

## Slide 23
SOIS – MOIMS MoU
The SOIS Services
Service | Description
Command & Data Acquisition | Provides access to onboard sensors and actuators.
Time distribution | Distributes the spacecraft onboard time to users.
File Transfer | Transfers files between onboard users.
Messaging | Provides message transfer capability to onboard users.

## Slide 24
SOIS – MOIMS MoU

## Slide 25
SOIS – MOIMS MoU
CSS (SLE, CSTS, CSSM) and
SLS (link, coding, modulation) live in here

## Slide 26: Proposed MO / MAL / SPP Mapping Diagram
MAL Transport Mapping to SPP
(data types & protocol fields)
MAL to Language “x” API
MAL API
Interface
MAL Transport
Implementation
All APIs expose the same services
All implementations have the same behavior
All bindings to the same transport use the same message structures and field specifications

## Slide 27: AMS mapping to MAL AMS BB Pg 2-5

## Slide 28: ESA SM&C / SOIS Future Architecture (from EGOS-GEN-SMCSOIS-TN-1001 1)
CSS (SLE, CSTS, CSSM) and
SLS (link, coding, modulation) live in here
SOIS

## Slide 29: SOIMS & SM&C Services “RASDS Cartoons” from 2003 study
The following RASDS style diagrams were developed during the early SOIS and SM&C discussions, Dec 2003
They appear to still be highly relevant, but need to be brought up to date to current SOIS and MOIMS services and component descriptions

## Slide 30: General SM&C Connectivity Model
Target
Model
SM&C Service Agent
Controller
SM&C Application
Comm.
Protocols
Target
SM&C Service Agent
SM&C Application
Comm.
Protocols

## Slide 31: End-to-End SM&C w/ Example Comm Protocols
S/C
Model
SM&C Service Agent
Ground
SM&C Application
SPP
Spacecraft
SM&C Service Agent
SM&C Application
SPP=Space
Packet
Protocol
Space Data Link
RF & Mod
SPP
Space Data Link
RF & Mod

## Slide 32: SOIS Command and Data Acquisition Service
C&DA is a core SOIS service that provides low overhead access to read data from simple sensors and to write to simple hardware interfaces.
C&DA is intended to provide the means to access sensors, effectors, and transducers that are connected via a number of different physical means and deployed in a variety of topologies, including hierarchical configurations.
C&DA implements the common M&C Protocol Services in order to communicate with other control applications.
C&DA also uses the common M&C Protocol Services to communicate with devices it controls
  Simplest devices may use a proxy to implement M&C functions and protocols
  More capable devices may directly implement M&C functions and protocols
Extended C&DA functions may be provided by a set of related services that perform data fusion, simple analysis, limit checking and results storage for access by other onboard services.

## Slide 33: SOIS Command and Data Acquisition Service, contd
C&DA access to devices is supported by a virtualization service that implements a set of virtual generic device models. This may be provided by device drivers for each class of device / link that implements the virtual device for the specific transducer, sensor or effector, or by smart devices themselves.
  This is a hardware abstraction layer (HAL).
A Plug & Play Service maps actual device characteristics onto the virtual device model. It may use information read directly from the device, ala USB or IEEE 1451, or may use a table driven approach to identify specific device characteristics.
  Device characteristics may include: attributes, engineering units, variables, parameter arrangement & relationships and calibration information.
The C&DA services may be called by other onboard services, such as the S/C Monitor and Control Service.

## Slide 34: Simplest On-board C&DA Proxy agent for simplest transducer
Device
Model
Controller
Device
Onboard
Data Link
Onboard
Physical
Onboard
Data Link
Simplest
Transducer
Device
Proxy / Driver
SM&C Service Agent
Onboard
Physical
C&DA Application
Device Virtualization

## Slide 35
Six extended capability sets (contd.):
  Data Product Acquisition: data from multiple sensors are accessed with a single read command, and the resulting product is a result of calculations based on data from the multiple sensors
  Data Pooling/Data Base: collection of data from sensors into a data pool (or data base) of recent readings
  Device Virtualization: where devices are read and controlled by using a virtual generic device image or model
  Device Access: conversion of user- supplied logical address into the network address, allowing device to be addressed from anywhere in the network
SOIS: Command and Data Acquisition Service

## Slide 36: SOIS Command and Data Acquisition Service
C&DA is a core SOIS service that provides low overhead access to read data from simple sensors and to write to simple hardware interfaces.
Extended C&DA functions are provided by a set of related services that perform data fusion, simple analysis, limit checking and results storage for access by other onboard services.
C&DA access to devices is supported by a virtualization service that implements a set of virtual generic device model and by device drivers for each class of device/link that implements the virtual device for the specific transducer, sensor or effector. This is a hardware abstraction layer (HAL).

## Slide 37
A Plug & Play Service maps actual device characteristics onto the virtual device model. It may use information read directly from the device, ala USB or IEEE 1451, or may use a table driven approach to identify specific device characteristics.
Device characteristics may include: attributes, engineering units, variables, parameter arrangement & relationships and calibration information.
The C&DA services may be called by other onboard services, such as the S/C Monitor and Control Service.
SOIS Command and Data Acquisition Service

## Slide 38: Data Pooling & Device Virtualization Services (from 871x1m1)

## Slide 39: SOIS Command and Data Acquisition Service Elements
C&DA
PnP
Service
DN - EU Conv
Data Product
Acquisition
Data
Monitoring
Data
Repository
Transducer
Device Access: Conversion of user- supplied logical address into a physical address
Device
Driver
Name/Addr
Mapping
Engineering Unit Conversion: Conversion of raw sensor data into engineering units
Data Product Acquisition: Data from multiple sensors are accessed with a single request and data products are produced
Data Monitoring: Comparison of monitored sensor data against red and yellow limits
Device Virtualization: Devices are read and controlled using a virtual generic device image or model. May be implemented in Driver or in Transducer itself.
Data Repository: Collection of data from sensors into a data base of recent readings
Plug & Play Service: Provides means for mapping actual device capabilities (device announced or table driven) onto virtual device model
Transducer: Physical sensor or effector connected via some link (physical or RF)
Device Driver: Implements virtual device model for specific transducer & link
Device
Virtualization

## Slide 40: Command and Data Acquisition Service Relationship to Monitor & Control Service
C&DA
PnP
Service
DN - EU Conv
Data Product
Acquisition
Data
Monitoring
Data
Repository
Transducer
Device
Driver
Name/Addr
Mapping
Device
Virtualization
Mon & Con
Service
Spacecraft Mon & Con Service: S/C service to control, monitor and manage resources, accept ground Data System (GDS) requests and supply responses
Command and Data Acquisition Service: send commands to transducers, read, process, and store results, perform limit checking
Standard M&C Protocol: Used by both the SM&C and C&DA services. Provides common communication for monitor & control.

## Slide 41: Example C&DA Protocol Services
Send Directive to Target
  Confirmed or Unconfirmed
  Immediate, triggered, or timed
Read State of Target
  Confirmed or Unconfirmed
Trigger Execution of Target
Send Indication to Controller
  Confirmed or Unconfirmed
Send Event to Controller
  Confirmed or Unconfirmed
Send Confirmed sensorDirective Immediate
Send effectorConfigParam Timed
Send sensorDirective Triggered
Send Confirmed FPGALoad Triggered
Read unConfirmed sensorState Immediate
Read effectorExecutionState Immediate
Read transducer Immediate
Trigger Confirmed FPGALoad
Trigger effector Immediate
Indicate FPGALoadComplete
Indicate FPGALoadVerificationComplete
Indicate effectorExecutionComplete
Indicate sensorDirectiveTriggered
Event overTempDetected
Event transducerValue
Event sensorFault
Event effectorOffLine
C&DA Examples

## Slide 42: Command and Data Acquisition Service TCP/IP Network Access to “Smart Device”
Data Link
Physical
Data Link
Physical
TCP/IP
TCP/IP
PnP
Service
Device
Driver
C&DA
DN - EU Conv
Data Product
Acquisition
Data
Monitoring
Data
Repository
“Smart” Device
Transducer
Device
Virtualization
Control Node

## Slide 43: Command and Data Acquisition Service Using MTS to access device on another node
C&DA
DN-EU Conv
Data Product
Acquisition
Data
Monitoring
Data
Repository
Data Link
Physical
Data Link
Physical
TCP/IP
TCP/IP
MTS
MTS
PnP
Service
Remote
C&DA
Transducer
Device
Driver
Remote C&DA & Device
On Remote Node
C&DA link to remote device uses remote C&DA agent connected by MTS which provides the message transport function
Device
Virtualization
Control Node

## Slide 44: Device Enumeration Service (from 871x3m1)

## Slide 45: Some Thoughts on SOIS and SM&C
SOIS would benefit from having a more complete set of on-board architecture diagrams for the services they have presently defined.
  The existing set of architecture diagrams are somewhat sketchy and incomplete
  These older diagrams, and the SOIS BB & MB diagrams, need to be updated to current state of the art
The mapping from MOIMS SM&C to SOIS on-board services is weak and incomplete at this point.
SM&C has some features such as a message abstract layer (MAL) and M&C services (still in formulation) that could potentially be mapped onto SOIS spacecraft on-board functions.
However, SOIS and SM&C will need to define the specific relationships between their respective sets of services, these do not exist in SM&C or in MOIMS today in any formal specs.
SOIS could directly adopt MTS over AMS as a messaging protocol, but it is not clear that is necessary. In any event there needs to be some concrete MAL to message bus mapping, if not AMS then what?

## Slide 46: Summary
CSS / SLE standards already provide a mature, widely deployed, set of interoperable cross support service interfaces.
CSS/ CSTS is maturing a new, interoperable, cross support service framework: monitor data (MD), tracking data (TD), service control (SC) and forward frame.
CSS / Cross Support Service Management (CSSM) provides an interoperable framework for planning, scheduling, configuring, monitoring and reporting on cross support services.
All of these, space link services, and even SIS and MOIMS Nav are included in the SCCS – ARD architecture which is a “foundation” for any application layer work.
SM&C has a set of application layer services that are still maturing, as are the interoperable MAL bindings. The SPP binding provides an obvious connection to space link services.
SM&C has agreed to map their application services for planning, scheduling, and accessing space links to the CSS services and interfaces.
SOIS has a set of abstract on-board services, but few concrete mappings. There are some obvious mappings that can be made between some of the SOIS application support services and the corresponding SM&C services.
Further work must be done to refine the SOIS on-board services and the SM&C on-board services and their relationships.
  This must include SM&C to SOIS service mappings (not yet done)
  This must include a concrete mapping between MAL and MTS, possibly using AMS

## Slide 47: BACKUP SLIDES
Service provider protocol stacks from SCCS-ARD
Service user protocol stacks from SCCS-ARD

## Slide 48: High Level Comparison of Cross Support and Mission Operations “Framework” Features
Cross Support
  Focus specifically on space communications cross support for service planning, request, forward / return data delivery and accounting
  Provides direct support for all space link service features
  Concrete specs for SLE/CSTS service interfaces, defined SM messages, interaction patterns, and services, and data transfer services and behavior, including normative XML and ASN.1 bindings
  Rely upon underlying data transport layers, SMTP & HTTP, TCP/IP are being used
  There is a formal data transport binding for SLE / CSTS to TCP/IP
Mission Operations
  Abstract set of services for common mission operations functions, largely terrestrial, but proposed for space
  Specifies an abstract message layer and common object model that may be generally applied in mission operations context
  Does not (yet) include either a concrete message spec, data representation binding, nor a data transport binding, these all must be specified separately
  Require use of space links and cross support services to plan for comm services, transmit commands and data, and receive telemetry, science, radiometric and accounting data

## Slide 49: MOIMS SM&C Standards (core only)
Message Abstraction Layer (MAL, CCSDS 521.0-B-2)
  Abstract interfaces, services, and message types
  Transactions and state transitions
  Abstract message composition
  Message interaction patterns
  Abstract access interface and transport layer interface
  Require a “transport mapping from the abstract MAL data structures into a specific and unambiguous encoding of the messages and to a defined and unambiguous mapping to a specific data transport ”
  XML schema may be used as the “message body type”
Common Object Model (COM, CCSDS 521.1-B-1)
  Abstract common object model (used in MAL) and abstract common services
  Objects have domain, types, relationships, unique identifiers and instances
  Services are event (publish), archive (CRUD), and activity tracking (progress signals)
  Activity / event chaining is described
  COM messages are described in terms of the MAL, and MAL fields are described in the COM
  There is a “normative” XML schema in SANA, but it is in the wrong place and ambiguous
Common Services (CCSDS 522.1-R-2)
  Defined in this draft Blue Book
  Services are: Directory, Login, Service Configuration, Interaction, and Replay
  Abstract services that use MAL messages and COM objects
  There is not yet even a reference XML set of service specifications
Service Management Application
  There is no service management application defined in the MORM (CCSDS 520.1-M-1)
  It might be part of the Planning function as referenced in the MO Service GB (CCSDS 520.0-G-3), but this is not clear and that is a Green Book
Transport Layer
  The only concrete transport layer spec at this point is a draft Red Book (CCSDS 524.1-R-0.1) for the Space Packet Protocol (SPP)
  This provides a concrete binding from the MAL abstractions to the SPP packet structures, this requires a further mapping onto CCSDS space links or some other underlying transport or link protocol

## Slide 50: The Nominal MO / MAL / SPP Mapping (From CCSDS 524.1-R-0.1 )
Produces / consumes SPP packets, requires a transport protocol

## Slide 51: SM&C use of the MAL
The MAL defines abstract interfaces, services, and message types; transactions and associated state transitions; abstract data types & message structures; and message interaction patterns. These are defined abstractly in a tabular form.
The COM defines a common object model (used in MAL) and a few abstract common services. Objects have domain, types, relationships, unique identifiers and instances. The common services are event (publish), archive (CRUD), and activity tracking (progress signals). COM service messages are described in terms of the MAL, and MAL fields are described in the COM.
In order to create an interoperable service a separate “technology mapping” must be defined. The technology mapping translates these abstract messages and data objects into concrete message transfers with an “on-the-wire” bit representation.
The technology mappings must translate the concrete MAL service and message model into a specific protocol tied to specific protocol data units (PDU). The technology mapping recommendation casts the MAL abstract data types and messages into specific bit representations appropriate to that protocol.
There are is only one draft technology mapping that is available and that is to SPP. SPP is a simple data structure suitable for use within a transport or link protocol such as TC or TCP/IP, but there is no spec for this binding.
There are not yet any application services, such as R-AF or SM service request handling, built using the MAL, that could directly substitute for the existing SLE and SM services. The services defined in the COM are defined in abstract terms in just a few pages, behavioral specifications are scant.
There is an XML schema for the MAL, but there is no directly transformable specification for SM&C services as there is for SLE; any service must be programmed by hand based on these three documents.

## Slide 52: SLE & CSTS use of ASN.1
SLE and CSTS services, PDUs, and data objects are all defined using ASN.1. Each document contains the complete, directly implementable, specification.
Abstract Syntax Notation (ASN.1) is an ISO spec (Information Technology—Abstract Syntax Notation One (ASN.1): Specification of Basic Notation. International Standard, ISO/IEC 8824-1:2008. 4th ed. Geneva: ISO, 2008.)
ASN.1 can describe, in unambiguous terms, specifications for data, structures, syntax, interfaces, and protocol data units
ASN.1 may be directly compiled into executable code using one of several COTS compilers
There are several different, specified, “on-the-wire” bindings from ASN.1 to bit-level data transfer syntax, see Information technology — ASN.1 encoding rules: Specification of Basic Encoding Rules (BER), Canonical Encoding Rules (CER) and Distinguished Encoding Rules (DER), ISO/IEC 8825-1:2008 and also packed and XML encoding rules
Both ESA and JPL have used ASN.1 compiled code to directly create interoperable, validated, service implementations, as have X.400, X.500, LDAP, SNMP & UMTS.

## Slide 53: SCCS-ADD Figure 2-2: Basic ABA Configuration
Space User
Node
ABA
ESLT
Earth User
Node
Terrestrial Service Provider Interface
Space-Link Service Provider Interface
Service
Management
Interface
Mission Operations terrestrial services are inside this element
CSS SM & SLE services are inside this element
NOTE: All figures are either directly borrowed from the SCCS-ADD (CCSDS 9021.0-G-1) or are annotated or expanded versions of those figures, as noted
Notes: I changed the lines here from dashed to solid.
7/25: Changed to ESLT now that the term is defined before this graphic.
Note that Earth-Space Link Terminals, while shown here, isn’t mentioned in the document until section 3. In part, that’s why I’ve not adjusted the term to show as “ESLT”.

## Slide 54: CSS Service and Interfaces
Service Management (SM)
  Service Management spec (CCSDS 910.11-B-1)
  Future Extensible Cross Support Service Management spec (CCSDS 902.0-G)
Service Delivery (SD)
  Forward CLTU (CCSDS 912.1-B-3)
  Return (All / Channel) Frames (CCSDS 911.1-B-3 & 911.2-B-2)
  CSTS Framework (CCSDS 921.1-R )
  Monitor Data (CCSDS 922.1-R)
  Radiometric (CCSDS 922.2-R)
  Future Generic File Transfer, Service Control, F-Frame specs

## Slide 55: SCCS-ADD Figure 4‑1: ABA Service View
ABA CSSE
UE (e.g., User MOC)
Service
Delivery (SD)
Interfaces
SD
I/F
SM
I/F
Service
Management (SM) Interface (I/F)
Service Production
CCSDS Cross Support
Service Management
CCSDS Cross Support
Transfer Services
SD
I/F
SM
I/F
Earth User Node
(UE Service User)
Space User
Node
ABA ESLT
(CSSE Service Provider)
Space
Link
Service Management
Service Provision
Position & Timing
Services
Radiometric
Services
Return Data
Delivery Services
Forward Data
Delivery Services
Notes: 12/2012: Removed “(e.g. Network)” from ABA CSSE box per John Pietras/Peter Shames direction (via e-mail).
Unclear why some items are italicized. Suggest removing italics.
Changed to solid lines

## Slide 56: Figure 6-1: ESLT Fwd / Ret Service Provider Protocol Stack Building Blocks
SLE F-CLTU
Processing
RF & Mod
TCP
SLE RAF
Processing
TCP
Frame Sync & De-Code
CSTS F-Frame
Processing
(Frame Muxing)
TCP
Code & Sync
SLE RCF
Processing
(Frame De-Muxing)
TCP
a) SLE F-CLTU
b) SLE RAFs
c) CSTS F-Frame
(multiplex)
d) SLE RCFs
(de-multiplex)
SLE F-CLTU
CSTS F-Frame
SLE RAF
SLE RCF
Frame Sync & De-Code
IP
RF & Mod
IP
RF & De-Mod
IP
RF & De-Mod
IP
Notes: 03 Jan 14 Changed back to Processing for all “function ovals”
11/28/12: Changed only the SLE F-CLTU Production and SLE RAF Production to read “Provision” instead of “Production” per Peter’s 11/25/12 e-mail.

## Slide 57: Figure 6-3: ABA Service-User Service Management Building Blocks
ESLT Service Management Processing
(Planning & Scheduling)
IP
TCP
HTTPS
SCCS-SM
User Service Management Application
(Planning & Scheduling)
IP
TCP
HTTPS
SCCS-SM
a) ABA ESLT Service Management
b) ABA User Service Management
NDM or ODM
Notes: 7/12: Made minor alignment adjustments.//cys

## Slide 58: Figure 6-8: Service User / Provider ABA CSTS Forward-File Building Block
CSTS F-Frame
Delivery Service
(Frame Muxing)
RF & Mod
IP
TCP
Code & Sync
Encapsulation
TC/AOS Link Framing
CSTS Forward-
File Processing
CFDP
a) ABA CSTS Forward-File Service Provider
Using CFDP File Delivery over SPP and CSTS F-Frame
CSTS F-Frame
User CSTS Forward-
File Application
IP
TCP
CSTS Transfer File
b) ABA User CSTS Forward-File
(Requires CSTS Transfer-File in Service Provider)
CSTS Transfer File

## Slide 59: Figure 6-10: ABA Service-User CLTU & F-Frame Building Blocks
User F-CLTU Application
(CLTU Processing)
IP
Code & Sync
TC Frame
User F-Frame Application
(Frame Processing)
IP
TCP
CSTS F-Frame
a) ABA User SLE F-CLTU
b) ABA User CSTS F-Frame
TCP
SLE F-CLTU
User Application
(Packet Processing)
User Application
(Packet Processing)
AOS/TC Frame
Notes: 7/12: Made minor alignment adjustments.//cys

## Slide 60: Figure 6-11: ABA Service-User Protocol Return-Frame & CFDP Building Block
b) ABA User CFDP File Return
over SPP and SLE RCF
User RCF Application
(Frame Processing)
IP
AOS/TM Frame
User RCF Application
(Frame Processing)
IP
TCP
SLE RAF or RCF
a) ABA User Return SLE RAF / RCF
TCP
SLE RAF or RCF
User Application
(Packet Processing)
AOS/TM Frame
User CFDP Return-
File Application
Encapsulation
CFDP
Notes: 7/12: Made minor spacing adjustments.//cys

## Slide 61: Figure 6-12: ABA Service User Radiometric / Monitor & Service Data Protocol Stack Building Blocks
a) User Radiometric Data Processing
User Radiometric
Data Processing
TCP
TD-CSTS
IP
User Service Control Data Processing
TCP
SC-CSTS
IP
User Service Monitor Data Processing
TCP
MD-CSTS
IP
b) User Monitor Data Processing
c) User Service Control Data Processing
Notes: 03 Jan 14 Changed back to Processing for all “function ovals”
11/28/12: Changed only the SLE F-CLTU Production and SLE RAF Production to read “Provision” instead of “Production” per Peter’s 11/25/12 e-mail.

## Slide 62: Cross Support / Mission Operations Interactions using SPP Mapping
ABA
ESLT
Earth User
Node
User Service Management Application
(Planning & Scheduling)
User CSTS Forward-
File Application
User Application
(Packet Processing)
User RCF Application
(Frame Processing)
User Radiometric
Data Processing
User Service Monitor Data Processing
User F-CLTU Application
(CLTU Processing)
Service
Delivery (SD)
Interfaces
Service
Management (SM) Interface (I/F)
Flight
Dynamics
Planning
Schedule
Execution
Monitor &
Control
MAL & Transport Adapter for SPP
SM over HTTP
F-CLTU over TCP
R-CF over TCP
MD-CSTS over TCP
TD-CSTS over TCP
SM&C MO Applications
(MAL Compliant)
Notes: I changed the lines here from dashed to solid.
7/25: Changed to ESLT now that the term is defined before this graphic.
Note that Earth-Space Link Terminals, while shown here, isn’t mentioned in the document until section 3. In part, that’s why I’ve not adjusted the term to show as “ESLT”.

## Slide 63: Specific Recommendations to SM&C From CESG Meeting, Sept 2009
CSS
  Adopt SM WG, SM & request specifications
  Harmonize SM WG and SM&C interaction patterns
  Adopt CSTS WG, Cross Support transfer service interfaces
    Adopt CSTS WG, Radiometric data transfer (using Nav TDM), Monitor Data
    Collaborate with CSTS WG, Proposed service control and file data cross support
  Collaborate with CSA WG, Cross Support Service Architecture
  Collaborate with CSA WG, Service agreements and catalogs
SIS
  Adopt CFDP WG, file transfer standard for space file transfers
  Adopt AMS WG, message transfer standard for space message transfer
  Adopt DTN WG, space internetworking standards
  Collaborate with Time Correlation BoF on protocol standards
SOIS
  Collaborate with App WG, message transfer standards (coordinated with AMS already, use AMS for space / ground xfers)
  Collaborate with Subnet WG on Time and File services
SEA
  Adopt Sec WG, Security Algorithms
  Adopt IA WG, Reference Architecture for Space Information Management
  Collaborate with SANA WG, Standard registries for CCSDS information (& services)
  Collaborate with Registries / Repositories SIG (SEA IA WG & MOIMS IPR WG)
    Emerging interoperable specs for registries & repositories and SOA framework