## Slide 1: Introduction to Functional Resources
October 2016
Rome, Italy
Wolfgang Hell, ESA
with material from
John Pietras
Global Science and Technology, Inc., Greenbelt, MD, USA
Revised by Erik Barkley for CESG Presentation

## Slide 2: Purpose
Introduce the concept of Functional Resources
Report on what has been developed so far and which support is available
Illustrate how this concept ties into SANA Registries and their management
Explain the applicability of the concept beyond CSS
Solicit inputs and propose plan for collecting inputs
The concept of Functional Resources is documented in “Functional Resource Reference Model” (Draft Technical Note CSSA 1-TN-0.11 – July 2016 – needs further work (see the Book Captain’s notes at the beginning of the document))
  http://cwe.ccsds.org/css/docs/CSS%20Area/CWE%20Private/Functional%20Resources%20and%20Service%20Components/FunctResRefModel_TechNote-TN-0.11-160707.zip

## Slide 3: Why Did CSS Area develop FRM?
CSS Area develops standards that need to work in terms of configuration and monitoring/reporting of TT+C agency resources for cross-support inter-operability
Does not work if parameters are expressed at level of implementing hardware/equipment
Functional Resource defines the functions of a TT+C network at an abstract level informed by real-world operations of TT+C networks such that CSS Area standards can be expressed

## Slide 4: Facets of a Functional Resource
A Functional Resource is an abstraction of a cross-support function (processing step) performed on space communication, tracking or management (monitoring and control) data
A Functional Resource represents a cohesive, atomic set of space communication functionality with which can be associated single instances of management parameters, monitored parameters, real-time control parameters, and event notifications
Functional
Resource
Type
space data to
be processed
processed space data
managed
parameters
controlled
parameters
(directives)
monitored
parameters
notifiable
events

## Slide 5: Facets of a Functional Resource
Originally the FR concept had been conceived as a framework for naming monitored parameters and notifiable events in the context of the MD-CSTS
  Subsequently the FR concept has been extended to include managed parameters (Service Management) and directives (real-time control)

## Slide 6: Some Key Features
  A Functional Resource may have
    Parameters (where each parameter can be monitored and some can be controlled)
    Notifiable Events (where such notification may carry additional information by means of an event value)
    Directives (where a directive qualifier may carry additional information needed for the execution of the directive)
  The “uses” relationship expresses the permissible interfacing with other FR types
  The Functional Resource type and the associated PEDs are identified by means of Object Identifiers, the instance of the FR type by an instance number
  Evolving needs can be accommodated by new versions of PEDs. More fundamental changes require the specification of a new FR type
  Operational robustness of real-time control is achieved by guard conditions at the level of the directive and/or the parameters affected by the directive execution

## Slide 7: Functional Resource Type Metamodel

## Slide 8: An Eye-Chart – The (current) realized model

## Slide 9: (Current) Model – Part 1 more legible

## Slide 10: (Current) Model – Part 2 more legible

## Slide 11: Getting a Handle on the Model  OIDs

## Slide 12: Big picture placement of OIDs re RMP/SANA
iso (1)
standard producing
organization (112)
identified
organization (3)
ccsds (4)
css (4)
crossSupport
Resources (2)
space link
extension (3)
csts (1)
framework (1)
services (2)
externallyDefinedType
AndValueExtensions (3)
modules (1)
operations (2)
procedures (3)
fwProcedures
Functionalities (4)
serviceGeneric
Identifiers (5)
crossSupport
Functionalities (1)
Agencies Functionalities (2)

## Slide 13: Status
  The presently defined set of Functional Resource types has been developed based on IOAG Service Catalog #1 services (single-hop space-ground services, also called ABA configuration). For some 50% of these types we have a detailed, but not yet reviewed specification
  Functional Resources for Space Internetworking have been added only to show where such Functional Resources fit in and that the concept is valid also for IOAG Service Catalog #2 services
  An initial set of monitored parameters has been created based on feedback from several agencies and based on existing implementations
  The set of configurable parameters is mostly based on the set of “managed parameters” identified in the Recommendation(s) related to the function modeled by the FR. In some cases Parameters have been added to cover operational needs and to permit cross support of missions not (fully) respecting the CCSDS Recommendations

## Slide 14: Status
  Notifiable Events are based on notifications specified for transfer service providers. The specification of additional events is most likely operationally desirable
  Directives specified so far for the most part permit the setting of parameters that can be controlled in real-time. Additional directives may be operationally desirable. The guard conditions specified so far are most likely incomplete
  The FR TN, the FR diagram and the corresponding XML file are incomplete in the sense that there are not (yet) covered Recommendations (CCSDS 415.1-B-1 (CDMA link incl. associated ranging), CCSDS 131.2-B-1 (high rate TM link and coding), CCSDS 131.3-B-1 (DVB-S2 coding), and CCSDS 355.0-B-1 (Space Data Link Security Protocol), and things in the pipeline such as ranging over suppressed carrier, sliced LDPC, USLP). Also Space Internetworking related Recommendations except IP over Encap are not covered yet.
  An all-in-one-go delivery of the FR definitions appears not to be feasible – we should discuss needs and priorities and a resulting delivery plan

## Slide 15: SANA FR Registry
  To have flexibility and extensibility, the MD-CSTS and the future SC-CSTS do not specify the notifiable events and parameters that can be monitored or controlled. Rather this information is provided by means of the SANA registry “Functional Resources” located at http://sanaregistry.org/r/functional_resources/.
  The actually supported subset shall be documented e.g. in the Service Agreement governing the given cross support arrangement
  Should the need arise to register agency-specific FR types, this is supported by means of agency-specific sub-branches in the FR OID tree
  The XML output of the FR Editor serves as input to SANA for populating the “Functional Resources” registry. The details of this CSS-SANA interface are documented in “Functional Resource Registry at SANA”, CSSA 2-TN-1.0, March 2016
  The Management Policy applicable to this registry is documented in the “Cross Support Transfer Service – Specification Framework”, CCSDS 921.1-B-1 (should be “blue” soon)

## Slide 16: SANA FR Registry

## Slide 17: Relevance beyond CSS
  Cross Support Services provision requires the configuration and monitoring of service production within an ESLT which in turn is governed by the associated Recommendations regarding RF and modulation, sync and coding, and space link protocols
  The CESG aims at preventing the proliferation of registries. The “Functional Resources” registry is readily available as a home for capturing space link related configuration, control and monitoring information
  The definition of FRs is adequately supported by the existing tool which not only is convenient for the editor, but also to some extent enforces consistency (e.g. in the OID assignment)
  Participation of the space link experts in the definition of the associated FRs ensures that domain specific knowledge is captured and the cross support services are “automatically” enhanced
  Participation of CSS ensures that the FRs are defined such that e.g. in terms of data types compatibility with existing and future cross support services is achieved

## Slide 18: Request & Proposal
CSS
This represents our (CSS Area) best understanding of the different types resources and “wiring” combinations
Is it correct?
Are there things missing?
Is this generally properly structured?
  E.g., does this allow for inclusion of optical communications in an expeditious manner?
CESG Mtg
Overview of FR
01-Feb-2017
CSS Area hosts telecon/webex for WG Chairs
Walk chairs through FRM
Spring 2017 Mtgs
Detailed feed back from WG Chairs
CSS Area hosts multi-WG area for face-to-face discussions at Spring ’17 meetings
ADs Request WG Chair participation
Perhaps responses requested just for limited sub-sets that make most sense for WG

## Slide 19: Some Good Feed Back
Betreff: response to SDLS Parameter Dependencies
Datum: 2016-10-21T16:30:23+0200
Von: "Moury Gilles" <Gilles.Moury@cnes.fr>
An: "Wolfgang Hell" <wo_._he@t-online.de>
Dear Wolfgang,
Sorry for being so late in providing you with the SDLS WG response to your questions on SDLS Parameter Dependencies (as stated in slide 5 & 6 of the attached presentation):
Refer to slides 5 and 6 of W.Hell presentation (attached) on SDLS parameter dependencies for Functional Resources (FR):
Authorized algorithm, key size and MAC size for cryptographic algorithms are defined in the BB for cryptographic algorithms (352.0-B-1 – attached)
Each algorithm should be associated with a set of key lengths and MAC lengths.
The list of authorized algorithms together with the allowed associated key length and MAC lengths are specified in :
Authentication algorithm : §4 of 352.0-B
Encryption algorithm : §3.1/3.2/3.3 of 352.0-B
Authenticated-encryption : §3.4 (only algorithm: GCM with key and MAC size 128 bits)
Another SA service type should be added : Authenticated-encryption (§3.4 of 352.0-B)
DSS is a family of algorithm, the possible algorithms are : RSA, DSA and ECDSA
Input re security for functional resources (Thanks to Giles)

## Slide 20: Comments, questions?

## Slide 21
Backup Material – More on CSS FRM Tooling

## Slide 22: Starting with TC Sync & Channel Encoding…

## Slide 23: …Screenshot 1…
  Example (as displayed by the FR Editor tool) FR type (1)
The type of input may be selected by a managed,
but not necessarily monitored parameter
Assembled from a list of standard acronyms
Optional free text e.g. for doc generation
Not part of the tool output – FRs have no version
Free text

## Slide 24: Status and Tools
  Example (as displayed by the FR Editor tool) FR type (2)
Lists all Events of the FR type
Lists all Directives of the FR type
“Uses” relationship: lists all FR types
generating data that this FR type may
consume
Lists all Parameters
of this FR type

## Slide 25: …Screenshot 1…
  Example (as displayed by the FR Editor tool) Event
Identifies the Event Value, if applicable

## Slide 26: …Screenshot 2…
  Example (as displayed by the FR Editor tool) Event Value
Data types specified such that they match the
CSTS Specification Framework

## Slide 27: …Screenshot 3…
  Example (as displayed by the FR Editor tool) Directive
Identifies the Directive Qualifier if applicable
Free text, but may be formal
Boolean expressions

## Slide 28: …Screenshot 4…
  Example (as displayed by the FR Editor tool) Directive Qualifier (1)

## Slide 29: …Screenshot 5…
  Example (as displayed by the FR Editor tool) Directive Qualifier (2)
Example of a complex parameter

## Slide 30: …Screenshot 6…
  Example (as displayed by the FR Editor tool) Parameter (1)

## Slide 31: …Screenshot 7…
  Example (as displayed by the FR Editor tool) Parameter (2)
Example of a Guard Condition

## Slide 32: Tool Ouput  SANA For Ingest
  The FR Editor tool is based on Eclipse and has been developed by CSTS (Holger Dreihahn, ESA)
  The tool’s output is the FR specification in XML format:
  </functionalResource>
  <functionalResource SemanticDefinition="The TcSyncAndChannelEncoding FR accepts as input one of the following:&#xD;&#xA;- CLTUs;&#xD;&#xA;- TC frames to be radated via a specific physical channel.&#xD;&#xA;It also accepts the CLCWs extracted from the return link associated with the forward link used by this FR.&#xD;&#xA;This FR provides the symbol stream to be used for modulating the forward carrier of the physical channel associated with this FR. &#xD;&#xA;" classifier="FwdTcSyncAndChnlEncoding" stringIdentifier="Forward TC Sync and Channel Encoding" version="1" creationDate="2016-02-29T00:00:00.000+0100" authorizingEntity="CSS Area" oidBit="4" uses="//@functionalResource.13 //@functionalResource.5 //@functionalResource.23 //@functionalResource.24">
  <oid>
  <oidBit>1</oidBit>
  <oidBit>3</oidBit>
  <oidBit>112</oidBit>
  <oidBit>4</oidBit>
  <oidBit>4</oidBit>
  <oidBit>2</oidBit>
  <oidBit>1</oidBit>
  <oidBit>4</oidBit>
  </oid>

## Slide 33: Output rendered via stylesheet
  With the associated style sheet, the specification can be read (and reviewed) using a conventional WEB Browser

## Slide 34: Final Tool Notes
  Further capabilities of the tool are
    the graphical presentation of the tree structure of the assigned OIDs
    a limited capability to check ASN.1 based data type specifications
  A capability that should be added is the specification of information and relationships to support Functional Resource Sets
    allows “plug and play” substitution as the catalog of new FR types grows and evolves, e.g., to allow substitution of Universal Space Link Protocol (USLP) functional resource types to be used instead of TC/TM/AOS SDLP FR types for a given Mission
    will be used to construct CCSDS-standard Space Communication Cross Support Service Management (SCCS-SM) Service Agreements and Configuration Profiles