Draft Recommendation for
Space Data System Standards

Spacecraft Onboard Interface Services—RFID Tag Encoding Specification

Draft Recommended Standard

CCSDS 881.1-R-1

Red Book

June 2015

AUTHORITY

|  | Issue: | Red Book, Issue 1 |  |
| --- | --- | --- | --- |
|  | Date: | June 2015 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the e-mail address below.

This document is published and maintained by:

CCSDS Secretariat

National Aeronautics and Space Administration

Washington, DC, USA

E-mail: secretariat@mailman.ccsds.org

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be sent to the CCSDS Secretariat at the e-mail address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- Electronics and Telecommunications Research Institute (ETRI)/Korea.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 881.1-R-1 | Spacecraft Onboard Interface Services—RFID Tag Encoding Specification, Draft Recommended Standard, Issue 1 | June 2015 | Current draft |

CONTENTS

Section	Page

1	Introduction	1-1

1.1	Purpose	1-1

1.2	Scope	1-1

1.3	Applicability	1-1

1.4	Rationale	1-1

1.5	Document Structure	1-2

1.6	Conventions	1-2

1.7	Acronyms	1-3

1.8	References	1-3

2	Overview	2-1

2.1	General	2-1

2.2	Tag Field Descriptions	2-1

2.3	Evolution of the Book	2-3

3	RFID Tag Encoding Recommended Standard	3-1

3.1	Overview	3-1

3.2	RFID Tag Encoding	3-2

ANNEX A	Implementation Conformance Statement 
ProForma  (Normative)	A-1

ANNEX B	Security, SANA, and Patent Cosiderations   (Informative)	B-1

ANNEX C	Encoding Example  (Informative)	C-1

ANNEX D	INFORMATIVE REFERENCES	D-1

ANNEX E	Abbreviations  (Informative)	E-1

ANNEX F	ECMA-113 Latin/Cyrillic Encoding Table  
(INFORMATIVE)	F-1

Figure

1-1	Bit Numbering Convention	1-2

2-1	IMS RFID Tag Encoding Schema	2-1

3-1	96-Bit Tag ID Logical Layout	3-1

3-2	Bitwise Mapping of the Fields	3-1

C-1	Legacy IMS RFID Tag Encoding Schema	C-1

C-2	RFID Tag Bank 012 Memory Layout	C-2

CONTENTS (continued)

Table	Page

3-1	96-Bit RFID-Tag Field Specification (Normative)	3-2

A-1	RFID Tag-Encoding Properties	A-5

B-1	SANA Registry—RFID Tag-Encoding Database-ID	B-3

B-2	SANA Registry—RFID Tag-Encoding Object-ID	B-4

C-1	Example Tag ID Field Encoding	C-3

F-1	Code Table of Latin/Cyrillic Alphabet	F-1

# Introduction

## Purpose

This document provides a Recommended Standard for the utilization of Radio Frequency Identification (RFID) protocol and communication standards in support of inventory management activities associated with space missions.  Relevant technical background information can be found in Wireless Network Communications Overview for Space Mission Operations (reference [D1]) and in RFID-Based Inventory Management systems (reference [D2]).

The recommended standards contained in this report enable member agencies to select the best option(s) available for interoperable RFID-based tag encoding in the support of inventory management applications.  The specification of a Recommended Standard facilitates interoperable communications and forms the foundation for cross-support of information systems between separate member space agencies.

## Scope

This Recommended Standard is targeted towards providing an augmented namespace definition in support of RFID-based applications.

## Applicability

This Recommended Standard specifies protocols that enable interoperable wireless inventory management systems that utilize RFID technologies.

NOTE	–	Inclusion of any specific wireless technology does not constitute any endorsement, expressed or implied, by the authors of this Recommended Standard or the agencies that supported the composition of this Recommended Standard.

## Rationale

From an engineering standpoint, mission managers, along with engineers and developers, are faced with a plethora of wireless communication choices, both standards-based and proprietary.  A CCSDS RFID tag encoding Recommended Standard provides guidance in the selection of naming conventions necessary to achieve interoperable information exchange in support of RFID-based applications.

## Document Structure

This document provides a normative recommendation for an RFID naming schema that supports the expanded operations of International Space Station (ISS) inventory management systems.  More information on space mission use cases addressed by RFID technology can be found in annex E of reference [D2].

Section 2 provides an overview of the basis for the tag encoding.

Section 3 provides a normative description for the recommended standard tag encoding schema.

Annex A provides the Implementation Conformance Statement (ICS) proforma.

Annex B discusses security, Space Assigned Numbers Authority (SANA), and patent considerations pertaining to RFID-based inventory management systems.

Annex C provides an informative tag-encoding example.

Annex D is a list of informative references.

Annex E is a glossary of abbreviations used in this document.

Annex F provides the ECMA-113 Latin/Cyrillic encoding definition table.

## Conventions

### Bit Numbering

In this document, the following convention is used to identify each bit in an N-bit field. The first bit in the field is defined to be ‘bit N-1; the following bit is defined to be ‘bit N-2’, and so on up to ‘bit 0’, as shown in figure 1-1.

Figure 1-1:  Bit Numbering Convention

In accordance with modern data communications practice, spacecraft data fields are often grouped into 8-bit ‘bytes’, which conform to the above convention.

### Nomenclature

#### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

#### Informative Text

In the normative section of this document (section 3), informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## Acronyms

A glossary of terms including common acronyms is provided in annex E.

## References

[1]	Space Assigned Numbers Authority (SANA). http://sanaregistry.org/.

[2]	8-Bit Single-Byte Coded Graphic Character Sets: Latin/Cyrillic Alphabet. 3rd ed. ECMA-113. Geneva: Ecma International, December 1999.

# Overview

## General

This Recommended Standard specifies tag-encoding options that augment, yet remain compatible with, a legacy ISS Inventory Management System (IMS) tag encoding schema established for early flight experiments.  This standard will enable more efficient, flexible, and expanded utilization of RFID technology for applications such as Autonomous Logistics Management (ALM) on ISS.  The tag encoding schema will allow various multinational operational and experimental applications, including inventory and asset management, sensors, and navigation assistance onboard ISS as a precursor to a more advanced standard for exploration.

## Tag Field Descriptions

The fields in the proposed standard are designed to represent a hierarchy of information, in which the values encoded in each successive field in the hierarchy may be re-used within different levels of the hierarchy. The order of hierarchical field namespace structure, from most significant to least significant is

{Database-ID, Owner-ID, Program-ID, Object-ID, Serial-ID}.

Figure 2-1 illustrates how the current IMS tag encoding schema maps onto the hierarchical field structure.

| Owner / Program name | Database-ID | Owner-ID | Program-ID | Unique-ID (Serial Number ID) | Owner-ID | Object-ID |
| --- | --- | --- | --- | --- | --- | --- |
|  | byte 0 | byte 1 | byte 2 | byte 3 | byte 4 | byte 5 | byte 6 | byte 7 | byte 8 | byte 9 | byte 10 | byte 11 |
| IMS | I | X | C | P |  |  |  |  |  | J |  |  |
| IMS Russian | I | X | 0 | 0 |  |  |  |  |  | R |  |  |
| coffee | I | X | F | 2 |  |  |  |  |  |  |  |  |
| coffee | I | X | F | 3 |  |  |  |  |  |  |  |  |
| food BOB | I | X | F | E |  |  |  |  |  |  |  |  |
| SF Tucker/Kimmel | I | H | R | F |  |  |  |  |  | J |  |  |
| CHeCS BPECG hardware | I | X | C | B |  |  |  |  |  | J |  |  |
| SF Water Kits | I | X | W | M | S |  |  |  |  | J |  |  |
| SD4 Bara medical | M | H | M | S |  |  |  |  |  |  |  |  |
| MCT Sam Hussey/GRC | M | M | C | T |  |  |  |  |  |  |  |  |
| EV4 testing | I | E | V | J |  |  |  |  |  |  |  |  |
| R2 testing | I | R | 2 | T | E | S | T |  |  |  |  |  |
|  |  | <--- | B | A | R | C | O | D | E | ---> |  |  |

Figure 2-1:  IMS RFID Tag Encoding Schema

The field designated as Database-ID, which comprises Byte 0, represents the organization responsible for defining and administering the namespace to which the tag belongs. This field is the most significant field in the hierarchical structure of the RFID naming convention, and as such, it is mandatory to use only values designated (see table B-1). Strictly speaking, a namespace owner need not maintain the remainder of the recommended hierarchical structure of the standard, and as such, SANA registries are not required for the remaining fields in the standard. In the current ISS utilization, the Database-ID is identified with the particular database in which the tagged item is recorded and tracked. Currently only the values ‘I’ (Inventory Management System) and ‘M’ (Medical) are utilized.

The field designated as Owner-ID, which comprises Bytes 1 and 9, represents the organization that owns the physical asset to which the tag is attached. This field is the second most significant field in the hierarchical structure specified in this standard. This implies that tags with different Database-ID designations may reuse and redefine Owner-ID values utilized within other Database-ID designations.

NOTE	–	In the current ISS utilization, Byte 9 may actually represent either a part of the Serial-ID or a part of the Owner-ID. That is, if Byte 9 is a number [0-9], then it represents Byte 6 of an extended (6-byte) Serial-ID. On the other hand, if Byte 9 is not a number then it represents Byte 2 of the 2-byte Owner-ID.

The field designated as Program-ID, which comprises Bytes 2 and 3, represents sub-organizations (such as programs) of the owner organization. This field is the third most significant field in the hierarchical RFID naming conventions specified in this standard. This implies that tags with different {Database-ID, Owner-ID} designations may reuse and redefine Program-ID values utilized within other {Database-ID, Owner-ID} designations.

The field designated as Object-ID, which comprises Bytes 10 and 11, represents classes of objects (e.g., medical equipment, food, tool, etc.) to which RFID tags will be affixed. This field is the fourth most significant field in the hierarchical RFID naming conventions specified in this standard. This implies that tags with different {Database-ID, Owner-ID, Program-ID} designations may reuse and redefine Object-ID values utilized within other {Database-ID, Owner-ID, Program-ID} designations. Values in the range

[0  :  32767]

can be assigned at the database manager’s discretion; values in the range

[32768  :  65535]

will be maintained (see table B-2) to promote tracking of common items across unique databases.

The field designated as Serial-ID, which comprises Bytes 4 through 8, represents unique objects to which RFID tags will be affixed.  This field is the least significant field in the hierarchical RFID naming conventions specified in this standard. This implies that tags with different {Database-ID, Owner-ID, Program-ID, Object-ID} designations may reuse and redefine Serial-ID values utilized within other {Database-ID, Owner-ID, Program-ID, Object-ID} designations.

## Evolution of the Book

This Recommended Standard addresses RFID tag encoding for inventory management applications.  As space-related applications arise that cannot be fulfilled based on the recommendations of this Recommended Standard, evolution of this book will be considered.  Methods to extend or adapt previous recommendations will be considered with preference over adoption of new standards, providing the resulting performance and cost are advantageous relative to those associated with adoption of one or more new standards.

# RFID Tag Encoding Recommended Standard

## Overview

This section presents the recommended standard naming specification for RFID tag encoding (96-bit) RFID tags to provide the basis for information interoperability.

The Recommended Standard pertains to RFID systems that provide stored data only, as opposed to sensor telemetry.  Applications are considered where no direct active tag power is required, which necessitates short-range communication and Interrogator-Talk-First (ITF) protocols.  (See references [D1] and [D2] for supporting technical background.)

Figure 3-1 depicts the logical layout of the 96-bit RFID tag name (ID), and figure 3-2 shows the bit-wise mappings of the fields; while table 3-1 defines the 5 proposed logical data fields encoded on each tag and the allowable range of values for each field.

Figure 3-1:  96-Bit Tag ID Logical Layout

Figure 3-2:  Bitwise Mapping of the Fields

## RFID Tag Encoding

For interoperable onboard spacecraft or internal-vehicle inventory management utilizing 96-bit wireless RFID tags, the tag encoding shall follow the format specified in table 3-1.

Table 3-1:  96-Bit RFID-Tag Field Specification (Normative)

| Tag ID Field Address | Field Type | Field | Description | Namespace Administrator |
| --- | --- | --- | --- | --- |
| 00h – 07h | 8-bit ECMA-113 character | Database-ID | ID of the database | SANA Registry (See table B-1) |
| 08h – 0Fh | 8-bit ECMA-113 character | Owner-ID Byte 0 | Byte 1 of 2-byte Owner-ID | Database-ID Owner |
| 10h – 17h | 8-bit ECMA-113 character | Program-ID Byte 0 | Byte 1 of 2-byte Program-ID | Database-ID Owner |
| 18h – 1Fh | 8-bit ECMA-113 character | Program-ID Byte 1 | Byte 2 of 2-byte Program-ID | Database-ID Owner |
| 20h – 27h | 8-bit ECMA-113 character | Serial-ID Byte 0 | Byte 1 of 5-byte or 6-byte Serial-ID | Database-ID Owner |
| 28h – 2Fh | 8-bit ECMA-113 character | Serial-ID Byte 1 | Byte 2 of 5-byte or 6-byte Serial-ID | Database-ID Owner |
| 30h – 37h | 8-bit ECMA-113 character | Serial-ID Byte 2 | Byte 3 of 5-byte or 6-byte Serial-ID | Database-ID Owner |
| 38h – 3Fh | 8-bit ECMA-113 character | Serial-ID Byte 3 | Byte 4 of 5-byte or 6-byte Serial-ID | Database-ID Owner |
| 40h – 47h | 8-bit ECMA-113 character | Serial-ID Byte 4 | Byte 5 of 5-byte or 6-byte Serial-ID | Database-ID Owner |
| 48h – 4Fh | 8-bit ECMA-113 character | Owner-ID Byte 1 | Byte 2 of 2-byte Owner-ID | Database-ID Owner |
| 50h – 5Fh | 16-bit integer | Object-ID | [0 – 65535] | Database-ID Owner [0 : 32767] SANA Registry (See table B-2) [32768 : 65535] |

Implementation Conformance Statement ProForma

(Normative)

Introduction

Overview

This annex provides the Protocol Implementation Conformance Statement (PICS) Requirements List (RL) for an implementation of RFID Tag-Encoding specified in Spacecraft Onboard Interface Services—RFID Tag Encoding Specification, CCSDS 881.1-R-1, June 2015.  Completing the RL in accordance with the instructions below generates the PICS for an implementation.  An implementation shall satisfy the mandatory conformance requirements referenced in the RL.

The RL in this annex is blank. An implementation’s completed RL is called the PICS. The PICS states which capabilities and options have been implemented. The following can use the PICS:

- the implementer, as a checklist to reduce the risk of failure to conform to the standard through oversight;

- a supplier or potential acquirer of the implementation, as a detailed indication of the capabilities of the implementation, stated relative to the common basis for understanding provided by the standard PICS proforma;

- a user or potential user of the implementation, as a basis for initially checking the possibility of interworking with another implementation (it should be noted that, while interworking can never be guaranteed, failure to interwork can often be predicted from incompatible PICSes);

- a tester, as the basis for selecting appropriate tests against which to assess the claim for conformance of the implementation.

Abbreviations and Conventions

The RL consists of information in tabular form. The status of features is indicated using the abbreviations and conventions described below.

Item Column

The item column contains sequential numbers for items in the table.

Description Column

The description column contains a brief description of the item. It implicitly means ‘is <item description> supported by the implementation?’

Reference Column

The reference column indicates the relevant subsection of Spacecraft Onboard Interface Services—RFID Tag Encoding Specification, CCSDS 881.1-R-1, (this document).

Status Column

The status column uses the following notations:

M	mandatory.

O	optional.

N/A	not applicable.

O.i	qualified optional—for a group of related optional items labeled by the same numeral i, the logic of their selection is defined immediately following the table.

C.j	conditional—the requirement on the capability (‘M’, ‘O’, or ‘N/A’) depends on the support of another optional item.  The numeral j identifies a unique conditional status expression defined immediately following the table.

Values Allowed Column

The values allowed column contains the list or range of values allowed. The following notations are used:

Range of values:	<min value> … <max value>

example		2 ... 16

list of values:		<value1>, <value2>, … , <valueN>

example		3, 6, 9, … , 21

N/A			not applicable

Item Support or Values Supported Column

In the item support or values supported column, the support of every item as claimed by the implementer shall be stated by entering the appropriate answer (‘Y’, ‘N’, or ‘N/A’) or the values supported:

Yes	yes, item supported by the implementation.

No	no, item not supported by the implementation.

range or list of values supported.

N/A	not applicable.

Instructions for Completing the RL

An implementer shows the extent of compliance to the Recommended Standard by completing the RL; that is, the state of compliance with all mandatory requirements and the options supported are shown. The resulting completed RL is called a PICS. The implementer shall complete the RL by entering appropriate responses in the support or values supported column, using the notation described in A1.2.  If a conditional requirement is inapplicable, N/A shall be used.   If a mandatory requirement is not satisfied, exception information must be supplied by entering a reference Xi, where I is a unique identifier, to an accompanying rationale for the noncompliance.

PICS Proforma for RFID Tag-Encoding

General Information

Identification of PICS

| Date of Statement (DD/MM/YYYY) |  |
| --- | --- |
| PICS Serial Number |  |
| System Conformance statement cross-reference |  |

Identification of Implementation Under Test (IUT)

| Implementation name |  |
| --- | --- |
| Implementation version |  |
| Special configuration |  |
| Other information |  |

Identification of Supplier

| Supplier |  |
| --- | --- |
| Contact point for queries |  |
| Implementation name(s) and versions |  |
| Other information necessary for full identification, e.g., name(s) and vendor(s) for machines and/or operating systems; System name(s) |  |

Identification of Specification

| CCSDS 881.1-R-1 |  |
| --- | --- |
| Addenda implemented |  |
| Amendments implemented |  |
| Have any exceptions been required? (Note: A YES answer means that the implementation does not conform to the Recommended Standard. Non-supported mandatory capabilities are to be identified in the PICS, with an explanation of why the implementation is non-conforming. | Yes _____ No _____ |

RFID Tag-Encoding

To be classified as CCSDS RFID Tag-Encoding compliant the following tag encoding rules MUST be followed:

- All fields (Database-ID, Owner-ID, Program-ID, Object-ID and Serial-ID) MUST be valid and present in the order specified.

- All character fields (Database-ID, Owner-ID, Program-ID and Serial-ID) MUST be encoded per the ECMA-113 / ISO 8859 Part 5 Standard for encoding Latin and Cyrillic characters.  See annex F for the ECMA-113 / ISO 8859 Part 5 allowable Latin and Cyrillic character sets.

- The Database-ID must be defined in the SANA RFID-TAG Database-ID Registry.

- The Object-ID must be an integer between [0 – 65535].

- If the Object-ID is to be tracked across multiple Database-IDs and Owner-IDs, then the Object-ID must be in the range of “Common Object IDs” which is [32768 – 65535].  If the Object-ID exists in the SANA RFID-Tag Object-ID Registry then the existing registered Object-ID MUST be utilized.  If a “Common Object ID” for a class of objects does not exist, then a request to add a NEW common Object-ID per the specified Registration Rule must be completed.

- If the Object-ID does not require common-object cross-referencing then the Object-ID must be in the range [0 – 32767] to indicate a unique agency test activity.

Table A-1: RFID Tag-Encoding Properties

| Item | Field Description | Reference | Status | Values Allowed | Item Support or Values Supported |
| --- | --- | --- | --- | --- | --- |
| 1 | Database-ID | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 2 | Owner-ID Byte 0 | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 3 | Program-ID Byte 0 | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 4 | Program-ID Byte 1 | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 5 | Serial-ID Byte 0 | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 6 | Serial-ID Byte 1 | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 7 | Serial-ID Byte 2 | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 8 | Serial-ID Byte 3 | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 9 | Serial-ID Byte 4 | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 10 | Owner-ID Byte 1 | 3.2 | M | (20h .. 7Eh) && (A0h .. FFh) |  |
| 11 | Object-ID | 3.2 | M | 0 .. 65535 |  |

Security, SANA, and Patent CoNsiderations 

(Informative)

Security Considerations

General

Security considerations discussed in annex A of reference [D2] apply to this specification.

Security Background

It is assumed that security concerns is provided by encryption, authentication methods, and access control to be performed at the application and/or transport layers. Mission and service providers are expected to select from recommended security methods suitable to the specific application profile. Specification of these security methods and other security provisions is outside the scope of this Recommended Standard.

Security Concerns

Security concerns in the areas of data privacy, integrity, authentication, access control, availability of resources, and auditing are to be addressed in the appropriate layers and are not related to this Recommended Standard. The use of the specified RFID Tag-Encoding schema described in this document does not affect the proper functioning of methods used to achieve such protection.

Potential Threats and Attack Scenarios

Security considerations discussed in annex A of reference [D2] apply to this specification.

Consequences of not Applying Security

Security considerations discussed in annex A of reference [D2] apply to this specification.

sana considerations

SANA is requested to create and maintain two formal registries:

- A registry to allocate unique Database-IDs.

- A registry to allocate unique Object-IDs that can be utilized by multiple Databases, Owners, and Programs for common item tracking.

When creating or processing ‘ADD’ or ‘MODIFY’ registry operations SANA is requested to enforce the field typing, field length, and field restrictions as specified in table 3-1.

SANA RFID Provider Registration

The RFID Provider Organization shall be one of the organizations registered in the CCSDS Organizations registry: (http://sanaregistry.org/r/organizations/organizations.html).

If an Organization does not exist in the Organizations registry the identified Agency Head of Delegation or Organization official Point of Contact may request of the SANA that it be added, using the existing SANA procedures for that registry.

The CCSDS Organizations registry shall be modified to add a Boolean attribute indicating that the Organization may be of type ‘RFIDProvider’.

For all Organizations that indicate that they offer RFID services this attribute shall be set ‘TRUE’, otherwise it shall be set ‘FALSE’.

Addition of any new organization shall require sponsorship by the CCSDS Member Agency for its country of origin or by the Secretariat if there is no CCSDS Member agency for its country of origin.

The Agency Head of Delegation or Organization official Point of Contact shall be added to the CCSDS Contacts registry (http://sanaregistry.org/r/contacts/contacts.html).

The Agency Head of Delegation or Organization official Point of Contact may appoint an Agency Representative (AR) as the point of contact for RFIDProvider requests.

The RFIDProvider AR shall be added to the CCSDS Contacts registry (http://sanaregistry.org/r/contacts/contacts.html).

The CCSDS Contacts registry shall be modified to add a Boolean attribute indicating that the person may be of type ‘RFIDProviderContact’.

For all Contacts that are identified as a RFIDProviderContact this attribute shall be set ‘TRUE’, otherwise it shall be set ‘FALSE’.

The RFIDProvider ‘user’ shall be the Spacecraft Name of one of the spacecraft registered in the CCSDS SCID registry (http://sanaregistry.org/r/spacecraftid/spacecraftid.html, or the field ‘UNALLOCATED’ or the field ‘PROVIDER-RFID’.

If the user spacecraft does not exist in the Spacecraft registry the identified SCID Agency Representative shall request of the SANA that one be assigned, following the SCID request procedures.

If there is not a current SCID Agency Representative, or if the user agency is not yet registered, the SCID registration procedures must be followed to create these entries.

The RFIDProvider ‘Database-ID’ shall use the Database-ID of one of the RFID-Tag Database-ID identifiers registered in the CCSDS RFID Database-ID registry http://sanaregistry.org/cgi/registry-auth?id=rfid_database_ids.

The RFIDProvider ‘Object-ID’ shall use the Object-ID of one of the RFID-Tag Object-ID identifiers registered in the CCSDS RFID-Tag Object-ID registry http://sanaregistry.org/cgi/registry-auth?id=rfid_object_ids.

If the Database-ID does not exist in the RFID-Tag Database-ID registry the identified RFIDProvider Agency Representative shall request of the SANA that one be assigned, following the RFID-Tag Database-ID registry request procedures.

If the Object-ID does not exist in the RFID-Tag Object-ID registry the identified RFIDProvider Agency Representative shall request of the SANA that one be assigned, following the RFID-Tag Object-ID registry request procedures.

If there is not a current RFIDProvider Agency Representative, or if the user agency is not yet registered, the Agency (SCID) registration procedures must be followed to create these entries.

SANA Registry: RFID TAG-Encoding Database-ID

It is the recommendation of this document that SANA create the following 2-field (RFID-Tag Database-ID, Database-ID Description) registry:

Table B-1:  SANA Registry—RFID Tag-Encoding Database-ID

| Registry Name: | RFID-Tag Database-ID |
| --- | --- |
| Column 1 Name: | RFID-Tag Database-ID |
| Column 1 Data Type: | 8-bit ECMA-113(see reference [2]) character encoding; SANA field size 8-bit character |
| Column 1 Initial Value(s): | Row 1: ‘I’ Row 2: ‘M’ |
| Column 2 Data Type: | 80-character ASCII string description |
| Column 2 Initial Value(s): | Row 1: “Inventory Management System” Row 2: “Medical” |
| Registration Rule: | Requests to add assignments to the registry or registries identified in this recommendation shall be submitted to SANA and shall come from a CCSDS Member Agency. The request shall be related to a RFID Tag-Encoding activity. After evaluation of the request and approval by the SOIS Area Director (AD) or SOIS Deputy Area Directory (DAD) or a person duly authorized by the AD or DAD, the new entity will be allocated and added to the appropriate registry. The contents of the new entity to be added to the indicated registry must be complete and compliant with the definitions of the applicable entity type. |

SANA Registry: RFID TAG-Encoding Object-ID

It is the recommendation of this document that SANA create the following 2-field (RFID-Tag Object-ID, Object-ID Description) registry:

Table B-2:  SANA Registry—RFID Tag-Encoding Object-ID

| Registry Name: | RFID-Tag Object-ID |
| --- | --- |
| Column 1 Name: | RFID-Tag Object-ID |
| Column 1 Data Type: | SANA field size 16-bit integer [32768 : 65535]; [0 : 32767] are NOT SANA-administered and are available for the database owner to utilize in any self-defined schema |
| Column 1 Initial Values | Row 1: 64000 |
| Column 2 Data Type: | 80-character ASCII string description |
| Column 2 Initial Values | Row 1: “Reserved for CCSDS Wireless Working Group” |
| Registration Rule: | Requests to add assignments to the registry or registries identified in this recommendation shall be submitted to SANA and shall come from a CCSDS Member Agency. The request shall be related to a RFID Tag-Encoding activity. After evaluation of the request and approval by the SOIS Area Director (AD) or SOIS Deputy Area Directory (DAD) or a person duly authorized by the AD or DAD, the new entity will be allocated and added to the appropriate registry. The contents of the new entity to be added to the indicated registry must be complete and compliant with the definitions of the applicable entity type. |

NOTE	–	For candidate Object-ID organizational schemas see references [D3] and [D4].

| Value | Description | Status | Reference |
| --- | --- | --- | --- |
| 0 – 32767 | Permanently unassigned for individual agency testing | Unassigned |  |
| 32768 – 65535 | Will be specified and allocated per registry update rule | Reserved | CCSDS 88X-R-0 |

Patent Considerations

The recommendation of this document is simply a namespace definition schema and thus has no patent issues.

Encoding Example

(Informative)

Figure C-1 shows the current (as of November 2014) legacy IMS RFID tag encoding schema.  This standard expands the available namespace and defines the rules for the addition of new encoding options as per table 3-1.  The example will encode a 96-bit RFID tag for the Owner IMS; a serial number of ‘12345’ and an Object-ID = 45678 are assumed.

| Owner / Program name | Database-ID | Owner-ID | Program-ID | Unique-ID (Serial Number ID) | Owner-ID | Object-ID |
| --- | --- | --- | --- | --- | --- | --- |
|  | byte 0 | byte 1 | byte 2 | byte 3 | byte 4 | byte 5 | byte 6 | byte 7 | byte 8 | byte 9 | byte 10 | byte 11 |
| IMS | I | X | C | P |  |  |  |  |  | J |  |  |
| IMS Russian | I | X | 0 | 0 |  |  |  |  |  | R |  |  |
| coffee | I | X | F | 2 |  |  |  |  |  |  |  |  |
| coffee | I | X | F | 3 |  |  |  |  |  |  |  |  |
| food BOB | I | X | F | E |  |  |  |  |  |  |  |  |
| SF Tucker/Kimmel | I | H | R | F |  |  |  |  |  | J |  |  |
| CHeCS BPECG hardware | I | X | C | B |  |  |  |  |  | J |  |  |
| SF Water Kits | I | X | W | M | S |  |  |  |  | J |  |  |
| SD4 Bara medical | M | H | M | S |  |  |  |  |  |  |  |  |
| MCT Sam Hussey/GRC | M | M | C | T |  |  |  |  |  |  |  |  |
| EV4 testing | I | E | V | J |  |  |  |  |  |  |  |  |
| R2 testing | I | R | 2 | T | E | S | T |  |  |  |  |  |
|  |  | <--- | B | A | R | C | O | D | E | ---> |  |  |

Figure C-1:  Legacy IMS RFID Tag Encoding Schema

Tag Memory Background:  The ‘Tag ID’, which identifies an RFID tag, resides in Memory Bank 012 of a tag as shown in figure C-2.  By convention each memory bank starts at address 00h and extends to the end address of the memory bank.  Bit 00h is the Most Significant Bit (MSB) of the memory bank.  For binary fields (including the 96-bit tag ID) that are encoded into the memory bank, the MSB of the binary field occupies the lowest-numbered memory bit address.  As shown in figure 1-1, the Least Significant Bit (LSB) is numbered ‘bit 0’.  For a 96-bit tag ID consisting of b95b94b93…b0, b95 is the MSB and b0 is the LSB.  When the 96-bit tag ID is encoded onto Bank 012 starting at memory bit address 20h–7Fh the MSB b95 is stored at address 20h and the LSB b0 is stored at address 7Fh.

Figure C-2:  RFID Tag Bank 012 Memory Layout

Example Basis: A 96-bit RFID tag is encoded for the Owner IMS; a serial number of ‘12345’ and an Object-ID = 45678 are assumed (cf. figure C-1 for byte positions).

The tag Database-ID (Byte 0 of figure C-1) is comprised of the character ‘I’.

The tag Owner-ID (Byte 1 and Byte 9 of figure C-1) is comprised of the characters ‘X’ and ‘J’.

The tag Program-ID (Byte 2 and Byte 3 of figure C-1) is comprised of the characters ‘C’ and ‘P’.

The tag Serial-ID (Byte 4–Byte 8 of figure C-1) is given as ‘1’, ‘2’, ‘3’, ‘4’, ‘5’.

The tag Object-ID (Byte 10 and Byte 11 of figure C-1) is given as the integer 45678.

The resulting encoding represented in binary and hexadecimal is given in table C-1.

Table C-1:  Example Tag ID Field Encoding

| Tag ID Field Address | Field Type | Field | Value | Value (binary) | Value (hexadecimal) |
| --- | --- | --- | --- | --- | --- |
| 00h – 07h | 8-bit ECMA-113 character | Database-ID | ‘I’ | 01001001 | 49h |
| 08h – 0Fh | 8-bit ECMA-113 character | Owner-ID Byte 0 | ‘X’ | 01011000 | 58h |
| 10h – 17h | 8-bit ECMA-113 character | Program-ID Byte 0 | ‘C’ | 01000011 | 43h |
| 18h – 1Fh | 8-bit ECMA-113 character | Program-ID Byte 1 | ‘P’ | 01010000 | 50h |
| 20h – 27h | 8-bit ECMA-113 character | Serial-ID Byte 0 | ‘1’ | 00110001 | 31h |
| 28h – 2Fh | 8-bit ECMA-113 character | Serial-ID Byte 1 | ‘2’ | 00110010 | 32h |
| 30h – 37h | 8-bit ECMA-113 character | Serial-ID Byte 2 | ‘3’ | 00110011 | 33h |
| 38h – 3Fh | 8-bit ECMA-113 character | Serial-ID Byte 3 | ‘4’ | 00110100 | 44h |
| 40h – 47h | 8-bit ECMA-113 character | Serial-ID Byte 4 | ‘5’ | 00110101 | 35h |
| 48h – 4Fh | 8-bit ECMA-113 character | Owner-ID Byte 1 | ‘J’ | 01001010 | 4Ah |
| 50h – 5Fh | 16-bit integer | Object-ID | 45678 | Byte 0: 01101110 Byte 1: 10110010 | B26Eh |

INFORMATIVE REFERENCES

[D1]	Wireless Network Communications Overview for Space Mission Operations. Issue 2. Report Concerning Space Data System Standards (Green Book), CCSDS 880.0-G-2. Washington, D.C.: CCSDS, April 2015.

[D2]	Spacecraft Onboard Interface Services—RFID-Based Inventory Management Systems. Issue 1. Recommendation for Space Data System Practices (Magenta Book), CCSDS 881.0-M-1. Washington, D.C.: CCSDS, May 2012.

[D3]	Kevin Gifford, et al. “Unified Communications for Space Inventory Management.” In Proceedings of AIAA Space 2009 Conference and Exposition (14–17 September 2009, Pasadena, California). AIAA 2009-6550. Reston, Virginia: AIAA, 2009.

[D4]	“MIT Space Logistics: Interplanetary Supply Chain Management and Logistics Architecture.” MIT - Massachusetts Institute of Technology. http://strategic.mit.edu/spacelogistics/. (5/4/2015)

Abbreviations

(Informative)

ALM	automated logistics management

CCSDS	Consultative Committee for Space Data Systems

CRC	cyclic redundancy code

EPC	electronic product code

IMS	inventory management system

ISS	International Space Station

LSB	Least Significant Bit

MSB	most significant bit

RFID	radio frequency identification

SANA	Space Assigned Numbers Authority

TID	tag ID (manufacturer)

ECMA-113 Latin/Cyrillic Encoding Table

(INFORMATIVE)

Table F-1:  Code Table of Latin/Cyrillic Alphabet

|  | b8 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | b7 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 |  |
|  | b6 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 |  |
|  | b5 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 |  |
|  | 00 | 01 | 02 | 03 | 04 | 05 | 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 |  |
| b4 | b3 | b2 | b1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 0 | 0 | 0 | 0 | 00 |  |  | SP | 0 | @ | P | ` | p |  |  | NBSP | А | Р | а | р | № | 0 |
| 0 | 0 | 0 | 1 | 01 |  |  | ! | 1 | A | Q | a | q |  |  | Ё | Б | С | б | с | ё | 1 |
| 0 | 0 | 1 | 0 | 02 |  |  | " | 2 | B | R | b | r |  |  | Ђ | В | Т | в | т | ђ | 2 |
| 0 | 0 | 1 | 1 | 03 |  |  | # | 3 | C | S | c | s |  |  | Ѓ | Г | У | г | у | ѓ | 3 |
| 0 | 1 | 0 | 0 | 04 |  |  | $ | 4 | D | T | d | t |  |  | Є | Д | Ф | д | ф | є | 4 |
| 0 | 1 | 0 | 1 | 05 |  |  | % | 5 | E | U | e | u |  |  | Ѕ | Е | Х | е | х | ѕ | 5 |
| 0 | 1 | 1 | 0 | 06 |  |  | & | 6 | F | V | f | v |  |  | І | Ж | Ц | ж | ц | і | 6 |
| 0 | 1 | 1 | 1 | 07 |  |  | ' | 7 | G | W | g | w |  |  | Ї | З | Ч | з | ч | ї | 7 |
| 1 | 0 | 0 | 0 | 08 |  |  | ( | 8 | H | X | h | x |  |  | Ј | И | Ш | и | ш | ј | 8 |
| 1 | 0 | 0 | 1 | 09 |  |  | ) | 9 | I | Y | i | y |  |  | Љ | Й | Щ | й | щ | љ | 9 |
| 1 | 0 | 1 | 0 | 10 |  |  | * | : | J | Z | j | z |  |  | Њ | К | Ъ | к | ъ | њ | A |
| 1 | 0 | 1 | 1 | 11 |  |  | + | ; | K | [ | k | { |  |  | Ћ | Л | Ы | л | ы | ћ | B |
| 1 | 1 | 0 | 0 | 12 |  |  | , | < | L | \ | l | ¦ |  |  | Ќ | М | Ь | м | ь | ќ | C |
| 1 | 1 | 0 | 1 | 13 |  |  | - | = | M | ] | m | } |  |  | SHY | Н | Э | н | э | § | D |
| 1 | 1 | 1 | 0 | 14 |  |  | . | > | N | ^ | n | ~ |  |  | Ў | О | Ю | о | ю | ў | E |
| 1 | 1 | 1 | 1 | 15 |  |  | / | ? | O | _ | o |  |  |  | Џ | П | Я | п | я | џ | F |
|  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | A | B | C | D | E | FC |  |

# Footnotes

Equivalent to Information Technology—8-Bit Single-Byte Coded Graphic Character Sets—Part 5: Latin/Cyrillic Alphabet. 2nd ed. International Standard, ISO/IEC 8859-5:1999. Geneva: ISO, 1999.

Based on table 2 of reference [2].