Draft Recommendation for
Space Data System Standards

Authentication Security Credentials

PROPOSED Draft Recommended Standard

CCSDS 000.0-W-0

White Book

October 2018

AUTHORITY

|  | Issue: | White Book, Issue 0 |  |
| --- | --- | --- | --- |
|  | Date: | October 2017 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies. The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

FOREWORD

The goal of this specification is to develop a profile to facilitate the use of X.509 certificates within Space applications for those communities wishing to make use of X.509 technology.   In order to relieve some of the obstacles to using X.509 certificates, this document defines a profile to promote certificate management systems for space interoperability. Some communities will need to supplement, this profile in order to meet the requirements of specialized application domains or environments with additional authorization, assurance, or   operational requirements.

The specification allows for Protected Simple Authentication Procedure in conformance with ISO/IEC 9594-8 standard for those communities that have performed an evaluations evaluation of its use.

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. CCSDS shall not be held responsible for identifying any or all such patent rights.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur. This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4). Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard. Its ‘White Book’ status indicates that its contents are not stable, and several iterations resulting in substantial technical changes are likely to occur before it is considered to be sufficiently mature to be released for review by the CCSDS Agencies.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 000.0-W-0 | Security Credentials, Proposed Draft Recommended Standard, Issue 0 | November 2017 | Current draft |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	SECURITY CREDENTIALS	1-1

1.2	PURPOSE	1-1

1.3	SCOPE	1-1

1.4	APPLICABILITY	1-1

1.5	RATIONALE	1-1

1.6	References	1-2

2	Overview	2-1

2.1	X.509 Certificates	2-1

2.2	Protected Simple Authentication 	2-2

3	Credential Specification	A-1

3.1	X.509 Certificates Syntax 	A-1

3.2	Protected Simple Authentication  PROCEDURE	A-1

ANNEX A Implementation Conformance  Statement (ICS) Proforma  (normative)	A-2

ANNEX B Security, SANA, and Patent Considerations  (Informative)	B-1

Figure

No table of contents entries found.

Table

No table of contents entries found.

# Introduction

## SECURITY CREDENTIALS

A credential is a document or certificate that enables trust between entities. In the CCSDS space environment, credentials are needed to allow communicating entities to authenticate each other to determine potential authorization and access control actions. CCSDS recommends two types of credentials in this document, X.509 certificates and protected simple authentication.  The X.509 certificates properties [1] are specified by the Internet Engineering Task Force (IETF) and this document specifies its CCSDS profile. Protected Simple Authentication Procedure, as specified Information Technology Open Systems Interconnection ISO 9594-8 [3], is recommended in this document as an alternative to X.509.

## PURPOSE

This CCSDS recommendation provides the specification for credentials to be used by for authentication CCSDS missions and ground-systems.

## SCOPE

This recommendation may be used by any CCSDS program that requires authentication.

## APPLICABILITY

This recommendation applies to any CCSDS mission requiring end-to-end confidentiality, authentication, or integrity from the sender to the receiver.

## RATIONALE

Many CCSDS missions require security services to protect commanding (command authentication, command confidentiality, command integrity) and payload data (confidentiality, integrity).  This document specifies a CCSDS “credential profiles” to enable the establishment of trust relationships between CCSDS entities.

## References

The following publications contain articles which, through reference in this text, constitute provisions of this document. At the time of publication, the editions indicated were valid. All publications are subject to revision, and users of this Recommended Standard are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below. The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

- RFC 5280 Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile, May 2008 https://www.ietf.org/rfc/rfc5280.txt

- RFC 5818 Updates to the Internet X.509 Public Key Infrastructure Certificate and Certificate Revocation List (CRL) Profile, January 2013 https://www.ietf.org/rfc/rfc6818.txt

- ISO/IEC 9594-8 Information technology — Open Systems Interconnection — The Directory — Part 8: Public-key and attribute certificate frameworks

- Information Technology—Abstract Syntax Notation One (ASN.1): Specification of Basic Notation. 4th ed. International Standard, ISO/IEC 8824-1:2008. Geneva: ISO, 2008.

- Information Technology—ASN.1 Encoding Rules: Specification of Basic Encoding Rules (BER), Canonical Encoding Rules (CER) and Distinguished Encoding Rules (DER). 4th ed. International Standard, ISO/IEC 8825-1:2008. Geneva: ISO, 2008.

- Information Security Glossary of Terms. Green Book. Issue 1. November 2012.CCSDS 350.8-G-1 https://public.ccsds.org/Pubs/350x8g1.pdf

- Time Code Formats. Issue 4. Recommendation for Space Data System Standards (Blue Book), CCSDS 301.0-B-4. Washington, D.C.: CCSDS, November 2010.

- Internet Security Glossary https://www.ietf.org/rfc/rfc2828.txt

- Privacy Enhancement for Internet Electronic Mail https://tools.ietf.org/html/rfc7292

# Overview

Credentials consist  of information that attest to the identity or other attributes of an individual or entity called the subject of the credentials. Some paper credentials include passports, birth certificates, driver’s licenses, and employee identity cards. The authenticity of credentials are established by complex mechanisms that are difficult to copy or forge.

CCSDS recommends two forms of credentials: X.509 certificates and protected simple authentication.

X.509 certificates provide a more secure mechanism than does protected simple authentication.  X.509 is the prime recommended credential for CCSDS.  However, a mission planer may elect to use protected simple authentication  for a space system.

## X.509 Certificates

The properties of X.509 certificates are specified by the Internet Engineering Task Force (IETF) [1].  The CCSDS X.509 profile is specified in this document.  A digital certificate binds a user or service’s identity to a public key by providing information about the subject of the certificate.

Certificate Authorities (CA) are responsible for all aspects of certificates issued to users and devices. This includes control over the enrollment process, the certificate manufacturing process, publication of certificates, revocation of certificates, and re-keying. The CA signs its produced certificates and instructions.

A subscriber is the entity (the user to whom, or device to which, a certificate is issued) whose Distinguished Name (DN) appears as the subject in a certificate, and who asserts that it uses the key and certificate in accordance with this policy.  The term “Subscriber” as used refers only to those who request certificates for uses other than signing and issuing certificates or certificate status information. CAs ensure that all subscribers are informed of their security obligations. The consequences of not complying with those obligations include the revocation of the certificates of subscribers found to have acted in a manner counter to those obligations.

- Subscribers include, but are not limited to the following categories of entities that may wish to conduct official business:

- Personnel: including part-time, Intermittent and temporary employees, contractors, commercial vendors, and agents

- Organizations, branches, departments and personnel, and their contractors and agents

- Workstations, guards and firewalls, routers, trusted servers (e.g., database, domain controller, FTP, and WWW), and other infrastructure components. These components must be under the cognizance of humans, who accept the certificate and are responsible for the correct protection and use of the associated private key. A public key infrastructure  (PKI) Sponsor fills the role of a Subscriber for groups, organizations, disabled personnel, and non-human system components named as public key certificate subjects.

## protected SIMPLE authentication

Protected Simple Authentication  [3] is intended to provide local authorization based upon the distinguished name of a user, a bilaterally agreed to password, and a bilateral understanding of the means of using and handling a password within a single domain. Simple authentication is primarily intended for local use only, that is for peer entity authentication between one Directory User Agent (DUA) and one Directory System Agent (DSA), or between one DSA and another DSA. Simple authentication may be accomplished by:

  - the transfer of the user's distinguished name, password, and a random number and/or a timestamp, all of which are protected by applying a one-way function;

  - the transfer of the protected information described in, a) together with a random number and/or a timestamp, all of which is protected by applying a one-way function.

This process is the basic protected logon activity.  The user name and password are entered and the computer adds data to protect the information that is sent to the server, which verifies the information and either accepts the connection or not.

# Credential Specification

## X.509 Certificate Syntax

### X.509 V3 certificates shall be used

### X.509 V3 certificates shall use generalized time

### X.509 V3 Certificates shall utilize the CCSDS Calendar Segmented Time Code (CCS) [7]

### X.509 V3 output file format shall use Personal Information Exchange Syntax (PKCS12) [9]

### X.509 V3 certificates shall use a digital signature algorithm specified in [CCSDS 352.0-B]

## Protected Simple Authentication  specification

### Protected Simple Authentication shall be implemented as stated in ref [3]

### Protected Simple Authentication shall use a password as stated in ref [3]

### Protected simple authentication shall utilize the CCSDS calendar segmented time code (CCS) formats [7]

### Protected Simple Authentication shall use a cipher algorithm specified in [CCSDS 352.0-B]

Implementation Conformance 
Statement (ICS) Proforma

(normative)

INTRODUCTION

OVERVIEW

This annex provides the Implementation Conformance Statement (ICS) Requirements List (RL) for an implementation of [Specification].  The ICS for an implementation is generated by completing the RL in accordance with the instructions below. An implementation claiming conformance must satisfy the mandatory requirements referenced in the RL.

ABBREVIATIONS AND CONVENTIONS

CRL distribution point: A directory entry or other distribution source for Certificate Revocation Lists (CRL); a CRL distributed through a CRL distribution point may contain revocation entries for only a subset of the full set of certificates issued by one CA or may contain revocation entries for multiple CAs, it is a managed parameter within the X.509 credential.

Conformance

The Conformance Requirements List consists of information in tabular form.  The status of features is indicated using the abbreviations and conventions described below.

Item Column

The item column contains sequential numbers for items in the table.

Feature Column

The feature column contains a brief descriptive name for a feature. It implicitly means “Is this feature supported by the implementation?”

Status Column

The status column uses the following notations:

- M		mandatory;

- O		optional;

- C		conditional;

- X		prohibited;

- I		out of scope;

- N/A		not applicable.

Support Column Symbols

The support column is to be used by the implementer to state whether a feature is supported by entering Y, N, or N/A, indicating:

Y	Yes, supported by the implementation.

N	No, not supported by the implementation.

N/A	Not applicable.

The support column should also be used, when appropriate, to enter values supported for a given capability.

Section three Structure

| Security Credential Structure |  |  |
| --- | --- | --- |
| Item # | Feature | Status | Support |
| 1 | ASN1 | M |  |
| 2 | DER | M |  |
| 3 | X.509.V3 | M |  |
| 4 | tbsCertificate | M |  |
| 5 | Version | M |  |
| 6 | Serial number | M |  |
| 7 | algorithm identification | M |  |
| 8 | Issuer Signature | M |  |
| 9 | Validity from | M |  |
| 10 | Validity to | M |  |
| 11 | Subject | M |  |
| 12 | Subject algorithm identification | M |  |
| 13 | Subject public Key | M |  |
| 14 | Issuer Unique ID | O |  |
| 15 | Subject Unique ID Public Key Info | O |  |
| 16 | Universal Time Coordinated Time Certificate | M |  |
| 17 | Generalized Time | M |  |
| 18 | object identifiers (OID) | O |  |
| 19 | Policy Mapping | O |  |
| 20 | Subject Alternative Name | O |  |
| 21 | Certificate Revocation Lists distribution points | O |  |
| 22 | signatureAlgorithim | M |  |
| 23 | signatureValue | M |  |

Table A-1.1 Security Credentials Structure

INSTRUCTIONS FOR COMPLETING THE RL

An implementer shows the extent of compliance to the Recommended Standard by completing the RL; that is, the state of compliance with all mandatory requirements and the options supported are shown. The resulting completed RL is called an ICS. The implementer shall complete the RL by entering appropriate responses in the support or values supported column, using the notation described in A1.3.  If a conditional requirement is inapplicable, N/A should be used. If a mandatory requirement is not satisfied, exception information must be supplied by entering a reference Xi, where i is a unique identifier, to an accompanying rationale for the noncompliance.

ICS PROFORMA FOR [SPECIFICATION]

GENERAL INFORMATION

Identification of ICS

| Date of Statement (DD/MM/YYYY) |  |
| --- | --- |
| ICS serial number |  |
| System Conformance statement cross-reference |  |

Identification of Implementation Under Test

| Implementation Name |  |
| --- | --- |
| Implementation Version |  |
| Special Configuration |  |
| Other Information |  |

Identification of Supplier

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation Name(s) and Versions |  |
| Other information necessary for full identification, e.g., name(s) and version(s) for machines and/or operating systems; System Name(s) |  |

Identification of Specification

| [CCSDS Document Number] |
| --- |
| Have any exceptions been required? NOTE – A YES answer means that the implementation does not conform to the Recommended Standard. Non-supported mandatory capabilities are to be identified in the ICS, with an explanation of why the implementation is non-conforming. | Yes [ ] No [ ] |

REQUIREMENTS LIST

[See CCSDS A20.1-Y-1, CCSDS Implementation Conformance Statements (Yellow Book, Issue 1, April 2014).]

Security, SANA, and Patent Considerations

(Informative)

Security Considerations

CCSDS utilization of X.509 and Protected Simple Authentication Procedure codifies the mechanisms to be used to validate the identities of users, applications, and devices. CCSDS organizations employ technologies to convey identity and to attest to the claims and trust are associated with those identities.

There are risks to CCSDS systems utilizing credentials if an attacker gains control of the credential management system and they can issue credentials. If a compromised credential management processes results, then there is a need to invalidate existing credentials and re-issue all credentials.

A CCSDS credential management program would result in higher levels of assurance of the credentials while ensuring interoperability and ease the deployments of systems that are pre-tested to integrate with credential management system. The system would provide unified administration, compliance, and auditing, of the x.509 credentials.

security concerns with respect to the CCSDS document

Standard credential usage will provide CCSDS missions with a standard means of authentication of communicating entities.

Data Privacy

Credentials provide a means of identifying/authenticating entities in order to provide accurate access controls to ensure data privacy.

Data Integrity

Credentials enable the means by which data integrity may be provided.

Authentication of Communicating Entities

Authentication is necessary to ensure that the exchange of information is between intended entities. This document specifies the protocols, used for CCSDS compliant systems.

Control of Access to Resources

The authenticity of X.509 certificates and/or Protected Simple Authentication password-based credentials is frequently the basis for assigning access rights to individuals, groups, and system services..

Availability of Resources

This document deals with exchange protocols and not internal system resources.

Auditing of Resource Usage

The authenticity of X.509 certificates and/or Protected Simple Authentication password-based credentials is frequently the basis for establishing accountability to specific individuals for actions taken on a system.  Non-repudiation of user actions cannot be assured if credentials cannot be assured..

Potential threats and attack scenarios

The authenticity of an X.509 certificate is dependent upon the digital signature of the Certificate Authority attesting to the credential.  If the digital signature algorithm used by the CA is of insufficient cryptographic strength, a credential may be spoofed.

Similarly, utilization of a weak cipher for carrying out Protected Simple Authentication makes it possible for a ‘man in the middle’ adversary to intercept the ciphered authentication data during transmission and possibly reverse-engineer the original password.

Consequences of not applying security to the technology

If authentication is not implemented, an attacker could inject false or unauthorized commands into a communications path to the spacecraft’s command chain, and potentially take over control of the spacecraft. This could result in the loss of a mission.

SANA Considerations

This document  does not require any action from SANA. A review of the SANA terms, several additions could be made for clarification reasons i.e. Credentials.

Patent Considerations

Algorithms and processes referenced in this document are in the public domain, and there are no known patents that apply to the recommendations in this document.

# Comments

This looks different than in other CCSDS documents (no brackets). Is this intentional (e.g. for Tom Gannett to fix)?

Are they really documents? What about “pieces of information” Biometric information can also be a credential.

Since this is really relevant why not tell what are todays methods to protect digital credentials?

Stonger = more secure?

I would at least mention briefly that the certificate authority also digitally signs the certificate and thus provides the “glue” with its private key.

What is department business?

This is VERY NASA specific. Is this even relevant for the document?

I am not sure we should allow this option

I don't know what this means.