## Slide 1
CCSDS System Engineering
Area (SEA):
Refined ALACAMAD Approach for CESG-P-2019-12-002
Peter Shames, SEA AD
Ken Andrews, Bernie Edwards, Jon Hamkins, Greg Kazz, Dennis Lee, Victor Sank
3 April 2020

## Slide 2: Motivation
Missions like Gateway, Artemis, and the whole Lunar program (ICSIS, IOAG) have requirements for many of the changes that have been identified.
  ISS has been using AOS over RS+convo for forward links for years, without being able to reference a supporting standard.
  New human exploration missions wish to use AOS over LDPC, for high rate forward and return links, and suitable modulation with ranging.
CCSDS is behind the curve and needs to catch up and provide its user community with the full set of options (via Blue Books) along with guidance on applicability (via a new Green Book).
NASA proposes a principled, architecturally sound, approach to refine the suite of space link standards that is identified as ALACAMAD, "all link (protocols)", "agreed codes and modulations", and "all directions"

## Slide 3: Observation
The refined NASA ALACAMAD position presented here adopts the novel approach stated in the DVB-S2 mods but proposes applying it across the board, with certain technical exceptions that will be clarified:
  DVB-S2: “high data rate telemetry transmission applications, such as Earth Exploration Satellite Services (EESS) payload telemetry and ground-to-space and space-to-space applications (Space Research Services [SRS], inter-satellite links)"
Note the change in scope, from high-rate, near Earth, downlink only, to "all directions”.
That change is coupled with this later statement:
  DVB-S2: Two sublayers of the Data Link Layer are defined for CCSDS space link protocols. The TM and AOS Space Data Link Protocols and the Unified Space Data Link Protocol (USLP) specified in references [3], and [4], and [7], respectively, correspond to the Data Link Protocol Sublayer and provide functions for transferring data using the protocol data unit called the Transfer Frame. The Synchronization and Channel Coding Sublayer provides methods of synchronization and channel coding for transferring Transfer Frames over a space link, while the Physical Layer provides the RF and modulation methods for transferring a stream of bits over a space link in a single direction.
With these changes, the DVB-S2 explicit inclusion of slicing, and a significant set of codes and modulations, there is something very close to the ALACAMAD position that NASA proposes (within the constraints that 131.3 allows).
The refined NASA position, detailed on the next page, seeks to adopt this exact same approach for the rest of the standard CCSDS spacelink protocols, codes, and modulations, including some constraints that make technical sense.

## Slide 4: NASA Position - ALACAMAD
NASA holds the following position:
  CCSDS 131.{0,2,3}-B standards may be used in any direction (forward, return, and cross link)
  CCSDS 131.{0,2,3}-B and 211.2-B standards may be used with fixed-length (AOS or USLP) Transfer Frames
  CCSDS 231.0-B may be used with variable-length (TC or USLP) Transfer Frames
  CCSDS 131.0-B standard block codes (turbo, LDPC, RS, and RS+CC) may be sliced, plus LDPC in CCSDS 211.2-B
  CCSDS 131.{0,2,3}-B standards may be used consistent with CCSDS 401.0-B modulation and ranging recommendations, with necessary revisions for all directions, and with limitations as stated in 131.{2,3}-B standards
  CCSDS 401.0-B modulation recommendations should support high-rate uplinks and cross links with ranging
  CCSDS 131.{0,2,3}-B and 211.2-B standards should support variable-length Transfer Frames, e.g., either natively or with suitable use of the Generic Frame Procedure (GFP)
NASA believes that this issue of how best to serve future missions should be tackled using a principled, architecturally sound, unifying concept that can be applied simultaneously to all affected standards.
A short-hand description of this is to adopt an architectural principle of "all link (protocols)", "agreed codes and modulations", and "all directions", ALACAMAD.
This architectural principle, and the specific set of inclusions/exclusions described in the above bullets, should be discussed within the C&S, SLP, and RFM WGs with the intention of applying the agreed changes, in a uniform fashion, to all 6 affected standards as a set, and committing to publishing those updated standards together, not separately.
Legend:
  CCSDS 131.0-B: TM Sync and Channel Coding
  CCSDS 131.2-B: SCCC
  CCSDS 131.3-B: DVB-S2
  CCSDS 211.2-B: Prox-1 Coding and Sync
  CCSDS 231.0-B: TC Sync and Channel Coding
  CCSDS 401.0-B: RF & Modulation

## Slide 5: BACKUP SLIDES

## Slide 6: NASA Comments on SLS Submission Extension of downlink channel codes to uplink and interface with USLP - Workplan
The history, as presented, leaves out the submission by NASA in Fall 2017, ”of the “three word corrigendum” that added the words “ground-to-space” back into the introduction. That was rejected (largely by Gian Paolo) with the feedback that we should down-select the codes to be used on a ground-to-space link. "
Two more options to resolve this impasse were presented in the Fall of 2018 (18 months ago) that aimed to do that. They were stalled in the WG.
The set of tasks that are listed fail to address a number of topics that NASA believes are important to have a consistent, and optimal, set of SLS standards. The highlighted items are missing from that plan:
  CCSDS 131.{0,2,3}-B standards may be used in any direction (forward, return, and cross link)
  CCSDS 131.{0,2,3}-B and 211.2-B standards may be used with fixed-length (AOS or USLP) Transfer Frames
  CCSDS 231.0-B may be used with variable-length (TC or USLP) Transfer Frames
  CCSDS 131.0-B standard block codes (turbo, LDPC, RS, and RS+CC) may be sliced, plus LDPC in CCSDS 211.2-B
  CCSDS 131.{0,2,3}-B standards may be used consistent with CCSDS 401.0-B modulation and ranging recommendations, with necessary revisions for all directions, and with limitations as stated in 131.{2,3}-B standards
  CCSDS 401.0-B modulation recommendations should support high-rate uplinks and cross links with ranging
  CCSDS 131.{0,2,3}-B and 211.2-B standards should support variable-length Transfer Frames, e.g., either natively or with suitable use of the Generic Frame Procedure (GFP)

## Slide 7: Issues with CESG-P-2019-12-002 History
In the beginning (1980’s)
  CCSDS had only TC and TM, two highly asymmetric protocols, and separate coding and modulation specs
  AOS was introduced in 1989 and the TM S&CC (CCSDS 101.0-B) was modified to state “In addition to being applicable to conventional Packet Telemetry systems [1], the codes in this recommendation are applicable to the forward and return links of Advanced Orbiting Systems (AOS) [2]. “
  In 2002-2003 the SDLP and S&CC docs were extensively revised, but still retained a “one book / one layer of protocol” approach.
In the revised 2003 version of TM S&CC, CCSDS 131.0-B-1, that “AOS forward and return” language was changed to “space-to-ground and space-to-space links”, as a result we added cross-links, but lost use of TM S&CC for AOS forward links.
  There was an attempt to restore this language, but it was rejected. As a result, at present there is no “official” way to encode AOS forward links.

## Slide 8: Issues with CESG-P-2019-12-002 History, contd
In 2012-2013 two new “omnibus” standards were introduced that broke the “one book / one layer of protocol” CCSDS approach. These had been two separate Orange Books, but were made Blue.
  SCCC (CCSDS 131.2-B) and DVB-S2 (CCSDS 131.3-B) are roughly parallel in construction and both contain coding, modulation, slicing of code blocks (convolutional, Turbo, and LDPC), and physical layer ACM/VCM signaling.
  Breaking with normal CCSDS practices that are followed in all other instances, these two, largely duplicative, standards combined these several functions into two parallel books.
  DVB-S2 was stated to be used “near Earth Exploration Satellite Services (EESS) payload telemetry” only, i.e. high rate space-to-ground.
Attempts to add slicing for general use by TM and AOS were largely rejected, and only LDPC downlink slicing was accepted (CCSDS 131.0-B-3).
USLP with features for fixed and variable length frames, and for forward, return, and cross links was published in 2018 (CCSDS 732.1-B-1).
  Attempts to allow generalized use of TM S&CC for USLP forward have also been tabled. At present there is no “official” way to encode USLP fixed length frame for forward links.
  Attempts to define use of variable length USLP frames over TC S&CC have also been tabled.
  Several different approaches to resolve this have been proposed, but these changes have all been rejected or led to impasse within the C&S WG. NASA itself has been a partial cause of some of these delays.

## Slide 9: Issues with CESG-P-2019-12-002 Current Status
The proposed mods to DVB-S2, CCSDS 131.3-P, would change the applicability of this spec from high rate space to ground telemetry to “high data rate telemetry transmission applications, such as Earth Exploration Satellite Services (EESS) payload telemetry and ground-to-space and space-to-space applications (Space Research Services [SRS], inter-satellite links).”
  This amounts to a change for this one omnibus standard to what we characterize as “All Links, All Codes, All Modulations, All Directions”, or “ALACAMAD”.
  A similar change for SCCC is said to be in development.
This amounts to prioritizing/expediting these two omnibus standards, and that is distinct from the response to trying to adopt similarly liberal approaches for AOS, USLP, and slicing, within the whole set of CCSDS mainline coding and modulation specifications.