## Slide 1
CCSDS
Systems Engineering Area
Overview for LIF
Peter Shames
Lunar Interoperability Forum
7 May 2024

## Slide 2: CCSDS Organization Structures
CCSDS Member Space Agencies: NASA, ESA, CNES, DLR, JAXA, ISA, CSA, CNSA, INPE, ROSCOSMOS, UKSA
CCSDS Management Council (CMC), members are the Heads of Delegation of the 11 civilian space agencies. Sami Asmar (NASA/JPL) is the General Secretary.
CCSDS Engineering Steering Group (CESG), members consist of the six Area Directors and their Deputies. Klaus-Juergen Schulz (ESA) is the Chair, Tim Pham (NASA/JPL) is the Deputy Chair.
Area Directors: Systems Engineering Area, Peter Shames (NASA/JPL); Mission Operations and Information Management Area, Daniel Fischer; (ESA), Cross Support Services Area, Erik Barkley (NASA/JPL), Spacecraft Onboard Services Area, Jonathan Wilmot (NASA); Space Link Services Area, Ignacio Sanchez (ESA); Space Internetworking Services Area, Tomaso de Cola (DLR).

## Slide 3: CCSDS Overview End-to-End Architecture
Data Archive Interoperability
Navigation
Spacecraft Monitor & Control
Mission Planning & Scheduling
Mission Ops &
Info Mgt Services
Motion Imagery & Apps
Delay Tolerant Networking
Voice
CFDP Revisions
Space Internetworking
Services
Service Management
Transfer Services
Cloud Computing
Cross Support
Services
RF & Modulation
Space Link Coding & Sync
Data Compression
Space Link Protocols
Space Data Link Layer Security
Optical Communications
Space Link
Services
One Organization’s Assets
Another Organization’s Assets
Onboard Wireless WG
Application Supt Services (incl. Plug-n-Play)
Subnetwork Services WG
Spacecraft Onboard
Interface Services
MISSION CONTROL
CENTER
MISSION CONTROL
CENTER
End Users
End Users
Applications/Archives
Security
Delta-DOR
Systems Architecture
Time Management
Systems Engineering
Six Technical Areas,
Twenty-Four Teams
Working Group (producing standards)
Birds-Of-a-Feather stage (pre-approval)
Special Interest Group (integration forum)

## Slide 4: Systems Engineering Area Working Group Products
Systems Architecture WG
  Systems Architecture methodology
  CCSDS end-to-end architecture description documents
Security WG
  Security Architecture document and implementation guidelines
  Security standards for link & network layer, encryption & authentication, certificates, and key management
Delta-DOR WG
  High precision plane-of-sky position measurements
Time Management WG
  Standards for time exchange, clock correlation, and clock synchronization

## Slide 5: CCSDS End-to-End Architecture Delay Tolerant Network (DTN) (From SCCS-ARD Cross Support Architecture)
CCSDS
Inter Spacecraft
Protocols
Terrestrial
WAN
Ground Station
CCSDS Space-Ground
Protocols
X-band
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node
S-Band
Prox-1
Bundle Agent (Router/S&F)
BP
USLP
ENCAP
BP
LTP
C & S
USLP
X-band
To
VC X&Z
Space User Node
From
VC Z
USLP
S-Band
Prox-1
Space File Application
BP
CFDP
IP-based Network
Terrestrial
WAN
To
VC X
User File Application
IP
BP
CFDP
TCP
Earth User Node
To
VC Z
User File Application
IP
TCP
BP
CFDP
Space Routing Node MOC
From
VC X
Space File Application
CFDP
CCSDS Ground-Ground Protocols
Interoperability Points
ENCAP
ENCAP

## Slide 6: CCSDS End-to-End Architecture Delay Tolerant Network (DTN) (with Optical Comm)
CCSDS
Inter Spacecraft
Protocols
Terrestrial
WAN
Ground Station
CCSDS Space-Ground
Protocols
Optical
IP
TCP
Optical C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node
S-Band
Prox-1
Bundle Agent (Router/S&F)
BP
USLP
ENCAP
BP
LTP
Optical C & S
USLP
Optical
To
VC X&Z
Space User Node
From
VC Z
USLP
S-Band
Prox-1
Space File Application
BP
CFDP
IP-based Network
Terrestrial
WAN
To
VC X
User File Application
IP
BP
CFDP
TCP
Earth User Node
To
VC Z
User File Application
IP
TCP
BP
CFDP
Space Routing Node MOC
From
VC X
Space File Application
CFDP
CCSDS Ground-Ground Protocols
ENCAP
ENCAP
Optical Comm instead of RF

## Slide 7: CCSDS End-to-End Architecture Delay Tolerant Network (DTN) (With Commercial Service Providers)
CCSDS
Inter Spacecraft
Protocols
Terrestrial
WAN
Ground Station
CCSDS Space-Ground
Protocols
X-band
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node
S-Band
Prox-1
Bundle Agent (Router/S&F)
BP
USLP
ENCAP
BP
LTP
C & S
USLP
X-band
To
VC X&Z
Space User Node
From
VC Z
USLP
S-Band
Prox-1
Space File Application
BP
CFDP
IP-based Network
Terrestrial
WAN
To
VC X
User File Application
IP
BP
CFDP
TCP
Earth User Node
To
VC Z
User File Application
IP
TCP
BP
CFDP
Space Routing Node MOC
From
VC X
Space File Application
CFDP
CCSDS Ground-Ground Protocols
ENCAP
ENCAP
Interoperability Points
Commercial Service Provider
Bundle Agent (Router/S&F)
Custom / Private DTN Network
Implementation
IP
TCP
BP
CFDP

## Slide 8: BACKUP

## Slide 9: Key SEA Standards that support Lunar Interoperability and DTN (1/2)
Standard | CCSDS# | Status | Synopsis | Comments
Reference Architecture for Space Data Systems | CCSDS 311.0-M-1 | Published (update in progress) | Formal methodology for describing space systems architectures | Leverages ISO 42010 and other best practices
Cross Support - Architecture Description Document | CCSDS 901.1-M-1 | Published (update in progress) | Pragmatic guide re how to use more than 50 CCSDS standards to build interoperable systems | CCSDS WGs produce “bricks”, this tells you how to build a wall out of them
CCSDS Guide for Secure System Interconnection | CCSDS 350.4-G-2 | Published | Guidelines for interconnecting space agency networks and IT systems, specifically to enable secure cross support | Leverages NIST 800-47 and tailors it for space systems, provides interconnect templates
Security Architecture for Space Data Systems | CCSDS 351.0-M-1 | Published (update in planning) | Define overall CCSDS conceptual framework for the incorporation of security into mission space data systems | Uses RASDS framework, leverages other CCSDS standards & IETF RFCs

## Slide 10: Key SEA Standards that support Lunar Interoperability and DTN (2/2)
Standard | CCSDS# | Status | Synopsis | Comments
CCSDS Cryptographic Algorithms | CCSDS 352.0-B-2 | Published | Recommendations for providing space mission information confidentiality, authentication, or authenticated confidentiality | Leverages FIPS, NIST, and ISO Standards
CCSDS Authentication Credentials | CCSDS 357.0-B-1 | Published | Provides specification for credentials to be used for authentication by CCSDS missions and ground systems | Leverages IETF X.509, PKI, other RFCs & ISO standards
Delta-Differential One Way Ranging (Delta-DOR) Operations | CCSDS 506.0-M-2 | Published | A VLBI technique used with Doppler and ranging data to enhance spacecraft navigation by improving spacecraft angular position in the plane of sky | Leverages VLBI techniques along with a Quasar catalog that provides a celestial reference frame
Time Management | CCSDS ???-G-1 | Draft (to be published) | Document existing frequency and timing standards, including GNSS, clock correlation, and time synchronization methods used in space missions | Leverages NIST, GPS, IETF RFCs, CCSDS, and other reference & mission sources

## Slide 11: CCSDS Overview End-to-End Architecture - Static
Data Archive Interoperability
Navigation
Spacecraft Monitor & Control
Mission Planning & Scheduling
Mission Ops &
Info Mgt Services
Motion Imagery & Apps
Delay Tolerant Networking
Voice
CFDP Revisions
Space Internetworking
Services
Service Management
Transfer Services
Cloud Computing
Cross Support
Services
RF & Modulation
Space Link Coding & Sync
Data Compression
Space Link Protocols
Space Data Link Layer Security
Optical Communications
Space Link
Services
One Organization’s Assets
Another Organization’s Assets
Onboard Wireless WG
Application Supt Services (incl. Plug-n-Play)
Subnetwork Services WG
Spacecraft Onboard
Interface Services
MISSION CONTROL
CENTER
MISSION CONTROL
CENTER
End Users
End Users
Applications/Archives
Security
Delta-DOR
Systems Architecture
Time Management
Systems Engineering
Six Technical Areas,
Twenty-Four Teams
Working Group (producing standards)
Birds-Of-a-Feather stage (pre-approval)
Special Interest Group (integration forum)