## Slide 1
CCSDS
Space Internetworking Services (SIS) Area
Standards Applicable for Lunar Interoperability
Tomaso de Cola
Lunar Interoperability Forum
7 May 2024

## Slide 2: SIS Area Relative to CCSDS Technical Organization
Data Archive Interoperability
Navigation
Spacecraft Monitor & Control
Mission Planning & Scheduling
Mission Ops &
Info Mgt Services
Motion Imagery & Apps
Delay Tolerant Networking
Voice
CFDP Revisions
Space Internetworking
Services
Service Management
Transfer Services
Cloud Computing
Cross Support
Services
RF & Modulation
Space Link Coding & Sync
Data Compression
Space Link Protocols
Space Data Link Layer Security
Optical Communications
Space Link
Services
One Organization’s Assets
Another Organization’s Assets
Onboard Wireless WG
Application Supt Services (incl. Plug-n-Play)
Subnetwork Services WG
Spacecraft Onboard
Interface Services
MISSION CONTROL
CENTER
MISSION CONTROL
CENTER
End Users
End Users
Applications/Archives
Security
Delta-DOR
Systems Architecture
Time Management
Systems Engineering

## Slide 3: SIS Area Standards Overview
Delay Tolerant Networking (DTN)
  Primarily concerned with standards enabling DTN operations across space and ground assets in complex multi-hop space missions
    Different ongoing activities aimed at consolidating DTN services (e.g., BP, LTP, security, network management, etc.)
CCSDS File Delivery Protocol revisions (CFDP)
  Primarily concerned with the maintenance and upgrade of CFDP and related interaction with the underlying protocol layers (e.g., DTN)
Motion Imagery and Applications (MIA)
  Primarily concerned with the generation of video streams and their transportation through the CCSDS protocol stack in space missions
    Current a special focus in on the interaction of MIA services with the DTN protocol stack
Voice
  Primarily concerned with voice applications for manned missions
    Currently dormant for lack of activity

## Slide 4: DTN E2E Enabled Architecture
CCSDS
Inter Spacecraft Protocols
Terrestrial WAN
Space Routing Node - A
S-Band
Prox-1
Bundle Agent (Router/S&F)
BP
USLP
ENCAP
BP
LTP
C & S
USLP
X-band
IP-based Network
To
VC X
User File Application
IP
BP
CFDP
TCP
Space Routing Node MOC
Ground Station
X-band
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
To
VC X&Z
From
VC X
Space File Application
CFDP
Space User Node
From
VC Z
USLP
S-Band
Prox-1
Space File Application
BP
CFDP
CCSDS Ground-Ground Protocols
Earth User Node
To
VC Z
User File Application
IP
TCP
BP
CFDP
CCSDS
Space-to-Ground Protocols
ENCAP
ENCAP
Bundle Agent (Router/S&F)

## Slide 5: Selected Key SIS books that support Lunar Interoperability (1/4)
Standard | CCSDS # | Status | Synopsis | Comments/Benefits
Bundle Protocol Specification (BPv6) | CCSDS 734.2-B-1 | Published | Protocol baseline for DTN protocol architecture | Specific CCSDS profile of IETF RFC 5050 to enable DTN operations in space missions and meet store-carry-forward requirements
Bundle Protocol Specification (BPv7) | CCSDS 734.2-B-2 | In progress (interoperability testing under preparation) | Protocol baseline for DTN protocol architecture | Update of the existing CCSDS blue book so as to define a new CCSDS profile of RFC 9171 and hence allow for more performant DTN operations in space. It is not compatible with the existing CCSDS BP specification.
Schedule-Aware Bundle Routing | CCSDS 734.3-B-1 | Published | Routing support in DTN | Definition of schedule-aware (i.e. contact-based) routing procedures implemented within BP, to support data distribution over deterministically intermittent links.

## Slide 6: Selected Key SIS books that support Lunar Interoperability (2/4)
Standard | CCSDS # | Status | Synopsis | Comments/Benefits
Bundle Protocol Security Protocol (BPsec) for CCSDS | CCSDS 734.5-B-1 | In progress (update after agency review) | Security specification for BP | It defines extension blocks to the BP as a CCSDS profile of IETF RFC 9172 to support integrity and confidentiality services
DTN Network Management | NA (orange book) | In progress | Network management support in DTN | Definition of the logical architecture of network management ecosystem and related , the data model used to express management directives, the structured syntax used to identify model objects, transport encodings, and a binding to carrying those encodings over the Bundle Protocol
Compressed Bundle Status Reporting and Custody Signaling | NA (orange book) | In progress | BP status reporting | Extension of the CCSDS BPv7 specification to provide report on bundle status (e.g. received, transmitted, etc.) and possible support to end-to-end retransmission and/or in-network reliability (custody transfer as it was in BPv6).

## Slide 7: Selected Key SIS books that support Lunar Interoperability (3/4)
Standard | CCSDS # | Status | Synopsis | Comments/Benefits
DTN Multipoint Delivery | NA (orange book) | In progress | Multipoint delivery (i.e., multicast) | Extension blocks for BP to enable multi-point delivery according to service requirements
Bundle in Bundle Encapsulation | NA (orange book) | In progress | Transport of a bundle within another bundle | It supports backward compatibility for applications that only support a previous version of the Bundle Protocol (e.g., BPv6 over BPv7) or provides BP-in BP tunnels for QoS and security purposes
Bundle Protocol Quality of Service Extensions | NA (orange book) | In progress | QoS support in DTN | Definition of quality of service (QoS) extensions for Bundle Protocol and related policies.

## Slide 8: Selected Key SIS books that support Lunar Interoperability (4/4)
Standard | CCSDS # | Status | Synopsis | Comments/Benefits
Licklider Transmission Protocol (LTP) for CCSDS | CCSDS 734.1-B-1 | Published | BP convergence layer protocol for communications over space links | Working underneath BP and on top of EPP/USLP to offer reliable (ARQ-based) or unreliable data communication services
High Performance Reliability Protocol (HPRP) | NA (orange book) | In progress | Upgrade of LTP | Revision of the LTP protocol specification to make it more effective from an implementation standpoint and more suitable for high data-rate links. It is not compatible with the existing CCSDS LTP specification.