## Slide 1
CCSDS
Space Link Service Area
Overview for LIF
Ignacio Aguilar Sánchez
Lunar Interoperability Forum
7 May 2024

## Slide 2: Space Link Services in CCSDS
Data Archive Ingestion
Navigation
Spacecraft Monitor & Control
Mission Planning & Scheduling
Mission Ops &
Info Mgt Services
Motion Imagery & Apps
Delay Tolerant Networking
Voice
CFDP Revisions
Space Internetworking
Services
CS Service Management
CS Transfer Services
Cloud Computing
Cross Support
Services
RF & Modulation
Space Link Coding & Sync.
Data Compression
Space Link Protocols
Space Data Link Layer Security
Optical Communications
Space Link
Services
One Organization’s Assets
Another Organization’s Assets
Onboard Wireless WG
Application Supt Services (incl. Plug-n-Play)
Subnetwork Services WG
Spacecraft Onboard
Interface Services
MISSION CONTROL
CENTER
MISSION CONTROL
CENTER
End Users
End Users
Applications/Archives
Security
Delta-DOR
Systems Architecture
Time Management
Systems Engineering
Typical Mission Profile

## Slide 3: Space Link Services Area Working Group Products (1/2)
RF Modulation WG
  Appropriate modulation schemes for telecommand, telemetry and ranging signals in applicable frequency bands for space-to-ground, ground-to-space and space-to-space links
Space Link Coding & Synchronization WG
  Efficient standards for coding and synchronization schemes for telecommand and telemetry for space-to-ground, ground-to-space and space-to-space links
Data Compression WG
  Data compression standards both for instrument telemetry and housekeeping enabling efficient data rates and data volume reduction

## Slide 4: Space Link Services Area Working Group Products (2/2)
Space Link Protocols WG
  Efficient space data link protocols and related interfaces to space link transfer services applicable to space-to-ground, ground-to-space and space-to-space links
Space Data Link Layer Security WG
  Security services compatible with Space Data Link Protocols: authentication (with anti-replay), confidentiality and authenticated confidentiality
  Associated security management functions (monitoring and control, security association, cryptographic keys)
Optical Communications WG
  ​Optical communications standards applicable to both physical as well as synchronization and channel coding for space links in two regimes: high photon efficiency and…

## Slide 5: Space Link Services Interoperability Points in E2E Architecture
CCSDS
Inter Spacecraft Protocols
Terrestrial WAN
Space Routing Node - A
S-Band
Prox-1
Bundle Agent (Router/S&F)
BP
USLP
ENCAP
BP
LTP
C & S
USLP
X-band
IP-based Network
To
VC X
User File Application
IP
BP
CFDP
TCP
Space Routing Node MOC
Ground Station
X-band
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
To
VC X&Z
From
VC X
Space File Application
CFDP
Space User Node
From
VC Z
USLP
S-Band
Prox-1
Space File Application
BP
CFDP
CCSDS Ground-Ground Protocols
Earth User Node
To
VC Z
User File Application
IP
TCP
BP
CFDP
CCSDS
Space-to-Ground Protocols

## Slide 6
BACKUP

## Slide 7: Key SLS Standards that support Lunar Interoperability (1/2)
Standard | CCSDS# | Status | Synopsis | Comments
Proximity-1 Space Data Link Protocol | CCSDS 211.0-B-6 | Published (update in progress) | Link layer protocol for proximity environments | Includes new directive set for lunar operations. Offers a standardized bi-directional communications protocol and corresponding operations concept between peers in planetary scenarios (e.g., orbiter-lander).
USLP | CCSDS 732.1-B-2 | Published (update in progress) | Link layer protocol for all environments | Version 3 pending secretariat release. Provides flexibility and improved capabilities inherited from TC, TM and AOS protocols, allowing its use in almost any space link scenario in microwave or optical communications technologies.
Proximity-1 – Coding and Synchronization sublayer | CCSDS 211.2-B-3 | Published | C&S layer for using Proximity-1 (see Prox-1 block in space user and routing node) | To be used in combination with 211.0-B and 211.1-B. Benefits in line with its Space Link Protocol companion.
TM synchronization and coding | CCSDS 131.0-B-5 | Published (update in progress) | C&S layer for space-to-Earth links and Earth-to-Space (see C&S block in space routing node and ground station) | Applicable to Earth-to-space only for TM-like links. Not meant for TC applications Update is in progress for Transfer Frame slicing and Turbo Code interleaver. Offers a portfolio of standardized flexible solutions to enhance space link power efficiency and error rate performances.

## Slide 8: Key SLS Standards that support Lunar Interoperability (2/2)
Standard | CCSDS# | Status | Synopsis | Comments
TC synchronization and coding | CCSDS 231.0-B-4 | Published | C&S layer for Earth-to-space link, specifically for TC applications | Meant to be combined only with modulations foreseen in (401) 2.2.2 – 2.2.8 Offers a portfolio of standardized flexible solutions to enhance space link power efficiency and error rate performances.
Proximity-1 – Physical Layer | CCSDS 211.1-B-4 | Published | Physical layer procedures used with Proximity-1 Data Link Layer | To be used in combination with 211.0-B and 211.2-B. Benefits in line with its Space Link Protocol companion. Operates in UHF Frequencies. Ongoing work to incorporate S-band and Ka-band frequencies.
Space Data Link Security Protocol | CCSDS 355.0-B-2 | Published | Provides optional security services to space link protocols (TC, TM, AOS and USLP). | Offers authentication, confidentiality or authenticated confidentiality services. It could protect access to Lunar communications relays.
Optical Communications Physical Layer | CCSDS 141.0-B-1 | Published | Specifies the physical characteristics of the telemetry signal and, separately, the physical characteristics of the beacon and optional telecommand signal. | Applicable to space-to-ground and ground-to-space photon starved links through an atmospheric channel. They could support optical TM links between Lunar region spacecraft and Earth.
Optical Communications Coding and Synchronization | CCSDS 142.0-B-1 | Published | Provides a specification for High Photon Efficiency (HPE) optical communications. | Applicable to space-to-ground and ground-to-space photon starved links through an atmospheric channel. They could support optical TM links between Lunar region spacecraft and Earth.