## Slide 1
CCSDS System Engineering
Area (SEA): System Architecture WG (SAWG)
RASDS++ Update Views
Peter Shames, Systems Engineering Area Director
Fred Slane, Ramon Krosley, Costin Radulescu, Shelbun Cheng, Christian Stangl
22 Nov 2024
(“Word” version, edited for easy use as figures)
Updated w/PID fixes post CESG review

## Slide 2: Revision of the Reference Architecture for Space Data Systems (RASDS)
Reference Architecture for Space Data Systems (RASDS) CCSDS 311.0-M-1 (ISO 13537) was published in Sept 2008
  RASDS has been leveraged by a number of CCSDS documents and also by several mission design projects.
  The document is consistently in the top 20-30 documents downloaded from the CCSDS web site, it is being used and referenced.
  RASDS is (over)due for a refresh, the question has been just what to do, and when.
The extensions to RASDS developed in producing the ASL ADD (CCSDS 371.0-G) and the SCCS-ARD and ADD, should be incorporated into the RASDS revision
  ASL ADD and SCCS-ADD examples may be adopted to improve graphics.
  Additional descriptive text on viewpoint & view construction should be added.
  In keeping with current MBSE best practices, an annex should be provided with a set of SysML representations. Published papers, and other CCSDS examples, addressing this already exist.
ISO TC20/SC14 wishes to make use of RASDS and is adopting it as a framework for describing their standards
  A liaison agreement has been agreed by the CMC, CMC-P-2020-03-003, dated 4-7-2020.
  A plan for these revisions has been outlined. See the following pages …

## Slide 3: Terminology, Taxonomy, Ontology
Terminology: Terminology is a group of specialized words and respective meanings in a particular field. A term is a word, compound word, or multi-word expressions that in specific contexts is given specific meanings—these may deviate from the meanings the same words have in other contexts and in everyday language.
Taxonomy: Taxonomy is the practice and science of categorization or classification. A taxonomy (or taxonomical classification) is a scheme of classification, especially a hierarchical classification, in which things are organized into groups or types. Many taxonomies are hierarchies (and thus, have an intrinsic tree structure), but not all are.
Ontology: In computer science and information science, an ontology encompasses a representation, formal naming, and definition of the categories, properties, and relations between the concepts, data, and entities that substantiate one, many, or all domains of discourse. More simply, an ontology is a way of showing the properties of a subject area and how they are related, by defining a set of concepts and categories that represent the subject.

## Slide 4
System Architecture Model Objectives
"Modeling, in the broadest sense, is the cost-effective use of something in place of something else for some cognitive purpose. It allows us to use something that is simpler, safer or cheaper than reality instead of reality for some purpose.
A model represents reality for the given purpose; the model is an abstraction of reality in the sense that it cannot represent all aspects of reality. This allows us to deal with the world in a simplified manner, avoiding the complexity, danger and irreversibility of reality."
  Rothenberg, Jeff. “The Nature of Modeling”, RAND, https://www.rand.org/content/dam/rand/pubs/notes/2007/N3027.pdf
Notes: 4

## Slide 5: Relationship of ASL & SCCS-ARD/ADD to RASDS++ Evolution
Two documents, the ASL ADD and the SCCS-ARD/ADD, both use the Reference Architecture for Space Data Systems (RASDS) framework
Each used a consistent set of viewpoints and views based on RASDS method and representations
  RASDS provided the baseline set of viewpoints (Enterprise, Functional, Connectivity (deployment), Protocol, and Information.
  The ASL ADD added some useful extensions for describing the functional viewpoint, improved representation for the information viewpoint, and added a tabular services viewpoint.
  The SCCS-ARD/ADD developed a representative set of physical elements (nodes), extensively used the Connectivity viewpoint featuring deployed functions and protocol stacks, and developed a set of protocol stack building blocks that could be used to describe end-to-end architectures.
  These extensions, and others needed to meet SC14 needs, are being incorporated into the RASDS++ update.

## Slide 6
Proposed RASDS++ Extensions
(SC 14 Collaboration)
Service Viewpoint
  Already introduced in CCSDS SCCS-ARD/ADD & ASL
  Covers exposed system service interfaces and interface bindings, hardware, software, and Persons
  Tabular representation, ties to protocol stacks and interface bindings
Physical / Structural Viewpoint
  Extracted from present Connectivity Viewpoint, defining Components and Connectors, to add new attributes & types
  Add support for physical aspects of elements, structures, energetic flows, position, attachment, field of view, power, thermal, radiation, other energetic views
Operations Viewpoint
  Create new Operations Viewpoint
  Add support to describe Operations processes, procedures, and related behavior
  Propose correlation to / derivation from from UML activity / sequence diagrams

## Slide 7
RASDS Concept Model … and Proposed TC20/SC14 extensions
RASDS++ as Architectural Framework *
Connectivity / Deployment Viewpoint
Connectivity
Components & connectors
RF & optical
Physics of Motion
End to End Views
External Forces
Performance
Physical Viewpoint -Structures:
Power
Mass
Thermal
Orbit
Propulsion
Enterprise Viewpoint (15288)
Organizations
Persons
Use Case
Contracts Agreements (CONFERS)
Glossary
Augment to Capture:
Capabilities
Mission Design & Drivers (OV-1?)
Requirements
Phases
Engineering Viewpoint
System Design & Construction - realization
Functional allocation
Distribution of functions and trade-offs
Development
Validation & verification & engineering processes
Just use 15288 or agency specs
* Reference Architecture for Space Data Systems (RASDS)
** Reference Model Open Distributed Processing (RMODP, ISO 10746 spec)
Functional Viewpoint
Functional Structure - abstract
Functional Behavior & abstract interfaces
End to End View
Cross Support Services
Communications Viewpoint
Protocols & comm standards
End to end Information Transfer Mechanisms
Cross Support Services
Service interface bindings
State & Sequence charts ?
Information Viewpoint
Information & information management
Data structures, syntax & semantics
Attributes & constraints (ASN, FRM, EDS)
Mission Assurance Viewpoint ??
Enterprise Risks
Cost
Validation & verification
Safety
Reliability & quality
Operations Viewpoint
Processes
Procedures
Activities, tasks, actions
Scenarios, Events
Modes & states
Services Viewpoint
Tabular views of functions, operations, and related standards
Support system Design & Construction - realization
Correspondence to Protocol stacks and interface bindings
Functional allocation and distribution of functions and trade-offs (correspondence)
Just use 15288 or agency specs
New Viewpoint
Modified Viewpoint
De-selected Viewpoint
Notes: 7

## Slide 8: Relationship to System Engineering “Vee”
Copied from: NASA SE Process NPR 7123.1D
Called the “SE Vee”, or the “SE Engine”
Questions:
- Where does systems architecture occur in this process?
- What process is recommended to create a systems architecture?
- How does systems architecture relate to the rest of this process?
Answer:
- “Logical decomposition” and “Preliminary Design” is what systems architecture is associated with.
- The process is described as “logical decomposition”.
- “Logical decomposition” is often convolved with requirements decomposition and design evolution.
Observations:
- There is no definition of “Architecture”, but there is one for Logical Decomposition: “The decomposition of the defined technical requirements by functions, time, and behaviors to determine the appropriate set of logical and data architecture models and related derived technical requirements. Models may include functional flow block diagrams, timelines, data control flow, states and modes, behavior diagrams, operator tasks, system data, metadata, data standards, taxonomy, and functional failure modes.“
- There is no stated methodology, but DoDAF is mentioned in the NASA SE Handbook
- This “Vee”, and variations on it, “Dual V”, “W”, appear in many related processes, including Agile development
- Sometimes they actually show “Architecture” and model based processes
- ISO 15288 has a more complete Architecture Design Process in Sec 5.5.4
Fig 2-1

## Slide 9: Relationship of Systems Architecting to Systems Engineering
The systems architect is an information and communications technology professional. Systems architects define the architecture of a computerized system (i.e., a system composed of software and hardware) in order to fulfill certain requirements. Such definitions include: a breakdown of the system into components, the component interactions and interfaces (including with the environment, especially the user), and the technologies and resources to be used in its design and implementation.
The systems architect's work should seek to avoid implementation issues and readily permit unanticipated extensions/modifications in future stages. Because of the extensive experience required for this, the systems architect is typically a very senior technologist with substantial, but general, knowledge of hardware, software, and similar (user) systems.
Wikipedia: https://en.wikipedia.org/wiki/Systems_architect
Systems engineering is an interdisciplinary field of engineering and engineering management that focuses on how to design, integrate, and manage complex systems over their life cycles. At its core, systems engineering utilizes systems thinking principles to organize this body of knowledge. The individual outcome of such efforts, an engineered system, can be defined as a combination of components that work in synergy to collectively perform a useful function.
Issues such as requirements engineering, reliability, logistics, coordination of different teams, testing and evaluation, maintainability and many other disciplines necessary for successful system design, development, implementation, and ultimate decommission become more difficult when dealing with large or complex projects. Systems engineering deals with work-processes, optimization methods, and risk management tools in such projects.
Wikipedia: https://en.wikipedia.org/wiki/Systems_engineering
Systems Architecting
Systems Engineering
Time:
Iteration (when necessary)
Enterprise Architecting
Fig 2-2

## Slide 10
Reference Architecture for Space Data Systems
Enterprise
Business Concerns
Capabilities, Organizations, Governance
Physical
Physical Concerns
Component & Connector perspective
Functional
Computational Concerns
Functional composition
Information
Data Concerns
Relationships and transformations
Communications
Protocol Concerns
Communications stack perspective
Derived from: RM-ODP, ISO 10746
Compliant with ISO 42010 and IEEE 1471
Connectivity Derived Viewpoint
Structural Derived Viewpoint
Services
System Service Concerns
Interfaces, protocols, and data exchanged
Operations
Operations Concerns
Processes, Activities, Products
Fig 2-3
Notes: 10

## Slide 11: Comments on Engineering and Mission Assurance Viewpoints
Engineering viewpoint concerns are already thoroughly covered by ISO 15288.
  The SE “V”
  Processes and steps, including Systems Architecture even if it may not be explicit
  There are also various agency specific standards
Mission Assurance processes are well covered by ISO 15288 and agency standards.
  Since both of these are process oriented in nature, and these processes are well documented, no added Viewpoint in RASDS is required.
What RASDS++ does, however, is provide a standardized method to create and document the system architectures.
  This is a capability that these standards implicitly require, but do not provide

## Slide 12: Revised RASDS++ (DRAFT) Top Level Object Ontology
Function
Behavior
Constraints
Interfaces
Logical structure
Connector
(Link)
Type
Communication
Protocol stack
Comm standards
Enterprise
Requirements
Objectives
Governance
Use Cases
Mission
FulfilledBy
Meets
IsImplementedBy
ComposedOf
ComposedOf
ComposedOf
Contains
Instances
Produces
Consumes
ConnectVia
Uses
ProvidesService
AssociatedWith
Implements
Information
Data
Metadata
Rules
Develops / Owns
Component
(Node)
Type
Attributes
(comm, power,
propulsion,
thermal, other)
Attachment /
Interface
Calls
Environment
Physical Environs
Location
Attributes
Meta-model
(for each Viewpoint)
Define Objects
Define Rules
Address Concerns
Define Relations
Operations
Processes
Activities
Tasks
Modes/states
Scenarios
Performs
Invokes
Service
Svc Behavior
Interface Binding
Svc Constraints
Offers
DefinedBy
Flows
(comm, power,
propulsion,
thermal, other)
Define Correspondences
Resources
Standards
Fig 2-4
Affects

## Slide 13: RASDS++ Viewpoint Specifications
Each RASDS++ Viewpoint addresses:
  Stakeholder concerns: What does the stakeholder care about (what must views address)
  Objects: The fundamental kinds of objects (functions, data, organizations, physical elements, protocols, etc)
  Relationships: The descriptions of object attributes and how they relate, including correspondences to other objects
  Representation: How objects and relationships of different types may be represented in diagrams
MBSE adaptations:
  The primary work that must be done to use RASDS++ with MBSE tools is to:
    Define profiles to accurately represent the different classes of objects and relationships
    Create stereotypes that can be used consistently in the tools
    Use the profiles and methods to develop the MBSE style representations

## Slide 14: RASDS++ Representations (with ASL and SC14 extensions)
Organizational Element
Communications Protocol
Data
Store
Data Store
Physical Node
InformationObject
Physical or
Functional Connection
Logical Link
between Elements
Organizational Domain
Router
Functional Element
Link Layer
Service Access Point
Peering
Arrangement
DATA
Service Provider
Service Consumer
Fig 3-1 w/ mods
Notes: ASL Fig 3-1, trim headers & footers

## Slide 15
Object
Unified Set of Object Features Representation
Core Functions
What the object
does
External Interfaces:
How external elements
are controlled
Management Interfaces:
How objects are configured
controlled, and monitored
Service Interfaces:
How services are
requested & supplied
Concerns:
Issues
Resources
Policies
Fig 3-2

## Slide 16: RASDS Relationship Types (UML derived)
Inheritance
Composition
Aggregation
Association (other relationship, labelled)
Directional Association
Correspondence
Read as sentence with subject = start of arrow, verb = label, and object = end of arrow
Inheritance: The ability of one class (child class) to inherit the identical functionality of another class (super class), and then add new functionality of its own. E.g. super class: “round ball”, child classes: “baseball”, “soccer ball”, “basketball”, but not “football”
Composition: A special case of association that describes a relationship between a whole and its existential parts. E.g. a person, with head, arms, legs. Note that the parts cannot exist separate from the rest of the person.
Aggregation: a special type of association in which objects are assembled or configured together to create a more complex object. E.g. a car is assembled from a body, wheels, and an engine. Note that the engine can exist apart from the rest of the car
Association (other relationship, labelled): Association is a relationship between classifiers which is used to show that instances of classifiers could be either linked to each other or combined logically.
Directional Association: Associations that are navigable in only one direction. A directed association indicates that control flows from one classifier to another; for example an actor to a use case.
Fig 3-3

## Slide 17: Example Ontology - Formalized Relationships among Terms (Functional Viewpoint example with added Correspondences)
Behavior
System
FunctionalObject
Processes ..
Implemented by 1.. (corr)
Data
Exposes 0..
Service
Interface
Function : The set of actions or activities performed by some object to achieve a goal; the transformation of inputs to outputs that may include the creation, modification, monitoring, or destruction of elements.
Correspondence: A function such that for elements in one viewpoint there is a related element in another viewpoint; the condition of being in conformity from elements in one viewpoint to elements in another.
Has …
Composed of …
Specified by .. (corr)
  Correspondence (corr): Colored objects shown with dashed lines are formally defined in other viewpoints and are referenced by correspondence
Implements
Fig 3-4

## Slide 18: Technical Architecture Definitions
System
  A System is a group of interacting or interrelated Elements that act according to a set of rules to form a unified whole. A System, surrounded and influenced by its environment, is described by its boundaries, structure and purpose and expressed in its functioning.
  A collection of interacting components organized to accomplish a specific function or set of functions. A System is composed of Elements, which may be any of: Hardware, Software, Persons, and Procedures.
Function
  A Function is the purpose for which an Element is intended. This can be an activity performed by the Element or the usage of this Element by other parts of the system.
  A Function is interpreted as a specific process, action or task that a System is able to perform.
Service
  A mechanism to enable access to a set of one or more functions of an Element, where the access is provided using a prescribed interface and is exercised consistent with constraints and policies as specified by the service description.
  A Service is an exposed interface of a Function.
Interface
  An Interface represents a set of mechanical, electrical, signal, or other properties that describe some aspect of a Element’s connection to or interaction with another Element.
  An interface is formed of the ports on two or more elements and the junction that joins them.

## Slide 19: Enterprise Viewpoint - Revised
The Enterprise Viewpoint focuses on the purpose, scope, and policies for the space data system. It describes the organizational entities and relationships; their roles, requirements, goals, objectives, scenarios, constraints; and how to meet them.
Stakeholder Concerns:
  the purpose, scope, and policies for the system;
  the objectives, operations concepts, and scenarios for the system;
  the requirements and constraints on the system;
  roles played by the system elements;
  activities undertaken by the system.
Enterprise Objects:
  Types: Organizations, both formal and informal (missions, projects, communities, with their roles and responsibilities), and Resources (facilities or other elements having enterprise operational or service roles);
  Attributes: name, role, objectives, point of contact, location, members, resources, provided services, types, interfaces and data, interaction modes, requirements, constraints;
Domains (boundaries of responsibility or ownership, includes requirements, system elements);
Relationships (ownership, membership, participation, roles, contractual);
Correspondences to Information objects (defined instances of documents, agreements, contracts, policies, requirements, objectives, goals, scenarios, membership lists, interface specifications, where formal specifications of the data to be exchanged are found in the Information Viewpoint).

## Slide 20
Enterprise Viewpoint - Enterprise Object
(Organizational Entity Features)
Attributes:
Identifier
Organization
Assets & Resources (Persons, Systems, Budget)
Roles
Objectives
Use cases
Requirements
Capabilities
Risk Management
Agreements / contracts
External Interfaces:
Scope
Requirements
Policies
Governance
Agreements / Contracts
Funding / Resources
Management Interfaces:
Scope
Requirements
Policies
Governance
Purpose / Mission / mission types
Funding / Resources
Service Interfaces:
Requirements
Agreements
Contracts
Funding
Enterprise
Object
Fig 4-1

## Slide 21
Enterprise Viewpoint - Enterprise Object
(Organizational Entity Features)
Notes
Enterprise Object Notes:
Interfaces of Enterprise Objects are often described as document exchanges
Specific Enterprise Objects may own / implement / operate a set of Functions or Components
  Enterprise Ontology Notes
  Assets: Devices, system components, applications, infrastructure components
  Resource: Anything available to a system that can support the achievement of objectives; any physical or virtual element that may be of limited availability within a system. In the Enterprise Viewpoint a resource is an entity that has some role, offers services, and performs some action within a system.
  Ref: TOGAF, NIST 800-207
  An enterprise capability denotes the “What” an enterprise can do, whereas an enterprise process outlines “how” a particular activity gets done.
  An enterprise process is defined as a set of activities and tasks that, once completed, will accomplish an organizational goal.
* An “Application” is a set of functions deployed (somehow) on a server as part of a system
Enterprise Concerns:
  Objectives
  Roles
  Requirements
  Policies
  Risk Management
  Lifecycle / Phases
  Configuration
  Contracts

## Slide 22: Formalized Relationships among Terms (Enterprise Viewpoint ontology)
Capabilities
Superior
Enterprise
Enterprise
(Organization)
Perform ..
Provides: Mission, Scope, Requirements, Governance, Resources …
Operations
Consumes / Expends ..
Resources
Possess set of 1..*
Composed of …
Create ..
Products
System Elements
Data
Artifact
Services
Any of 1..
Domain
Controls / Operates in 1..*
Persons
Requirements
Assets
Values…
Specifies…
Constrain …
Produce ..
Fig 4-2

## Slide 23: RASDS Enterprise View Representation
DATA
Logical Link: Node to Node interface
Domain Boundary
(optional)
Organization Object
(Org, Project, Business)
Denotes a specific Organization (org, project, business), may have embedded components
Denotes a function an organization carries out (optional, see Functional Viewpoint)
Denotes a Logical Link (information flow of some sort) between two Organizations
Denotes an information object (optional, allows data to be characterized, see Information Viewpoint)
Denotes an organization / domain boundary (ownership / responsibility)
Specific and Generic Object Types and Containment:
Organizations (Agency, Project, Business) will explicitly connect via a Logical Link. May show the organization domain of control or ownership, or containment (sub-org).
May show allocation of Functions that an organization carries out (tied by correspondence to the Functional View where they are defined).
May explicitly identify the information objects (such as contracts, requirements, agreements) exchanged between organizations (tied by correspondence to the Information View where they are defined).
Org A
Org B
Function A
Function B
Sub-Org B1
DATA
Information Object
(optional)
Include Use Case in Enterprise view tie to Services view
Fig 4-3
Notes: ASL Fig 3-4, trim headers & footers

## Slide 24: Simple Enterprise View Single Agency Mission Domain & Enterprise Objects Operations Planning Phase
Agency A
Mission &
Support
Organizations
Mission A
Instrument
Control
Team C
Mission A
Spacecraft
Control Team
Agency B
Ground
Tracking Network
Agency A
Operations
Domain
Instrument
Support
Agreement
Long range
Tracking Plan
Tracking
Configurations
Comm Link
Modes
Mission A
Spacecraft
Instrument
C
Fig 4-4

## Slide 25
Enterprise View - Mars Exploration Program Example
MSL Proj
MRO Ops
MMO
Svc Org Z
DSN
MRO Proj
NASA/
JPL
S/C Contractor
MEx Proj
Prog S
ExoMars Prog
ESA
Operations
Agreements
Cross- Support
Agreements
Instr Org S
Instrument
Integration
Agreement
Science
PI Org
Tracking
Agreements
ICDs
Mars Exploration
Program Federation
Fig 4-5

## Slide 26: Enterprise View Multi-Agency Mission Domain & Enterprise Objects Launch Operations Phase
Agency ABC
Instrument
Control Team
Mission Z
Spacecraft Control
Team
Agency ABC
Ground Tracking
Network Ops
Agency ABC
Operations
Domain
Instrument
Observation
Request
Comm Link Configs
Tracking Requests
Mission Z
Spacecraft
Agency ABC
Space Relay
Network Ops
Instrument
ABC
Agency ABC
Science Team
Agency QRS
Science Team
Agency QRS
Flight
Operations
Domain
Mission Z Operations Domain
Science Planning
Coordination
Agency WXY
Launch Facility
Agency WXY
Launch Tracking
Network
Agency WXY
Operations
Domain
Instrument
Observation
Request
Agency WXY
Launch Vehicle
Post-Launch Flight Telemetry
Spacecraft Mode and State Change
Pre-Launch Vehicle Health
Mission Z
Spacecraft (stowed configuration)
Fig 4-6

## Slide 27: Enterprise Behavior Modelling Ontology - Formalized Relationships (Enterprise Capability / Process ontology, from TOGAF)
Enterprise Process
Capability
Persons
Performed
by
Enterprise
Possess set of 1..
Implemented by 1..
Uses …
Application
Information
Services …
Uses
Department
Member
of
Enterprise
Service
Data Artifact
Uses …
Accesses
Organizational Goal
Accomplishes
Application
Helps Provide …
Fig 4-7

## Slide 28: “Enterprise Architecture” Definitions
Enterprise Capability
  An expression of what an enterprise does and can do. An enterprise capability denotes the “What” an enterprise can do and has responsibility for, whereas an enterprise process outlines how a particular activity gets performed by enterprise systems.
  At an elemental level, an enterprise capability is the encapsulation of the underlying functionality expressed abstractly, in general and high-level terms, requiring a combination of organization, Persons, processes, and technology to achieve.
Asset
  An item of value to stakeholders. An asset may be tangible (e.g., a physical item such as hardware, firmware, computing platform, network device, or other technology component) or intangible (e.g., humans, data, information, software, capability, function, service, trademark, copyright, patent, intellectual property, image, or reputation). NIST 800-160

## Slide 29: “Enterprise Architecture” Definitions, contd
Enterprise Process
  An enterprise process is defined as a set of activities and tasks that, once completed, will accomplish an organizational goal.
Activity
  Work, not specific to a single organization, operational system or individual that transforms inputs (Resources) into outputs (Resources) or changes their state. (DoDAF, edited)
Actor
  An actor specifies a role played by a user or any other system that interacts with the subject. It may represent roles played by human users, software, external hardware, or other subjects. (UML)
Application
  An application (app), application program or application software is a computer program designed to help Persons perform an activity (Wikipedia)
Data
  The representation forms of information that may be stored and/or exchanged by systems and users thereof. (Information)
  Not completely clear what a “data artifact” might be. In some contexts it is defined like this:
    A data artifact is a data flaw caused by equipment, techniques or conditions. Common sources of data flaws include hardware or software errors, conditions such as electromagnetic interference and flawed designs such as an algorithm prone to miscalculations.

## Slide 30: Formalized Relationships between Enterprise & Technical Architecture (Recolored for the Viewpoint the objects are defined in)
System
Hardware
Software
Persons
Procedures
Composed of 1..
Environment
Affects
Function
Implement 1..
Function offers 0.. Service Interfaces
Process
Action
Task
Business Process
Capability
Persons
Performed
by
Business
Possess set of 1..
Implemented by 1..
Uses …
Application
Business
Information
Services …
Uses
Department
Member
of
(Business) Service
Application
Data Artifact
Uses …
Accesses
“Logical” Enterprise System Boundary
Process is an ordered set of Functions
The “Enterprise Architecture”, in actuality, is implemented by the Technical Architecture
The “Technical Architecture” implements the systems, services, and processes.
Supports the Enterprise
(System)
Service
Implemented by …
Fig 4-8
Technical System Boundary

## Slide 31: Formalized Relationships among Terms (System Viewpoint aspects, related to Capability)
System**
System
Element
Hardware
Software
Persons
Procedures
Function
Has 1..
Composed of 1..
Implements 1..
Environment
Affects
Offers 0..
Service
Technical Process
Action
Task
** A “System” may be de-composed into System Elements.
  System: A collection of interacting components organized to accomplish a specific function or set of functions.
  A System is composed of Elements, which may be any of: Hardware, Software, Person, and Procedures.
Capability
Provides 1…
Offers 1..
(Transitive)
Remove, but include back reference to Connectivity VP with combo VP slide

## Slide 32
Formalized Relationships between Enterprise & Technical Architecture (Recolored for the Viewpoint the objects are defined in)
(Notes)
* An “Application” is Software, a set of functions deployed (somehow) on a hardware platform or a server as part of a system, with defined interfaces
  The Enterprise Architecture defines processes, services, and applications, all of which are implemented by the Technical Architecture, but without directly addressing the technical details or relationships among functions, HW, SW, and Persons that are defined in the Technical Architecture.
** The technical aspects of the “Enterprise System” may not be defined as part of the Enterprise Architecture. It may stop at the Service, Application, and Data level.

## Slide 33: Functional Viewpoint
The Functional Viewpoint describes the functional decomposition of the space data system into abstract objects that interact at interfaces.
Stakeholder Concerns:
  a functional decomposition of the system into objects that interact at interfaces;
  the abstract behavior of the system, its interactions and constraints.
Functional Objects (abstract set of functions, their behaviors, interfaces and configurations);
  Types: data source, data sink, data transformation, control, planning, monitoring, analysis;
  Attributes: role, name, type, behavior, interface types, data types handled, interaction modes, constraints, allocated requirements;
Logical Links (connections between Functional Objects, connected to associated logical behavior and properties);
Relationships (configuration, precedence, control and data flows, management flows, allocations);
Information (representations of data that are exchanged among Functional Objects, where formal specifications for the information objects are found (by correspondence) in the Information Viewpoint).

## Slide 34
Functional Object
Functional Viewpoint
(Abstract Functional Object Features)
Attributes
Identifier
Type
Behavior
Data
External Interfaces:
How other Functional Objects are used to support the performance of this Object
Management Interfaces:
How functions are configured,
controlled, and monitored
Service Interfaces:
How services are
requested by & supplied
to other Functional Objects
Concerns:
Performance constraints
Resource requirements
Constraints
Fig 5-1, w/ mods

## Slide 35: Formalized Relationships among Terms (Functional Viewpoint ontology)
Behavior
System
Element
Function
Produces /
Consumes ..
Implemented by 1.. (corr)
Data
Offers 0..
Service
Has …
Composed of …
Requirement
Fulfilled by 1.. (corr)
Specified by .. (corr)
Function : The set of actions or activities performed by some object to achieve a goal; the transformation of inputs to outputs that may include the creation, modification, monitoring, or destruction of elements.
Behavior: A set of actions performed by an object for some purpose.
Protocol
Stack
Uses to communicate
Implemented by 1.. (corr)
Implements
Fig 5-2

## Slide 36: Extended RASDS Functional View Representation*
Function A
DATA
Logical Link: end-to-end interface between functions
Service Provider
(provided I/F, optional)
Service Consumer
(required I/F, optional arrowhead)
Data Object
(optional)
* Revisions from ASL, dropped Standardization Status
Functional Objects are abstract representations of behavior. They may be instantiated or realized in different logical or physical constructs.
Functions may themselves be decomposed into lower level functions, shown by containment.
Different deployments or realizations of the same Functional Object may be expressed in other views and referenced by correspondence.
Functional Objects may explicitly define a service providing interface, but this is not required.
They may explicitly identify the information objects that are exchanged (tied by correspondence to the Information View where they are defined).
Sub-Function B1
Function B
Fig 5-3, with mods
Denotes a defined function, may show containment (example shown)
Denotes a Logical Link between two Functions and flow direction (optional)
Information Object describing communicated data, which may be described in the Information Viewpoint and referenced by correspondence
Denotes a provided service interface (optional)
Specific and Generic Object Types and Containment:
DATA
Notes: ASL Fig 3-4, trim headers & footers

## Slide 37
Directive
Generation
Directive
Execution
Simple Alternative Functional VP
representation examples
Directive
Management
Directive
Generation
Directive
Execution
Directive
Management
SCEP
SCD
Data Object Key:
SCEP - S/C Event Plans
SCD - S/C Directives
SCC - S/C Commands
SCD
SCC
Two different simple Functional Object views, one just showing data flow directions, the other explicitly showing provided interfaces and data objects.
Data flow directions
Provided interfaces and data objects
Fig 5-4

## Slide 38: Simplified functional VP example
Mission
Planning
Mission
Analysis
Spacecraft
Analysis
Monitor &
Control
Directive
Generation
Data
Acquisition
Orbit
Determ
Tracking
Radiometric
Data Collect
LT Data
Repository
Data
Repository
Directive
Execution
Directive
Management
Insert as new Fig 5-5???
See revised fig 5-6 …

## Slide 39: Example: MO top-level Functional Decomposition, Data and Services (from ASL)
Navigation & Timing
Planning & Scheduling
Mission Control
Data Storage and Archiving
Operations Preparation
User Support
TT&C
Spacecraft Development & Maintenance
NAVT
MPS
NAVT
NAVT
MCS
MCS
MCS
OPD
MCS
OPD
MPS
MPS
NAVT
NAVT
MPS
MCS
NAVT
MDP
Functions and Data Colour Coded: Data in Rectangles; Services indicated at Provider End by Circle MDP = Mission Data Product
MCS
MCS
OPD
Mission Data Processing
MCS
MPS
NAVT
MDP
MDP
NAVT
NAVT
MCS
MPS
SLE-Ret
TRM
OPD
CSSM-ES
SC-CSTS
MD-CSTS
CSSM
TD-CSTS
Fig 5-5
Notes: ASL Figure 4-2, trim top & bottom
The 5 MOIMS Areas are colour coded.
Each application level interaction is annotated with the Data exchanged. At this level all Data generated by each Function is grouped as a single type (the abbreviation reflects the function name).
Potential service interfaces identified by MO are indicated by a colour-coded circle representing the Service Provider
Data formats may be separately defined [NAV, MPS] or specified in the context of the service [MO M&C, MPS].
File Handling is a bit different – there are special services for File Management and File Transfer [the latter delegated to a lower level protocol, such as CFDP or FTP], but the file content my be associated with any of the other Functional Areas. It essentially provides the transport layer for bulk transfer of service messages or data formats. Mission Data Products may also be transferred as files.
Note Planning/Scheduling interactions with the GSTS are greyed out as they are outside the scope of MOIMS standardisation [CSS boundary agreement].

## Slide 40: Functional Objects and Information Management Infrastructure Elements redrawn 8 Feb 24
Fig 5-6
Mission
Planning
Monitor &
Control
Directive
Generation
Data
Acquisition
Information
Management
Directive
Execution
Directive
Management
Repository
Service
Product
Service
Registry
Service
Query
Service
Common Schema & Dictionaries
Domain Data Models
Local Data Models
Information Management Functional Objects
Representative Functional Objects
Data Objects
Query / Results
Metadata / Resources
Service
Interfaces

## Slide 41: Physical Viewpoint - New
The Physical Viewpoint describes the engineered decomposition of the space system into physical Components (Nodes) that connect physically or energetically to other Components. The Physical Viewpoint describes the physical aspects of the space system and the external environment within which it operates, the physical connections and behavior (fixity or motion) of the Components, and their physical composition.
Stakeholder Concerns:
  The physical Components that compose the system;
  The physical connections among the physical elements in the system and the structural or energetic flows and junctions required to support these connections among objects in the system;
  The characterization of these different physical aspects in their own views, with tailored language for connection modalities: mechanical, electrical, thermal, electro-magnetic, gravitational, propulsive, ..;
  The selected allocation of physical functions to the Components of the system, including their implementation choices and constraints on implementation, connections, configuration, and features imposed by the nature of the physical connections and the environment;
  The behavior and performance of elements in the system, including their capabilities, fixity or physical motion, and their interactions with the physical environment.
  The impacts and constraints on connections, energy flows, motion, ….

## Slide 42: Physical / Structural Viewpoint - New, contd
Engineering Objects (Components, Connectors, Applications):
  Nodes (hardware Engineering Objects, provide mechanical, power, thermal and other structural or physical resources, connection points, performance and other associated physical behavior):
    Types: hardware objects, composite hardware objects;
    Attributes: name, type, mass/power/orientation, location (place, trajectory, orbit), laws of motion, physical interfaces, capabilities (e.g., attachment type, fixity / motion, connection properties, etc.), allocated functions, constraints;
  Connections between Components (associated physical flows, behaviors, and properties);
    Types: connectors / weldments / mating surfaces, joints, waveguides, heat pipes, cables, free-space radiation, …
    Attributes: name, type, end-points (connected nodes), physical interfaces, performance (e.g., capacity, flows, range of motion), constraints, environmental effects, etc.);
Relationships (composition, interfaces/connections, constraints, configurations, allocation);
  Environment (physical environs, physical forces [gravity, electromagnetic, radiation, and others], physical interactions and effects);
  Flows (defined representations of energetic flows that are exchanged among Engineering Objects, where formal descriptions of flows are found in the Information Viewpoint).
NOTE – Physical Components and Connectors in any given space system may include many more aspects and many more attributes than those shown here. The Data Communications aspects of Components (Nodes) and Connectors (Links) are covered in the Connectivity Viewpoint.

## Slide 43
Physical Base Viewpoint - Physical Object
(Hardware Component Representation)
Attributes:
Name/identifier
Composition (engineering objects)
Physical environment
Extensions
Physical Attributes (mass, power, moment of inertia, thermal, Distribution / frame of reference)
Connection types (flows, energetic, structural,…)
Constraints
External Interfaces:
Physical Connections
to other Components
Management Interfaces:
How Components are configured,
controlled, and reported upon
Service Interfaces:
Physical Connections
from other Components
Physical Component
Physical Environment
Laws of Motion
Other energetic inputs, gravity, Solar, radiation,…
Fig 6-1

## Slide 44: Relationships among Terms (Physical Viewpoint ontology - redrawn)
Attachment
(Interface)
System
Element
Component
Implements 1..
Is a …
Function
Offers 0..
Service
Has Provided / Required 1…
Hardware
Software
Person
Composed of 1..
Environment
Affects
Connector
Connect via 1…
Composed of …
Location / Motion
Has
Flow
Provides / Conveys
Fig 6-2
Interface Standard
Defines

## Slide 45: RASDS Physical View Representation
Flow
Physical Connection: Component to Component connection
Service Provider
(provider, optional)
Service Consumer
(consumer, optional)
Physical Connection
Related to the Connectivity Viewpoint, but focus here is on physical characterization, connections and energetic flow, not data.
Nodes (Components) will explicitly connect via some Physical Link. Nodes will have mass, power, thermal, and other properties. A Node may explicitly define a physical interface, but this is not required.
Physical connection (represents energetic constraint). This may be dynamic or static, structural / rigid, flexible, or other energetic (electro-magnetic, thrust, gravitational, thermal radiation).
May show allocation of implemented Functions, in hardware (a sub-node) tied by correspondence to the Functional View where they are defined.
May explicitly identify the flows exchanged by the objects using the link (defined in these views).
May explicitly identify the physical interface or connection type.
Component A
Component B
Function A
Function B
Sub-Component B1
Connection
Flow (data or other)
(0..n, optional)
Physical I/Fs
(compatibility, optional)
Fig 6-3, with mods
Denotes a specific Node (physical component), may have embedded components
Denotes an implementation of a defined function, may be software or hardware (optional and referenced by correspondence, see Functional Viewpoint)
Denotes a Physical Link (Connection of some sort) between two Nodes
Denotes a Physical Interface (optional, allows interface type to be characterized)
Information Object describing flow or connection, which may be fully defined in the Information Viewpoint and referenced by correspondence
Specific and Generic Object Types and Containment:
FLOW
Notes: ASL Fig 3-4, trim headers & footers

## Slide 46: Figure 6-4 Recreated original
Servicing Spacecraft
Conduit
Fluid Storage & Delivery
Spacecraft
Fluid Pump
Fluid Tanks
Fluid Flow
Fig 6-4

## Slide 47
Science
Instrument
S/C
Transceiver
Attitude
Control
Computer
Command &
Data Handling
Computer
Science Spacecraft
Simple Physical View Example
Components & Connectors
RF Antenna
Physical elements
- Mass
- Position
- Center of Gravity
Fig 6-5

## Slide 48: Connectivity Viewpoint
The Connectivity Viewpoint describes the engineered decomposition of a space data system into components (nodes) that exchange data across connectors (links). The Connectivity Viewpoint describes the physical aspects of space data systems communications and the external environment within which they operate, the physical behavior (and motion) of the nodes, and their physical decomposition into communicating elements.
Stakeholder Concerns:
  The mechanisms and functions required to support distributed communications between objects in the system;
  The selected allocation of functions to the nodes of the system, including their implementation choices and constraints on implementation, connections, configuration, and operations imposed by the communication links and the environment;
  The behavior and performance of elements in the system, including their communications capabilities, physical motion, and their interactions with the physical environment.
Engineering Objects (Nodes, Links, Applications):
  Nodes (hardware Engineering Objects, provide communications, processing and other computing and data resources, ports, performance and other associated physical behavior):
    Types: hardware objects, composite hardware objects, ports;
    Attributes: name, type, location (place, trajectory, orbit), laws of motion, available resources, physical interfaces, capabilities (e.g., processor speed, throughput, bandwidth, storage capacity, aperture size, etc.), allocated functions, constraints;

## Slide 49: Connectivity Viewpoint, contd
Engineering Objects (Nodes, Links, Applications), contd:
  Links (communications connections between Nodes, associated physical behavior and properties);
    Types: space link (RF or optical), physical link (e.g., point-to-point, bus, network, copper, fiber, etc.);
    Attributes: name, type, end-points (port on node), physical interfaces, performance (e.g., throughput, bandwidth, frequency band, Round Trip Light Time (RTLT), pointing and view periods, signal attenuation, constraints, environmental effects, etc.), access and ownership;
  Applications (software Engineering Objects, behavior, and processing/resource requirements, may be layered):
    Types: software Engineering Objects, composite software Engineering Objects;
    Attributes: name, type, algorithms, implemented functions, allocation/ deployment to nodes, required resources (e.g., memory, CPU, storage), implemented interfaces (provided and required), implementation language, Operating System (OS)/framework dependencies, constraints;
Relationships (composition, interfaces, constraints, configurations, allocation);
  Environment (physical environs, physical forces [gravity and others], physical interactions and effects);
  Information correspondences (defined representations of data that are exchanged among Engineering Objects, where formal specifications of data architecture are found in the Information Viewpoint).
NOTE – Physical Nodes and Links in any given space system may include many more aspects (physical structures, connections, and flows), types (power, propulsion, thermal) and many more attributes than those shown here. The physical, structural, and energetic flow aspects of Nodes and Links are covered in the new Physical / Structural Viewpoint.

## Slide 50
Connectivity Viewpoint - Physical Object
(Node / Component Features)
Attributes:
Name/identifier
Address
Composition (engineering objects)
Performance
Distribution / frame of reference
Sub-nodes
Communication links and Ports
Physical environment
Configuration
Constraints
External Interfaces:
Communication links to other Nodes
Management Interfaces:
How Nodes are configured,
controlled, and monitored
Service Interfaces:
Communication links from other Nodes
Node
(Component)
Physical Environment
Laws of Motion
Communications Geometry
Fig 7-1

## Slide 51
Connectivity Viewpoint - Physical Object
(Node / Component Features)
Notes
Node/Component Notes:
Interfaces of Components may be described by an EDS.
Specific Components may implement a set of Functions.
  Connectivity Viewpoint Aspect notes
  Node: A model of a space data system physical entity operating in a physical environment. A Node is a configuration of Engineering Objects forming a single unit for the purpose of location in space, and embodying a set of processing, storage and communication functions.
  Link: A Link provides interconnections between Nodes for communication and coordination. A Link may be implemented by a wired connection or with some RF or optical communications media.

## Slide 52: Formalized Relationships among Terms (Connectivity Viewpoint Ontology)
Port
(Interface)
System
Element
Node
(Component)
Implements 1..
Is a …
Function
Offers 0..
Service
Has 1…
Hardware
Software
Persons
Composed of 1..
Environment
Affects
Link
(Connector)
Connect via 1…
Composed of / Aggregation of …
Location / Motion
Has
Protocol
(Stack)
Offers 0..
Fig 7-2
ICD
References 1..
Defines
Documents …

## Slide 53: Relationships among Terms (Connectivity Viewpoint ontology - redrawn)
Communication Protocol
System
Element
Node
Implements 1..
Is a …
Function
Offers 0..
Service
Has Provided / Required 1…
Hardware
Software
Person
Composed of 1..
Environment
Affects
Link
Connect via 1…
Composed of …
Location / Motion
Has
Flow
Provides / Conveys

## Slide 54: RASDS Connectivity View Representation
DATA
Physical Link: Node to Node connection
Service Provider I/F
(provided I/F, optional)
Service Consumer I/F
(required I/F, optional)
Information Object
(optional)
Denotes a specific Node (physical component), may have embedded components
Denotes an implementation of a defined function, may be software or hardware (optional, see Functional Viewpoint)
Denotes a Physical Link (Connector of some sort) between two Nodes
Denotes a physical interface (optional, allows interface type to be characterized)
Information Object describing communicated data, which may be defined in the Information Viewpoint and referenced by correspondence
Denotes a protocol layer at an interface (not shown here, optional overlay, allows interface binding to be characterized by correspondence, see Communications Viewpoint)
Specific and Generic Object Types and Containment:
Related to the Physical Viewpoint, but focus is on data connections not physical connections or energetic flows.
Nodes (Components) will explicitly connect via some Physical Link. This may be free space (RF or optical) or it may be a hardware connection of some sort (cable, twisted pair, fiber optic).
A Node may explicitly define a physical interface, but this is not required. Nodes may have a provider/consumer relationship or they may be peers.
May show allocation of implemented Functions, in hardware (as a sub-node) or in software. These are tied by correspondence to the Functional View where they are defined.
May explicitly identify the information objects exchanged over the link (tied by correspondence to the Information View where they are defined).
May explicitly identify the protocol stack at an interface (tied by correspondence to the Communications View where they are defined).
Node A
Node B
Function A
Function B
Sub-Node B1
Function Deployment
(optional)
Fig 7-3, with mods
DATA
Notes: ASL Fig 3-4, trim headers & footers

## Slide 55
Simple Connectivity View Example
Nodes & Links
Science Spacecraft
Tracking
Station
Spacecraft
Control Center
Science
Institute
Fig 7-4

## Slide 56
Connectivity View w/ Node Details
Nodes & Links
Science
Instrument
S/C
Transceiver
Attitude
Control
Computer
Command &
Data Handling
Computer
Tracking
Computer
Predict
Generation
Computer
RF & Ant
Systems
Mission
Planning
Computer
Science
Processing
Data
Management
Computer
Spacecraft
Control
Computer
Monitor &
Control
Computer
Flight
Dynamics
Computer
Science Spacecraft
Tracking Station
Spacecraft Control Center
Science
Institute
Fig 7-5

## Slide 57: ASL Connectivity View: Simple ABA Mission example showing application layer function deployment to Nodes
Science Spacecraft
Tracking Station
Spacecraft Control Center
Science Institute
Spacecraft Development & Maintenance
TT&C
Planning & Scheduling
Navigation & Timing
Mission
Control
Data Storage & Archiving
Operations
Preparation
Plan Execution
Time/Pos Det
M&C Automation OBCM
OB File Store
CSSM
TRM
TDM
MD-CSTS
ODM
TRP
TDM
PEC
PLN
AUT
OBPM
OBSM
MDP
MPS
SDB
APD
OBSW
FTM
MDP
XTCE
M&C
MCS
NAVT
SLE-Ret
MCS
NAVT
TD-CSTS
SC-CSTS
Fig 7-6
Notes: ASL Fig 9-2, trim headers & footers
ABA: Spacecraft, ESLT, MOC and SMC (ignore NOC) On-board Functions: Basic M&C; On-board Procedures; On-board Scheduler Tracking done by Dedicated ESLT S/C DB, OBSW and OBCPs from S/C Manufacturer, also supporting performance monitoring and fault diagnosis All other functions in MOC

## Slide 58: Functional View Example for Image Compression (section 6)
Compression
Function
Image Data
Compressed Data
Data Management
Function
Stored Compressed Data
Fig 7-7
Data
Source

## Slide 59: Connectivity View Example for Software Image Compression (section 6)
Flight Data Recorder
Subnetwork
C&DH Processor
Compression
Software
Compressed Data
Data Management
Software
Data Repository
Compressed Data
Fig 7-8a
Data
Source
Image Data

## Slide 60: Connectivity View Example for Hardware Image Compression (section 6)
Flight Data Recorder
Subnetwork
C&DH Processor
Data Management
Software
Data Repository
Compressed Data
Image Data
Compression Hardware
Fig 7-8b
Data
Source

## Slide 61: Is this exactly the same as Physical VP, fig 6-1???
Fig 8-
Structural Base Viewpoint - Physical Object
(Hardware Component Representation)

## Slide 62: Relationships among Terms (Structural Viewpoint ontology - redrawn)
Attachment
(Interface)
System
Element
Structural Component
Implements 1..
Is a …
Function
Offers 0..
Service
Has Provided / Required 1…
Hardware
Software
Person
Composed of 1..
Environment
Affects
Structural Connector
Connect via 1…
Composed of …
Location / Motion
Has
Flow of Heat , Torque, Vibration, etc.
Provides / Conveys
Fig 8-1
ICD
References 1..
Interface Standard
Documents …
Defines

## Slide 63: RASDS Physical (Structural) View Representation
Flow
Physical Link: Node to Node connection
Service Provider
(provider, optional)
Service Consumer
(consumer, optional)
Physical Connection
Related to the Connectivity Viewpoint, but focus here is on physical characterization, connections and energetic flow, not data.
Nodes (Components) will explicitly connect via some Physical Link. Nodes will have mass, power, thermal, and other properties. A Node may explicitly define a physical interface, but this is not required.
Physical connection (represents energetic constraint). This may be dynamic or static, structural / rigid, flexible, or other energetic (electro-magnetic, thrust, gravitational, thermal radiation).
May show allocation of implemented Functions, in hardware (a sub-node) tied by correspondence to the Functional View where they are defined.
May explicitly identify the flows exchanged by the objects using the link (defined in these views).
May explicitly identify the physical interface or connection type.
Node A
Node B
Function A
Function B
Sub-Node B1
Connection
Energy Flow
(0..n, optional)
Physical I/Fs
(compatibility, optional)
Fig 8-2, with mods
Denotes a specific Node (physical component), may have embedded components
Denotes an implementation of a defined function, may be software or hardware (optional and referenced by correspondence, see Functional Viewpoint)
Denotes a Physical Link (Connection of some sort) between two Nodes
Denotes a Physical Interface (optional, allows interface type to be characterized)
Information Object describing flow or connection, which may be fully defined in the Information Viewpoint and referenced by correspondence
Specific and Generic Object Types and Containment:
FLOW
Notes: ASL Fig 3-4, trim headers & footers

## Slide 64
Physical Base Viewpoint - Physical Object
(Hardware Component Representation)
(Notes)
Physical Object Notes:
Different Connection types will be treated as different aspects of the Nodes.
They may require different descriptors and attributes for the different flows and Connections.
Physical Object Ontology Notes
Component (Node): A model of a space data system physical entity operating in a physical environment. A Node is a configuration of Engineering Objects forming a single unit for the purpose of location in space, and embodying a set of processing, storage and communication functions.
Interface: A set of interactions performed by an object for participation with another object for some purpose, along with constraints on how they can occur. An interface is therefore where the behavior of an object is exposed.

## Slide 65
Heat
Mounting Pattern
Hinge
Location and Orientation
Articulation
Hinge Base
Radiator
Heat
Hinge Mount
Heat Radiation
Controller
Angle Command
Structural View – Hinge Assembly
Fig 8-3

## Slide 66
Physical Viewpoint - Component / Connector Derived VP Examples
Structural
  Components (S/C bus, physical link, arm/articulation, structural attributes of other components)
  Connectors (joint, bolt (incl explosive), weld)
Power
  Components (solar panel, battery, RTG, switches, power attributes of other components)
  Connectors (power bus, rotational power connectors)
Thermal
  Components (cooler, heater, thermal attributes of other components)
  Connectors (heat pipe, duct, free space radiation)
Propulsion
  Components (motor, wheel, thruster, gyro)
  Connectors (contact patch, gravity, radiation pressure)
Notes: 66

## Slide 67: RASDS Simple Structural View Simple Example
This diagram represents connection for on-orbit servicing using structural conduit and fluid flow information to “client”.
OOS Servicing Spacecraft
OOS Client
Spacecraft
Fluid Flow
Flexible Conduit described in spacecraft manifest
Fluid Tanks
Fluid Storage & Delivery
Fluid Pump
Dynamics of Fluid Flow between elements
Physical interface of Conduit to spacecraft
Physical Link: Servicing Spacecraft to “Client” connection
Conduit
Fig 8-4

## Slide 68: Physical - Derived Structural View
Command &
Data Handling
Computer
ACS
Computer
S/C Bus
SPACECRAFT
Spacecraft
Transceiver
Science
Instrument
Power
Subsystem
Articulated
RF Antenna
Fig 8-5

## Slide 69
Science
Instrument
S/C
Transceiver
Attitude
Control
Computer
Command &
Data Handling
Computer
Tracking
Computer
Predict
Generation
Computer
RF & Ant
Systems
Mission
Planning
Computer
Science
Processing
Data
Management
Computer
Spacecraft
Control
Computer
Monitor &
Control
Computer
Flight
Dynamics
Computer
Science Spacecraft
Tracking Station
Spacecraft Control Center
Science
Institute
Connectivity View Example
Nodes & Links _ rework
Thermal VP and ??? Fred

## Slide 70: Physical Viewpoint: Some Aspects
Concern | Aspect | Service
DeltaV | Propulsion | Linear Thrust
Temperature Range | Thermal | Heat Flow
Agility, Pointing Accuracy, Mass Expulsion Control Capacity | Attitude Control | Torque
Power Storage Capacity, Voltage Range, Power Consumption | Electrical | Amperage Supply, Electrical Load
Device Orientation, Device Articulation, Keep Out Zone, Field of View | Structural | Mounting, Articulation Control

## Slide 71: Comments on Physical View (and deriving other Views)
Structural / Mechanical View can be directly derived from Physical View
  Same sets of Components, different Connector types, different flows (energetic), different attributes
  The same representation may be used (for crude mechanical drawings)
  The Mechanical Engineering world has its own preferred representations and specialized analyses
Thermal & Power views may also be similarly modeled using PPT diagrams
  Nodes are the same, but different attributes are relevant
  Value of these specific representations, except as a way to relate the different views seems questionable
Physical / Propulsion, Magnetic, Gravitational and other views also require different views of these energetic processes

## Slide 72: Proposal for Physical View (and deriving Connectivity View)
Architecture diagrams that relate Connectivity view objects, essential for communications & protocols, can only weakly support engineering and other detailed Physical views
  Recommend using a common set of simplified 3-D architecture diagrams, where useful, to tie these viewpoints together logically
  Expect to use engineering domain specific representations that are able to support detailed analyses
    Identify that there are some engineering disciplines that are now coupling various physical aspects, such as thermal and electrical flow from spot welding, or finite element analysis that connects structural, thermal, and other flows.
  Recommend using a single, common, underlying information model, with suitable attribute sets, to model these elements and tie these different aspects together
    Use RASDS Information VP approach, with semi-formal ontologies

## Slide 73: Communications Viewpoint
The Communications Viewpoint focuses on the mechanisms and functions required to engineer and implement the protocols and communications standards for the space data system, including implementation choices and specifications, and relationships among elements in different protocol layers.
Stakeholder Concerns:
  the choice of communications and data transfer standards in the system;
  the end-to-end communications protocol functionality and reliability;
  implementation of the protocol specifications and the services they provide;
  the relevant protocol stacks, interface bindings, and interactions;
  interaction of protocol design with environmental constraints;
  support for design, evaluation of suitability, and integration into the rest of the system.
Protocol Entities (elements that implement specific protocols, protocol stacks, with Service Access Point (SAP) and peer interactions optionally shown):
  Types: protocol purpose (e.g., coding, modulation, link, network, transport, middleware, application service);
  Attributes: name, type, capabilities (e.g., in order, once only, bandwidth efficient, error correcting, delay tolerant), applicability (e.g., deep space, near Earth, in situ), constraints, services (offered, required), service access point (requests, indications, responses, confirmations), API (where appropriate), standard reference identifier, standards organization;
Protocol design specification elements (PDU description), behavior (state machine or table description), reliability (acknowledged, unacknowledged, selectively acknowledged), other design views of the communications protocol or protocol stack;
Correspondences to Nodes and Links (representations of physical elements from the Connectivity Viewpoint, for context);
Correspondences to Software Engineering Objects (representations of implemented functions from the Connectivity Viewpoint, for context).

## Slide 74
Core Functions
Peer behaviors
PDUs
Signaling
Required Interface (SAP):
How protocol services are requested from & supplied to this layer by lower layers (Layer N-1 SDU)
Management Interfaces
(may be represented by a MIB):
How protocol is configured
controlled, and monitored
Provided interface (service access point):
How protocol services are requested of & supplied by this layer (SAP, Layer N SDU)
Attributes:
Standards
Functionality
Technology
Applicability
Protocol Entity
Communications Viewpoint
(Protocol Entity Representation)
Fig 9-1, with mods

## Slide 75
Communications Viewpoint
(Protocol Entity Representation)
Notes
Protocol Entity Note
Each protocol entity represents a standard
Protocol Entities are usually shown in a stack
Protocol stack at an interface may be described by an EDS
  Protocol Viewpoint ontology note
  Protocol: A set of rules and formats (semantic and syntactic) used to determine the communication behavior of (N-layer)-protocol-entities in the performance of (N-layer)- functions; the description of the state machines within a Protocol Entity and the PDUs that are exchanged between these entities.

## Slide 76: Formalized Relationships among Terms (Protocol Viewpoint ontology)
Provided/required
Service
Interfaces
Protocol
Formalizes PDUs …
Protocol Data Units
Specifies 1..
Protocol
Behavior
Provides /
requires 1…
Service Data Units
Formalizes
SDUs …
Standard
Provides Normative
Specification
Protocol
Stack
Participates in …
Interface
Binding
Specifies (corr)
Fig 9-2
Port
(Interface)
Defines (corr)
25 Nov 2024
Fig 9-2

## Slide 77: RASDS Protocol View Representation
Protocol Layer N peer
Protocol Layer N
Protocol PDUs
(logical flow)
PDUs may be simplex or bi-directional
Protocol behavior (may be described by state machine or other)
Protocol Layer N-1
Service Provided Interface (N SAP, optional)
Service Required Interface (of N-1 SAP, optional)
physical layer flow
Protocol Layer N-1 peer
Flow direction arrows (optional)
Protocol SDUs
(data flow)
Fig 9-3, with mods
Denotes a protocol layer (typically defined in a standard)
Denotes a Service Access Point (SAP, optional, may be defined in a standard)
Denotes the actual flow of wrapped PDUs (as Service Data Units) between two layers
Denotes a logical, peer to peer, protocol flow within a layer (Protocol Data Units)
Specific and Generic Object Types and Containment:
Protocol
Notes: ASL Fig 3-6, trim headers & footers

## Slide 78
Notes from Protocol Representation
Layer type and naming usually follows ISO / IEC 7498 Basic Reference Model (BRM).
PDUs get exchanged between peer entities at the same layer. Service Data Units (SDU) get exchanged between upper layer and lower layer protocol entities.
Each protocol must have defined behavior, PDUs, and required / provided interfaces. If there is an inter-layer interface mismatch a “shim” or adapter may be required, and this may be complicated enough to be treated as a separate protocol.
Behavior may be defined using a state machine, state table, or narrative form. Usually only defines behavior of sending side, but may define both ends.
May (optionally) formalize the SAP definitions and show Requests and Indications at the SAPs. SAPs, APIs, and implementations of protocols are language and deployment specific.
RASDS Protocol View Representation
(Notes)

## Slide 79: Simple Communications View example Basic ABA End-to-End Forward CLTU Protocols
From VC X
ABA Earth-Space
Link Terminal
ABA Earth User Node
ABA Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
VC X
To VC X
RF & Mod
IP
TCP
F-CLTU
F-CLTU
Production
Space TC SLP
Application
TC
RF & Mod
C & S
User TC SLP
Application
IP
TCP
F-CLTU
TC
C & S
C & S = Coding & Synchronization
Fig 9-4
Notes: 12/12/12: Updated Peter’s version so all lines were the same width, alignment within text boxes was center, general alignment adjustments. Added “C & S” definition to bottom.
79

## Slide 80: Simple E2E protocol diagram (… something more real, a simple ABA Return one)
ABA
ABA
ABA
Fig 9-5
To VC Z
ABA Earth-Space
Link Terminal
ABA Earth User Node
ABA Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
VC Z
From VC Z
RF & Mod
IP
TCP
R-CF
R-AF
Production
Space USLP
Application
USLP
RF & Mod
User USLP
Application
IP
TCP
R-CF
USLP
C & S = Coding & Synchronization
C & S
C & S

## Slide 81: CCSDS – “Full Stack” with Relay assets Forward, SSI Class 2 ESLT (no security shown)
Inter Satellite
Link
Terrestrial
WAN
Space Routing Node - B
SSI
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
SSI
RF & Mod
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
Bundle Agent (Router/S&F)
X-Band
ENCAP
BP
C & S
USLP
RF & Mod
To
VC X&Z
LTP
LTP
Xyz Phy
C & S
BP
Xyz Link
Space User Node
SSI
From
VC Z
Xyz Link
Xyz Phy
C & S
Space File Application
BP
CFDP
IP-based Network
Terrestrial
WAN
Space to Planet
Relay Link
SSI
To
VC X
User File Application
IP
BP
CFDP
TCP
Earth User Node
SSI
To
VC Z
User File Application
IP
TCP
BP
CFDP
Space Routing Node MOC
From
VC X
Space File Application
CFDP
Fig 9-6
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
81

## Slide 82: Simple E2E protocol diagram (Replace with something more real, or even two, a simple one (ABA) and a relay one???)

## Slide 83: Fig 9-7: SPP PDU diagram
Fig 9-7

## Slide 84: Fig 9-8 SLE Bind state chart
Fig 9-8

## Slide 85
SCCS example: SSI Secure End-to-End Forward Protocol Deployment - SSI Agency Supporting SSI Agency
Earth-Space
Link Terminal
Earth User Node
Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
SSI
SSI
SSI
VC X
CMD
VC X
USLP
RF & Mod
C & S
CFDP
ENCAP
Space Msg
Application
Space File Application
BP
AMS
LTP
RF & Mod
IP
C & S
F-Frame
Mux F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP/BPSec
LTP
USLP
BP/BPSec
To VC X
User File Application
IP
TCP
BP
User Msg
Application
CMD
CFDP
AMS
File Secure
BPSec
File Secure
BPSec
TCP
Fig 9-9
Notes: ASL Fig 9-16, trim headers & footers
12/12/12: New slide from Peter. Figure title in document is shown above. PPT original figure title is “SSI Secure Single Link Cross Support – Forward
(File, Frame & Message all DTN)
85

## Slide 86: Information Viewpoint
The Information Viewpoint focuses on the kinds of information handled by the system, the syntax and semantics of the information, and the interpretation of that information.
Stakeholder Concerns:
  the structure and semantics of information and information management in a system;
  the rules and constraints on information transformations and permanence in a system.
Information Objects (abstract definitions of information elements, structures, semantics, schema):
  Types: data, metadata, information, package, schema, model, meta-model;
  Attributes: name, type, length, structure, syntax, semantics, permanence, provenance, realized by, rules, policies;
Relationships (information object aggregates, transformations);
Constraints (type checking rules, permanence, policies).

## Slide 87
Information Object
Information Viewpoint
(Information Object Features)
Management Interfaces:
Rules (transformations, access)
Schema
Permanence
Element types
Constraints
Concerns:
Rules & Constraints
Resource requirements
Core Capabilities:
Type
Identifier
Structure
Semantics
Relationships
Fig 10-1, with mods

## Slide 88: Formalized Relationships among Terms (Information Viewpoint ontology)
Representation
Function
Information
Constrained by ..
Produces / Consumes (corr)
Rules
Realizes 0.. (corr)
Data
Artifact
Has …
Relationships …
  Information: Data, along with the necessary structure and syntax to allow interpretation and use of that data; may also have associated metadata, including the relationships among Data Objects, rules for their use and transformation, and policies on access.
Specifies
Fig 10-2

## Slide 89: Information Representation (ASL version) (Relationships derived from UML)
Information Class B
Information Class A
Relationship
0..1
*
Optional relationship type label
Optional multiplicity specifier
Relationship Types (UML derived): Read as sentence with subject = start of arrow, verb = label, and object = end of arrow
Information Objects are abstract representations of information and data structures. They may be referenced in many other views.
The explicit definitions of Information Objects in this Viewpoint are tied by correspondence to the Functional or other Views where they are referenced.
Information objects may themselves be decomposed into lower level objects, shown by containment or relationships.
Specific information object structures will typically be instantiated during design and realized in different forms during development.
Different instantiations or realizations of the same Information Object may occur in different deployments.
Fig 10-3, with mods
Inheritance
Composition
Aggregation
Association (other relationship, labelled)
Directional Association
Correspondence
Notes: ASL Fig 3-6, trim headers & footers

## Slide 90: Information Architecture Definitions
Ontology
  an ontology encompasses a representation, formal naming, and definitions of the categories, properties, and relations between the concepts, data, or entities that pertain to one, many, or all domains of discourse, Wikipedia
Taxonomy
  a hierarchical classification or categorization system in which all the terms belong to a single hierarchical structure and have parent/child or broader/narrower relationships to other terms.
Information
  Any communication or representation of knowledge such as facts, data, or opinions in any medium or form, including textual, numerical, graphic, cartographic, narrative, or audiovisual. NIST
Data
Data Type
Metadata
Range
Domain
Encoding
Structure
Schema

## Slide 91
Simple Information Viewpoint
Abstract Information Structures
Information
Data Type
0..*
Representation
described by
Range
Name
Name
Encoding
0..1
0..*
0..*
0..*
Structure
association
ordered
Fig 10-4

## Slide 92
Information Viewpoint Objects
Showing Instantiation & Realization
Schema &
Structure
Definitions
Concrete
Data
Object
Abstract
Information
Architecture
Data
Models
Actual
Data
Objects
Instantiation
Realization
Conceptualization
Abstract description of information objects
Information
Data Type
0..*
Representation
described by
Range
Name
Name
Encoding
0..1
0..*
0..*
0..*
Structure
association
ordered
Instantiated description of specific data models
Realized actual data objects
Fig 10-5

## Slide 93: Fig 10-6, Functional View with Representation of Information Objects
T
rack
Directive
Generation
Directive
Execution
S/C Event
Instrument
Commands
S/C
Commands
Observation
Plans
Operation
Plans
Fig 10-6

## Slide 94: ASL Info model example: SOIS System Model: Concept Diagram
Rounded rectangles represent elements define by SOIS.
Solid lines represent structural relationships between elements.
Dashed lines represent other relationships, pointing from subject to object.
Dotted lines represent references, pointing to referenced object.
Dash-dotted lines represent aggregation, pointing to aggregated object.
Mission Application Interfaces
PackageFIle
describes
Application Support Service Interfaces
describes
SO Model
DoT
references
Device Service Interfaces
specifies
Datasheet
Device
describes
references
references
Deployment Description
references
Management Service Interfaces
specifies
Subnetwork
describes
Fig 10-7
Notes: ASL Figure 5-15, trim top & bottom

## Slide 95: ASL example: SOIS System Model - OWL Dictionary of Terms Diagram
Dictionary of Terms (DOT) Diagram from Protégé using OWL
Inheritance tree for classes of objects
Fig 10-8
Notes: ASL Figure 5-16, trim top & bottom

## Slide 96: Changes for SC14 Perspectives/Viewpoints
  Functional, Enterprise, Physical and Operations: Physical has Hardware and Software Development as sub-viewpoints
  From a non-exhaustive list including:
  Functional Viewpoint: The identification of various abstract functions and their allocation to space domain physical objects (Note: adopt CCSDS RASDS Viewpoint)
  Connectivity Viewpoint: How space domain physical objects are deployed and are connected for communications (RF, optical, cabling) (Note: Adopt CCSDS RASDS Viewpoint)
  Enterprise Viewpoint: How organizations are structured to produce & operate space domain objects, requirements and agreements, governance including laws, regulations, policy, and industry guidance or rules for other Viewpoints
  Physical (Hardware) Viewpoint: How space domain physical objects are deployed and connected from a physical / structural perspective (attachment, mating, umbilicals) (Note: Adapted from CCSDS RASDS Connectivity Viewpoint)
  Operations Viewpoint: How space domain systems objects are operated, tasks, procedures & processes. This Viewpoint also includes end-of-life disposal. (Note: new CCSDS RASDS Viewpoint)
  Communications Viewpoint: How space domain physical and software objects communicate, protocols and end-to-end views (Note: adopt CCSDS RASDS Viewpoint)
  Hardware Development Viewpoint: The development and V&V processes for space domain physical objects
  Software Development Viewpoint: The development and V&V processes for space domain software and firmware objects (Note: uses new CCSDS RASDS Operations/ Process Viewpoints)
  Information Viewpoint: This Viewpoint includes information and data definitions, data structures and relationships, best practices, or a library of Voluntary Consensus Standards. (Note: adopt CCSDS RASDS Viewpoint)

## Slide 97
Proposed RASDS++ Extensions
(including TC20 / SC 14 Joint Effort)
New Service Viewpoint
  As introduced in CCSDS SCCS-ARD/ADD and ASL
  Covers system service interfaces and interface bindings
  Possibly leverage TOGAF, DODAF SV, or other service models
New Operations Viewpoint
  Add support for organizational tasks, activities, processes, procedures, and related behavior
  Effectively extends existing Enterprise Viewpoint, uses Systems
  Possibly leverage DODAF OV’s or other process models
Adapted Physical Object viewpoint
  Leverage existing Connectivity Viewpoint (Nodes & Links) to cover all sorts of physical & energetic aspects, using Components (Nodes) & Connectors (Links) as starting point
  Add new aspects for physical elements (structures, articulation, power, thermal views, propulsion, electro-magnetic) perhaps each with their own View attributes

## Slide 98: Services Viewpoint - New
The Services Viewpoint focuses on the exposed services offered by a space system, formalized by functions and interfaces. It describes the interfaces of systems entities (hardware, software, Persons, and/or procedures), how to request and provide services, and their operations and interface bindings.
Stakeholder Concerns:
  The services provided by the system (H/W, SW, Persons);
  The interfaces, access points, and protocols for the system;
  The requirements and constraints on the services;
  The required and provided data for the services;
  Any contractual arrangements or agreements for services.
Service Objects:
  Types: Service types, both formal and informal (systems, Persons, software, etc), data types, and Resources (access to elements having service roles);
  Attributes: service name, type, operations, point of contact, interfaces, interface bindings, and data, interaction modes, policies, constraints;
Domains (boundaries of responsibility or ownership);
Relationships (ownership, membership, participation, roles, contractual);
Information (defined instances of services, functions, and data specifications, along with documents, agreements, contracts, policies, requirements, objectives, goals, scenarios, membership lists, where formal specifications of all of the data to be exchanged are found in Information Views).

## Slide 99
Service Viewpoint - Service Object
(Specialized Functional Entity Features)
Service
Object
Attributes
Identifier
Type
Behavior
Data
External Interfaces:
How other Functional Objects are used to support the performance of this Object
Management Interfaces:
How service is configured,
controlled, and monitored
Service Interfaces:
How services are
requested by & supplied
to “user” Objects
Fig 11-1

## Slide 100: Formalized Relationships among Terms (Service Viewpoint aspects)
Service
Behavior
System
Element
Service
Processes ..
Implemented by 1..
Data
Artifacts
Offers 0..
Service
Interface
Has …
Composed of …
Interface
Binding
Accessed using 1..
Supports ..
Operations
Implements ..
Function
Protocol
Stack
Implemented by (corr)
Fig 11-2

## Slide 101: RASDS Service Protocol Representation
Service Protocol
Service Protocol PDUs
(logical flow)
Service PDUs may be simplex or bi-directional
Service Protocol behavior (may be described by state machine or other)
Protocol Layer N-1
Service Provided Protocol Interface (Service SAP)
Service Required Interface (of comm protocol SAP)
physical layer flow
Protocol Layer N-1 peer
Flow direction arrows (optional)
Service User I/F
Authorization
Interface Binding Protocol Stack
(multiple layers)
Svc Access Authorization (optional)
Service
Provider
Service Protocol peer
Service Protocol SDUs
(data flow)
Fig 11-3, with mods
Function that offers a service
Denotes a (service or optional authorization) protocol layer (typically defined in a standard)
Denotes a Service Access Point (SAP, required, usually defined in a standard or ICD)
Denotes the actual flow of wrapped PDUs (as Service Data Units) between two layers
Denotes a logical, peer to peer, protocol flow within a layer (Protocol Data Units)
Specific and Generic Object Types and Containment:
Protocol
Notes: ASL Fig 3-6, trim headers & footers

## Slide 102: Simple Service View with Protocol Layer (showing corresponding Function and protocol stack deployments)
Svc Provider Node
Monitor Data (Provider)
CSTS Messages
MD-CSTS Provider
Svc User Node
Monitor Function
(Consumer)
CSTS Messages
MD-CSTS User
DATA
TCP/IP Technology Binding
IP Network Protocol
TCP Transport Protocol
Link Layer
IP Network Protocol
TCP Transport Protocol
Link Layer
TCP/IP Technology Binding
Physical Link
Service Logical Link
End-to-end Service
Stack of Communications Layer Protocols
Stack of Application Layer Protocols
Service Access Point
Deployment Node
Fig 11-4
Notes: ASL Fig 3-7, trim headers & footers

## Slide 103
Formalized Relationships among Terms (Service Viewpoint aspects)
Notes
Service Object Notes:
Interfaces of Service Objects may involve an app (thick or thin client), or expose a service protocol, or they may have their own UI, or they may be deployed in the cloud and use HTTP/REST and a web browser.
  Service Ontology Notes
  Service: A provision of an interface of an object to support actions of another object.
  Interface: A set of interactions performed by an object for participation with another object for some purpose, along with constraints on how they can occur. An interface is therefore where the behavior of an object is exposed.
Service Protocol Notes
ISO /IEC 7498 Basic Reference Model (BRM) treats all of this as “Application Layer”. Server, web/cloud, or virtualized deployments fit this same pattern.
Service protocol must have defined behavior, PDUs, and required / provided interfaces. Behavior may be defined in a state machine, state table, or narrative form. Usually only defines behavior of sending side, but may define both ends.
Service Protocol may be built upon a standard protocol such as HTTP/REST, or a protocol like AMS, or accessed via a defined API with a bespoke protocol. Underlying protocol stacks follow normal Communication View rules.
Services may use externally supplied Authentication mechanisms. They may also rely upon security mechanisms (encryption, authentication of data payloads) implemented within the layer or in underlying layers.
Reflect on how this pattern can be used to describe Message Bus, Web or Cloud, or AMS Service types
- MB is a service API
- Web uses HTTP from client (browser) to provider
- Cloud is like Web, but Cloud offers other internal services via HTTP
- AMS is a “thick client” application protocol over space links (or other)

## Slide 104: ASL-style Services Viewpoint Example: Mission Control Service Table and correspondences
Monitoring and Control
M&C
Node A
Function A (Provider)
Message Abstraction
Service Layer
Technology Binding
Network Protocol
Transport Protocol
Link Layer
Services Viewpoint Table
Function, Operation, Data
Service View:
Service
Description
Communications
view:
Layered Service
Interface
Protocol Bindings
Information
View:
Information Object
Description
Fig 11-5

## Slide 105: Relationship of Services to Message Bus, Web or Cloud, or Message Protocols
A service has four properties according to one of many definitions of SOA (Definitions taken from https://en.wikipedia.org/wiki/Service-oriented_architecture):
  It logically represents a business activity with a specified outcome.
  It is self-contained (not well defined).
  It may be a black box for its consumers, meaning the consumer does not have to be aware of the service's inner workings.
  It may consist of other underlying services.
The CCSDS use of “Service” is consistent with these definitions
From a protocol / interface binding perspective services may be deployed in many different ways, built upon different underlying protocol stacks: message bus, web services, “cloud”, or other messaging protocols.
  Message Bus: Typically a bespoke protocol implementation, possibly in an on-board context, or using something like JMS. Often uses an API to hide implementation details which may not employ an interoperability spec, but may be layered on underlying transport/network layer like TCP/IP or a link layer.
  Web or Cloud: Typically use HTTP(S)/REST or related protocols on top of a network/transport layer. Server may be on local hardware, or at a data center, or a “cloud” deployment. Actual End-to-End protocol stack may involve intermediate caching systems for performance.
  Message protocols: May use an interoperable message protocol spec like AMS and layer upon TCP/IP or DTN network layer.
Services come in many different deployment “flavors”, including: thick client, thin client, browser “app”, virtualized, SaaS, PaaS, IaaS, … All use one flavor or another of application and underlying comm protocol stacks with different deployment models.

## Slide 106: Operations Viewpoint - New
The Operations Viewpoint …
Stakeholder Concerns:
  The operations enabled by using the system;
  The activities carried out by using the system;
  The requirements on operations and activities (from Enterprise);
  Responding to constraints (e.g. cost, performance, policies) on operations and activities (from Enterprise) and Murphy…;(
  Describing how these support enterprise capabilities (from Enterprise);
  How these utilize systems capabilities (from Connectivity/Deployment); .
Operations Objects:
  Types: Capabilities (), Tasks, Processes (), Activities (), Scenarios (), Resources (systems, Persons, data, etc) having Operations roles;
  Attributes: names, types, flows, relationships, interaction modes, states (nominal, off-nominal), constraints;
Domains: boundaries of responsibility or ownership, related to org/team;
Relationships (implemented by, executed by, satisfies, provides);
Information (defined instances of requirements, plans, processes, resources, objectives, goals, scenarios, where formal specifications of the data to be exchanged are found in the Information Viewpoint).
Correspondences to Enterprise (requirements, objectives, Persons, policies), Systems (Connectivity view), Information (defined instances of documents, agreements, contracts, policies, requirements, objectives, goals, scenarios)
Operations viewpoint defines the objects and relations and rules for constructing views
Operations views are used to address specific concerns and represent activities, processes, and behaviors.

## Slide 107
Operations Object
Operations Viewpoint
(Abstract Operations Object Representation)
Attributes
Type (task, activity, process)
Properties
Products
Performance constraints
External Interfaces:
How Products are supplied to and requests are made of other Operations Objects
Management Interfaces:
How operations are configured,
controlled, and reported upon
Service Interfaces:
How operations tasks are requested by other Organization or Operations Objects
Fig 12-1

## Slide 108: Formalized Relationships among Terms (Operations Viewpoint ontology)
Operations Process
Operations
Requirements
Persons
Performed
by
Implemented by 1..
Describes / Uses …
Specify
Department
Member
of
Operations
Procedure
Data
Artifacts
Uses …
Accesses
Work
Performs
System Element
Perform …
Product
Produces
Fig 12-2
Standard
Operations
Procedure
Defines
Normative
Specification

## Slide 109: RASDS Operations View Representation
Swimlane (System B)
Swimlane (System A)
Task A
DATA
Logical Link: flow between tasks
Source Task
(start/stop or duration, optional)
Subsequent Task
(start time or event, optional)
Information Object
(optional)
Operations Objects are Tasks, treated like functions, abstract representations of behavior. For this purpose they are shown within some system context (swimlanes).
Operations Objects may themselves be decomposed into lower level Operations. Different uses of the same Operations Object may be expressed in other views and referenced by correspondence.
Operations views are intended to describe temporal flows among different systems elements.
Operations views may explicitly show timing and/or duration, and are suitable for representing instances, durative events, and sequences of events.
They may explicitly identify the information objects that are exchanged (tied by correspondence to the Information View where they are defined).
Sub-Function B1
Task B
Fig 12-3, with mods
Denotes a defined function, may show containment (example shown)
Denotes a Logical Link between two Functions and flow direction (optional)
Information Object (optional) describing communicated data, which may be described in the Information Viewpoint and referenced by correspondence
Denotes a specific set of activities / tasks associated with a given System Object or Organization
Specific and Generic Object Types and Containment:
DATA
Swim-lane Name
Task flow
Notes: ASL Fig 3-4, trim headers & footers

## Slide 110: Operational Viewpoint (temporal aspect)
Process
Procedure
Activity
Task
Product
System
Element
Action
Event
has_inter_connected
has_ordered_set
has_cohesive_set
performs
invokes
creates
generates
provides_ordering_for
describes
Plan
Schedule
part_of
has
sets_parameters
change
uses
trigger
Fig 12-4

## Slide 111: Formalized Relationships among Terms (Operations Process ontology)
Operations Process
Activity
(Std Ops)
Procedure
Task
Action
Has 1 .. Inter-related
Has cohesive set of 1 ..
Ordered set of 1 ..
Performs …
Product
Produces
Work
Is …
System
Element
Occurs within …
Hardware
Software
Person
Composed of 1..
Missing temporal aspects (Event) from recent Costin work
Data
Artifacts

## Slide 112
Operations Viewpoint
(Abstract Operations Object Representation)
Notes
Viewpoint Concerns:
Issues
Resources requirements
Constraints
* A System Element includes “Application”, which is a set of functions deployed (somehow) on a server as part of a system
  An enterprise capability denotes the “What” an enterprise can do, whereas an Operations process outlines “how” a particular activity gets done.
Operations Process: An Operations process is defined as a set of activities and tasks that, once completed, will produce a product or perform work

## Slide 113: Simple–Operations Activity Example
Mission Planning & Sequencing
Activity
Command
Delivery
Activity
Command Generation
Activity
Uplink Generation
Activity
Fig 12-5
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 114: Functional Viewpoint – Telemetry & Mission Operations Functions & Service Interfaces
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Processing
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Fig 12-6
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 115: Temporal Aspects of Operational Viewpoint (UPDATED)
The Operational Viewpoint may describe any of the following:
  Activity, Procedure and Task all may have stated temporal aspects
    May have start time, stop time, or duration specified
    May be used to represent both planning views and actual “as executed” views
  Action:
    An Action may be instantaneous or have some finite duration
    An Action may have both planning estimates and actual “as executed” observations
  Event:
    “Any observable system or natural occurrence.” NIST (modified)
    “The fundamental entity of observed physical reality represented by a point designated by three coordinates of place and one of time in the space-time continuum postulated by the theory of relativity”, Merriam Webster
  Sequence of Events (SOE):
    “a number of events or activities that come one after another in a particular order”
    “the predicted order of events during spacecraft operations”, also
    “the observed order of events during spacecraft operations”
Temporal aspects extend core ops model
Plan = Captures the (acceptable) balance of risk vs. result in generating an operational product. E.g. Nominal or Off-nominal plans.
Schedule = Captures temporal context for Plan. (e.g. keeps track of SoE <anomaly vs. “as predicted/expected”>)
Process = What needs to happen in the plan to generate an operational product.

## Slide 116: Operations Viewpoint Selected Definitions of Terms
For the Operations Viewpoint we need a self-consistent set of terms and associated definitions.
  Process:
    “set of interrelated or interacting activities which transforms inputs into outputs” NIST
  Activity:
    “Set of cohesive tasks of a process.” NIST
  Procedure:
    “An ordered set of tasks for performing some action.” Wikipedia
    Std Operations Procedure - A set of instructions used to describe a process or procedure that performs an explicit task or explicit reaction to a given event.” NIST
  Task:
    “A Task is a specific defined piece of work that, combined with other identified Tasks, composes the work in a specific specialty area or work role.” NIST
  Action:
    “An action is something that happens within an object, either with or without participation of another object. An interaction is an action performed by an object with participation of another object or with its environment. “ RASDS
  Product:
    “Result of a process. Note: A system as a “product” is what is delivered by systems engineering.” NIST
  Scenario
    A sequential, narrative account of a hypothetical incident that provides the catalyst for the exercise and is intended to introduce situations that will inspire responses and thus allow demonstration of the exercise objectives. NIST
    a postulated sequence or development of events. Oxford
    a description of how things might happen in the future. Oxford
See temporal aspects slide

## Slide 117: Operations Viewpoint – Mission Control Process Diagram (tasks & data flows)
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive service
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Science Data
    NOTE: All of these may have start time, stop time, or duration specified
Fig 12-7

## Slide 118: Relationships between Functional and Operations views
Functional View
  Shows Functions (and associated Functional Group using color coding)
  May show Provided Interfaces
  Shows Data that is exchanged (defined in Information Views)
  Does not show any temporal aspects or recursion
Operations View
  Describes how to perform a process to accomplish Tasks
  Shows tasks executed within System Elements (vertical or horizontal swimlanes)
  Shows temporal ordering of flows (starting upper left in this case) between Activities (or Tasks), may show recursion
  May show timing and duration of activities (or tasks)
  Names the Data objects that are exchanged
  May show timing (start/stop or duration) or events
  May represent predicted or observed sequence of events

## Slide 119: RASDS++ in wider social context
Enterprise
Information
Environment
Function
Requirement
Design & Engineering
Production
Verification
Operations
System
Venue
Region
Globe
Space
City
Lifecycle
RASDS++
Interoperability Viewpoints
Disposal
Scope
Component
Services
Communication
Mission assurance
Service/Operation
Wider
Spatial Scope
Protocol
RF
Data model
Services
Business
model
Architecture
Operations
Source: Koki Asari, Japan Space Systems
ISO TC 20/SC 14/WG8
Functional model
Ops Process
Fig 13-1
Optical

## Slide 120: RASDS Object Hierarchies
In many systems architecture contexts explicitly identify different kinds of objects, and different hierarchies or aggregates of objects, that are needed in the domain:
  Enterprise: mission phases, org structures, requirements decomposition “levels”
  Functions: high level “functional groups”, “complex functions”, “atomic functions”
  System Elements: systems, subsystems, elements, devices, components …
  Aggregation: of objects with similar purposes, data types, uses, …
Because of the wide range of possible domains RASDS cannot create any definitive hierarchies, but it can provide examples and descriptions of how to do this.
RASDS recommends that such hierarchies are defined, documented, and used consistently.

## Slide 121: UML System Decomposition Profile
The following is just one possible example of how to do this:
  Created using SysML
  Defines the <<stereotype>> for the top level system elements
  Defines names for successive levels of decomposition of system elements, down to Subsystem
  Splits below that level into a hardware hierarchy (HW) and a software hierarchy (SW)
  Other hierarchies of terms and levels may be selected and defined, as driven by project needs. Just use them consistently.
  Use the same basic process to create other decomposition hierarchies, like SE or RQ Levels.
This example also defines a non-normative color palette for different groupings of function types, i.e. kinds of functions, or different ownership.

## Slide 122
RASDS++ System Architecture Model
Objectives
RASDS++ provides an Architecture Description Framework and methodology, a specific Space System Reference Architecture model …
  Provides clear & unambiguous viewpoints for describing space systems architectures
  Shows relationship of design to requirements and driving scenarios
  Separates abstract design from implementation concerns in the model to maintain a degree of freedom to do trades
  Details the model & views to the level appropriate for further systems engineering and supports evolution of the detailed design
  Enables concurrent design of spacecraft, ground systems, communications & control systems, components, and their mission or science operations
Notes: 122

## Slide 123: A reminder from DoDAF: DoDAF Viewpoints and Models - intro
To assist decision-makers, DoDAF provides the means of abstracting essential information from the underlying complexity and presenting it in a way that maintains coherence and consistency. One of the principal objectives is to present this information in a way that is understandable to the many stakeholder communities involved in developing, delivering, and sustaining capabilities in support of the stakeholder's mission. It does so by dividing the problem space into manageable pieces, according to the stakeholder's viewpoint, further defined as DoDAF-described Models.
Each viewpoint has a particular purpose, and usually presents one or combinations of the following:
  Broad summary information about the whole enterprise (e.g., high-level operational concepts).
  Narrowly focused information for a specialist purpose (e.g., system interface definitions).
  Information about how aspects of the enterprise are connected (e.g., how business or operational activities are supported by a system, or how program management brings together the different aspects of network enabled capability).
However, it should be emphasized that DoDAF is fundamentally about creating a coherent model of the enterprise to enable effective decision-making. The presentational aspects should not overemphasize the pictorial presentation at the expense of the underlying data.
RASDS defines specific objects and representations for different viewpoints and a methodology that may be used to define and aid understanding of different systems technical architectures, information & communications aspects, and deployment approaches.

## Slide 124: Mapping RASDS Into SysML
Introduce general approach of mapping RASDS PPT presentation style to SysML / MBSE
  Create Profile
  List diagram type to Viewpoint mapping approaches
Use the following set of “PPT hacked” example diagrams?
Or use example diagrams from Shames, Sarrel, Friedenthal paper?
Consider SysML V2???

## Slide 125: Mapping RASDS into SysML
No simple one for one mapping from RASDS to SysML, their intent and scope are different
RASDS uses Viewpoints to expose different concerns of a single system
SysML uses specific diagrams to capture system structure, behavior, parameters and requirements
More than one SysML diagram, focused on different RASDS object classes, may be usefully applied to different Viewpoints
Extended SysML Views may be used to define the relationships between Viewpoints and Diagrams
SysML can provide useful tooling and offer support for more accurate fine grained modeling of structure, relationships and behavior than was expected of RASDS

## Slide 126: Mapping RASDS into SysML
Enterprise
  Organizational component & collaboration diagrams
  Use case, interaction overview diagrams
  Requirements & constraints for rules, policies & agreements
Connectivity
  Physical component, composition, collaboration & class diagrams
  Parametric diagram for physical link characterization
Functional
  Logical component, collaboration & class diagrams
  Activity, state chart, parametric, & timing diagrams
Informational
  Information class & parametric diagrams
Communication
  Protocol component & collaboration diagrams
  State machine, sequence, activity & timing diagrams
Operations
  Activity / swimlane diagrams, tasks and flows

## Slide 127: SysML Example of System Decomposition
Fig C-1

## Slide 128: Note to CTE
See separate VG package for Fig C-1 thru C-5…
  SCaN Trade Space Architecture Model SO12-1275283 25 Nov 24

## Slide 129: SysML Version (INCOSE-IS-2016) RASDS Physical / Connectivity - E2E
Copyright INCOSE IS 2016 by Peter Shames, Sandy Freidenthal, Marc Sarrel
Used with permission
Fig C-6

## Slide 130: SysML Version (INCOSE-IS-2016) RASDS Connectivity - Components
Copyright INCOSE IS 2016 by Peter Shames, Sandy Freidenthal, Marc Sarrel
Used with permission
Fig C-7

## Slide 131: SysML Version (INCOSE-IS-2016) RASDS Communications - Protocol entity
Copyright INCOSE IS 2016 by Peter Shames, Sandy Freidenthal, Marc Sarrel
Used with permission
Fig C-8

## Slide 132: SysML Version (INCOSE-IS-2016) RASDS Communications - Protocol State Chart
Copyright INCOSE IS 2016 by Peter Shames, Sandy Freidenthal, Marc Sarrel
Used with permission
Fig C-9

## Slide 133: SysML Version (INCOSE-IS-2016) RASDS Information
Copyright INCOSE IS 2016 by Peter Shames, Sandy Freidenthal, Marc Sarrel
Used with permission
Fig C-10

## Slide 134: RASDS Revision – ISO 42010-2022 conceptual framework (ontology)… from http://www.iso-architecture.org/42010/cm/
We adopt and build upon this system architecture meta-meta-model framework, creating meta-models for viewpoints aligned with it that are suitable for space system architecture description
Copyright 1998-2023 by Rich Hilliard
Used with permission
Fig D-1

## Slide 135: Meta-models: relationships between UML, ISO 42010, RASDS meta-models, and user models
Copyright 1998-2016 by Rich Hilliard :: http://www.iso-architecture.org/42010
Used with permission
Reference: Jean Bezivin, “On the unification power of models”, 2005
RASDS meta-model defines specific Viewpoints, Objects, and Representations, and conforms to ISO 42010
A RASDS conformant Architecture Description Model adopts specific Views & Model attributes, users may extend
Users adopt / adapt RASDS to describe their specific systems architecture
representedBy
conformsTo
conformsTo
Fig D-2

## Slide 136: ISO 42010-2022 Architecture Definitions
Architecture Viewpoint
  Set of conventions for the creation, interpretation, and use of an architecture view to frame one or more concerns
  Note: a viewpoint is a frame of reference for the concerns determined by the architect as relevant to the purpose of the architecture description.
  Note: The conventions of an architecture viewpoint are included in a specification of this viewpoint. In some communities and architecture frameworks, “view specification” is used to mean the same thing.
Architecture View
  An Information item, governed by an architecture viewpoint, comprising a portion of an architecture description
  Note: An architecture view could include contextual schema, conceptual, logical and physical data models, data dictionary and documents as view components, and entities, relations and attributes as AD elements.
Concern
  Matter of relevance or importance to a stakeholder regarding an entity of interest, or some matter related to that entity.
  Note: Stated concerns are useful when relevant to the purpose of the architecting effort and refer to specific rather than categorical difficulties, problems, or requirements.
Correspondence
  Identified or named relationship between two or more architecture description elements
  Note: A function such that for elements in one viewpoint there is a related element in another viewpoint; the condition of being in conformity from elements in one viewpoint to elements in another.
  Note: Correspondences are used to express a wide range of relationships, such as equivalence, composition, refinement, consistency, traceability, dependency, constraint, satisfaction, and obligation.

## Slide 137: Earlier Arch Viewpoints
From JPL Pub 89-24, “The Voyager Neptune Travel Guide”, Charles Kohlhase editor, June 1, 1989 (artist Phil Gwinn)
Fig D-3

## Slide 138: Enterprise View Using SysML Use Case Diagram
Preliminary
<<usage>>
Enterprise: Use Case
Mars Exploration
Program Federation
Mission A
Agency ABC
GTN B
Mission Q
Instr C
Agency QRS
Instrument
Integration
Operations
Contract
<<includes>>
<<includes>>
<<includes>>
<<includes>>
<<includes>>
<<includes>>
<<extends>>
Cross Support
Agreement
<<extends>>
<<extends>>
Service Operations
Team
<<Secondary>>
Science
Team
<<primary>>
Science
Team
<<primary>>
Instrument
Team
<<Secondary>>
Relay
Service A
<<extends>>
TT&C
Service B
Mission
Operations
Team
<<Primary>>

## Slide 139: Connectivity View (Nodes & Links) Using SysML Components (Spacecraft)
Preliminary
Derived from: SysML Partners
sciInstr : scienceInstrument
CDH : CmdDataHandlingSystem
dl : DownLink
Spacecraft
s :
Sensor
ic :
InstrControl
ap : Aperture
ap: Mechanical
ObsFin
Port
DataDonePort
dm :
DataManager
ecu : Execution
Control Unit
oc :
ObsControl
InstrCmnd
Port
TelemPort
TakeObs
SensorData
RFAntenna
ul : UpLink
TeleCmndPort
CmndIn
Port

## Slide 140: Connectivity View (Nodes & Links) Using SysML Components (MOS & TT&C Systems)
TT&C : TrackTelemCommand
MOS : MissionOpsSystem
TM :
Telemetry
TC :
Telecommand
Pt : Pointing
Ant: Mechanical
TelemDonePort
dm :
DataManager
MOP : Mission
OpsPlanning
SC :
SendCmnd
Cmnd Port
Telem
Port
PointingData
TelemData
RF
Ant
Tele
Cmnd
Port
ObsReq
Port
ul : UpLink
dl : DownLink
CmndData
Re
Trans
Port
DL
Port
UL
Port

## Slide 141: Connectivity View (Composition) Using SysML Components
Global structure inherited by each kind of Spacecraft …
… and constrained for each kind
Preliminary
TT&C : TrackTelemCommand
MOS : MissionOpsSystem
TM :
Telemetry
TC :
Telecommand
Pt :
Pointing
Ant:
Mechanical
TelemDone
Port
dm :
DataManager
MOP : Mission
OpsPlanning
SC :
SendCmnd
Cmnd Port
Telem
Port
Pointing
Data
TelemData
RF
Ant
Tele
Cmnd
Port
ObsReq
Port
ul : UpLink
dl : DownLink
CmndData
Re
Trans
Port
DL
Port
UL
Port
sciInstr : scienceInstrument
CDH : CmdDataHandlingSystem
dl : DownLink
Spacecraft
S :
Sensor
IC :
InstrControl
Ap :
Aperture
AP:
Mechanical
ObsFin
Port
DataDone
Port
dm :
DataManager
ecu : Execution
Control Unit
oc :
ObsControl
InstrCmnd
Port
TelemPort
Take
Obs
SensorData
RFAnt
ul : UpLink
TeleCmndPort
Cmndin
Port
RF: link [X-band]
RF: link [KaBand]

## Slide 142: Operations View Using SysML Activity Diagram
Preliminary
Showing component allocations (optional)
Spacecraft
Ground System
Instrument
S/C Control
Mission Ops
Prepare
Cmnd
Accept
Data
Finish
ObsSeq
Take Obs
plannedObs
Instr
Cmnd
Plan
ObsSeq
TT&C Network
Xmit
Cmnd
Recv
Data
Transmit
Data
Store
Data
Execute
Cmnd
retransReq
readyCmnd
Recv
Cmnd
obsComplete
retransDataReq

## Slide 143: Informational View Using SysML Class Diagram
Preliminary
Reusable, refinable information structure:
<<info obj>>
InstrCmndFile
1..*
1
describes
Global representation inherited by each kind of Information Object
Derived from: SysML Partners
<<data obj>>
InstrCmndList
<<data obj>>
InstrCmnd
1..*
<<metadata obj>>
InstrCmndMetaData
<<metadata obj>>
InstrCmndSemantics
<<metadata obj>>
InstrCmndStructure

## Slide 144: Communication View (Protocol Objects) Using SysML Component Diagram
Preliminary
Derived from: SysML Partners
TC :
TeleCmnd
<<protocol>>
LL: LinkLayer
SC : SpaceCraft
CmndData:RF
<<protocol>>
PL: PhysLayer
<<protocol>>
IP: InternetLayer
<<protocol>>
TP: TransportLayer
CmndIn
Port
SC :
SendCmnd
<<protocol>>
LL: LinkLayer
MOS : MissionOpsSystem
<<protocol>>
PL: PhysLayer
<<protocol>>
IP: InternetLayer
<<protocol>>
TP: TransportLayer
Cmnd
Port
ECU : Execution
Control Unit
MOP : Mission
OpsPlanning
RF: link [Xband]
<<controls>>

## Slide 145: Communication View Using SysML State Machine Diagram
Preliminary
<<protocol>>
TP: TransportLayer
Derived from: SysML Partners
Idle
Waiting
Sending
evSend /
transmitCount=0
tm(Wait Time)
[transmitCount<LIMIT]
evDoneSend /
++transmitCount
evACK[isValid]
tm(Wait Time)
Throw(“Unable to Send”)
Protocol specifications inherited by each instance of Protocol Objects

## Slide 146
CCSDS / SC14 - RASDS update project
Proposed RASDS update tasks
  Update RASDS, add new viewpoints
    Integrate ASL & SCCS ADD approaches to refine framework
    Work in collaboration with TC20/SC14 SE team to extend framework
    Incorporate published diagrams from ASL and SCCS where appropriate
    Update security view sections, as needed
    => Is a new Engineering / Process Viewpoint needed to deal with SC14 V&V and process considerations? No, leave for ISO 15288 and agency stds.
  Add annex with MBSE / SysML representations
    May use SysML representations or just adopt a uniform set of OWL / ontology diagrams documenting the concepts for each viewpoint
    The methodology is the same for either approach, but the representation differs
    Incorporate representation & figures from published MBSE papers
  With TC20/SC14 refine and extend existing CCSDS Glossary
    Leverage SANA on-line repository for human and machine access
    Add SC14 specific terms where required
    ECSS interests may also be considered

## Slide 147: BACKUP

## Slide 148: “Singing and Dancing” Views
Shows the relationship between related Functional and Task flows shown using a UML Activity diagram.
UML Activity diagram is better for showing temporal flows
Functional diagram is better at showing relationships, interfaces, and data source / sink behavior
Each step in the flow is marked to show the active functions

## Slide 149: Functional & Operations Diagram Tracking #1
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 150: Functional & Operations Diagram Tracking #2
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 151: Functional & Operations Diagram Tracking #3
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 152: Functional & Operations Diagram Tracking #4
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 153: Original RASDS Top Level Object Ontology
Function
Behavior
Interfaces
Constraints
Logical structure
Connector
Type
Attributes
Communication
Protocol stack
Standards
Organization
Requirements
Objectives
Goals
Scenarios
Mission
FulfilledBy
Fulfills
IsAllocatedTo
ComposedOf
Composed Of
ComposedOf
ContainsInstances
Produces
Consumes
ConnectVia
ConnectToPort
Uses
ProvidesService
AssociatedWith
ImplementedOn
Information
Data
Metadata
Rules
Owns/Operates
Component
Type
Attributes
Ports
Calls
Environment
Physical Environs
Affects
Location
Attributes
Meta-model
(each Viewpoint)
Defines Objects
Defines Rules
Exposes Concerns
Defines Relations

## Slide 154: Organizations value and manage Assets (NIST 800-207 terms)
System
Assets
Resource
Assets have attributes: Asset Type {Data, Database, virtual artifacts}; Deployment Type {Physical, virtual, cloud}; Asset state {Sensitivity, Integrity, Security posture}; Environmental attributes {…}; Other {…}
Catalog
Organization
Values
Hardware
Virtual Platform
Data
Creates Catalog
Person
Device
Network
IT Circuit
Resource = All hardware, software, programs, information, data, and other devices that are in use within or connected to a given system
Procedures
Is an
Is composed of …
Software
Is Inventory of

## Slide 155: Research: Operations Viewpoint Identified Definitions of Terms
For the Operations Viewpoint we need a hierarchy of terms and associated definitions. We did some research and found these (not necessarily self-consistent):
  Action:
    “An action is something that happens within an object, either with or without participation of another object. An interaction is an action performed by an object with participation of another object or with its environment. “ RASDS
  Activity:
    “Work, not specific to a single organization, Operations system or individual that transforms inputs (Resources) into outputs (Resources) or changes their state.” DoDAF – modified
    “An activity is a specification of behavior described as a sequence of actions” RASDS
    “Set of cohesive tasks of a process.” NIST
    “An Activity is a generic term for work that company performs. An Activity can be atomic or non- atomic (compound). The types of Activities are: Task and Sub-Process.” BPMN
  Procedure:
    “An ordered set of tasks for performing some action.” Wikipedia
  Process:
    “A Process is an activity authorized by a Work Package in support of delivering a Component or producing a Product. “ IMCE
    “Business Process Model is a network of graphical objects, which are activities (i.e., work) and the flow controls that define their order of performance. “ BPMN
    “A logical, systematic sequence of activities, triggered by an event, producing a meaningful output.” DoDAF
    “set of interrelated or interacting activities which transforms inputs into outputs” NIST
  Product:
    “A Product is a concrete output of the design process. It may be a Component or a Document. A Product is any Element that an Authority properly supplies or produces. “ IMCE
    “Result of a process. Note: A system as a “product” is what is delivered by systems engineering.” NIST
  Task:
    “An action, activity or undertaking enabling missions, activities or functions to be performed or accomplished.” DoDAF
    “A Task is a specific defined piece of work that, combined with other identified Tasks, composes the work in a specific specialty area or work role.” NIST

## Slide 156: DRAFT Operations Meta-model (OWL) Replace / Update
Process
Activity
Procedure
Task
Action
Has 1 .. Inter-related
Has cohesive set of 1 ..
Ordered set of 1 ..
Performs …
Product
Produces
Work
Is …
Systems
Object
Occurs within …
If these are the definitions of terms and relationships, does this ontology accurately reflect them?

## Slide 157: Formalized Relationships between Enterprise & Technical Architecture (Enterprise Viewpoint & System Architecture Viewpoint objects)
System **
Hardware
Software
Persons
Procedures
Composed of 1..
Environment
Affects
Function
Implement 1..
Function offers 0.. Service Interfaces
Process
Action
Task
* An “Application” is Software, a set of functions deployed (somehow) on a server as part of a system, with defined interfaces
(Business) Process
Capability
Actor
Performed
by
Business
Possess set of 1..
Implemented by 1..
Uses …
Application
Business
Information
Services …
Uses
Department
Member
of
Service
Application*
Data Artifact
Uses …
Accesses
“Logical” Enterprise System Boundary **
  The Enterprise Architecture addresses processes, services, and applications, all of which are implemented by the Technical Architecture, but without directly addressing the relationships among functions, HW, SW, and Persons that are addressed in the Technical Architecture.
Process is an ordered set of Functions
The “Enterprise Architecture”, in actuality, is implemented by the Technical Architecture
“Actors” are Persons who have assigned identities and roles in a real system.
The “Technical Architecture” implements the systems, services, and processes.
Supports the Enterprise

## Slide 158: Connectivity View Nodes & Links
Mission Planning
Computer
Spacecraft
Control
Computer
Space Link
Internet
Ground
Tracking
Station
Command &
Data Handling
Computer
ACS
Computer
S/C Bus
Science
Instrument
Spacecraft
Transceiver
Connectivity Concerns:
  Distribution
  Communication
  Physical Environment
  Behaviors
  Constraints
  Configuration
SPACECRAFT

## Slide 159: Meta-models: UML relationships among meta-models, user models, and instances

## Slide 160: ASL Connectivity Example: Physical Model (SSI) With representative Functional Deployment
Relay Spacecraft
Lander/Rover
or Habitat
ESLT
TT&C
Spacecraft
NAVT
MCS
DSA
MPS
NAVT
MCS
DSA
MPS
NAVT
MCS
DSA
MPS
MOC
DPC
DAC
POC
PI/User
SCM
NSC
OPS
NAVT
MCS
DSA
MPS
OPS
NAVT
MCS
DSA
MPS
Mission Data Processing
User Support
Spacecraft
Development &
Maintenance
NAVT
DSA
OPS
NAVT
DSA
MPS
Notes: ASL Fig 8-4, trim headers & footers

## Slide 161: ASL Example: Mission Control functional decomposition
Navigation & Timing
Planning & Scheduling
Navigation Interface
Data Storage and Archiving
Operations Preparation
TT&C
Automation
On-board Configuration Management
Monitoring and Control
M&C
ODM
PRM
ADM
NEM
M&C
AUT
M&C
OBSM
OBPM
OBSM
OBPM
APD
SDB
M&C
User Support
Mission Data Processing
Spacecraft Development & Maintenance
M&C
M&C
AUT
OBSM
OBPM
AUT
TCM
OBSW
APD
M&C
SC-CSTS
MD-CSTS
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 162: Alternate Functional & Protocol Diagram (for a Single Process)
put
get
MIB
Outbound Link PDU
Inbound Link PDU
put
get
database
Outbound App PDU
Inbound App PDU
application
protocol
application
encryption
service
link protocol
Protocol SAP

## Slide 163
Enterprise
Information
Environment
Function
Requirement
Design & Engineering
Production
Verification
Operations
System
Venue
Region
Globe
Space
City
Lifecycle
RASDS/RASDS++
Interoperability viewpoints
Disposal
Scope
Component
Connectivity
(Structure)
Communication
Mission assurance
Service/Operation
Wider
Spatial Scope
Proposed Utilization of RASDS/RASDS++
Protocol
RF
Data model
3D-view of views: Viewpoints, adding Lifecycle, Scope dimensions
Business
model
Architecture
Operations
Source: Koki Asari, Japan Space Systems
ISO TC 20/SC 14/WG8
Try to align the colors of VP & objects w/ RASDS canonical choices

## Slide 164: DoDAF Operations Viewpoint (for consideration …)
DoDAF-described Models in the Operations Viewpoint describe the tasks and activities, Operations elements, and resource flow exchanges required to conduct operations. A pure Operations model is materiel independent. However, operations and their relationships may be influenced by new technologies, such as collaboration technology, where process improvements are in practice before policy can reflect the new procedures.
Use of Operations Viewpoint DoDAF-described Models should improve the quality of requirements definitions by:
  Explicitly tying user requirements to strategic-level capability needs, enabling early agreement to be reached on the capability boundary.
  Providing a validated reference model of the business/operations against which the completeness of a requirements definition can be assessed (visualization aids validation).
  Explicitly linking functional requirements to a validated model of the business or operations activities.
  Capturing information-related requirements (not just Information Exchange Requirements [IERs]) in a coherent manner and in a way that really reflects the user collaboration needs.
  Providing a basis for test scenarios linked to user requirements.
  Capturing the activities for Process Engineering or Process Re-engineering.

## Slide 165: DoDAF Operational Viewpoint, contd Possible Model Views
Model | Description
OV-1: High-Level Operational Concept Graphic | The high-level graphical/textual description of the operational concept.
OV-2: Operational Resource Flow Description | A description of the Resource Flows exchanged between operational activities.
OV-3: Operational Resource Flow Matrix | A description of the resources exchanged and the relevant attributes of the exchanges.
OV-4: Organizational Relationships Chart | The organizational context, role or other relationships among organizations.
OV-5a: Operational Activity Decomposition Tree | The capabilities and activities (operational activities) organized in a hierarchal structure.
OV-5b: Operational Activity Model | The context of capabilities and activities (operational activities) and their relationships among activities, inputs, and outputs; Additional data can show cost, performers or other pertinent information.
OV-6a: Operational Rules Model | One of three models used to describe activity (operational activity). It identifies business rules that constrain operations.
OV-6b: State Transition Description | One of three models used to describe operational activity (activity). It identifies business process (activity) responses to events (usually, very short activities).
OV-6c: Event-Trace Description | One of three models used to describe activity (operational activity). It traces actions in a scenario or sequence of events.
Operations Model Descriptions

## Slide 166
RASDS background – from the
IEEE-1471-2000 conceptual framework…
We formalize and adapt this generic conceptual
framework into one for
suitable for space data system design
Notes: 166

## Slide 167: SAWG Observations on Terminology
Some of the terms used in CCSDS documents are not even in the CCSDS Glossary
We only have accurate information models and schema for a small sub-set of the terms in use
Some terminology is defined in multiple different standards, and this is where issues arise
Lack of consistent terminology makes automation and cross use of terms much more difficult
Some terminology is in isolated domains and not an issue
Multiple inconsistencies in use of terminology
  Collisions of usage (same word, two different meanings)
  Specializations (same word, on analysis one derived from another)
  Multiple terms used for the same things
  Internal inconsistencies in usage or definitions
  Inconsistent use of representations (lack of class diagrams)
  Inconsistent references to external standards (ISO BRM and other)
Some differences appear to be easy to resolve (reference the document/namespace), others will require more work

## Slide 168: DoDAF Services Viewpoint
The DoDAF-described Models within the Services Viewpoint describes services and their interconnections providing or supporting, DoD functions. DoD functions include both mission and business functions. The Service Models associate service resources to the operational and capability requirements. These resources support the operational activities and facilitate the exchange of information.
The relationship between architectural data elements across the Services Viewpoint to the Operational Viewpoint and Capability Viewpoint can be exemplified as services are procured and fielded to support the operations and capabilities of organizations. The structural and behavioral models in the OVs and SvcVs allow architects and stakeholders to quickly ascertain which functions are carried out by humans and which by Services for each alternative specification and so carry out trade analysis based on risk, cost, reliability, etc.
Services are not limited to internal system functions and can include Human Computer Interface (HCI) and Graphical User Interface (GUI) functions or functions that consume or produce service data to or from service functions. The external service data providers and consumers can be used to represent the human that interacts with the service.

## Slide 169: DoDAF Services Viewpoint, cont Possible Model Views
Model | Description
SvcV-1 Services Context Description | The identification of services, service items, and their interconnections.
SvcV-2 Services Resource Flow Description | A description of Resource Flows exchanged between services.
SvcV-3a Systems-Services Matrix | The relationships among or between systems and services in a given Architectural Description.
SvcV-3b Services-Services Matrix | The relationships among services in a given Architectural Description. It can be designed to show relationships of interest, (e.g., service-type interfaces, planned vs. existing interfaces).
SvcV-4 Services Functionality Description | The functions performed by services and the service data flows among service functions (activities). (Note: service de-composition into functions)
SvcV-5 Operational Activity to Services Traceability Matrix | A mapping of services (activities) back to operational activities (activities).
SvcV-6 Services Resource Flow Matrix | It provides details of service Resource Flow elements being exchanged between services and the attributes of that exchange. (Note: Explicitly includes security attributes)
SvcV-7 Services Measures Matrix | The measures (metrics) of Services Model elements for the appropriate timeframe(s).
SvcV-8 Services Evolution Description | The planned incremental steps toward migrating a suite of services to a more efficient suite or toward evolving current services to a future implementation.
SvcV-9 Services Technology & Skills Forecast | The emerging technologies, software/hardware products, and skills that are expected to be available in a given set of time frames and that will affect future service development.
SvcV-10a Services Rules Model | One of three models used to describe service functionality. It identifies constraints that are imposed on systems functionality due to some aspect of system design or implementation. (Note: includes components, interfaces, links, I/O, and state)
SvcV-10b Services State Transition Description | One of three models used to describe service functionality. It identifies responses of services to events.
SvcV-10c Services Event-Trace Description | One of three models used to describe service functionality. It identifies service-specific refinements of critical sequences of events described in the Operational Viewpoint.
Service Model Descriptions