## Slide 1: CSTS Versioning (FF pseudo-RID JPL-PS-3)
12 March 2020
John Pietras
Global Science and Technology, Inc.

## Slide 2: Background (1 of 2)
Each CSTS Specification references the procedures of one and only one version (issue) of the CSTS Specification Framework (SFW)
  References section “boilerplate” has been changed in the FF-CSTS book
    Normally, future versions of all referenced documents are candidates for being used by implementations of the FF service
    The modification of the boilerplate excludes the future versions of the SFW from being used with “this” version of the FF specification: the SFW version cited by a given version of the CSTS specification is the only version that can be used with that CSTS version.
  All CSTS specifications will (eventually) carry this modification of the boilerplate and be constrained to use only the referenced SFW version.
While reviewing the post-Red Book draft of the FF-CSTS book to see how the use of the FF service in support of Delay Tolerant Networking (DTN) was addressed in response to pseudo-RID JPL PS-1, Peter Shames encountered, and subsequently objected to, excluding future versions of the SFW from possible use by future implementations of the B-1 version of the FF service
  After several rounds of correspondence, Mr. Shames understands why this restriction is in place
  However, Mr. Shames is rightfully concerned that when the SFW has multiple versions, any older “active” CSTS specification that references a previous version of the SFW essentially keeps that older version also active
    This is a different paradigm from the current “one Blue (active), possibly multiple Silver versions” approach

## Slide 3: Background (2 of 2)
J. Pietras stated to Mr. Shames his belief that the CSTSWG would update each older CSTS specification as soon as reasonably possible to bring it into compliance with the current version of the SFW
  At any given time, there might be at most a few versions of the SFW that are actively referenced by CSTS Blue Books
  In the (hopefully near) future, updates to the SFW will decrease in frequency, and those updates that do occur will be focused on features (e.g., procedures) needed by new services but that do not affect existing services except superficially)
    Required updates of existing CSTS Blue Books will become infrequent and involve a few changes to reference the latest SFW version
Mr. Shames agreed to drop his objection to the approach only if the CSS CSTS WG makes a commitment to:
  “making sure that this situation is made blazingly clear”, and
  “fixing this at the soonest possible opportunity”
This issue is being carried as Forward Frame CSTS pseudo-RID JPL-PS-3

## Slide 4: “making sure that this situation is made blazingly clear”
Proposal - Add words to the Scope section along the lines of saying that the SFW procedures defined in the specific version of the SFW cited in the References is required, and furthermore state that if and when future versions of the SFW are published “this Recommended Standard” will be updated as necessary to comply with those updated SFW versions
  Proposed by Pietras, acceptable to Shames
(Shames) also address it “where the dependency on the SFW is directly addressed in the body of the standard itself”
  Proposal
    In the requirements of section 3, replace statements along the lines of “The version number of the XYZ procedure shall be the same as the version number of the XYZ procedure from reference [1]” with The version number of the XYZ procedure shall be ABC, indicating that the XYZ procedure specified reference [1] must be used without substitution of any other version of the XYZ procedure.”
    In the tables of section 3, replace the dashes (“-”) in the Version rows with the explicit version numbers from the referenced version of the SFW

## Slide 5: “fixing this at the soonest possible opportunity” (1 of 2)
I have interpreted “fixing this” as updating the MD-CSTS and TD-CSTS as soon as possible to reference SFW-B-2 procedure versions and to use SFW-B-2 definitions and data types (This seems consistent with WG plans)
Alternatively, could we make SFW backward compatible?
  I.e., instead of updating every CSTS specification to use the latest/current SFW version, make every SFW version support all of the features/versions of all previous SFWs
    This would allow any version of a CSTS to be compatible with the latest version of the SFW
  Example:
    SFW-B-1 CCSDS-CSTS-COMMON-TYPES ASN.1 module (no version) defines the Label type as Label ::= SEQUENCE { functionalResourceOrProcedureType CHOICE { functionalResourceType [1] FunctionalResourceType , procedureType [2] ProcedureType } , paramOrEventId PublishedIdentifier }
    SFW-B-2 CCSDS-CSTS-COMMON-TYPES ASN.1 module (version 2) defines the Label type as Label ::= PublishedIdentifier
    E.g., an implementation of MD-CSTS would have to specify whether it used the unversioned Label definition, the version-2 Label definition, or both
    In general, each CSTS specification would have to identify which SFW module version it uses
    This approach would require a considerable reworking of SFW-B-2 to include all features of SFW-B-1

## Slide 6: “fixing this at the soonest possible opportunity” (2 of 2)
Are there any other ways to handle this?
If we adopt the approach by which every existing CSTS specification is updated ASAP to use the latest SFW version, how soon could the MD-CSTS and TD-CSTS be updated to use SFW-B-2?