## Slide 1: Services Supported by Functional Resource Tiers
CSSA Workshop
Cyberspace
26 October 2020
John Pietras
Global Science and Technology, Inc.

## Slide 2: Purpose
To view the current (Tier-1) and possible future tiers from the perspective of which user-visible services are made available by them
This approach may help us decide what should be in Tier-2
There are other FRs that are not mentioned here (e.g., the CCSDS 415 Space Link Carriers)
Red-text color coding for proposed Tier-2 Services and FRs
  a new service
  a new capability of a service that is already supported by Tier-1, and
  An FR that needs to be developed to support the new service or new capability

## Slide 3: Services Supported by Tier-1 (1 of 2)
  F-CLTU (CLTUs can contain TC or VLF USLP frames, or other variable-length SL-PDUs)
  Over TC PLOP, Sync & Channel Encoding, CCSDS 401 Space Link Carrier Xmit, Antenna
  CLTUs can contain TC or VLF USLP frames (other)
  CLCW (RF, bit lock), feedback from TM and AOS return links
    [TM/AOS VC Demux], TM/AOS MC Demux, FLF Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
FF-CSTS
  TC Frames
    Over TC VC Mux, TC MC Mux, TC PLOP, Sync & Channel Encoding, CCSDS 401 Space Link Carrier Xmit, Antenna
    CLCW (RF, bit lock), feedback from TM and AOS return links
      [TM/AOS VC Demux], TM/AOS MC Demux, FLF Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
  AOS Frames
    Over AOS VC Mux, AOS MC Mux, FLF Sync, Channel Encoding and OID Generation, CCSDS 401 Space Link Carrier Xmit, Antenna
    (no CLCW feedback for AOS frames)
  FLF USLP Frames
    Over FLF USLP VC Mux, FLF USLP MC Mux, FLF Sync, Channel Encoding and OID Generation, CCSDS 401 Space Link Carrier Xmit, Antenna
    RF/bit lock CLCW (if available) is assumed to NOT affect FLF USLP frame transmission
  CADUs (CLTUs can contain AOS or FLF USLP frames, or other fixed-length SL-PDUs)
    FLF Sync, Channel Encoding and OID Generation, CCSDS 401 Space Link Carrier Xmit, Antenna
    RF/bit lock CLCW (if available) is assumed to NOT affect FLF USLP frame transmission

## Slide 4: Services Supported by Tier-1 (2 of 2)
RAF
  Online: TM, AOS or FLF USLP frames over FLF Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
  Offline: TM, AOS or FLF USLP frames extracted from Offline Frames Buffer
RCF
  Online: TM, AOS or FLF USLP frames over FLF Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
  Offline: TM, AOS or FLF USLP frames extracted from Offline Frames Buffer
ROCF
  Online: Extracts OCFs from TM, AOS or FLF USLP frames over FLF Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
  Offline: Extracts OCFs from TM, AOS or FLF USLP frames extracted from Offline Frames Buffer
TD-CSTS (real-time raw radiometric data: version 1)
  Online: Over TDM Segment Generation, Antenna, (CCSDS 401 Space Link Carrier Xmit, CCSDS 401 Space Link Carrier Rcpt, Ranging Transmission, and/or Range and Doppler Extraction)
  Offline: TDM Atomic Segments from TDM Recording Buffer
    Structure of the FR definitions
  References
MD-CSTS (version 1)

## Slide 5: Services Proposed for Tier-2 (1 of 4)
  FSP
    Over TC Encap and MAP Pkt Processing, TC MAP Mux, TC Encap, VC Pkt Processing, & VC Generation, TC PLOP, Sync & Channel Encoding, CCSDS 401 Space Link Carrier Xmit, Antenna
  F-CLTU
  CLCW (RF, bit lock), feedback from FLF USLP return links
    FLF MC Demux, FLF Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
  CLCW (RF, bit lock), feedback from VLF USLP return links
    FLF MC Demux, TC Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
FF-CSTS
  VLF USLP Frames
    Over VLF USLP VC Mux, VLF USLP MC Mux, TC PLOP, Sync & Channel Encoding, CCSDS 401 Space Link Carrier Xmit, Antenna
    CLCW (RF, bit lock), feedback from FLF USLP return links
      FLF USLP MC Demux, FLF Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
    CLCW (RF, bit lock), feedback from VLF USLP return links
      VLF USLP MC Demux, TC Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
    NOTE - CLCW (RF, bit lock), feedback from TM and AOS return links is already available, if mixed USLP-xmit / TM/AOS rcpt is envisioned
RAF
  Online: VLF USLP frames over TC Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
  Offline: VLF USLP frames extracted from Offline Frames Buffer

## Slide 6: Services Proposed for Tier-2 (2 of 4)
RAF
  Online: VLF USLP frames over TC Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
  Offline: VLF USLP frames extracted from Offline Frames Buffer
RCF
  Online: VLF USLP frames over TC Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
  Offline: VLF USLP frames extracted from Offline Frames Buffer
ROCF
  Online: Extracts OCFs from VLF USLP frames over TC Sync and Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna
  Offline: Extracts OCFs from VLF USLP frames extracted from Offline Frames Buffer
Delta DOR (raw data collection and transfer)
  Online: D-DOR Raw Data Store, D-DOR Receiver/Formatter, Antenna
  Offline: D-DOR Raw Data Store, TGFT Host

## Slide 7: Services Proposed for Tier-2 (3 of 4)
  Forward CFDP File Service (We need a clear concept of operations)
  TGFT Host, Forward File Data Store, CFDP File Transmission Processng, CFDP Entity over:
    TC Encap & MAP Pkt Processing, TC MAP Mux, TC Encap, VC Pkt Processing & VC Generation, TC VC Mux, TC MC Mux, TC PLOP, Sync & Channel Encoding, CCSDS 401 Space Link Carrier Xmit, Antenna;
    TC Encap, VC Pkt Processing & VC Generation, TC VC Mux, TC MC Mux, TC PLOP, Sync & Channel Encoding, CCSDS 401 Space Link Carrier Xmit, Antenna;
    AOS Encap, VC Pkt Processing & VC Generation, AOS VC Mux, AOS MC Mux, FLF Sync, Channel Encoding and OID Generation, CCSDS 401 Space Link Carrier Xmit, Antenna;
    VLF USLP Encap & MAP Pkt Processing, VLF USLP MAP Mux, VLF USLP Encap, VC Pkt Processing & VC Generation, VLF USLP VC Mux, VLF USLP MC Mux, TC PLOP, Sync & Channel Encoding, CCSDS 401 Space Link Carrier Xmit, Antenna; and
    FLF USLP Encap & MAP Pkt Processing, FLF USLP MAP Mux, FLF USLP Encap, VC Pkt Processing & VC Generation, FLF USLP VC Mux, FLF USLP MC Mux, TC PLOP, Sync & Channel Encoding, CCSDS 401 Space Link Carrier Xmit, Antenna
Return CFDP File Service (We need a clear concept of operations)
  TGFT Host, Return File Data Store, CFDP File Reception Processing, CFDP Entity over:
    TM/AOS Packet Extraction and De-encapsulation, TM/AOS VC Demux, TM/AOS MC Demux, FLF Sync & Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna;
    FLF USLP De-encap & MAP Pkt Extraction, FLF USLP MAP Demux, FLF USLP VC Demux, FLF USLP MC Demux, FLF Sync & Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna; and
    VLF USLP De-encap & MAP Pkt Extraction, VLF USLP MAP Demux, VLF USLP VC Demux, VLF USLP MC Demux, TC Sync & Channel Decoding, CCSDS 401 Space Link Carrier Rcpt, Antenna

## Slide 8: Services Proposed for Tier-2 (4 of 4)
Validated Radiometric Data
  Online: Antenna; Non-Validated Radiometric Data Collection, Non-Validated Radiometric Data Store
  Offline: Validated Radiometric Data Store, TGFT Host