## Slide 1: Options for Dealing with VLF USLP Frames on the Return Link (1 of 3)
Background
  USLP supports variable length frames in either direction, theoretically allowing VLF MCs/VCs on the return link into ESLTs
  Draft RAF, RCF, and ROCF updates already accommodate VLF USLP frames
  The only sync and channel coding (S&CC) Blue Book that is applicable to VLF USLP on the return link into ESLTs is the TC S&CC BB
    Prox-1 does not apply to ESLTs
  Work has begun on the VLF Sync and Channel Decoding FR
    Based on the Receiving End functions of the TC S&CC BB
Delimiting and verifying frames is defined in and allocated to the VLF USLP functions
  The VLF USLP Reception FRs implement these functions
However, SLE Transfer Services (Tses - RAF, RCF, and ROCF) expect to have some level of frame processing performed and the results annotated
  What level of delimiting and verification should be performed by the VLF S&CD FR for use by SLE RAF, RCF, and ROCF?
  The issue is complicated because VLF USLP includes “truncated” frames which require VC-specific information to fully delimit and verify frames

## Slide 2
Options
  Have VLF S&CD FR simply pass along the set of decoded codewords to SLE Tses without further inspection: the user of SLE TS is responsible for frame delimiting and final validity check
    Inherently supports truncated and non-truncated frames
    RCF may erroneously transfer wrong frames due to uncorrected GVCID
    ROCF cannot distinguish between non-truncated frames (which may carry OCFs) and truncated frames (which cannot carry OCFs)
  Have VLF S&CD FR delimit and validate non-truncated frames but simply pass along the set of decoded codewords for truncated frames
    Determination of truncated/non-truncated based on inspection of End of Primary Header Flag bit in decoded “frame” (always in the same location)
    Delimiting of frame from fill based on Frame Length (always in the same location)
    Additional ‘good-truncated’ and ‘erred-truncated’ annotations allow SLE Tses to properly handle the frames
  Do not support truncated frames in VLF S&CD FR for SLE TSes
    Although not formally specified as such, the motivation for the truncated frames is to be able to send low-level commands to spacecraft; presumably there is no use case for truncated frames on the return link
Options for Dealing with VLF USLP Frames on the Return Link (2 of 3)

## Slide 3
Options (concluded)
  Do not define VLF USLP S&CD FR at this time (i.e., for inclusion in Issue 1 of the FRM Magenta Book and the accompanying set of SANA FR definitions
    Although the TC S&CC book is currently the only reference cited for VLF USLP that is applicable to ESLTs, the only known discussions for use of VLF USLP on the return link are in the context of a different (future?) S&CC standard (e.g., optical)
    RAF, RCF, and ROCF sections of the FRM MB would describe the ability to handle VLF USLP as a future capability, implemented when an applicable VLF S&CC FR is developed
John P will add per-VC truncated frame length to the configuration parameter set of the VLF USLP VC Demux Reception FR to support possible future use of that FR by spacecraft
Options for Dealing with VLF USLP Frames on the Return Link (3 of 3)