## Slide 1: Tracking Data Message Pv2.02 CCSDS Real-Time Tracking Data
12 June 2023
Juan Crenshaw
Blue = suggested edits, changes, new content or comments
Red = considerations from feedback

## Slide 2: Agenda
Realtime Tracking data in connection with CCSDS 503.0-B-2
Impacts of CCSDS 503.0-B-2 on real-time TDM support
Proposed updates in support of Realtime TDM
Notes: no implementations of CSTS currently available

## Slide 3: Realtime Tracking data in connection with CCSDS 503.0-B-2
CCSDS Realtime tracking data is currently supported via CCSDS 922.2-B-2 (CROSS SUPPORT TRANSFER SERVICE— TRACKING DATA SERVICE) - https://public.ccsds.org/Pubs/922x2b2.pdf
“The TD-CSTS is a transfer service that allows a spaceflight mission to receive periodic measurements of certain tracking data as soon as they are generated by a Cross Support Complex or anytime thereafter.”
“The TD-CSTS delivers the tracking data as a periodic sequence of data segments formatted in accordance with components of a CCSDS Tracking Data Message (TDM), as specified in the TDM Recommended Standard (reference [3]).”  CCSDS 503.0-B-2

## Slide 4: Impacts of CCSDS 503.0-B-2 on real-time TDM support
Section 1.3: “NOTE – However, the TDM that results from transfer via the TD-CSTS will likely be larger than a TDM that contains the same information but that is generated at a single time (i.e., after the conclusion of the tracking pass) because the transfer of TDM data via the TD-CSTS involves the repetition of metadata with every tracking data measurement in order to facilitate the incremental transfer of tracking data in near real time.”
1.6.1.8 Terms Defined in This Specification: “TDM atomic segment: a TDM Segment (i.e., Metadata Section and Data Section), constrained to contain a single tracking data measurement and its associated metadata.”
Section 2.1: “NOTE – Even though the complete data delivery mode can be used to deliver the tracking data measurements a significant time after they were observed, the complete data delivery mode still delivers the measurements formatted as though they were to be transferred in real time, i.e., not formatted as a TDM file, which would avoid the overhead caused by the metadata sent for each tracking data measurement (see also the NOTE in 1.3).”

## Slide 5: Real-Time Data Updates for TDM format. Considering to Add to 503v2.02 pink book
Real-Time data with current TDM format requires inclusion of Header and Metadata for every data point or section of data transmitted
  Lots of overhead
Potential Implementation Solution
  Utilize TRACK_ID (include text describing TRACK_ID)
  Each atomic segment identifies applicable TRACK_ID, with no need to repeat all the metadata information.
  A new TRACK_ID_SEGMENT keyword could also be used to index messages
    Erik: CSTS has package count functionality. CSSM provides an analogous to track ID (service package identifier) – Need to look
    Holger: functionality already captured by CSTS sequence counter
    Erik: could be optional and not used for CSTS. Would it be useful for other implementations?
  What other information in the KVN or XML would need to be repeated?
This could apply to CSTS TRACKING DATA SERVICE, CCSDS 922.2
It could also apply to other means of real-time tracking implementations

## Slide 6: Real-Time Data Example CCSDS 922.2-B-2 Sections B2, B3 no edits
CCSDS_TDM_VERS = 1.0
CREATION_DATE = 2007-075T11:42:28.000
ORIGINATOR = JPL
META_START
TIME_SYSTEM = UTC
START_TIME = 2007-075T11:50:43.000
STOP_TIME = 2007-075T11:50:53.000
PARTICIPANT_1 = DSS-26
MODE = SEQUENTIAL
TRANSMIT_BAND = X
META_STOP
DATA_START
TRANSMIT_FREQ_1 = 2007-075T11:50:43.000 7175510611.700343
DATA_STOP
Would removing the need to repeat the Metadata with every atomic segment be beneficial?
META_START
TIME_SYSTEM = UTC
START_TIME = 2007-075T11:50:43.000
STOP_TIME = 2007-075T11:50:43.000
PARTICIPANT_1 = DSS-26
MODE = SEQUENTIAL
TRANSMIT_BAND = X
META_STOP
DATA_START
TRANSMIT_FREQ_RATE_1 = 2007-075T11:50:43.000 0.0
DATA_STOP
META_START
TIME_SYSTEM = UTC
START_TIME = 2007-075T11:50:48.000
STOP_TIME = 2007-075T11:50:48.000
PARTICIPANT_1 = DSS-26
MODE = SEQUENTIAL
TRANSMIT_BAND = X
META_STOP
DATA_START
TRANSMIT_FREQ_1 = 2007-075T11:50:48.000 7175510611.700343
DATA_STOP
META_START
TIME_SYSTEM = UTC
START_TIME = 2007-075T11:50:48.000
STOP_TIME = 2007-075T11:50:48.000
PARTICIPANT_1 = DSS-26
MODE = SEQUENTIAL
TRANSMIT_BAND = X
META_STOP
DATA_START
TRANSMIT_FREQ_RATE_1 = 2007-075T11:50:48.000 0.0
DATA_STOP
META_START
TIME_SYSTEM = UTC
START_TIME = 2007-075T11:50:43.000
STOP_TIME = 2007-075T11:50:53.000
PARTICIPANT_1 = DSS-26
PARTICIPANT_2 = XENOSAT
MODE = SEQUENTIAL
PATH = 1,2,1
INTEGRATION_REF = START
RANGE_MODE = COHERENT
RANGE_MODULUS = 2.0e+26
RANGE_UNITS = km
META_STOP
DATA_START
RANGE = 2007-075T11:50:43.000 80452.7025
DATA_STOP
META_START
TIME_SYSTEM = UTC
START_TIME = 2007-075T11:50:53.000
STOP_TIME = 2007-075T11:50:53.000
PARTICIPANT_1 = DSS-26
MODE = SEQUENTIAL
TRANSMIT_BAND = X
META_STOP
DATA_START
TRANSMIT_FREQ_1 = 2007-075T11:50:53.000 7175510611.700343
DATA_STOP
META_START
TIME_SYSTEM = UTC
START_TIME = 2007-075T11:50:53.000
STOP_TIME = 2007-075T11:50:53.000
PARTICIPANT_1 = DSS-26
MODE = SEQUENTIAL
TRANSMIT_BAND = X
META_STOP
DATA_START
TRANSMIT_FREQ_RATE_1 = 2007-075T11:50:53.000 0.0
DATA_STOP

## Slide 7: Real-Time Data Example CCSDS 922.2-B-2 Sections B2, B3 with changes in TDM format
CCSDS_TDM_VERS = 2.0
CREATION_DATE = 2007-075T11:42:28.000
ORIGINATOR = JPL
META_START
TRACK_ID = 2007-0075_TxFreq-0001
TIME_SYSTEM = UTC
START_TIME = 2007-075T11:50:43.000
STOP_TIME = 2007-075T11:50:43.000
PARTICIPANT_1 = DSS-26
MODE = SEQUENTIAL
TRANSMIT_BAND = X
META_STOP
DATA_START
TRANSMIT_FREQ_1 = 2007-075T11:50:43.000 7175510611.700343
DATA_STOP
META_START
TRACK_ID = 2007-0075_TxFreq-0001
TRACK_ID_SEGMENT = 2
META_STOP
DATA_START
TRANSMIT_FREQ_RATE_1 = 2007-075T11:50:43.000 0.0
DATA_STOP
META_START
TRACK_ID = 2007-0075_TxFreq-0001
TRACK_ID_SEGMENT = 3
META_STOP
DATA_START
TRANSMIT_FREQ_1 = 2007-075T11:50:48.000 7175510611.700343
DATA_STOP
META_START
TRACK_ID = 2007-0075_TxFreq-0001
TRACK_ID_SEGMENT = 4
META_STOP
DATA_START
TRANSMIT_FREQ_RATE_1 = 2007-075T11:50:48.000 0.0
DATA_STOP
META_START
TRACK_ID = 2007-0075_Range-0001
TIME_SYSTEM = UTC
START_TIME = 2007-075T11:50:43.000
STOP_TIME = 2007-075T11:50:53.000
PARTICIPANT_1 = DSS-26
PARTICIPANT_2 = XENOSAT
MODE = SEQUENTIAL
PATH = 1,2,1
INTEGRATION_REF = START
RANGE_MODE = COHERENT
RANGE_MODULUS = 2.0e+26
RANGE_UNITS = km
META_STOP
DATA_START
RANGE = 2007-075T11:50:43.000 80452.7025
DATA_STOP
META_START
TRACK_ID = 2007-0075_TxFreq-0001
TRACK_ID_SEGMENT = 5
META_STOP
DATA_START
TRANSMIT_FREQ_1 = 2007-075T11:50:53.000 7175510611.700343
DATA_STOP
META_START
TRACK_ID = 2007-0075_TxFreq-0001
TRACK_ID_SEGMENT = 6
META_STOP
DATA_START
TRANSMIT_FREQ_RATE_1 = 2007-075T11:50:53.000 0.0
DATA_STOP
META_START
TRACK_ID = 2007-0075_Range-0001
TRACK_ID_SEGMENT = 2
META_STOP
DATA_START
RANGE = 2007-075T11:50:53.000 80492.4025
DATA_STOP
TRACK_ID is an existing keyword
Should TRACK_ID_SEGMENT functionality be addressed externally (e.g. SLE?
Erik: Track_ID would need to resolve with service management.
Erik: Working out cloud computing algorithms that address this. Would need to verify if this would be helpful.
Dave: Question, how are credentials addressed: Credentials worked out a priori.
Erik: Would like to run this through Holger Dreihahn
TD-CTTS had a recent update (February 2023)