Terminology: MAL and AMS

(INFORMATIVE)

The CCSDS Asynchronous Message Service (AMS) specification and Message Abstraction Layer (MAL) specification are both concerned with message exchange in CCSDS communication environments.  They differ in that MAL defines the required service capabilities for Mission Operations message exchange in an abstract manner, which could be satisfied by any number of properly configured message exchange protocols, while AMS defines one particular, concrete message exchange protocol that can be used to implement MAL among other message exchange models.  Since MAL and AMS were developed independently and for different purposes, and since both address some operational concerns for which there is no well-established standard technical terminology, the two specifications discuss some common concepts in sometimes divergent language.  This Annex aligns key elements of MAL and AMS terminology.

Note that this Annex is strictly informative, with no normative significance.  Remarks regarding deployment or implementation of these specifications are merely suggestions offered to illustrate these notes on terminology alignment.

Component v. module

MAL components are true components as defined in the ECOOP 96 definition of a software component: “A software component is a unit of composition with contractually specified interfaces and explicit context dependencies only. A software component can be deployed independently and is subject to composition by third parties.”  In particular, the interface definitions of components advertise specific processing services.

The communicating entities in AMS include both entities that exchange application data, which are termed modules, and “infrastructure” entities (configuration servers and registration servers) that only exchange AMS configuration data.  The AMS infrastructure entities have no MAL equivalents, but an AMS module has a component-like nature in that it interacts with other modules by exchanging application data messages rather than by implicit effects on shared context.  However, a properly formed component must satisfy requirements that are a good deal more stringent than those that an AMS module must satisfy: any process/task/thread can be a full-fledged AMS module, even if it lacks the formally published interface of a true software component.

That is, any MAL component could function as an AMS module, but not all AMS modules are components.

Message

Both MAL and AMS regard a message as a unit of information that is passed between two communicating entities (components or modules) to accomplish some operations of a service or application.

Continuum v. network zone

The AMS term continuum and the MAL term network zone both identify a set of communicating entities (components or modules) that are in generally close physical proximity to one another.  As a rough rule of thumb, by “close physical proximity” we typically mean that the signal propagation delay between any two communicating entities is no more than one second.  When AMS is used to implement MAL, it will likely makes sense to implement each MAL network zone as a single AMS continuum.

Venture v. session v. domain v. unit

AMS ventures are exactly like MAL sessions in that they are parallel message-exchange universes that exist concurrently.

AMS units are exactly like MAL domains in that they provide a hierarchical organizational structure that is used to scope the frame of reference of message exchange.

An AMS unit is a subset of a venture.  A venture may be wholly contained within a single continuum, may be coterminous with a continuum, or may span several continua, in exactly the way that a MAL domain may be wholly contained within a single network zone, may be coterminous with a network zone, or may span several network zones.

Note, though, that the “root unit” of an AMS venture is coterminous with the venture itself – in effect, an organizational view of the same set of nodes for which the venture is an operational view.

This correspondence explains why a top-level MAL “domain” looks like a venture, in addition to looking like a unit: it functions in the MAL model both as the venture and also as the root unit of that venture.

Cell v. sub-domain

By alluding to the concept of a “top-level” domain we implicitly introduce the MAL concept of a sub-domain.  A sub-domain is an organizational subdivision of a domain.  A sub-domain that resides wholly within some single network zone would in AMS be termed a cell, which is that portion of a unit that resides wholly within some single continuum.  If that unit happens to be the root unit, which is coterminous with the entire venture, then the cell is referred to as the “root cell”.  The root cell is coterminous with what AMS calls a message space – that portion of a venture that resides wholly within some single continuum.  Again, the difference between a root cell and a message space is simply one of perspective, organizational versus operational.

Remarks

In MAL terms, a Message belongs to a Session, originates from a Network Zone, and is concerned with a particular Domain.

Similarly, in AMS terms, a Message belongs to a Venture, originates from a Continuum, and is concerned with a particular Unit.  More precisely, a message is issued by a module in one unit of a venture, residing in some continuum, and is destined for another module in some unit (the same unit or another) of the same venture – possibly in another continuum.

In exactly the same way that a MAL subscription is restricted to a single Session, an AMS subscription is restricted to a single Venture (characterized by explicit authority ID – the “operational scenario” that characterizes a MAL session – and also by application ID, which in MAL is implicit).

And in the same way that a MAL subscription is additionally restricted to a specific Domain, an AMS subscription is additionally restricted to a single Unit (which may be the root unit, in which case the restriction is moot).  Network zone has no effect on a MAL subscription just as continuum has no effect on an AMS subscription.

Differences

So here are the differences between AMS terminology and AMS terminology:

- MAL components advertise services, which are invisible to AMS, because MAL is component-oriented and AMS is not.  Any MAL component might be an AMS module, but not all AMS modules are required to be well-formed components.

- AMS draws an explicit distinction between a venture and its root unit, a distinction that has not been needed in MAL.

- AMS identifies the concepts “message space” and “cell”, which have not been needed in MAL.