Draft Recommendation for
Space Data System Standards

Open Archival Information System Interoperability Framework (OAIS-IF) Architecture Description

PROPOSED Draft Recommended Standard

CCSDS 671.0-W-0

Blue Book

May 2019

AUTHORITY

|  | Issue: | Blue Book, Issue 0 |  |
| --- | --- | --- | --- |
|  | Date: | May 2019 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the e-mail address below.

This document is published and maintained by:

CCSDS Secretariat

National Aeronautics and Space Administration

Washington, DC, USA

E-mail: secretariat@mailman.ccsds.org

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommendations and are not in themselves considered binding on any Agency.

CCSDS Recommendations take two forms: Recommended Standards that are prescriptive and are the formal vehicles by which CCSDS Agencies create the standards that specify how elements of their space mission support infrastructure shall operate and interoperate with others; and Recommended Standards that are more descriptive in nature and are intended to provide general guidance about how to approach a particular problem associated with space mission support. This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommended Standard is entirely voluntary and does not imply a commitment by any Agency or organization to implement its recommendations in a prescriptive sense.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member Standards and implementations are not negated or deemed to be non-CCSDS compatible. It is the responsibility of each member to determine when such Standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new Standards and implementations towards the later version of the Recommended Standard.

FOREWORD

This document is a draft technical Recommended Standard for use in developing and maintaining broader consensus on what is required for an archive to provide permanent, or indefinite long term, preservation of digital information.

This draft Recommended Standard establishes a framework of specifications that forms the basis for the Open Archival Information System (OAIS) Interoperability Framework (IF).  OAIS is a long-established Process Framework to enable digital preservation in trustworthy archives.  The OAIS-IF supplements OAIS with interoperable technical specifications that will allow interoperability between users and multiple archives, and between multiple archives.  The OAIS-IF is not required for an archive to cite compliance with OAIS.

OAIS provides a basis for further standardization within an archival context.  OAIS-IF is an example of that further standardization.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be sent to the CCSDS Secretariat at the e-mail address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- Electronics and Telecommunications Research Institute (ETRI)/Korea.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘White Book’ status indicates that the document is under active development by the responsible CCSDS Working Group. It may be technically immature and has not yet been released for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response as it is being developend.

Once this document becomes mature and is released for formal review, it will contain the following statement.

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

# DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 671.0-W-0 | Open Archival Information System Interoperability Framework (OAIS-IF) Architecture Description, Proposed Draft Recommended Standard, Issue 0 | May 2019 | Current proposed draft |

# TABLE OF CONTENTS

Section	Page

DOCUMENT CONTROL	viii

TABLE OF CONTENTS	ix

TABLE OF FIGURES	x

1	Introduction	1-1

1.1	PURPOSE AND SCOPE	1-1

1.2	APPLICABILITY	1-1

1.3	OAIS-IF Stakeholders	1-2

1.4	RATIONALE	1-3

1.5	CONFORMANCE	1-3

1.6	DOCUMENT STRUCTURE	1-4

1.6.1	Organization by Section	1-4

1.6.2	Typographical Conventions	1-5

1.7	DEFINITIONS	1-5

1.7.1	Acronyms and abbreviations	1-5

1.7.2	Terminology	1-6

1.8	References	1-7

2	Overview	2-1

2.1	OAIS Interoperability Framework (OAIS-IF)	2-1

2.2	OAIS Functional Entity	2-2

2.3	Derived Interface	2-7

2.4	OAIS ApplicationS	2-7

3	Interoperability Framework	3-9

3.1	Software and Services Architecture	3-9

3.1.1	Registry	3-9

3.1.2	Repository	3-13

3.1.3	Method	3-14

3.1.4	Method Signature	3-21

3.1.5	Binding	3-27

3.2	Information Architecture	3-27

3.2.2	Information Model	3-27

3.2.3	Data_Structure	3-45

# TABLE OF FIGURES

Figure 1 - OAIS Environment	2-2

Figure 2 - OAIS Functional Entities	2-3

Figure 3 - Access Fuctional Entity	2-4

Figure 4 - Archival Storage Functional Entity	2-5

Figure 5 - Ingest Functional Entity	2-6

Figure 6 - Registry Hierarchy	3-9

Figure 7 - Repository and Registry Object	3-13

Figure 8 - Services	3-14

Figure 9 - Archive Abstraction Layer	3-15

Figure 10 - OAIS Interoperability Framework Information Model	3-29

Figure 11- OAIS Information Model	3-30

Figure 12 - regObjFileURIStatArrList	3-42

Figure 13 - regObjPIDStatArrList	3-43

# Introduction

## PURPOSE AND SCOPE

The purpose of this document is to define the CCSDS and International Organization for Standardization (ISO) Open Archival Information System (OAIS) Interoperability Framework (IF).  An OAIS is an Archive, consisting of an organization, which may be part of a larger organization, of people and systems, that has accepted the responsibility to preserve information and make it available for a Designated Community.  The OAIS-IF is a supplement to that overarching standard that adds capabilities for system interoperability between users and archives, and between coordinating archives.  This document outlines a data system architectural approach and a set of specifications for interfaces that will be defined in additional subordinate standards to be issued subsequently.  This standard is the Architecture Description document that sets the overall architectural framework for the OAIS-IF suite of standards.

The OAIS-IF is an implementable framework for digital repositories that enables international and collaborative research.  Its aim is to provide a set of interoperable protocols and interface specifications that will enable the access, merging, and re-use of the data, both within and across the operational boundaries of trusted digital repositories. The framework will also provide support for the fundamental scientific technique of checking the reproducibility of results.  The OAIS-IF is designed to be effectively applied broadly across a spectrum of small, medium, and large use cases and involving a wide variety of stakeholders.

Implementers and system developers that plan to develop systems compliant with the OAIS-IF suite of standards should have a solid grasp of the precepts, concepts and terminology of the Reference Model for an OAIS as described in CCSDS 650.0-M-2 (reference [TBD]).

At least some of the information being maintained in these Archives has been deemed to need Long Term Preservation, even if the OAIS itself is not permanent. Long Term is long enough to be concerned with the impacts of changing technologies, as well as support for new media and data formats, or with a changing Knowledge Base of the Designated Community or changes within the Designated Community or its definition.  Long Term may extend indefinitely.  Further treatment of the scope of Long Term preservation is in the RM for OAIS, CCSDS 650.0-M-2 (reference [TBD]}.-

## APPLICABILITY

Like the OAIS Reference Model in CCSDS 650.0-M-2, this document may be applicable to any Archive that complies with that OAIS standard.  It is specifically applicable to organizations with the responsibility of making information available for the Long Term.  This includes organizations with other responsibilities, such as processing and distribution in response to programmatic needs.

This architecture is specifically designed to supplement OAIS Archives.  However, this architecture or components of it may be used by archives that are partially or fully non-compliant to the Reference Model for OAIS.    It is hoped that in these cases use of the OAIS-IF will encourage greater adoption of the RM for OAIS as archives learn the value of the OAIS practices that enable truly trustworthy Archives for preserving valuable information.

It is intended that the functionality and components in OAIS-IF will exactly mirror the content of the RM for OAIS.  However, since these are two separate documents with updates released at different times and different approval cycles, it may be that new functions can be added to OAIS-IF that are not yet in the RM for OAIS.  Likewise, there may be new functions in OAIS that are not yet in the OAIS-IF.  The intention is to keep the OAIS RM practice and the OAIS-IF specification as closely aligned as possible.  However, perfect alignment may not be possible at every given point in time.

These specifications, including the functional and information modeling concepts, are relevant to the comparison and design of facilities which hold information, on a temporary basis, for three reasons:

- When taking into consideration the rapid pace of technology changes or possible changes in a Designated Community, there is the likelihood that facilities, thought to be holding information on a temporary basis, will in fact find that some or much of their information holdings will need Long Term Preservation attention.  Stable OAIS-IF standards will help abate the disruption of technology changes.

- Although some facilities holding information may themselves be temporary, some or all of their information may need to be preserved indefinitely.  Such facilities need to become active participants in the Long Term Preservation effort and adoption of OAIS-IF will facilitate that transition.

- Regardless of preservation objectives, this architecture enables interoperability for efficiency benefits, preservation benefits, and cross-discipline research  benefits.

## OAIS-IF Stakeholders

In a broad sense, OAIS-IF has applicability to the following stakeholders.  This is not an exclusive list, but is intended to illustrate how the document should be of interest to key organization participants.

- Any organization who has implemented or plans to implement an OAIS-compliant system.  Not all OAIS-compliant systems will have OAIS-IF capabilities.  Indeed, as this first version of OAIS-IF is released, none of the OAIS systems in the world will be OAIS-IF compliant.  But OAIS implementers should evaluate the benefits to themselves and their customers from implementing an OAIS-IF compliant interoperable archive.  Therefore, they have a stake in OAIS-IF.

- Managers, who we assume are key decision makers and determine technology adoption and use. We use the Manager stakeholder broadly for anyone with management responsibility across procurement, development and/or operations.

- Application Software Developers, who are those responsible for providing software at an application level (i.e. software implementing any of the six functional entities1 of an OAIS). Application software is likely to be repository-specific.

- Infrastructure Software Developers, who are those responsible for providing the underlying software framework or environment which may be used by application software developers. This software is much less likely to be repository specific. The distinction between application and infrastructure is not necessarily exact but the separation from application software is useful in identifying the parts of OAIS-IF that form part of the underling infrastructure and are more likely to be reused from repository to repository.

## RATIONALE

The rationale for OAIS and the Reference Model for OAIS is captured in CCSDS 650.0-M-2.

The rationale for the OAIS Interoperability Framework includes the rationale for OAIS (not repeated here) because it supports OAIS by augmenting it with capabilities for interoperability.

The rationale and vision for OAIS-IF is that in the long-range future it will provide:

- A common user interface experience for users (providers and consumers) of OAIS archives when accessing many diverse kinds of OAIS-IF archives.

- An efficient standardized way for archives to exchange data between archives using the same standardized OAIS-IF interfaces.

- Given broad acceptance of OAIS-IF in the OAIS community, a better chance that long-term preservation will work because future generations can easily find the interfacing resources (plug-ins, etc.) that can be used to access legacy archives.

- Enhanced capabilities for cross-discipline research when many different disciplines use the same interface, and access to a new archive outside of your Designated Community can be accomplished via OAIS-IF.

## CONFORMANCE

An Archive may conform to the Reference Model for OAIS without conforming to the OAIS-IF.

An OAIS archive that also conforms to OAIS-IF must implement the normative sections of this document, namely sections 3 and 4.

While the OAIS Reference Model does not define or require any particular method of implementation, the OAIS-IF must necessarily bound some implementation options in order to insure interoperability.  However, the goal of OAIS-IF is to only limit implementation options necessary for interoperability.  This is intended to restrict implementation at the interface of systems, but those interfaces are usually characterized to support underlying functionality as required by the OAIS Reference Model.  Therefore the definitions at the interfaces and protocols may necessarily imply some underlying functionality as part of the OAIS-IF suite of standards.

A conformant OAIS-IF Archive may provide additional services that are beyond those required of the OAIS-IF standards.

This document does not assume or endorse any specific computing platform, system environment, system design paradigm, system development methodology, database management system, database design paradigm, data definition language, technology, or media required for implementation.

The OAIS-IF is designed as an implementation framework to support the development of interoperability in OAIS Archives.  As such, it attempts to address all the major activities of an interoperable information-preserving Archive in order to define a consistent and useful set of interoperability terms and concepts.  A standard or other document that claim to be conformant to the OAIS-IF shall use the terms and concepts defined in the OAIS-IF in the same manner.

## DOCUMENT STRUCTURE

### Organization by Section

A general description of this document’s sections are:

- Section 1 Purpose and Scope describes the problem space and rationale for OAIS-IF, and advice on what to expect from the document organization and conventions.

- Section 2 Overview provides an informative (non-normative) explanation of the relationships between OAIS-IF components and between them and the environment..

- Section 3 Interoperability Framework is a normative description of the requirements on the components of an OAIS-IF architecture.  It presents the technical concepts that OAIS-IF uses in order to perform the functions of an OAIS in an interoperable way.

- (Add explanation of annexes once they are solidified)

This document begins with a description of the context for the creation of OAIS-IF in the form of the motivation and rationale for the framework.   Further sections in this document then offers greater levels of detail about OAIS-IF generated directly from a formal model of the OAIS-IF. This detailed information is presented using the object-oriented paradigm. Each class, attribute, and relationship is formally defined using text and UML diagrams. It is anticipated that these sections will be primarily applicable to system developers but will be of interest to other stakeholders.

It is expected that after this document is approved and published by CCSDS, the model will be made available online by CCSDS.  This should be a valuable aid to system developers of OAIS-IF systems.

### Typographical Conventions

There are many terms which are used in this framework and which need to have well-defined meanings. These terms are defined in subsection 1.6.2.  When first used in the text, they are shown in bold and are capitalized.  Subsequent use employs capitalization only.  Because of their extensive use in this document, the defined terms ‘data’ and ‘information’ will not always be capitalized unless they are part of another defined term. The defined term ‘archive’ will not be capitalized unless it is used as the equivalent of an ‘OAIS Archive’.

## DEFINITIONS

### Acronyms and abbreviations

AIC	Archival Information Collection

AIP	Archival Information Package

AIU	Archival Information Unit

API	Application Programming Interface

ASCII	American Standard Code for Information Interchange

CCSDS	Consultative Committee for Space Data Systems

CD-ROM	Compact Disk - Read Only Memory

CDO	Content Data Object

CRC	Cyclic Redundancy Check

CSV	Comma Separated Value

DBMS	Data Base Management System

DIP	Dissemination Information Package

DRM	Digital Rights Management

FITS	Flexible Image Transport System

FTP	File Transfer Protocol

HFMS	Hierarchical File Management System

IEEE	Institute of Electrical and Electronics Engineers

IETF	Internet Engineering Task Force

ISBN	International Standard Book Number

ISO	International Organization for Standardization

MPEG	Moving Picture Experts Group

OAIS	Open Archival Information System

OAIS-IF	Open Archival Information System Interface Framework

PDF	Portable Document Format

PDI	Preservation Description Information

QA	Quality Assurance

RFC	Request For Comment

RM	Reference Model

SIP	Submission Information Package

UML	Unified Modeling Language

VHS	Video Home System

WWW	World Wide Web

XFDU	XML Formatted Data unit

XML	eXtensible Markup Language

### Terminology

There are many terms which are used in this standard and which need to have well-defined meanings. These terms are defined in this subsection.  When first used in the text, they are shown in bold and are capitalized.  Subsequent use employs capitalization only.

As in RM-OAIS, this standard is applicable to all disciplines and organizations that do, or expect to, preserve and provide information in digital form, these terms cannot match all of those familiar to any particular discipline (e.g., traditional archives, digital libraries, science data centers).  Rather, the approach taken is to use terms that are not already overloaded with meaning so as to reduce conveying unintended meanings.  Therefore, it is expected that all disciplines and organizations will find that they need to map some of their more familiar terms to those of the OAIS Reference Model and OAIS-IF.  This should not be difficult and is viewed as a contribution, rather than a deterrent, to the success of these standards.  For example, archival science focuses on preservation of the ‘record’.  This term is not used in these standards, but one mapping might approximately equate it with ‘Content Data Object within an Archival Information Package’.

TERMS TO BE SUPPLIED (Probably after current OAIS Red Book is published)

## References

The following publications contain provisions which, through reference in this text, constitute provisions of this document. At the time of publication, the editions indicated were valid. All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below. The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[Only references required as part of the specification are listed in the References subsection. See CCSDS A20.0-Y-4, CCSDS Publications Manual (Yellow Book, Issue 4, April 2014) for additional information on this subsection.]

Reference Model for an Open Archival Information System (OAIS). Magenta Book. CCSDS 650.0-M-2 Issue 2. June 2012.  (to be changed to Issue 3 when issue 3 is released)

OTHER REFERENCES TO BE SUPPLIED

# Overview

The following concepts set the context for the normative definitions starting in section 3.

## OAIS Interoperability Framework (OAIS-IF)

An Archive is an organization that intends to preserve information for access and use by a Designated Community.

An Open Archival Information System (OAIS) is an Archive, consisting of an organization, which may be part of a larger organization, of people and systems, that has accepted the responsibility to preserve information and make it available for a Designated Community. It meets a set of responsibilities that allows an OAIS Archive to be distinguished from other uses of the term ‘Archive’.

The OAIS Interoperability Framework (OAIS-IF) is a framework based on the concepts presented in the OAIS Reference Model (RM) and augmented with additional features. The OAIS-IF is designed to be implementable and is an interoperable framework that fosters the acquisition, stewardship, and continuing access to data products, related information resources, and services for a designated community.

The environment surrounding an OAIS includes Management, Consumers, and Producers. The resulting environment of the OAIS-IF is illustrated in figure 1.

Figure 1 - OAIS Environment

Management is the role played by those who set overall OAIS policy as one component in a broader policy domain, for example as part of a larger organization.

Producer is the role played by those persons or client systems that provide the information to be preserved. This can include other OAISes or internal OAIS persons or systems. A Producer creates a Submission Information Package (SIP) and submits it to the Archive where it is processed into an Archival Information Package (AIP).

A Consumer is the role played by those persons, or client systems, who interact with OAIS services to find preserved information of interest and to access that information in detail. A consumer receives a Dissemination Information Package (DIP) from the Archive.

## OAIS Functional Entity

Within an OAIS (archive), an OAIS Functional Entity is an entity responsible for a function that is required to ensure the reliable operation of a specific part of an Open Archive Information System (OAIS). The OAIS functional entities include Access, Administration, Archival Storage, Data Management, Ingest, and Preservation Planning. The OAIS Interoperability Framework, being based on the OAIS model, has two additional functional entities the Archive Abstraction Layer and the Analytics Platform. This is shown in figure 2. All of these Functional Entities will be described below and will be further decomposed in figures below.

Figure 2 - OAIS Functional Entities

The Access Functional Entity (aka Access) contains the services and functions which make the archival information holdings and related services visible to Consumers. Access generates and provides a DIP to a Consumer, produces a Query Response for a Consumer, and provides Report Assistance to a Consumer.

Figure 3 - Access Fuctional Entity

The Administration Functional Entity (aka Administration) contains the services and functions needed to control the operation of the other OAIS functional entities on a day-to-day basis. For Consumers and Producers Administration sends Information Requests, Bills and Special Request Responses to Consumers.  Final Ingest Report and possible liens are sent to a Producer.

The Archival Storage Functional Entity (aka Archival Storage) contains the services and functions used for the storage and retrieval of Archival Information Packages.

Figure 4 - Archival Storage Functional Entity

The Data Management Functional Entity (aka Data Management) contains the services and functions for populating, maintaining, and accessing a wide variety of information. Some examples of this information are catalogs and inventories on what may be retrieved from Archival Storage, processing algorithms that may be run on retrieved data, Consumer access statistics, Consumer billing, Event Based Orders, security controls, and OAIS schedules, policies, and procedures.

The Ingest Functional Entity (aka Ingest) contains the services and functions that accept Submission Information Packages from Producers, prepares Archival Information Packages for storage, and ensures that Archival Information Packages and their supporting Descriptive Information become established within the OAIS. Ingest sends Receipt Confirmation to a Producer.

Figure 5 - Ingest Functional Entity

The Preservation Planning Functional Entity (aka Preservation Planning) provides the services and functions for monitoring the environment of the OAIS and provides recommendations and preservation plans to ensure that the information stored in the OAIS remains accessible to, and understandable by, and sufficiently usable by, the Designated Community over the Long Term, even if the original computing environment becomes obsolete. Preservation Planning surveys a Consumer and surveys a Producer.

The Archive Abstraction Layer Functional Entity (aka) provides a mapping and possible translation between an object in an OAIS AIP and an object in a non-conforming information package. For example a user asking for Provenance Information as defined for an OAIS AIP would receive information about a derived product, the source products, and processing software that was grouped and classified as processing history in a non-AIP information package. This is of course if the Archive Abstraction Layer had definitions of the two information packages, how their components were related, and how to translate from one to the other if needed.

The Analytical Platform is a unified data analysis solution designed to address the demands of users beyond the data management infrastructure necessary for maintaining a long-term trusted digital repository. In general it provides contextual analyzed data from across the repository and joins different tools for creating analytics systems.

## Derived Interface

Derived Interfaces are interfaces that are derived from relationships between OAIS Producers, Consumers, and Functional Entities. The following interfaces have been identified

- Access_generates_DIP_for_Consumer

- Access_produces_Query_Response_for_Consumer

- Report_to_Producer

- Administration_sends_Information_Requests_to_Consumers

- Administration_sends_Lien_to_Producer

- Response_to_Consumers

- Consumer_Interface

- Consumer_makes_Payment_to_Administration

- Consumer_makes_Special_Service_Request_to_Administration

- Consumer_submits_Service_Requirements_to_Preservation_Planning

- Consumer_submits_a_Query_Request_to_Access

- Consumer_submits_a_Report_Request_to_Access

- Consumer_submits_an_Order_Assistance_Request_to_Access

- Ingest_sends_Receipt_Confirmation_to_Producer

- Ingest_sends_Resubmit_Request_to_Producer

- Preservation_Planning_surveys_Consumers

- Preservation_Planning_surveys_Producers

- Producer_proposes_Product_Technologies_to_Preservation_Planning

- Producer_provides_a_Submission_Interface_Package_to_the_Ingest_Functional_Entity

## OAIS ApplicationS

An Application is a computer program designed to perform a group of coordinated functions, tasks, or activities for the benefit of the user. Many of these applications are services, software components that performs work that benefits another. In a service-oriented architecture (SOA) a service is a style of software design where services are provided to the other components by application components, through a communication protocol over a network. The basic principles of service oriented architecture are independent of vendors, products and technologies.

The OAIS Applications are computer programs written for each of the OAIS’s Functional Entities outline in the previous section, for OAIS Consumers or Producers, or for OAIS system services.

The Producer Application class includes applications for users acting as a producer for a data archive. The Consumer Application class includes applications for users acting as a consumer of a data archive

An Access Aid is a software program or document that allows Consumers to locate, analyze, order or retrieve information from an OAIS. A Finding Aid is a type of Access Aid that allows a user to search for and identify Archival Information Packages of interest.  An Ordering Aid is an application that assists the Consumer in discovering the cost of, and in ordering, AIPs of interest. A Retrieval Aid is an application that allows authorized users to retrieve the Content Information and PDI described by the Package Description.

A Harvester is a software tool used for extracting data from digital files for use by a search platform.

A Search Platform, also often called a Search Engine is a tool that provides a search capability that typically includes features such as full-text search, faceted search, database integration, and rich document (e.g., Word, PDF) handling. Its operations include the indexing of documents into a machine-readable format, the parsing of user queries, the mapping the of user queries to ingested documents to find the appropriate result, and ranking the outcome as per relevance.

TBD…

# Interoperability Framework

## Software and Services Architecture

The Software and Services Architecture consists of the software, services (methods), and protocols.

### Registry

A Registry maintains a record of objects.

#### Annotation_Registry

Annotation_Registry: A registry for evaluations of the quality of a data collection.

- Subclass of: Registry

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

#### Authentication_Registry

Authentication_Registry: A registry for authentication information.

- Subclass of: Registry

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

#### Data_Type_Registry

A Data Type Registry registers data types and their structured descriptions.

- Subclass of: Registry

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

#### License_Registry

License_Registry: A registry for licensing information.

- Subclass of: Registry

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

#### Persistent_Identifier_Registry

Persistent_Identifier_Registry: A registry for persistent identifier information.

- Subclass of: Registry

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

8. The Registry has a getPersistentIdentifier Method.

#### Registry

Registry: A registry maintains a record of objects.

- Subclass of: Active_Object

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

#### Representation_Information_Registry

Representation_Information_Registry: A registry for representation information.

- Subclass of: Information_Object_Registry

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

#### Resource_Registry

Resource_Registry: A registry of system resources.

- Subclass of: Registry

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

#### Subscription_Registry

Subscription_Registry: A registry for subscriptions.

- Subclass of: Registry

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

8. The Registry has a subscriptionServicehasSubscribeUser Method

#### Tools_Registry

Tools_Registry: A registry for software and tools.

- Subclass of: Registry

1. The Active Object has a GetServiceStatus Method

2. The Registry has a GetInformationObjectData Method

3. The Registry has a GetInformationObjectMetadata Method

4. The Registry has a GetInformationObject Method

5. The Registry has a RegisterInformationObject Method

6. The Registry has a ValidateInformationObjectData Method

7. The Registry has a ValidateInformationObjectMetaData Method

### Repository

A Repository is a location in which objects are stored and managed.

#### Repository

A Repository is a location in which objects are stored and managed.

- Subclass of: Active_Object

1. The Active Object has a GetServiceStatus Method

2. The Repository has a GetDigitalObject Method

3. The Repository has a PackageObjects Method

4. The Repository has a PullPackage Method

5. The Repository has a PushPackage Method

6. The Repository has a PutInformationObject

### Method

A Method in object-oriented programming (OOP) is a procedure associated with a message and an object.

#### Method

Method: A method in object-oriented programming (OOP) is a procedure associated with a message and an object. /wikipedia -- For all methods except getDigitalObject, only URIs or UIDs are returned.

#### Method_Signature

Method_Signature: A function signature (or type signature, or method signature) defines input and output of functions or methods. A signature can include: parameters and their types. a return value and type. exceptions that might be thrown or passed back.

- Subclass of: Interface

#### bagInformationObjects

bagInformationObject: a method that packages one or more information objects for network transfer.

- Subclass of: Method

1. A Method has a Signature.

#### configureSearchEngine

configureSearchEngine: a method that configures a search engine using the results of a harvest of one or more Information Objects&apos; metadata.

- Subclass of: Method

1. A Method has a Signature.

#### createQueryModel

createQueryModel: a method that creates a model that identifies search parameters.

- Subclass of: createSIP

1. has_regIOFileManifest__Input

2. A Method has a Signature.

3. A Method has a Signature.

#### getDigitalObject

getDigitalObject: a method that gets a digital object (binary stream) from a repository.

- Subclass of: Method

1. has_DigitalObject__Output

2. has_regIOFileManifest__Input

3. A Method has a Signature.

#### getInformationObject

getInformationObject: a method that gets an Information Object in the form of a file manifest from a registry.

- Subclass of: Method

1. The Method has the parameter RegObjPID__Input

2. A Method has a Signature.

#### getInformationObjectData

getInformationObjectData: a method that gets the data object part of an information object from a registry.

- Subclass of: Method

1. The Method has the parameter RegObjPID__Input

2. has_regIOFileManifest __Output

3. A Method has a Signature.

#### getInformationObjectMetadata

getInformationObjectMetadata: a method that gets the metadata part of an information object from a repository.

- Subclass of: Method

1. The Method has the parameter RegObjPID__Input

2. has_regIOFileManifest __Output

#### getMetrics

getMetrics: a method that gets access and processing metrics from a registry.

- Subclass of: Method

1. A Method has a Signature.

#### getPersistentIdentifier

getPersistentIdentifier: a method that gets a persistent identifier.

- Subclass of: Method

1. A Method has a Signature.

#### getServiceStatus

getServiceStatus: a method that gets the current status of a service.

- Subclass of: Method

1. A Method has a Signature.

#### harvestMetadata

harvestMetadata: a method that harvests metadata.

- Subclass of: Method

1. A Method has a Signature.

#### mapNonOAISStructuresToAIP

mapNonOAISStructuresToAIP: a method that maps one or more structures from a non OAIS archive to an OAIS Archival Information Package.

- Subclass of: Method

1. A Method has a Signature.

#### migratelnformationObject

migrateInformationObject: a method that migrates an information object.

- Subclass of: Method

1. A Method has a Signature.

#### packageInformationObjects

packageInformationObjects: a method that creates a Information Package.

- Subclass of: Method

1. A Method has a Signature.

#### processInformationObject

processInformationObject: a method that processes an information object.

- Subclass of: Method

1. A Method has a Signature.

#### pullBag

pullBag: a method that performs a pull type of network transfer of a package of one or more information objects.

- Subclass of: Method

1. A Method has a Signature.

#### pushBag

pushBag: a method that performs a push type of network transfer of a package of one or more information objects.

- Subclass of: Method

1. A Method has a Signature.

#### putConfiguration

putConfiguration: a method that puts a configuration file in registry.

- Subclass of: Method

1. A Method has a Signature.

#### putInformationObject

putInformationObject: a method that puts (transfers) an information object to a repository.

- Subclass of: Method

1. has_regIOFileManifest__Input

2. A Method has a Signature.

#### putInformationObjectData

putInformationObject: a method that puts (transfers) the data object part of an information object to a repository.

- Subclass of: Method

1. A Method has a Signature.

#### putInformationObjectMetadata

putInformationObject: a method that puts (transfers) the metadata part of an information object to a repository.

- Subclass of: Method

1. A Method has a Signature.

#### putQueryModel

putQueryModel: a method that puts a query model in a registry.

- Subclass of: Method

1. A Method has a Signature.

#### queryRegistry

queryRegistry: a method that queries a reqistry.

- Subclass of: Method

1. The Method has the parameter RegObjUIDStatArrList__Output

2. The Method has the parameter RegistryQueryString__Input

3. A Method has a Signature.

#### registerInformationObject

registerInformationObject: a method that registers an information object in a registry.

- Subclass of: Method

1. has_regIOFileManifest__Input

2. A Method has a Signature.

#### subscribeUser

subscribeUser: a method that subscibes a user.

- Subclass of: Method

1. A Method has a Signature.

#### transformInformationObject

transformInformationObject: a method that transforms an information object.

- Subclass of: Method

1. A Method has a Signature.

#### updateConfiguration

updateConfiguration: a method that updates a configuration file.

- Subclass of: Method

1. A Method has a Signature.

#### updateQueryModel

updateQueryModel: a method that updates a query model.

- Subclass of: Method

1. A Method has a Signature.

#### validateInformationObjectData

validateInformationObjectData: a method that validates an information object&apos;s data part.

- Subclass of: Method

1. has_regIOFileManifest__Input

2. A Method has a Signature.

#### validateInformationObjectMetadata

validateInformationObjectMetadata: a method that validates an information object&apos;s metadata part.

- Subclass of: Method

1. has_regIOFileManifest__Input

2. A Method has a Signature.

#### validateUser

validateUser: a method that validates a user.

- Subclass of: Method

1. A Method has a Signature.

### Method Signature

A Method signature is part of the method declaration and is the combination of the method name and the parameter list.

#### bagInformationObjects

The Signature for the Method bagInformationObjects

- Subclass of: Method_Signature

#### configureSearchEngine

The Signature for the Method configureSearchEngine

- Subclass of: Method_Signature

#### createQueryModel

The Signature for the Method createQueryModel

- Subclass of: Method_Signature

#### createSIP

The Signature for the Method createSIP

- Subclass of: Method_Signature

#### getAccessRightsInformation

The Signature for the Method getAccessRightsInformation

- Subclass of: Method_Signature

#### getContextInformation

The Signature for the Method getContextInformation

- Subclass of: Method_Signature

#### getDataObject

The Signature for the Method getDataObject

- Subclass of: Method_Signature

#### getDigitalObject

The Signature for the Method getDigitalObject

- Subclass of: Method_Signature

#### getFixityInformation

The Signature for the Method getFixityInformation

- Subclass of: Method_Signature

#### getIdentificationInformation

The Signature for the Method getIdentificationInformation

- Subclass of: Method_Signature

#### getInformationObjectData

The Signature for the Method getInformationObjectData

- Subclass of: Method_Signature

#### getInformationObjectMetadata

The Signature for the Method getInformationObjectMetadata

- Subclass of: Method_Signature

#### getInformationObject

The Signature for the Method getInformationObject

- Subclass of: Method_Signature

#### getMetrics

The Signature for the Method getMetrics

- Subclass of: Method_Signature

#### getPID

The Signature for the Method getPID

- Subclass of: Method_Signature

#### getPersistentIdentifier

The Signature for the Method getPersistentIdentifier

- Subclass of: Method_Signature

#### getProvenanceInformation

The Signature for the Method getProvenanceInformation

- Subclass of: Method_Signature

#### getReferenceInformation

The Signature for the Method getReferenceInformation

- Subclass of: Method_Signature

#### getRepresentationInformation

The Signature for the Method getRepresentationInformation

- Subclass of: Method_Signature

#### getServiceStatus

The Signature for the Method getServiceStatus

- Subclass of: Method_Signature

#### harvestMetadata

The Signature for the Method harvestMetadata

- Subclass of: Method_Signature

#### ingestSIP

The Signature for the Method ingestSIP

- Subclass of: Method_Signature

#### mapNonOAISStructuresToAIP

The Signature for the Method mapNonOAISStructuresToAIP

- Subclass of: Method_Signature

#### migratelnformationObject

The Signature for the Method migratelnformationObject

- Subclass of: Method_Signature

#### packageInformationObjects

The Signature for the Method packageInformationObjects

- Subclass of: Method_Signature

#### processInformationObject

The Signature for the Method processInformationObject

- Subclass of: Method_Signature

#### pullBag

The Signature for the Method pullBag

- Subclass of: Method_Signature

#### pushBag

The Signature for the Method pushBag

- Subclass of: Method_Signature

#### putConfiguration

The Signature for the Method putConfiguration

- Subclass of: Method_Signature

#### putInformationObjectData

The Signature for the Method putInformationObjectData

- Subclass of: Method_Signature

#### putInformationObjectMetadata

The Signature for the Method putInformationObjectMetadata

- Subclass of: Method_Signature

#### putInformationObject

The Signature for the Method putInformationObject

- Subclass of: Method_Signature

#### putQueryModel

The Signature for the Method putQueryModel

- Subclass of: Method_Signature

#### queryForAIP

The Signature for the Method queryForAIP

- Subclass of: Method_Signature

#### queryForSIP

The Signature for the Method queryForSIP

- Subclass of: Method_Signature

#### queryRegistry

The Signature for the Method queryRegistry

- Subclass of: Method_Signature

#### registerInformationObject

The Signature for the Method registerInformationObject

- Subclass of: Method_Signature

#### retrieveDIP

The Signature for the Method retrieveDIP

- Subclass of: Method_Signature

#### setDataObject

The Signature for the Method setDataObject

- Subclass of: Method_Signature

#### setPID

The Signature for the Method setPID

- Subclass of: Method_Signature

#### setRepresentationInformation

The Signature for the Method setRepresentationInformation

- Subclass of: Method_Signature

#### subscribeUser

The Signature for the Method subscribeUser

- Subclass of: Method_Signature

#### transformInformationObject

The Signature for the Method transformInformationObject

- Subclass of: Method_Signature

#### updateConfiguration

The Signature for the Method updateConfiguration

- Subclass of: Method_Signature

#### updateQueryModel

The Signature for the Method updateQueryModel

- Subclass of: Method_Signature

#### validateInformationObjectData

The Signature for the Method validateInformationObjectData

- Subclass of: Method_Signature

#### validateInformationObjectMetadata

The Signature for the Method validateInformationObjectMetadata

- Subclass of: Method_Signature

#### validateUser

The Signature for the Method validateUser

- Subclass of: Method_Signature

### Binding

A Binding is a wrapper library that bridges two programming languages, so that a library written for one language can be used in another language.

#### Binding

A Binding is a wrapper library that bridges two programming languages, so that a library written for one language can be used in another language.

#### Protocol

A Protocol is a set of rules governing the format of messages that are exchanged between computers.

## Information Architecture

The Information Architecture consists of the information model and supporting artifacts.

#### Information_Architecture

The Information_Architecture abstract class groups the information classes for the Data Archive Architecture.

### Information Model

An information model is a representation of concepts and the relationships, constraints, rules, and operations to specify data semantics for a chosen domain of discourse.

#### Conceptual_Object

The Conceptual Object class defines a non-tangible object that is also not a digital object.

- Subclass of: Data_Object

1. A data object is interpreted by Representation Information. The relationship is a simple association with cardinality (1..1).

#### Transformational_Information_Property

Transformational Information Property: An Information Property the preservation of the value of which is regarded as being necessary but not sufficient to verify that any Non- Reversible Transformation has adequately preserved information content. This could be important as contributing to evidence about Authenticity. Such an Information Property is dependent upon specific Representation Information, including Semantic Information, to denote how it is encoded and what it means. (The term ‘significant property’, which has various definitions in the literature, is sometimes used in a way that is consistent with its being a Transformational Information Property).

- Subclass of: Information_Property

1. Information Property is a selected part of Content Information

#### Access_Rights_Information

Access Rights Information: The information that identifies the access restrictions pertaining to the Content Information, including the legal framework, licensing terms, and access control. It contains the access and distribution conditions stated within the Submission Agreement, related to both preservation (by the OAIS) and final usage (by the Consumer). It also includes the specifications for the application of rights enforcement measures.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

#### Archival_Information_Collection

Archival Information Collection (AIC): An Archival Information Package whose Content Information is an aggregation of other Archival Information Packages.

- Subclass of: Archival_Information_Package

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. An Information Package is delimited by Packaging Information.

10. An Information Package is described by a Package Description.

11. An Information Package has Content Information.

12. An Information Package is described by an Associated Description.

13. An Archival Information Collection organizes a set of Archival Information Packages.

#### Archival_Information_Package

Archival Information Package (AIP): An Information Package, consisting of the Content Information and the associated Preservation Description Information (PDI), which is preserved within an OAIS.

- Subclass of: Information_Package

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. An Information Package is delimited by Packaging Information.

10. An Information Package is described by a Package Description.

11. An Information Package has Content Information.

12. An Information Package is described by an Associated Description.

#### Archival_Information_Unit

Archival Information Unit (AIU): An Archival Information Package where the Archive chooses not to break down the Content Information into other Archival Information Packages. An AIU can consist of multiple digital objects (e.g., multiple files).

- Subclass of: Archival_Information_Package

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. An Information Package is delimited by Packaging Information.

10. An Information Package is described by a Package Description.

11. An Information Package has Content Information.

12. An Information Package is described by an Associated Description.

#### Associated_Description

Associated Description: The information describing the content of an Information Package from the point of view of a particular Access Aid.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. An Associated Description is derived from an Archival Information Package.

10. An Associated Description provides data for an Access Aid.

#### Bit

Bit: A bit is a basic unit of information in computing and digital communicationssources.

#### Content_Data_Object

Content Data Object: The Data Object, that together with associated Representation Information, comprises the Content Information.

- Subclass of: Data_Object

1. A data object is interpreted by Representation Information. The relationship is a simple association with cardinality (1..1).

#### Content_Information

Content Information: A set of information that is the original target of preservation or that includes part or all of that information. It is an Information Object composed of its Content Data Object and its Representation Information.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. Content Information is further described by Preservation Descriptive Information.

10. Content Information has a Content Data Objects.

#### Context_Information

Context Information: The information that documents the relationships of the Content Information to its environment. This includes why the Content Information was created and how it relates to other Content Information objects.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

#### Data_Object

Data Object: Either a Physical Object or a Digital Object.

1. A data object is interpreted by Representation Information. The relationship is a simple association with cardinality (1..1).

#### Descriptive_Information

Descriptive Information: The set of information, consisting primarily of Package Descriptions, which is provided to Data Management to support the finding, ordering, and retrieving of OAIS information holdings by Consumers.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

#### Digital_Object

Digital Object: An object composed of a set of bit sequences.

- Subclass of: Data_Object

1. A data object is interpreted by Representation Information. The relationship is a simple association with cardinality (1..1).

2.

#### Dissemination_Information_Package

Dissemination Information Package (DIP): An Information Package, derived from one or more AIPs, and sent by Archives to the Consumer in response to a request to the OAIS.

- Subclass of: Information_Package

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. An Information Package is delimited by Packaging Information.

10. An Information Package is described by a Package Description.

11. An Information Package has Content Information.

#### Fixity_Information

Fixity Information: The information which documents the mechanisms that ensure that the Content Information object has not been altered in an undocumented manner. An example is a Cyclical Redundancy Check (CRC) code for a file.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

#### Information_Object

Information Object: A Data Object together with its Representation Information.

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

#### Information_Package

Information Package: A logical container composed of optional Content Information and optional associated Preservation Description Information. Associated with this Information Package is Packaging Information used to delimit and identify the Content Information and Package Description information used to facilitate searches for the Content Information.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. An Information Package is delimited by Packaging Information.

10. An Information Package is described by a Package Description.

11. An Information Package has Content Information.

#### Information_Property

Information Property: That part of the Content Information as described by the Information Property Description. The detailed expression, or value, of that part of the information content is conveyed by the appropriate parts of the Content Data Object and its Representation.

1. Information Property is a selected part of Content Information

#### Other_Representation_Information

Other Representation Information: Representation Information which cannot easily be classified as Semantic or Structural. For example software, algorithms, encryption, written instructions and many other things may be needed to understand the Content Data Object, all of which therefore would be, by definition, Representation Information, yet would not obviously be either Structure or Semantics. Information defining how the Structure and the Semantic Information relate to each other, or software needed to process a database file would also be regarded as Other Representation Information.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

#### Overview_Description

Overview Description: A specialization of the Collection Description that describes the collection as a whole.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. Collection Description is derived from an Archival Information Collection

#### Package_Description

Package Description: The information intended for use by Access Aids.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. A Package Description is derived from an Information Package.

10. A Package Description has an Associated Description.

#### Packaging_Information

Packaging Information: The information that is used to bind and identify the components of an Information Package. For example, it may be the ISO 9660 volume and directory information used on a CD-ROM to provide the content of several files containing Content Information and Preservation Description Information.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. Packaging Information contains Content Information.

10. Packaging Information contains Perservation Description Information.

11. Packaging Information is discoverable by Descriptive Information.

12. Packaging Information identifies the components of an Informaiton Package.

#### Physical_Object

Physical Object: An object (such as a moon rock, bio-specimen, microscope slide) with physically observable properties that represent information that is considered suitable for being adequately documented for preservation, distribution, and independent usage.

- Subclass of: Data_Object

1. A data object is interpreted by Representation Information. The relationship is a simple association with cardinality (1..1).

#### Preservation_Description_Information

Preservation Description Information (PDI): The information which is necessary for adequate preservation of the Content Information and which can be categorized as Provenance, Reference, Fixity, Context, and Access Rights Information.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. Preservation Description Information includes Access Rights Information

10. Preservation Description Information includes Context Information

11. Preservation Description Information includes Provenance Information

12. Preservation Description Information includes Reference Information

13. Preservation Description Information provides preservation description for Content Information.

#### Provenance_Information

Provenance Information: The information that documents the history of the Content Information. This information tells the origin or source of the Content Information, any changes that may have taken place since it was originated, and who has had custody of it since it was originated. The Archive is responsible for creating and preserving Provenance Information from the point of Ingest; however, earlier Provenance Information should be provided by the Producer. Provenance Information adds to the evidence to support Authenticity.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

#### Reference_Information

Reference Information: The information that is used as an identifier for the Content Information. It also includes identifiers that allow outside systems to refer unambiguously to a particular Content Information. An example of Reference Information is an ISBN.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

#### Representation_Information

Representation Information: The information that maps a Data Object into more meaningful concepts. An example of Representation Information for a bit sequence which is a FITS file might consist of the FITS standard which defines the format plus a dictionary which defines the meaning in the file of keywords which are not part of the standard. Another example is JPEG software which is used to render a JPEG file; rendering the JPEG file as bits is not very meaningful to humans but the software, which embodies an understanding of the JPEG standard, maps the bits into pixels which can then be rendered as an image for human viewing.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. Representation Information can be interpreted using recursively by Representation Information.

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. Representation Information can have other Other Represention Information.

10. Representation Informatin includes Semantic Information.

11. Representation Information includes Structure Information.

12. Representation Information is a member of a Representation_Network

#### Representation_Network

Representation Network: The set of Representation Information that fully describes the meaning of a Data Object. Representation Information in digital forms needs additional Representation Information so its digital forms can be understood over the Long Term.

- Subclass of: Information_Object

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

#### Submission_Information_Package

Submission Information Package (SIP): An Information Package that is delivered by the Producer to the OAIS for use in the construction or update of one or more AIPs and/or the associated Descriptive Information.

- Subclass of: Information_Package

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. An Information Package is delimited by Packaging Information.

10. An Information Package is described by a Package Description.

11. An Information Package has Content Information.

#### Unit_Description

Unit Description: A type of Package Description that is specialized to provide information about an Archival Information Unit for use by Access Aids.

- Subclass of: Package_Description

1. An Information Object has one Data Object. The relationship is an aggregation with cardinality (1..1).

2. The Definitional Informational Model has Definitional Information. The relationship is an aggregation with cardinality (1..0)

3. has_getDataObject

4. Information_Object has the method getPID.

5. has_getRepresentationInformation

6. has_setDataObject

7. Information_Object has the method setPID.

8. has_setRepresentationInformation

9. A Package Description is derived from an Information Package.

10. A Package Description has an Associated Description.

11. A Unit Description provides information about an Archival Information Unit.

### Data_Structure

A Data Structure is a particular way of organizing data in a computer so that it can be used efficiently.

#### Registry_Object

The Registry Object is a digital object defined to be stored and managed in a digital repository and recorded in a registry using a unique identifier.

- Subclass of: Other_Component

#### regObjPID

regObjPID: A data structure that contains an object&apos;s Persistent Identifier.

- Subclass of: Data_Structure

#### regObjPIDStatArrList

regObjPIDStatArrList: The data structure regObjPIDArrList with a status for each entry.

- Subclass of: Data_Structure

#### registryQueryString

registryQueryString: A data structure that contains a query string. eg. (parm=value (and/or/not parm=value)*

- Subclass of: Data_Structure

[IMPLEMENTATIONs]

[Informative]

[Annexes contain ancillary information. Normative annexes precede informative annexes. Informative references are placed in an informative annex. See CCSDS A20.0-Y-4, CCSDS Publications Manual (Yellow Book, Issue 4, April 2014) for discussion of the kinds of material contained in annexes.]

Technology

This annex provides a list and brief description of several example implementations.  Implementation is the realization of an application, model, design, specification, standard, algorithm, or policy.

Apache_Jena_Fuseki

Apache Jena Fuseki is a SPARQL server. Fuseki can run as an operating system service, as a Java web application (WAR file), and as a standalone server. It provides security (using Apache Shiro) and has a user interface for server monitoring and administration.  /Website

Apache_Solr

Apache Solr is an open source enterprise search platform that provides full-text search, faceted search, real-time indexing, and rich document handling. /Wikipedia

Bagit

BagIt is a set of hierarchical file system conventions designed to support disk- based storage and network transfer of arbitrary digital content. A “bag” consists of a “payload” (the arbitrary content) and “tags”, which are metadata files intended to document the storage and transfer of the bag. A required tag file contains a manifest listing every file in the payload together with its corresponding checksum. The name, BagIt, is inspired by the “enclose and deposit” method, sometimes referred to as “bag it and tag it”. /Wikipedia

Java

Java is a general-purpose computer-programming language that is concurrent, class-based, object-oriented, and specifically designed to have as few implementation dependencies as possible.

OData

OData (Open Data Protocol) is a protocol for the creation and consumption of RESTful APIs. /wikipedia

OData_DELETE

DELETE: Remove the resource.

Subclass of: OData

OData_GET

GET: Get the resource (a collection of entities, a single entity, a structural property, a navigation property, a stream, etc.).

Subclass of: OData

OData_Metadata_Document

The metadata document describes the types, sets, functions and actions understood by the OData service. Clients can use the metadata document to understand how to query and interact with entities in the service.

Subclass of: OData

OData_PATCH

PATCH: Update an existing resource by replacing part of its properties with a partial instance.

Subclass of: OData

OData_POST

POST: Create a new resource.

Subclass of: OData

OData_PUT

PUT: Update an existing resource by replacing it with a complete instance.

Subclass of: OData

OData_Service_Document

The service document lists entity sets, functions, and singletons that can be retrieved. Clients can use the service document to navigate the model in a hypermedia-driven fashion.

Subclass of: OData

REST_HTTP

REST_HTTP identifies a protocol stack for network communications which is built on the classic internet protocol stack. Representational state transfer (REST) or RESTful web services is an approach that leverages the HTTP protocol to provide interoperability between computer systems on the Internet using a uniform and predefined set of stateless operations. The Hypertext Transfer Protocol (HTTP) is an application protocol for distributed, collaborative, and hypermedia information systems.

SPARQL

SPARQL is an RDF query language, that is, a semantic query language for databases, able to retrieve and manipulate data stored in Resource Description Framework (RDF) format.  /Wikipedia

ebXML_Registry

The ebXML Registry Services Specification OASIS Standard (ISO 15000-4) defines interoperable registries and repositories, with an interface that enables submission, query and retrieval of contents. /website

- Other Archives [Informative]

Non_OAIS

An archival information system that is not compatible with OAIS.

Subclass of: Archive

Astronomy_Data_Archive

Astronomy_Data_Archive - A data archive for Astrononmy

Subclass of: Non_OAIS

Earth_Science_Data_Archive

Earth_Science_Data_Archive - A data archive for Earth_Science /jsh

Subclass of: Non_OAIS

Mission_Housekeeping_Archive

Mission_Housekeeping_Data_Archive - A data archive for Mission_Housekeeping data /jsh

Subclass of: Non_OAIS

Implementation Conformance 
Statement (ICS) Proforma

(normative)

INTRODUCTION

OVERVIEW

This annex provides the Implementation Conformance Statement (ICS) Requirements List (RL) for an implementation of [Specification].  The ICS for an implementation is generated by completing the RL in accordance with the instructions below. An implementation claiming conformance must satisfy the mandatory requirements referenced in the RL.

ABBREVIATIONS AND CONVENTIONS

The RL consists of information in tabular form.  The status of features is indicated using the abbreviations and conventions described below.

Item Column

The item column contains sequential numbers for items in the table.

Feature Column

The feature column contains a brief descriptive name for a feature. It implicitly means “Is this feature supported by the implementation?”

Status Column

The status column uses the following notations:

- M		mandatory;

- O		optional;

- C		conditional;

- X		prohibited;

- I		out of scope;

- N/A		not applicable.

Support Column Symbols

The support column is to be used by the implementer to state whether a feature is supported by entering Y, N, or N/A, indicating:

Y	Yes, supported by the implementation.

N	No, not supported by the implementation.

N/A	Not applicable.

The support column should also be used, when appropriate, to enter values supported for a given capability.

INSTRUCTIONS FOR COMPLETING THE RL

An implementer shows the extent of compliance to the Recommended Standard by completing the RL; that is, the state of compliance with all mandatory requirements and the options supported are shown. The resulting completed RL is called an ICS. The implementer shall complete the RL by entering appropriate responses in the support or values supported column, using the notation described in A1.2.  If a conditional requirement is inapplicable, N/A should be used. If a mandatory requirement is not satisfied, exception information must be supplied by entering a reference Xi, where i is a unique identifier, to an accompanying rationale for the noncompliance.

ICS PROFORMA FOR [SPECIFICATION]

GENERAL INFORMATION

Identification of ICS

Test

| Date of Statement (DD/MM/YYYY) |  |
| --- | --- |
| ICS serial number |  |
| System Conformance statement cross-reference |  |

Identification of Implementation Under Test

| Implementation Name |  |
| --- | --- |
| Implementation Version |  |
| Special Configuration |  |
| Other Information |  |

Identification of Supplier

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation Name(s) and Versions |  |
| Other information necessary for full identification, e.g., name(s) and version(s) for machines and/or operating systems; System Name(s) |  |

Identification of Specification

| [CCSDS Document Number] |
| --- |
| Have any exceptions been required? NOTE – A YES answer means that the implementation does not conform to the Recommended Standard. Non-supported mandatory capabilities are to be identified in the ICS, with an explanation of why the implementation is non-conforming. | Yes [ ] No [ ] |

REQUIREMENTS LIST

[See CCSDS A20.1-Y-1, CCSDS Implementation Conformance Statements (Yellow Book, Issue 1, April 2014).]

Security, SANA, and Patent Considerations

(Informative)

Security Considerations

security concerns with respect to the CCSDS document

Data Privacy

Data Integrity

Authentication of Communicating Entities

Control of Access to Resources

Availability of Resources

Auditing of Resource Usage

Potential threats and attack scenarios

Consequences of not applying security to the technology

SANA Considerations

[See CCSDS 313.0-Y-1, Space Assigned Numbers Authority (SANA)—Role, Responsibilities, Policies, and Procedures (Yellow Book, Issue 1, July 2011).]

Patent Considerations

[See CCSDS A20.0-Y-4, CCSDS Publications Manual (Yellow Book, Issue 4, April 2014).]

# Comments

Seems as if a global replace to Recommended Practice was made and messed up at least this page.

If BB then is setting actual implementations not just working on consensus about requirements

No mention of architecture?

Missing annexes

Still to be added to document?

How?

Will we be abbreviating this in this document?  In others docs we haven’t.  I’ve added RM to abbreviations in case we use it.

We don’t guarantee this for OAIS compliant archives either.

Why comparison?  What’s the point of that?  Left it because it was in OAIS, but I don’t understand the significance of comparison of archives.

Comparison of how repositories implement OAIS-IF may cause a user to pick one over another with the expectation that one or the other will be more likely to preserve data appropriately.

Where is note?

Will OAIS-IF make this less true?

Why are they stakeholders?

What will be in 4?

Does conformance with 3 mean you need to use our Info Model and all methods in your archive?

So what exactly is required? How would user know what parts are required and which are not?

This requires all archives to use our terminology.  This is much stricter than OAIS conformance.

Is there a plan for a section 4 mentioned in Conformance section?

Isolates this document from change of color.  Also document color does not have any relevance to ISO.  Most readers who are not active in CCSDS will not understand the color significance anyway.

Kept this for now, to better mirror RM-OAIS.  This section/paragraph is at least partially duplicative of section 1.6.2.  Can’t we combine them?

Steve:  Confirm whether this is the plan for your UML illustrations, or change/delete it.

Copied from OAIS, but refers to OAIS sections.  Don’t think this is relevant to this document.

Suspect many of these are not used in this document

Should probably try to get this done sooner than later.  If we don’t know what terms are here, we can’t check if typographical conventions are correctly done, i.e. should capitalization and bolding be applied. Can apply this later, but is a lot of work to add in and check later.

CCSDS style would be figure 2-1.  Correct throughout document.

Need explanation of how to interpret figure and explanation of figures in general.

Text does not align well with figure,  Text mentions items not shown in figure and several items in figure not described or even mentioned,

In OAIS RM, we tried not to leave off Functional Entity when discussing it so confusion does not arise.  This is probably most prone to that.  Will have to see how this plays out in this document.

Will need an overall diagram

What other subsections planned?

What is purpose of this?

Is this needed?  Can you conform without conforming to everything?  How is this related to conformance section?