Comments and Questions on the EAST Pink Sheets of 12Feb04

1-- Dates:  The issue date is 12/02/04, which we well understand to be February and not December.  We in the US are used to reading this as December  and it is probably the complete opposite most other countries.  Could CCSDS adopt a policy that all dates put in documents be written using the name of the month or an abbreviation of it?

2-- In the proposed new Figure 3-21, Component Declaration Diagram, the last iterative block “Constant Declaration” is not seen in the current Figure 3-21.    Is this intended?  If so, is it reflected in the text?

3-- For some reason, some of the new figures have extra lines and squares around the text. in the electronic as well as printed form.  Is this an incompatibility in the diagramming tools used?

4-- In the bottom of page 5/8 of the pink sheets, the last line was left off of Figure 3-8:

-- type VECTOR is array (NUMBER range <>) of REAL;

Though this is about text describing the changes, it should be complete so it does not inadvertently get propagated to the updated EAST document.

5—On page 4/8, it is stated that the Default Value is already used (as in current BB Figure 3-11) and not defined.   Should Value not be defined too?

6—On page 6/8, last line of Example 3-11,

-  A  question is:  In the variant record, depending on the value of the PRESENCE_FLAG, either SOURCE_DATA_0 is used or SOURCE_DATA_1.  Since these are two different identifiers,  and the choice is not known until  the data is read,  what happens if the EAST library unit is asked to look for one identifier when the other is read?  Based on the EAST description, is the library capable of reading both identifier names and choosing the correct one while giving the other a null value?  Or does an error status result?

-  A typo occurs in mid-line on bottom.

7-- On page 7/8,

The proposed paragraph is,

“If the size of an array is deduced from several discriminants by a calculation its virtual size declaration remains unchanged (as shown on Example 3-10).  The calculation to be done is described later after the object declaration section.”

Recommend following editing:

“If the size of an array is deduced from several discriminants by a calculation, its virtual size declaration remains unchanged (as shown on example 3-10).  The calculation to be done is described later after the object declaration section where the components are instantiated (or assigned to data), as shown in Example 3-11.”

8-- Check title of proposed Example 3-11b.  Also the title below the next Example 3-11, “Calculated component presence condition.”

9—In Figure 3-11b, can we assume that the EAST syntax checker will check that the expression result will be type BOOLEAN?

EAST BB:

On page 3-16, Figure 3-22: Index Constraint Diagram,  shouldn’t the box “Integer Literal” be added to both lower and upper indices?