Maneuver Planning Message

- Use Cases of MPM

  - Notification of Future Maneuver

    - Request MOC schedule block(s) of tracking network time for maneuvers, notify tracking networks of potential critical event

    - Notify Scientists and other users that data is going to be ratty or unavailable

  - Notify Conjunction Assessment team a maneuver will be taking place

- Required:

  - Originator, Object Name, Object ID, Time System, Creation Date

  - Maneuver ID, Start Epoch & Duration

- Optional:

  - Purpose of maneuver

  - Desired changes in selected elements (apo raise, etc)

  - Coord system (Center & Ref Frame), dV or dH magnitude & direction or component in each axis

  - OD & Attitude states (with coord sys) used to plan mnvr (can be epoch only, full Cart or Kepl state, or even just ID)

  - Initial sc mass, final sc mass or change in mass

  - Orbit & Attitude states (with coord sys) at ignition, at end of burn

MPM Use Case 1: Notification of Stationkeeping Maneuver/Mnvr Request

CCSDS_MPM_VERS = 1.0

COMMENT Generated by GSFC FDF

COMMENT Maneuver Notification: SK09 Sequence

CREATION_DATE = 2014-10-01T12:33:22.123

ORIGINATOR = NASA

OBJECT_NAME = TerSat

OBJECT_ID = 2009-123A

TIME_SYSTEM = UTC

COMMENT SK09 Maneuver Sequence

NUMBER_OF_MANEUVERS = 5

COMMENT First maneuver: Slew to SK09a attitude

MAN_NAME = SK09a_ATT

MAN_TYPE = ATTITUDE

MAN_EPOCH_IGNITION = 2014-10-14T09:00:00.00

MAN_DURATION = 600.00 [s]

COMMENT 2nd maneuver: SK09a

MAN_NAME = SK09a_ORB

MAN_TYPE = ORBIT

MAN_EPOCH_IGNITION = 2014-10-14T09:15:00.00

MAN_DURATION = 712.20 [s]

COMMENT 3rd maneuver: SK09b attitude

MAN_NAME = SK09b_ATT

MAN_TYPE = ATTITUDE

MAN_EPOCH_IGNITION = 2014-10-14T09:45:00.00

MAN_DURATION = 1200.464 [s]

COMMENT 4th maneuver: SK09b

MAN_NAME = SK09b_ORB

MAN_TYPE = ORBIT

MAN_EPOCH_IGNITION = 2014-10-14T10:15:00.00

MAN_DURATION = 687.40 [s]

COMMENT 5th maneuver: Return to Sci Attitude

MAN_NAME = SK09_SCI_ATT

MAN_TYPE = ATTITUDE

MAN_EPOCH_IGNITION = 2014-10-14T10:15:00.00

MAN_DURATION = 300.264 [s]

MPM Use Case 2: Notification of Future Maneuver to Conjunction Assessment

CCSDS_MPM_VERS = 1.0

COMMENT Generated by Generic Flight Dynamics

COMMENT Maneuver Notification: TerSat StationKeeping 09

CREATION_DATE = 2014-10-01T12:33:22.123

ORIGINATOR = NASA

OBJECT_NAME = TerSat

OBJECT_ID = 2009-123A

TIME_SYSTEM = UTC

COMMENT Spacecraft parameters

MASS = 1234.567 [kg]

SOLAR_RAD_AREA = 10.000 [m**2]

SOLAR_RAD_COEFF = 1.300

GM = 398600.4415 [km**3/s**2]

COMMENT Initial State Vector Cartesian

CENTER_NAME = Earth

REF_FRAME = EME2000

TIME_SYSTEM = UTC

EPOCH = 2014-10-13T00:00:00.000

X = 6655.9942 [km]

Y = -40218.5751 [km]

Z = -82.9177 [km]

X_DOT = 3.11548208 [km/s]

Y_DOT = 0.47042605 [km/s]

Z_DOT = -0.00101495 [km/s]

COMMENT SK09 Maneuver Sequence

NUMBER_OF_MANEUVERS = 2

COMMENT 1st maneuver: SK09a

MAN_NAME = SK09a_ORB

MAN_TYPE = ORBIT

MAN_EPOCH_IGNITION = 2014-10-14T09:15:00.00

MAN_DURATION = 712.20 [s]

MAN_CENTER = EARTH

MAN_REF_FRAME = EME2000

MAN_DV_1 = -0.00200 [km/s]

MAN_DV_2 = -0.00300 [km/s]

MAN_DV_3 = 0.00100 [km/s]

COMMENT 2nd maneuver: SK09b

MAN_NAME = SK09b_ORB

MAN_TYPE = ORBIT

MAN_EPOCH_IGNITION = 2014-10-14T10:15:00.00

MAN_DURATION = 687.40 [s]

MAN_CENTER = EARTH

MAN_REF_FRAME = EME2000

MAN_DV_1 = -0.00600 [km/s]

MAN_DV_2 = 0.00100 [km/s]

MAN_DV_3 = 0.00000 [km/s]

Use Cases of MDM

- FDT to MOC to provide maneuver command parameters

- FDT to OD/MOC to generate predicted orbit with maneuvers

- FDT to ACS/MOC to verify attitude plan for maneuver, run through sc simulator

- FDT to Propulsion Engineer/MOC for verification of initial & expected propulsion parameters

- Required:

  - Originator, Sat Name, Sat Number, Creation Date

  - Maneuver ID, Start Epoch & Duration

  - Coord system (Center & Ref Frame), dV or dH magnitude & direction or component in each axis

- Optional:

  - Thrusters to be used, Tanks to be used, Pressure, Temp, mass flow rate, pulse width, duty cycle, spin rate…

  - Purpose of maneuver

  - Desired changes in selected elements (apo raise, etc)

  - OD & Attitude states (with coord sys) used to plan mnvr (can be epoch only, full Cart or Kepl state, or even just ID)

  - Initial sc mass, final sc mass or change in mass

  - Orbit & Attitude states (with coord sys) at ignition, at end of burn

MDM Use Case 1: Convey Command Parameters to MOC

CCSDS_MDM_VERS = 1.0

COMMENT Generated by Generic Flight Dynamics

COMMENT Final Maneuver Plan: SK09 Sequence

CREATION_DATE = 2014-10-01T12:33:22.123

ORIGINATOR = NASA

OBJECT_NAME = TerSat

OBJECT_ID = 2009-123A

TIME_SYSTEM = UTC

COMMENT SK09 Maneuver Sequence

NUMBER_OF_MANEUVERS = 5

COMMENT 1st maneuver: Slew to SK09a attitude

MAN_NAME = SK09a_ATT

MAN_TYPE = ATTITUDE

MAN_EPOCH_IGNITION = 2014-10-14T09:00:00.00

MAN_DURATION = 600.00 [s]

MAN_CENTER = BODY

MAN_REF_FRAME = PRY

SEQUENCE = 123

MAN_ANGLE_1 = 30.00 [deg]

MAN_ANGLE_2 = 4.65 [deg]

MAN_ANGLE_3 = -90.00 [deg]

COMMENT 2nd maneuver: SK09a

MAN_NAME = SK09a_ORB

MAN_TYPE = ORBIT

MAN_EPOCH_IGNITION = 2014-10-14T09:15:00.00

MAN_DURATION = 712.20 [s]

MAN_CENTER = BODY

MAN_REF_FRAME = RTN

MAN_DV_1 = 0.00201500 [km/s]

MAN_DV_2 = -0.00187300 [km/s]

MAN_DV_3 = 0.00000000 [km/s]

COMMENT 3rd maneuver: SK09b attitude

MAN_NAME = SK09b_ATT

MAN_TYPE = ATTITUDE

MAN_EPOCH_IGNITION = 2014-10-14T09:45:00.00

MAN_DURATION = 1200.464 [s]

MAN_CENTER = BODY

MAN_REF_FRAME = PRY

SEQUENCE = 123

MAN_ANGLE_1 = 00.00 [deg]

MAN_ANGLE_2 = 0 [deg]

MAN_ANGLE_3 =180.00 [deg]

COMMENT 4th maneuver: SK09b

MAN_NAME = SK09b_ORB

MAN_TYPE = ORBIT

MAN_EPOCH_IGNITION = 201Ter4-10-14T10:15:00.00

MAN_DURATION = 93.60 [s]

MAN_CENTER = BODY

MAN_REF_FRAME = RTN

MAN_DV_1 = -0.0020000 [km/s]

MAN_DV_2 = 0.001900 [km/s]

MAN_DV_3 = 0.00000000 [km/s]

COMMENT 5th maneuver: Return to Sci Attitude

MAN_NAME = SK09_TO_SCI_ATT

MAN_TYPE = ATTITUDE

MAN_EPOCH_IGNITION = 2014-10-14T10:15:00.00

MAN_DURATION = 300.264 [s]

MAN_REF_FRAME = PRY

SEQUENCE = 123

MAN_ANGLE_1 = 45.00 [deg]

MAN_ANGLE_2 = 6 [deg]

MAN_ANGLE_3 =180.00 [deg]

:

MDM Use Case 2: Propulsion System to PROP Engineer for Verification

CCSDS_MDM_VERS = 1.0

COMMENT Generated by Generic Flight Dynamics

COMMENT Final Maneuver Plan: SK09 Sequence

CREATION_DATE = 2014-10-01T12:33:22.123

ORIGINATOR = NASA

OBJECT_NAME = TerSat

OBJECT_ID = 2009-123A

TIME_SYSTEM = UTC

COMMENT SK09 Maneuver Sequence

NUMBER_OF_MANEUVERS = 5

SC_MASS = 1234.229 [kg]

INITIAL_FUEL_MASS = 198.317 [kg]

PROP_MODE = BLOWDOWN

COMMENT 1st maneuver: Slew to SK09a attitude

MAN_NAME = SK09a_ATT

MAN_TYPE = ATTITUDE

MAN_EPOCH_IGNITION = 2014-10-14T09:00:00.00

MAN_DURATION = 600.00 [s]

MAN_CENTER = BODY

MAN_REF_FRAME = PRY

SEQUENCE = 123

MAN_ANGLE_1 = 30.00 [deg]

MAN_ANGLE_2 = 4.65 [deg]

MAN_ANGLE_3 = -90.00 [deg]

THRUSTER1 = AT1

THRUSTER1_ISP = 230.584

THRUSTER1_SCALEFACTOR = 0.97

THRUSTER1_DUTYCYCLE = 0.66

THRUSTER1_INIT_THRUST = 16.315 [N]

THRUSTER1_END_THRUST = 16.215 [N]

THRUSTER2 = AT2

THRUSTER2_ISP = 232.385

THRUSTER2_SCALEFACTOR = 0.988

THRUSTER2_DUTYCYCLE = 0.88

THRUSTER2_INIT_THRUST = 21.417 [N]

THRUSTER2_END_THRUST = 21.317 [N]

THRUSTER3 = AT3…

THRUSTER4 = AT4…

TANK1 = FUEL1

TANK1_PRES_START = 315 [psi]

TANK1_PRES_STOP = 314 [psi]

TANK1_TEMP_START = 20 [degC]

TANK1_TEMP_STOP = 19 [degC]

FUEL_USED = -0.211 [kg]

COMMENT 2nd maneuver: SK09a

MAN_NAME = SK09a_ORB

MAN_TYPE = ORBIT

MAN_EPOCH_IGNITION = 2014-10-14T09:15:00.00

MAN_DURATION = 92.20 [s]

MAN_CENTER = BODY

MAN_REF_FRAME = RTN

MAN_DV_1 = 0.00201500 [km/s]

MAN_DV_2 = -0.00187300 [km/s]

MAN_DV_3 = 0.00000000 [km/s]

THRUSTER1 = OT1

THRUSTER1_ISP = 219

THRUSTER1_SCALEFACTOR = 0.96

THRUSTER1_DUTYCYCLE = 1.00

THRUSTER1_INIT_THRUST = 70.315 [N]

THRUSTER1_END_THRUST = 69.215 [N]

THRUSTER2 = AT1

THRUSTER2_SCALEFACTOR = 0.98

THRUSTER2_DUTYCYCLE = 0.07

THRUSTER2_INIT_THRUST = 16.215 [N]

THRUSTER2_END_THRUST = 15.100 [N]

THRUSTER3 = AT2…

THRUSTER4 = AT3…

THRUSTER5 = AT4…

TANK1 = FUEL1

TANK1_PRES_START = 314 [psi]

TANK1_PRES_STOP = 306 [psi]

TANK1_TEMP_START = 20 [degC]

TANK1_TEMP_STOP = 18.2 [degC]

FUEL_USED = -3.6 [kg]

COMMENT 3rd maneuver: SK09b attitude

MAN_NAME = SK09b_ATT

MAN_TYPE = ATTITUDE

MAN_EPOCH_IGNITION = 2014-10-14T09:45:00.00

MAN_DURATION = 1200.464 [s]

MAN_CENTER = BODY

MAN_REF_FRAME = PRY

SEQUENCE = 123

MAN_ANGLE_1 = 00.00 [deg]

MAN_ANGLE_2 = 0 [deg]

MAN_ANGLE_3 =180.00 [deg]

tHRUSTER1 = AT1…

THRUSTER4 = AT4…

TANK1 = FUEL1…

COMMENT 4th maneuver: SK09b

MAN_NAME = SK09b_ORB…:

Use Cases of MAM

- FDT to MOC to provide maneuver reconstruction/calibration.fuel usage

- FDT to Propulsion Engineer/MOC for comparison

- Required:

  - Originator, Sat Name, Sat Number, Creation Date

  - Maneuver ID, Start Epoch & Duration

  - Coord system (Center & Ref Frame), dV or dH magnitude & direction or component in each axis

- Optional:

  - Thrusters to be used, Tanks to be used, Pressure, Temp, mass flow rate, pulse width, duty cycle, spin rate…

  - Purpose of maneuver

  - Desired changes in selected elements (apo raise, etc)

  - OD & Attitude states (with coord sys) used to plan mnvr (can be epoch only, full Cart or Kepl state, or even just ID)

  - Initial sc mass, final sc mass or change in mass

  - Orbit & Attitude states (with coord sys) at ignition, at end of burn

MAM Use Case 1: Maneuver Reconstruction Report for MOC

CCSDS_MAM_VERS = 1.0

COMMENT Generated by Generic Flight Dynamics

COMMENT SK09 Maneuver Calibration Report

CREATION_DATE = 2014-10-15T20:00:12.123

ORIGINATOR = NASA

OBJECT_NAME = TerSat

OBJECT_ID = 2009-123A

TIME_SYSTEM = UTC

COMMENT SK09 Maneuver Sequence

NUMBER_OF_MANEUVERS = 2

SC_MASS = 1234.229 [kg]

INITIAL_FUEL_MASS = 197.000 [kg]

PROP_MODE = BLOWDOWN

COMMENT 1st Orbit Maneuver: SK09a

MAN_NAME = SK09a_ORB

MAN_TYPE = ORBIT

MAN_EPOCH_IGNITION = 2014-10-14T09:15:02.256

MAN_DURATION = 91.80 [s]

MAN_CENTER = BODY

MAN_REF_FRAME = RTN

MAN_DV_1 = 0.00201400 [km/s]

MAN_DV_2 = -0.00187200 [km/s]

MAN_DV_3 = 0.00000000 [km/s]

THRUSTER1 = OT1

THRUSTER1_ISP = 218.9

THRUSTER1_SCALEFACTOR = 0.985

THRUSTER1_DUTYCYCLE = 1.00

THRUSTER1_INIT_THRUST = 70.315 [N]

THRUSTER1_END_THRUST = 69.715 [N]

THRUSTER2 = AT1

THRUSTER2_SCALEFACTOR = 0.98

THRUSTER2_DUTYCYCLE = 0.088

THRUSTER2_INIT_THRUST = 16.215 [N]

THRUSTER2_END_THRUST = 15.100 [N]

THRUSTER3 = AT2…

THRUSTER4 = AT3…

THRUSTER5 = AT4…

TANK1 = FUEL1

TANK1_PRES_START = 314 [psi]

TANK1_PRES_STOP = 307 [psi]

TANK1_TEMP_START = 20 [degC]

TANK1_TEMP_STOP = 18.9 [degC]

FUEL_USED = -3.567 [kg]

COMMENT 2nd Orbit maneuver: SK09b

MAN_NAME = SK09b_ORB

MAN_TYPE = ORBIT

MAN_EPOCH_IGNITION = 2014-10-14T10:15:02.512

MAN_DURATION = 93.612 [s]

MAN_CENTER = BODY

MAN_REF_FRAME = RTN

MAN_DV_1 = -0.0020000 [km/s]

MAN_DV_2 = 0.001900 [km/s]

MAN_DV_3 = 0.00000000 [km/s]

THRUSTER1 = OT1

THRUSTER1_ISP = 218.7

THRUSTER1_SCALEFACTOR = 0.980

THRUSTER1_DUTYCYCLE = 1.00

THRUSTER1_INIT_THRUST = 69.000 [N]

THRUSTER1_END_THRUST = 68.715 [N]

THRUSTER2 = AT1

THRUSTER2_SCALEFACTOR = 0.98…

THRUSTER4 = AT4…

TANK1 = FUEL1…

etc