Recommendation for Space Data System Standards

Attitude Data Messages

Recommended Standard

CCSDS 504.0-B-1

Proposed PINK Book

Nov 2015

AUTHORITY

|  | Issue: | Recommended Standard, Issue 1 |  |
| --- | --- | --- | --- |
|  | Date: | May 2008 |  |
|  | Location: | Washington, DC, USA |  |

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS Recommendations is detailed in the Procedures Manual for the Consultative Committee for Space Data Systems (reference [F3]), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

STATEMENT OF INTENT

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

This document is a Recommended Standard for Attitude Data Messages (ADMs) and has been prepared by the Consultative Committee for Space Data Systems (CCSDS).  The set of attitude data messages described in this Recommended Standard is the baseline concept for attitude representation in data interchange applications that are cross-supported between Agencies of the CCSDS.

This Recommended Standard establishes a common framework and provides a common basis for the interchange of attitude data.  It allows implementing organizations within each Agency to proceed coherently with the development of compatible derived standards for the flight and ground systems that are within their cognizance.  Derived Agency standards may implement only a subset of the optional features allowed by the Recommended Standard and may incorporate features not addressed by this Recommended Standard.

Through the process of normal evolution, it is expected that expansion, deletion or modification to this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, as defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK: CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 504.0-B-1 | Attitude Data Messages, Recommended Standard, Issue 1 | May 2008 | Current issue. |

# CONTENTS

Section	Page

1	INTRODUCTION	1-1

1.1	PURPOSE	1-1

1.2	Scope and APPLICABILITY	1-1

1.3	Conventions and Definitions	1-2

1.4	Structure of this document	1-2

1.5	References	1-3

2	Overview	2-1

2.1	attitude data Message types	2-1

2.2	ATTITUDE Parameter Message (APM)	2-1

2.3	ATTITUDE Ephemeris Message (AEM)	2-1

2.4	Message formats	2-2

2.5	Exchange of multiple messages	2-2

2.6	Exchange Scheme	2-2

3	ATTITUDE PARAMETER MESSAGE (APM)	3-1

3.1	Overview	3-1

3.2	APM Content	3-1

3.3	APM Examples	3-8

4	ATTITUDE EPHEMERIS MESSAGE (AEM)	4-1

4.1	Overview	4-1

4.2	AEM content	4-1

4.3	AEM EXAMPLE	4-10

5	ADM KVN Syntax	5-1

5.1	Introduction	5-1

5.2	APM	5-1

5.3	AEM	5-1

5.4	Lines	5-1

5.5	Keywords	5-1

5.6	Values	5-2

5.7	Units	5-4

5.8	Comments	5-4

6	ADM XML Syntax	6-7

6.1	Introduction	6-7

7	Security	7-1

7.1	Introduction	7-1

7.2	Security Concerns with Respect to this Recommended Standard	7-1

7.3	Potential Threats and Attack Scenarios	7-2

7.4	Consequences of Not Applying STATED Security to the Technology	7-2

7.5	Data Security Implementation Specifics	7-2

ANNEX A	VALUES FOR SELECTED KEYWORDS  (NORMATIVE)	B-1

ANNEX B	Rationale for Attitude Data Messages  
(Informative)	C-1

ANNEX C	ITEMS FOR AN INTERFACE CONTROL DOCUMENT  (Informative)	D-1

ANNEX D	ABBREVIATIONS AND ACRONYMS  (Informative)	E-1

ANNEX E	Informative References  (Informative)	F-1

Figure	Page

3-1	APM File Example Using Comments to Denote Updates	3-8

3-2	APM File Example Using Frame of Another Spacecraft	3-9

3-3	APM File Example Describing Sensor Frame to Body Frame Transform	3-9

3-4	APM File Example Describing Orientation of Instrument	3-10

3-5	APM File Example with Euler Angle Rates	3-10

3-6	APM File Example with Euler Angle Rates (Repeated Axis)	3-11

3-7	APM File Example with Mission Elapsed Time	3-12

3-8	APM File Example with Optional Euler Elements and One Maneuver	3-13

4-1	AEM Example	4-11

4-2	AEM Spinner Example	4-11

Table

3-1	APM Header	3-1

3-2	APM Metadata	3-2

3-3	APM Data	Erreur ! Signet non défini.

4-1	AEM File Layout Specifications	4-2

4-2	AEM Header	4-3

4-3	AEM Metadata	4-4

4-4	Types of Attitude Ephemeris Data Lines	4-7

B-1	Primary Requirements	C-2

B-2	Heritage Requirements	C-3

# CONTENTS (continued)

Table	Page

B-3	Desirable Characteristics	C-3

B-4	Applicability of the Criteria to Attitude Data Messages	C-4

B-5	Services Available with Attitude Data Messages	C-4

C-1	Items Recommended for an ICD	D-1

# INTRODUCTION

## PURPOSE

This Attitude Data Message (ADM) Recommended Standard specifies two standard message formats for use in transferring spacecraft attitude information between space agencies: the Attitude Parameter Message (APM) and the Attitude Ephemeris Message (AEM).  Such exchanges are used for:

- preflight planning for tracking or attitude estimation support;

- scheduling attitude and data processing support;

- carrying out attitude operations;

- performing attitude comparisons;

- carrying out attitude propagations and/or sensor predictions;

- testing to initialize sub-system simulators (communications, power, etc.).

This Recommended Standard includes sets of requirements and criteria that the message formats have been designed to meet.  For exchanges where these requirements do not capture the needs of the participating agencies, another mechanism may be selected.

## Scope and APPLICABILITY

This document contains two attitude data messages designed for applications involving data interchange in space data systems.  The rationale behind the design of each message is described in annex C and may help the application engineer to select a suitable message.  Definition of the attitude accuracy underlying a particular attitude message is outside of the scope of this Recommended Standard and should be specified via Interface Control Document (ICD) between data exchange participants.  Applicability information specific to each Attitude Data Message format appears in sections 3 and 4, as well as in annex subsection C3.

This Recommended Standard is applicable only to the message format and content, but not to its transmission.  The transmission of the message between agencies is outside the scope of this document and should be specified in an ICD or by following a CCSDS standard on transmission.

Description of the message formats based on the use of the eXtensible Markup Language (XML) is available.  An XML schema is defined by the CCSDS Recommended Standard titled ‘XML Specification for Navigation Data Messages’ (reference [5]).  Agencies should specify, via ICD, the ASCII file format to be exchanged (Keyword Value Notation [KVN] or XML).

## Conventions and Definitions

The following conventions apply throughout this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification; and

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

## Structure of this document

Section 2 provides a brief overview of the CCSDS-recommended Attitude Data Message types, the Attitude Parameter Message (APM) and Attitude Ephemeris Message (AEM).

Section 3 provides details about the structure and content of the APM.

Section 4 provides details about the structure and content of the AEM.

Section 5 provides details regarding syntax of the APM and AEM messages for the KVN format.

Section 6 provides details regarding syntax of the APM and AEM messages for the XML format.

Section 7 provides information regarding security concerns related to the access and transmission of the Attitude Data Messages.

Annex A provides conventions relative to quaternion, euler angles and angular velocity vector.

Annex C provides a list of approved values for selected keywords in the ADM Metadata sections.

Annex C lists a set of requirements that were taken into consideration in the design of the APM and AEM, along with tables and discussion regarding the applicability of the two message types to various attitude estimation tasks and functions.

Annex D lists a number of items that should be covered in ICDs prior to exchanging ADMs on a regular basis.  There are several statements throughout the document that refer to the desirability or necessity of such a document; this annex lists all the suggested ICD items in a single place in the document.

Annex E is a list of abbreviations and acronyms applicable to the ADM.

Annex F is a list of informative references.

## References

The following documents contain provisions which, through reference in this text, constitute provisions of this Recommended Standard.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this Recommended Standard are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS Recommended Standards.

[1]	Information Technology—8-Bit Single-Byte Coded Graphic Character Sets—Part 1: Latin Alphabet No. 1.  International Standard, ISO/IEC 8859-1:1998.  Geneva:  ISO, 1998.

[2]	Spacewarn Bulletin. Greenbelt, MD, USA: WDC-SI.  <http://nssdc.gsfc.nasa.gov/spacewarn>

[3]	JPL Solar System Dynamics.  Pasadena, CA, USA: JPL.  <http://ssd.jpl.nasa.gov>

[4]	Time Code Formats.  Recommendation for Space Data System Standards, CCSDS 301.0-B-3.  Blue Book.  Issue 3.  Washington, D.C.: CCSDS, January 2002.

[5]	XML Specification for Navigation Data Messages.  Draft Recommendation for Space Data System Standards, CCSDS 505.0-R-1.  Red Book.  Issue 1.  Washington, D.C.: CCSDS, November 2005.

[6]	IEEE Standard for Binary Floating-Point Arithmetic.  IEEE Std 754-1985.  New York: IEEE, 1985.

[7]	Orbit Data Messages.  Recommendation for Space Data System Standards, CCSDS 502.0-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, September 2004.

NOTE	–	A list of informative references can be found in annex F.

# Overview

## attitude data Message types

Two CCSDS-recommended Attitude Data Messages (ADMs) are described in this Recommended Standard: the Attitude Parameter Message (APM) and the Attitude Ephemeris Message (AEM).

The recommended attitude data messages are ASCII text format.  While binary-based attitude data message formats are computer efficient and minimize overhead on uplinked/downlinked data streams, there are ground-segment applications for which an ASCII character-based message is more appropriate.  For example, when files or data objects are created using text editors or word processors, ASCII character-based attitude data format representations are necessary.  They are also useful in transferring text files between heterogeneous computing systems, because the ASCII character set is nearly universally used and is interpretable by all popular systems.  In addition, direct human-readable downloads of text files or objects to displays or printers are possible without preprocessing.  The penalty for this convenience is inefficiency.

As currently specified, an APM or AEM file is to represent attitude data for a single object.

## ATTITUDE Parameter Message (APM)

An APM specifies the attitude state of a single object at a specified epoch.  This message is suited to inter-agency exchanges that (1) involve automated interaction and/or human interaction.

The APM requires the use of a propagation technique to determine the attitude state at times different from the specified epoch, leading to a higher level of effort for software implementation than for the AEM. .

The APM allows for modeling of any number of finite maneuvers and simple modeling of solar radiation pressure and atmospheric torque.  Note that an Orbit Parameter Message (OPM) is needed for proper solar radiation pressure modeling.

## ATTITUDE Ephemeris Message (AEM)

An AEM specifies the attitude state of a single object at multiple epochs, contained within a specified time range.  The AEM is suited to inter-agency exchanges that (1) involve automated interaction (e.g., computer-to-computer communication where frequent, fast, automated time interpretation and processing are required), and (2) require high fidelity or high precision dynamic modeling.

The AEM requires the use of an interpolation technique to interpret the attitude state at times different from the tabular epochs.

.

## Message formats

Two formats exist for the APM and AEM : KVN and XML. The two formats are equivalent and enable the representation of the same data. Which one to use mainly depends on the available tools used to read or write the data.

## Exchange of multiple messages

For a given object, multiple APM or AEM messages may be provided in a message exchange session to achieve attitude fidelity requirements.  If attitude information for multiple objects is to be exchanged, then multiple APM or AEM files may be used.

## Exchange Scheme

The method of exchanging ADMs shall be decided on a case-by-case basis by the participating agencies and documented in an ICD.

The ADM file naming scheme shall be agreed to on a case-by-case basis between the participating agencies, and should be documented in ICD.

# ATTITUDE PARAMETER MESSAGE (APM)

## Overview

Attitude information may be exchanged between two participants by sending the attitude state (see reference [F4]) for a specified epoch using an Attitude Parameter Message (APM).  The APM shall consist of attitude data for a single object.  It shall be easily readable by both humans and computers.

The APM file naming scheme shall be agreed to on a case-by-case basis between the participating agencies, and should be documented in an ICD.  The method of exchanging APMs shall be decided on a case-by-case basis by the participating agencies and documented in an ICD.

## APM Content

### General

The APM shall have the following structure:

- a header;

- metadata (data about the data);

- data.

Table XXX:  APM structure

| Section | Content |
| --- | --- |
| Header | Header of message |
| Metadata | Metadata (Information about the data) |
| Data | Data |

### APM header

Table 3-1 specifies for each header item:

- the keyword to be used;

- a short description of the item;

- examples of allowed values; and

- whether the item is obligatory or optional.

Only those keywords shown in table 3-1 shall be used in an APM header.

Table 3-1:  APM Header

| Keyword | Description | Examples of Values | Obligatory |
| --- | --- | --- | --- |
| CCSDS_APM_VERS | Format version in the form of ‘x.y’, where ‘y’ is incremented for corrections and minor changes, and ‘x’ is incremented for major changes. | 2.0 | Yes |
| COMMENT | Comments (allowed at the beginning of the APM header after the APM version number). There may be more than one comment, each one beginning with this keyword. | This is a comment | No |
| CREATION_DATE | File creation date/time in one of the following formats: YYYY-MM-DDThh:mm:ss[.d→d] or YYYY-DDDThh:mm:ss[.d→d] where ‘YYYY’ is the year, ‘MM’ is the two-digit month, ‘DD’ is the two-digit day, ‘DDD’ is the three-digit day of year, ‘T’ is constant, ‘hh:mm:ss[.d→d]’ is the UTC time in hours, minutes, seconds, and optional fractional seconds. As many ‘d’ characters to the right of the period as required may be used to obtain the required precision. All fields require leading zeros. | 2001-11-06T11:17:33 2002-204T15:56:23 1996-12-18T14:28:15.1172 | Yes |
| ORIGINATOR | Creating agency (value should be specified in an ICD). | CNES ESOC GSFC GSOC JPL JAXA | Yes |

### APM metadata

Table 3-2 specifies for each metadata item:

- the keyword to be used;

- a short description of the item;

- examples of allowed values; and

- whether the item is obligatory or optional.

Only those keywords shown in table 3-2 shall be used in APM metadata.  For some keywords (OBJECT_NAME, OBJECT_ID, CENTER_NAME) there are no definitive lists of authorized values maintained by a control authority; the references listed in 1.5 and annex F are the best known sources for authorized values to date.

Table 3-2:  APM Metadata

| Keyword | Description | Normative Values / Examples | Obligatory |
| --- | --- | --- | --- |
| COMMENT | Comments (allowed only at the beginning of the APM Metadata before OBJECT_NAME). There may be more than one comment, each one beginning with this keyword. | COMMENT This is a comment | No |
| OBJECT_NAME | Name of the object corresponding to the attitude data to be given. There is no CCSDS-based restriction on the value for this keyword, but it is recommended to use names from the SPACEWARN Bulletin (reference [2]), which include the Object name and international designator of the participant. | EUTELSAT W1 MARS PATHFINDER STS106 NEAR | Yes |
| OBJECT_ID | Spacecraft identifier of the object corresponding to the attitude data to be given. While there is no CCSDS-based restriction on the value for this keyword, the names could be drawn from the SPACEWARN Bulletin (reference [2]). If this is chosen, it is recommended that values have the format YYYY-NNNP{PP}, where: YYYY = year of launch; NNN = three-digit serial number of launch in year YYYY (with leading zeros); P{PP} = at least one capital letter for the identification of the part brought into space by the launch. In cases where the asset is not listed in the bulletin, the value should be provided in an ICD. | 2000-052A 1996-068A 2000-053A 1996-008A | Yes |
| OBJECT_FRAME | Name of object’s frame . See Annex B4 for of the list of recommended names. In cases where the object’s frame name is not listed, the value should be provided in an ICD. | BODY | No |
| REF_FRAME | Reference frame relative to which the attitude of the object is given. See annex B3 for the list of recommended names. | EME2000 TNW | Yes |
| CENTER_NAME | Origin of reference frame, which may be a natural solar system body (planets, asteroids, comets, and natural satellites), including any planet barycenter or the solar system barycenter, or another spacecraft (in this the value for ‘CENTER_NAME’ is subject to the same rules as for ‘OBJECT_NAME’). There is no CCSDS-based restriction on the value for this keyword, but for natural bodies it is recommended to use names from the NASA/JPL Solar System Dynamics Group (reference [3]). | EARTH EARTH BARYCENTER MOON SOLAR SYSTEM BARYCENTER SUN JUPITER BARYCENTER STS 106 EROS | No |
| TIME_SYSTEM | Time system used for attitude and maneuver data . The full set of allowed values is enumerated in annex B, with an excerpt provided in the ‘Normative Values/Examples’ column. Explanations of these time systems can be found in Navigation Definitions and Conventions (reference [F4]). | UTC TAI TT GPS TDB UTC | Yes |
| CONTENTS | Message contents ; names of the data blocks that are defined in the message. The possible data block names are : QUATERNION, EULER, ANGULAR_VELOCITY, SPIN, INERTIA and MANEUVER The order does not matter. All block names must be different from each other. | QUATERNION EULER SPIN | No |

### APM Data

Introduction

An APM data block shall have the following structure :

- a header : comment and epoch

- a list of data blocks as defined below

Table XXX:  APM data structure

| Section | Content |
| --- | --- |
| Header | Header of data |
| Data blocks | Data List of data blocks |

Data header

The data header shall have the following structure :

| Keyword | Description | Normative Units/Values | Obligatory |
| --- | --- | --- | --- |
| COMMENT | Zero or more comments See XXX for syntax | n/a | No |
| EPOCH | Epoch of attitude data. See XXX for syntax | n/a | Yes |

Data blocks

The data blocks may be given in any order. Each data block shall be contain the data as described in the tables below.

The meaning of the “obligatory” keyword in this section is to be considered under the condition that the block is present.

QUATERNION data block

The QUATERNION data block shall have the following structure:

| BLOCK | QUATERNION | n/a | Yes |
| --- | --- | --- | --- |
| Q1 | e1 * sin(/2)  = rotation angle | n/a | Yes |
| Q2 | e2 * sin(/2)  = rotation angle | n/a | Yes |
| Q3 | e3 * sin(/2)  = rotation angle | n/a | Yes |
| QC | cos(/2)  = rotation angle | n/a | Yes |
| Q1_DOT | Time derivative of Q1 | 1/s | No |
| Q2_DOT | Time derivative of Q2 | 1/s | No |
| Q3_DOT | Time derivative of Q3 | 1/s | No |
| QC_DOT | Time derivative of QC | 1/s | No |

Note: See Annex xxx for the definition of quaternion.

EULER data block

The EULER data block shall have the following structure:

| BLOCK | EULER | n/a | Yes |
| --- | --- | --- | --- |
| EULER_ROT_SEQ | Rotation sequence (X=X-axis, Y = Y-axis …) | XYZ ZXZ | Yes |
| ANGLE_1 | Angle of the first rotation in the sequence (= leftmost letter) | deg | Yes |
| ANGLE_2 | … | deg | Yes |
| ANGLE_3 | … | deg | Yes |
| ANGLE_1_DOT | Time derivative of ANGLE_1 | deg/s | No |
| ANGLE_2_DOT | … | deg/s | No |
| ANGLE_3_DOT | … | deg/s | No |

Note: See Annex xxx for the definition of Euler angles.

ANGULAR_VELOCITY data block

The ANGULAR_VELOCITY data block shall have the following structure :

| BLOCK | ANGULAR_VELOCITY | n/a | Yes |
| --- | --- | --- | --- |
| ANGVEL_FRAME | Coordinates frame where the components are given: only 2 values are accepted: OBJECT and REF. | OBJECT REF | Yes |
| ANGVEL_X | X component of the angular velocity vector of object frame with respect to reference frame (with components in ANGVEL_FRAME). | deg/s | Yes |
| ANGVEL_Y | X component of the angular velocity vector of object frame with respect to reference frame (with components in ANGVEL_FRAME). | deg/s | Yes |
| ANGVEL_Z | X component of the angular velocity vector of object frame with respect to reference frame (with components in ANGVEL_FRAME). | deg/s | Yes |

SPIN data block

The SPIN data block shall have the following structure:

| BLOCK | SPIN | n/a | Yes |
| --- | --- | --- | --- |
| SPIN_ALPHA | Right ascension of spin axis vector | deg | Yes |
| SPIN_DELTA | Declination of the spin axis vector | deg | Yes |
| SPIN_ANGLE | Phase of the satellite about the spin axis | deg | Yes |
| SPIN_ANGLE_VEL | Angular velocity of satellite around spin axis | deg/s | No |
| PRECESSION_ANGLE | Nutation angle of spin axis | deg | No |
| PRECESSION_PERIOD | Precession period of the spin axis | s | No |
| PRECESSION_PHASE | precession phase | deg | No |

Note: See Annex xxx for the definition of spin data.

INERTIA data block

The INERTIA data block shall have the following structure :

| BLOCK | INERTIA | n/a | Yes |
| --- | --- | --- | --- |
| INERTIA_ FRAME | Coordinate system for the inertia tensor | n/a | Yes |
| IXX | Moment of Inertia about the X-axis | kg*m**2 | NoYes |
| IYY | Moment of Inertia about the Y-axis | kg*m**2 | NoYes |
| I33IZZ | Moment of Inertia about the Z-axis | kg*m**2 | NoYes |
| I12IXY | Inertia Cross Product of the X & Y axes | kg*m**2 | NoYes |
| I13IXZ | Inertia Cross Product of the X & Z axes | kg*m**2 | NoYes |
| I23IYZ | Inertia Cross Product of the Y & Z axes | kg*m**2 | NoYes |

Since the inertia matrix of a rigid body is symmetric, it is necessary to only specify six elements instead of nine.  To reconstruct the full inertia matrix, the elements IYX = IXY, IZX = IXZ, and IZY = IYZ.  The inertia cross products used for this message assume a negative double integral

MANEUVER data block

The MANEUVER data block shall have the following structure:

| BLOCK | MANEUVER | n/a | Yes |
| --- | --- | --- | --- |
| MAN_EPOCH_START | Epoch of start of maneuver – see remark 1.1.1.1.1 | n/a | No |
| MAN_DURATION | Maneuver duration | s | No |
| MAN_ FRAME | Coordinate system for the torque vector | n/a | No |
| MAN_TOR_X | 1st component of the torque vector | N*m | No |
| MAN_TOR_Y | 2nd component of the torque vector | N*m | No |
| MAN_TOR_Z | 3rd component of the torque vector | N*m | No |

The maneuver data block may be repeated several times as required.

### Remarks

#### DATA FORMAT (KVN)

In specifying the EPOCH of the message, care must be taken if UTC is used as the TIME_SYSTEM.  If an APM message reports attitude during a time of leap seconds, the system making use of the message should be able to recognize 60 as a valid value for the seconds (e.g.,  200x-xx-xxT23:59:58.000 .. 200x-xx-xxT23:59:59.000 .. 200x-xx-xxT23:59:60.000 .. 200x-xx-xxT00:00:00.000)

#### GENERAL

It may become necessary to utilize particular orbit information to process Euler angle elements or a local orbit frame (e.g., LVLH, QSW) properly.  An approach to this is to add a ‘COMMENT’ block specifying a particular OPM message to use in conjunction with a particular APM.

### APM KEYWORD SET

The header shall include the CREATION_DATE keyword with the value set to the Coordinated Universal Time (UTC) when the file was created, formatted according to reference [4].  A description of APM header keywords and values is provided in table 3-1.

The first header line must be the first non-blank line in the file.

## APM Examples

Following figures show examples of Attitude Parameter Messages.

CCSDS_APM_VERS = 1.0

CREATION_DATE  = 2003-09-30T19:23:57

ORIGINATOR     = GSFC

COMMENT          GEOCENTRIC, CARTESIAN, EARTH FIXED

COMMENT          OBJECT_ID:  1997-009A

COMMENT $ITIM  = 1997 NOV 21 22:26:18.40000000, $ original launch time

OBJECT_NAME    = TRMM

OBJECT_ID      = 1997-009A

CENTER_NAME    = EARTH

TIME_SYSTEM    = UTC

COMMENT          Current attitude for orbit 335

COMMENT          Attitude state quaternion

COMMENT          Accuracy of this attitude is 0.02 deg RSS.

EPOCH          = 2003-09-30T14:28:15.1172

BLOCK          = QUATERNION

Q1             = 0.00005

Q2             = 0.87543

Q3             = 0.40949

QC             = 0.25678

Figure 3-1:  APM File Example Using Comments to Denote Updates

CCSDS_APM_VERS = 1.0

CREATION_DATE  = 2003-09-30T19:23:57

ORIGINATOR     = GSFC

COMMENT          GEOCENTRIC, CARTESIAN, EARTH FIXED

COMMENT          OBJECT_ID:  1999-068A

COMMENT $ITIM  = 1999 DEC 18 $ original launch time

OBJECT_NAME    = TERRA

OBJECT_ID      = 1999-068A

CENTER_NAME    = EARTH

TIME_SYSTEM    = UTC

COMMENT          Current attitude for orbit 335

COMMENT          Attitude state quaternion

COMMENT	      SC_BODY_A references EO-1 body frame

COMMENT	      OPM = EO1_2003_09_30_1900 2100.ephem

EPOCH          = 2003-09-30T14:28:15.1172

BLOCK          = QUATERNION

Q1             = 0.00005

Q2             = 0.00362

Q3             = 0.00013

QC             = 0.99934

Figure 3-2:  APM File Example Using Frame of Another Spacecraft

CCSDS_APM_VERS = 1.0

CREATION_DATE  = 2003-09-30T19:23:57

ORIGINATOR     = GSFC

COMMENT          OBJECT_ID:  1999-068A

COMMENT $ITIM  = 1999 DEC 18 $ original launch time

OBJECT_NAME    = TERRA

OBJECT_ID      = 1999-068A

CENTER_NAME    = EARTH

TIME_SYSTEM    = UTC

COMMENT          Current attitude for orbit 335

COMMENT          Attitude state quaternion

COMMENT	      Defines orientation between the body axes and DSS_1 sensor.

EPOCH          = 2003-09-30T14:28:15.1172

Q1             = 0.07481

Q2             = 0.38175

Q3             = 0.30317

QC             = 0.86992

Figure 3-3:  APM File Example Describing Sensor Frame to Body Frame Transform

CCSDS_APM_VERS = 1.0

CREATION_DATE  = 2003-09-30T19:23:57

ORIGINATOR     = GSFC

COMMENT          OBJECT_ID:  1999-068A

COMMENT $ITIM  = 1999 DEC 18 $ original launch time

OBJECT_NAME    = TERRA

OBJECT_ID      = 1999-068A

CENTER_NAME    = EARTH

TIME_SYSTEM    = UTC

COMMENT          Current attitude for orbit 335

COMMENT          Attitude state quaternion

COMMENT	      Defines orientation of MODIS (INSTRUMENT_A).

EPOCH          = 2003-09-30T14:28:15.1172

Q1             = 0.32915

Q2             = 0.12209

Q3             = 0.84888

QC             = 0.39517

Figure 3-4:  APM File Example Describing Orientation of Instrument

CCSDS_APM_VERS  = 1.0

CREATION_DATE   = 2004-02-14T19:23:57

ORIGINATOR      = GSFC

OBJECT_NAME     = TRMM

OBJECT_ID       = 1997-009A

CENTER_NAME     = EARTH

TIME_SYSTEM     = UTC

COMMENT           GEOCENTRIC, CARTESIAN, EARTH FIXED

COMMENT OBJECT_ID: 1997-009A

COMMENT $ITIM  = 1997 NOV 21 22:26:18.40000000, $ original launch time

COMMENT           Attitude state quaternion

EPOCH           = 2004-02-14T14:28:15.1172

BLOCK           = QUATERNION

Q1              = 0.03123

Q2              = 0.78543

Q3              = 0.39158

QC              = 0.47832

BLOCK           = EULER

EULER_ROT_SEQ   = ZXY

ANGLE1          =

ANGLE2          =

ANGLE3          =

Figure 3-5:  APM File Example with Euler Angle Rates

CCSDS_APM_VERS  = 1.0

CREATION_DATE   = 2006-03-13T13:13:33

ORIGINATOR      = GSFC

OBJECT_NAME     = GOES-P

OBJECT_ID       = 2006-003A

CENTER_NAME     = EARTH

TIME_SYSTEM     = UTC

COMMENT           GEOSYNCHRONOUS, CARTESIAN, EARTH FIXED

COMMENT OBJECT_ID: 2006-003A

COMMENT $ITIM  = 2006 FEB 5 03:23:45.60000000, $ original launch time

COMMENT           Attitude state quaternion

EPOCH           = 2006-03-12T09:56:39.4987

BLOCK           = QUATERNION

Q1              = 0.03123

Q2              = 0.78543

Q3              = 0.39158

QC              = 0.47832

BLOCK           = EULER

EULER_FRAME_A   = SC_BODY_1

EULER_FRAME_B   = ITRF-97

EULER_DIR	     = A2B

EULER_ROT_SEQ   = 212

RATE_FRAME	     = EULER_FRAME_A

Y_ANGLE	     = -26.78 [deg ]

X_ANGLE	     =  46.26 [deg ]

Y_ANGLE	     = 144.10 [deg ]

Y_RATE          = 0.1045   [deg/s]

X_RATE          = 0.03214  [deg/s]

Y_RATE          = 0.02156  [deg/s]

Figure 3-6:  APM File Example with Euler Angle Rates (Repeated Axis)

CCSDS_APM_VERS  = 1.0

CREATION_DATE   = 2008-03-08T13:13:33

ORIGINATOR      = JSC

OBJECT_NAME     = ISS

OBJECT_ID       = 2008-003A

CENTER_NAME     = EARTH

TIME_SYSTEM     = MET

COMMENT           International Space Station, Kibo segment

COMMENT    OBJECT_ID: 2008-003A

COMMENT    MET Relative to the following Epoch:

COMMENT    UTC   2008-03-12T06:54:37

COMMENT           Attitude state quaternion

EPOCH           = 0000-045T15:43:28.93

Q_FRAME_A	     = SC_BODY_1

Q_FRAME_B       = J2000

Q_DIR	     = A2B

Q1              = 0.03123

Q2              = 0.78543

Q3              = 0.39158

QC              = 0.47832

COMMENT           Euler rates

EULER_FRAME_A   = SC_BODY_1

EULER_FRAME_B   = J2000

EULER_DIR	     = A2B

EULER_ROT_SEQ   = 123

RATE_FRAME	     = EULER_FRAME_A

X_RATE          = 0.05901   [deg/s]

Y_RATE          = 0.00348  [deg/s]

Z_RATE          = 0.00214  [deg/s]

Figure 3-7:  APM File Example with Mission Elapsed Time

CCSDS_APM_VERS  = 1.0

CREATION_DATE   = 2004-02-14T19:23:57

ORIGINATOR      = JPL

OBJECT_NAME     = MARS SPIRIT

OBJECT_ID       = 2004-003A

CENTER_NAME     = EARTH

TIME_SYSTEM     = UTC

COMMENT           GEOCENTRIC, CARTESIAN, EARTH FIXED

COMMENT OBJECT_ID: 2004-003

COMMENT  $ITIM  = 2004 JAN 14 22:26:18.400000, $ original launch time 14:36

COMMENT           Generated by JPL

COMMENT           Current attitude for orbit 20 and attitude maneuver

COMMENT           planning data.

COMMENT           Attitude state quaternion

EPOCH           = 2004-02-14T14:28:15.1172

Q_FRAME_A	     = INSTRUMENT_A

Q_FRAME_B       = ITRF-97

Q_DIR	     = A2B

Q1              = 0.03123

Q2              = 0.78543

Q3              = 0.39158

QC              = 0.47832

COMMENT           Attitude specified as Euler elements

EULER_FRAME_A   = INSTRUMENT_A

EULER_FRAME_B   = ITRF-97

EULER_DIR	     = A2B

EULER_ROT_SEQ   = 312

RATE_FRAME	     = EULER_FRAME_A

Z_ANGLE         = -53.3688 [deg]

X_ANGLE         = 139.7527 [deg]

Y_ANGLE         = 25.0658  [deg]

Z_RATE          = 0.02156  [deg/s]

X_RATE          = 0.1045   [deg/s]

Y_RATE          = 0.03214  [deg/s]

COMMENT           Spacecraft Parameters

I11             = 6080.0   [kg*m**2]

I22             = 5245.5   [kg*m**2]

I33             = 8067.3   [kg*m**2]

I12             = -135.9   [kg*m**2]

I13             = 89.3     [kg*m**2]

I23             = -90.7    [kg*m**2]

COMMENT           Data follows for 1 planned maneuver.

COMMENT           First attitude maneuver for: MARS SPIRIT

COMMENT           Impulsive, torque direction fixed in body frame

MAN_EPOCH_START = 2004-02-14T14:29:00.5098

MAN_DURATION    = 3        [s]

MAN_REF_FRAME   = INSTRUMENT_A

MAN_TOR_1       = -1.25    [N*m]

MAN_TOR_2       = -0.5     [N*m]

MAN_TOR_3       = 0.5      [N*m]

Figure 3-8:  APM File Example with Optional Euler Elements and One Maneuver

# ATTITUDE EPHEMERIS MESSAGE (AEM)

## Overview

Attitude state information may be exchanged between participants by sending an ephemeris in the form of a series of attitude states using an Attitude Ephemeris Message (AEM).  The message recipient must have a means of interpolating across these attitude states to obtain the attitude state at an arbitrary time contained within the span of the attitude ephemeris.

The AEM shall be a text file consisting of attitude data for a single object.  It shall be easily readable by both humans and computers.

The file naming scheme shall be agreed to on a case-by-case basis between the participating agencies, typically using an Interface Control Document (ICD).  The method of exchanging AEMs shall be decided on a case-by-case basis by the participating agencies and documented in an ICD.

## AEM content

### General

The AEM shall be represented as a combination of the following:

- a header;

- metadata (data about data);

- attitude data.

- Optional comments may be present as indicated below.

AEM files must have a set of minimum required sections; some may be repeated.

Table 4-1 outlines the contents of an AEM.

Table 4-1:  AEM File Layout Specifications

| Item |  |  | Obligatory? |
| --- | --- | --- | --- |
| Header |  |  | Yes |
| Body | Segment 1 | Metadata 1 | Yes |
|  |  | Data 1 |  |
|  | Segment 2 | Metadata 2 | No |
|  |  | Data 2 |  |
|  | . . . | . . . | No |
|  | Segment n | Metadata n | No |
|  |  | Data n |  |

### AEM Header

The AEM header assignments are shown in table 4-2, which specifies for each item:

- the keyword to be used;

- a short description of the item;

- examples of allowed values; and

- whether the item is obligatory or optional.

Only those keywords shown shall be used in an AEM header.

Table 4-2:  AEM Header

| Keyword | Description | Normative Values / Examples | Obligatory |
| --- | --- | --- | --- |
| CCSDS_AEM_VERS | Format version in the form of ‘x.y’, where ‘y’ is incremented for corrections and minor changes, and ‘x’ is incremented for major changes. | 2.0 | Yes |
| COMMENT | Comments (allowed after AEM version number and META_START and before a data block of ephemeris lines). Each comment line shall begin with this keyword. | This is a comment. | No |
| CREATION_DATE | File creation date/time in one of the following formats: YYYY-MM-DDThh:mm:ss[.d→d] or YYYY-DDDThh:mm:ss[.d→d] where ‘YYYY’ is the year, ‘MM’ is the two-digit month, ‘DD’ is the two-digit day, ‘DDD’ is the three-digit day of year, ‘T’ is constant, ‘hh:mm:ss[.d→d]’ is the UTC time in hours, minutes, seconds, and optional fractional seconds. As many ‘d’ characters to the right of the period as required may be used to obtain the required precision. All fields require leading zeros. | 2001-11-06T11:17:33 2002-204T15:56:23 1996-12-18T14:28:15.1172 | Yes |
| ORIGINATOR | Creating agency (value should be specified in an ICD). | CNES, ESOC, GSFC, GSOC, JPL, JAXA, etc. | Yes |

### AEM metadata

The AEM metadata assignments are shown in table 4-3, which specifies for each item:

- the keyword to be used;

- a short description of the item;

- examples of allowed values; and

- whether the item is obligatory or optional.

Only those keywords shown shall be used in AEM metadata.  For some keywords (OBJECT_NAME, OBJECT_ID, CENTER_NAME) there are no definitive lists of authorized values maintained by a control authority; the references listed in 1.5 are the best known sources for authorized values to date.

Table 4-3:  AEM Metadata

| Keyword | Description | Normative Values / Examples | Obligatory |
| --- | --- | --- | --- |
| META_START | The AEM message contains both metadata and attitude ephemeris data; this keyword is used to delineate the start of a metadata block within the message (metadata are provided in a block, surrounded by ‘META_START’ and ‘META_STOP’ markers to facilitate file parsing). This keyword must appear on a line by itself. | n/a | Yes |
| COMMENT | Comments allowed only at the beginning of the Metadata section. Each comment line shall begin with this keyword. | COMMENT This is a comment. | No |
| OBJECT_NAME | Spacecraft name of the object corresponding to the attitude data to be given. There is no CCSDS-based restriction on the value for this keyword, but it is recommended to use names from the SPACEWARN Bulletin (reference [2]), which include the Object name and international designator of the participant. | EUTELSAT W1 MARS PATHFINDER STS106 NEAR | Yes |
| OBJECT_ID | Spacecraft identifier of the object corresponding to the attitude data to be given. While there is no CCSDS-based restriction on the value for this keyword, the names could be drawn from the SPACEWARN Bulletin (reference [2]). If this is chosen, it is recommended that values have the format YYYY-NNNP{PP}, where: YYYY = year of launch; NNN = three-digit serial number of launch in year YYYY (with leading zeros); P{PP} = At least one capital letter for the identification of the part brought into space by the launch. In cases where the asset is not listed in the bulletin, the value should be provided in an ICD. | 2000-052A 1996-068A 2000-053A 1996-008A | Yes |
| OBJECT_FRAME | Name of object’s frame . See Annex B4 for of the list of recommended names. In cases where the object’s frame name is not listed, the value should be provided in an ICD. | BODY | No |
| CENTER_NAME | Origin of reference frame, which may be a natural solar system body (planets, asteroids, comets, and natural satellites), including any planet barycenter or the solar system barycenter, or another spacecraft (in this the value for ‘CENTER_NAME’ is subject to the same rules as for ‘OBJECT_NAME’). There is no CCSDS-based restriction on the value for this keyword, but for natural bodies it is recommended to use names from the NASA/JPL Solar System Dynamics Group (reference [3]). | EARTH EARTH BARYCENTER MOON SOLAR SYSTEM BARYCENTER SUN JUPITER BARYCENTER STS 106 EROS | No |
| REF_FRAME | Reference frame relative to which the attitude of the object is to be given. See annex XXX for list. | EME2000 | Yes |
|  |  |  | Yes |
|  |  |  | Yes |
| TIME_SYSTEM | Time system used for both attitude ephemeris data and metadata (also see tables 4-3 and 4-4). The full set of allowed values is enumerated in annex B, with an excerpt provided in the ‘Values/Examples’ column. Explanations of these time systems can be found in Navigation Definitions and Conventions (reference [F4]). | UTC TAI TT GPS TDB UTC | Yes |
| START_TIME | Start of TOTAL time span covered by attitude ephemeris data immediately following this metadata block. The START_TIME time tag at a new block of attitude ephemeris data must be equal to or greater than the STOP_TIME time tag of the previous block. | 1996-12-18T14:28:15.1172 2001-277T07:22:54 | Yes |
| USEABLE_ START_TIME, USEABLE_ STOP_TIME | Optional start and end of USEABLE time span covered by attitude ephemeris data immediately following this metadata block. To allow for proper interpolation near the ends of the attitude ephemeris data block, it may be necessary, depending upon the interpolation method to be used, to utilize these keywords with values within the time span covered by the attitude ephemeris data records as denoted by the START/STOP_TIME time tags. | 1996-12-18T14:28:15.1172 2001-277T07:22:54 | No |
| STOP_TIME | End of TOTAL time span covered by the attitude ephemeris data immediately following this metadata block. The STOP_TIME time tag for the block of attitude ephemeris data must be equal to or less than the START_TIME time tag of the next block. | 1996-12-18T14:28:15.1172 2001-277T07:22:54 | Yes |
| ATTITUDE_TYPE | The format of the data lines in the message. This keyword must have a value from the set specified at the right. See 4.2.5 for details of the data contained in each line. | QUATERNION QUATERNION/DERIVATIVE QUATERNION/RATE EULER_ANGLE EULER_ANGLE/DERIVATIVE EULER_ANGLE/RATE SPIN SPIN/NUTATION | Yes |
| EULER_ROT_SEQ | The rotation sequence, that is the successive axes names of the 3 successive rotations with (X: X axis, Y; Yaxis). See annex XXX for examples | ZXZ XYZ | No |
| RATE_FRAME | The frame in which the coordinates of the angular velocity vector are given. Only 2 values are accepted: OBJECT and REF. | OBJECT REF | No |
| INTERPOLATION_METHOD | Recommended interpolation method for attitude ephemeris data in the block immediately following this metadata block. | LINEAR HERMITE lagrange | No |
| INTERPOLATION_DEGREE | Recommended interpolation degree for attitude ephemeris data in the block immediately following this metadata block. It must be an integer value. This keyword must be used if the ‘INTERPOLATION_METHOD’ keyword is used. | 5 1 | No |
| META_STOP | The end of a metadata block within the message. The AEM message contains both metadata and attitude ephemeris data; this keyword is used to delineate the end of a metadata block within the message (metadata are provided in a block, surrounded by ‘META_START’ and ‘META_STOP’ markers to facilitate file parsing). This keyword must appear on a line by itself. | n/a | Yes |

Keywords START_TIME, USEABLE_START_TIME, USEABLE_STOP_TIME, and STOP_TIME all denote a spacecraft event time.

### AEM Data

See 4.2.5, Attitude Ephemeris Data Lines, for specifications regarding AEM data.

The Data section of the AEM shall be delineated by the ‘DATA_START’ and ‘DATA_STOP’ keywords.  These keywords are intended to facilitate parsing, and will also serve to advise the recipient that all the attitude data records associated with the immediately preceding AEM Metadata section have been received (the rationale for including this is that data volumes can be very large, so knowing when the data begins and ends is desirable).  The AEM recipient may process the ‘DATA_STOP’ keyword as a ‘local’ end-of-file marker.

### Attitude ephemeris data lines

For AEMs, each set of attitude ephemeris data, including the time tag, must be provided on a single line.  Table 4-4 lists the allowable combinations of data items, with each item following the same definition as given in table Erreur ! Source du renvoi introuvable..  The order in which the data items are given shall be fixed as in table 4-4, with the exception of Euler angle data for which the order of angle data must correspond with the sequence given by EULER_ROT_SEQ.

The choice of one of the formats in table 4-4 shall be specified via the ATTITUDE_TYPE keyword in the metadata.

Table 4-4:  Types of Attitude Ephemeris Data Lines

| Keyword | Value | Ephemeris Data Line |
| --- | --- | --- |
| Quaternion Options (note that keywords and values appear only in Metadata) |
| ATTITUDE_TYPE | QUATERNION | Epoch, QC, Q1, Q2, Q3 |
|  | QUATERNION/DERIVATIVE | Epoch, QC, Q1, Q2, Q3, QC_DOT, Q1_DOT, Q2_DOT, Q3_DOT |
|  | QUATERNION/ RATE | Epoch, QC, Q1, Q2, Q3, X_RATE, Y_RATE, Z_RATE |
| Euler Angle Options (note that keywords and values appear only in Metadata) |
| ATTITUDE_TYPE | EULER_ANGLE | Epoch, ANGLE1, ANGLE2, ANGLE3 |
|  | EULER_ANGLE/DERIVATIVESRATE | Epoch, ANGLE1, ANGLE2, ANGLE3, ANGLE1_DOT, ANGLE2_DOT, ANGLE3_DOT |
|  | EULER_ANGLE/ RATE | Epoch, X_ANGLE, Y_ANGLE, Z_ANGLE, X_RATE, Y_RATE, Z_RATE |
| Spin Axis Options (note that keywords and values appear only in Metadata) |
| ATTITUDE_TYPE | SPIN | Epoch, SPIN_ALPHA, SPIN_DELTA, SPIN_ANGLE, SPIN_ANGLE_VEL |
|  | SPIN/NUTATION | Epoch, SPIN_ALPHA, SPIN_DELTA, SPIN_ANGLE, SPIN_ANGLE_VEL, NUTATION, NUTATION_PER, NUTATION_PHASE |

#### FORMAT

At least one space character must be used to separate the items in each attitude ephemeris data line.

#### TECHNICAL

Attitude ephemeris data lines must be ordered by increasing time, and time tags must not be repeated, except in the case where the STOP_TIME of a set of attitude ephemeris data lines is equal to the START_TIME of the following set of attitude ephemeris data lines.  The time step duration may vary within a given AEM.

The occurrence of a second (or greater) metadata block after some attitude ephemeris data shall indicate that interpolation using succeeding attitude ephemeris data with attitude ephemeris data occurring prior to that metadata block shall not be done.  This method may be used for proper modeling of propulsive maneuvers or any other source of a discontinuity such as eclipse entry or exit.

Details about the interpolation method should be specified using the INTERPOLATION_METHOD and INTERPOLATION_DEGREE keywords within the AEM.  All data blocks must contain a sufficient number of attitude ephemeris data records to allow the recommended interpolation method to be carried out consistently throughout the AEM.

Note on rotations

### AEM format

### AEM structure

### Increasing dates…

### AEM Keyword set

The header shall provide a CCSDS Attitude Data Message version number that identifies the format version; this is included to anticipate future changes.  The version keyword shall be CCSDS_AEM_VERS and the value shall have the form of ‘x.y’, where ‘y’ is incremented for corrections and minor changes, and ‘x’ is incremented for major changes.  Version 1.0 shall be reserved for the initial version accepted by the CCSDS as an official Recommended Standard (‘Blue Book’).  Testing shall be conducted using AEM version numbers less than 1.0 (e.g., 0.x).  Participating agencies should specify in the ICD the specific AEM version numbers they will support.

The header shall include the CREATION_DATE keyword with the value set to the Coordinated Universal Time (UTC) when the file was created, according to reference [4].  A description of AEM header keywords and values is provided in table 4-2.

The first header line must be the first non-blank line in the file.

Only those keywords shown in tables 4-2 and 4-3 shall be used in an AEM.  Some keywords represent obligatory items and some are optional.  KVN assignments representing optional items may be skipped.  The two USEABLE_START/STOP_TIME keywords, marked as optional items, may not be necessary depending on the recommended interpolation method. (It is safer to use the USEABLE_START/STOP_TIME capability in all cases.)

A single METADATA group shall precede each attitude ephemeris data block.  Multiple occurrences of a METADATA group followed by an attitude ephemeris data block may be used (e.g., METADATA, DATA, METADATA, DATA, etc.).

Before each METADATA group the string ‘META_START’ shall appear on a separate line and after each METADATA group (and before the associated DATA_START keyword) the string ‘META_STOP’ shall appear on a separate line.

## AEM EXAMPLE

Figure 4-1 is an example of an AEM.  Note that some attitude ephemeris lines were omitted.

CCSDS_AEM_VERS = 1.0

CREATION_DATE = 2002-11-04T17:22:31

ORIGINATOR = NASA/JPL

META_START

COMMENT  This file was produced by M.R. Somebody, MSOO NAV/JPL, 2002 OCT 04.

COMMENT  It is to be used for attitude reconstruction only.  The relative accuracy of these COMMENT   attitudes is 0.1 degrees per axis.

OBJECT_NAME          = MARS GLOBAL SURVEYOR

OBJECT_ID            = 1996-062A

CENTER_NAME          = mars barycenter

REF_FRAME_A          = EME2000

REF_FRAME_B          = SC_BODY_1

ATTITUDE_DIR	      = A2B

TIME_SYSTEM          = UTC

START_TIME           = 1996-11-28T21:29:07.2555

USEABLE_START_TIME   = 1996-11-28T22:08:02.5555

USEABLE_STOP_TIME    = 1996-11-30T01:18:02.5555

STOP_TIME            = 1996-11-30T01:28:02.5555

ATTITUDE_TYPE        = QUATERNION

QUATERNION_TYPE      = LAST

INTERPOLATION_METHOD = hermite

INTERPOLATION_DEGREE = 7

META_STOP

DATA_START

1996-11-28T21:29:07.2555 0.56748   0.03146   0.45689   0.68427

1996-11-28T22:08:03.5555 0.42319   -0.45697  0.23784   0.74533

1996-11-28T22:08:04.5555 -0.84532  0.26974   -0.06532  0.45652

< intervening data records omitted here >

1996-11-30T01:28:02.5555  0.74563   -0.45375   0.36875   0.31964

DATA_STOP

META_START

COMMENT   This block begins after trajectory correction maneuver TCM-3.

OBJECT_NAME          = mars global surveyor

OBJECT_ID            = 1996-062A

CENTER_NAME          = MARS BARYCENTER

REF_FRAME_A          = EME2000

REF_FRAME_B	      = SC_BODY_1

ATTITUDE_DIR	      = A2B

TIME_SYSTEM          = UTC

START_TIME           = 1996-12-18T12:05:00.5555

USEABLE_START_TIME   = 1996-12-18T12:10:00.5555

USEABLE_STOP_TIME    = 1996-12-28T21:23:00.5555

STOP_TIME            = 1996-12-28T21:28:00.5555

ATTITUDE_TYPE        = QUATERNION

QUATERNION_TYPE      = LAST

META_STOP

DATA_START

1996-12-18T12:05:00.5555  -0.64585  0.018542   -0.23854  0.72501

1996-12-18T12:10:05.5555  0.87451   -0.43475   0.13458   -0.16767

1996-12-18T12:10:10.5555  0.03125   -0.65874   0.23458   -0.71418

< intervening records omitted here >

1996-12-28T21:28:00.5555  -0.25485  0.58745   -0.36845   0.67394

DATA_STOP

Figure 4-1:  AEM Example

Figure 4-2 is an example of an AEM describing a spinning spacecraft.  Note that some attitude ephemeris lines were omitted.

CCSDS_AEM_VERS = 1.0

CREATION_DATE      = 2008-071T17:09:49

ORIGINATOR         = GSFC FDF

META_START

OBJECT_NAME        = ST5-224

OBJECT_ID          = 2006224

CENTER_NAME        = EARTH

REF_FRAME_A        = J2000

REF_FRAME_B        = SC_BODY_1

ATTITUDE_DIR       = A2B

TIME_SYSTEM        = UTC

START_TIME         = 2006-090T05:00:00.071

USEABLE_START_TIME = 2006-090T05:00:00.071

USEABLE_STOP_TIME  = 2006-090T05:00:00.946

STOP_TIME          = 2006-090T05:00:00.946

ATTITUDE_TYPE      = SPIN

META_STOP

DATA_START

COMMENT              Spin KF ground solution, SPINKF rates

2006-090T05:00:00.071   2.6862511e+002  6.8448486e+001  1.5969509e+002 -1.0996528e+002

2006-090T05:00:00.196   2.6863990e+002  6.8432197e+001  1.4593720e+002 -1.0996493e+002

2006-090T05:00:00.321   2.6864591e+002  6.8412960e+001  1.3218766e+002 -1.0996455e+002

2006-090T05:00:00.446   2.6863697e+002  6.8392049e+001  1.1845280e+002 -1.0996402e+002

2006-090T05:00:00.571   2.6861072e+002  6.8371266e+001  1.0473305e+002 -1.0996370e+002

2006-090T05:00:00.696   2.6856625e+002  6.8353279e+001  9.1030304e+001 -1.0996339e+002

2006-090T05:00:00.821   2.6850631e+002  6.8340398e+001  7.7341548e+001 -1.0996317e+002

2006-090T05:00:00.946   2.6843571e+002  6.8332398e+001  6.3662262e+001 -1.0996304e+002

DATA_STOP

Figure 4-2:  AEM Spinner Example

# ADM KVN Syntax

## Introduction

This section details the syntactical requirements for attitude messages.  All APM and AEM messages shall observe the syntax described in subsections 5.2 through 5.6.

## APM

The APM shall be a plain text file, using keyword descriptions given in 3.2.1 through 3.2.6.

## AEM

The AEM shall be a plain text file, using the keyword descriptions given in 4.2.1 through 4.2.8.

## Lines

Each APM and AEM line must not exceed 254 ASCII characters and spaces (excluding line termination character[s]).

Only printable ASCII characters and blanks shall be used.  Control characters (such as TAB, etc.) shall not be used, except as indicated below for the termination of lines.

Blank lines may be used at any position within the file.

Comment lines shall be optional.  See 5.8.2 for details regarding the placement of comment lines in an APM.  See 5.8.3 for details regarding the placement of comment lines in an AEM.

APM and AEM lines shall be terminated by a single Carriage Return or a single Line Feed, or a Carriage Return/Line Feed pair or a Line Feed/Carriage Return pair.

## Keywords

All header, metadata, and APM data lines, with exceptions as noted in 5.5.8, shall use ‘keyword = value’ notation, abbreviated as KVN.

Only a single ‘keyword = value’ assignment shall be made on a line.

Keywords must be uppercase and must not contain blanks.

Any white space immediately preceding or following the keyword shall not be significant.

Any white space immediately preceding or following the ‘equals’ sign shall not be significant.

Any white space immediately preceding the end of line shall not be significant.

The order of occurrence of obligatory and optional KVN assignments shall be fixed as shown in tables 3-1, 3-2, and Erreur ! Source du renvoi introuvable. for the APM, and as shown in tables 4-2 and 4-3 for the AEM.  Exceptions to this rule for the APM shall be for quaternion and Euler angle ordering, as described in 3.2.5.

The keywords COMMENT, META_START, META_STOP, DATA_START and DATA_STOP, and AEM data lines are exceptions to the KVN syntax.

## Values

The range of values for angle measurements is -360 degrees <= x <= 360 degrees.  If agencies wish to exchange using radians, this must be specified in an ICD because it is nominally outside the standard.

Blanks shall not appear within numeric values and time values.

Integer values shall consist of a sequence of decimal digits with an optional leading sign (‘+’ or ‘-’).  If the sign is omitted, ‘+’ shall be assumed.  Leading zeros may be used.  The range of values that may be expressed as an integer is:

-2 147 483 648 <= x <= +2 147 483 647 (i.e., -231 <= x <= 231-1).

Non-integer numeric values may be expressed in either fixed-point or floating-point notation.  Both representations may be used within an APM or an AEM.

Non-integer numeric values expressed in fixed-point notation shall consist of a sequence of decimal digits separated by a period as a decimal point indicator, with an optional leading sign (‘+’ or ‘-’).  If the sign is omitted, ‘+’ shall be assumed.  Leading and trailing zeros may be used.  At least 1 digit is required before and after a decimal point.  The number of digits shall be 16 or fewer.

Non-integer numeric values expressed in floating-point notation shall consist of a sign, a mantissa, an alphabetic character indicating the division between the mantissa and exponent, and an exponent, constructed according to the following rules:

- The sign may be ‘+’ or ‘-’.  If the sign is omitted, ‘+’ shall be assumed.

- The mantissa must be a string of no more than 16 decimal digits with a decimal point ‘.’ in the second position of the ASCII string, separating the integer portion of the mantissa from the fractional part of the mantissa.

- The character used to denote exponentiation shall be ‘E’ or ‘e’.  If the character indicating the exponent and the following exponent are omitted, an exponent value of zero shall be assumed (essentially yielding a fixed-point value).

- The exponent must be an integer, and may have either a ‘+’ or ‘-’ sign (if the sign is omitted, then ‘+’ shall be assumed).

- The maximum positive floating-point value is approximately 1.798E+308, with precision of 16 significant decimal digits.  The minimum positive floating-point value is approximately 4.94E-324, with precision of 16 significant decimal digits.

These specifications for integer, fixed-point, and floating-point values conform to the XML specifications for the data types four-byte integer ‘xsd:int’, ‘decimal’ and ‘double’ respectively.  The specifications for floating-point values conform to the IEEE double precision type (reference [6]).  Floating-point numbers in IEEE extended-single or IEEE extended-double precision may be represented, but do require an ICD between participating agencies because of their implementation-specific attributes (reference [6]).  Note that NaN, +Inf, -Inf, and -0 are not supported values.

Text value fields must be constructed using only all uppercase or all lowercase.

A non-empty value field must be specified for each keyword provided, except as noted in 5.5.8.

In value fields that are text, an underscore shall be equivalent to a single blank. Individual blanks between non-blank characters shall be retained (shall be significant) but multiple blanks shall be equivalent to a single blank.

In value fields that represent a timetag or epoch, one of the following two formats shall be used:

YYYY-MM-DD:Thh:mm:ss[.d(d][Z]

or

YYYY-DDDThh:mm:ss[.d(d][Z]

where ‘YYYY’ is the year, ‘MM’ is the two-digit month, ‘DD’ is the two-digit day, ‘DDD’ is the three-digit day of year, ‘T’ is constant, ‘hh:mm:ss[.d(d] is the time in hours, minutes seconds, and optional fractional seconds; ‘Z’ is an optional time code terminator (the only permitted value is ‘Z’ for Zulu, i.e., UTC).  All fields shall have leading zeros.  See reference [4], ASCII Time Code A and B.

## Units

### APM Restrictions

For clarity, units may be included as ASCII text after a value, but they must exactly match the units specified in table Erreur ! Source du renvoi introuvable. (including case).  If units are displayed, then:

- there must be at least one blank character between the value and the units text;

- the units must be enclosed within square brackets (e.g., ‘[deg]’);

- multiplication of units shall be denoted with a single asterisk ‘*’ (e.g., ‘[N*m]’).

- exponents of units shall be denoted with a double asterisk ‘**’ (e.g., ‘[kg*m**2]’).

### AEM Restrictions

In an AEM, units shall be assigned to the keywords as follows:

- dimensionless:  EPOCH, Q1, Q2, Q3, QC;

- 1/s:  Q1_DOT, Q2_DOT, Q3_DOT, QC_DOT;

- deg:  X_ANGLE, Y_ANGLE, Z_ANGLE, SPIN_ALPHA, SPIN_DELTA, SPIN_ANGLE, NUTATION, NUTATION_PHASE;

- deg/s:  X_RATE, Y_RATE, Z_RATE, SPIN_ANGLE_VEL;

- s:  NUTATION_PER.

Units shall not be displayed; the applicable units are determined by the value set for the ATTITUDE_TYPE keyword.

## Comments

### General

All comment lines shall begin with the ‘Comment’ keyword followed by at least one space.  This keyword must appear on every comment line, not just the first such line.  The remainder of the line shall be the comment value.  White space shall be retained (shall be significant) in comment values.

Comments may be used to provide provenance information or to help describe dynamical events or other pertinent information associated with the data.  This additional information is intended to aid in consistency checks and elaboration where needed, but shall not be required for successful processing of a file.

There are certain pieces of information that provide clarity and remove ambiguity about the interpretation of the information in a file, yet are not standardized so as to fit cleanly into the ‘keyword = value’ paradigm.  Rather than force the information to fit into a space limited to one line, the APM or AEM producer should put certain information into comments and use the ICD to provide further specifications.

The following comment should be provided in an APM or AEM message:  information regarding the genesis, history, interpretation, intended use, etc., of the attitude state and any additional information that may be of use to the receiver of the APM or AEM.  Example:

COMMENT  Source: File created by GSFC Flight Dynamics Facility as part

COMMENT  of Launch Operations Readiness Test held on 15 July 2004.

### APM Specific

Comments are optional and may appear only at the beginning of the APM Header and APM Metadata sections, as shown in tables 3-1 and 3-2.  In the APM Data section, comments shall appear only at the beginning of a logical block.  Comments must not appear between the components of any logical block in the APM Data section.  The logical blocks in the APM Data section are indicated in table Erreur ! Source du renvoi introuvable..

The following type of comment may be provided as part of the APM to provide information regarding the attitude estimation accuracy:

COMMENT  The 1-sigma accuracy determined by the GSFC Flight

COMMENT  Dynamics Facility for this attitude solution was

COMMENT  [0.02670  0.00945  0.00832] DEG.

The purpose of this comment is to enable some specification on the quality of the attitude estimate.  The interpretation of the message or the values placed herein should be specified in an ICD.

### AEM specific

#### General

Comments are optional and may appear only after the specification of the keyword CCSDS_AEM_VERS, at the beginning of Metadata sections (only after META_START and before OBJECT_NAME), and immediately following the DATA_START keyword.  Comments must not appear between attitude ephemeris data lines, nor after the DATA_STOP keyword.

#### AEM Accuracy vs. Efficiency

The producer of an AEM may optionally report in comment lines the expected accuracy of the attitude ephemeris.  The user may then use this additional information to smooth or otherwise compress the data without affecting the accuracy of the attitude, but is not required to utilize this information to successfully process the message. The AEM producer also should strive to achieve not only the best accuracy possible, taking into account prediction errors, but also consider the efficiency of the attitude representation (e.g., step sizes of fractional seconds between attitude ephemeris lines may be necessary for precision scientific reconstruction of an attitude, but may be excessive in some cases).

# ADM XML Syntax

## Introduction

This section details the syntactical requirements for attitude messages.  All APM and AEM messages shall observe the syntax described in subsections xxx through xxx.

# Security

## Introduction

This section presents the results of an analysis of security considerations applied to the technologies specified in this Recommended Standard.

## Security Concerns with Respect to this Recommended Standard

### Data Privacy

Privacy of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

### Data Integrity

Integrity of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

### Authentication of Communicating Entities

Authentication of communicating entities involved in the transport of data which complies with the specifications of this Recommended Standard should be provided by the systems and networks on which this Recommended Standard is implemented.

### Data Transfer Between Communicating Entities

The transfer of data formatted in compliance with this Recommended Standard between communicating entities should be accomplished via secure mechanisms approved by the IT Security functionaries of exchange participants.

### Control of Access to Resources

This Recommended Standard assumes that control of access to resources will be managed by the systems upon which provider formatting and recipient processing are performed.

### Availability of Resources

This Recommended Standard assumes an adequate availability of resources on the systems on which provider formatting and recipient processing are performed.

### Auditing of Resource Usage

This Recommended Standard assumes that auditing of resource usage will be handled by the management of systems and networks on which this Recommended Standard is implemented.

## Potential Threats and Attack Scenarios

There are no known potential threats or attack scenarios that apply specifically to the technologies specified in this Recommended Standard.  Potential threats or attack scenarios applicable to the systems and networks on which this Recommended Standard is implemented should be addressed by the management of those systems and networks.  Protection from unauthorized access is especially important if the mission utilizes open ground networks such as the Internet to provide ground station connectivity for the exchange of data formatted in compliance with this Recommended Standard.

## Consequences of Not Applying STATED Security to the Technology

There are no known consequences of not applying the security to the technologies specified in this Recommended Standard.  The consequences of not applying security to the systems and networks on which this Recommended Standard is implemented could include potential loss, corruption, and theft of data.

## Data Security Implementation Specifics

Specific information-security interoperability provisions that may apply between agencies involved in an exchange of data formatted in compliance with this Recommended Standard should be specified in an ICD.

Conventions for DATA EXCHANGE

Definition of Attitude Quaternion

Let F0 be some reference frame, and F the reference frame associated with the object whose attitude is to be described.

Let R be the rotation that transforms the basis vectors of frame F0 into the basis vectors of frame F. That is to say: the basis vectors of frame F are the respective images of the basis vectors of frame F by the rotation R.

The quaternion that describes the attitude of the object is then defined as follows:

qc = cos(/2)

q1 = sin(/2) * ax

q2 = sin(/2) * ay

q3 = sin(/2) * az

Where:

- is the rotation angle,

- ax, ay and az are the coordinates of the rotation axis in either frame F or frame F0.

Let X0 be the coordinates of some vector in frame F0, and X the coordinates of the same vector in frame F.

The frame transformation matrix M is defined by :

X = M * X0

M can be written as function of the quaternion components as:

Example:

The 3 axes that define the object’s frame are denoted u, v, w respectively.

Their components in F0 noted U, V, W respectively are:

(u,v,w) are obtained from (u0, v0, w0) by applying a rotation of angle pi/4 around the Z axis.

The quaternion of the rotation is then given by:

Q1 = 0

Q2 = 0

Q3 = sin(pi/8)

QC = cos(pi/8)

Euler angles

The rotation that transforms the basis vectors of frame F0 into the basis vectors of frame F can equivalently be defined by 3 successive rotations.

Let’s consider the successive rotation axes : ZYX as an example.

The rotation is the combination of 3 rotation of respective angles ANGLE1, ANGLE2, ANGLE3 around the respective axes Z, Y, X :

First rotation of angle angle1 around the Z-axis, followed by a

Second rotation of angle ANGLE2 around (the new) Y-axis, followed by a

third rotation of angle ANGLE3 around (the new) X-axis.

Example :

Let’s considere the same quaternion as in A1:

Q1 = 0

Q2 = 0

Q3 = sin(pi/8)

QC = cos(pi/8)

Axes = ZYX

Angles = pi/8, 0, 0

Axes = YXY

Angles = -pi/2, pi/4, pi/2

SPIn Information Definition

| SPIN_ALPHA | Right ascension of spin axis vector |
| --- | --- |
| SPIN_DELTA | Declination of the spin axis vector |
| SPIN_ANGLE | Phase of the satellite about the spin axis |
| SPIN_ANGLE_VEL | Angular velocity of satellite around spin axis |
| PRECESSION ANGLE | Nutation angle of spin axis |
| PRECESSION PERIOD | Body nutation period of the spin axis |
| PRECESSION PHASE | Inertial nutation phase |

The Z axis of the spacecraft frame is supposed to be the spin axis.

The attitude frame is obtained from the reference frame by the 3 successive rotations:

- 1st rotation around Z of angle: SPIN ALPHA

- 2nd rotations aound Y of angle: π/2 – SPIN_DELTA

- 3rd rotation around Z of angle: SPIN_ANGLE

PRECESSION_ANGLE is the same as to π/2 – SPIN_DELTA

PRECESSION_PHASE is the same as SPIN ALPHA

PRECESSION_PERIOD the period of the conical motion of the spin axis around the Z axis of the reference frame F0.

The angular velocity vector is :

is the SPIN ANGULAR VELOCITY

is the PRECESSION ANGULAR VELOCITY

VALUES FOR SELECTED KEYWORDS

(NORMATIVE)

Overview

The values in this annex represent the acceptable values for selected keywords.  Each keyword’s values delineated here are present in either an APM or AEM message.  For details and descriptions of the keyword interpretations, the reader is directed to reference [F4].  If exchange partners wish to use different settings, they should be documented in an ICD.

time_system mETADATA KEYWORD

| TIME_SYSTEM Value | Meaning/Description |
| --- | --- |
| GMST | Greenwich Mean Sidereal Time |
| GPS | Global Positioning System |
| MET | Mission Elapsed Time |
| MRT | Mission Relative Time |
| SCLK | Spacecraft Clock (receiver) |
| TAI | International Atomic Time |
| TCB | Barycentric Coordinated Time |
| TDB | Barycentric Dynamical Time |
| TT | Terrestrial Time |
| UT1 | Universal Time |
| UTC | Coordinated Universal Time |

Note that if MET or MRT are chosen as the TIME_SYSTEM, then the epoch of either the start of the mission for MET, or of the event for MRT, should either be given in a comment in the message, or provided in an ICD. The time system for the start of the mission or the event should also be provided in the comment or the ICD.  If these values are used for the TIME_SYSTEM, then the times given in the file denote a duration from the mission start or event.  However, for clarity, an ICD should be used to fully specify the interpretation of the times if these values are to be used.  Note that the time format should only utilize three digit days from the MET or MRT epoch, not months and days of the months.

Note that if SCLK is chosen as a TIME_SYSTEM, the transformation of this time to one of the other specified time systems in B2 should be given in an ICD.  The intent of this keyword is to allow for the use of SCLK as a TIME_SYSTEM, but there is currently no standard way to transform this time system to other time systems listed in B2.

Inertial and Local Orbital Frame Keyword Values

The following table enumerates the allowable keywords for inertial frames that can be used by ADM messages.  They are valid for keywords:  Q_FRAME_*, EULER_FRAME_*, and SPIN_FRAME_* in an APM, and REF_FRAME_* in an AEM, where ‘*’ denotes ‘A’ or ‘B’.

| Keyword Value | Meaning/Description |
| --- | --- |
| EME2000 | Earth Mean Equator and Equinox of J2000 |
| GTOD | Greenwich True of Date |
| ICRF | International Celestial Reference Frame |
| CIRF |  |
| TIRF |  |
| ITRF |  |
| ITRF2000 | International Terrestrial Reference Frame 2000 |
| ITRF-93 | International Terrestrial Reference Frame 1993 |
| ITRF-97 | International Terrestrial Reference Frame 1997 |
| ITRFxxxx |  |
| ITRF-xx |  |
| J2000 | Earth Mean Equator and Equinox of J2000 |
| LVLH | Local Vertical Local Horizontal |
| RTN, QSW | Radial, Transverse, Normal Orbital Frame |
| TOD | True of Date |
| TNW, NTW | Tangential, Normal, Omega (W) Orbital Frame |
| RSW | Relative Orbit Frame describing the relative motion of two satellites (Clohessy-Wiltshire Equations) |

LOcal spacecraft body reference frames

The following table enumerates the allowed values for the keyword Q_FRAME_*, EULER_FRAME_*, SPIN_FRAME_* in the APM and REF_FRAME_* in the AEM messages, where ‘*’ denotes ‘A’ or ‘B’.  These frames will vary from object to object, but provide a mechanism of denoting different reference frames than the object’s BODY axes to specify an orientation.  It is the responsibility of the end user to have an understanding of the location of these frames for their particular object, typically via an ICD.

| Keyword Value | Meaning/Description |
| --- | --- |
| ACTUATOR_x | Actuator reference frame (‘x’ = 0→9): could denote reaction wheels, solar arrays, thrusters, etc. |
| CSS_xy | Coarse Sun Sensor (‘x’ = 0→9, ‘y’ = 0→9) |
| DSS_x | Digital Sun Sensor (‘x’ = 0→9) |
| GYRO_x | Gyroscope Reference Frame (‘x’ = 0→9) |
| INSTRUMENT_y | Instrument ‘y’ reference frame (‘y’ = A→Z, 0→9) |
| SC_BODY_x | Spacecraft Body Frame (‘x’ = 0→9) |
| SC_BODY_y | Spacecraft Body Frame of another object (‘y’ = A→Z) |
| SENSOR_x | Sensor ‘x’ reference frame (‘x’ = A→Z, 0→9) |
| STARTRACKER_x | Star Tracker Reference Frame (‘x’ = 0→9) |
| TAM_x | Three Axis Magnetometer Reference Frame (‘x’ = 0→9) |
| BODY |  |

Rationale for Attitude Data Messages

(Informative)

Overview

This annex presents the rationale behind the design of each message.  It may help the application engineer to select a suitable message. Corrections and/or additions to these requirements are expected during future updates.

A specification of requirements agreed to by all parties is essential to focus design and to ensure the product meets the needs of the Member Agencies.  There are many ways of organizing requirements, but the categorization of requirements is not as important as the agreement to a sufficiently comprehensive set.  In this annex the requirements are organized into three categories:

- Primary Requirements:  These are the most elementary and necessary requirements.  They would exist no matter the context in which the CCSDS is operating, i.e., regardless of pre-existing conditions within the CCSDS or its Member Agencies.

- Heritage Requirements:  These are additional requirements that derive from pre-existing Member Agency requirements, conditions, or needs.  Ultimately these carry the same weight as the Primary Requirements.  This Recommended Standard reflects heritage requirements pertaining to some of the technical participants’ home institutions collected during the preparation of the document; it does not speculate on heritage requirements that could arise from other Member Agencies.

- Desirable Characteristics:  These are not requirements, but they are felt to be important or useful features of the Recommended Standard.

PRIMARY REQUIREMENTS ACCEPTED BY THE ATTITUDE DATA MESSAGES

Table C-1:  Primary Requirements

| Requirement | Accepted for APM? | Accepted for AEM? |
| --- | --- | --- |
| Data must be provided in digital form (computer file). | Y | Y |
| The file specification must not require of the receiving agency the separate application of, or modeling of, spacecraft dynamics or gravitational force models, or integration or propagation. | N | Y |
| The interface must facilitate the receiver of the message to generate an attitude state at any required epoch. | Y | Y |
| Attitude state information must be provided in a reference frame that is clearly identified and unambiguous. | Y | Y |
| Identification of the object must be clearly identified and unambiguous. | Y | Y |
| Identification of the center of attitude motion must be clearly identified and unambiguous. NOTE – The specification of a center name is not required for the unambiguous specification of attitude but may be provided if desired. | N | N |
| Time measurements (time stamps, time tags, or epochs) must be provided in a commonly used, clearly specified system. | Y | Y |
| The time bounds of the attitude ephemeris must be unambiguously specified. | N | Y |
| The standard must provide for clear specification of units of measure. | Y | Y |
| Files must be readily ported between, and useable within, all Member Agency computational environments that could be used to exchange Attitude Data Messages. | Y | Y |
| Files must have means of being uniquely identified and clearly annotated. The file name alone is considered insufficient for this purpose. | Y | Y |
| File name syntax and length must not violate computer constraints for those Member Agency computing environments that could be used to exchange Attitude Data Messages. | Y | Y |

Table C-2:  Heritage Requirements

| Requirement | Accepted for APM? | Accepted for AEM? |
| --- | --- | --- |
| A complete attitude ephemeris, not subject to integration or propagation by the customer, must be provided. | N | Y |
| The standard is, or includes, an ASCII format. | Y | Y |
| The standard does not require software supplied by other agencies. | Y | Y |

Table C-3:  Desirable Characteristics

| Requirement | Accepted for APM? | Accepted for AEM? |
| --- | --- | --- |
| The standard applies to non-traditional objects, such as landers, rovers, balloons, and natural bodies (asteroids, comets). | Y | Y |
| The standard allows attitude states to be provided in other than the traditional EME2000 inertial reference frame; one example is the International Astronomical Union (IAU) Mars body-fixed frame. (In such a case, provision or ready availability of supplemental information needed to transform data into a standard frame must be arranged.) | Y | Y |
| The standard is extensible with no disruption to existing users or uses. | Y | Y |
| The standard is consistent with, and ideally a part of, attitude products and processes used for other space science purposes. | N | N |
| The standard is as consistent as reasonable with any related CCSDS attitude standards used for earth-to-spacecraft or spacecraft-to-spacecraft applications. | Y | Y |
| The standard allows for the specification of the accuracy of the attitude solution. | Y | Y |

APPLICABILITY OF CRITERIA TO MESSAGE OPTIONS

The selection of one particular message will depend on the optimization criteria in the given application.  Table C-4 compares the two recommended messages in terms of the relevant selection criteria identified by the CCSDS:

Table C-4:  Applicability of the Criteria to Attitude Data Messages

| Criteria | Definition | Applicable to APM? | Applicable to AEM? |
| --- | --- | --- | --- |
| Modeling Fidelity | Permits modeling of any dynamic perturbation to the attitude. | N | Y |
| Human Readability | Provides easily readable message corresponding to widely used attitude representations. | Y | Y |
| Remote Body Extensibility | Permits use for assets on remote solar system bodies. | Y | Y |
| Lander/Rover Compatibility | Permits exchange of non-orbit attitudes. | Y | Y |

Services related to the different attitude data MESSAGE formats

The different attitude data messages have been distinguished by their self-interpretability.  Both attitude data messages provide for recognizing the boundaries of the attitude data fields and thus can transfer each field, as a block, to another location.  The different services that can be achieved without special arrangements between users of the CCSDS attitude data messages are listed in table C-5.

Table C-5:  Services Available with Attitude Data Messages

| Service | Definition | Applicable to APM? | Applicable to AEM? |
| --- | --- | --- | --- |
| Absolute Attitude Interpretation | State availability at specific times for use in additional computations (geometry, event detection, etc.). | Y | Y |
| Relative Attitude Interpretation | Trajectory comparison and differencing for events based on the same time source. | Only at time specified at Epoch | Y |

ITEMS FOR AN INTERFACE CONTROL DOCUMENT

(Informative)

In several places in this document there are references to items which should be specified in an ICD between agencies participating in an exchange of attitude data.  The ICD should be jointly produced by both agencies participating in a cross-support activity involving the transfer of attitude data.  This annex compiles those recommendations into a single list.

Table D-1:  Items Recommended for an ICD

| ICD Item | Section Trace |
| --- | --- |
| 1 | ADM and AEM file naming conventions. | 3.1.2 4.1.3 |
| 2 | Method of exchanging ADMs (transmission). | 1.2.2 3.1.2 4.1.3 |
| 3 | Definition of attitude accuracy requirements pertaining to data in an ADM as well as attitude dynamics modeling. | 1.2.1 1.1.1 5.8.2.2 |
| 4 | Specific APM and/or AEM version numbers that will be exchanged. | 1.1.1.1 4.2.8.1 |
| 5 | Format on values used for the ‘ORIGINATOR’ keyword. | table 3-1 table 4-2 |
| 6 | Values used for the ‘OBJECT_ID’ keyword for cases when the value is not published in the SPACEWARN Bulletin (reference [2]). | table 3-2 table 4-3 |
| 7 | Values and definition of the ‘Q_FRAME_*’, ‘EULER_FRAME_*’, ‘SPIN_FRAME_*’, or ‘REF_FRAME_*’ keywords to be used in ADM exchanges, if the value is not given in annex B. | 1.1.1.1.1, tables Erreur ! Source du renvoi introuvable. and 4-3 |
| 8 | Values and definition of the ‘SPIN_FRAME_*’ keyword if they are going to be used in ADM exchanges, as well as the convention for values of the ‘SPIN_ANGLE’ keyword if not expressed in reference [F4]. | 3.2.5.5 |
| 9 | If floating-point numbers in extended-single or extended-double precision are to be used, then discussion of implementation-specific attributes is required. | 5.6.5 |
| 10 | Information which must appear in comments for any given ADM exchange. | 5.8.1.3 |
| 11 | Whether the format of the ADM will be KVN or XML. | 1.2.3 |
| 12 | A reference orientation should be specified in an ICD if a body-fixed frame is to be used for the specification of Euler angles. For instance, demonstrating the alignment of the body axes with the local orbit frame or an inertial frame that gives a context to interpret the Euler angle data. | 1.1.1.1 1.1.1.1 |
| 13 | If the angle units will be radians (outside the standard), this must be specified in the ICD. | 5.6.1 |
| 14 | Provisions that are made to ensure information security. | 6 |
| 15 | Values used for those keywords listed in annex B when those values are different from those given in annex B. | B |
| 16 | Specification of interpretation of MET, MRT and SCLK, if to be exchanged, and how to transform it to a standardized time system such as UTC, TAI, etc. An ICD should specify that elapsed days are to be used for epochs, with year starting at zero. | B2 |
| 17 | Exact specification of reference frames used in messages, if different from those specified in annex B. | B4 |

ABBREVIATIONS AND ACRONYMS

(Informative)

ASCII	American Standard Code for Information Interchange

ADM	Attitude Data Message

AEM	Attitude Ephemeris Message

APM	Attitude Parameter Message

CCIR	International Coordinating Committee for Radio Frequencies

CCSDS	Consultative Committee for Space Data Systems

EME2000	Earth Mean Equator and Equinox of J2000 (Julian Date 2000)

GPS	Global Positioning System

IAU	International Astronomical Union

ICD	Interface Control Document

ICRF	International Celestial Reference Frame

IEC	International Electrotechnical Commission

ISO	International Organization for Standardization

ITRF	International Terrestrial Reference Frame

KVN	Keyword = Value Notation

LVLH	Local Vertical Local Horizontal

NTW	Normal, Tangential (to velocity vector) and Normal to Orbit Plane

ODM	Orbit Data Message

OEM	Orbit Ephemeris Message

OPM	Orbit Parameter Message

TAI	International Atomic Time

TCB	Barycentric Coordinated Time

TDB	Barycentric Dynamical Time

TDM	Tracking Data Message

TOD	True Equator and Equinox of Date

TT	Terrestrial Dynamical Time

UTC	Coordinated Universal Time

XML	eXtensible Markup Language

Informative References

(Informative)

[F1]	XML Schema Part 2: Datatypes.  2nd ed.  P. Biron and A. Malhotra, eds. W3C Recommendation 28.  n.p.: W3C, 2004.

[F2]	Standard Frequencies and Time Signals.  Volume 7 of Recommendations and Reports of the CCIR:  XVIIth Plenary Assembly.  Geneva:  CCIR, 1990.

[F3]	Procedures Manual for the Consultative Committee for Space Data Systems.  CCSDS A00.0-Y-9.  Yellow Book.  Issue 9.  Washington, D.C.:  CCSDS, November 2003.

[F4]	Navigation Data—Definitions and Conventions.  Report Concerning Space Data System Standards, CCSDS 500.0-G-2.  Green Book.  Issue 2.  Washington, D.C.: CCSDS, November 2005.

NOTE	– Normative references are provided in 1.5.

# Footnotes

The greater the amount of material specified via ICD, the lesser the utility/benefit of the ADM (custom programming will be required to tailor software for each ICD).

XML implementation awaiting approval as a standard.

# Comments

Provisions …

again

Not true => remove.

Separate section : no link with previous sentence.

Remove : too much detail at this point

??? true ?

??? true ?

Not exact: model in APM is a simple model.

Insert a title: purpose to the paragraph (2.3.1, 2.3.2, 2.3.3)

No need to compare with APM here.

Not exactly “modeling”

Too much detail at this point (just the introduction)

Améliorer

Useless

No need for repetitions

Requirements => keep

Reference not about attitude state

Useless and not true : no need for a propagator

Not necessarily a file

No impact on attitude definition.

TBC

One possibility : block names in the order they appear.

Example : QUAT EULER

Not necessary

What to do with this ? could be removed.

OK?

meaning ?

any frame ?

Objective :

Move all remarks :

- Either to normative / informative annex

- Either in note in concerned data block

- Or in additional paragraph relative to format (KVN)

Obvious from structure

Move tp appropriate section

All examples are not up to date

Strange order !

A2B

A = Spacecraft

???

???

???

Take sentence from APM.

Take sentence from APM

Make consistent with APM

Added as generic name