Pointing Request Message test Plan/Report

CCSDS Record

CCSDS 509.1-Y-1

Yellow Book

July 2016

FOREWORD

This document records the plans for prototype testing and results of that testing for the Pointing Request Message, CCSDS 509.0-R-1, Red Book. As a record of prototype testing, it is expected that expansion, deletion, or modification of this document will not occur. This document is subject to CCSDS document management and change control procedures, which are defined in the Organization and Processes for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK: CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

# DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 509.1-Y-1 | Pointing Request Message Test/Plan Report, CCSDS Record, Issue 1 | July 2016 | Initial Issue |

# CONTENTS

Section	Page

1	INTRODUCTION	1-1

1.1	PURPOSE	1-1

1.2	SCOPE	1-1

1.3	APPLICABILITY	1-1

1.4	RATIONALE	1-1

1.5	DOCUMENT STRUCTURE	1-1

1.6	References	1-2

2	CONCLUSION/RECOMMENDATION	2-1

3	CONJUNCTION  DATA MESSAGE (PRM) TESTING GOALS	3-2

3.1	PRM OVERVIEW	3-2

4	TEST PLAN OVERVIEW	4-3

5	TEST PLAN DETAILS	5-4

5.1	TEST CASE #1: JSpOC CSM COMPARISON	5-4

5.1.1	TEST PURPOSE	5-4

5.1.2	TEST DESCRIPTION	5-4

5.1.3	EXPECTED RESULTS	5-4

5.2	TEST CASE #2: JSpOC OCM COMPARISON	5-4

5.2.1	TEST PURPOSE	5-4

5.2.2	TEST DESCRIPTION	5-4

5.2.3	EXPECTED RESULTS	5-5

5.3	TEST CASE #3: NASA/JPL NON-EARTH CENTERED PRM	5-5

5.3.1	TEST PURPOSE	5-5

5.3.2	TEST DESCRIPTION	5-5

5.3.3	EXPECTED RESULTS	5-5

5.4	TEST CASE #4: CNES SPECIFIC PRM	5-6

5.4.1	TEST PURPOSE	5-6

5.4.2	TEST DESCRIPTION	5-6

5.4.3	EXPECTED RESULTS	5-6

5.5	TEST CASE #5: AGI/CSSI PRM INCLUDING COLLISION PROBABILITY	5-6

5.5.1	TEST PURPOSE	5-6

5.5.2	TEST DESCRIPTION	5-6

5.5.3	EXPECTED RESULTS	5-6

5.6	TEST CASE #6: ESA/ESAC PRM INCLUDING screening volume	5-7

5.6.1	TEST PURPOSE	5-7

5.6.2	TEST DESCRIPTION	5-7

5.6.3	EXPECTED RESULTS	5-7

5.7	TEST CASE #7: Xml to KVN Conversion	5-7

5.7.1	TEST PURPOSE	5-7

5.7.2	TEST DESCRIPTION	5-7

5.7.3	EXPECTED RESULTS	5-7

5.8	TEST CASE #8: TRACING of OBLIGATORY KEYWORDS TO Annex b PRIMARY requirements	5-8

5.8.1	TEST PURPOSE	5-8

5.8.2	TEST DESCRIPTION	5-8

5.8.3	EXPECTED RESULTS	5-8

6	TEST REPORT OVERVIEW	6-1

7	Test report details	7-1

7.1	test case #1 jspoc csm comparison	7-1

7.1.1	Iridium TEst results	7-1

7.1.2	AGI/CSSI Test results	7-3

7.1.3	jaxa test results	7-4

7.1.4	CNES test results	7-6

7.1.5	ESA/esac test results	7-8

7.1.6	DLR/GSOC test results	7-10

7.1.7	OVERALL test result	7-11

7.2	Test case #2: JSpOC OCM COMPARISON	7-12

7.2.1	Test case 2a: Nasa/jsc results	7-12

7.2.2	Test case 2B: Nasa/GSFC results	7-13

7.2.3	Test case 2C: Nasa/GSFC results	7-14

7.2.4	OVERALL test result	7-15

7.3	TEST CASE #3: NASA/JPL NON-EARTH CENTERED PRM	7-16

7.3.1	Test case 3a: Nasa/GSFC results	7-16

7.3.2	Test case 3B: ESA/ESOC results	7-16

7.3.3	OVERALL test result	7-17

7.4	Test case #4: CNes specific PRM	7-18

7.5	Test case #5: AGI/CSSI PRM  INCLUDING  COLLISION  PROBABILITY	7-20

7.6	Test case #6: ESA/ESAC PRM  INCLUDING  screening  volume	7-22

7.7	TEST CASE #7: Xml to KVN Conversion	7-25

7.8	TEST CASE #8: TRACING of OBLIGATORY KEYWORDS TO Annex b PRIMARY requirements	7-27

ANNEX A ABBREVIATIONS AND ACRONYMS	7-31

# INTRODUCTION

## PURPOSE

The purpose of this document is to describe the prototype testing conducted on the CCSDS

Pointing Request Message (PRM), CCSDS 509.0-R-1 (reference [2]).

## SCOPE

The scope of this document is testing of the Pointing Request Message (PRM). The PRM is part of the technical program of the CCSDS Navigation WG (NWG). The PRM document completed a CCSDS Agency Review in January through March 2016, with revisions following this initial review to apply RIDs  from the review and proofreading changes; this process is described in reference [1].

Note that in applicable places the prototyping includes results based on modifications to

the PRM document provided via the Agency Review Item Discrepancy (RID) process

. Changes based on the ongoing working group activity were also incorporated as applicable.

## APPLICABILITY

This document applies to the prototype testing required to advance the PRM from Red Book to Blue Book status.

## RATIONALE

The CCSDS Procedures Manual states that for a Recommendation to become a Blue Book,

the draft standard must be tested in an operational manner. The following requirements for an

implementation exercise were excerpted from reference [1]:

“At least two independent and interoperable prototypes or implementations

must have been developed and demonstrated in an operationally relevant

environment, either real or simulated.”

This document outlines the NavWG’s approach to meeting this requirement for the PRM 509.0 Red Book.

## DOCUMENT STRUCTURE

The first sections of this document describe the Test Plan for the prototyping activity; the

last sections of the document provide a Test Report of the realized plan. Acronyms are provided in Annex A.

## References

The following documents are referenced in this document.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS documents.

[1] 	Organization and Processes for the Consultative Committee for Space Data Systems. CCSDS A02.1-Y-4. Yellow Book. Issue 4. Washington, D.C.: CCSDS, April 2014.

[2] 	Pointing Request Message. Recommendation for Space Data System Standards, CCSDS 509.0-R-1. Red Book, Washington, D.C.: CCSDS, April 2016.

[3] 	http://beta.sanaregistry.org/r/pointing_request_message/pointing_request_message.html

# CONCLUSION/RECOMMENDATION  (DRAFT)

[Editor's Note:  It is intended that the following draft conclusion/recommendation will be substantiated, with applicable revisions, via the testing process.]

The test plan and test reports documented herein substantiate that the organizations

participating in the CCSDS NWG have successfully conducted prototype testing of the Pointing Request Message (PRM) document (reference [2]).  During the testing, PRMs  were produced by 5 different organizations, and the ability to correctly interpret the messages and utilize the information in analyses was demonstrated by 9 different organizations.

The prototype implementations demonstrated the utility of the PRM, and the few minor discrepancies identified helped to improve the quality of the prototype implementations.

Based on the diversity of organizations able to read/write the messages, and the positive test results, the NavWG recommends that the PRM Red Book document be promoted to a Blue Book CCSDS Recommended Standard.

# Pointing Request Message (PRM) TESTING GOALS

The tests of the PRM described in Section 4 and Section 5 of this plan will be conducted in order to meet the CCSDS requirements described in Section 2. In Section 6 and Section 7, the results of the testing are presented.

## PRM OVERVIEW

The PRM is an Extensible Markup Language (XML) formatted message. It specifies a standard message format for use in exchanging spacecraft pointing request information between originators of pointing data, satellite owner/operators and other authorized parties. The message is organized into 3 sections: a header section, a metadata/definition section and a data/request section. The header section contains identification information (version, creation date, originator, etc.). The metadata section contains information regarding the objects, the reference frames and other definition defining the basic elements of the pointing request. The data section contains the detailed characteristics of the pointing that combined with the definition complete the pointing request.

# TEST PLAN OVERVIEW

Prototyping of the PRM will be performed as shown in the following table, which lists by Test Number the participating member agencies of the Navigation Working Group, and their roles in the tests. Because the PRM standard is based on pre-defined templates as well as in a generic procedure using basic PRM building elements, the prototyping is implemented in two steps, one exercising the use of the use of the templates and another one covering the application of the generic procedure.

Table 1: Pointing Request Message Tests Table

| Test# | Type | Message #1 | Message #2 | Test Judge [Arbitrator?] |
| --- | --- | --- | --- | --- |
| 1 | Template |  |  |  |
| 2 | Template |  |  |  |
| 3 | Template |  |  |  |
| 4 | Template |  |  |  |
| 5 | Template |  |  |  |
| 6 | Template |  |  |  |
| 7 | Template |  |  |  |
| 8 | Template |  |  |  |
| 9 | Template |  |  |  |
| 10 | Template |  |  |  |
| 11 | General procedure |  |  |  |

[Fran:  I'm thinking that we should have a neutral judge for each test case to determine whether or not the messages coded by the participants are equivalent. It might be good that ESA/ESOC (you) are the judge, and 2 other agencies produce the messages for each scenario. What do you think?]

This is fine for me. In this case I (ESOC) cannot be one of the prototyping agencies.

# TEST PLAN DETAILS

## TEST CASE #1: Inertial Pointing

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a request for inertial pointing with boresight offset using the Inertial Pointing Template.

### TEST DESCRIPTION

Generate a request based on the Inertial Pointing Template such that:

General details:

Base reference frame is GCRF

Time scale is UTC

Satellite is Hipparcos (1989-062B)

The reference direction for the inertial pointing is the star Vega (RA 18h 36m 56s | Dec +38° 47′ 1″)

The spacecraft X-axis points to Vega.

The phase angle is defined such that the Y-axis is contained in the plane Vega- Spacecraft-Aldebaran (RA 4h 35m 55s | Dec +16° 30′ 33″)

The pointing is set with an offset of 10º away from Vega to the half plane containing Aldebaran.

The attitude is to be maintained during 3 hours after 2016-02-10T23:00:00.000

A second pointing is to be implemented starting on 2016-02-27T00:00:00.000 for 1.5 hours. This second pointing has no offset with respect to Vega.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the assigned Test Judge.

## TEST CASE #2: Sun Pointing

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a request for Sun pointing with boresight offset and constant spin around the pointing axis using the Sun  Pointing Template.

### TEST DESCRIPTION

Generate a request based on the Sun Pointing Template such that:

General details:

Base reference frame is GCRF

Time scale is TDB

Satellite is SOHO (1995-065A)

The spacecraft X-axis points to the Sun.

The phase angle is defined such that the Y-axis is contained in the plane Sun-Spacecraft-Aldebaran (RA 4h 35m 55s | Dec +16° 30′ 33″)

The pointing is set with an offset of 10º away from the Sun to the half plane containing Aldebaran.

The shall rotate at a rate of 1º per hour around the X-axis.

The attitude is to be maintained during 3 hours after 2016-02-10T23:00:00.000

A second pointing is to be implemented starting on 2016-02-27T00:00:00.000 for 1.5 hours. The Y-axis points to the Sun, with no offset and no rotation rate around the pointing axis.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the assigned Test Judge.

## TEST CASE #3: TRACK WITH INERTIAL DIRECTION YAW STEERING

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a request using the Track With Inertial Direction Yaw Steering Template.

### TEST DESCRIPTION

Generate a request based on the Track with Inertial Direction Yaw Steering Template such that:

General details:

Base reference frame is GCRF

Time scale is TDB

Satellite is MEX (2003-022A)

The spacecraft X-axis points to Mars.

The phase angle is defined according to the yaw steering law defined in the template description using the Y-axis as spacecraft reference direction and the direction Aldebaran (RA 4h 35m 55s | Dec +16° 30′ 33″) as inertial reference direction.

The yaw steering phase angle is 0º.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the assigned Test Judge.

## TEST CASE #4: TRACK WITH Power Optimized YAW STEERING

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a request using the Track with Power Optimized Yaw Steering Template.

### TEST DESCRIPTION

Generate a request based on the Track with Power Optimized Yaw Steering Template such that:

General details:

Base reference frame is GCRF

Time scale is TDB

Satellite is MEX (2003-022A)

The spacecraft X-axis points to Mars.

The phase angle is defined according to the yaw steering law defined in the template description using the Y-axis as spacecraft reference direction.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the Test Judge.

## TEST CASE #5: NADIR WITH Power Optimized YAW STEERING

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a request using the Nadir with Power Optimized Yaw Steering Template.

### TEST DESCRIPTION

Generate a request based on the Nadir with Power Optimized Yaw Steering Template such that:

General details:

Base reference frame is ITRF

Time scale is UTC

Satellite is METOP-1A (2006-044A)

The central body used to define the nadir direction is the Earth.

The spacecraft Z-axis points to the nadir direction.

The phase angle is defined according to the yaw steering law defined in the template description using the Y-axis as spacecraft reference direction.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the Test Judge.

## TEST CASE #6: NADIR WITH GroundTrack Aligned YAW STEERING

### TEST PURPOSE

This tests intends to proof the ability of the PRM to model a request using the Nadir with Ground-track Aligned Yaw Steering Template.

### TEST DESCRIPTION

Generate a request based on the Nadir with Groundtrack Aligned Yaw Steering Template such that:

General details:

Base reference frame is ITRF

Time scale is UTC

Satellite is METOP-1A (2006-044A)

The central body used to define the nadir direction is the Earth.

The spacecraft Z-axis points to the nadir direction.

The phase angle is defined according to the yaw steering law defined in the template description using the Y-axis as spacecraft reference direction.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the Test Judge.

## TEST CASE #7: NADIR WITH Orbital Pole Aligned YAW STEERING

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a request using the Nadir with Orbital Pole Aligned Yaw Steering Template.

### TEST DESCRIPTION

Generate a request based on the Nadir with Orbital Pole Aligned Yaw Steering Template such that:

General details:

Base reference frame is GCRF

Time scale is TDB

Satellite is ULYSSES (1990-090B)

The central body used to define the nadir direction is the Jupiter.

The spacecraft Z-axis points to the nadir direction.

The phase angle is defined according to the yaw steering law defined in the template description using the Y-axis as spacecraft reference direction.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the Test Judge.

## TEST CASE #8: Limb Pointing with Power Optimized YAW STEERING

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a request using the Limb Pointing with Power Optimized Yaw Steering Template.

### TEST DESCRIPTION

Generate a request based on the Limb Pointing with Power Optimized Yaw Steering Template such that:

General details:

Base reference frame is ITRF

Time scale is UTC

Satellite is METOP-1A (2006-044A)

The central body used to define the limb direction is the Earth.

The spacecraft Z-axis points to the limb direction 10 km above the Earth surface.

The phase angle is defined according to the yaw steering law defined in the template description using the Y-axis as spacecraft reference direction.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the Test Judge.

## TEST CASE #9: Limb PoiNting with Inertial Direction YAW STEERING

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a request using the Limb Pointing with Inertial Direction Yaw Steering Template.

### TEST DESCRIPTION

Generate a request based on the Limb Pointing with Inertial Direction Yaw Steering Template such that:

General details:

Base reference frame is ITRF

Time scale is UTC

Satellite is METOP-1A (2006-044A)

The central body used to define the limb direction is the Earth.

The spacecraft Z-axis points to the limb direction 10 km above the Earth surface.

The phase angle is defined according to the yaw steering law defined in the template description using the Y-axis as spacecraft reference direction and the direction Aldebaran (RA 4h 35m 55s | Dec +16° 30′ 33″) as inertial reference direction.

The yaw steering phase angle is 45º.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the Test Judge.

## TEST CASE #10: VELOCITY POINTING WITH ORBITAL POLE YAW STEERING

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a request using the Velocity Pointing with Orbital Pole Yaw Steering Template.

### TEST DESCRIPTION

Generate a request based on the Velocity Pointing with Orbital Pole Yaw Steering Template such that:

General details:

Base reference frame is GCRF

Time scale is TDB

Satellite is BEPI-COLOMBO (2018-013A)

The central body used to define the limb direction is Mercury.

The spacecraft X-axis is pointed towards the spacecraft velocity relative to Mercury.

The phase angle is defined according to the yaw steering law defined in the template description using the Y-axis as spacecraft reference direction.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the template available on the SANA Registry (see reference [3]).

The requests provided by all participants will provide comparable values in all template fields, as determined by the Test Judge.

## TEST CASE #11: PRM from General Build PRocedure

### TEST PURPOSE

This test will demonstrate the ability of the PRM to model a general request using the procedure described in section 5 of the PRM standard.

### TEST DESCRIPTION

Generate a request based on the procedure described in section 5 of the PRM standard:

General details:

Base reference frame is GCRF

Time scale is TDB

Satellite is GAIA (2013-074A)

To be written.

### EXPECTED RESULTS

Each participant shall provide a complete PRM using the procedure described in section 5 of the PRM standard.

The requests provided by all participants will provide comparable values in all fields, as determined by the Test Judge.    [Is this too strict for the general case?]

The involvement of the Test Judge allows that a qualitative assessment can be done. I do not think it is to strict but there should be some objective parameters that allow assessing the correctness of the messages.

# TEST REPORT OVERVIEW

The Test Judge will provide the Pointing Request Message (PRM) Prototype Test Data Sheets (see next page) to the NWG. The NWG will discuss the results in a teleconference or other working group meeting to determine success.

The test report details will be consolidated in Section 7 of this document. A summary of the test process and the recommendation of the NWG may be found in Section 2 of the report. The report will be submitted to the CCSDS Engineering Steering Group (CESG) and CCSDS Management Council (CMC), along with results of the agency reviews. At that time, a formal request will be submitted to the CMC for progression of the PRM to CCSDS Blue Book status.

The next page contains a format for the test data sheets that will be used to report the results

of individual tests.

SAMPLE

Pointing Request Message (PRM) Prototype Test Data Sheet

| Report Date |  |
| --- | --- |
| Test Case Number |  |
| PRM Originator Message #1 |  |
| PRM Originator Message #2 |  |
| Test Judge |  |
| Test Results Considerations | [do we need this line? perhaps not?] Let’s keep it to allow for some relevant comments in the process. I propose an alternative title |
| Discrepancies from Expected Results |  |
| Test Judge’s Recommendation (Pass, Partial Pass, Fail) |  |
| NWG Disposition (To be filled out by NWG) |  |

# Test report details

## TEST CASE #1: INERTIAL POINTING

## TEST CASE #2: Sun Pointing

## TEST CASE #3: TRACK WITH INERTIAL DIRECTION YAW STEERING

## TEST CASE #4: TRACK WITH Power Optimized YAW STEERING

## TEST CASE #5: NADIR WITH Power Optimized YAW STEERING

## TEST CASE #6: NADIR WITH GroundTrack Aligned YAW STEERING

## TEST CASE #7: NADIR WITH Orbital Pole Aligned YAW STEERING

## TEST CASE #8: Limb Pointing with Power Optimized YAW STEERING

## TEST CASE #9: Limb PoiNting with Inertial Direction YAW STEERING

## TEST CASE #10: VELOCITY POINTING WITH ORBITAL POLE YAW STEERING

## TEST CASE #11: PRM from General Build PRocedure

ABBREVIATIONS AND ACRONYMS

(INFORMATIVE)

AGI/CSSI	Analytical Graphics Incorporated/Center for Space Standards and Innovation

ASCII		American Standard Code for Information Interchange

CCSDS	Consultative Committee for Space Data Systems

CNES		Centre National d’Etudes Spatiales

DLR/GSOC	Deutsches Zentrum für Luft und Raumfahrt (German Aerospace 				Center)/German Space Operations Center

ESA/ESOC	European Space Agency/European Space Operations Center

ESA/ESAC	European Space Agency/European Space Astronomy Center

GCRF		Geocentric Celestial Reference Frame

ITRF		International Terrestrial Reference Frame

JAXA		Japan Aerospace Exploration Agency

NASA/GSFC	National Aeronautics and Space Administration/Goddard Space Flight Center

NASA/JPL	National Aeronautics and Space Administration/Jet Propulsion Laboratory

NASA/JSC	National Aeronautics and Space Administration/Johnson Space Flight Center

NWG		CCSDS Navigation Working Group

PRM		Pointing Request Message

SANA		Space Assigned Numbers Authority

TDB		Barycentric Dynamic Time

UTC		Universal Time Coordinated

XML 		Extensible Markup Language