Re-entry Data Message test plan/report

DRAFT CCSDS Record

CCSDS 508.2-Y-1.5

Draft Yellow Book

April 2019

FOREWORD

This document records the plans for prototype testing and the prototyping results for the Re-entry Data Message Version 1 Blue Book. As a record of prototype testing, it is expected that expansion, deletion, or modification of this document will not occur. This document is subject to CCSDS document management and change control procedures, which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

# DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| CCSDS 508.2-Y-1 | Re-entry Data Message prototyping test plan/report, Draft CCSDS Record, Issue 1 | April 2018 | Initial draft |
| CCSDS 508.2-Y-1.1 | Re-entry Data Message prototyping test plan/report, Draft CCSDS Record, Issue 1.1 | November 2018 | pre-prototyping draft |
| CCSDS 508.2-Y-1.3 | Re-entry Data Message prototyping test plan/report, Draft CCSDS Record, Issue 1.3 | December 2018 | prototyping draft |
| CCSDS 508.2-Y-1.4 | Re-entry Data Message prototyping test plan/report, Draft CCSDS Record, Issue 1.4 | February 2019 | WG review draft |
| CCSDS 508.2-Y-1.5 | Re-entry Data Message prototyping test plan/report, Draft CCSDS Record, Issue 1.5 | April 2019 | Final draft |

# CONTENTS

Section	Page

DOCUMENT CONTROL	iii

CONTENTS	iv

1	Introduction	1-1

1.1	Purpose and scope	1-1

1.2	Applicability	1-1

1.3	Document structure	1-1

1.4	References	1-1

2	Blue Book promotion criteria	2-1

3	conclusions and recommendation	3-1

4	RDM Test plan	4-1

4.1	RDM test plan overview	4-1

4.2	Test plan details	4-1

4.2.1	Test case #1: KVN-XML conversion	4-1

4.2.2	Test case #2: Long-term prediction	4-2

4.2.3	Test case #3: short-term prediction	4-2

4.2.4	Test case #4: ground impact location	4-3

4.2.5	Test case #5: ground impact location uncertainty	4-3

5	RDM test report	5-1

5.1	Test results overview	5-1

5.2	Test results	5-2

5.2.1	Test case #1: KVN to XML conversion	5-2

5.2.2	Test case #2: long term prediction	5-3

5.2.3	Test case #3: short term prediction	5-6

5.2.4	Test case #4: ground impact location	5-9

5.2.5	Test case #5: ground impact location uncertainty	5-13

# Introduction

## Purpose and scope

The purpose of this document is to describe the prototyping conducted for the CCSDS Re-entry Data Message (RDM), specified in reference [1]. Both the prototyping plan and the report are contained in this document.

The scope of this document is test plans and test reports for version 1 of the CCSDS Re-entry Data Message.

## Applicability

The document applies to the entirety of the Re-entry Data Message, version 1, as specified in reference [1].

## Document structure

Section 2 contains the promotion criteria from a Red Book to a Blue Book.

Section 3 presents the conclusions and recommendations of this prototyping campaign.

Section 4 presents the test plan followed by the RDM prototyping campaign.

Section 5 contains the results of the RDM prototyping campaign.

Annex A lists the distribution of RDM keywords between the prototyping tests.

Annex B contains the test plan report template.

Annex C lists the acronyms used in this document.

Annex D contains the OPMs used as input for the re-entry simulations in the prototyping campaign.

Annex E contains the RDMs generated during the prototyping campaign.

## References

The following publications are referenced in this document.  At the time of publication, the editions indicated were valid.  All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

| [1] | Re-entry Data Message. Recommendation for Space Data System Standards (Red Book), CCSDS 508.1-R-1.3. Washington, D.C.: CCSDS, October 2018. |
| --- | --- |
| [2] | Organization and Processes for the Consultative Committee for Space Data Systems. Issue 4. Report Concerning Space Data Systems Standards (Yellow Book). CCSDS A02.1-Y-4. Washington, D.C.: CCSDS, April 2014. |

# Blue Book promotion criteria

The CCSDS Procedures Manual [2] states that for a Recommendation to become a Blue Book, the standard must be tested in an operational manner. Reference [2] contains the following requirements for an implementation exercise:

“At least two independent and interoperable prototypes or implementations must have been developed and demonstrated in an operationally relevant environment, either real or simulated, unless a waiver of the interoperability testing requirement has been approved:”

This document will outline the Navigation Working Group’s approach to meeting this requirement for the RDM.

# conclusions and recommendation

Three RDM Prototypes were developed at two CCSDS member agencies: ESA/ESOC (2 prototypes) and DLR/GSOC. A suite of five test cases covered the interagency exchange of re-entry prediction results (long-term, short-term, ground impact location, ground impact location uncertainty, and KVN to XML conversion). The re-entry data was generated by the re-entry prediction systems operated by ESA/ESOC and DLR/GSOC using their normal operational procedures and processes. An orbit based on the SATCAT was used for the long-term prediction test case, while orbits determined by ESA/ESOC from real tracking data were used for the short-term, ground impact, and ground impact uncertainty cases. Based on this operational diversity and the positive test results, the RDM prototyping effort successfully addresses the Blue Book promotion criteria. It is thus proposed to approve the Re-entry Data Message as a CCSDS Recommended Standard.

# RDM Test plan

## RDM test plan overview

The testing approach for the RDM will contain the following cases:

- Long-term re-entry prediction

- Short-term re-entry prediction

- Ground impact (no uncertainty)

- Ground impact (with impact location uncertainty)

- XML Re-entry Data Message

The following table lists the test number, spacecraft, agencies involved (including the direction of the data flow), which test case is being covered, and tentative schedule.

| Test# | Spacecraft | Agencies, Direction | Test Case | Schedule |
| --- | --- | --- | --- | --- |
| 1 | multiple spacecraft | ESA/ESOC internal | KVN-XML conversion | Late 2018 |
| 2 | AVUM R/B (2012-006K) | ESA/ESOC internal (2 prototypes) DLR/GSOC=>ESA/ESOC | Long-term prediction | Late 2018 |
| 3 | AVUM R/B (2012-006K) | ESA/ESOC internal (2 prototypes) DLR/GSOC=>ESA/ESOC | Short-term prediction | Late 2018 – Early 2019 |
| 4 | AVUM R/B (2012-006K) | ESA/ESOC internal (2 prototypes) DLR/GSOC=>ESA/ESOC | Ground impact location (no uncertainty) | Late 2018 – Early 2019 |
| 5 | AVUM R/B (2012-006K) | ESA/ESOC internal (2 prototypes) DLR/GSOC=>ESA/ESOC | Ground impact location (with impact location uncertainty) | Late 2018 – Early 2019 |

All tests described in this document will be conducted to meet the CCSDS prototyping requirements. The results of these tests are presented in section 5. The distribution of mandatory and optional keywords between the test cases can be found in annex A.

## Test plan details

### Test case #1: KVN-XML conversion

This is an internal test case and will not involve message exchange between agencies. ESA/ESOC will generate a set of KVN RDMs for multiple dummy re-entries. The RDMs will contain all the mandatory keywords, plus varying optional keywords by message, and user defined keywords. ESA will process the RDMs with its RDM tool and convert them from KVN to XML to KVN to XML to KVN. The XML RDMs will be checked for compliance against the RDM XML schema with Liquid XML. The two sets of KVN RDMs generated by the ESOC prototype tool will be compared to see if they are identical as well. The Test Data Sheet will be supplied by ESA/ESOC.

Expected results

The conversions from KVN to XML and from XML to KVN shall be completed without errors. The XML RDMs will comply with the schema. The KVN RDMs produced by the tool and the originals shall contain the same data (allowing for formatting differences). The KVN RDMs generated by the tool at different steps shall be identical. Assuming these criteria are met, the test will be considered successful. In the event of discrepancies, troubleshooting will be conducted by ESA/ESOC.

### Test case #2: Long-term prediction

For this test case, a reference OPM for the 2012-006K AVUM rocket body will be generated, based on its TLE around 1 year before re-entry. This OPM will be ingested by both the ESA/ESOC and DLR/GSOC re-entry prediction systems and both will generate one RDM containing the remaining orbit lifetime, re-entry altitude, orbit lifetime window start and end, one state vector, and object properties (a full list of expected keywords in these RDMs can be found in column #2 in the table in annex A). The contents of the two RDMs (one generated by ESA/ESOC, one by DLR/GSOC) will be compared. ESA/ESOC will generate RDMs in XML and DLR/GSOC in KVN. The Test Data Sheet will be provided by ESA/ESOC.

As both the ESA/ESOC and DLR/GSOC re-entry prediction systems write the state vector used as input to the output RDM, re-running the tests with the other agency's RDM as input will not be performed. The KVN-XML converter will be used to read the files and check that they comply with the standard. The converter does not share any code with the ESA/ESOC re-entry prediction system or its RDM-generating components.

Expected results

It is anticipated that the two RDMs produced will contain remaining orbital lifetimes within each other's confidence intervals and that both will be read/converted without issues. Assuming these criteria are met, the test will be considered successful. In the event of discrepancies, troubleshooting will be conducted by the participating agencies.

### Test case #3: short-term prediction

For this test case, a reference OPM for the 2012-006K AVUM rocket body will be generated by ESA/ESOC, based on available tracking data in the last few weeks/days before re-entry. The OPM will be ingested by both the ESA/ESOC and DLR/GSOC re-entry prediction systems and both will generate one RDM containing the predicted re-entry epoch, re-entry window start/end, one state vector, and object properties (a full list of expected keywords in these RDMs can be found in column #3 in the table in annex A). The contents of the two RDMs (one generated by ESA/ESOC, one by DLR/GSOC) will be compared. ESA/ESOC will generate RDMs in XML and DLR/GSOC in KVN. The Test Data Sheet will be provided by ESA/ESOC.

As both the ESA/ESOC and DLR/GSOC re-entry prediction systems write the state vector used as input to the output RDM, re-running the tests with the other agency's RDM will not be performed. The KVN-XML converter will be used to read the files and check that they comply with the standard. The converter does not share any code with the ESA/ESOC re-entry prediction system or its RDM-generating components.

Expected results

It is anticipated that the two RDMs produced will contain predicted re-entry epochs within each other's re-entry windows and that both will be read/converted without issues. Assuming these criteria are met, the test will be considered successful. In the event of discrepancies, troubleshooting will be conducted by the participating agencies.

### Test case #4: ground impact location

For this test case, a reference OPM for the 2012-006K AVUM rocket body will be generated by ESA/ESOC, based on available tracking data in the last few weeks/days before re-entry. The OPM will be ingested by both the ESA/ESOC and DLR/GSOC re-entry prediction systems and both will generate one RDM containing the predicted ground impact location (a full list of expected keywords in these RDMs can be found in column #4 in the table in annex A). The contents of the two RDMs (one generated by ESA/ESOC, one by DLR/GSOC) will be compared and the location plotted. ESA/ESOC will generate RDMs in XML and DLR/GSOC in KVN.  The KVN-XML converter will be used to read the files and check that they comply with the standard. The converter does not share any code with the ESA/ESOC re-entry prediction system or its RDM-generating components. The Test Data Sheet will be provided by ESA/ESOC.

Expected results

It is anticipated that both RDMs will be read/converted without issues and the ground impact location can be plotted. In the event of discrepancies, troubleshooting will be conducted by the participating agencies.

### Test case #5: ground impact location uncertainty

For this test case, a reference OPM for the 2012-006K AVUM rocket body will be generated by ESA/ESOC, based on available tracking data in the last few weeks/days before re-entry. The OPM will be ingested by both the ESA/ESOC and DLR/GSOC re-entry prediction systems and both will generate one RDM containing the predicted ground impact location and 3 confidence intervals (a full list of expected keywords in these RDMs can be found in column #5 in the table in annex A). The contents of the two RDMs (one generated by ESA/ESOC, one by DLR/GSOC) will be compared. ESA/ESOC will generate RDMs in XML and DLR/GSOC in KVN. The KVN-XML converter will be used to read the files and check that they comply with the standard. The converter does not share any code with the ESA/ESOC re-entry prediction system or its RDM-generating components. The Test Data Sheet will be provided by ESA/ESOC.

Expected results

It is anticipated that both RDMs will be read/converted without issues and the ground impact location and uncertainties can be plotted. In the event of discrepancies, troubleshooting will be conducted by the participating agencies.

# RDM test report

## Test results overview

Engineers at participating agencies will prepare test data sheets as noted in the Test Plan Details above, and send them to the Navigation Working Group via email.

The Test Report Details will be found in the following sections of this document.  A summary of the test process and the recommendation of the Navigation Working Group may be found in Section 3 of the report.  The report will be posted to the Navigation Working Group Common Working Environment (CWE) on the CCSDS web page at http://cwe.ccsds.org. The report will be submitted to the CCSDS Engineering Steering Group (CESG) and CCSDS Management Council (CMC), along with results of the Agency Reviews. At that time, a formal request will be submitted to the CMC for progression of the RDM to CCSDS Blue Book status.

Annex B contains a format for the test data sheets that will be used to report the results of individual tests.

Annex D contains the OPM files used as input for the simulations.

Annex E contains all the RDMs produced for test cases #2 to #5 (both KVN and XML).

## Test results

### Test case #1: KVN to XML conversion

| 1 | Test Case Number: | 1 |
| --- | --- | --- |
| 2 | Report Date: | 1-Nov-2018 |
| 3 | Program Under Test: | Re-entry Data Message V1 (RDM) Prototype |
| 4 | Agencies Participating in this Test Case: | ESA/ESOC: Space Debris Office |
| 5 | Agency Responsible for Prototype: | RDM Generation: ESA/ESOC RDM Processing: ESA/ESOC |
| 6 | Prototype Version # (if applicable): | RDM Generation: v0.3 RDM Processing: v0.3 |
| 7 | Test Engineer: | RDM Generation: Alexandru Mancas RDM Processing: Alexandru Mancas |
| 8 | Spacecraft: | multiple dummy spacecraft |
| 9 | Re-entry keywords tested: | all keywords tested in 7 files: reference_kvn_all_keywords.rdm: all keywords, including 3 user defined keywords reference_kvn_all_keywords_no_blanks.rdm: all keywords, including 3 user defined keywords reference_kvn_covariance.rdm: mandatory keywords + covariance-related keywords reference_kvn_ground_impact_small.rdm: mandatory keywords + 2 ground impact keywords reference_kvn_minimal.rdm: only mandatory keywords reference_kvn_spacecraft.rdm: mandatory keywords + object physical properties keywords reference_kvn_state_vector.rdm: mandatory keywords + state vector keywords reference_kvn_state_vector_covariance.rdm: mandatory keywords + state vector keywords + covariance keywords |
| 10 | Values for the keywords of interest: | n/a |
| 11 | Variances from Expected Results: | none |
| 12 | Results (Pass, Partial Pass, Fail): | Pass |
| 13 | Comments: | ESA/ESOC developed a converter between XML and KVN RDMs in FORTRAN. The tool reads multiple RDM files in either XML or KVN and writes one output RDM in KVN or XML respectively for each RDM read. No changes are made to the contents of the input messages, but the 'default' formatting is imposed on all output files. The tool successfully read KVN RDMs written by hand or by the tool and XML RDMs written by the tool. All the XML RDMs written were checked against the schema with Liquid XML and were compliant. This test case included all keywords, including user defined keywords. |

### Test case #2: long term prediction

| 1 | Test Case Number: | 2 |
| --- | --- | --- |
| 2 | Report Date: | 18-Feb-2019 |
| 3 | Program Under Test: | Re-entry Data Message V1 (RDM) Prototype |
| 4 | Agencies Participating in this Test Case: | ESA/ESOC DLR/GSOC |
| 5 | Agency Responsible for Prototype: | RDM Generation: ESA/ESOC, DLR/GSOC RDM Processing: ESA/ESOC |
| 6 | Prototype Version # (if applicable): | RDM Generation: n/a RDM Processing: n/a |
| 7 | Test Engineer: | RDM Generation: Alexandru Mancas, Michael Kirschner RDM Processing: Alexandru Mancas |
| 8 | Spacecraft: | AVUM R/B (2012-006K) |
| 9 | Re-entry keywords tested: | ORBIT_LIFETIME, REENTRY_ALTITUDE, ORBIT_LIFETIME_WINDOW_START, ORBIT_LIFETIME_WINDOW_END, state vector block, covariance block, object properties block |
| 10 | Values for the keywords of interest: | see table later in section 5.2.2 |
| 11 | Variances from Expected Results: | The ORBIT_LIFETIME_CONFIDENCE values did not appear to be correct. After discussions with the other engineers involved in the prototyping, it was determined the name of the keyword does not match the description that well, and that the description is not clear enough. The value is supposed to be a confidence level, but was interpreted during prototype implementation as a confidence interval. The draft standard was corrected to eliminate this ambiguity; the keyword was changed to ORBIT_LIFETIME_ CONFIDENCE_LEVEL and the description clarified. |
| 12 | Results (Pass, Partial Pass, Fail): | Pass |
| 13 | Comments: | The orbit lifetime of each message is within the lifetime window of the other message. Both re-entry prediction systems write the state vector that was used as input to the output RDM. Since the state vectors are (almost) the same (there is a 20 ms difference between them), there was no need to re-run the simulation using the other agency's RDM as input. |

The RDM files produced by ESA/ESOC and DLR/GSOC contained the relevant keywords and values shown the table below.

| keyword | ESA/ESOC value | DLR/GSOC value |
| --- | --- | --- |
| header |
| CCSDS_RDM_VERS | 0.1 | 1.0 |
| COMMENT | Test-case#2: long term prediction | — |
| CREATION_DATE | 2015-11-02T11:24:20.000000 | 2018-11-30T15:30:54.272 |
| ORIGINATOR | ESA-SDO | GSOC |
| MESSAGE_ID | 2012-006K_20181108112420_ESA-SDO_5343 | GSOC/2018-11-30T15:30:54UTC |
| metadata |
| COMMENT | — | — |
| OBJECT_NAME | AVUM (Vega) | AVUM R/B |
| INTERNATIONAL_DESIGNATOR | 2012-006K | 2012-006K |
| CATALOG_NAME | SATCAT | SATCAT |
| OBJECT_DESIGNATOR | 38086 | 12345 |
| OBJECT_TYPE | ROCKET BODY | UNKNOWN |
| CONTROLLED_REENTRY | NO | NO |
| CENTER_NAME | EARTH | EARTH |
| TIME_SYSTEM | UTC | UTC |
| EPOCH_TZERO | 2015-11-01T20:05:40.020000 | 2015-11-01T20:05:40.000 |
| REF_FRAME | EME2000 | TOD |
| GRAVITY_MODEL | GEM-T1: 8D 8O | GGM01S: 08D 08O |
| ATMOSPHERIC_MODEL | DTM-13 | JACCHIA-GILL |
| SOLAR_FLUX_PREDICTION | ESA SOLMAG | PREDICTED: MLLRT |
| N_BODY_PERTURBATIONS | MOON, SUN | SUN, MOON |
| SOLAR_RAD_PRESSURE | CYLINDRICAL | CANNONBALL |
| EARTH_TIDES | NO | MCCARTHY1996 |
| INTRACK_THRUST | NO | NO |
| DRAG_PARAMETERS_SOURCE | CD FITTING WITH FOCUS2 | OD |
| DRAG_PARAMETERS_ALTITUDE | 244.72 | 491.8595 |
| REENTRY_UNCERTAINTY_METHOD | EMPIRICAL | EMPIRICAL |
| REENTRY_DISINTEGRATION | NONE | NONE |
| data |
| atmospheric re-entry |
| COMMENT | Prediction 1 year before re-entry | — |
| ORBIT_LIFETIME | 366.677083333333 | 385.4993 |
| REENTRY_ALTITUDE | 78.417 | 120.0000 |
| ORBIT_LIFETIME_WINDOW_START | 293.341666666667 | 308.3994 |
| ORBIT_LIFETIME_WINDOW_END | 440.0125 | 462.5992 |
| ORBIT_LIFETIME_CONFIDENCE | 20.0000 | 20.0 |
| state vector |
| COMMENT | epoch of latest TLE (same as epoch_tzero) | — |
| EPOCH | 2015-11-01T20:05:40.020000 | 2015-11-01T20:05:40.000 |
| X | -5915.23575248928 | -5925.7575000000 |
| Y | 2990.05003661959 | 2969.1288510000 |
| Z | -0.00415629948475475 | -9.2273870000 |
| X_DOT | -1.22748377325454 | -1.2300694874 |
| Y_DOT | -2.47530416266088 | -2.4793156054 |
| Z_DOT | 7.38675878149886 | 7.3849831139 |
| object properties |
| COMMENT | Cr is fixed, Cd includes all effects | — |
| WET_MASS | 960.0 | 960.0 |
| DRY_MASS | 410.0 | — |
| SOLAR_RAD_AREA | 1.0 | 1.0 |
| SOLAR_RAD_COEFF | 1.2 | 1.2 |
| DRAG_AREA | 3.9545 | 3.95 |
| DRAG_COEFF | 2.4108 | 2.4108 |
| BALLISTIC_COEFF | 0.009931 | — |

### Test case #3: short term prediction

| 1 | Test Case Number: | 3 |
| --- | --- | --- |
| 2 | Report Date: | 18-Feb-2019 |
| 3 | Program Under Test: | Re-entry Data Message V1 (RDM) Prototype |
| 4 | Agencies Participating in this Test Case: | ESA/ESOC DLR/GSOC |
| 5 | Agency Responsible for Prototype: | RDM Generation: ESA/ESOC, DLR/GSOC RDM Processing: ESA/ESOC |
| 6 | Prototype Version # (if applicable): | RDM Generation: n/a RDM Processing: n/a |
| 7 | Test Engineer: | RDM Generation: Alexandru Mancas, Michael Kirschner RDM Processing: Alexandru Mancas |
| 8 | Spacecraft: | AVUM R/B (2012-006K) |
| 9 | Re-entry keywords tested: | ORBIT_LIFETIME, REENTRY_ALTITUDE, NOMINAL_REENTRY_EPOCH, REENTRY_WINDOW_START, REENTRY_WINDOW_END state vector block, covariance block, spacecraft properties block |
| 10 | Values for the keywords of interest: | See table later in section 5.2.3 |
| 11 | Variances from Expected Results: | The two re-entry prediction systems use different atmospheric models, solar flux predictions, and slightly different re-entry altitudes (all are clearly described in the metadata of each message): 70 km for DLR/GSOC and 76.88 km for ESA/ESOC. As a consequence, there is a 3.5 hour difference between the values of the NOMINAL_REENTRY_EPOCH keywords between the messages, but both are inside the predicted re-entry window of the other message. The two predicted windows show the same shift of about 4 hours between the ESA/ESOC and DLR/GSOC start/stop epochs. The ORBIT_LIFETIME_CONFIDENCE values did not appear to be correct. After discussions with the other engineers involved in the prototyping, it was determined the name of the keyword does not match the description that well, and that the description is not clear enough. The value is supposed to be a confidence level, but was interpreted during prototype implementation as a confidence interval. The draft standard was corrected to eliminate this ambiguity; the keyword was changed to ORBIT_LIFETIME_ CONFIDENCE_LEVEL and the description clarified. |
| 12 | Results (Pass, Partial Pass, Fail): | Pass |
| 13 | Comments: | Both re-entry prediction systems write the state vector that was used as input to the output RDM. Since the state vectors are (almost) the same (there is a 3.84 ms difference between them), there was no need to re-run the simulation using the other agency's RDM as input. |

The RDM files produced by ESA/ESOC and DLR/GSOC contained the relevant keywords and values shown the table below.

| keyword | ESA/ESOC value | DLR/GSOC value |
| --- | --- | --- |
| header |
| CCSDS_RDM_VERS | 0.3 | 1.0 |
| COMMENT | Test-case#3: short term prediction | — |
| CREATION_DATE | 2016-10-28T14:22:56.000000 | 2019-01-10T13:13:24.063 |
| ORIGINATOR | ESA-SDO | GSOC |
| MESSAGE_ID | 2012-006K_20181108142256_ESA-SDO_9F5B | GSOC/2019-01-10T13:13:24UTC |
| metadata |
| OBJECT_NAME | AVUM (Vega) | AVUM R/B |
| INTERNATIONAL_DESIGNATOR | 2012-006K | 2012-006K |
| CATALOG_NAME | SATCAT | — |
| OBJECT_DESIGNATOR | 38086 | — |
| OBJECT_TYPE | ROCKET BODY | — |
| CONTROLLED_REENTRY | NO | NO |
| CENTER_NAME | EARTH | EARTH |
| TIME_SYSTEM | UTC | UTC |
| EPOCH_TZERO | 2016-10-28T11:41:00.000384 | 2016-10-28T11:41:00.000 |
| REF_FRAME | EME2000 | TOD |
| GRAVITY_MODEL | GEM-T1: 8D 8O | GGM01S: 20D 20O |
| ATMOSPHERIC_MODEL | DTM-13 | JACCHIA-GILL |
| SOLAR_FLUX_PREDICTION | ESA SOLMAG | PREDICTED: MLLRT |
| N_BODY_PERTURBATIONS | MOON, SUN | SUN, MOON |
| SOLAR_RAD_PRESSURE | CYLINDRICAL SHADOW | CANNONBALL |
| EARTH_TIDES | NO | MCCARTHY1996 |
| INTRACK_THRUST | NO | NO |
| DRAG_PARAMETERS_SOURCE | CD FITTING WITH FOCUS2 | — |
| DRAG_PARAMETERS_ALTITUDE | 244.72 | — |
| REENTRY_UNCERTAINTY_METHOD | EMPIRICAL | — |
| REENTRY_DISINTEGRATION | NONE | NONE |
| data |
| atmospheric re-entry |
| COMMENT | Prediction based on 2 TIRA passes as last orbit state, 5 days before re-entry | — |
| ORBIT_LIFETIME | 5.04375 | 4.8915 |
| REENTRY_ALTITUDE | 76.88 | 70.0000 |
| NOMINAL_REENTRY_EPOCH | 2016-11-02T12:38:07.000000 | 2016-11-02T09:04:43.000 |
| REENTRY_WINDOW_START | 2016-11-01T12:31:31.000000 | 2016-11-01T09:35:58.400 |
| REENTRY_WINDOW_END | 2016-11-03T12:56:43.000000 | 2016-11-03T08:33:27.600 |
| ORBIT_LIFETIME_CONFIDENCE | 20.0000 | 20.0000 |
| state vector |
| COMMENT | epoch of OD from 2 TIRA tracks | — |
| EPOCH | 2016-10-28T11:41:00.000384 | 2016-10-28T11:41:00.000 |
| X | -2095.41001813074 | -2092.8991170000 |
| Y | -3040.70137293811 | -3048.2867570000 |
| Z | 5458.83815375429 | 5455.5699160000 |
| X_DOT | 6.87141346593969 | 6.8607473416 |
| Y_DOT | 1.3852134950239 | 1.4109533544 |
| Z_DOT | 3.36023038345871 | 3.3712971129 |
| object properties |
| COMMENT | Cr is fixed, Cd includes all effects | — |
| WET_MASS | 960.0 | 960.0000000000 |
| DRY_MASS | 410.0 | — |
| SOLAR_RAD_AREA | 1.0 | 1.0000000000 |
| SOLAR_RAD_COEFF | 1.2 | 1.2000000000 |
| DRAG_AREA | 3.9545 | 3.9500000000 |
| DRAG_COEFF | 2.3588 | 2.3588000000 |
| BALLISTIC_COEFF | 0.009717 | — |
| OD parameters |
| COMMENT | two TIRA tracks | — |
| TIME_LASTOB_START | 2016-10-27T11:54:20.000000 | — |
| TIME_LASTOB_END | 2016-10-28T11:41:00.000000 | — |
| RECOMMENDED_OD_SPAN | 2.0 | — |
| ACTUAL_OD_SPAN | 1.0 | — |
| OBS_AVAILABLE | 655 | — |
| OBS_USED | 655 | — |
| TRACKS_AVAILABLE | 2 | — |
| TRACKS_USED | 2 | — |
| RESIDUALS_ACCEPTED | 100.0 | — |
| WEIGHTED_RMS | 0.0097 | — |

### Test case #4: ground impact location

| 1 | Test Case Number: | 4 |
| --- | --- | --- |
| 2 | Report Date: | 18-Feb-2019 |
| 3 | Program Under Test: | Re-entry Data Message V1 (RDM) Prototype |
| 4 | Agencies Participating in this Test Case: | ESA/ESOC DLR/GSOC |
| 5 | Agency Responsible for Prototype: | RDM Generation: ESA/ESOC, DLR/GSOC RDM Processing: ESA/ESOC |
| 6 | Prototype Version # (if applicable): | RDM Generation: n/a RDM Processing: n/a |
| 7 | Test Engineer: | RDM Generation: Alexandru Mancas, Michael Kirschner RDM Processing: Alexandru Mancas |
| 8 | Spacecraft: | AVUM R/B (2012-006K) |
| 9 | Re-entry keywords tested: | ORBIT_LIFETIME, REENTRY_ALTITUDE, NOMINAL_REENTRY_EPOCH, REENTRY_WINDOW_START, REENTRY_WINDOW_END, NOMINAL_IMPACT_EPOCH, IMPACT_WINDOW_START, IMPACT_WINDOW_END, IMPACT_REF_FRAME, NOMINAL_IMPACT_LON, NOMINAL_IMPACT_LAT, NOMINAL_IMAPCT_ALT. state vector block, covariance block, spacecraft properties block |
| 10 | Values for the keywords of interest: | See table later in section 5.2.4 |
| 11 | Variances from Expected Results: | The nominal impact location coordinates are quite different, but the nominal impact epochs are within the other message's window. The former is to be expected, as the two re-entry prediction systems use different gravity, atmospheric, solar flux, solar radiation pressure, and Earth tides models. The ORBIT_LIFETIME_CONFIDENCE values did not appear to be correct. After discussions with the other engineers involved in the prototyping, it was determined the name of the keyword does not match the description that well, and that the description is not clear enough. The value is supposed to be a confidence level, but was interpreted during prototype implementation as a confidence interval. The draft standard was corrected to eliminate this ambiguity; the keyword was changed to ORBIT_LIFETIME_ CONFIDENCE_LEVEL and the description clarified. |
| 12 | Results (Pass, Partial Pass, Fail): | Pass |
| 13 | Comments: | — |

The RDM files produced by ESA/ESOC and DLR/GSOC contained the relevant keywords and values shown the table below.

| keyword | ESA/ESOC value | DLR/GSOC value |
| --- | --- | --- |
| header |
| CCSDS_RDM_VERS | 0.1 | 1.0 |
| COMMENT | Test-case#4: short term prediction with ground impact location | — |
| CREATION_DATE | 2016-10-28T15:22:56.000000 | 2019-01-10T13:18:45.160 |
| ORIGINATOR | ESA-SDO | GSOC |
| MESSAGE_ID | 2012-006K_20181108152256_ESA-SDO_2345 | GSOC/2019-01-10T13:18:45UTC |
| metadata |
| OBJECT_NAME | AVUM (Vega) | AVUM R/B |
| INTERNATIONAL_DESIGNATOR | 2012-006K | 2012-006K |
| CATALOG_NAME | SATCAT | — |
| OBJECT_DESIGNATOR | 38086 | — |
| OBJECT_TYPE | ROCKET BODY | — |
| CONTROLLED_REENTRY | NO | NO |
| CENTER_NAME | EARTH | EARTH |
| TIME_SYSTEM | UTC | UTC |
| EPOCH_TZERO | 2016-10-28T11:41:00.000384 | 2016-10-28T11:41:00.000 |
| REF_FRAME | EME2000 | — |
| GRAVITY_MODEL | GEM-T1: 8D 8O | — |
| ATMOSPHERIC_MODEL | DTM-13 | — |
| SOLAR_FLUX_PREDICTION | ESA SOLMAG | — |
| N_BODY_PERTURBATIONS | MOON, SUN | — |
| SOLAR_RAD_PRESSURE | CYLINDRICAL SHADOW | — |
| EARTH_TIDES | NO | — |
| INTRACK_THRUST | NO | — |
| DRAG_PARAMETERS_SOURCE | CD FITTING WITH FOCUS2 | — |
| DRAG_PARAMETERS_ALTITUDE | 179.490 | — |
| REENTRY_UNCERTAINTY_METHOD | EMPIRICAL | — |
| REENTRY_DISINTEGRATION | NONE | NONE |
| data |
| atmospheric re-entry |
| COMMENT | Prediction based on 2 TIRA passes as last orbit state, 5 days before re-entry | — |
| ORBIT_LIFETIME | 5.04375 | 4.8913 |
| REENTRY_ALTITUDE | 76.88 | 70.0000 |
| NOMINAL_REENTRY_EPOCH | 2016-11-02T12:38:07.000000 | — |
| REENTRY_WINDOW_START | 2016-11-01T12:31:31.000000 | — |
| REENTRY_WINDOW_END | 2016-11-03T12:56:43.000000 | — |
| ORBIT_LIFETIME_CONFIDENCE | 20.0000 | 20.0000 |
| ground impact |
| COMMENT | As it is 5 days before re-entry, still all the world is under the ground-track | — |
| PROBABILITY_OF_IMPACT | 1.0 | — |
| PROBABILITY_OF_BURN_UP | 0.0 | — |
| PROBABILITY_OF_BREAK_UP | 0.5 | — |
| PROBABILITY_OF_LAND_IMPACT | 0.3 | — |
| PROBABILITY_OF_CASUALTY | 1e-05 | — |
| NOMINAL_IMPACT_EPOCH | 2016-11-02T12:44:07.000000 | 2016-11-02T09:04:30.000 |
| IMPACT_WINDOW_START | 2016-11-01T12:31:31.000000 | 2016-11-01T09:35:48.000 |
| IMPACT_WINDOW_END | 2016-11-03T12:56:43.000000 | 2016-11-03T08:33:12.000 |
| IMPACT_REF_FRAME | WGS84 | WGS84 |
| NOMINAL_IMPACT_LON | 150.47 | 2.3946 |
| NOMINAL_IMPACT_LAT | -29.79 | -15.6304 |
| NOMINAL_IMPACT_ALT | 8.2028 | 70.0000 |
| state vector |
| COMMENT | epoch of OD from 2 TIRA tracks | — |
| EPOCH | 2016-10-28T11:41:00.000384 | — |
| X | -2095.41001813074 | — |
| Y | -3040.70137293811 | — |
| Z | 5458.83815375429 | — |
| X_DOT | 6.87141346593969 | — |
| Y_DOT | 1.3852134950239 | — |
| Z_DOT | 3.36023038345871 | — |
| object properties |
| COMMENT | Cr is fixed, Cd includes all effects | — |
| WET_MASS | 960.0 | — |
| DRY_MASS | 410.0 | — |
| SOLAR_RAD_AREA | 1.0 | — |
| SOLAR_RAD_COEFF | 1.2 | — |
| DRAG_AREA | 3.9545 | — |
| DRAG_COEFF | 2.3588 | — |
| BALLISTIC_COEFF | 0.009717 | — |
| OD parameters |
| COMMENT | two TIRA tracks | — |
| TIME_LASTOB_START | 2016-10-27T11:54:20.000000 | — |
| TIME_LASTOB_END | 2016-10-28T11:41:00.000000 | — |
| RECOMMENDED_OD_SPAN | 2.0 | — |
| ACTUAL_OD_SPAN | 1.0 | — |
| OBS_AVAILABLE | 655 | — |
| OBS_USED | 655 | — |
| TRACKS_AVAILABLE | 2 | — |
| TRACKS_USED | 2 | — |
| RESIDUALS_ACCEPTED | 100.0 | — |
| WEIGHTED_RMS | 0.0097 | — |

The compasion between the DLR/GSOC predicted impact location (red) and ESA/ESOC predicted location (blue) can be seen in the figure below.

### Test case #5: ground impact location uncertainty

| 1 | Test Case Number: | 5 |
| --- | --- | --- |
| 2 | Report Date: | 18-Feb-2019 |
| 3 | Program Under Test: | Re-entry Data Message V1 (RDM) Prototype |
| 4 | Agencies Participating in this Test Case: | ESA/ESOC DLR/GSOC |
| 5 | Agency Responsible for Prototype: | RDM Generation: ESA/ESOC, DLR/GSOC RDM Processing: ESA/ESOC |
| 6 | Prototype Version # (if applicable): | RDM Generation: n/a RDM Processing: n/a |
| 7 | Test Engineer: | RDM Generation: Alexandru Mancas, Michael Kirschner RDM Processing: Alexandru Mancas |
| 8 | Spacecraft: | AVUM R/B (2012-006K) |
| 9 | Re-entry keywords tested: | ORBIT_LIFETIME, REENTRY_ALTITUDE, NOMINAL_REENTRY_EPOCH, REENTRY_WINDOW_START, REENTRY_WINDOW_END, NOMINAL_IMPACT_EPOCH, IMPACT_WINDOW_START, IMPACT_WINDOW_END, IMPACT_REF_FRAME, NOMINAL_IMPACT_LON, NOMINAL_IMPACT_LAT, NOMINAL_IMAPCT_ALT, IMPACT_*_CONFIDENCE, IMPACT_*_START_LON, IMPACT_*_START_LAT, IMPACT_*_STOP_LON, IMPACT_*_STOP_LAT, IMPACT_*_CROSS_TRACK. |
| 10 | Values for the keywords of interest: | See table later in section 5.2.5 |
| 11 | Variances from Expected Results: | The DLR/GSOC-predicted ground impact epoch is 50 minutes before the epoch predicted by ESA/ESOC, but inside ESA's impact window. The DLR impact window is short and the ESA nominal impact epoch is outside of it. The predicted impact locations and uncertainties do not match, but that is to be expected due to the different modelling and impact uncertainty methods used. The ORBIT_LIFETIME_CONFIDENCE values did not appear to be correct. After discussions with the other engineers involved in the prototyping, it was determined the name of the keyword does not match the description that well, and that the description is not clear enough. The value is supposed to be a confidence level, but was interpreted during prototype implementation as a confidence interval. The draft standard was corrected to eliminate this ambiguity; the keyword was changed to ORBIT_LIFETIME_ CONFIDENCE_LEVEL and the description clarified. |
| 12 | Results (Pass, Partial Pass, Fail): | Pass |
| 13 | Comments: | — |

The RDM files produced by ESA/ESOC and DLR/GSOC contained the relevant keywords and values shown the table below.

| keyword | ESA/ESOC value | DLR/GSOC value |
| --- | --- | --- |
| header |
| CCSDS_RDM_VERS | 0.1 | 1.0 |
| COMMENT | Test-case#5: very short term prediction with ground impact location and uncertainties | — |
| CREATION_DATE | 2016-11-01T20:14:02.000000 | 2018-11-30T15:15:51.554 |
| ORIGINATOR | ESA-SDO | GSOC |
| MESSAGE_ID | 2012-006K_20181109141402_ESA-SDO_E231 | GSOC/2018-11-30T15:15:51UTC |
| metadata |
| OBJECT_NAME | AVUM (Vega) | AVUM R/B |
| INTERNATIONAL_DESIGNATOR | 2012-006K | 2012-006K |
| CATALOG_NAME | SATCAT | — |
| OBJECT_DESIGNATOR | 38086 | — |
| OBJECT_TYPE | ROCKET BODY | — |
| CONTROLLED_REENTRY | NO | NO |
| CENTER_NAME | EARTH | EARTH |
| TIME_SYSTEM | UTC | UTC |
| EPOCH_TZERO | 2016-11-01T19:03:00.673920 | 2016-11-01T19:03:00.000 |
| REF_FRAME | EME2000 | — |
| GRAVITY_MODEL | GEM-T1: 8D 8O | — |
| ATMOSPHERIC_MODEL | DTM-13 | — |
| SOLAR_FLUX_PREDICTION | ESA SOLMAG | — |
| N_BODY_PERTURBATIONS | MOON, SUN | — |
| SOLAR_RAD_PRESSURE | CYLINDRICAL | — |
| EARTH_TIDES | NO | — |
| INTRACK_THRUST | NO | — |
| DRAG_PARAMETERS_SOURCE | CD FITTING WITH FOCUS2 | — |
| DRAG_PARAMETERS_ALTITUDE | 141.04 | — |
| REENTRY_UNCERTAINTY_METHOD | EMPIRICAL | — |
| REENTRY_DISINTEGRATION | NONE | BREAK-UP |
| IMPACT_UNCERTAINTY_METHOD | EMPIRICAL | MONTE CARLO |
| data |
| atmospheric re-entry |
| COMMENT | COMMENT Latest prediction | — |
| ORBIT_LIFETIME | 0.416666666666667 | 0.3758 |
| REENTRY_ALTITUDE | 77.0460000000000 | 80.0000 |
| NOMINAL_REENTRY_EPOCH | 2016-11-02T04:57:42.000000 | — |
| REENTRY_WINDOW_START | 2016-11-02T02:57:42.000000 | — |
| REENTRY_WINDOW_END | 2016-11-02T06:57:42.000000 | — |
| ground impact |
| COMMENT | Still 3 complete ground tracks around the globe | — |
| NOMINAL_IMPACT_EPOCH | 2016-11-02T05:03:42.000000 | 2016-11-02T04:13:13.000 |
| IMPACT_WINDOW_START | 2016-11-02T03:03:42.000000 | 2016-11-02T04:11:03.000 |
| IMPACT_WINDOW_END | 2016-11-02T07:03:42.000000 | 2016-11-02T04:14:42.000 |
| IMPACT_REF_FRAME | WGS84 | WGS84 |
| NOMINAL_IMPACT_LON | 113.21 | -85.1700 |
| NOMINAL_IMPACT_LAT | 61.73 | -27.1000 |
| NOMINAL_IMPACT_ALT | 8.22 | 0.0000 |
| IMPACT_1_CONFIDENCE | 10.0000000000000 | 66.6667 |
| IMPACT_1_START_LON | 90.8728300000000 | -85.9810 |
| IMPACT_1_START_LAT | 44.5794400000000 | -25.0910 |
| IMPACT_1_STOP_LON | 173.207370000000 | -84.0710 |
| IMPACT_1_STOP_LAT | 68.6096400000000 | -29.7080 |
| IMPACT_1_CROSS_TRACK | 2.00000000000000 | 0.7510 |
| IMPACT_2_CONFIDENCE | 20.0000000000000 | 95.0000 |
| IMPACT_2_START_LON | 79.6142500000000 | -86.8830 |
| IMPACT_2_START_LAT | 23.0323900000000 | -22.7720 |
| IMPACT_2_STOP_LON | -146.303880000000 | -83.0500 |
| IMPACT_2_STOP_LAT | 54.4247800000000 | -32.0050 |
| IMPACT_2_CROSS_TRACK | 5.00000000000000 | 1.5020 |
| IMPACT_3_CONFIDENCE | 30.0000000000000 | 99.7300 |
| IMPACT_3_START_LON | 64.0955300000000 | -87.7540 |
| IMPACT_3_START_LAT | -22.4338300000000 | -20.4470 |
| IMPACT_3_STOP_LON | -121.898660000000 | -81.9780 |
| IMPACT_3_STOP_LAT | 12.4541700000000 | -34.2910 |
| IMPACT_3_CROSS_TRACK | 10.0000000000000 | 2.2520 |

The compasion between the DLR/GSOC predicted impact location and location uncertainty (red) and ESA/ESOC predicted location and location uncertainty (blue) can be seen in the figure below.

RDM keyword distribution between test cases

The following table shows the distribution of mandatory and optional RDM keywords between the five test cases. An 'X' in the column of a test number means that keyword will be covered in the test. The color coding is as follows:

- Blue – mandatory keywords, will be covered in all test cases;

- Red – optional keywords, covered only in test #1 (KVN-XML conversion);

- Orange – TBD; and

- Green – optional keywords, covered in at least one of tests #2 to #5.

|  | Feature | Keyword | Status | #1 | #2 | #3 | #4 | #5 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | RDM Header | N/A | M |  |  |  |  |  |
|  | RDM version | CCSDS_RDM_VERS | M | X | X | X | X | X |
|  | Comment | COMMENT | O | X |  |  |  |  |
|  | Message creation date/time | CREATION_DATE | M | X | X | X | X | X |
|  | Message originator | ORIGINATOR | M | X | X | X | X | X |
|  | Unique message identifier | MESSAGE_ID | M | X | X | X | X | X |
|  | RDM Metadata | N/A | M |  |  |  |  |  |
|  | Comment | COMMENT | O | X |  |  |  |  |
|  | General information about the re-entering object | N/A | M |  |  |  |  |  |
|  | Spacecraft name | OBJECT_NAME | M | X | X | X | X | X |
|  | Spacecraft international designator | INTERNATIONAL_DESIGNATOR | M | X | X | X | X | X |
|  | Object catalogue used | CATALOG_NAME | O | X | X | X | X | X |
|  | Spacecraft ID in the catalogue | OBJECT_DESIGNATOR | O | X | X | X | X | X |
|  | Spacecraft type | OBJECT_TYPE | O | X | X | X | X | X |
|  | Spacecraft owner | OBJECT_OWNER | O | X |  |  |  |  |
|  | Spacecraft operator | OBJECT_OPERATOR | O | X |  |  |  |  |
|  | Controlled re-entry | CONTROLLED_REENTRY | M | X | X | X | X | X |
|  | Celestial body orbited by the object | CENTER_NAME | M | X | X | X | X | X |
|  | Time system user for the data in the metadata and data sections | TIME_SYSTEM | M | X | X | X | X | X |
|  | Reference epoch to which orbit lifetime is computed | EPOCH_TZERO | M | X | X | X | X | X |
|  | Information about any provided orbit data for the object/spacecraft | N/A | O |  |  |  |  |  |
|  | Reference frame | REF_FRAME | O | X | X | X |  |  |
|  | Reference frame epoch | REF_FRAME_EPOCH | O | X |  |  |  |  |
|  | External ephemeris file identifier | EPHEMERIS_NAME | O | X |  |  |  |  |
|  | Information about the orbit propagator used for re-entry prediction and orbit determination | N/A | O |  |  |  |  |  |
|  | gravity model used | GRAVITY_MODEL | O | X | X | X | X | X |
|  | atmospheric model used | ATMOSPHERIC_MODEL | O | X | X | X | X | X |
|  | method used to estimate the solar flux indices for the atmospheric model | SOLAR_FLUX_PREDICTION | O | X | X | X | X | X |
|  | n-body perturbations considered | N_BODY_PERTURBATIONS | O | X | X | X | X | X |
|  | solar rad pressure | SOLAR_RAD_PRESSURE | O | X | X | X | X | X |
|  | earth tides | EARTH_TIDES | O | X | X | X | X | X |
|  | any thrust from the spacecraft | INTRACK_THRUST | O | X |  |  |  |  |
|  | the source of the object drag parameters | DRAG_PARAMETERS_SOURCE | O | X |  |  |  |  |
|  | the altitude at which the drag parameters apply | DRAG_PARAMETERS_ALTITUDE | O | X |  |  |  |  |
|  | the method used to estimate the uncertainty in the reentry date | REENTRY_UNCERTAINTY_METHOD | O | X |  |  |  |  |
|  | any accounting for break-up and demise | REENTRY_DISINTEGRATION | O | X | X | X | X | X |
|  | method used to determine the uncertainty in the ground impact location | IMPACT_UNCERTAINTY_METHOD | O | X |  |  | X | X |
|  | Previous and next related RDM | N/A | O |  |  |  |  |  |
|  | Identifier of the previous RDM | PREVIOUS_MESSAGE_ID | O | X |  |  |  |  |
|  | Epoch of the previous RDM (predicted) | PREVIOUS_MESSAGE_EPOCH | O | X |  |  |  |  |
|  | Time at which the next RDM will be issued (predicted) | NEXT_MESSAGE_EPOCH | O | X |  |  |  |  |
|  | RDM Data | N/A | M |  |  |  |  |  |
|  | Atmospheric re-entry information | N/A | M |  |  |  |  |  |
|  | Comment | COMMENT | O | X |  |  |  |  |
|  | Remaining orbit lifetime | ORBIT_LIFETIME | M | X | X | X | X | X |
|  | Defined re-entry altitude | REENTRY_ALTITUDE | M | X | X | X | X | X |
|  | Orbit lifetime window | ORBIT_LIFETIME_WINDOW_START | O | X | X |  |  |  |
|  |  | ORBIT_LIFETIME_WINDOW_END | O | X | X |  |  |  |
|  | Predicted re-entry epoch | NOMINAL_REENTRY_EPOCH | O | X |  | X | X | X |
|  | Re-entry window | REENTRY_WINDOW_START | O | X |  | X | X | X |
|  |  | REENTRY_WINDOW_END | O | X |  | X | X | X |
|  | Orbit lifetime confidence | ORBIT_LIFETIME_CONFIDENCE | O | X |  |  |  |  |
|  | Ground impact information | N/A | O | X |  |  |  |  |
|  | Comment | COMMENT | O | X |  |  |  |  |
|  | Probability any re-entry fragments reach the Earth surface | PROBABILITY_OF_IMPACT | O | X |  |  |  |  |
|  | Probability all re-entry fragments suffer total demise | PROBABILITY_OF_BURN_UP | O | X |  |  |  |  |
|  | Probability fragments are generated during re-entry | PROBABILITY_OF_BREAK_UP | O | X |  |  |  |  |
|  | Land impact probability | PROBABILITY_OF_LAND_IMPACT | O | X |  |  |  |  |
|  | Probabilities of casualties occurring due to the re-entry | PROBABILITY_OF_CASUALTY | O | X |  |  |  |  |
|  | Predicted (ground) impact epoch | NOMINAL_IMPACT_EPOCH | O | X |  |  | X | X |
|  | Predicted (ground) impact window | IMPACT_WINDOW_START | O | X |  |  | X | X |
|  |  | IMPACT_WINDOW_END | O | X |  |  | X | X |
|  | Reference frame of (ground) impact location | IMPACT_REF_FRAME | O | X |  |  | X | X |
|  | Impact location | NOMINAL_IMPACT_LON | O | X |  |  | X | X |
|  |  | NOMINAL_IMPACT_LAT | O | X |  |  | X | X |
|  |  | NOMINAL_IMPACT_ALT | O | X |  |  | X |  |
|  | Impact dispersion | IMPACT_1_CONFIDENCE | O | X |  |  |  | X |
|  |  | IMPACT_1_START_LON | O | X |  |  |  | X |
|  |  | IMPACT_1_START_LAT | O | X |  |  |  | X |
|  |  | IMPACT_1_STOP_LON | O | X |  |  |  | X |
|  |  | IMPACT_1_STOP_LAT | O | X |  |  |  | X |
|  |  | IMPACT_1_CROSS_TRACK | O | X |  |  |  | X |
|  |  | IMPACT_2_CONFIDENCE | O | X |  |  |  | X |
|  |  | IMPACT_2_START_LON | O | X |  |  |  | X |
|  |  | IMPACT_2_START_LAT | O | X |  |  |  | X |
|  |  | IMPACT_2_STOP_LON | O | X |  |  |  | X |
|  |  | IMPACT_2_STOP_LAT | O | X |  |  |  | X |
|  |  | IMPACT_2_CROSS_TRACK | O | X |  |  |  | X |
|  |  | IMPACT_3_CONFIDENCE | O | X |  |  |  | X |
|  |  | IMPACT_3_START_LON | O | X |  |  |  | X |
|  |  | IMPACT_3_START_LAT | O | X |  |  |  | X |
|  |  | IMPACT_3_STOP_LON | O | X |  |  |  | X |
|  |  | IMPACT_3_STOP_LAT | O | X |  |  |  | X |
|  |  | IMPACT_3_CROSS_TRACK | O | X |  |  |  | X |
|  | Spacecraft state vector section | N/A | O |  |  |  |  |  |
|  | Comment | COMMENT | O | X |  |  |  |  |
|  | State vector epoch | EPOCH | O | X | X | X | X | X |
|  | Position and velocity vectors | X | O | X | X | X | X | X |
|  |  | Y | O | X | X | X | X | X |
|  |  | Z | O | X | X | X | X | X |
|  |  | X_DOT | O | X | X | X | X | X |
|  |  | Y_DOT | O | X | X | X | X | X |
|  |  | Z_DOT | O | X | X | X | X | X |
|  | Spacecraft state vector covariance information | N/A | O |  |  |  |  |  |
|  | Comment | COMMENT | O | X |  |  |  |  |
|  | Covariance reference frame | COV_REF_FRAME | O | X | ? | ? |  |  |
|  | 6x6 position/velocity covariance matrix elements | CX_X | O | X |  | X | X | X |
|  |  | CY_X | O | X |  | X | X | X |
|  |  | CY_Y | O | X |  | X | X | X |
|  |  | CZ_X | O | X |  | X | X | X |
|  |  | CZ_Y | O | X |  | X | X | X |
|  |  | CZ_Z | O | X |  | X | X | X |
|  |  | CX_DOT_X | O | X |  | X | X | X |
|  |  | CX_DOT_Y | O | X |  | X | X | X |
|  |  | CX_DOT_Z | O | X |  | X | X | X |
|  |  | CX_DOT_X_DOT | O | X |  | X | X | X |
|  |  | CY_DOT_X | O | X |  | X | X | X |
|  |  | CY_DOT_Y | O | X |  | X | X | X |
|  |  | CY_DOT_Z | O | X |  | X | X | X |
|  |  | CY_DOT_X_DOT | O | X |  | X | X | X |
|  |  | CY_DOT_Y_DOT | O | X |  | X | X | X |
|  |  | CZ_DOT_X | O | X |  | X | X | X |
|  |  | CZ_DOT_Y | O | X |  | X | X | X |
|  |  | CZ_DOT_Z | O | X |  | X | X | X |
|  |  | CZ_DOT_X_DOT | O | X |  | X | X | X |
|  |  | CZ_DOT_Y_DOT | O | X |  | X | X | X |
|  |  | CZ_DOT_Z_DOT | O | X |  | X | X | X |
|  | Spacecraft properties | N/A | O |  |  |  |  |  |
|  | Comments | COMMENT | O | X | X |  |  |  |
|  | Total (wet) mass | WET_MASS | O | X | X | X | X | X |
|  | Dry mass | DRY_MASS | O | X |  |  |  |  |
|  | List of hazardous substances on board | HAZARDOUS_SUBSTANCES | O | X | X | X | X | X |
|  | Solar radiation area | SOLAR_RAD_AREA | O | X |  |  |  |  |
|  | Solar radiation coefficient | SOLAR_RAD_COEFF | O | X |  |  |  |  |
|  | Drag area | DRAG_AREA | O | X | X | X | X | X |
|  | Coefficient of drag | DRAG_COEFF | O | X | X | X | X | X |
|  | Radar Cross-Section | RCS | O | X | X | X | X | X |
|  | Ballistic coefficient | BALLISTIC_COEFF | O | X | X | X | X | X |
|  | Object’s acceleration used in OD and propagation | THRUST_ACCELERATION | O | X |  |  |  |  |
|  | Orbit determination information | N/A | O |  |  |  |  |  |
|  | Comment | COMMENT | O | X |  |  |  |  |
|  | Interval during which the last accepted observation occurred | TIME_LASTOB_START | O | X |  |  |  |  |
|  |  | TIME_LASTOB_END | O | X |  |  |  |  |
|  | Recommend timespan for OD and actual timespan used | RECOMMENDED_OD_SPAN | O | X |  |  |  |  |
|  |  | ACTUAL_OD_SPAN | O | X |  |  |  |  |
|  | Total number of observations available and used | OBS_AVAILABLE | O | X |  |  |  |  |
|  |  | OBS_USED | O | X |  |  |  |  |
|  | Total number of sensor tracks available and used | TRACKS_AVAILABLE | O | X |  |  |  |  |
|  |  | TRACKS_USED | O | X |  |  |  |  |
|  | Percentage of residuals accepted in OD | RESIDUALS_ACCEPTED | O | X |  |  |  |  |
|  | Weighted RMS of the OD residuals | WEIGHTED_RMS | O | X |  |  |  |  |
|  | User defined parameters | USER_DEFINED_x Any supported user defined parameters should be listed here. | O | X |  |  |  |  |

Sample RDM Prototype test data sheet

| 1 | Test Case Number: |  |
| --- | --- | --- |
| 2 | Report Date: |  |
| 3 | Program Under Test: | Re-entry Data Message V1 (RDM) Prototype |
| 4 | Agencies Participating in this Test Case: | ESA/ESOC DLR/GSOC |
| 5 | Agency Responsible for Prototype: | RDM Generation: RDM Processing: |
| 6 | Prototype Version # (if applicable): | RDM Generation: RDM Processing: |
| 7 | Test Engineer: | RDM Generation: RDM Processing: |
| 8 | Spacecraft: | AVUM R/B (2012-006 K) |
| 9 | Re-entry keywords tested: |  |
| 10 | Values for the keywords of interest: |  |
| 11 | Variances from Expected Results: |  |
| 12 | Results (Pass, Partial Pass, Fail): |  |
| 13 | Comments: |  |

Acronyms

| CCSDS | Consultative Committee for Space Data Systems |
| --- | --- |
| CESG | CCSDS Engineering Steering Group |
| CMC | CCSDS Management Council |
| CWE | Common Working Environment |
| DLR | Deutsches Zentrum für Luft und Raumfahrt |
| ESA | European Space Agency |
| ESOC | European Space Operations Centre |
| GSOC | German Space Operations Centre |
| KVN | Keyword Value Notation |
| NASA | National Aeronautics and Space Administration |
| RID | Review Item Discrepancy |
| RDM | Re-entry Data Message |
| XML | eXtensible Markup Language |

OPMs used as re-entry simulation input

The following OPMs were prepared by ESA/ESOC as input for both ESA/ESOC and DLR/GSOC re-entry prediction simulations.

CCSDS_OPM_VERS = 2.0 COMMENT Input OPM for Test Case #2 - long term re-entry prediction CREATION_DATE = 2018-11-30T07:39:00 ORIGINATOR = ESA/SDO OBJECT_NAME = AVUM R/B OBJECT_ID = 2012-006K CENTER_NAME = EARTH REF_FRAME = EME2000 TIME_SYSTEM = UTC COMMENT obtained from the latest TLE EPOCH = 2015-11-01T20:05:40 X = -5915.235752489283 Y = 2990.050036619588 Z = -0.004156299484754752 X_DOT = -1.2274837732545412 Y_DOT = -2.475304162660883 Z_DOT = 7.386758781498862 MASS = 960.0 SOLAR_RAD_AREA = 1.000 SOLAR_RAD_COEFF = 1.200 DRAG_AREA = 3.9545 DRAG_COEFF = 2.4108 COMMENT made-up covariance for the TLE COV_REF_FRAME = RTN CX_X = 0.0109 CY_X = 0.00262 CY_Y = 0.309 CZ_X = 0.0000236 CZ_Y = 0.0047 CZ_Z = 0.0192 CX_DOT_X = -0.00000299 CX_DOT_Y = -0.0000114 CX_DOT_Z = -0.000000401 CX_DOT_X_DOT = 0.000000312 CY_DOT_X = -0.0003 CY_DOT_Y = -0.00000158 CY_DOT_Z = -0.000000337 CY_DOT_X_DOT = 0.00000000185 CY_DOT_Y_DOT = 0.0000000122 CZ_DOT_X = -0.00000722 CZ_DOT_Y = -0.000000151 CZ_DOT_Z = 0.00000122 CZ_DOT_X_DOT = 0.00000000022 CZ_DOT_Y_DOT = -0.00000000169 CZ_DOT_Z_DOT = 0.0000000218

Figure D-1 Input OPM for Test Case #2 - long term re-entry prediction

CCSDS_OPM_VERS = 2.0 COMMENT Input OPM for Test Case #3 - short term re-entry prediction CREATION_DATE = 2018-11-30T07:39:00 ORIGINATOR = ESA/SDO OBJECT_NAME = AVUM R/B OBJECT_ID = 2012-006K CENTER_NAME = EARTH REF_FRAME = EME2000 TIME_SYSTEM = UTC COMMENT OD from 2 TIRA passes; EPOCH is OD epoch EPOCH = 2016-10-28T11:41:00 X = -2095.410018130742 Y = -3040.7013729381097 Z = 5458.838153754293 X_DOT = 6.871413465939689 Y_DOT = 1.3852134950239 Z_DOT = 3.360230383458709 COMMENT CD fitting with FOCUS2 MASS = 960.0 SOLAR_RAD_AREA = 1.000 SOLAR_RAD_COEFF = 1.200 DRAG_AREA = 3.9545 DRAG_COEFF = 2.3588 COMMENT covariance from the OD COV_REF_FRAME = RTN CX_X = 0.00834 CY_X = -0.00271 CY_Y = 0.00189 CZ_X = 0.000735 CZ_Y = 0.00153 CZ_Z = 0.00327 CX_DOT_X = 0.0000586 CX_DOT_Y = -0.0000102 CX_DOT_Z = 0.00000501 CX_DOT_X_DOT = 0.000000442 CY_DOT_X = -0.0000177 CY_DOT_Y = 0.0000029 CY_DOT_Z = 0.0000113 CY_DOT_X_DOT = -0.0000000725 CY_DOT_Y_DOT = 0.0000000126 CZ_DOT_X = 0.00000664 CZ_DOT_Y = -0.00000162 CZ_DOT_Z = 0.0000235 CZ_DOT_X_DOT = 0.0000000553 CZ_DOT_Y_DOT = -0.0000000115 CZ_DOT_Z_DOT = 0.000000172

Figure D-2 Input OPM for Test Case #3 - short term re-entry prediction

CCSDS_OPM_VERS = 2.0 COMMENT Input OPM for Test Case #4 - short term re-entry prediction with COMMENT ground impact location CREATION_DATE = 2018-11-30T07:39:00 ORIGINATOR = ESA/SDO OBJECT_NAME = AVUM R/B OBJECT_ID = 2012-006K CENTER_NAME = EARTH REF_FRAME = EME2000 TIME_SYSTEM = UTC COMMENT OD from 2 TIRA passes; EPOCH is OD epoch EPOCH = 2016-10-28T11:41:00 X = -2095.410018130742 Y = -3040.7013729381097 Z = 5458.838153754293 X_DOT = 6.871413465939689 Y_DOT = 1.3852134950239 Z_DOT = 3.360230383458709 COMMENT CD fitting with FOCUS2 MASS = 960.0 SOLAR_RAD_AREA = 1.000 SOLAR_RAD_COEFF = 1.200 DRAG_AREA = 3.9545 DRAG_COEFF = 2.3588 COMMENT covariance from the OD COV_REF_FRAME = RTN CX_X = 0.00834 CY_X = -0.00271 CY_Y = 0.00189 CZ_X = 0.000735 CZ_Y = 0.00153 CZ_Z = 0.00327 CX_DOT_X = 0.0000586 CX_DOT_Y = -0.0000102 CX_DOT_Z = 0.00000501 CX_DOT_X_DOT = 0.000000442 CY_DOT_X = -0.0000177 CY_DOT_Y = 0.0000029 CY_DOT_Z = 0.0000113 CY_DOT_X_DOT = -0.0000000725 CY_DOT_Y_DOT = 0.0000000126 CZ_DOT_X = 0.00000664 CZ_DOT_Y = -0.00000162 CZ_DOT_Z = 0.0000235 CZ_DOT_X_DOT = 0.0000000553 CZ_DOT_Y_DOT = -0.0000000115 CZ_DOT_Z_DOT = 0.000000172

Figure D-3 Input OPM for Test Case #4 - short term re-entry prediction with ground impact location

CCSDS_OPM_VERS = 2.0 COMMENT Input OPM for Test Case #5 - very short term re-entry prediction with COMMENT ground impact location and ground impact location uncertainty CREATION_DATE = 2018-11-30T07:39:00 ORIGINATOR = ESA/SDO OBJECT_NAME = AVUM R/B OBJECT_ID = 2012-006K CENTER_NAME = EARTH REF_FRAME = EME2000 TIME_SYSTEM = UTC COMMENT from latest TLE EPOCH = 2016-11-01T19:03:00 X = 4388.709204989278 Y = -1149.1211887059094 Z = 4686.185669397925 X_DOT = 5.692732085207659 Y_DOT = 2.594935544817214 Z_DOT = -4.69455708111904 COMMENT CD fitting with FOCUS2 MASS = 960.0 SOLAR_RAD_AREA = 1.000 SOLAR_RAD_COEFF = 1.200 DRAG_AREA = 3.9545 DRAG_COEFF = 2.5388

Figure D-4 Input OPM for Test Case #5 - very short term re-entry prediction with ground impact location uncertainty

Re-entry data messages produced during prototyping

The following XML RDMs were produced by the ESA/ESOC prototype.

<?xml version="1.0" encoding="utf-8"?> <ndm:rdm xmlns:ndm="urn:ccsds:recommendation:navigation:schema:ndmxml" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation="../xmlSchema/ndmxml-1.0-rdm-1.0-oneFile.xsd" id="CCSDS_RDM_VERS" version="0.3"> <header> <COMMENT>Test-case#2: long term prediction</COMMENT> <CREATION_DATE>2015-11-02T11:24:20.000000</CREATION_DATE> <ORIGINATOR>ESA-SDO</ORIGINATOR> <MESSAGE_ID>2012-006K_20181108112420_ESA-SDO_5343</MESSAGE_ID> </header> <body> <segment> <metadata> <OBJECT_NAME>AVUM (Vega)</OBJECT_NAME> <INTERNATIONAL_DESIGNATOR>2012-006K</INTERNATIONAL_DESIGNATOR> <CATALOG_NAME>SATCAT</CATALOG_NAME> <OBJECT_DESIGNATOR>38086</OBJECT_DESIGNATOR> <OBJECT_TYPE>ROCKET BODY</OBJECT_TYPE> <CONTROLLED_REENTRY>NO</CONTROLLED_REENTRY> <CENTER_NAME>EARTH</CENTER_NAME> <TIME_SYSTEM>UTC</TIME_SYSTEM> <EPOCH_TZERO>2015-11-01T20:05:40.020000</EPOCH_TZERO> <REF_FRAME>EME2000</REF_FRAME> <GRAVITY_MODEL>GEM-T1: 8D 8O</GRAVITY_MODEL> <ATMOSPHERIC_MODEL>DTM-13</ATMOSPHERIC_MODEL> <SOLAR_FLUX_PREDICTION>ESA SOLMAG</SOLAR_FLUX_PREDICTION> <N_BODY_PERTURBATIONS>MOON, SUN</N_BODY_PERTURBATIONS> <SOLAR_RAD_PRESSURE>CYLINDRICAL SHADOW</SOLAR_RAD_PRESSURE> <EARTH_TIDES>NO</EARTH_TIDES> <INTRACK_THRUST>NO</INTRACK_THRUST> <DRAG_PARAMETERS_SOURCE>CD FITTING WITH FOCUS2</DRAG_PARAMETERS_SOURCE> <DRAG_PARAMETERS_ALTITUDE units="km">244.72</DRAG_PARAMETERS_ALTITUDE> <REENTRY_UNCERTAINTY_METHOD>EMPIRICAL</REENTRY_UNCERTAINTY_METHOD> <REENTRY_DISINTEGRATION>NONE</REENTRY_DISINTEGRATION> <IMPACT_UNCERTAINTY_METHOD>EMPIRICAL</IMPACT_UNCERTAINTY_METHOD> </metadata> <data> <atmosphericReentryParameters> <COMMENT>Prediction 1 year before re-entry</COMMENT> <ORBIT_LIFETIME units="d">366.677083333333</ORBIT_LIFETIME> <REENTRY_ALTITUDE units="km">78.417</REENTRY_ALTITUDE> <ORBIT_LIFETIME_WINDOW_START units="d">293.341666666667</ORBIT_LIFETIME_WINDOW_START> <ORBIT_LIFETIME_WINDOW_END units="d">440.0125</ORBIT_LIFETIME_WINDOW_END> <NOMINAL_REENTRY_EPOCH>2016-11-02T12:15:36.000000</NOMINAL_REENTRY_EPOCH> <REENTRY_WINDOW_START>2016-08-21T04:19:01.000000</REENTRY_WINDOW_START> <REENTRY_WINDOW_END>2017-01-14T20:25:01.000000</REENTRY_WINDOW_END> <ORBIT_LIFETIME_CONFIDENCE units="%">20.0</ORBIT_LIFETIME_CONFIDENCE> </atmosphericReentryParameters> <stateVector> <COMMENT>epoch of latest TLE (same as epoch_tzero)</COMMENT> <EPOCH>2015-11-01T20:05:40.020000</EPOCH> <X units="km">-5915.23575248928</X> <Y units="km">2990.05003661959</Y> <Z units="km">-0.00415629948475475</Z> <X_DOT units="km/s">-1.22748377325454</X_DOT> <Y_DOT units="km/s">-2.47530416266088</Y_DOT> <Z_DOT units="km/s">7.38675878149886</Z_DOT> </stateVector> <covarianceMatrix> <COMMENT>This is an invented covariance for a TLE</COMMENT> <COV_REF_FRAME>RTN</COV_REF_FRAME> <CX_X units="km**2">0.0109</CX_X> <CY_X units="km**2">0.00262</CY_X> <CY_Y units="km**2">0.309</CY_Y> <CZ_X units="km**2">2.36e-05</CZ_X> <CZ_Y units="km**2">0.0047</CZ_Y> <CZ_Z units="km**2">0.0192</CZ_Z> <CX_DOT_X units="km**2/s">-2.99e-06</CX_DOT_X> <CX_DOT_Y units="km**2/s">-1.14e-05</CX_DOT_Y> <CX_DOT_Z units="km**2/s">-4.01e-07</CX_DOT_Z> <CX_DOT_X_DOT units="km**2/s**2">3.12e-07</CX_DOT_X_DOT> <CY_DOT_X units="km**2/s">-0.0003</CY_DOT_X> <CY_DOT_Y units="km**2/s">-1.58e-06</CY_DOT_Y> <CY_DOT_Z units="km**2/s">-3.37e-07</CY_DOT_Z> <CY_DOT_X_DOT units="km**2/s**2">1.85e-09</CY_DOT_X_DOT> <CY_DOT_Y_DOT units="km**2/s**2">1.22e-08</CY_DOT_Y_DOT> <CZ_DOT_X units="km**2/s">-7.22e-06</CZ_DOT_X> <CZ_DOT_Y units="km**2/s">-1.51e-07</CZ_DOT_Y> <CZ_DOT_Z units="km**2/s">1.22e-06</CZ_DOT_Z> <CZ_DOT_X_DOT units="km**2/s**2">2.2e-10</CZ_DOT_X_DOT> <CZ_DOT_Y_DOT units="km**2/s**2">-1.69e-09</CZ_DOT_Y_DOT> <CZ_DOT_Z_DOT units="km**2/s**2">2.18e-08</CZ_DOT_Z_DOT> </covarianceMatrix> <spacecraftParameters> <COMMENT>Cr is fixed, Cd includes all effects</COMMENT> <WET_MASS units="kg">960.0</WET_MASS> <DRY_MASS units="kg">410.0</DRY_MASS> <SOLAR_RAD_AREA units="m**2">1.0</SOLAR_RAD_AREA> <SOLAR_RAD_COEFF>1.2</SOLAR_RAD_COEFF> <DRAG_AREA units="m**2">3.9545</DRAG_AREA> <DRAG_COEFF>2.4108</DRAG_COEFF> <BALLISTIC_COEFF units="kg/m**2">0.009931</BALLISTIC_COEFF> </spacecraftParameters> </data> </segment> </body> </ndm:rdm>

Figure E-1 ESA/ESOC XML RDM for Test Case #2

<?xml version="1.0" encoding="utf-8"?> <ndm:rdm xmlns:ndm="urn:ccsds:recommendation:navigation:schema:ndmxml" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation="../xmlSchema/ndmxml-1.0-rdm-1.0-oneFile.xsd" id="CCSDS_RDM_VERS" version="0.3"> <header> <COMMENT>Test-case#3: short term prediction</COMMENT> <CREATION_DATE>2016-10-28T14:22:56.000000</CREATION_DATE> <ORIGINATOR>ESA-SDO</ORIGINATOR> <MESSAGE_ID>2012-006K_20181108142256_ESA-SDO_9F5B</MESSAGE_ID> </header> <body> <segment> <metadata> <OBJECT_NAME>AVUM (Vega)</OBJECT_NAME> <INTERNATIONAL_DESIGNATOR>2012-006K</INTERNATIONAL_DESIGNATOR> <CATALOG_NAME>SATCAT</CATALOG_NAME> <OBJECT_DESIGNATOR>38086</OBJECT_DESIGNATOR> <OBJECT_TYPE>ROCKET BODY</OBJECT_TYPE> <CONTROLLED_REENTRY>NO</CONTROLLED_REENTRY> <CENTER_NAME>EARTH</CENTER_NAME> <TIME_SYSTEM>UTC</TIME_SYSTEM> <EPOCH_TZERO>2016-10-28T11:41:00.000384</EPOCH_TZERO> <REF_FRAME>EME2000</REF_FRAME> <GRAVITY_MODEL>GEM-T1: 8D 8O</GRAVITY_MODEL> <ATMOSPHERIC_MODEL>DTM-13</ATMOSPHERIC_MODEL> <SOLAR_FLUX_PREDICTION>ESA SOLMAG</SOLAR_FLUX_PREDICTION> <N_BODY_PERTURBATIONS>MOON, SUN</N_BODY_PERTURBATIONS> <SOLAR_RAD_PRESSURE>CYLINDRICAL SHADOW</SOLAR_RAD_PRESSURE> <EARTH_TIDES>NO</EARTH_TIDES> <INTRACK_THRUST>NO</INTRACK_THRUST> <DRAG_PARAMETERS_SOURCE>CD FITTING WITH FOCUS2</DRAG_PARAMETERS_SOURCE> <DRAG_PARAMETERS_ALTITUDE units="km">179.49</DRAG_PARAMETERS_ALTITUDE> <REENTRY_UNCERTAINTY_METHOD>EMPIRICAL</REENTRY_UNCERTAINTY_METHOD> <REENTRY_DISINTEGRATION>NONE</REENTRY_DISINTEGRATION> <IMPACT_UNCERTAINTY_METHOD>EMPIRICAL</IMPACT_UNCERTAINTY_METHOD> <PREVIOUS_MESSAGE_ID></PREVIOUS_MESSAGE_ID> </metadata> <data> <atmosphericReentryParameters> <COMMENT>Prediction based on 2 TIRA passes as last orbit state, 5 days before re-entry</COMMENT> <ORBIT_LIFETIME units="d">5.04375</ORBIT_LIFETIME> <REENTRY_ALTITUDE units="km">76.88</REENTRY_ALTITUDE> <ORBIT_LIFETIME_WINDOW_START units="d">4.035</ORBIT_LIFETIME_WINDOW_START> <ORBIT_LIFETIME_WINDOW_END units="d">6.0525</ORBIT_LIFETIME_WINDOW_END> <NOMINAL_REENTRY_EPOCH>2016-11-02T12:38:07.000000</NOMINAL_REENTRY_EPOCH> <REENTRY_WINDOW_START>2016-11-01T12:31:31.000000</REENTRY_WINDOW_START> <REENTRY_WINDOW_END>2016-11-03T12:56:43.000000</REENTRY_WINDOW_END> <ORBIT_LIFETIME_CONFIDENCE units="%">20.0</ORBIT_LIFETIME_CONFIDENCE> </atmosphericReentryParameters> <stateVector> <COMMENT>epoch of OD from 2 TIRA tracks</COMMENT> <EPOCH>2016-10-28T11:41:00.000384</EPOCH> <X units="km">-2095.41001813074</X> <Y units="km">-3040.70137293811</Y> <Z units="km">5458.83815375429</Z> <X_DOT units="km/s">6.87141346593969</X_DOT> <Y_DOT units="km/s">1.3852134950239</Y_DOT> <Z_DOT units="km/s">3.36023038345871</Z_DOT> </stateVector> <covarianceMatrix> <COMMENT>This is the covariance from the OD</COMMENT> <COV_REF_FRAME>RTN</COV_REF_FRAME> <CX_X units="km**2">0.00834</CX_X> <CY_X units="km**2">-0.00271</CY_X> <CY_Y units="km**2">0.00189</CY_Y> <CZ_X units="km**2">0.000735</CZ_X> <CZ_Y units="km**2">0.00153</CZ_Y> <CZ_Z units="km**2">0.00327</CZ_Z> <CX_DOT_X units="km**2/s">5.86e-05</CX_DOT_X> <CX_DOT_Y units="km**2/s">-1.02e-05</CX_DOT_Y> <CX_DOT_Z units="km**2/s">5.01e-06</CX_DOT_Z> <CX_DOT_X_DOT units="km**2/s**2">4.42e-07</CX_DOT_X_DOT> <CY_DOT_X units="km**2/s">-1.77e-05</CY_DOT_X> <CY_DOT_Y units="km**2/s">2.9e-06</CY_DOT_Y> <CY_DOT_Z units="km**2/s">1.13e-05</CY_DOT_Z> <CY_DOT_X_DOT units="km**2/s**2">-7.25e-08</CY_DOT_X_DOT> <CY_DOT_Y_DOT units="km**2/s**2">1.26e-08</CY_DOT_Y_DOT> <CZ_DOT_X units="km**2/s">6.64e-06</CZ_DOT_X> <CZ_DOT_Y units="km**2/s">-1.62e-06</CZ_DOT_Y> <CZ_DOT_Z units="km**2/s">2.35e-05</CZ_DOT_Z> <CZ_DOT_X_DOT units="km**2/s**2">5.53e-08</CZ_DOT_X_DOT> <CZ_DOT_Y_DOT units="km**2/s**2">-1.15e-08</CZ_DOT_Y_DOT> <CZ_DOT_Z_DOT units="km**2/s**2">1.72e-07</CZ_DOT_Z_DOT> </covarianceMatrix> <spacecraftParameters> <COMMENT>Cr is fixed, Cd includes all effects</COMMENT> <WET_MASS units="kg">960.0</WET_MASS> <DRY_MASS units="kg">410.0</DRY_MASS> <SOLAR_RAD_AREA units="m**2">1.0</SOLAR_RAD_AREA> <SOLAR_RAD_COEFF>1.2</SOLAR_RAD_COEFF> <DRAG_AREA units="m**2">3.9545</DRAG_AREA> <DRAG_COEFF>2.3588</DRAG_COEFF> <BALLISTIC_COEFF units="kg/m**2">0.009717</BALLISTIC_COEFF> </spacecraftParameters> <odParameters> <COMMENT>two TIRA tracks</COMMENT> <TIME_LASTOB_START>2016-10-27T11:54:20.000000</TIME_LASTOB_START> <TIME_LASTOB_END>2016-10-28T11:41:00.000000</TIME_LASTOB_END> <RECOMMENDED_OD_SPAN units="d">2.0</RECOMMENDED_OD_SPAN> <ACTUAL_OD_SPAN units="d">1.0</ACTUAL_OD_SPAN> <OBS_AVAILABLE>655</OBS_AVAILABLE> <OBS_USED>655</OBS_USED> <TRACKS_AVAILABLE>2</TRACKS_AVAILABLE> <TRACKS_USED>2</TRACKS_USED> <RESIDUALS_ACCEPTED units="%">100.0</RESIDUALS_ACCEPTED> <WEIGHTED_RMS>0.0097</WEIGHTED_RMS> </odParameters> </data> </segment> </body> </ndm:rdm>

Figure E-2 ESA/ESOC XML RDM for Test Case #3

<?xml version="1.0" encoding="utf-8"?> <ndm:rdm xmlns:ndm="urn:ccsds:recommendation:navigation:schema:ndmxml" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation="../xmlSchema/ndmxml-1.0-rdm-1.0-oneFile.xsd" id="CCSDS_RDM_VERS" version="0.3"> <header> <COMMENT>Test-case#4: short term prediction with ground impact location</COMMENT> <CREATION_DATE>2016-10-28T15:22:56.000000</CREATION_DATE> <ORIGINATOR>ESA-SDO</ORIGINATOR> <MESSAGE_ID>2012-006K_20181108152256_ESA-SDO_2345</MESSAGE_ID> </header> <body> <segment> <metadata> <OBJECT_NAME>AVUM (Vega)</OBJECT_NAME> <INTERNATIONAL_DESIGNATOR>2012-006K</INTERNATIONAL_DESIGNATOR> <CATALOG_NAME>SATCAT</CATALOG_NAME> <OBJECT_DESIGNATOR>38086</OBJECT_DESIGNATOR> <OBJECT_TYPE>ROCKET BODY</OBJECT_TYPE> <CONTROLLED_REENTRY>NO</CONTROLLED_REENTRY> <CENTER_NAME>EARTH</CENTER_NAME> <TIME_SYSTEM>UTC</TIME_SYSTEM> <EPOCH_TZERO>2016-10-28T11:41:00.000384</EPOCH_TZERO> <REF_FRAME>EME2000</REF_FRAME> <GRAVITY_MODEL>GEM-T1: 8D 8O</GRAVITY_MODEL> <ATMOSPHERIC_MODEL>DTM-13</ATMOSPHERIC_MODEL> <SOLAR_FLUX_PREDICTION>ESA SOLMAG</SOLAR_FLUX_PREDICTION> <N_BODY_PERTURBATIONS>MOON, SUN</N_BODY_PERTURBATIONS> <SOLAR_RAD_PRESSURE>CYLINDRICAL SHADOW</SOLAR_RAD_PRESSURE> <EARTH_TIDES>NO</EARTH_TIDES> <INTRACK_THRUST>NO</INTRACK_THRUST> <DRAG_PARAMETERS_SOURCE>CD FITTING WITH FOCUS2</DRAG_PARAMETERS_SOURCE> <DRAG_PARAMETERS_ALTITUDE units="km">179.49</DRAG_PARAMETERS_ALTITUDE> <REENTRY_UNCERTAINTY_METHOD>EMPIRICAL</REENTRY_UNCERTAINTY_METHOD> <REENTRY_DISINTEGRATION>NONE</REENTRY_DISINTEGRATION> <IMPACT_UNCERTAINTY_METHOD>EMPIRICAL</IMPACT_UNCERTAINTY_METHOD> <PREVIOUS_MESSAGE_ID></PREVIOUS_MESSAGE_ID> </metadata> <data> <atmosphericReentryParameters> <COMMENT>Prediction based on 2 TIRA passes as last orbit state, 5 days before re-entry</COMMENT> <ORBIT_LIFETIME units="d">5.04375</ORBIT_LIFETIME> <REENTRY_ALTITUDE units="km">76.88</REENTRY_ALTITUDE> <ORBIT_LIFETIME_WINDOW_START units="d">4.035</ORBIT_LIFETIME_WINDOW_START> <ORBIT_LIFETIME_WINDOW_END units="d">6.0525</ORBIT_LIFETIME_WINDOW_END> <NOMINAL_REENTRY_EPOCH>2016-11-02T12:38:07.000000</NOMINAL_REENTRY_EPOCH> <REENTRY_WINDOW_START>2016-11-01T12:31:31.000000</REENTRY_WINDOW_START> <REENTRY_WINDOW_END>2016-11-03T12:56:43.000000</REENTRY_WINDOW_END> <ORBIT_LIFETIME_CONFIDENCE units="%">20.0</ORBIT_LIFETIME_CONFIDENCE> </atmosphericReentryParameters> <groundImpactParameters> <COMMENT>As it is 5 days before re-entry, still all the world is under the ground-track</COMMENT> <PROBABILITY_OF_IMPACT>1.0</PROBABILITY_OF_IMPACT> <PROBABILITY_OF_BURN_UP>0.0</PROBABILITY_OF_BURN_UP> <PROBABILITY_OF_BREAK_UP>0.5</PROBABILITY_OF_BREAK_UP> <PROBABILITY_OF_LAND_IMPACT>0.3</PROBABILITY_OF_LAND_IMPACT> <PROBABILITY_OF_CASUALTY>1e-05</PROBABILITY_OF_CASUALTY> <NOMINAL_IMPACT_EPOCH>2016-11-02T12:44:07.000000</NOMINAL_IMPACT_EPOCH> <IMPACT_WINDOW_START>2016-11-01T12:31:31.000000</IMPACT_WINDOW_START> <IMPACT_WINDOW_END>2016-11-03T12:56:43.000000</IMPACT_WINDOW_END> <IMPACT_REF_FRAME>WGS84</IMPACT_REF_FRAME> <NOMINAL_IMPACT_LON units="deg">150.47</NOMINAL_IMPACT_LON> <NOMINAL_IMPACT_LAT units="deg">-29.79</NOMINAL_IMPACT_LAT> <NOMINAL_IMPACT_ALT units="m">8.2028</NOMINAL_IMPACT_ALT> </groundImpactParameters> <stateVector> <COMMENT>epoch of OD from 2 TIRA tracks</COMMENT> <EPOCH>2016-10-28T11:41:00.000384</EPOCH> <X units="km">-2095.41001813074</X> <Y units="km">-3040.70137293811</Y> <Z units="km">5458.83815375429</Z> <X_DOT units="km/s">6.87141346593969</X_DOT> <Y_DOT units="km/s">1.3852134950239</Y_DOT> <Z_DOT units="km/s">3.36023038345871</Z_DOT> </stateVector> <covarianceMatrix> <COMMENT>This is the covariance from the OD</COMMENT> <COV_REF_FRAME>RTN</COV_REF_FRAME> <CX_X units="km**2">0.00834</CX_X> <CY_X units="km**2">-0.00271</CY_X> <CY_Y units="km**2">0.00189</CY_Y> <CZ_X units="km**2">0.000735</CZ_X> <CZ_Y units="km**2">0.00153</CZ_Y> <CZ_Z units="km**2">0.00327</CZ_Z> <CX_DOT_X units="km**2/s">5.86e-05</CX_DOT_X> <CX_DOT_Y units="km**2/s">-1.02e-05</CX_DOT_Y> <CX_DOT_Z units="km**2/s">5.01e-06</CX_DOT_Z> <CX_DOT_X_DOT units="km**2/s**2">4.42e-07</CX_DOT_X_DOT> <CY_DOT_X units="km**2/s">-1.77e-05</CY_DOT_X> <CY_DOT_Y units="km**2/s">2.9e-06</CY_DOT_Y> <CY_DOT_Z units="km**2/s">1.13e-05</CY_DOT_Z> <CY_DOT_X_DOT units="km**2/s**2">-7.25e-08</CY_DOT_X_DOT> <CY_DOT_Y_DOT units="km**2/s**2">1.26e-08</CY_DOT_Y_DOT> <CZ_DOT_X units="km**2/s">6.64e-06</CZ_DOT_X> <CZ_DOT_Y units="km**2/s">-1.62e-06</CZ_DOT_Y> <CZ_DOT_Z units="km**2/s">2.35e-05</CZ_DOT_Z> <CZ_DOT_X_DOT units="km**2/s**2">5.53e-08</CZ_DOT_X_DOT> <CZ_DOT_Y_DOT units="km**2/s**2">-1.15e-08</CZ_DOT_Y_DOT> <CZ_DOT_Z_DOT units="km**2/s**2">1.72e-07</CZ_DOT_Z_DOT> </covarianceMatrix> <spacecraftParameters> <COMMENT>Cr is fixed, Cd includes all effects</COMMENT> <WET_MASS units="kg">960.0</WET_MASS> <DRY_MASS units="kg">410.0</DRY_MASS> <SOLAR_RAD_AREA units="m**2">1.0</SOLAR_RAD_AREA> <SOLAR_RAD_COEFF>1.2</SOLAR_RAD_COEFF> <DRAG_AREA units="m**2">3.9545</DRAG_AREA> <DRAG_COEFF>2.3588</DRAG_COEFF> <BALLISTIC_COEFF units="kg/m**2">0.009717</BALLISTIC_COEFF> </spacecraftParameters> <odParameters> <COMMENT>two TIRA tracks</COMMENT> <TIME_LASTOB_START>2016-10-27T11:54:20.000000</TIME_LASTOB_START> <TIME_LASTOB_END>2016-10-28T11:41:00.000000</TIME_LASTOB_END> <RECOMMENDED_OD_SPAN units="d">2.0</RECOMMENDED_OD_SPAN> <ACTUAL_OD_SPAN units="d">1.0</ACTUAL_OD_SPAN> <OBS_AVAILABLE>655</OBS_AVAILABLE> <OBS_USED>655</OBS_USED> <TRACKS_AVAILABLE>2</TRACKS_AVAILABLE> <TRACKS_USED>2</TRACKS_USED> <RESIDUALS_ACCEPTED units="%">100.0</RESIDUALS_ACCEPTED> <WEIGHTED_RMS>0.0097</WEIGHTED_RMS> </odParameters> </data> </segment> </body> </ndm:rdm>

Figure E-3 ESA/ESOC XML RDM for Test Case #4

<?xml version="1.0" encoding="utf-8"?> <ndm:rdm xmlns:ndm="urn:ccsds:recommendation:navigation:schema:ndmxml" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance" xsi:noNamespaceSchemaLocation="../xmlSchema/ndmxml-1.0-rdm-1.0-oneFile.xsd" id="CCSDS_RDM_VERS" version="0.3"> <header> <COMMENT>Test-case#5: very short term prediction with ground impact location and uncertainties</COMMENT> <CREATION_DATE>2016-11-01T20:14:02.000000</CREATION_DATE> <ORIGINATOR>ESA-SDO</ORIGINATOR> <MESSAGE_ID>2012-006K_20181109141402_ESA-SDO_E231</MESSAGE_ID> </header> <body> <segment> <metadata> <OBJECT_NAME>AVUM (Vega)</OBJECT_NAME> <INTERNATIONAL_DESIGNATOR>2012-006K</INTERNATIONAL_DESIGNATOR> <CATALOG_NAME>SATCAT</CATALOG_NAME> <OBJECT_DESIGNATOR>38086</OBJECT_DESIGNATOR> <OBJECT_TYPE>ROCKET BODY</OBJECT_TYPE> <CONTROLLED_REENTRY>NO</CONTROLLED_REENTRY> <CENTER_NAME>EARTH</CENTER_NAME> <TIME_SYSTEM>UTC</TIME_SYSTEM> <EPOCH_TZERO>2016-11-01T19:03:00.673920</EPOCH_TZERO> <REF_FRAME>EME2000</REF_FRAME> <GRAVITY_MODEL>GEM-T1: 8D 8O</GRAVITY_MODEL> <ATMOSPHERIC_MODEL>DTM-13</ATMOSPHERIC_MODEL> <SOLAR_FLUX_PREDICTION>ESA SOLMAG</SOLAR_FLUX_PREDICTION> <N_BODY_PERTURBATIONS>MOON, SUN</N_BODY_PERTURBATIONS> <SOLAR_RAD_PRESSURE>CYLINDRICAL SHADOW</SOLAR_RAD_PRESSURE> <EARTH_TIDES>NO</EARTH_TIDES> <INTRACK_THRUST>NO</INTRACK_THRUST> <DRAG_PARAMETERS_SOURCE>CD FITTING WITH FOCUS2</DRAG_PARAMETERS_SOURCE> <DRAG_PARAMETERS_ALTITUDE units="km">141.04</DRAG_PARAMETERS_ALTITUDE> <REENTRY_UNCERTAINTY_METHOD>EMPIRICAL</REENTRY_UNCERTAINTY_METHOD> <REENTRY_DISINTEGRATION>NONE</REENTRY_DISINTEGRATION> <IMPACT_UNCERTAINTY_METHOD>EMPIRICAL</IMPACT_UNCERTAINTY_METHOD> <PREVIOUS_MESSAGE_ID></PREVIOUS_MESSAGE_ID> </metadata> <data> <atmosphericReentryParameters> <COMMENT>Latest prediction</COMMENT> <ORBIT_LIFETIME units="d">0.416666666666667</ORBIT_LIFETIME> <REENTRY_ALTITUDE units="km">77.046</REENTRY_ALTITUDE> <ORBIT_LIFETIME_WINDOW_START units="d">0.333333333333333</ORBIT_LIFETIME_WINDOW_START> <ORBIT_LIFETIME_WINDOW_END units="d">0.5</ORBIT_LIFETIME_WINDOW_END> <NOMINAL_REENTRY_EPOCH>2016-11-02T04:57:42.000000</NOMINAL_REENTRY_EPOCH> <REENTRY_WINDOW_START>2016-11-02T02:57:42.000000</REENTRY_WINDOW_START> <REENTRY_WINDOW_END>2016-11-02T06:57:42.000000</REENTRY_WINDOW_END> <ORBIT_LIFETIME_CONFIDENCE units="%">20.0</ORBIT_LIFETIME_CONFIDENCE> </atmosphericReentryParameters> <groundImpactParameters> <COMMENT>Still 3 complete ground tracks around the globe</COMMENT> <PROBABILITY_OF_IMPACT>1.0</PROBABILITY_OF_IMPACT> <PROBABILITY_OF_BURN_UP>0.0</PROBABILITY_OF_BURN_UP> <PROBABILITY_OF_BREAK_UP>0.5</PROBABILITY_OF_BREAK_UP> <PROBABILITY_OF_LAND_IMPACT>0.3</PROBABILITY_OF_LAND_IMPACT> <PROBABILITY_OF_CASUALTY>1e-05</PROBABILITY_OF_CASUALTY> <NOMINAL_IMPACT_EPOCH>2016-11-02T05:03:42.000000</NOMINAL_IMPACT_EPOCH> <IMPACT_WINDOW_START>2016-11-02T03:03:42.000000</IMPACT_WINDOW_START> <IMPACT_WINDOW_END>2016-11-02T07:03:42.000000</IMPACT_WINDOW_END> <IMPACT_REF_FRAME>WGS84</IMPACT_REF_FRAME> <NOMINAL_IMPACT_LON units="deg">113.21</NOMINAL_IMPACT_LON> <NOMINAL_IMPACT_LAT units="deg">61.73</NOMINAL_IMPACT_LAT> <NOMINAL_IMPACT_ALT units="m">8.22</NOMINAL_IMPACT_ALT> <IMPACT_1_CONFIDENCE units="%">10.0</IMPACT_1_CONFIDENCE> <IMPACT_1_START_LON units="deg">90.87283</IMPACT_1_START_LON> <IMPACT_1_START_LAT units="deg">44.57944</IMPACT_1_START_LAT> <IMPACT_1_STOP_LON units="deg">173.20737</IMPACT_1_STOP_LON> <IMPACT_1_STOP_LAT units="deg">68.60964</IMPACT_1_STOP_LAT> <IMPACT_1_CROSS_TRACK units="km">2.0</IMPACT_1_CROSS_TRACK> <IMPACT_2_CONFIDENCE units="%">20.0</IMPACT_2_CONFIDENCE> <IMPACT_2_START_LON units="deg">79.61425</IMPACT_2_START_LON> <IMPACT_2_START_LAT units="deg">23.03239</IMPACT_2_START_LAT> <IMPACT_2_STOP_LON units="deg">-146.30388</IMPACT_2_STOP_LON> <IMPACT_2_STOP_LAT units="deg">54.42478</IMPACT_2_STOP_LAT> <IMPACT_2_CROSS_TRACK units="km">5.0</IMPACT_2_CROSS_TRACK> <IMPACT_3_CONFIDENCE units="%">30.0</IMPACT_3_CONFIDENCE> <IMPACT_3_START_LON units="deg">64.09553</IMPACT_3_START_LON> <IMPACT_3_START_LAT units="deg">-22.43383</IMPACT_3_START_LAT> <IMPACT_3_STOP_LON units="deg">-121.89866</IMPACT_3_STOP_LON> <IMPACT_3_STOP_LAT units="deg">12.45417</IMPACT_3_STOP_LAT> <IMPACT_3_CROSS_TRACK units="km">10.0</IMPACT_3_CROSS_TRACK> </groundImpactParameters> <stateVector> <COMMENT>epoch of latest TLE (same as epoch_tzero)</COMMENT> <EPOCH>2016-11-01T19:03:00.673920</EPOCH> <X units="km">4388.70920498928</X> <Y units="km">-1149.12118870591</Y> <Z units="km">4686.18566939793</Z> <X_DOT units="km/s">5.69273208520766</X_DOT> <Y_DOT units="km/s">2.59493554481721</Y_DOT> <Z_DOT units="km/s">-4.69455708111904</Z_DOT> </stateVector> <spacecraftParameters> <WET_MASS units="kg">960.0</WET_MASS> <DRY_MASS units="kg">410.0</DRY_MASS> <SOLAR_RAD_AREA units="m**2">1.0</SOLAR_RAD_AREA> <SOLAR_RAD_COEFF>1.2</SOLAR_RAD_COEFF> <DRAG_AREA units="m**2">3.9545</DRAG_AREA> <DRAG_COEFF>2.5388</DRAG_COEFF> <BALLISTIC_COEFF units="kg/m**2">0.010458</BALLISTIC_COEFF> </spacecraftParameters> </data> </segment> </body> </ndm:rdm>

Figure E-4 ESA/ESOC XML RDM for Test Case #5

The following KVN RDMs were produced by the DLR/GSOC prototype.

CCSDS_RDM_VERS = 1.0 CREATION_DATE = 2018-11-30T15:30:54.272 ORIGINATOR = GSOC MESSAGE_ID = GSOC/2018-11-30T15:30:54UTC OBJECT_NAME = AVUM R/B INTERNATIONAL_DESIGNATOR = 2012-006K CATALOG_NAME = SATCAT OBJECT_DESIGNATOR = 12345 OBJECT_TYPE = UNKNOWN CONTROLLED_REENTRY = NO CENTER_NAME = EARTH TIME_SYSTEM = UTC EPOCH_TZERO = 2015-11-01T20:05:40.000 REF_FRAME = TOD GRAVITY_MODEL = GGM01S: 08D 08O ATMOSPHERIC_MODEL = JACCHIA-GILL SOLAR_FLUX_PREDICTION = PREDICTED: MLLRT N_BODY_PERTURBATIONS = SUN, MOON SOLAR_RAD_PRESSURE = CANNONBALL EARTH_TIDES = MCCARTHY1996 INTRACK_THRUST = NO DRAG_PARAMETERS_SOURCE = OD DRAG_PARAMETERS_ALTITUDE = 491.8595 [km] REENTRY_UNCERTAINTY_METHOD = EMPIRICAL REENTRY_DISINTEGRATION = NONE ORBIT_LIFETIME = 385.4993 [d] REENTRY_ALTITUDE = 120.0000 [km] ORBIT_LIFETIME_WINDOW_START = 308.3994 [d] ORBIT_LIFETIME_WINDOW_END = 462.5992 [d] ORBIT_LIFETIME_CONFIDENCE = 20.0000 [%] EPOCH = 2015-11-01T20:05:40.000 X = -5925.7575000000 [km] Y = 2969.1288510000 [km] Z = -9.2273870000 [km] X_DOT = -1.2300694874 [km/s] Y_DOT = -2.4793156054 [km/s] Z_DOT = 7.3849831139 [km/s] COV_REF_FRAME = TOD CX_X = 0.1993482000E+05 [km**2] CY_X = 0.1699190000E+05 [km**2] CY_Y = 0.4277394000E+05 [km**2] CZ_X = -.4360502000E+05 [km**2] CZ_Y = -.8070623000E+05 [km**2] CZ_Z = 0.2763912000E+06 [km**2] CX_DOT_X = -.4341996000E+02 [km**2/s] CX_DOT_Y = 0.1864858000E+02 [km**2/s] CX_DOT_Z = 0.9977287000E+01 [km**2/s] CX_DOT_X_DOT = 0.2541062000E+00 [km**2/s**2] CY_DOT_X = -.7624604000E+02 [km**2/s] CY_DOT_Y = 0.4105582000E+02 [km**2/s] CY_DOT_Z = -.4225089000E+01 [km**2/s] CY_DOT_X_DOT = -.1159934000E+00 [km**2/s**2] CY_DOT_Y_DOT = 0.7962669000E-01 [km**2/s**2] CZ_DOT_X = 0.2537051000E+03 [km**2/s] CZ_DOT_Y = -.1264063000E+03 [km**2/s] CZ_DOT_Z = -.9858566000E+00 [km**2/s] CZ_DOT_X_DOT = -.4018615000E-03 [km**2/s**2] CZ_DOT_Y_DOT = 0.2305920000E-02 [km**2/s**2] CZ_DOT_Z_DOT = 0.1226711000E-01 [km**2/s**2] WET_MASS = 960.0000000000 [kg] SOLAR_RAD_AREA = 1.0000000000 [m**2] SOLAR_RAD_COEFF = 1.2000000000 DRAG_AREA = 3.9500000000 [m**2] DRAG_COEFF = 2.4108000000

Figure E-5 DLR/GSOC KVN RDM for Test Case #2

CCSDS_RDM_VERS = 1.0 CREATION_DATE = 2019-01-10T13:13:24.063 ORIGINATOR = GSOC MESSAGE_ID = GSOC/2019-01-10T13:13:24UTC OBJECT_NAME = AVUM R/B INTERNATIONAL_DESIGNATOR = 2012-006K CONTROLLED_REENTRY = NO CENTER_NAME = EARTH TIME_SYSTEM = UTC EPOCH_TZERO = 2016-10-28T11:41:00.000 REF_FRAME = TOD GRAVITY_MODEL = GGM01S: 20D 20O ATMOSPHERIC_MODEL = JACCHIA-GILL SOLAR_FLUX_PREDICTION = PREDICTED: MLLRT N_BODY_PERTURBATIONS = SUN, MOON SOLAR_RAD_PRESSURE = CANNONBALL EARTH_TIDES = MCCARTHY1996 INTRACK_THRUST = NO REENTRY_DISINTEGRATION = NONE ORBIT_LIFETIME = 4.8915 [d] REENTRY_ALTITUDE = 70.0000 [km] NOMINAL_REENTRY_EPOCH = 2016-11-02T09:04:43.000 REENTRY_WINDOW_START = 2016-11-01T09:35:58.400 REENTRY_WINDOW_END = 2016-11-03T08:33:27.600 ORBIT_LIFETIME_CONFIDENCE = 20.0000 [%] EPOCH = 2016-10-28T11:41:00.000 X = -2092.8991170000 [km] Y = -3048.2867570000 [km] Z = 5455.5699160000 [km] X_DOT = 6.8607473416 [km/s] Y_DOT = 1.4109533544 [km/s] Z_DOT = 3.3712971129 [km/s] COV_REF_FRAME = TOD CX_X = 0.3444576000E+04 [km**2] CY_X = 0.2776114000E+04 [km**2] CY_Y = 0.4644814000E+04 [km**2] CZ_X = -.3522417000E+04 [km**2] CZ_Y = -.8150142000E+03 [km**2] CZ_Z = 0.5410610000E+04 [km**2] CX_DOT_X = 0.1716400000E+02 [km**2/s] CX_DOT_Y = 0.1813913000E+02 [km**2/s] CX_DOT_Z = -.2741168000E+02 [km**2/s] CX_DOT_X_DOT = 0.1355194000E+00 [km**2/s**2] CY_DOT_X = 0.4100798000E+01 [km**2/s] CY_DOT_Y = 0.2948572000E+02 [km**2/s] CY_DOT_Z = -.1155865000E+02 [km**2/s] CY_DOT_X_DOT = 0.3382276000E-01 [km**2/s**2] CY_DOT_Y_DOT = 0.1886625000E+00 [km**2/s**2] CZ_DOT_X = -.2658308000E+02 [km**2/s] CZ_DOT_Y = -.6260346000E+01 [km**2/s] CZ_DOT_Z = 0.3835028000E+02 [km**2/s] CZ_DOT_X_DOT = -.1992697000E+00 [km**2/s**2] CZ_DOT_Y_DOT = -.8625371000E-01 [km**2/s**2] CZ_DOT_Z_DOT = 0.3024180000E+00 [km**2/s**2] WET_MASS = 960.0000000000 [kg] SOLAR_RAD_AREA = 1.0000000000 [m**2] SOLAR_RAD_COEFF = 1.2000000000 DRAG_AREA = 3.9500000000 [m**2] DRAG_COEFF = 2.3588000000

Figure E-6 DLR/GSOC KVN RDM for Test Case #3

CCSDS_RDM_VERS = 1.0 CREATION_DATE = 2019-01-10T13:18:45.160 ORIGINATOR = GSOC MESSAGE_ID = GSOC/2019-01-10T13:18:45UTC OBJECT_NAME = AVUM R/B INTERNATIONAL_DESIGNATOR = 2012-006K CONTROLLED_REENTRY = NO CENTER_NAME = EARTH TIME_SYSTEM = UTC EPOCH_TZERO = 2016-10-28T11:41:00.000 REENTRY_DISINTEGRATION = NONE IMPACT_UNCERTAINTY_METHOD = EMPIRICAL ORBIT_LIFETIME = 4.8913 [d] REENTRY_ALTITUDE = 70.0000 [km] ORBIT_LIFETIME_CONFIDENCE = 20.0000 [%] NOMINAL_IMPACT_EPOCH = 2016-11-02T09:04:30.000 IMPACT_WINDOW_START = 2016-11-01T09:35:48.000 IMPACT_WINDOW_END = 2016-11-03T08:33:12.000 IMPACT_REF_FRAME = WGS84 NOMINAL_IMPACT_LON = 2.3946 [deg] NOMINAL_IMPACT_LAT = -15.6304 [deg] NOMINAL_IMPACT_ALT = 70.0000 [m]

Figure E-7 DLR/GSOC KVN RDM for Test Case #4

CCSDS_RDM_VERS = 1.0 CREATION_DATE = 2018-11-30T15:15:51.554 ORIGINATOR = GSOC MESSAGE_ID = GSOC/2018-11-30T15:15:51UTC OBJECT_NAME = AVUM R/B INTERNATIONAL_DESIGNATOR = 2012-006K CONTROLLED_REENTRY = NO CENTER_NAME = EARTH TIME_SYSTEM = UTC EPOCH_TZERO = 2016-11-01T19:03:00.000 REENTRY_DISINTEGRATION = BREAK-UP IMPACT_UNCERTAINTY_METHOD = MONTE CARLO ORBIT_LIFETIME = 0.3758 [d] REENTRY_ALTITUDE = 80.0000 [km] NOMINAL_IMPACT_EPOCH = 2016-11-02T04:13:13.000 IMPACT_WINDOW_START = 2016-11-02T04:11:03.000 IMPACT_WINDOW_END = 2016-11-02T04:14:42.000 IMPACT_REF_FRAME = WGS84 NOMINAL_IMPACT_LON = -85.1700 [deg] NOMINAL_IMPACT_LAT = -27.1000 [deg] NOMINAL_IMPACT_ALT = 0.0000 [m] IMPACT_1_CONFIDENCE = 66.6667 [%] IMPACT_1_START_LON = -85.9810 [deg] IMPACT_1_START_LAT = -25.0910 [deg] IMPACT_1_STOP_LON = -84.0710 [deg] IMPACT_1_STOP_LAT = -29.7080 [deg] IMPACT_1_CROSS_TRACK = 0.7510 [km] IMPACT_2_CONFIDENCE = 95.0000 [%] IMPACT_2_START_LON = -86.8830 [deg] IMPACT_2_START_LAT = -22.7720 [deg] IMPACT_2_STOP_LON = -83.0500 [deg] IMPACT_2_STOP_LAT = -32.0050 [deg] IMPACT_2_CROSS_TRACK = 1.5020 [km] IMPACT_3_CONFIDENCE = 99.7300 [%] IMPACT_3_START_LON = -87.7540 [deg] IMPACT_3_START_LAT = -20.4470 [deg] IMPACT_3_STOP_LON = -81.9780 [deg] IMPACT_3_STOP_LAT = -34.2910 [deg] IMPACT_3_CROSS_TRACK = 2.2520 [km]

Figure E-8 DLR/GSOC KVN RDM for Test Case #5