## Slide 1: Tracking Data Message Pv2.01 CCSDS Fall 2022 Meeting
18 Oct 2022
Juan Crenshaw
Cheryl Gramling
Red = considerations from WG

## Slide 2: Objectives
Overview of rationale behind main updates
Review of major changes / examples
Discuss feedback from WG on additional update items

## Slide 3: Criteria
Maximize backwards compatibility with the latest CCSDS TDM document
Evolve the TDM structure to facilitate modularization
  Potential support for real-time tracking data, in addition to the current file-based approach
Ensure consistency with other navigation message implementations (e.g. ODM, ADM)
When adding new keywords, capture generic functionality that could apply to different tracking techniques and/or sensor types.

## Slide 4: Modularizing (Current)
Header | CCSDS_TDM_VERS
 | COMMENT
 | CREATION_DATE
 | ORIGINATOR
 | MESSAGE_ID
Metadata | META_START | 
 | COMMENT | 
 | TRACK_ID | 
 | CLASSIFICATION | 
 | PREVIOUS_MESSAGE_ID | 
 | NEXT_MESSAGE_ID | 
 | DATA_TYPES | 
 | TDM_BASIS | 
 | TDM_BASIS_ID | 
 | TIME_SYSTEM | 
 | START_TIME | 
 | STOP_TIME | 
 | PARTICIPANT_n | 
 | ODM_MSG_LINK _n | 
 | ADM_MSG_LINK_n | 
 | PRM_MSG_LINK_n | 
 | RDM_MSG_LINK_n | 
 | MODE | 
 | PATH_m | 
 | TRANSMIT_BAND_n | 
 | RECEIVE_BAND_n | 
 | TURNAROUND_NUMERATOR_n | 
 | TURNAROUND_DENOMINATOR_n | 
 | TIMETAG_REF | 
 | TIMETAG_UNCERTAINTY | 
 | INTEGRATION_INTERVAL | 
 | INTEGRATION_REF | 
 | FREQ_OFFSET | 
 | RANGE_MODE | 
 | RANGE_MODULUS | 
 | RANGE_UNITS | 
 | MAG_UNCERTAINTY | 
 | RCS_UNITS | 
 | MINIMUM_RCS | 
 | ASTROMETRIC_STAR_COUNT | 
 | PHOTOMETRIC_STAR_COUNT | 
 | PHOTOMETRIC_SNR | 
 | FRAME_LIMITING_BRIGHTNESS | 
 | ANGLE_TYPE | 
 | ANGLE_UNITS | 
 | REFERENCE_FRAME | 
 | INTERPOLATION | 
 | INTERPOLATION_DEGREE | 
 | DOPPLER_COUNT_BIAS | 
 | DOPPLER_COUNT_SCALE | 
 | DOPPLER_COUNT_ROLLOVER | 
 | TRANSMIT_DELAY_n | 
 | RECEIVE_DELAY_n | 
 | FRONT_END_ID_n | 
 | SYSTEM_MODE_n | 
 | SYSTEM_PATH_n | 
 | CLOCK_REF_ID_n | 
 | DATA_QUALITY | 
 | CORRECTION_* | CORRECTION_ANGLE_1
 |  | CORRECTION_ANGLE_2
 |  | CORRECTION_DOPPLER
 |  | CORRECTION_MAG
 |  | CORRECTION_RANGE
 |  | CORRECTION_RCS
 |  | CORRECTION_RECEIVE
 |  | CORRECTION_TRANSMIT
 |  | CORRECTION_ABERRATION_YEARLY
 |  | CORRECTION_ABERRATION_DIURNAL
 |  | CORRECTION_TIME
 | CORRECTIONS_APPLIED | 
 | META_STOP | 
CARRIER_POWER
DOPPLER_COUNT
DOPPLER_INSTANTANEOUS
DOPPLER_INTEGRATED
PC_N0
RECEIVE_PHASE_CT_n (n = 1, 2, 3, 4, 5)
TRANSMIT_PHASE_CT_n (n = 1, 2, 3, 4, 5)
PR_N0
RANGE
RECEIVE_FREQ_n (n = 1, 2, 3, 4, 5)
RECEIVE_FREQ
TRANSMIT_FREQ_n (n = 1, 2, 3, 4, 5)
TRANSMIT_FREQ_RATE_n (n = 1, 2, 3, 4, 5)
DOR
VLBI_DELAY
ANGLE_1
ANGLE_1_RATE
ANGLE_2
ANGLE_2_RATE
ANGLE_MODE
OBSERVATION_COVARIANCE
MAG
RCS
CLOCK_BIAS
CLOCK_DRIFT
STEC
TROPO_DRY
TROPO_WET
PRESSURE
RHUMIDITY
TEMPERATURE
COMMENT
CORRECTIONS_APPLIED
CORRECTION_*
DATA_START
DATA_STOP
DATA_QUALITY
Header
Metadata
Data

## Slide 5: Modularizing (thoughts for TDM V3)
Header | CCSDS_TDM_VERS
 | COMMENT
 | CREATION_DATE
 | ORIGINATOR
 | MESSAGE_ID
Metadata | META_START
 | COMMENT
 | TRACK_ID
 | CLASSIFICATION
 | PREVIOUS_MESSAGE_ID
 | NEXT_MESSAGE_ID
 | DATA_TYPES_t
 | TDM_BASIS
 | TDM_BASIS_ID
 | TIME_SYSTEM
 | START_TIME
 | STOP_TIME
 | PARTICIPANT_n
 | MODE
 | PATH_m
 | META_STOP
Participant_n | ODM_MSG_LINK _n
 | ADM_MSG_LINK_n
 | PRM_MSG_LINK_n
 | RDM_MSG_LINK_n
 | TRANSMIT_BAND_n
 | RECEIVE_BAND_n
 | TURNAROUND_NUMERATOR_n
 | TURNAROUND_DENOMINATOR_n
 | TRANSMIT_DELAY_n
 | RECEIVE_DELAY_n
 | FRONT_END_ID_n
 | SYSTEM_MODE_n
 | SYSTEM_PATH_n
 | CLOCK_REF_ID_n
Data_Type_t | TIMETAG_REF | 
 | TIMETAG_UNCERTAINTY | 
 | INTEGRATION_INTERVAL | 
 | INTEGRATION_REF | 
 | CORRECTION_TIME | 
 | Doppler | FREQ_OFFSET
 |  | INTERPOLATION
 |  | INTERPOLATION_DEGREE
 |  | DOPPLER_COUNT_BIAS
 |  | DOPPLER_COUNT_SCALE
 |  | DOPPLER_COUNT_ROLLOVER
 |  | CORRECTION_DOPPLER
Data | Signal Related Keywords | CARRIER_POWER
 |  | DOPPLER_COUNT
 |  | DOPPLER_INSTANTANEOUS
 |  | DOPPLER_INTEGRATED
 |  | PC_N0
 |  | RECEIVE_PHASE_CT_n (n = 1, 2, 3, 4, 5)
 |  | TRANSMIT_PHASE_CT_n (n = 1, 2, 3, 4, 5)

## Slide 6: Real-Time Data Thought for TDM V3
Real-Time data with current TDM format requires inclusion of Header and Metadata for every data point or section of data transmitted
  Lots of overhead
Potential Implementation Solution
  Include optional METADATA_ID (or similar)
  Data section identifies applicable METADATA_ID, with no need to repeat all the information
NOTE – However, the TDM that results from transfer via the TD-CSTS will likely be larger than a TDM that contains the same information but that is generated at a single time (i.e., after the conclusion of the tracking pass) because the transfer of TDM data via the TD-CSTS involves the repetition of metadata with every tracking data measurement in order to facilitate the incremental transfer of tracking data in near real time.
CSTS TRACKING DATA SERVICE
https://public.ccsds.org/Pubs/922x2b1.pdf

## Slide 7: Categories for Incorporated Updates
  Providing and allocating appropriate fields for relevant information could reduce the amount of TDM version spinoffs from what is in the blue book
  Categories
    New Metadata
      New functionality consistent with ODM/ADM
    amendments to metadata
    new measurement types
    handling of relay systems
    assigning new data attributes
    incorporate onboard data types

## Slide 8: TDM Vp2.01 Changes (1 of 2) New Meta Data Consistent with ODM / ADM
Link the TDM to other MESSAGE_ID references
  Incorporated changes to ensure consistency with ODM, ADM implementation.
  Added keywords: PREVIOUS_MESSAGE_ID, NEXT_MESSAGE_ID, ODM_MSG_LINK, ADM_MSG_LINK, PRM_MSG_LINK, RDM_MSG_LINK
    …_LINK keywords are included with _n to be able to associate with different participants.
  Removed keyword: EPHEMERIS_NAME (functionality covered under new ODM_MSG_LINK keyword)  keep in this version. <add text to mention this is for non-ODM files> - use similar language for CDM- (propose something  see following text)
Incorporate “MODALITY” functionality.
  Identify if data is OPERATIONAL, SIMULATED, TEST, PLAYBACK.  clarify that playback is operational (added text: “PLAYBACK” shall be utilized when retransmitting “OPERATIONAL” data.)
  Added keyword: TDM_BASIS (consistent with ODM “TRAJ_BASIS” from OCM and incorporates functionality)
Suggested addition to EPHEMERIS_NAME: Message originators are encouraged to employ ODM_MSG_LINK to reference ephemerides in ODM format. Otherwise, the EPHEMERIS_NAME keyword should be used to reference ephemeris files that are not in ODM format (for backward compatibility purposes).

## Slide 9: TDM Vp2.01 Changes (2 of 2) New Meta Data Consistent with ODM / ADM
Incorporated “COLLECTION_ID” functionality
  A tracking session identifier, useful when several objects are tracked simultaneously. Helps the processing entity in correlation of observables to objects and in identifying/resolving potential biases from the sensor system. Also, added “TASKING_ID” functionality. A tasking request ID the dataset is responding to.
  Added keyword: TDM_BASIS_ID (consistent with ODM and inclusion of collection and tasking functionality). Formed by Request ID followed by Collection ID, to the extent either are applicable to the TRACK and relate to the TRACK_ID.
  Comments on utilizing the “tasking” terminology. Need to figure out what different entities use. Perhaps mention “request”- [Ralph will provide feedback after some thought] [Jose Miguel to check what is used for Tasking]
Incorporate functionality for SENSOR_POSITION_VELOCITY_VECTOR: position/velocity vector for sensor at time of datum (EME2000; km, km/s) (useful for orbiting sensors, too)
  Already incorporated under #1 (allowing for use of new “XYZ”_MSG_LINK keywords to specify ODM or ADM messages that apply to a specific sensor). Added text to alternatively reference applicable files, as with prior EPHEMERIS_NAME keyword (how to ensure antenna offsets are taken into account: could use pointing?) – perhaps find some text explaining how this could be accomplished

## Slide 10: TDM Vp2.01 Changes (1 of 2) New Metadata
Incorporate classification and special data handling information
  Added Keyword: CLASSIFICATION
  Move up after COMMENT keyword in the header [need to decide where this goes] – do the same with NEXT_MSG_ID and previous??
Incorporate “TIMING_UNCERTAINTY” functionality. Expected uncertainty (1-sigma) in time tag values.
  Added keyword: TIMETAG_UNCERTAINTY
Incorporate system configuration information
  such as EQUIPMENT_ID_PATHn or CONFIGURATION_Px (Px= Xth Participant’s signal path), MODEM_ID, TIME_FREQ_REF_SOURCE_ID, OSCILLATOR_ID (esp for onboard systems with external oscillator option), DSP_ID, Multiple Access System: Center frequency of each link, beamformer ID
  Added keywords: FRONT_END_ID, SYSTEM_PATH, SYSTEM_MODE, TFR_ID
  Would it make sense to have CONFIG_ appended for all configuration items? Part of modularization

## Slide 11: TDM Vp2.01 Changes (2 of 2) New Metadata
Incorporate new angle units, radians and “Angle Units” similar to “Range Units” implementation
  Angle Units rationale: for sensors whose pointing is defined by units of a potentiometer, or other discrete intervals.
  Should Angle Units (AU) be defined in the TDM for interpreting purposes? It appears Range Units (RU) definitions are relegated to ICD.
  Perhaps there is a need to eliminate ICD need and include both interpretations for RU and AU in TDM – for group discussion??
  Track with OPEN COMMENT #2
  Added keyword: ANGLE_UNITS
  Discussion: do we want to allow oddities? [think of impacts of not including]  it could be a problem to include if the message does not include tools to interpret the values
Incorporate “CCD_BINNING” information: integer for bins
Added CCD binning as an example under the new SYSTEM_PATH keyword (see #9)
Incorporate MINIMUM_DETECTABLE_RCS (minimum object RCS detectable by waveform and sequence)
  Added meta keywords: MINIMUM_RCS, RCS UNITS (to include dBsm)
  RCS_MIN and RCS_MAX look at implementation in ODM  RCS_MIN_DETECTABLE
  Jose Miguel will check with operations about the units used for each parameter (MIN_RCS vs RCS)
  Should we consider single keywords for each unit??

## Slide 12: TDM Vp2.01 Changes (1 of 2) Meta Data & Data changes
7) Incorporate new DATA_QUALITY keyword entries and enable DATA_QUALITY in the Data Section
  Added possible values to DATA_QUALITY: VERIFIED, INVALID. VERIFIED=coarse checks, and repurposing VALIDATED=meet requirements (maintains backwards compatibility)
  Included changes in different sections of the document to enable the possibility of incorporating quality “indicators” for each observable (also when corrections apply – see #8). Allow flexibility (still kept in meta to provide backwards compatibility).
8) Allow for designation of corrections for each data type and incorporate new CORRECTION_TIME keyword.
  Included changes in different sections of the document to enable the possibility of incorporating correction “indicators” for each observable (similar as done with #7, see example ahead)
  Added keyword: CORRECTION_TIME

## Slide 13: TDM Vp2.01 Changes (2 of 2) Meta Data & Data changes
16) Incorporate functionality for ANGLE_2_TRAIN (deg): offset of antenna in ANGLE_2 (elevation) that can vary during a track; differs from a constant CORRECTION_ANGLE_2
  Did not add ANGLE_2_TRAIN observable.
  Added CORRECTION_* keyword to data section. (provides flexibility to update corrections dynamically if needed)
  (add to either have corrections in metadata section or data section but not both)
  Could potentially add a corrections keyword with all corrections
    E.g. CORRECTIONS = <timestamp> ANGLE_1 0.02 ANGLE_2 0.024 RANGE 123.023

## Slide 14: TDM Vp2.01 Changes – Example Meta Data & Data changes
META_START
…
DATA_TYPES = [ANGLE_1 ANGLE_2]
START_TIME = 2012-10-29T17:46:39.02
STOP_TIME = 2012-10-29T17:50:53.02
PARTICIPANT_1 = 211
PARTICIPANT_2 = 27715
MODE = SEQUENTIAL
PATH = 2,1
ANGLE_TYPE = AZEL
ANGLE_UNITS = deg
DATA_QUALITY = VERIFIED, INVALID
CORRECTION_ANGLE_1 = 0.003478
CORRECTION_ANGLE_2 = 0.0080
…
META_STOP
DATA_START
ANGLE_1 = 2012-10-29T17:46:39.02 332.2298750 I-U
ANGLE_2 = 2012-10-29T17:46:39.02 16.3028389 I-C
ANGLE_1 = 2012-10-29T17:48:46.02 332.7485833 V-U
ANGLE_2 = 2012-10-29T17:48:46.02 16.1876917 V-C
ANGLE_1 = 2012-10-29T17:50:53.02 333.2668750 V-U
CORRECTION_ANGLE_2 = 2012-10-29T17:50:53.02 0.0180
ANGLE_2 = 2012-10-29T17:50:53.02 16.0716806 V-C
DATA_STOP
Date/Time Data Value Validity-Correction_Applied
V = Verified C = Corrected
I = Invalid U = Uncorrected

## Slide 15: TDM Vp2.01 Changes – Example Meta Data & Data changes
META_START
…
DATA_TYPES = [ANGLE_1 ANGLE_2]
START_TIME = 2012-10-29T17:46:39.02
STOP_TIME = 2012-10-29T17:50:53.02
PARTICIPANT_1 = 211
PARTICIPANT_2 = 27715
MODE = SEQUENTIAL
PATH = 2,1
ANGLE_TYPE = AZEL
ANGLE_UNITS = deg
DATA_QUALITY = VERIFIED, INVALID
CORRECTION_ANGLE_1 = 0.003478
CORRECTION_ANGLE_2 = 0.0080
…
META_STOP
DATA_START
ANGLE_1 = 2012-10-29T17:46:39.02 332.2298750 I
ANGLE_2 = 2012-10-29T17:46:39.02 16.3028389 I
ANGLE_1 = 2012-10-29T17:48:46.02 332.7485833 V
ANGLE_2 = 2012-10-29T17:48:46.02 16.1876917 V
ANGLE_1 = 2012-10-29T17:50:53.02 333.2668750 V
CORRECTION_ANGLE_2 = 2012-10-29T17:50:53.02 0.0180
ANGLE_2 = 2012-10-29T17:50:53.02 16.0716806 V
DATA_STOP
Date/Time Data Value Validity
V = Verified
I = Invalid
As part of WG feedback, removed correction indicators (pink) – from prior slide; since corrections for a specific observable are likely applied or not for the entire data section. Need to work on separating corrections for each observable within the metadata section to make that work.

## Slide 16: TDM V2.01 Participant Changes Meta Data Amended
5) Updated PARTICIPANT_n: Increase the number of participants to accommodate relay and constellation systems
  Modified PARTICIPANT_n field
  Added a new MODE=RELAY
  Added text explaining RELAY mode

## Slide 17: Participant_5 Example scenario (does not work)
LO Ref 2
Return 2
Return 1
Forward 2
Forward 1
LO Ref 1
Relay #1
Relay #2
Participants
  Participant_1 = Station #1
  Participant_2 = Relay #1
  Participant_3 = User S/C
  Participant_4 = Relay #2
  Participant_5 = Station #2
Paths
  PATH_1 = 1, 2, 3, 4, 5 (4-way path)
  PATH_2 = 1, 2 (LO Ref #1)
  PATH_3 = 5, 4 (LO Ref #2)
Transmit Bands
  Using Path to determine transmit bands
  TRANSMIT_BAND_1 ?? Does not work cleanly for PATH_1, as there are more than one transmission band. Would need more than one metadata section, but the measurements for PATH_1 correspond to settings from different metadata sections??
  TRANSMIT_BAND_2 = Ku (LO Ref #1)
  TRANSMIT_BAND_3 = Ku (LO Ref #2)
Station #1
Station #2
User S/C
NOT IMPLEMENTED, just an example of the limitations of having 5 participants for the relay case

## Slide 18: Participant_9 Example scenario (implemented in TDM Vp2.01)
LO Ref 2
Return 2
Return 1
Forward 2
Forward 1
LO Ref 1
Relay #1
Relay #2
Participants
  Participant_1 = Station #1 (4-way path)
  Participant_2 = Relay #1 (4-way path)
  Participant_3 = User S/C (4-way path)
  Participant_4 = Relay #2 (4-way path)
  Participant_5 = Station #2 (4-way path)
  Participant_6 = Station #1 (LO Ref #1)
  Participant_7 = Relay #1 (LO Ref #1)
  Participant_8 = Station #2 (LO Ref #2)
  Participant_9 = Relay #2 (LO Ref #2)
Paths
  PATH_1 = 1, 2, 3, 4, 5 (4-way path)
  PATH_2 = 6, 7 (LO Ref #1)
  PATH_3 = 8, 9 (LO Ref #2)
Transmit Bands (similar with Receive Band)
  different links can simply utilize “n” from transmit entity for each PATH (and link within each path)
  TRANSMIT_BAND_1 = Ku (Forward #1)
  TRANSMIT_BAND_2 = S (Forward 2)
  TRANSMIT_BAND_3 = S (Return 1)
  TRANSMIT_BAND_4 = Ku (Return 2)
  TRANSMIT_BAND_6 = Ku (LO Ref #1)
  TRANSMIT_BAND_8 = Ku (LO Ref #2)
Station #1
Station #2
User S/C
Turn-around numerator and denominator
  TURNAROUND_NUMERATOR_3 = 240
  TURNAROUND_DENOMINATOR_3 = 221
  TURNAROUND_NUMERATOR_7 = TBS
  TURNAROUND_DENOMINATOR_7 = TBS
  TURNAROUND_NUMERATOR_9 = TBS
  TURNAROUND_DENOMINATOR_9 = TBS

## Slide 19: TDM Vp2.01 Changes (1 of 3) Data Additions
11) Incorporate “ANT_TRACK_TYPE” functionality
  Identify antenna tracking mode, Program or Autotrack (aided or unaided feedback loop)
  Added data keyword: ANGLE_MODE to the data section to allow mode changes)
  ANGLE_MODE or POINTING_MODE or TRACK_MODE (too generic to refer to angles only)?  could take this under SYSTEM_STATUS?
Incorporated new “SYSTEM_STATUS” functionality in the data section, to allow for multiple system status updates to be captured in TDM’s. Allows functionality to include:
  APERTURE_FILTERS n: name photometric filters applied during track
  APERTURE_FILTER_ZERO_PT n: telescope photometric zero point and uncertainty for the filter
  RECEIVER LOCK indicators (carrier lock, PN synch, PN lock)
  SNR for signal on each PATH between two PARTICIPANTS
  Beamformer Telemetry (bias, noise, thermal)
  Added keyword: SYSTEM_STATUS

## Slide 20: TDM Vp2.01 Changes (2 of 3) Data Additions
14) Incorporate “OBSERVATION COVARIANCE (mixed)”.
  Symmetric, positive definite matrix for estimation error of each observable and cross-correlations. Used for space surveillance sessions.
  Added data keyword: OBSERVATION_COVARIANCE
  Take a look at adding potential for providing order
17) Incorporate ANGLE_RATE observables.
  Measured or derived from angles.
  Added keywords: ANGLE_1_RATE, ANGLE_2_RATE

## Slide 21: TDM Vp2.01 Changes (3 of 3) Data Additions
18) Incorporate ASTROMETRIC_STAR_COUNT (number of correlated stars used for frames) and PHOTOMETRIC_STAR_COUNT (number of correlated stars in photometric solution)
  Added data keywords: ASTROMETRIC_STAR_COUNT, PHOTOMETRIC_STAR_COUNT
19) Incorporate VISUAL_MAGNITUDE_UNCERTAINTY (uncertainty from frame photometric solution that calculates visual magnitude)
  Added data keyword: MAG_UNCERTAINTY
20) Incorporate PHOTOMETRIC_SNR (signal to noise ratio of total photometric content of evaluated signal)
  Added data keyword: PHOTOMETRIC_SNR
21) Incorporate FRAME LIMITING BRIGHTNESS (dimmest object expected to be detected in interrogated location)
  Added data keyword: FRAME_LIMITING_BRIGHTNESS

## Slide 22: TO-DO List (Incorporate to TDM Vp2.x)
Incorporate more comprehensive examples
  relay example
  + another optical
  should we include same examples in xml??
Adjust Appendix areas accordingly
Incorporate ranging parameters
  Tone set (major through minors)
  PN Integration intervals
  Mod Index
  Etc
  Perhaps add under ne keyword “SYSTEM_MODE”

## Slide 23: TO-DO List (Incorporate as much as possible for TDM Vp2. update)
Incorporate new onboard measurements
  General (for example):
    Data Latch Delay: time bias associated with latching data
    Local Oscillator ID
  Accelerometers
  Crosslink
  Received Communications Link
  X-Ray Pulsar Observations for Navigation
  Optical (image) Navigation observation
  Point Solution
  NavSol from GNSS Receiver filter

## Slide 24: Open Comments (1 of 3)
(CjG) Sec 3.3.1.8  Add clarifying text to indicate index starts with #1
(CjG) Sec 3.3.1.10  Shall we aim to reduce ICD reliance; call it an "agreement"; or keep as is?
(CjG) Sec 3.3.1.11  Can TDM v3 address this so that all TRK for an object in a session is contained in a single TDM?
(CjG) Table PARTICIPANT_n description  Need to adjust wording to cover tracking scenarios beyond RF links, e.g. visual.

## Slide 25: Open Comments (2 of 3)
(JC) Table CORRECTION_* keywords  Keywords are not explained anywhere… for example, it is not indicated what observable is corrected with the CORRECTION_RECEIVE, CORRECTION_TRANSMIT, CORRECTION_ABERRATION_YEARLY, CORRECTION_ABERRATION_DIURNAL keywords. Also, how those corrections are applied to the observables. CORRECTION_RECEIVE and ABERRATION_CORRECTION_YEARLY are included in an example for RADEC measurement, however there is no explanation as to how these corrections translate to right ascension and declination correction values.
(JC) Table CORRECTION_* keywords  Units should be the same as the observable… how about when Doppler_Count is used, will Doppler_Correction be a Doppler count for the specified integration period?
  Also, is CORRECTION_TIME simply in seconds?

## Slide 26: Open Comments (3 of 3)
(JC) Sec 3.3.2.7 Angle data should apply to the participants tracking the specific object subject of the tracking session. Need to update this section to reflect that
(JC) Sec 3.4.6  ‘DATA_START’ and ‘DATA_STOP’: This does not apply to XML format, correct?
(JC) Sec 4.3.10  Why not use TIME_SYSTEM for all keywords?

## Slide 27: BACKUP

## Slide 28: Addressing REQUEST  COLLECT  TRACK
Request_ID: Request for sensor time for specific object or ephem or location (e.g. Az, El)
Collection_ID: Refers to the entirety of sensed objects during the data span
Tracking_ID: Refers to the data set specific to the object that is a Participant.
TDM_BASIS_ID: Formed by Request ID followed by Collection ID, to the extent either are applicable to the TRACK and relate to the TRACK_ID.
Do we need to specify OBJECT_ID in the TDM? It’s not explicit, just part of participant.
COLLECTION_ID
TRACK_ID <1>
TRACK_ID <2>
TRACK_ID <3>