## Slide 1: Tracking Data Message Pv2.02 CCSDS Summary of Updates Included
10 April 2024
Juan Crenshaw
Blue = highlighted changes

## Slide 2: Objectives
Provide Summary of Changes from 503x0b2

## Slide 3: General Changes
TDM Header
  New CLASSIFICATION keyword
TDM Metadata
  New PREVIOUS_MESSAGE_ID
  New NEXT_MESSAGE_ID
  New TDM_BASIS
  New TDM_BASIS_ID
  New ODM_MSG_LINK_n
  New ADM_MSG_LINK_n
  New PRM_MSG_LINK_n
  New RDM_MSG_LINK_n
  New CDM_MSG_LINK_n
  Update EPHEMERIS_NAME_n (metadata) to mention preference for use of ODM
  Update START_TIME to mention use with the addition of real-time tracking data
  Update STOP_TIME to mention use with the addition of real-time tracking data
  New TIME_UNCERTAINTY

## Slide 4: Up the number of participants to 9 and Include support for relay tracking
Changes to 3.3.1.11 to up participant and support relay tracking
PARTICIPANT_n (metadata) index updated (and other associated keywords)
Update MODE (metadata)
Update PATH_m (metadata)
Update to metadata TRANSMIT_BAND_n, RECEIVE_BAND_n, TURNAROUND_NUMERATOR_n, TURNAROUND_DENOMINATOR_n
New section 3.3.2.4 describing the new “RELAY” mode.
Update text in 3.3.2.5.4 (formerly 3.3.2.4.4) to reflect 9 participants
Update 3.3.2.7 (formerly 3.3.2.6) to consider angles provided by other participants that are not the final participant.
Data keyword ANGLE_1 and ANGLE_2 changed to ANGLE_1_n and ANGLE_2_n, to enable providing angles from different PARTICIPANTS
Update (example) Figure G 23: TDM Example: Use of Doppler Counts  Figure G 23: TDM Example: Use of RECEIVE_PHASE_CT and Relay Mode

## Slide 5: Addition of Data Quality Indicators in the Data Section
Updated DATA_QUALITY keyword to enable data quality indicators within the data section.
Updated Table 3-4 to include the indicators into the “Tracking Data Record Generic Format”
Modified 3.4.3 and 3.4.4 to include the new quality indicator element
Data keyword section: Added Data Quality Indicator Symbols
Modified 4.2.5 to include KVN support for the quality indicators
Modified 5.3.8.2 and 5.3.8.3 to include XML support for quality indicators

## Slide 6: Correction Keywords Functionality (Updates)
Replaced CORRECTION_ABERRATION_YEARLY with CORRECTION_ABERRATION_YEARLY_ANGLE_1 and CORRECTION_ABERRATION_YEARLY_ANGLE_2
Replaced CORRECTION_ABERRATION_DIURNAL with CORRECTION_ABERRATION_ DIURNAL _ANGLE_1 and CORRECTION_ABERRATION_ DIURNAL _ANGLE_2
Updated (example) Figure G 22: TDM Example: Use of ‘TRACK_ID’  to add per-angle aberration corrections
New CORRECTIONS_ORDER_n keyword  functionality to provide CORRECTION updates in the Data Section
  Update CORRECTION_APPLIED keyword
  Update section 3.4.15.2 and 3.4.15.3 to support dynamical corrections in the data section.
  New Data Keyword CORRECTIONS_n
  New (example) Figure G 24: TDM Example: Use of dynamically updated data correction values
Provided definitions to CORRECTION_* keywords
  See document for definitions
Update 3.5.9.2 to mention that corrections keyword must come in before the first data points (or at the same time); and may not be needed if corrections are applied to data.
  Enabled the use of short keyword names

## Slide 7: CORRECTION Definitions
New CORRECTION_TIMETAG_k (adding _k) represents a correction time value in seconds (real number) that applies to each timetag in the data section, provides possibility to differentiate between transmit and receive timetags
New CORRECTIONS_ORDER_n provide order of corrections provided in the data section
New CORRECTION_TIMETAG_OBS_k for defining relevant observables for timetag corrections
CORRECTION_RECEIVE considered obsolete, but maintained for backwards compatibility
CORRECTION_TRANSMIT considered obsolete, but maintained for backwards compatibility

## Slide 8: Optical Tracking Support Updates
Update PARTICIPANT_n (metadata)
New RCS_MIN (metadata)
New RCS_MAX (metadata)
Included RCS_MIN and RCS_MAX under the new SYSTEM_CONFIG keyword
Update 3.5.2.8 (former 3.5.2.11)
New ANGLE_RATE_1 and ANGLE_RATE_2 (data) keywords.
New OBSERVATION_COVARIANCE (data) keyword, which can be used for other types of tracking support
Update MAG (data) keyword: updated to include “stellar magnitudes” and error value “-999”.
New (data) Keywords: MAG_UNCERTAINTY, ASTRONOMIC_STAR_COUNT, PHOTOMETRIC_STAR_COUNT, PHOTOMETRIC_SNR, FRAME_LIMITING_BRIGHTNESS
New (example) Figure G 20: TDM Example: Ground Based Optical Tracking with Magnitude
New functionalities under SYSTEM_CONFIG and SYSTEM_STATUS keywords
Note: MAG_UNCERTAINTY  The uncertainty shall be expressed as a Poisson second moment in photon flux units (photons/m**2/sec ), as the errors more closely follow a normal distribution.

## Slide 9: New SYSTEM_CONFIG and SYSTEM STATUS functionalities
Added SYSTEM_CONFIG_n section in metadata As a mechanism to add needed additional items in support of precision tracking.
  New 3.3.1.14  Included a section that describes the use of the SYSTEM_CONFIG keywords and the associated parameters that can be provided with it.
Added SYSTEM_STATUS_n section in data As a mechanism to add needed additional items in support of precision tracking.
  New 3.5.9.8  Included a section that describes the use of the SYSTEM_STATUS keywords and the associated parameters that can be provided with it.

## Slide 10: SYSTEM_CONFIG and SYSTEM_STATUS Examples
SYSTEM_CONFIG_1_START
  Front_End_ID=GRA43245
  System_Mode=SA
  System_Path=Pol1_UC2
  TFR_ID=2
  Exposure_Time=0.453
  Absorption_Normalization_Applied=YES
SYSTEM_CONFIG_1_STOP
SYSTEM_STATUS_1_START
  Aperture_Filter = 2023-09-03T23:43:56.000 NONE
  System_Temperature = 2023-09-03T23:43:56.000 294.5
SYSTEM_STATUS_1_STOP

## Slide 11: SYSTEM_CONFIG Parameters Included
‘Front_End_ID’=<identifier> [Precision tracking]
‘System_Mode’=<mode> [Relay tracking]
‘System_Path’=<path> [Precision tracking]
‘TFR_ID’=<identifier> [Precision tracking]
‘Exposure_Time’=<time> [Optical tracking]
‘Absorption_Normalization_Applied’=<YES or NO> [Optical tracking]
‘Normalization_Distance’=<distance> [Optical tracking]
‘Normalization_Phase_Angle’=<angle> [Optical tracking]
‘Astrometry_Catalogue’=<identifier> [Optical tracking]
‘Photometry_Catalogue’=<identifier> [Optical tracking]
‘RCS_MIN’=<value> [Optical tracking]
‘RCS_MAX’=<value> [Optical tracking]
‘Sensor_Offset’=<X, Y, Z> [Precision tracking]
‘Obs_Granularity=<OBS>,<value> [Precision tracking, late addition]

## Slide 12: SYSTEM_STATUS Parameters Included
  ‘PN_Status’=<Lock, Sync, Search> [radiometric ranging]
  ‘Carrier_Status’=<Lock, Acq, Search> [radiometric tracking]
  ‘Range_Quality_Factor’=<0.0 to 1.0> [radiometric ranging]
  ‘Signal_SNR’=<dBHz> [radiometric tracking]
  ‘Aperature_Filter’=<NONE, JOHNSON B, SLOAN z> [optical tracking]
  ‘Aperature_Filter_Zero_Pt’=<[values]> [optical tracking]
  ‘System_Temperature’=<value> [radiometric tracking]
  ‘Beamformer_Bias’=<bias> [relay tracking]
  ‘Beamformer_Noise’=<noise> [relay tracking]
  ‘Pointing_Mode’=<AUTOTRACK, PROGRAM, MANUAL, LOCKED>[Angle tracking]
  ‘Range_Calibration’=<yes or averaged cals> [Precision tracking]
  ‘RECEIVE_PHASE_CT_Rollover’=<yes or no> [radiometric tracking]
  ‘TRANSMIT_PHASE_CT_Rollover’=<yes or no> [radiometric tracking]
  ‘Wind_Speed’=<km/h> [weather, awareness]
  ‘Wind_Direction=<deg from North> [weather, awareness]

## Slide 13: Removed DOPPLER_COUNT as an observable
Ported functionalities for DOPPLER_COUNT_BIAS, DOPPLER_COUNT_SCALE to new keywords: RECEIVE_PHASE_CT_BIAS and RECEIVE_PHASE_CT_SCALE.
Moved DOPPLER_COUNT_ROLLOVER functionality to SYSTEM_STATUS  PHASE_CT_Rollover parameter
Removed DOPPLER_COUNT from data keywords
Updated data keyword RECEIVE_PHASE_CT_n to include support for the above items formerly provided with DOPPLER_COUNT.
Update (example) Figure G 23: TDM Example: Use of Doppler Counts  Figure G 23: TDM Example: Use of RECEIVE_PHASE_CT and Relay Mode
Added the details of assumptions for DOPPLER_COUNT support to Annex F

## Slide 14: Added Real-time Tracking Support
Update 3.3.1.7
New 3.3.1.12  Explanation of mechanism for support of real-time tracking support
Update TRACK_ID (metadata)  To include new function for real-time tracking
New TRACK_ID_SEGMENT (metadata)  Sequential Increment counter
New (example) Figure G 23: TDM Example: Use of TRACK_ID in multiple segments  real-time tracking support

## Slide 15: Frequency Difference of Arrival (FDOA) and Time Difference of Arrival (TDOA) Support
New DIFF_FREQ data keyword introduced to support FDOA
Updated text to 3.3.2.6.1 (former 3.3.2.5.1), 3.3.2.6.5 (former 3.3.2.5.5) to include differenced frequency support
Updated 3.3.2.6.8 (former 3.3.2.5.8) to include DOR outside of “Delta-DOR”
New Example (Figure G-27) includes single differenced mode use

## Slide 16: Other General Corrections and Comments

## Slide 17: Corrections to language or inconsistencies
Reduce the mentions of reliance on ICD, mostly using the text from the ODM: “pre-coordinated between exchanging entities by mutual agreement”
1.3.4.2  dBHz: decibels referenced to the noise within one Hz bandwidth
3.3.1.9  …The ‘n’ in the keyword is an indexer. The indexer shall start at 1 and not be the same for any two participants in a given Metadata Section.
INTEGRATION_INTERVAL  Enabled use for this keyword in both ranging and Doppler type measurements.
FREQ_OFFSET  Enabled the use of this keyword for the following data types in addition to RECEIVE_FREQ: RECEIVE_PHASE_CT, TRANSMIT_FREQ, TRANSMIT_PHASE_CT
TRANSMIT_DELAY_n and RECEIVE_DELAY_n  Clarification: “If the user wishes to convey a ranging transponder delay, then one half of the transponder delay should be specified via the TRANSMIT_DELAY_n keyword, unless an associated transponder transmit delay is known.”
Updated text in 3.3.2.5.3 (formerly 3.3.2.4.3) to reflect an actual 4-way path. From ‘PATH=1,2,3,4’ to ‘PATH=1,2,3,4,5’.
Added clarifying text to 3.4.6 to explain that XML does not have explicit DATA_START and DATA_STOP keywords.
Data keyword TRANSMIT_PHASE_CT: corrected typo referencing incorrect keyword.

## Slide 18: Addressing Comments (1 of 2)
Metadata keyword INTERPOLATION_DEGREE  Added explanation: This is for recreation of the forward transmit frequency under forward Doppler compensation (know in DSN as ramped data).
Added linear interpolation algorithm to annex F. Other methods not been implemented
Conditional vs Normative / Examples  Transitioned to include definition of “conditional”, in line with other NavWG docs.
Data keyword DOPPLER_INSTANTANEOUS  Clarified that a value in km/s is inherently not a “Doppler” measurement, but rather an estimation of range-rate potentially based on a Doppler measurement.
Update PARTICIPANT_n description to adjust wording to cover tracking scenarios beyond RF links, e.g. visual
Update keyword DOPPLER_INTEGRATED to clarify that a value in km/s is inherently not a “Doppler” measurement, but rather an estimation of range-rate potentially based on a Doppler measurement.

## Slide 19: Addressing Comments (2 of 2)
Update 3.5.2.7.2 (former 3.5.2.10.2) to reflect that positive Doppler definition in the document corresponds to a S/C moving away in the line-of-sight.
4.3.10  Not using TIME_SYSTEM for all keywords, but changed “shall” to “should” statements for values outside the data section.
Updated Annex E2 (former Annex G2) to include the latest tracking data principles
Revised the exclusion of laser ranging and all other exclusions, to be less prescriptive
Re-ordered annexes to align with other NavWG documents

## Slide 20: Tracking Data Principles (Spring 2023) by priority
The TDM standard provides a format to exchange tracking data (and associated parameters) between space organizations.
The TDM shall seek to minimize the need for development of non-standard conventions or extensive ICD arrangements.
The TDM standard shall progressively accommodate new tracking data types or sensor phenomenologies that may become prevalent for space object tracking or navigation. The standard must be extensible, while maximizing backwards compatibility.
Every tracking instrument should have a defined reference location and orientation that could be defined in the ODM and ADM format. This reference location should not depend on the observing geometry. If the reference location changes, the format should provide an avenue to convey the changes.
The time-tags of the tracking data should reflect the best estimate of the transmit/receive time at the instrument reference location.
The TDM standard should allow for corrections of observables, such as media corrections, biases, or as derived from path delay calibrations.
The data conveyed in a TDM should be as independent of the equipment that was used to perform the tracking as possible, while maintaining the integrity of the observations.
Corrections applicable to the data should be agreed by the service provider and the customer.
The TDM standard should minimize the keywords needed to represent equivalent observables. The observables’ units should provide flexibility to most closely represent the native system implementation.