## Slide 1: Packet Distribution Service
Proposal for new MO Service
Roger Thompson ESA

## Slide 2: Proposed MO Packet Distribution Service
IOAG Catalog 3 calls for a Telemetry Packet Distribution Service
  Ground-based
  Across Space Internet / DTN
CCSDS-CSS provides Space Link Extension from TT&C Ground Station Network to a Mission Control Centre (prime or back-up), but not subsequent distribution of selected packets to multiple users
Use Cases for forwarding selected Packets to multiple destinations:
  Forwarding payload data to Payload Data Processing facilities
  Forwarding science data to PIs
  Forwarding telemetry for Hosted Payloads
  Forwarding selected packets to partner Agencies
  Forwarding subsystem/payload data to Manufacturers for performance/anomaly analysis
  Forwarding selected packets to specialised multi-mission systems for Spacecraft Navigation, Mission Planning, Operations Preparation or Long-term Data Archiving
  Forwarding encrypted packets to Secure Facilities

## Slide 3: Scope of Packet Distribution Service
Mission Control
TT&C Network
Spacecraft
Payload Control
Payload Data Processing
Secure Operations
PIs / Users
Data Archive
Navigation Services
Spacecraft Manufacturer
SLS Space Link
CSS Space Link Extension
CCSDS Telemetry Packets
CCSDS MO Packet Distribution
SSI Router
SSI Router
SSI Router

## Slide 4: Scope of Packet Distribution Service
Traditional Space Link Deployments:
  CCSDS Packets used over SLS to Ground Station
  CSS Space Link Extension used to MCC
  MCC provides terrestrial MO Packet Distribution Service to potentially multiple consumers: PIs / Users; Payload Control; Payload Data Processing; Secure Operations; Data Archives; Navigation Services or Spacecraft Manufacturers
Future Space System Internet (SSI) Deployments:
  SIS SSI Routers located in Space Segment Assets; Ground Stations and MCC facilities provide delay-tolerant internet connectivity
  MO Packet Distribution Service can be provided at any node in the network: from MCC as above, or directly from a Space Segment Asset across the DTN.

## Slide 5: Proposed MO Packet Distribution Service
MO M&C Services identified in CCSDS Application Support Layer ADD include Parameter, Action and Alert services – but not a Packet service
  Pattern similar to Parameter service
  Could be included in 5yr update of M&C Service
Scope limited to the streamed distribution of selected CCSDS Packets
Information Model: single class for Packet:
  Reception Timestamp as MAL::Time
  Generation Timestamp as MAL::Time
  Metadata as List<MAL::NameValuePair> (for PUB-SUB subscription criteria)
  Packet as MAL::Blob (binary packet data)
Service Operations
  monitorPacket: subscribe to receive selected subset of Packets
Subscription Criteria:
  Domain of subscribed Packets (hierarchical – e.g. Mission.Spacecraft) is supported as a specific subscription field
  APID
  Packet Type
  Packet SubType
  Packet Structure ID (SID)
  Type, SubType and Packet Structure ID are mission specific criteria, compatible with PUS compliant missions

## Slide 6: monitorPacket Service Operation (PUB-SUB)
PDS
Consumer
Broker
PDS Provider
opt monitorPacket
PUBLISH_REGISTER(List<EntityKey>)
PUBLISH_REGISTER_ACK()
REGISTER(subscriptionID, List<EntityRequest>)
REGISTER_ACK()
*monitorPacket PUBLISH(Packet)
*monitorPacket NOTIFY(Packet)
DEREGISTER(List<subscriptionID>)
DEREGISTER_ACK()
PUBLISH_DEREGISTER()
PUBLISH_DEREGISTER_ACK()
Subscribe
Receive Packets
Unsubscribe
Register
Publish Packets
Deregister
Forward Packets, subject to Subscription Criteria
Subscription Criteria: APID, Type, SubType, SID
Metadata: APID, Type, SubType, SID