## Slide 1: Packet Distribution Service
Proposal for new MO Service
Roger Thompson ESA

## Slide 2: Proposed MO Packet Distribution Service
IOAG Catalog 3 calls for a Telemetry Packet Distribution Service
  Ground-based
  Across Space Internet / DTN
Use Cases for forwarding selected Packets to multiple destinations:
  Forwarding payload data to Payload Data Processing facilities
  Forwarding science data to PIs
  Forwarding telemetry for Hosted Payloads
  Forwarding selected packets to partner Agencies
  Forwarding subsystem/payload data to Manufacturers for performance/anomaly analysis
  Forwarding selected packets to specialised multi-mission systems for Spacecraft Navigation, Mission Planning, Operations Preparation or Long-term Data Archiving
  Forwarding encrypted packets to Secure Facilities
  Consolidation of Packets by MCC prior to distribution

## Slide 3: Scope of Packet Distribution Service
Mission Control
TT&C Network
Spacecraft
Payload Control
Payload Data Processing
Secure Operations
PIs / Users
Data Archive
Navigation Services
Spacecraft Manufacturer
SLS Space Link
CSS Space Link Extension
CCSDS Telemetry Packets
CCSDS MO Packet Distribution
SSI Router
SSI Router
SSI Router

## Slide 4: Potential Use of SLE and Limitations
CCSDS-CSS provides Space Link Extension from TT&C Ground Station Network to a Mission Control Centre
  Can support multiple connections
SLE Limitations:
  Unconsolidated Packet Stream: MCC performs consolidation of multiple passes and of Live/Recorded TM
  Requires Consumer to be aware of TT&C contact schedule (which TT&C station and when in contact)
  Packets filtered by Virtual Channel only
  Return path to Spacecraft (Forward CLTU) restricted to two connections only (prime or back-up)
MO PDS Advantages:
  Allows for more Packet filtration options
  Packet Distribution Provider can be MCC or any node in the network
  Provision of consolidated TM packet stream
  Consumer knowledge of TT&C contact schedule not required
  Can be deployed across Space Internet/DTN

## Slide 5: Scope of Packet Distribution Service
Traditional Space Link Deployments:
  CCSDS Packets used over SLS to Ground Station
  CSS Space Link Extension used to MCC
  MCC provides terrestrial MO Packet Distribution Service to potentially multiple consumers: PIs / Users; Payload Control; Payload Data Processing; Secure Operations; Data Archives; Navigation Services or Spacecraft Manufacturers
Future Space System Internet (SSI) Deployments:
  SIS SSI Routers located in Space Segment Assets; Ground Stations and MCC facilities provide delay-tolerant internet connectivity
  MO Packet Distribution Service can be provided at any node in the network: from MCC as above, or directly from a Space Segment Asset across the DTN.

## Slide 6: Proposed MO Packet Distribution Service
MO M&C Services identified in CCSDS Application Support Layer ADD include Parameter, Action and Alert services – but not a Packet service
  Pattern similar to Parameter service
  Could be included in 5yr update of M&C Service
Scope limited to the streamed distribution of selected CCSDS Packets
Information Model: single class for Packet:
  Reception Timestamp as MAL::Time
  Generation Timestamp as MAL::Time
  Metadata as List<MAL::NameValuePair> (for PUB-SUB subscription criteria)
  Packet as MAL::Blob (binary packet data)
Service Operations
  monitorPacket: subscribe to receive selected subset of Packets
Subscription Criteria:
  Domain of subscribed Packets (hierarchical – e.g. Mission.Spacecraft) is supported as a specific subscription field
  APID
  Mission-specific Metadata parameters
  ECSS PUS Profile would include Packet Type, SubType and Structure ID as standard metadata parameters

## Slide 7: monitorPacket Service Operation (PUB-SUB)
PDS
Consumer
Broker
PDS Provider
opt monitorPacket
PUBLISH_REGISTER(List<EntityKey>)
PUBLISH_REGISTER_ACK()
REGISTER(subscriptionID, List<EntityRequest>)
REGISTER_ACK()
*monitorPacket PUBLISH(Packet)
*monitorPacket NOTIFY(Packet)
DEREGISTER(List<subscriptionID>)
DEREGISTER_ACK()
PUBLISH_DEREGISTER()
PUBLISH_DEREGISTER_ACK()
Subscribe
Receive Packets
Unsubscribe
Register
Publish Packets
Deregister
Forward Packets, subject to Subscription Criteria
Subscription Criteria: APID, Type, SubType, SID
Metadata: APID, Type, SubType, SID

## Slide 8: Open Points
Publication of Packet Distribution Service:
  Inclusion in MO M&C Services Blue Book (update required anyway for MO v2)
  Publication as stand-alone Blue Book
Potential support for TM Frames:
  Would cater for Frame level Encryption
Potential inclusion of Packet Retrieval based on specified time period (T1-T2)
  Additional one-shot “Get” Operation (Progress with multiple returns, not PubSub). Request includes Filter Options as before, but with the addition of the time range.
  Note filtering must be handled by the Provider, not the Broker. Alternative is PubSub with a “Replay” session managed by additional operations.
  If included for TM Packets, should this facility also be extended to other M&C Objects: Parameters, Actions and Alerts.