Recommendation for Space Data System Standards

Mission Operations Message Abstraction Layer

Recommended Standard

CCSDS 521.0-B-3

Blue Book

April 2022

AUTHORITY

|  | Issue: | Recommended Standard, Issue 2 |  |
| --- | --- | --- | --- |
|  | Date: | April 2022 |  |
|  | Location: | Washington, DC, USA |  |

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems, and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

STATEMENT OF INTENT

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than three years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. CCSDS shall not be held responsible for identifying any or all such patent rights.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-3).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- CSIR Satellite Applications Centre (CSIR)/Republic of South Africa.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 521.0-B-1 | Mission Operations Message Abstraction Layer, Recommended Standard, Issue 1 | October 2010 | Original issue (superseded) |
| CCSDS 521.0-B-2CCSDS 521.0-B-3 | Mission Operations Message Abstraction Layer, Recommended Standard, Issue 2 | March 2013 | Updates: addresses the request to add a slight restriction to the MAL data model regarding polymorphism; adds ability to use external data type specifications such as XML Schemas; moves XML to the SANA registry; changes type short forms to integers rather than strings; shows optional fields in composites; changes lists to a template rather than explicit types; adds unsigned integer and File data types. |
| CCSDS 521.0-B-3 | Mission Operations Message Abstraction Layer, Recommended Standard, Issue 3 | November 2021 | Current issue. The following updates were performed: clarifies/updates polymorphism restrictions. updates the subscription keys for PUBSUB operations; simplified the MessageHeader introduced the MO Object data type Added new data structures for support to services. |

NOTE	–	Changes from the original issue are too numerous to permit markup.

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	General	1-1

1.2	Purpose and Scope	1-1

1.3	Document structure	1-1

1.4	Definition of Terms	1-2

1.5	NOMENCLATURE	1-4

1.6	References	1-4

2	Overview	2-1

2.1	General	2-1

2.2	Abstract Interface Specifications	2-1

2.3	Abstract Service Specifications	2-8

3	Abstract Service Specifications	3-1

3.1	Overview	3-1

3.2	Transaction handling	3-1

3.3	State transitions	3-1

3.4	Message Composition	3-2

3.5	MAL Service Interface	3-4

3.6	Access Control Interface	3-97

4	MAL Data Type Specification	4-2

4.1	Overview	4-2

4.2	Fundamentals	4-10

4.3	MO Objects	4-11

4.4	Attributes	4-13

4.5	Data Structures	4-6

5	MAL Errors	5-1

6	Service Specification XML	6-1

7	Conformance Matrix	7-1

ANNEX A	Protocol Implementation Conformance  Statement (PICS) Proforma (Normative)	B-1

ANNEX B SECURITY, SANA and patent considerations  (Normative)	B-4

ANNEX C Definition of Acronyms  (INFORMATIVE)	C-1

ANNEX D Informative References  (Informative)	D-1

# CONTENTS (continued)

Figure	Page

2-1	Message Exchange Sequence Example	2-2

2-2	Request, Indication, and Message Relationship	2-4

2-3	Consumer State Diagram Example	2-5

2-4	Message Decomposition Key	2-7

2-5	Message Header Decomposition Example	2-7

2-6	Message Body Decomposition Example	2-7

3-1	SEND Interaction Pattern Message Sequence	3-4

3-2	SUBMIT Interaction Pattern Message Sequence	3-8

3-3	SUBMIT Interaction Pattern Error Sequence	3-9

3-4	SUBMIT Consumer State Chart	3-10

3-5	SUBMIT Provider State Chart	3-11

3-6	REQUEST Interaction Pattern Message Sequence	3-16

3-7	REQUEST Interaction Pattern Error Sequence	3-17

3-8	REQUEST Consumer State Chart	3-18

3-9	REQUEST Provider State Chart	3-19

3-10	INVOKE Interaction Pattern Message Sequence	3-24

3-11	INVOKE Interaction Pattern Error Sequence	3-25

3-12	INVOKE Consumer State Chart	3-27

3-13	INVOKE Provider State Chart	3-28

3-14	PROGRESS Interaction Pattern Message Sequence	3-36

3-15	PROGRESS Interaction Pattern Error Sequence	3-37

3-16	PROGRESS Consumer State Chart	3-39

3-17	PROGRESS Provider State Chart	3-41

3-18	PUBLISH-SUBSCRIBE Interaction Pattern Message Sequence	3-53

3-19	PUBLISH-SUBSCRIBE Pattern Alternative Message Sequence	3-54

3-20	PUBLISH-SUBSCRIBE Interaction Pattern Consumer Error Sequence	3-58

3-21	PUBLISH-SUBSCRIBE Interaction Pattern Provider Error Sequence	3-59

3-22	PUBLISH-SUBSCRIBE Consumer State Chart	3-65

3-23	PUBLISH-SUBSCRIBE Broker to Consumer State Chart	3-67

3-24	PUBLISH-SUBSCRIBE Provider State Chart	3-69

3-25	PUBLISH-SUBSCRIBE Broker to Provider State Chart	3-71

3-26	CHECK Access Control Pattern Message Sequence	3-97

3-27	CHECK Access Control Pattern Error Sequence	3-98

# CONTENTS (continued)

Table	Page

2-1	Example Operation Template	2-3

2-2	Example Primitive List	2-4

2-3	Service Overview Table	2-8

3-1	MAL Message Header Fields	3-3

3-2	SEND Operation Template	3-5

3-3	SEND Primitive List	3-5

3-4	SEND Message Header Fields	3-7

3-5	SUBMIT Operation Template	3-9

3-6	SUBMIT Primitive List	3-10

3-7	SUBMIT Message Header Fields	3-13

3-8	Submit ACK Message Header Fields	3-14

3-9	REQUEST Operation Template	3-17

3-10	REQUEST Primitive List	3-18

3-11	REQUEST Message Header Fields	3-21

3-12	Request RESPONSE Message Header Fields	3-22

3-13	INVOKE Operation Template	3-26

3-14	INVOKE Primitive List	3-26

3-15	INVOKE Message Header Fields	3-30

3-16	Invoke ACK Message Header Fields	3-31

3-17	Invoke RESPONSE Message Header Fields	3-33

3-18	PROGRESS Operation Template	3-38

3-19	PROGRESS Primitive List	3-38

3-20	PROGRESS Message Header Fields	3-44

3-21	Progress ACK Message Header Fields	3-45

3-22	Progress UPDATE Message Header Fields	3-47

3-23	Progress RESPONSE Message Header Fields	3-50

3-24	PUBLISH-SUBSCRIBE Operation Template	3-60

3-25	PUBLISH-SUBSCRIBE Register Operation Template	3-60

3-26	PUBLISH-SUBSCRIBE Publish Register Operation Template	3-61

3-27	PUBLISH-SUBSCRIBE Publish Operation Template	3-61

3-28	PUBLISH-SUBSCRIBE Publish Error Operation Template	3-62

3-29	PUBLISH-SUBSCRIBE Notify Operation Template	3-62

3-30	PUBLISH-SUBSCRIBE Notify Error Operation Template	3-63

3-31	PUBLISH-SUBSCRIBE Deregister Operation Template	3-63

3-32	PUBLISH-SUBSCRIBE Publish Deregister Operation Template	3-63

3-33	PUBLISH-SUBSCRIBE Primitive List	3-64

3-34	REGISTER Message Header Fields	3-74

3-35	REGISTER_ACK Message Header Fields	3-75

3-36	PUBLISH_REGISTER Message Header Fields	3-78

3-37	PUBLISH_REGISTER_ACK Message Header Fields	3-79

3-38	PUBLISH Message Header Fields	3-83

3-39	PUBLISH_ERROR Message Header Fields	3-84

3-40	NOTIFY Message Header Fields	3-86

3-41	DEREGISTER Message Header Fields	3-89

3-42	DEREGISTER_ACK Message Header Fields	3-91

3-43	PUBLISH_DEREGISTER Message Header Fields	3-92

3-44	PUBLISH_DEREGISTER_ACK Message Header Fields	3-94

3-45	CHECK Operation Template	3-99

3-46	CHECK Primitive List	3-99

3-47	Object Identity Fields	4-12

5-1	Standard MAL Error Codes	5-1

7-1	Conformance Matrix	7-1

# Introduction

## General

This Recommended Standard defines the Mission Operations (MO) Message Abstraction Layer (MAL) in conformance with the service framework specified in reference [D1], Mission Operations Services Concept.

The MO MAL is a framework that provides generic service patterns to the Mission Operation services defined in reference [D1]. These Mission Operations services are defined in terms of the MAL.

## Purpose and Scope

This Recommended Standard defines, in an abstract manner, the MAL in terms of:

- the concepts that it builds upon;

- the basic types it provides;

- the message headers required by the layer;

- the relationship between, and the valid sequence of, the messages and resulting behaviours.

It does not specify:

- individual implementations or products;

- the implementation of entities or interfaces within real systems;

- the methods or technologies required for communications.

## Document structure

This Recommended Standard is organised as follows:

- section 1 provides purpose and scope, and lists definitions, conventions, and references used throughout the Recommended Standard;

- section 2 presents an overview of the concepts;

- section 3 specifies the interaction patterns used to define services;

- section 4 is a formal specification of the MAL data structures;

- section 5 is a formal specification of the MAL errors;

- section 6 is the formal service specification Extensible Markup Language (XML) schema;

- section 8 is the formal compliance requirements of the MAL.

## Definition of Terms

Software Component (component): A software unit containing the business function. Components offer their function as Services, which can either be used internally or which can be made available for use outside the component through Provided Service Interfaces. Components may also depend on services provided by other components through Consumed Service Interfaces.

Service: A set of capabilities that a component provides to another component via an interface. A Service is defined in terms of the set of operations that can be invoked and performed through the Service Interface. Service specifications define the capabilities, behaviour, and external interfaces, but do not define the implementation.

Service Interface: A set of interactions provided by a component for participation with another component for some purpose, along with constraints on how they can occur. A Service Interface is an external interface of a Service where the behaviour of the Service Provider Component is exposed. Each Service will have one defined ‘Provided Service Interface’, and may have one or more ‘Consumed Service Interface’ and one ‘Management Service Interface’.

Provided Service Interface: A Service Interface that exposes the Service function contained in a component for use by Service Consumers. It receives the MAL messages from a Consumed Service Interface and maps them into API calls on the Provider component.

Consumed Service Interface: The API presented to the consumer component that maps from the Service operations to one or more Service Data Units(s) contained in MAL messages that are transported to the Provided Service Interface.

Management Service Interface: A Service Interface that exposes management functions of a Service function contained in a component for use by Service Consumers.

Area: An Area marks the functional context of a group of related services. It is used as a taxonomy means for grouping a set of related services and data. Examples of Areas are Monitoring and Control, Mission Planning, Telerobotics, Navigation, Automation.

Domain: A means of applying hierarchical taxonomy to mission operation related data and messages. The term domain is used with different meanings in specific mission and deployment scenarios, in order to be able to distinguish between data and message from different sources. For instance in a constellation, the domain may be used to distinguish the data from individual spacecrafts of the constellation. In a different context the domain may be used to distinguish between different applications, subsystems, and payloads.

Object: Objects are representations of complex data types with two specific characteristics: Objects have a unique and an immutable identity and can be referenced unambiguously. Objects are used to represent and formally specify the complex data model in service specifications. Section 4.3 provides a detailed definition and explanation of the MO Object and its characteristics.

Service Provider (provider): A component that offers a Service to another by means of one of its Provided Service Interfaces.

Service Consumer (consumer): A component that consumes or uses a Service provided by another component. A component may be a provider of some Services and a consumer of others.

Service Data Unit (SDU): A unit of data that is sent by a Service Interface, and is transmitted semantically unchanged, to a peer Service Interface.

Binding: The access mechanism for a Service. Bindings are used to locate and access Service Interfaces. Services use bindings to describe the access mechanisms that consumers have to use to call the Service. The binding specifies unambiguously the protocol stack required to access a Service Interface. Bindings may be defined statically at compile time or they may use a variety of dynamic run-time mechanisms (DNS, ports, discovery).

Service Capability Set: A grouping of the service operations that remains sensible and coherent, and also provides a Service Provider with an ability to communicate to a Consumer its capability.  The specification of services is based on the expectation that different deployments require different levels of complexity and functionality from a service. To this end a given service may be implementable at one of several distinct levels, corresponding to the inclusion of one or more capability sets.

Service Connection (connection): A communications connection between a Consumed Service Interface and a Provided Service Interface over a specific Binding.  When a component consumes the services of a provider component, this link is known as a Service Connection (connection).

Service Extension: Addition of capabilities to a base Service.  A Service may extend the capabilities of another Service with additional operations. An extended Service is indistinguishable from the base Service to consumers such that consumers of the base Service can also be consumers of the extended Service without modification.

Broker: In a publish-subscribe interaction pattern, the broker acts as an intermediary component and decouples the publishers of messages from the subscribers.

## NOMENCLATURE

The following conventions apply throughout this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

## References

The following documents contain provisions which, through reference in this text, constitute provisions of this Recommended Standard.  At the time of publication, the editions indicated were valid.  All documents are subject to revision, and users of this Recommended Standard are encouraged to investigate the possibility of applying the most recent editions of the documents indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS Recommended Standards.

[1]	Mission Operations Reference Model.  Recommendation for Space Data System Standards, CCSDS 520.1-M-1.  Magenta Book.  Issue 1.  Washington, D.C.: CCSDS, July 2010.

[2]	“MIME Media Types.”  Internet Assigned Numbers Authority.  http://www.iana.org/assignments/media-types.

[3]	IEEE Standard for Floating-Point Arithmetic (IEEE STD 754-2019), IEEE Computer Society, 2019-07-22.

[4]	The Unicode® Standard, Version 14.0 – Core Specification, The Unicode Consortium (ISBN 978-1-936213-29-0), Published in Mountain View, CA, September 2021.

[5]	“Uniform Resource Identifier (URI): Generic Syntax” (RFC 3986), Berners-Lee, et al., W3C/MIT, January 2005.

[6]	“XML Media Types” (RFC 7303), H. Thompson & C. Lilley, W3C, July 2014.

[7]	Space Assigned Numbers Authority (SANA). https://sanaregistry.org/

NOTE	–	Informative references are listed in annex D.

# Overview

## General

The MO service specifications detail a standard set of services. These services form a contract between a consumer of a service and the provider of that service. Each operation of a service has a set behaviour: a message is sent from the consumer to the provider to instigate the operation, and zero or more messages can be exchanged thereafter depending on the specific pattern and operation. This set of messages, and the pattern in which they are exchanged, needs to be defined for each operation of each service.

An interaction pattern details a standard exchange pattern that removes the need for each operation to detail its exchange pattern individually. By defining a pattern and stating that a given operation is defined in terms of that pattern, the operation definition can focus on the specifics of that operation and rely on the standard pattern to facilitate the interaction.

The MAL defines this set of standard interaction patterns as an abstract interface that is used by the MO services. There are two abstract interfaces defined in the MAL specification: the first is the abstract interface of the MAL that is presented to the higher layers, and the second is the abstract interface of the Access Control component.

The MO service specifications and the MAL are abstract in their definition; they do not contain any specific information on how to implement them for a particular programming language or transport encoding. In a concrete deployment, e.g. in a system for a particular space mission scenario, moving from the abstract to concrete, it is required to define a Language Mapping that states how the abstract MAL and MO service specifications are to be realised in some specific language: this defines the API in that language. In addition a transport mapping is required that defines the mapping from the abstract MAL data structures into a specific and unambiguous encoding of the messages and to a defined and unambiguous mapping to a specific data transport. It is only when these mappings are defined that is possible to implement services that use the MAL interface and use the transport bindings to exchange data. (For further information on this, see reference [1].)

This document contains the formal specification for these abstract interfaces and the abstract objects that they reference. More information about the MO Concept can be found in reference [D1], and more information about the Reference Model can be found in reference [1].

## Abstract Interface Specifications

### General

Each abstract interface is defined as a set of interaction patterns. For each pattern defined there is a common layout of the document section.

The following subsections describe the sections and diagram formats specific to the interaction patterns.

### Pattern Overview

The overview section of the pattern contains a message exchange sequence, which shows the interaction sequence between a source consumer and a destination provider.

The main aspects to note are the direction of the arrows (giving message direction) and the order of the messages (top down). The bars under the consumer and provider show synchronicity of the message exchange.

In the following example (figure 2-1) it can be seen that the consumer sends an initial message to the provider, which responds with an acknowledgement. The acknowledgment is in response to the initial message, as shown by the connected bars under the consumer and provider.

At some time in the future the provider will send another response:

Figure 2-1:  Message Exchange Sequence Example

Because the pattern shows the response, the consumer can expect it, but because the bars are not connected it is considered to be indeterminate.  This means that although the message will arrive it cannot be determined when arrival will occur. It is important to note that any synchronicity shown is concerned only with messages; it does not imply, or require, a synchronous (blocking) behaviour in either the client or provider, as these are implementation issues.

### Description and Usage

The Description and Usage sections are used to describe the pattern and define the expected usage respectively.

### Error Handling

The Error Handling section defines the positions in the pattern where errors are permitted to be generated. It uses the same sequence diagram notation as the nominal pattern sequence from the Overview section.

### Operation Template

Each interaction pattern definition contains a table that defines the template for operations that use that pattern:

Table 2-1:  Example Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | <<Interaction pattern name>> |
| Pattern Sequence | Message | Type Signature |
| <<Message direction>> | <<Message name>> | <<Message signature*>> |
| … | … | … |

The message direction denotes the direction of the message relative to the provider of the pattern and is either IN or OUT. So all messages directed towards the provider are IN messages, and all messages directed away from the provider are OUT messages. It is expected that message names match those defined in the Primitives section.

Blue cells (dark grey when printed on a monochrome printer) contain table headings, light grey cells contain fields that are fixed for a pattern, and white cells contain values that must be provided by the operation or structure.

The Type Signature column contains the list of types that make up the Body of a particular message and the respective field names. Zero to many types may be listed here and together define the body of the indicated message.

This document defines a data type specification language in section 3.6 that is specified as MAL data types.  The Type Signatures are defined using the MAL data types to define the various base data types, the notation used to describe them, and the rules for their combination into complex data structures. This is separate from the encoding technology used which is responsible for mapping the abstract data type notation from the data type specification into an actual ‘bits and bytes’ representation.

Even though the Body Types in this specification are defined using the MAL data types, any data type specification language (such as XML Schema) may be used in an actual service specification which requires a separate mapping step of abstract data types to real data types and of abstract message exchanges to a real data transport protocol.

### Primitives

Each pattern defines a set of primitives in a table as below:

Table 2-2:  Example Primitive List

Primitive

<<Primitive name>>

For each listed primitive there exists a Request, Message and Indication of the same name. The Requests and Indications are used by the following State Diagrams. Requests are transitions that are triggered by the component being modelled; Indications are transitions that are triggered by an external activity. Messages are the entities that are transferred between the two components to progress the interaction (see figure 2-2).

Figure 2-2:  Request, Indication, and Message Relationship

Therefore a component issues Requests, which cause Messages to be transmitted, which raise Indications in the destination component.

### state Charts

For each defined interaction there can also be specified one or more state diagrams (see figure 2-3). The diagrams define the allowed states and transitions between those states.

Figure 2-3:  Consumer State Diagram Example

The states are those of the MAL of the relevant component and apply to a single instance of a pattern; for example, figure 2-3 shows the allowed states and transitions for a specific pattern on the consumer, but it is the responsibility of the consumer MAL to maintain that state information and reject invalid state transitions.

Note that in a concrete MAL implementation in a given deployment there can be many interactions concurrently occurring. In that case, the MAL implementation would need to be able to track the state of each interaction instance independently.

Figure 2-3 shows the state diagram for the Consumer component from the example in figure 2-1, and includes some error state transitions that are not shown in the example.

### Requests and Indications

#### General

For each pattern there are a set of Requests that can be issued and a set of Indications that can be received. These sets are defined in the Primitives section for the pattern.  The allowed state transitions are defined in the State Charts section for the pattern.

Each pattern defines the following subsections for each primitive.

#### Function

The Function subsection defines the use of a specific Request or Indication.

#### Semantics

The Semantics subsection defines what information is required for the Request or Indication. It is equivalent to the arguments of a programming language function call.

#### When Generated

The When Generated subsection specifies the circumstances that trigger the generation of the Request or Indication.

#### Effect on Reception

The Effect on Reception subsection specifies what the effects of the reception of a Request by a MAL or an Indication by an Application are. Usually for a Request is it the transmission of a Message to the destination and for an Indication it is pattern specific.

#### Message Header

The MAL defines a standard message header that is used to manage the interaction. The Message Header subsection specifies the values of the fields of the Message Header to be used for the message. The subsection can specify all the fields, or only fields that are different from another Request/Indication.

The full definition of the message header structure is provided in 3.4.

### Message Example decompositions

Each pattern is illustrated with an example which shows how each message will look when decomposed into a packet-like structure. It is important to note that the implemented version of such a type of structure is completely dependent on the chosen encoding and transport bindings adopted for each deployment.

Each message is split into up to three parts as presented in figure 2-4. Each message will contain a Message Header, a Standard Pattern Body, and a Service-Specific Body:

Figure 2-4:  Message Decomposition Key

Each message part, is then broken down into its composing fields. For example, the Message Header is decomposed into a set of fields as presented in figure 2-5:

Figure 2-5:  Message Header Decomposition Example

Field values are provided as an example and as such more human-readable values are used rather than numeric equivalents that may be used in highly efficient encodings. The detailed definitions of the message header fields shown in this example are specified in section 3.4.

Figure 2-6 shows an example set of fields for the Standard Pattern Body and Service-Specific Body parts of a message. If more complex structures are being shown (as in figure 2-6), a single field can be part of a more complex structure:

Figure 2-6:  Message Body Decomposition Example

In the example above the ‘Time’ field is part of the ‘Test Notify’ structure.

NOTE	–	The structures used in the body of the examples for each pattern are only examples, and as such no explanation of contained values or meanings is provided or required.

## Abstract Service Specifications

Each abstract service specification includes an overview table that details the Area and Service Identifiers and then lists the operations of that service (see table 2-3).

Table 2-3:  Service Overview Table

| Area Identifier | Service Identifier | Area Number | Service Number | Service Version |
| --- | --- | --- | --- | --- |
| Interaction Pattern | Operation Identifier | Operation Number | Capability Set |

The values of table 2-3 are used to populate the [Service Area][Service][Service Operation][Service Version] fields of the Message Header. The Area Number, Service Number, and Operation Number fields provide an alternative numerical identification scheme parallel to the Identifier scheme.

The choice of whether to use Identifiers, numbers, or another alternative in a concrete transport is transport specific, as long as it is possible to correctly determine the area, service, operation, and version values from the transmitted information. The numbers are expected to be used by transports that require a more efficient identification mechanism than Identifiers, and will not overlap with existing service definitions. The set of permissible values are in the UShort range and start at ‘1’.

The Service Version is a number that is used to differentiate between issues of a service. Initially it will be set to the number ‘1’, and future updates to the service will increase that number. The set of permissible values are in the UOctet range.

The Capability set field is a numerical identifier that holds the Service Capability Set number for that operation. Operations that hold the same Capability Set number within a service specification are considered to be part of the same Service Capability Set. The set of permissible values are in the UShort range.

# Abstract Service Specifications

## Overview

There are two abstract interfaces defined in this specification.  The first is the abstract interface of the MAL. The MAL abstract interface defines the interactions that are presented to the higher layers, the information and interaction between the two interacting components, and also the expected behaviour of the application layer that uses the MAL. It is detailed in 3.5.

The second is the abstract interface of the Access Control component. To support the access control and security aspects of the reference model in reference [1] the MAL requires a standard abstract interface to an Access Control component. The access control component only has the single interaction that is used by the MAL as defined in the Reference Model (reference [1]). The implementation of the Access Control component is deployment specific, as is the security policy and rules to be used; however, the interaction with that component is part of the MAL standard. The concept of the generic Access Control Interface and the delegation of responsibilities is detailed in section 3.6.

General constraints that apply to all patterns are defined in 3.2, 3.3, and 3.4.

## Transaction handling

The message header shall contain a transaction identifier field providing a mechanism for the originating MAL of a message exchange to uniquely identify the response, or set of responses, to a message.

Each instance of a pattern shall be considered a single transaction.

The transaction identifier shall be:

- used by the originating MAL to identify messages in a particular instance of an interaction pattern, and

- returned by the service provider in matching messages (returns from submits, etc.).

The originating MAL shall ensure that the combination of the following Message Header fields form a unique index: pattern type, transaction identifier, the source, the service area, the service, and operation.

## State transitions

Each pattern shall specify the set of states that both the provider and consumer can attain during the execution of the pattern.

To move between the states, each pattern shall define the set of legal transitions either as a Request or an Indication.

For a Request to be issued, the source entity shall be in the correct state.

Issuing a Request when in the incorrect state shall cause an INCORRECT_STATE error to be raised by the local MAL, and the pattern shall end at this point.

For Indications, the receiving entity shall be required to be in the correct state.

Reception of an Indication in a state other than the correct one shall cause an INCORRECT_STATE error to be raised by the local MAL, and the pattern shall end at this point.

## Message Composition

### Message Header field values

The header fields, with the values specified in table 3-1, shall be used for all interaction patterns.

Each interaction pattern may override the values in table 3-1 with values defined in the relevant Request and Indication section for that pattern.

The type of the fields From and To is an Identifier. MAL makes no assumption what type of addressing information is used to indicate the source and destination of MAL messages. For a particular implementation/deployment these fields may contain a URI-formatted text [5], a textual name (such as the name of an Agency) or a number (e.g. indicating an application ID, APID). How these values are used for routing of the messages from the source to destination is deployment and implementation specific and must be specified in outbound agreements such as Interface Control Documents.

The Supplements field may contain a set of optional named values in form of a list of field names and values. MAL does not define any default set of supplement fields. If for a particular deployment, supplements fields are to be used these shall be captured in outbound agreements.

Table 3-1:  MAL Message Header Fields

| Field | Type | Value |
| --- | --- | --- |
| From | Identifier | Message Source |
| Authentication Id | Blob | Authentication Identifier of Message Originator |
| To | Identifier | Message Destination |
| Timestamp | Time | Message generation timestamp |
| Interaction Type | InteractionType | Interaction Pattern Type |
| Interaction Stage | UOctet | Interaction Pattern Stage |
| Transaction Id | Long | Unique to consumer |
| Service Area | UShort | Service Area |
| Service | UShort | Service |
| Operation | UShort | Service Operation |
| Service version | UOctet | Service version |
| Is Error Message | Boolean | ‘True’ if this is an error message; else ‘False’ |
| Supplements | List<NamedValue> | Optional supplementary fields |

### Message Body

The message body shall be composed of the types listed in the Type Signature column of the operation template in a service specification.

Zero to many types may be listed in the Type Signature column, each type being one part of the message body, and together form the complete body of the indicated message.

The listed types should use the MAL data type specification (or service-specific types derived from these) as defined in section 4 of this specification.

How the message body is encoded is dependent on the encoding specification used.

### Error Messages

A service specification shall define which error numbers may be returned for a specific operation and also if any extra information is provided with the error message.

The service specification shall specify the data type of the extra information for the specific error.

A UInteger value containing the Error Number (see section 5) shall immediately follow the Message Header.

The extra information value shall immediately follow the Error Number.

If no extra information is provided by an error, then the extra information value shall be set to NULL.

## MAL Service Interface

### SEND Interaction Pattern

#### Overview

The SEND pattern is the most basic interaction (figure 3-1); it is a single message from the consumer to the provider. No acknowledgement is sent by the provider.

Figure 3-1:  SEND Interaction Pattern Message Sequence

#### Description

The SEND pattern is the basic interaction of which all other patterns can be considered extensions. It is the simple passing of a message from a consumer to a provider. Because there is no message ‘conversation’ implied with a simple SEND, there is no requirement for a transaction identifier in the message.  However, one may be specified.  No return message is sent from the provider to the consumer, so the consumer has no indication the provider has received the message.

#### Usage

The SEND pattern is expected to be used for non-critical messages where the possible loss of one or more of these messages is not considered critical.  An example would be regular heartbeat-type messages.

#### Error Handling

Errors (see section 5) may be generated by the consumer service layers, but no error can be generated by the provider as the interaction pattern does not allow for the provider to return an error.

#### Operation Template

The SEND template only contains the operation name and the type signature containing both the type of the structure and respective field name that is sent as the message body:

Table 3-2:  SEND Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | SEND |
| Pattern Sequence | Message | Type Signature |
| IN | SEND | << Type signature>> |

#### Primitives

Table 3-3:  SEND Primitive List

Primitive

SEND

#### State Charts

##### Consumer Side

The state chart contains only one transition from the initial state to the final one, so it is not represented. This transition is triggered by the primitive SEND Request.

##### Provider Side

The state chart contains only one transition from the initial state to the final one, so it is not represented. This transition is triggered by the primitive SEND Indication.

#### Requests and Indications

##### SEND

###### Function

The SEND Request primitive shall be used by the consumer application to initiate a SEND Interaction.

The SEND Indication primitive shall be used by the provider MAL to deliver a SEND Message to a provider and initiate a SEND Interaction.

###### Semantics

SEND Request and SEND Indication shall provide parameters as follows:

(SEND Message Header, SEND Message Body)

###### When Generated

- A SEND Request may be generated by the consumer application at any time.

- A SEND Indication shall be generated by the provider MAL upon reception of a SEND Message, once checked via the Access Control interface, from a consumer.

###### Effect on Reception

- Reception of a SEND Request shall, once checked via the Access Control interface, cause the consumer MAL to initiate a SEND Interaction by transmitting a SEND Message to the provider.

- The pattern shall end at this point for the consumer.

- On reception of a SEND Indication a provider shall process the operation.

- The pattern shall end at this point for the provider.

###### Message Header

- For the SEND Message the message header fields shall be as defined in 3.4 except for the fields in table 3-4.

- The contents of the SEND Message body, as specified in the operation template, shall immediately follow the message header.

Table 3-4:  SEND Message Header Fields

| Field | Value |
| --- | --- |
| From | Consumer |
| Authentication Id | Consumer Authentication Identifier |
| To | Provider |
| Interaction Type | SEND |
| Interaction Stage | Not used |
| Transaction Id | Not used |

#### Example

The following example shows a simple example service with a single SEND pattern-based operation:

| Operation Identifier | testSend |
| --- | --- |
| Interaction Pattern | SEND |
| Pattern Sequence | Message | Type Signature |
| IN | SEND | TestBody body |

The TestBody structure is defined below:

| Name | TestBody |
| --- | --- |
| Extends | Composite |
| Short Form Part | Example Only |
| Field | Type | Nullable | Comment |
| FirstItem | String | Yes | Example String item |
| SecondItem | Integer | Yes | Example Integer item |

This corresponds to the following message:

NOTE	–	An actual service specification, rather than the example given here, would fully specify the meaning of, and required values of, all structures used by the service.

### SUBMIT Interaction Pattern

#### Overview

The SUBMIT pattern is a simple confirmed message exchange pattern (figure 3-2). The consumer sends a message to a provider and the provider acknowledges it.

Figure 3-2:  SUBMIT Interaction Pattern Message Sequence

The meaning of the return acknowledgement is operation specific.  Each operation specification details the exact meaning of the operation’s return acknowledgement for its context.

#### Description

The SUBMIT pattern extends the SEND pattern by providing a return acknowledgment message from the provider back to the consumer. The service specification details the meaning of the acknowledgment message for a specific operation.

#### Usage

The SUBMIT pattern is used for simple operations that complete quickly but must be confirmed to the consumer.

#### Error Handling

- The return acknowledgment shall be replaced with an error message (see section 5) if an error occurs during the processing of the operation as shown in figure 3-3.

Figure 3-3:  SUBMIT Interaction Pattern Error Sequence

- Either the acknowledgment or the error message shall be returned but never both.

- The service specification shall specify that the acknowledgement is not returned until all processing that can generate an error has been completed, if a service is required to be able to return an error during the processing of the message.

#### Operation Template

The SUBMIT template only contains the operation name and the type signature containing both the type of the structure and respective field name that is submitted as the Submit message body:

Table 3-5:  SUBMIT Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Type Signature |
| IN | SUBMIT | << Type signature>> |

The return acknowledgement message does not have a body to keep the operation as simple as possible.  Because of this it is not shown in the operation template.

NOTE	–	If a service-defined return message is required, for example, to return an identifier for the operation, then the REQUEST pattern should be used instead of the SUBMIT pattern.

#### Primitives

Table 3-6:  SUBMIT Primitive List

Primitive

SUBMIT

ACK

ERROR

#### State Charts

##### Consumer Side

Figure 3-4 shows the consumer side state chart for the SUBMIT pattern:

Figure 3-4:  SUBMIT Consumer State Chart

- The initial transition is triggered by the primitive SUBMIT Request and shall lead to the Initiated State.

- There are two possible transitions from the Initiated State:

- the first is the indication of an acknowledgement, ACK Indication, and shall lead to the final state;

- the second is the indication of an error, ERROR Indication, and shall lead to the final state.

##### Provider Side

Figure 3-5 shows the provider side state chart for the SUBMIT pattern:

Figure 3-5:  SUBMIT Provider State Chart

- The initial transition is triggered by the primitive SUBMIT Indication and shall lead to the Initiated State.

- There are two possible transitions from the Initiated State:

- the first is the transmission of an acknowledgement, ACK Request, and shall lead to the final state;

- the second is the transmission of an error, ERROR Request, and shall lead to the final state.

#### Requests and Indications

##### SUBMIT

###### Function

- The SUBMIT Request primitive shall be used by the consumer application to initiate a SUBMIT Interaction.

- The SUBMIT Indication primitive shall be used by the provider MAL to deliver a SUBMIT Message to a provider and initiate a SUBMIT Interaction.

###### Semantics

SUBMIT Request and SUBMIT Indication shall provide parameters as follows:

(SUBMIT Message Header, SUBMIT Message Body)

###### When Generated

- A SUBMIT Request may be generated by the consumer application at any time.

- A SUBMIT Indication shall be generated by the provider MAL upon reception of a SUBMIT Message, once checked via the Access Control interface, from a consumer.

###### Effect on Reception

- Reception of a SUBMIT Request shall, once checked via the Access Control interface, cause the consumer MAL to initiate a SUBMIT Interaction by transmitting a SUBMIT Message to the provider.

- The consumer MAL shall then enter the Initiated State.

- On reception of a SUBMIT Indication by the provider, the provider MAL shall enter the Initiated State.

- The provider shall then start processing the operation at this point.

###### Message Header

- For the SUBMIT Message the message header fields shall be as defined in 3.4 except for the fields in table 3-7.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-7:  SUBMIT Message Header Fields

| Field | Value |
| --- | --- |
| From | Consumer |
| Authentication Id | Consumer Authentication Identifier |
| To | Provider |
| Interaction Type | SUBMIT |
| Interaction Stage | 1 |
| Transaction Id | Provided by consumer MAL |

##### ACK

###### Function

- The ACK Request primitive shall be used by the provider application to acknowledge a SUBMIT Interaction.

- The ACK Indication primitive shall be used by the consumer MAL to deliver an ACK Message to a consumer.

###### Semantics

ACK Request and ACK Indication shall provide parameters as follows:

(ACK Message Header)

###### When Generated

- An ACK Request shall be used by the provider application with the provider MAL in the Initiated State to acknowledge a SUBMIT Interaction.

- An ACK Indication shall be generated by the consumer MAL in the Initiated State upon reception of an ACK Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of an ACK Request shall, once checked via the Access Control interface, cause the provider MAL to transmit an ACK Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of an ACK Indication a consumer shall end the interaction pattern with success.

###### Message Header

For the ACK message the message header fields shall be as defined in 3.4 except for the fields in table 3-8.

Table 3-8:  Submit ACK Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Consumer |
| Interaction Type | SUBMIT |
| Interaction Stage | 2 |
| Transaction Id | Transaction Id from initial message |

##### ERROR

###### Function

- The ERROR Request primitive shall be used by the provider application to end a SUBMIT Interaction with an error.

- The ERROR Indication primitive shall be used by the consumer MAL to deliver an ERROR Message to a consumer.

###### Semantics

ERROR Request and ERROR Indication shall provide parameters as follows:

(ERROR Message Header, Error Number, Extra Information)

###### When Generated

- An ERROR Request shall be used by the provider application with the provider MAL in the Initiated State to transmit an error.

- An ERROR Indication shall be generated by the consumer MAL in the Initiated State upon one of two events:

- the reception of an ERROR Message, once checked via the Access Control interface, from a provider;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of an ERROR Request shall, once checked via the Access Control interface, cause the provider MAL to transmit an ERROR Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of an ERROR Indication a consumer shall end the interaction with an error.

###### Message Header

- For the ERROR Message the message header fields shall be the same as for the ACK Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error number and any extra information (referred to as the ‘Error information’ from this point onwards) shall immediately follow the message header.

#### Example

The following example shows a simple example service with a single SUBMIT pattern-based operation:

| Operation Identifier | testSubmit |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Type Signature |
| IN | SUBMIT | TestBody body |

The TestBody structure is defined in 3.5.1.9. This corresponds to the following message being transmitted:

and corresponds to the following acknowledgement being returned:

NOTE	–	An actual service specification, rather than the example given here, would fully specify the meaning of, and required values of, all structures used by the service.

### REQUEST Interaction Pattern

#### Overview

The REQUEST pattern extends the SUBMIT pattern by replacing the simple acknowledgement with a data response message (figure 3-6). No acknowledgement other than the data response is sent.

Figure 3-6:  REQUEST Interaction Pattern Message Sequence

#### Description

The REQUEST pattern provides a simple request/response message exchange. Unlike the SUBMIT pattern, no acknowledgement is sent upon reception of the request; however, a data response is sent. The lack of an acknowledgement and only the return data response for this pattern means that it is primarily expected to be used for situations where the operation takes minimal time.

#### Usage

It is expected that the REQUEST pattern is to be used only for operations that complete in a relatively short period of time. If a more extended or indeterminate period is possible then the more advanced INVOKE or PROGRESS patterns should be specified.

#### Error Handling

Figure 3-7:  REQUEST Interaction Pattern Error Sequence

- The data response shall be replaced with an error message (see section 5) if an error occurs during the processing of the operation (figure 3-7).

- Either the data response or the error message shall be returned but never both.

#### Operation Template

The REQUEST pattern template extends the SUBMIT template by adding the requirement for a return message signature:

Table 3-9:  REQUEST Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Type Signature |
| IN | REQUEST | <<Request type>> |
| OUT | RESPONSE | <<Response type>> |

#### Primitives

Table 3-10:  REQUEST Primitive List

Primitive

REQUEST

RESPONSE

ERROR

#### State Charts

##### Consumer Side

Figure 3-8 shows the consumer side state chart for the REQUEST pattern:

Figure 3-8:  REQUEST Consumer State Chart

- The initial transition is triggered by the primitive REQUEST Request and shall lead to the Initiated State.

- There are two possible transitions from the Initiated State:

- the first is the indication of a response, RESPONSE Indication, and shall lead to the final state;

- the second is the indication of an error, ERROR Indication, and shall lead to the final state.

##### Provider Side

Figure 3-9 shows the provider side state chart for the REQUEST pattern:

Figure 3-9:  REQUEST Provider State Chart

- The initial transition is triggered by the primitive REQUEST Indication and shall lead to the Initiated State.

- There are two possible transitions from the Initiated State:

- the first is the transmission of a response, RESPONSE Request, and shall lead to the final state;

- the second is the transmission of an error, ERROR Request, and shall lead to the final state.

#### Requests and Indications

##### REQUEST

###### Function

- The REQUEST Request primitive shall be used by the consumer application to initiate a REQUEST Interaction.

- The REQUEST Indication primitive shall be used by the provider MAL to deliver a REQUEST Message to a provider and initiate a REQUEST Interaction.

###### Semantics

REQUEST Request and REQUEST Indication shall provide parameters as follows:

(REQUEST Message Header, REQUEST Message Body)

###### When Generated

- A REQUEST Request may be generated by the consumer application at any time.

- A REQUEST Indication shall be generated by the provider MAL upon reception of a REQUEST Message, once checked via the Access Control interface, from a consumer.

###### Effect on Reception

- Reception of a REQUEST Request shall, once checked via the Access Control interface, cause the consumer MAL to initiate a REQUEST Interaction by transmitting a REQUEST Message to the provider.

- The consumer MAL shall enter the Initiated State at this point.

- On reception of a REQUEST Indication by the provider, the provider MAL shall enter the Initiated State.

- The provider shall then start processing the operation at this point.

###### Message Header

- For the REQUEST Message the message header fields shall be as defined in 3.4 except for the fields in table 3-11.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-11:  REQUEST Message Header Fields

| Field | Value |
| --- | --- |
| From | Consumer |
| Authentication Id | Consumer Authentication Identifier |
| To | Provider |
| Interaction Type | REQUEST |
| Interaction Stage | 1 |
| Transaction Id | Provided by consumer MAL |

##### RESPONSE

###### Function

- The RESPONSE Request primitive shall be used by the provider application to transmit a response to a REQUEST Interaction.

- The RESPONSE Indication primitive shall be used by the consumer MAL to deliver a RESPONSE Message to a consumer.

###### Semantics

RESPONSE Request and RESPONSE Indication shall provide parameters as follows:

(RESPONSE Message Header, RESPONSE Message Body)

###### When Generated

- A RESPONSE Request shall be used by the provider application with the provider MAL in the Initiated State to transmit a final response to a REQUEST Interaction.

- A RESPONSE Indication shall be generated by the consumer MAL in the Initiated State upon reception of a RESPONSE Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of a RESPONSE Request shall, once checked via the Access Control interface, cause the provider MAL to transmit the supplied response as a RESPONSE Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of a RESPONSE Indication a consumer shall end the interaction pattern with success.

###### Message Header

- For the RESPONSE Message, the message header fields shall be as defined in 3.4 except for the fields in table 3-12.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-12:  Request RESPONSE Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Consumer |
| Interaction Type | REQUEST |
| Interaction Stage | 2 |
| Transaction Id | Transaction Id from initial message |

##### ERROR

###### Function

- The ERROR Request primitive shall be used by the provider application to end a REQUEST Interaction with an error.

- The ERROR Indication primitive shall be used by the consumer MAL to deliver an ERROR Message to a consumer.

###### Semantics

ERROR Request and ERROR Indication shall provide parameters as follows:

(ERROR Message Header, Error Number, Extra Information)

###### When Generated

- An ERROR Request shall be used by the provider application with the provider MAL in the Initiated State to transmit an error.

- An ERROR Indication shall be generated by the consumer MAL in the Initiated State upon one of two events:

- the reception of an ERROR Message, once checked via the Access Control interface, from a provider;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of an ERROR Request shall, once checked via the Access Control interface, cause the provider MAL to transmit an ERROR Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of an ERROR Indication a consumer shall end the interaction with an error.

###### Message Header

- For the ERROR Message the message header fields shall be the same as the RESPONSE Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error information shall immediately follow the message header.

#### Example

The following example shows a simple service that defines a single REQUEST operation:

| Operation Identifier | testRequest |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Type Signature |
| IN | REQUEST | TestBody body |
| OUT | RESPONSE | TestResponse response |

The TestBody structure is defined in 3.5.1.9 and the TestResponse structure is defined below:

| Name | TestResponse |
| --- | --- |
| Extends | Composite |
| Short Form Part | Example Only |
| Field | Type | Nullable | Comment |
| RspnItem | Boolean | Yes | Example Boolean item |
| RspnField | Float | Yes | Example Float item |

This corresponds to the following message being transmitted:

And corresponds to the following response being returned:

NOTE	–	An actual service specification, rather than the example given here, would fully specify the meaning of, and required values of, all structures used by the service.

### INVOKE Interaction Pattern

#### Overview

The INVOKE pattern extends the REQUEST pattern to add a mandatory acknowledgement of the initial message (figure 3-10). This allows the operation to confirm the receipt of the request before proceeding to process the request.

Figure 3-10:  INVOKE Interaction Pattern Message Sequence

The acknowledgement message is an extension of the acknowledgment used in the SUBMIT pattern. This pattern allows the acknowledgment to return a service-specific message body. A service-defined acknowledgement is required because the INVOKE pattern is indeterminate. It allows an operation to provide an indication of the operation status upon INVOKE reception.  An example would be validation of the invoke arguments.

#### Description

The INVOKE pattern extends the REQUEST pattern with the addition of a mandatory acknowledgement of the initial message.

#### Usage

The INVOKE pattern is expected to be used when there is a significant or indeterminate amount of time taken to process the request and produce the data response. The provision of the service-defined acknowledgement message allows an operation to return supplementary, status, or summary information about the request before processing continues (for example, an identifier used for querying INVOKE status using another operation).

#### Error Handling

The INVOKE pattern can report failure in two distinct ways:

Figure 3-11:  INVOKE Interaction Pattern Error Sequence

- The provider may return an error message (see section 5) in replacement of the ACK message, shown in the first sequence in figure 3-11.

- The provider may return an error after the acknowledgement is sent in replacement of the RESPONSE message, shown in the second sequence in figure 3-11.

- After an error message is sent no further messages shall be generated as part of the pattern.

NOTE	–	It is expected that the first case would be used to report an error with the invoke request and the second to report an error that occurs during processing.

#### Operation Template

The INVOKE template extends the REQUEST pattern template by requiring a message signature for the acknowledgment message. INVOKE operations take a message body argument and return an acknowledgment followed by a single data response:

Table 3-13:  INVOKE Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Type Signature |
| IN | INVOKE | <<Request type>> |
| OUT | ACK | <<Ack type>> |
| OUT | RESPONSE | <<Response type>> |

#### Primitives

Table 3-14:  INVOKE Primitive List

Primitive

INVOKE

ACK

RESPONSE

ACK_ERROR

RESPONSE_ERROR

#### State Charts

##### Consumer Side

Figure 3-12 shows the consumer side state chart for the INVOKE pattern:

Figure 3-12:  INVOKE Consumer State Chart

- The initial transition is triggered by the primitive INVOKE Request and shall lead to the Initiated State.

- There are two possible transitions from the Initiated State:

- the first is the indication of an acknowledgement, ACK Indication, and shall lead to the Acknowledged State;

- the second is the indication of an error, ACK_ERROR Indication, and shall lead to the final state.

- There are two possible transitions from the Acknowledged State:

- the first is the indication of a response, RESPONSE Indication, and shall lead to the final state;

- the second is the indication of an error, RESPONSE_ERROR Indication, and shall lead to the final state.

##### Provider Side

Figure 3-13 shows the provider side state chart for the INVOKE pattern:

Figure 3-13:  INVOKE Provider State Chart

- The initial transition is triggered by the primitive INVOKE Indication and shall lead to the Initiated State.

- There are two possible transitions from the Initiated State:

- the first is the transmission of an acknowledgement, ACK Request, and shall lead to the Acknowledged State;

- the second is the transmission of an error, ACK_ERROR Request, and shall lead to the final state.

- There are two possible transitions from the Acknowledged State:

- the first is the transmission of a response, RESPONSE Request, and shall lead to the final state;

- the second is the transmission of an error, RESPONSE_ERROR Request, and shall lead to the final state.

#### Requests and Indications

##### INVOKE

###### Function

- The INVOKE Request primitive shall be used by the consumer application to initiate an INVOKE Interaction.

- The INVOKE Indication primitive shall be used by the provider MAL to deliver an INVOKE Message to a provider and initiate an INVOKE Interaction.

###### Semantics

INVOKE Request and INVOKE Indication shall provide parameters as follows:

(INVOKE Message Header, INVOKE Message Body)

###### When Generated

- An INVOKE Request may be generated by the consumer application at any time.

- An INVOKE Indication shall be generated by the provider MAL upon reception of an INVOKE Message, once checked via the Access Control interface, from a consumer.

###### Effect on Reception

- Reception of an INVOKE Request shall, once checked via the Access Control interface, cause the consumer MAL to initiate an INVOKE Interaction by transmitting an INVOKE Message to the provider.

- The consumer MAL shall enter the Initiated State.

- On reception of an INVOKE Indication by the provider, the provider MAL shall enter the Initiated State.

- The provider shall then start processing the operation at this point.

###### Message Header

- For the INVOKE Message the message header fields shall be as defined in 3.4 except for the fields in table 3-15.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-15:  INVOKE Message Header Fields

| Field | Value |
| --- | --- |
| From | Consumer |
| Authentication Id | Consumer Authentication Identifier |
| To | Provider |
| Interaction Type | INVOKE |
| Interaction Stage | 1 |
| Transaction Id | Provided by consumer MAL |

##### ACK

###### Function

- The ACK Request primitive shall be used by the provider application to acknowledge an INVOKE Interaction.

- The ACK Indication primitive shall be used by the consumer MAL to deliver an ACK Message to a consumer.

###### Semantics

ACK Request and ACK Indication shall provide parameters as follows:

(ACK Message Header, ACK Message Body)

###### When Generated

- An ACK Request shall be used by the provider application with the provider MAL in the Initiated State to acknowledge the INVOKE Interaction.

- An ACK Indication shall be generated by the consumer MAL in the Initiated State upon reception of an ACK Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of an ACK Request shall, once checked via the Access Control interface, cause the provider MAL to transmit the supplied acknowledgement as an ACK Message to the consumer.

- A provider MAL in the Initiated State shall enter the Acknowledged State.

- On reception of an ACK Indication by the consumer, the consumer MAL shall enter the Acknowledged State.

###### Message Header

- For the ACK Message the message header fields shall be as defined in 3.4 except for the fields in table 3-16.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-16:  Invoke ACK Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Consumer |
| Interaction Type | INVOKE |
| Interaction Stage | 2 |
| Transaction Id | Transaction Id from initial message |

##### ACK_ERROR

###### Function

- The ACK_ERROR Request primitive shall be used by the provider application to end an INVOKE Interaction with an error.

- The ACK_ERROR Indication primitive shall be used by the consumer MAL to deliver an ACK_ERROR Message to a consumer.

###### Semantics

ACK_ERROR Request and ACK_ERROR Indication shall provide parameters as follows:

(ACK_ERROR Message Header, Error Number, Extra Information)

###### When Generated

- ACK_ERROR Request shall be used by the provider application with the provider MAL in the Initiated State to transmit an error.

- An ACK_ERROR Indication shall be generated by the consumer MAL in the Initiated State upon one of two events:

- the reception of an ACK_ERROR Message, once checked via the Access Control interface, from a provider;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of an ACK_ERROR Request shall, once checked via the Access Control interface, cause the provider MAL to transmit an ACK_ERROR Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of an ACK_ERROR Indication a consumer shall end the interaction with an error.

###### Message Header

- For the ACK_ERROR Message the message header fields shall be the same as for the ACK Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error information shall immediately follow the message header.

##### RESPONSE

###### Function

- The RESPONSE Request primitive shall be used by the provider application to transmit a response to an INVOKE Interaction.

- The RESPONSE Indication primitive shall be used by the consumer MAL to deliver a RESPONSE Message to a consumer.

###### Semantics

RESPONSE Request and RESPONSE Indication shall provide parameters as follows:

(RESPONSE Message Header, RESPONSE Message Body)

###### When Generated

- A RESPONSE Request shall be used by the provider application with the provider MAL in the Acknowledged State to transmit a final response to an INVOKE interaction.

- A RESPONSE Indication shall be generated by the consumer MAL in the Acknowledged State upon reception of a RESPONSE Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of a RESPONSE Request shall, once checked via the Access Control interface, cause the provider MAL to transmit the supplied response as a RESPONSE Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of a RESPONSE Indication a consumer shall end the INVOKE Interaction with success.

###### Message Header

- For the RESPONSE Message the message header fields shall be as defined in 3.4 except for the fields in table 3-17.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-17:  Invoke RESPONSE Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Consumer |
| Interaction Type | INVOKE |
| Interaction Stage | 3 |
| Transaction Id | Transaction Id from initial message |

##### RESPONSE_ERROR

###### Function

- The RESPONSE_ERROR Request primitive shall be used by the provider application to end an INVOKE Interaction with an error.

- The RESPONSE_ERROR Indication primitive shall be used by the consumer MAL to deliver a RESPONSE_ERROR Message to a consumer.

###### Semantics

RESPONSE_ERROR Request and RESPONSE_ERROR Indication shall provide parameters as follows:

(RESPONSE_ERROR Message Header, Error Number, Extra Information)

###### When Generated

- A RESPONSE_ERROR Request shall be used by the provider application with the provider MAL in the Acknowledged State to transmit an error.

- A RESPONSE_ERROR Indication shall be generated by the consumer MAL in the Acknowledged State upon one of two events:

- the reception of a RESPONSE_ERROR Message, once checked via the Access Control interface, from a provider;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of a RESPONSE_ERROR Request shall, once checked via the Access Control interface, cause the provider MAL to transmit a RESPONSE_ERROR Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of a RESPONSE_ERROR Indication a consumer shall end the interaction with an error.

###### Message Header

- For the RESPONSE_ERROR Message the message header fields shall be the same as for the RESPONSE Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error information shall immediately follow the message header.

#### Example

The following example shows a simple example service that contains a single INVOKE operation. The operation sends a TestBody structure and returns a TestAck acknowledgment structure followed by a TestResponse structure:

| Operation Identifier | testInvoke |
| --- | --- |
| Interaction Pattern | INVOKE |
| Pattern Sequence | Message | Type Signature |
| IN | INVOKE | TestBody body |
| OUT | ACK | TestAck ack |
| OUT | RESPONSE | TestResponse response |

The TestBody structure is defined in 3.5.1.9 and the TestResponse structure is defined in 3.5.3.9. The TestAck structure is defined below:

| Name | TestAck |
| --- | --- |
| Extends | Composite |
| Short Form Part | Example Only |
| Field | Type | Nullable | Comment |
| AckId | Identifier | Yes | Example Identifier item |

This corresponds to the following message being transmitted:

And corresponds to the following acknowledgement being returned:

And finally corresponds to the following response being returned:

NOTE	–	An actual service specification, rather than the example given here, would fully specify the meaning of, and required values of, all structures used by the service.

### PROGRESS Interaction Pattern

#### Overview

The PROGRESS pattern extends the INVOKE pattern to add a set of progress updates of the request message (figure 3-14). This allows the operation to confirm the receipt of the request before proceeding to process the request and also to show progress of the operation.

Figure 3-14:  PROGRESS Interaction Pattern Message Sequence

#### Description

The PROGRESS pattern extends the INVOKE pattern with the addition of a set of mandatory progress messages. The type of progress messages and their number is defined by the service and not by the pattern.

#### Usage

The PROGRESS pattern is expected to be used when there is a significant or indeterminate amount of time taken to process the request and produce the data response, and where monitoring of the progress of the operation is required or the data response is to be returned in blocks. The order of the update messages is not guaranteed by the MAL, thus it is delegated to the transport layer on an implementation-specific basis.

#### Error Handling

The PROGRESS pattern can report failure in three distinct ways:

Figure 3-15:  PROGRESS Interaction Pattern Error Sequence

- The acknowledgement may be replaced with an error message (see section 5) shown in the first sequence in figure 3-15.

- An error may be generated during the processing of the body of the operation, after the initial acknowledgement is sent, as shown in the second sequence in figure 3-15 and replaces any of the progress updates.

- An error may be generated after the updates and replace the final response as shown in the third sequence in figure 3-15.

- After an error message is sent, no further messages shall be generated as part of the pattern.

#### Operation Template

The PROGRESS template is similar to the INVOKE pattern template but adds a progress update message:

Table 3-18:  PROGRESS Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | PROGRESS |
| Pattern Sequence | Message | Type Signature |
| IN | PROGRESS | <<Request type>> |
| OUT | ACK | <<Ack type>> |
| OUT | UPDATE | <<Update value type>> |
| OUT | RESPONSE | <<Response type>> |

#### Primitives

Table 3-19:  PROGRESS Primitive List

Primitive

PROGRESS

ACK

ACK_ERROR

UPDATE

UPDATE_ERROR

RESPONSE

RESPONSE_ERROR

#### State Charts

##### Consumer Side

Figure 3-16 shows the consumer side state chart for the PROGRESS pattern:

Figure 3-16:  PROGRESS Consumer State Chart

- The initial transition is triggered by the primitive PROGRESS Request and shall lead to the Initiated State.

- There are two possible transitions from the Initiated State:

- the first is the indication of an acknowledgement, ACK Indication, and shall lead to the Acknowledged State;

- the second is the indication of an error, ACK_ERROR Indication, and shall lead to the final state.

- There are four possible transitions from the Acknowledged State:

- the first is the indication of an update, UPDATE Indication, and shall lead to the Progressing State;

- the second is the indication of an error in generating an initial update, UPDATE_ERROR Indication, and shall lead to the final state;

- the third is the indication of a response, RESPONSE Indication, and shall lead to the final state;

- the fourth is the indication of an error in generating the response, RESPONSE_ERROR Indication, and shall lead to the final state.

- There are four possible transitions from the Progressing State:

- the first is the indication of another update, UPDATE Indication, and shall lead back to the Progressing State;

- the second is the indication of an error in generating an update, UPDATE_ERROR Indication, and shall lead to the final state;

- the third is the indication of a response, RESPONSE Indication, and shall lead to the final state;

- the fourth is the indication of an error in generating the response, RESPONSE_ERROR Indication, and shall lead to the final state.

##### Provider Side

Figure 3-17 shows the provider side state chart for the PROGRESS pattern:

Figure 3-17:  PROGRESS Provider State Chart

- The initial transition is triggered by the primitive PROGRESS Indication and shall lead to the Initiated State.

- There are two possible transitions from the Initiated State:

- the first is the transmission of an acknowledgement, ACK Request, and shall lead to the Acknowledged State;

- the second is the transmission of an error, ACK_ERROR Request, and shall lead to the final state.

- There are four possible transitions from the Acknowledged State:

- the first is the transmission of an update, UPDATE Request, and shall lead to the Progressing State;

- the second is the transmission of an error in generating an initial update, UPDATE_ERROR Request, and shall lead to the final state;

- the third is the transmission of a response, RESPONSE Request, and shall lead to the final state;

- the fourth is the transmission of an error in generating the response, RESPONSE_ERROR Request, and shall lead to the final state.

- There are four possible transitions from the Progressing State:

- the first is the transmission of another update, UPDATE Request, and shall lead back to the Progressing State;

- the second is the transmission of an error in generating an update, UPDATE_ERROR Request, and shall lead to the final state;

- the third is the transmission of a response, RESPONSE Request, and shall lead to the final state;

- the fourth is the transmission of an error in generating the response, RESPONSE_ERROR Request, and shall lead to the final state.

#### Requests and Indications

##### PROGRESS

###### Function

- The PROGRESS Request primitive shall be used by the consumer application to initiate a PROGRESS Interaction.

- The PROGRESS Indication primitive shall be used by the provider MAL to deliver a PROGRESS Message to a provider and initiate a PROGRESS Interaction.

###### Semantics

PROGRESS Request and PROGRESS Indication shall provide parameters as follows:

(PROGRESS Message Header, PROGRESS Message Body)

###### When Generated

- A PROGRESS Request may be generated by the consumer application at any time.

- A PROGRESS Indication shall be generated by the provider MAL upon reception of a PROGRESS Message, once checked via the Access Control interface, from a consumer.

###### Effect on Reception

- Reception of a PROGRESS Request shall, once checked via the Access Control interface, cause the consumer MAL to initiate a PROGRESS Interaction by transmitting a PROGRESS Message to the provider.

- The consumer MAL shall enter the Initiated State.

- On reception of a PROGRESS Indication by a provider, the provider MAL shall enter the Initiated State.

- The provider shall then start processing the operation at this point.

###### Message Header

- For the PROGRESS Message the message header fields shall be as defined in 3.4 except for the fields in table 3-20.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-20:  PROGRESS Message Header Fields

| Field | Value |
| --- | --- |
| From | Consumer |
| Authentication Id | Consumer Authentication Identifier |
| To | Provider |
| Interaction Type | PROGRESS |
| Interaction Stage | 1 |
| Transaction Id | Provided by consumer MAL |

##### ACK

###### Function

- The ACK Request primitive shall be used by the provider application to acknowledge a PROGRESS Interaction.

- The ACK Indication primitive shall be used by the consumer MAL to deliver an ACK Message to a consumer.

###### Semantics

ACK Request and ACK Indication shall provide parameters as follows:

(ACK Message Header, ACK Message Body)

###### When Generated

- An ACK Request shall be used by the provider application with the provider MAL in the Initiated State to acknowledge a PROGRESS Interaction.

- An ACK Indication shall be generated by the consumer MAL in the Initiated State upon reception of an ACK Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of an ACK Request shall, once checked via the Access Control interface, cause the provider MAL to transmit the supplied acknowledgement as an ACK Message to the consumer.

- A provider MAL in the Initiated State shall enter the Acknowledged State.

- On reception of an ACK Indication by the consumer, the consumer MAL shall enter the Acknowledged State.

###### Message Header

- For the ACK Message the message header fields shall be as defined in 3.4 except for the fields in table 3-21.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-21:  Progress ACK Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Consumer |
| Interaction Type | PROGRESS |
| Interaction Stage | 2 |
| Transaction Id | Transaction Id from initial message |

##### ACK_ERROR

###### Function

- The ACK_ERROR Request primitive shall be used by the provider application to end a PROGRESS Interaction with an error.

- The ACK_ERROR Indication primitive shall be used by the consumer MAL to deliver an ACK_ERROR Message to a consumer.

###### Semantics

ACK_ERROR Request and ACK_ERROR Indication shall provide parameters as follows:

(ACK_ERROR Message Header, Error Number, Extra Information)

###### When Generated

- An ACK_ERROR Request shall be used by the provider application with the provider MAL in the Initiated State to transmit an error.

- An ACK_ERROR Indication shall be generated by the consumer MAL in the Initiated State upon one of two events:

- the reception of an ACK_ERROR Message, once checked via the Access Control interface, from a provider;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of an ACK_ERROR Request shall, once checked via the Access Control interface, cause the provider MAL to transmit an ACK_ERROR Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of an ACK_ERROR Indication a consumer shall end the interaction with an error.

###### Message Header

- For the ACK_ERROR Message the message header fields shall be the same as for the ACK Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error information shall immediately follow the message header.

##### UPDATE

###### Function

- The UPDATE Request primitive shall be used by the provider application to transmit an update during a PROGRESS Interaction.

- The UPDATE Indication primitive shall be used by the consumer MAL to deliver an UPDATE Message to a consumer.

###### Semantics

UPDATE Request and UPDATE Indication shall provide parameters as follows:

(UPDATE Message Header, UPDATE Message Body)

###### When Generated

- An UPDATE Request shall be used by the provider application with the provider MAL in either the Acknowledged State or Progressing State to transmit an update to a PROGRESS interaction.

- An UPDATE Indication shall be generated by the consumer MAL in either the Acknowledged State or the Progressing State upon reception of an UPDATE Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of an UPDATE Request shall, once checked via the Access Control interface, cause the provider MAL to transmit the supplied update as an UPDATE Message to the consumer.

- A provider MAL in the Acknowledged State shall enter the Progressing State.

- On reception of an UPDATE Indication by the consumer, the consumer MAL in the Acknowledged State shall enter the Progressing State.

###### Message Header

- For the UPDATE Message, of which there may be several, the message header fields shall be as defined in 3.4 except for the fields in table 3-22.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-22:  Progress UPDATE Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Consumer |
| Interaction Type | PROGRESS |
| Interaction Stage | 3 |
| Transaction Id | Transaction Id from initial message |

##### UPDATE_ERROR

###### Function

- The UPDATE_ERROR Request primitive shall be used by the provider application to end a PROGRESS Interaction with an error.

- The UPDATE_ERROR Indication primitive shall be used by the consumer MAL to deliver an UPDATE_ERROR Message to a consumer.

###### Semantics

UPDATE_ERROR Request and UPDATE_ERROR Indication shall provide parameters as follows:

(UPDATE_ERROR Message Header, Error Number, Extra Information)

###### When Generated

- An UPDATE_ERROR Request shall be used by the provider application with the provider MAL in either the Acknowledged State or the Progressing State to transmit an error.

- An UPDATE_ERROR Indication shall be generated by the consumer MAL in either the Acknowledged State or the Progressing State upon one of two events:

- the reception of an UPDATE_ERROR Message, once checked via the Access Control interface, from a provider;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of an UPDATE_ERROR Request shall, once checked via the Access Control interface, cause the provider MAL to transmit an UPDATE_ERROR Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of an UPDATE_ERROR Indication a consumer shall end the interaction with an error.

###### Message Header

- For the UPDATE_ERROR Message the message header fields shall be the same as for the UPDATE Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error information shall immediately follow the message header.

##### RESPONSE

###### Function

- The RESPONSE Request primitive shall be used by the provider application to transmit a response to a PROGRESS Interaction.

- The RESPONSE Indication primitive shall be used by the consumer MAL to deliver a RESPONSE Message to a consumer.

###### Semantics

RESPONSE Request and RESPONSE Indication shall provide parameters as follows:

(RESPONSE Message Header, RESPONSE Message Body)

###### When Generated

- A RESPONSE Request shall be used by the provider application with the provider MAL in either the Acknowledged State or Progressing State to transmit a final response to a PROGRESS interaction.

- A RESPONSE Indication shall be generated by the consumer MAL in either the Acknowledged State or the Progressing State upon reception of a RESPONSE Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of a RESPONSE Request shall, once checked via the Access Control interface, cause the provider MAL to transmit the supplied response as a RESPONSE Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of a RESPONSE Indication a consumer shall end the PROGRESS Interaction with success.

###### Message Header

- For the RESPONSE Message the message header fields shall be as defined in 3.4 except for the fields in table 3-23.

- The contents of the Message Body, as specified in the operation template, shall immediately follow the message header.

Table 3-23:  Progress RESPONSE Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Consumer |
| Interaction Type | PROGRESS |
| Interaction Stage | 4 |
| Transaction Id | Transaction Id from initial message |

##### RESPONSE_ERROR

###### Function

- The RESPONSE_ERROR Request primitive shall be used by the provider application to end a PROGRESS Interaction with an error.

- The RESPONSE_ERROR Indication primitive shall be used by the consumer MAL to deliver a RESPONSE_ERROR Message to a consumer.

###### Semantics

RESPONSE_ERROR Request and RESPONSE_ERROR Indication shall provide parameters as follows:

(RESPONSE_ERROR Message Header, Error Number, Extra Information)

###### When Generated

- A RESPONSE_ERROR Request shall be used by the provider application with the provider MAL in either the Acknowledged State or Progressing State to transmit an error.

- A RESPONSE_ERROR Indication shall be generated by the consumer MAL in either the Acknowledged State or the Progressing State upon one of two events:

- the reception of a RESPONSE_ERROR Message, once checked via the Access Control interface, from a provider;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of a RESPONSE_ERROR Request shall, once checked via the Access Control interface, cause the provider MAL to transmit a RESPONSE_ERROR Message to the consumer.

- The pattern shall end at this point for the provider.

- On reception of a RESPONSE_ERROR Indication a consumer shall end the interaction with an error.

###### Message Header

- For the RESPONSE_ERROR Message the message header fields shall be the same as for the RESPONSE Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error information shall immediately follow the message header.

#### Example

The following example shows a simple example service that contains a single PROGRESS operation. The operation sends a TestBody structure, which is acknowledged with a TestAck structure, reports progress with a TestProgress structure, and returns a TestResponse structure:

| Operation Identifier | testProgress |
| --- | --- |
| Interaction Pattern | PROGRESS |
| Pattern Sequence | Message | Type Signature |
| IN | PROGRESS | TestBody body |
| OUT | ACK | TestAck ack |
| OUT | UPDATE | TestProgress progress |
| OUT | RESPONSE | TestResponse response |

The TestBody structure is defined in 3.5.1.9, TestAck structure is defined in 3.5.4.9, and the TestResponse structure is defined in 3.5.3.9. The TestProgress structure is defined below:

| Name | TestProgress |
| --- | --- |
| Extends | Composite |
| Short Form Part | Example Only |
| Field | Type | Nullable | Comment |
| RspnStage | Integer | Yes | Example Integer item |

This corresponds to the following message being transmitted:

And corresponds to the following acknowledgement being returned:

Progress is reported using the following message; in this example two stages are reported:

And finally corresponds to the following response being returned:

NOTE	–	An actual service specification, rather than the example given here, would fully specify the meaning of, and required values of, all structures used by the service.

### Publish-Subscribe Interaction Pattern

#### Overview

The PUBLISH-SUBSCRIBE pattern provides the ability for consumers to register interest in a specific topic and receive updates from one or more providers without requiring awareness of the number of, and location of, these providers.

The basic outline of the pattern is: 1. consumers register interest by sending a subscription list; 2. providers register on the broker; 3. providers publish updates; 4. updates are then sent to registered consumers; 5. and when no further updates are required the consumer cancels its subscription by deregistering.

The PUBLISH-SUBSCRIBE pattern can be deployed in two distinct ways; the first is where an intermediary shared message broker resides between the consumers and the providers (figure 3-18). In this deployment the shared broker permits a decoupling of the consumer from the providers, receiving the subscriptions from consumers and the updates from providers, and is responsible for dispatching the required updates to registered consumers:

Figure 3-18:  PUBLISH-SUBSCRIBE Interaction Pattern Message Sequence

The shared message broker manages the consumer subscription lists; the providers are not aware of what consumers there are and what entities they require. Because of this they must publish all items they are configured to generate to the broker so that it can manage the updates to the consumers.

At a later time, when updates are no longer required, the consumer can deregister for these updates from the message broker.

The broker acknowledges both the consumer and provider register/deregister operations; these are treated like normal SUBMIT messages. No acknowledgement of the publish message is provided by the broker and no acknowledgement by the consumer of the notify message is required.

The second deployment of the PUBLISH-SUBSCRIBE pattern is when there is a single update provider and the message broker is private to it. This is an example of an observe type relationship where a consumer observes some aspect of a specific provider.

In this deployment, because of the one-to-one relationship between the consumer and the provider, the functionality of the message broker does not necessarily require a separate entity. It is completely possible for the message broker logic to reside in the provider application; the provider publishes updates to itself for distribution to consumers (figure 3-19):

Figure 3-19:  PUBLISH-SUBSCRIBE Pattern Alternative Message Sequence

However, because the pattern is still the same, all features of the first deployment (multiple concurrent subscription lists) are still supported.

In terms of implementation, for both the shared or private broker pattern, there are three primary implementation designs (others may exist, however). The first is where the broker logic resides in the MAL layer, the second is where it is natively supported by the message transport technology used, and the third is where it is implemented as a standalone component external to the MAL. In all three cases the pattern of interaction is the same; it is only the physical location of the broker that changes.

#### Description

The PUBLISH-SUBSCRIBE pattern for both the consumer and provider register/deregister has a predefined pattern message structure which allows an implementation of the message broker to manage the mapping of consumers to updates and hide this complexity from Provider applications.

#### Subscriptions

A consumer informs the broker of the updates to send it by the use of subscriptions. Subscriptions are sent during the registration.

- A single consumer may define many subscription lists concurrently by specifying a different subscription identifier during the registration.

- To change the contents of a subscription list a consumer may redefine it by registering a new list with the same identifier. The consumer is not required to deregister the subscription first.

- For a broker the replacement of a subscription is an atomic operation; no updates shall be missed as a result of the subscription replacement operation.

- The Consumer Entity name and the subscription identifier shall form the unique identifier of the subscription; this means that two consumers cannot share subscriptions, as they have different Consumer entity names.

- The consumer deregister message takes a list of identifiers of the subscription lists to cancel and shall completely remove the subscriptions from the list of active subscriptions.

- The update rate shall be an aspect of a provider; the consumer cannot specify it.

For example, if a consumer initially registers for updates on the set (A, B, C) but at a later date requires also ‘D’, another register message is required to be sent with the set (A, B, C, D). The register call replaces the previous subscription list with the new list. The deregister message completely cancels the identified lists.

Another way of describing this is the register message defines an update ‘report’ and the deregister message clears that ‘report’ definition.

NOTE	–	If a single subscription definition lists the same parameter more than once, only one update is sent to the consumer for that list. However, if a consumer defines two concurrent subscription lists that request the same parameters, then the consumer will receive two updates of those common parameters, one for each subscription. If this is an issue, then the consumer still has the option of maintaining a single subscription and splitting the results internally.

#### Published Messages Routing on the Broker

The routing of the published messages in the Broker will be based on two parts, (1) specific fields from the message header and (2) the subscription key values:

- The area, service, and operation identifiers of the message header shall form the first part to be matched.

- The published subscription key values shall form the second part to be matched with the Subscription filters provided by the consumers.

- The published subscription key shall not use NULL as a value as this is reserved for the wildcard value (see 3.5.6.5).

#### Subscription Filter Matching on the Broker

This subsection details the rules for subscription filter matching in the PUBLISH-SUBSCRIBE pattern. The subscription is matched on two aspects: the optional domain field, and the optional filters (which are ANDed together).

The following paragraphs detail the rules for filter matching:

- The filters field holds a list of filters composed of a name (type: Identifier) and a set of possible values (type: List<MAL::Attribute>) to be matched.

- Each filter shall hold as a value, one of following two types: (1) a specific value, or (2) a NULL value that represents a wildcard.

- If a filter contains a specific value it shall only match a subkey that contains the same value. This includes an empty ‘’ value for text-based data types. The matches are case sensitive.

- If a filter contains the NULL wildcard value it shall match a subkey that contains any value including NULL.

If a publish message includes in the Extra field in the MAL Header, an entry containing a “domain” name with a respective value, the following rules for domain field matching of the subscription with the publish message shall be applied:

- The domain of the update message shall match the domain of the subscription message.

- If the subscription included a domain field, then this shall be matched to the domain of the update message.

- Any of the Identifiers of the domain may be the wildcard character ‘*’.

For example, suppose a provider is publishing a set of updates with the following domains:

- spacecraftA

- spacecraftA.aocs

- spacecraftA.aocs.thrustA

- spacecraftA.payload

- spacecraftA.payload.cameraA.tempB

- spacecraftB

- agency.spacecraftA

- spacecraftB.payload.cameraA.tempB

A subscription filter with the domain of ‘spacecraftA’ would only match the first update.

A subscription filter with the domain of ‘spacecraftA.aocs’ would only match the second update.

A subscription filter with the domain of ‘spacecraftA.payload.*’ would match the fourth and fifth updates.

A subscription filter with the domain of ‘*.payload.cameraA.*’ would match the fifth and eighth updates.

A subscription filter with the domain of ‘spacecraftA.*’ would match updates 1 to 5.

#### Usage

The PUBLISH-SUBSCRIBE pattern provides the ability for asynchronous updates to be sent to registered consumers.

#### Error Handling

The PUBLISH-SUBSCRIBE pattern can report failure for a consumer in two distinct ways:

Figure 3-20:  PUBLISH-SUBSCRIBE Interaction Pattern Consumer Error Sequence

- The register acknowledgement may be replaced with an error message (see section 5) shown in the first sequence in figure 3-20.

- A notify may be replaced by an error by the message broker shown in the second sequence in figure 3-20.

- After an error message is sent no further messages shall be transmitted to the relevant consumer as part of the pattern.

For a publisher the PUBLISH-SUBSCRIBE pattern can report failure in two distinct ways:

Figure 3-21:  PUBLISH-SUBSCRIBE Interaction Pattern Provider Error Sequence

- The publish register acknowledgement may be replaced with an error message (see section 5) shown in the first sequence in figure 3-21.

- After a PUBLISH_REGISTER_ERROR message is sent no further messages shall be transmitted to or from the relevant publisher as part of the pattern.

- When an error is detected by the message broker on reception of a PUBLISH message from a provider, a PUBLISH_ERROR message shall be sent to the provider as shown in the second sequence in figure 3-21. The error is sent asynchronously to the provider.

#### Operation Template

The PUBLISH-SUBSCRIBE template is below:

Table 3-24:  PUBLISH-SUBSCRIBE Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Subscription Keys | <<Subscription Key types and names>> |
| Pattern Sequence | Message | Type Signature |
| OUT | PUBLISH/NOTIFY | <<Update value>> |

- The Subscription Keys row shall present the list of available subscription keys for the defined operation. The type signature will include the name and its respective data type for each subscription key.

- The PUBLISH/NOTIFY message shall follow the same rules for message bodies (as defined in 3.4.23.4.2.2, where the message body may be composed of several types. Subsection 3.5.6.12 provides an example of this for this interaction pattern.

- A single update shall require a value for each type listed in the operation template in the case where it is defined using multiple types. Subsection 3.5.6.12 provides an example of this for this interaction pattern.

- The update value shall be the same as it is passed in the provider-to-broker PUBLISH and broker-to-consumer NOTIFY messages.

- The contents of these messages are fixed and therefore not present in the operation template for PUBLISH-SUBSCRIBE. The PUBLISH-SUBSCRIBE pattern is actually made up of consumer and provider register/deregister, publish, and notify messages, the templates of which are given below. The message directions (IN/OUT) are all from the point of view of the broker, as it is involved in all operations:

Table 3-25:  PUBLISH-SUBSCRIBE Register Operation Template

| Operation Identifier | register<< PUBLISH-SUBSCRIBE Operation Name>> |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Type Signature |
| IN | REGISTER | Subscription subscription |

- The consumer register method takes a subscription which is composed of an identifier, a domain, and a list of filters. The identifier shall be used by the broker to uniquely identify the subscription when combined with the consumer entity name; this allows a consumer to set up several different concurrent subscriptions.

- Each subscription shall contain a list of filters which contain an identifier key name, and a list of values to be matched.

Table 3-26:  PUBLISH-SUBSCRIBE Publish Register Operation Template

| Operation Identifier | publishRegister<< PUBLISH-SUBSCRIBE Operation Name>> |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Type Signature |
| IN | PUBLISH_REGISTER |  |

- The provider register message takes no arguments. It shall register the provider from which updates will be performed.

Table 3-27:  PUBLISH-SUBSCRIBE Publish Operation Template

| Operation Identifier | publish<< PUBLISH-SUBSCRIBE Operation Name>> |
| --- | --- |
| Interaction Pattern | SEND |
| Pattern Sequence | Message | Type Signature |
| IN | PUBLISH | UpdateHeader header <<Update Value>> |

- The provider-to-broker publish message shall match the provider register message on the area identifier, service identifier, version identifier, and operation identifier.

- The provider-to-broker publish message domain shall match exactly, or be a sub-domain of (see 3.5.6.5), the domain of the provider register message.

- A PUBLISH standard pattern body shall contain an UpdateHeader followed by the Update Value defined in the top-level PUBSUB template. For example, a PUBSUB operation defined using the types of [Boolean, Octet, MyComposite] will result in a PUBLISH message with the body containing [UpdateHeader, Boolean, Octet, MyComposite].

- For each update being published there shall be an UpdateHeader and the corresponding Update Value.

- Each UpdateHeader shall optionally contain the source of the update, and the update key values.

- The key values in the UpdateHeader message shall be ordered as defined by the operation so that the corresponding key names can be matched with the entries in the list.

Table 3-28:  PUBLISH-SUBSCRIBE Publish Error Operation Template

| Operation Identifier | publishError<< PUBLISH-SUBSCRIBE Operation Name>> |
| --- | --- |
| Interaction Pattern | SEND |
| Pattern Sequence | Message | Type Signature |
| OUT | PUBLISH_ERROR | UInteger errorNumber |

- If a provider publishes an update with more or less key values than expected, then the broker shall return an UNKNOWN error in a PUBLISH_ERROR message.

Table 3-29:  PUBLISH-SUBSCRIBE Notify Operation Template

| Operation Identifier | notify<< PUBLISH-SUBSCRIBE Operation Name>> |
| --- | --- |
| Interaction Pattern | SEND |
| Pattern Sequence | Message | Type Signature |
| OUT | NOTIFY | Identifier subscriptionId UpdateHeader updateHeader <<Update Values>> |

- The broker-to-consumer NOTIFY message body shall contain a single Identifier, an UpdateHeader followed by the Update Value defined in the top-level PUBSUB template, which hold the update set for a single subscription. For example, a PUBSUB operation defined using the types of [Boolean, Octet, MyComposite] will result in a NOTIFY message with the body containing [Identifier, UpdateHeader, Boolean, Octet, MyComposite].

- The key values in the UpdateHeader message shall be ordered as defined by the operation so that the corresponding key names can be matched with the entries in the list.

- The single Identifier in the notify message shall contain the subscription identifier for the subscription being notified.

- In the NOTIFY message there shall be the update values for each type defined in the top level PUBSUB template.

- If all entries in the UpdateHeader list are NULL, then the whole list shall be replaced with a NULL in order to increase efficiency.

Table 3-30:  PUBLISH-SUBSCRIBE Notify Error Operation Template

| Operation Identifier | notifyError<< PUBLISH-SUBSCRIBE Operation Name>> |
| --- | --- |
| Interaction Pattern | SEND |
| Pattern Sequence | Message | Type Signature |
| OUT | NOTIFY_ERROR | UInteger errorNumber Element extraInformation |

- If the broker wants to shutdown, then the broker shall return an SHUTDOWN error in a NOTIFY_ERROR message and an extra information message on the cause.

- If the broker has an internal error, then the broker shall return an INTERNAL error in a NOTIFY_ERROR message and an extra information message on the cause.

Table 3-31:  PUBLISH-SUBSCRIBE Deregister Operation Template

| Operation Identifier | deregister<< PUBLISH-SUBSCRIBE Method Name>> |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Type Signature |
| IN | DEREGISTER | List<Identifier> subscriptionIds |

- The consumer deregister message shall take a list of identifiers of the active subscription lists to cancel.

Table 3-32:  PUBLISH-SUBSCRIBE Publish Deregister Operation Template

| Operation Identifier | publishDeregister<< PUBLISH-SUBSCRIBE Method Name>> |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Type Signature |
| IN | PUBLISH_DEREGISTER |  |

- The provider deregister message takes no arguments. It shall completely remove the provider from the set of providers from which updates are permitted.

- In all cases, for consumer/provider register and deregister, the acknowledge message shall only be sent when the registration/deregistration has completed and is a confirmation that the operation has succeeded.

#### Primitives

Table 3-33:  PUBLISH-SUBSCRIBE Primitive List

Primitive

REGISTER

REGISTER_ACK

REGISTER_ERROR

PUBLISH_REGISTER

PUBLISH_REGISTER_ACK

PUBLISH_REGISTER_ERROR

PUBLISH

PUBLISH_ERROR

NOTIFY

NOTIFY_ERROR

DEREGISTER

DEREGISTER_ACK

PUBLISH_DEREGISTER

PUBLISH_DEREGISTER_ACK

#### State Charts

##### General

Several state charts are defined:

- one state chart on the consumer side related to the interaction between the consumer and the broker;

- one state chart on the broker side related to the interaction between the consumer and the broker;

- one state chart on the provider side related to the interaction between the provider and the broker;

- another state chart on the broker side related to the interaction between the provider and the broker.

##### Consumer Side

Figure 3-22 shows the consumer side state chart for the PUBLISH-SUBSCRIBE pattern:

Figure 3-22:  PUBLISH-SUBSCRIBE Consumer State Chart

- The state chart applies to a single subscription for a single consumer, the state chart shall be replicated for each consumer and for each subscription.

- The transaction identifier of the initial REGISTER Message shall be used to identify messages that relate to one PUBLISH-SUBSCRIBE interaction to avoid race conditions.

- The initial transition is triggered by the primitive REGISTER Request and shall lead to the Register Initiated State.

- There are two possible transitions from the Register Initiated State:

- the first is the indication of an acknowledgement, REGISTER_ACK Indication, and shall lead to the Registered State;

- the second is the indication of an error, REGISTER_ERROR Indication, and shall lead to the final state.

- There are four possible transitions from the Registered State:

- the first is the indication of a notification, NOTIFY Indication, and shall lead back to the Registered State;

- the second is the indication of an error, NOTIFY_ERROR Indication, and shall lead to the final state;

- the third transition shall be triggered by the primitive DEREGISTER Request and shall lead to the Deregister Initiated State;

- the fourth transition shall be triggered by the primitive REGISTER Request and shall lead to the ReRegister Initiated State.

- There are four possible transitions from the ReRegistered Initiated State:

- The first is the indication of a notification, NOTIFY Indication, and shall lead back to the ReRegistered Initiated State. In this case the NOTIFY Message will have been sent before the REGISTER Message was received by the broker and therefore forms part of the previous subscription. It shall, however, be passed to the consumer application as normal.

- The second is the indication of a registration error, REGISTER_ERROR Indication, and shall lead to the final state.

- The third is the indication of a notify error, NOTIFY_ERROR Indication, and shall lead to the final state. In this case the NOTIFY_ERROR Message will have been sent before the REGISTER Message was received by the broker and therefore forms part of the previous subscription. It shall, however, be passed to the consumer application as normal. The transaction identifier shall be used by the broker to ensure that the reception of the REGISTER Message after the NOTIFY_ERROR Message was sent shall not cause the restart of the subscription.

- The fourth transition is the indication of an acknowledgement, REGISTER_ACK Indication, and shall lead to the Registered State.

- There are three possible transitions from the Deregister Initiated State:

- the first is the indication of a notification, NOTIFY Indication, and shall lead back to the Deregister Initiated State;

- the second is the indication of an error, NOTIFY_ERROR Indication, and shall lead to the final state;

- the third transition is the indication of an acknowledgement, DEREGISTER_ACK Indication, and shall lead to the final state.

##### Broker Side (Related to the Consumer)

Figure 3-23 shows the broker to consumer state chart for the PUBLISH-SUBSCRIBE pattern:

Figure 3-23:  PUBLISH-SUBSCRIBE Broker to Consumer State Chart

- The state chart applies to a single subscription for a single consumer.  The state chart shall be replicated for each consumer and for each subscription.

- The initial transition is triggered by the primitive REGISTER Indication and shall lead to the Register Initiated State.

- There are two possible transitions from the Register Initiated State:

- the first is the triggering of an acknowledgement, REGISTER_ACK Request, and shall lead to the Registered State;

- the second is the triggering of an error, REGISTER_ERROR Request, and shall lead to the final state.

- There are four possible transitions from the Registered State;

- the first is the triggering of a notification, NOTIFY Request, and shall lead back to the Registered State;

- the second is the triggering of an error, NOTIFY_ERROR Request, and shall lead to the final state;

- the third transition shall be triggered by the primitive DEREGISTER Indication and shall lead to the Deregister Initiated State;

- the fourth transition shall be triggered by the primitive REGISTER Indication and shall lead to the ReRegister Initiated State.

- There are two possible transitions from the ReRegister Initiated State:

- the first is the triggering of an acknowledgement, REGISTER_ACK Request, and shall lead to the Registered State;

- the second is the triggering of an error, REGISTER_ERROR Request, and shall lead to the final state.

- There is only one possible transition from the Deregister Initiated State; it is the triggering of an acknowledgement, DEREGISTER_ACK Request, and shall lead to the final state.

##### Provider Side

Figure 3-24 shows the provider side state chart for the PUBLISH-SUBSCRIBE pattern:

Figure 3-24:  PUBLISH-SUBSCRIBE Provider State Chart

- The state chart applies to a single provider.  The state chart shall be replicated for each provider.

- The initial transition is triggered by the primitive PUBLISH_REGISTER Request and shall lead to the Register Initiated State.

- There are two possible transitions from the Register Initiated State:

- the first is the indication of an acknowledgement, PUBLISH_REGISTER_ACK Indication, and shall lead to the Registered State;

- the second is the indication of an error, PUBLISH_REGISTER_ERROR Indication, and shall lead to the final state.

- There are four possible transitions from the Registered State:

- the first is the triggering of a publish, PUBLISH Request, and shall lead back to the Registered State;

- the second is the indication of an error, PUBLISH_ERROR Indication, and shall lead back to the Registered State;

- the third transition shall be triggered by the primitive PUBLISH_REGISTER Request and shall lead to the ReRegister Initiated State;

- the fourth transition shall be triggered by the primitive PUBLISH_DEREGISTER Request and shall lead to the Deregister Initiated State.

- There are three possible transitions from the ReRegister Initiated State:

- The first is the indication of an acknowledgement, PUBLISH_REGISTER_ACK Indication, and shall lead to the Registered State.

- The second is the indication of a registration error, PUBLISH_REGISTER_ERROR Indication, and shall lead to the final state.

- The third is the indication of a publish error, PUBLISH_ERROR Indication, and shall lead back to the Re-Registered State. In this case the PUBLISH_ERROR Message will have been sent before the PUBLISH_REGISTER Message was received by the broker and therefore forms part of the previous subscription.

- There are two possible transitions from the Deregister Initiated State:

- the first is the indication of an acknowledgement, PUBLISH_DEREGISTER_ACK Indication, and shall lead to the final state;

- the second is the indication of a publish error, PUBLISH_ERROR Indication, and shall lead back to the Deregister Initiated State.

##### Broker Side (Related to the Provider)

Figure 3-25 shows the broker to provider state chart for the PUBLISH-SUBSCRIBE pattern:

Figure 3-25:  PUBLISH-SUBSCRIBE Broker to Provider State Chart

- The state chart applies to a single provider.  The state chart shall be replicated for each provider.

- The initial transition is triggered by the primitive PUBLISH_REGISTER Indication and shall lead to the Publish Register Initiated State.

- There are two possible transitions from the Publish Register Initiated State:

- the first is the triggering of an acknowledgement, PUBLISH_REGISTER_ACK Request, and shall lead to the Publish Initiated State;

- the second is the triggering of an error, PUBLISH_REGISTER_ERROR Request, and shall lead to the final state.

- There are four possible transitions from the Publish Initiated State:

- the first is the indication of a publish, PUBLISH Indication, and shall lead back to the Publish Initiated State;

- the second is the triggering of an error, PUBLISH_ERROR Request, and shall lead back to the Publish Initiated State

- the third transition shall be triggered by the primitive PUBLISH_DEREGISTER Indication and shall lead to the Publish Deregister Initiated State;

- the fourth transition shall be triggered by the primitive PUBLISH_REGISTER Indication and shall lead to the Publish ReRegister Initiated State.

- There are two possible transitions from the Publish ReRegister Initiated State:

- the first is the triggering of an acknowledgement, PUBLISH_REGISTER_ACK Request, and shall lead to the Publish Initiated State;

- the second is the triggering of an error, PUBLISH_REGISTER_ERROR Request, and shall lead to the final state.

- There is only one possible transition from the Publish Deregister Initiated State; it is the triggering of an acknowledgement, PUBLISH_DEREGISTER_ACK Request, and shall lead to the final state.

#### Requests and Indications

##### REGISTER

###### Function

- The REGISTER Request primitive shall be used by the consumer application to initiate a PUBSUB Interaction with a subscription or to update an existing subscription for the specified subscription identifier.

- The REGISTER Indication primitive shall be used by the broker MAL to deliver a REGISTER Message to a broker and initiate a PUBSUB Interaction or to update an existing subscription for the specified subscription identifier.

###### Semantics

REGISTER Request and REGISTER Indication shall provide parameters as follows:

(REGISTER Message Header, Subscription)

###### When Generated

- A REGISTER Request may be used by the consumer application at any time to start a new subscription or when the consumer MAL is in the Registered State to update an existing subscription.

- A REGISTER Indication shall be generated by the broker MAL for a new subscription or when the broker MAL is in the Registered State for existing subscriptions for that consumer upon reception of a REGISTER Message, once checked via the Access Control interface, from a consumer.

###### Effect on Reception

- Reception of a REGISTER Request shall, once checked via the Access Control interface, cause the consumer MAL to initiate a PUBSUB Interaction by transmitting a REGISTER Message to the broker for a new subscription.

- The consumer MAL shall enter the Register Initiated State in this case.

- If the consumer MAL is in the Registered State, reception of a REGISTER Request shall, once checked via the Access Control interface, cause the consumer MAL to update the subscription by transmitting a REGISTER Message to the broker.

- The consumer MAL shall enter the ReRegister Initiated State in this case.

- On reception of a REGISTER Message by the broker MAL, once the message has been checked via the Access Control interface, the broker MAL shall enter the Register Initiated State if this is the first message in a new PUBSUB Interaction or enter the ReRegister Initiated State if currently in the Registered State and then pass a REGISTER Indication to the broker.

- The broker shall store the subscription of the consumer or update an existing subscription from the same consumer if the subscription identifier is already used by that consumer.

- The broker shall start processing the subscription at this point.

###### Message Header

- For the REGISTER Message the message header fields shall be as defined in 3.4 except for the fields in table 3-34.

- The contents of the Subscription structure, as specified in the operation template, shall immediately follow the message header.

Table 3-34:  REGISTER Message Header Fields

| Field | Value |
| --- | --- |
| From | Consumer |
| Authentication Id | Consumer Authentication Identifier |
| To | Broker |
| Interaction Type | PUBSUB |
| Interaction Stage | 1 |
| Transaction Id | Provided by consumer MAL |

##### REGISTER_ACK

###### Function

- The REGISTER_ACK Request primitive shall be used by the broker to acknowledge a PUBSUB Interaction subscription.

- The REGISTER_ACK Indication primitive shall be used by the consumer MAL to deliver a REGISTER_ACK Message to a consumer.

###### Semantics

REGISTER_ACK Request and REGISTER_ACK Indication shall provide parameters as follows:

(REGISTER_ACK Message Header)

###### When Generated

- A REGISTER_ACK Request shall be used by the broker with the broker MAL in either the Register Initiated State or ReRegister Initiated State to acknowledge the successful registration by a consumer in a PUBSUB Interaction.

- A REGISTER_ACK Indication shall be generated by the consumer MAL in either the Register Initiated State or ReRegister Initiated State upon reception of a REGISTER_ACK Message, once checked via the Access Control interface, from a broker.

###### Effect on Reception

- Reception of a REGISTER_ACK Request shall, once checked via the Access Control interface, cause the broker MAL to transmit the supplied acknowledgement as a REGISTER_ACK Message to the consumer.

- A broker MAL in the Register Initiated State or ReRegister Initiated State shall enter the Registered State.

- On reception of a REGISTER_ACK Message by the consumer MAL, once the message has been checked via the Access Control interface, the consumer MAL shall enter the Registered State and pass a REGISTER_ACK Indication to the consumer application.

###### Message Header

For the REGISTER_ACK Message the message header fields shall be as defined in 3.4 except for the fields in table 3-35.

Table 3-35:  REGISTER_ACK Message Header Fields

| Field | Value |
| --- | --- |
| From | Broker |
| Authentication Id | Broker Authentication Identifier |
| To | Consumer |
| Interaction Type | PUBSUB |
| Interaction Stage | 2 |
| Transaction Id | Transaction Id from initial message |

##### REGISTER_ERROR

###### Function

- The REGISTER_ERROR Request primitive shall be used by the broker to reject a subscription request and end a PUBSUB Interaction with an error.

- The REGISTER_ERROR Indication primitive shall be used by the consumer MAL to deliver a REGISTER_ERROR Message to a consumer.

###### Semantics

REGISTER_ERROR Request and REGISTER_ERROR Indication shall provide parameters as follows:

(REGISTER_ERROR Message Header, Error Number, Extra Information)

###### When Generated

- A REGISTER_ERROR Request shall be used by the broker with the broker MAL in either the Register Initiated State or ReRegister Initiated State to reject a register request.

- The broker may reject the register attempt for one of the following reasons:

- More subscriptions than the broker can support shall cause a TOO_MANY error to be sent. The extra information field of the error contains an Integer which provides the maximum number of subscriptions supported.

- Shutdown, the broker is shutting down. A SHUTDOWN error message shall be returned.

- Internal error, the broker has experienced an internal error. An INTERNAL error message shall be returned.

- UNKNOWN shall not be generated for subscriptions that identify keys that have not been currently registered by a publisher. This is because the consumer cannot know what entities are currently provided and which providers are currently registered.

- A REGISTER_ERROR Indication shall be generated by the consumer MAL in either the Register Initiated State or ReRegister Initiated State upon one of two events:

- the reception of a REGISTER_ERROR Message, once checked via the Access Control interface, from a broker;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of a REGISTER_ERROR Request shall, once checked via the Access Control interface, cause the broker MAL to transmit a REGISTER_ERROR Message to the consumer.

- The pattern shall end at this point for the broker.

- On reception of a REGISTER_ERROR Message by the consumer MAL, once the message has been checked via the Access Control interface, the consumer MAL shall end the interaction by passing the error to the consumer application.

###### Message Header

- For the REGISTER_ERROR Message the message header fields shall be the same as for the REGISTER_ACK Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error information shall immediately follow the message header.

##### PUBLISH_REGISTER

###### Function

- The PUBLISH_REGISTER Request primitive shall be used by the provider application to initiate a PUBSUB Interaction with the list of entities being published or to update an existing list.

- The PUBLISH_REGISTER Indication primitive shall be used by the broker MAL to deliver a PUBLISH_REGISTER Message to a broker and initiate a PUBSUB Interaction or to update an existing publish list if one exists for the specified provider.

###### Semantics

PUBLISH_REGISTER Request and PUBLISH_REGISTER Indication shall provide parameters as follows:

(PUBLISH_REGISTER Message Header)

###### When Generated

- A PUBLISH_REGISTER Request may be generated by the provider application at any time to start a publishing session or when the provider MAL is already in the Registered State to update an existing publish list.

- A PUBLISH_REGISTER Indication shall be generated by the broker MAL if a new publisher is detected or in the Publish Registered State for the provider upon reception of a PUBLISH_REGISTER Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of a PUBLISH_REGISTER Request shall, once checked via the Access Control interface, cause the provider MAL to initiate a PUBSUB Interaction by transmitting a PUBLISH_REGISTER Message to the broker.

- The provider MAL shall enter the Register Initiated State in this case.

- If the provider MAL is already in the Registered State, reception of a PUBLISH_REGISTER Request shall, once checked via the Access Control interface, cause the provider MAL to transmit a PUBLISH_REGISTER Message to the broker.

- The provider MAL shall enter the ReRegister Initiated State in this case.

- On reception of a PUBLISH_REGISTER Message by the broker MAL, once the message has been checked via the Access Control interface, the broker MAL shall enter the Publish Register Initiated State if this is the first message in a new PUBSUB Interaction with the provider or enter the Publish ReRegister Initiated State if currently in the Publish Registered State with that provider and then pass a PUBLISH_REGISTER Indication to the broker.

###### Message Header

- For the PUBLISH_REGISTER Message the message header fields shall be as defined in 3.4 except for the fields in table 3-36.

Table 3-36:  PUBLISH_REGISTER Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Broker |
| Interaction Type | PUBSUB |
| Interaction Stage | 3 |
| Transaction Id | Provided by provider MAL |

##### PUBLISH_REGISTER_ACK

###### Function

- The PUBLISH_REGISTER_ACK Request primitive shall be used by the broker to acknowledge a PUBSUB Interaction publish list from a provider.

- The PUBLISH_REGISTER_ACK Indication primitive shall be used by the provider MAL to deliver a PUBLISH_REGISTER_ACK Message to a provider.

###### Semantics

PUBLISH_REGISTER_ACK Request and PUBLISH_REGISTER_ACK Indication shall provide parameters as follows:

(PUBLISH_REGISTER Message Header)

###### When Generated

- A PUBLISH_REGISTER_ACK Request shall be used by the broker with the broker MAL in either the Publish Register Initiated State or Publish ReRegister Initiated State to acknowledge the successful registration by a provider in a PUBSUB Interaction.

- A PUBLISH_REGISTER_ACK Indication shall be generated by the provider MAL in either the Register Initiated State or ReRegister Initiated State upon reception of a PUBLISH_REGISTER_ACK Message, once checked via the Access Control interface, from a broker.

###### Effect on Reception

- Reception of a PUBLISH_REGISTER_ACK Request shall, once checked via the Access Control interface, cause the broker MAL to transmit the supplied acknowledgement as a PUBLISH_REGISTER_ACK Message to the provider.

- A broker MAL in the Publish Register Initiated State or Publish ReRegister Initiated State shall then enter the Registered State.

- On reception of a PUBLISH_REGISTER_ACK Message by the provider MAL, once the message has been checked via the Access Control interface, the provider MAL shall enter the Registered State and pass a PUBLISH_REGISTER_ACK Indication to the provider application.

###### Message Header

For the PUBLISH_REGISTER_ACK Message the message header fields shall be as defined in 3.4 except for the fields in table 3-37.

Table 3-37:  PUBLISH_REGISTER_ACK Message Header Fields

| Field | Value |
| --- | --- |
| From | Broker |
| Authentication Id | Broker Authentication Identifier |
| To | Provider |
| Interaction Type | PUBSUB |
| Interaction Stage | 4 |
| Transaction Id | Transaction Id from provider register message |

##### PUBLISH_REGISTER_ERROR

###### Function

- The PUBLISH_REGISTER_ERROR Request primitive shall be used by the broker to reject a publish registration request from a provider and end a PUBSUB Interaction with an error.

- The PUBLISH_REGISTER_ERROR Indication primitive shall be used by the provider MAL to deliver a PUBLISH_REGISTER_ERROR Message to a provider.

###### Semantics

PUBLISH_REGISTER_ERROR Request and PUBLISH_REGISTER_ERROR Indication shall provide parameters as follows:

(PUBLISH_REGISTER_ERROR Message Header, Error Number, Extra Information)

###### When Generated

- A PUBLISH_REGISTER_ERROR Request shall be used by the broker with the broker MAL in either the Publish Register Initiated State or Publish ReRegister Initiated State to reject a register request.

- The broker may reject the register attempt for one of the following reasons:

- More providers than the broker can support shall cause a TOO_MANY error to be sent. The extra information field of the error contains an Integer which provides the maximum number of providers supported.

- Shutdown, the broker is shutting down. A SHUTDOWN error message shall be returned.

- Internal error, the broker has experienced an internal error. An INTERNAL error message shall be returned.

- A PUBLISH_REGISTER_ERROR Indication shall be generated by the provider MAL in either the Register Initiated State or ReRegister Initiated State upon one of two events:

- the reception of a PUBLISH_REGISTER_ERROR Message, once checked via the Access Control interface, from a broker;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of a PUBLISH_REGISTER_ERROR Request shall, once checked via the Access Control interface, cause the broker MAL to transmit a PUBLISH_REGISTER_ERROR Message to the provider.

- The pattern shall end at this point for the broker.

- On reception of a PUBLISH_REGISTER_ERROR Message by the provider MAL, once the message has been checked via the Access Control interface, the provider MAL shall end the interaction by passing the error indication to the provider application.

###### Message Header

- For the PUBLISH_REGISTER_ERROR Message the message header fields shall be the same as for the PUBLISH_REGISTER_ACK Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error information structure shall immediately follow the message header.

##### PUBLISH

###### Function

- The PUBLISH Request primitive shall be used by the provider to publish an entity update.

- The PUBLISH Indication primitive shall be used by the broker MAL to deliver a PUBLISH Message to a broker.

###### Semantics

PUBLISH Request and PUBLISH Indication shall provide parameters as follows:

(PUBLISH Message Header, UpdateHeader,

<<Update Value Type>>, <<Update Value Type N>>)

###### When Generated

- A PUBLISH Request shall be used by the provider with the provider MAL in the Registered State to publish an entity update.

- A PUBLISH Indication shall be generated by the broker MAL in the Publish Initiated State upon reception of a PUBLISH Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of a PUBLISH Request shall, once checked via the Access Control interface, cause the provider MAL to transmit the supplied update as a PUBLISH Message to the broker.

- On reception of a PUBLISH Message by the broker MAL, once the message has been checked via the Access Control interface, the broker MAL shall pass a PUBLISH Indication to the broker application.

- The broker application shall match the Update to the subscriptions of registered consumers that are in the Registered State using the match rules in 3.5.6.5.

- The matched update shall be transmitted to the relevant consumers by the broker using a NOTIFY Request.

###### Message Header

- For the PUBLISH Message the message header fields shall be as defined in 3.4 except for the fields in table 3-38.

- The contents of the message body, as specified in the operation template, shall immediately follow the message header.

Table 3-38:  PUBLISH Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Broker |
| Interaction Type | PUBSUB |
| Interaction Stage | 5 |
| Transaction Id | Transaction Id from provider register message |

##### PUBLISH_ERROR

###### Function

- The PUBLISH_ERROR Request primitive shall be used by the broker to reject a publish request from a provider.

- The PUBLISH_ERROR Indication primitive shall be used by the provider MAL to deliver a PUBLISH_ERROR Message to a provider.

###### Semantics

PUBLISH_ERROR Request and PUBLISH_ERROR Indication shall provide parameters as follows:

(PUBLISH_ERROR Message Header, Error Number, )

###### When Generated

- A PUBLISH_ERROR Request shall be used by the broker with the broker MAL in the Publish Initiated State to reject a publish request.

- The broker may reject the publish attempt for one of the following reasons:

- Unknown provider: a provider has not previously registered for publishing. An INCORRECT_STATE error message shall be returned.

- Unknown Subscription Key: a provider has attempted to publish a an incorrect number of Subscription Keys. An UNKNOWN error shall be returned in this case;

- Shutdown: the broker is shutting down. A SHUTDOWN error message shall be returned.

- Internal error: the broker has experienced an internal error. An INTERNAL error message shall be returned.

- Communications/Encoding/Access Control errors shall be returned to a provider using this error message. This allows a provider to receive notification of underlying errors without the publishing overhead of acknowledging each PUBLISH Message.

- A PUBLISH_ERROR Indication shall be generated by the provider MAL in either the ReRegister Initiated State, Registered State or Deregister Initiated State upon one of two events:

- the reception of a PUBLISH_ERROR Message, once checked via the Access Control interface, from a broker;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of a PUBLISH_ERROR Request shall, once checked via the Access Control interface, cause the broker MAL to transmit a PUBLISH_ERROR Message to the provider.

- On reception of a PUBLISH_ERROR Message by the provider MAL, once the message has been checked via the Access Control interface, the provider MAL shall pass the error indication to the provider application.

###### Message Header

- For the PUBLISH_ERROR Message the message header fields shall be the same as for the PUBLISH Message except for the fields in table 3-39.

- In the case where an error is being return without a previous PUBLISH_REGISTER message, the Transaction Identifier shall be taken from the PUBLISH message.

- The Error information shall immediately follow the message header.

Table 3-39:  PUBLISH_ERROR Message Header Fields

| Field | Value |
| --- | --- |
| From | Broker |
| Authentication Id | Broker Authentication Identifier |
| To | Provider |
| Is Error Message | TRUE |

##### NOTIFY

###### Function

- The NOTIFY Request primitive shall be used by the broker to transmit an entity update to a consumer.

- The NOTIFY Indication primitive shall be used by the consumer MAL to deliver a NOTIFY Message to a consumer.

###### Semantics

NOTIFY Request and NOTIFY Indication shall provide parameters as follows:

(NOTIFY Message Header, Identifier, UpdateHeader,

<<Update Value Type>>, … <<Update Value Type N>>)

###### When Generated

- A NOTIFY Request shall be used by the broker with the broker MAL in the Registered State to transmit an entity update from a provider PUBLISH Message to a consumer.

- A NOTIFY Indication shall be generated by the consumer MAL in either the ReRegister Initiated State, Registered State or Deregister Initiated State upon reception of a NOTIFY Message, once checked via the Access Control interface, from a broker.

###### Effect on Reception

- Reception of a NOTIFY Request shall, once checked via the Access Control interface, cause the broker MAL to transmit the supplied subscription update as a NOTIFY Message to the consumer.

- On reception of a NOTIFY Message by the consumer MAL, once the message has been checked via the Access Control interface, the consumer MAL shall pass a NOTIFY Indication to the consumer application.

###### Message Header

- For the NOTIFY Message the message header fields shall be as defined in 3.4 except for the fields in table 3-40.

- The contents of the subscription update, as specified in the operation template, shall immediately follow the message header.

- The transaction identifier shall be the same as in the initial register message that created the first subscription. If several register requests have been sent for the same subscription (without any deregister requests in between), the transaction identifier of the first request shall be used.

Table 3-40:  NOTIFY Message Header Fields

| Field | Value |
| --- | --- |
| From | Broker |
| Authentication Id | Broker Authentication Identifier |
| To | Consumer |
| Interaction Type | PUBSUB |
| Interaction Stage | 6 |
| Transaction Id | Transaction Id from consumer register message |

##### NOTIFY_ERROR

###### Function

- The NOTIFY_ERROR Request primitive shall be used by the broker to inform a consumer of an error and end a PUBSUB Interaction.

- The NOTIFY_ERROR Indication primitive shall be used by the consumer MAL to deliver a NOTIFY_ERROR Message to a consumer.

###### Semantics

NOTIFY_ERROR Request and NOTIFY_ERROR Indication shall provide parameters as follows:

(NOTIFY_ERROR Message Header, Error Number)

###### When Generated

- A NOTIFY_ERROR Request shall be used by the broker with the broker MAL in the Registered State to inform a consumer of an error.

- The broker may send an error for one of the following reasons:

- Shutdown: the broker is shutting down. A SHUTDOWN error message shall be returned.

- Internal error: the broker has experienced an internal error. An INTERNAL error message shall be returned.

- A NOTIFY_ERROR Indication shall be generated by the consumer MAL in either the ReRegister Initiated State, Registered State or Deregister Initiated State upon one of two events:

- the reception of a NOTIFY_ERROR Message, once checked via the Access Control interface, from a broker;

- an error raised by the local communication layer.

###### Effect on Reception

- Reception of a NOTIFY_ERROR Request shall, once checked via the Access Control interface, cause the broker MAL to transmit a NOTIFY_ERROR Message to the consumer.

- The pattern shall end at this point for the broker.

- On reception of a NOTIFY_ERROR Message by the consumer MAL, once the message has been checked via the Access Control interface, the consumer MAL shall end the interaction by passing the error to the consumer application.

###### Message Header

- For the NOTIFY_ERROR Message the message header fields shall be the same as for the NOTIFY Message except for the ‘Is Error Message’ field which is set to TRUE.

- The Error information shall immediately follow the message header.

##### DEREGISTER

###### Function

- The DEREGISTER Request primitive shall be used by the consumer to end subscriptions for the specified subscription identifiers.

- The DEREGISTER Indication primitive shall be used by the broker MAL to deliver a DEREGISTER Message to a broker and end existing subscriptions for the specified subscription identifiers.

###### Semantics

DEREGISTER Request and DEREGISTER Indication shall provide parameters as follows:

(DEREGISTER Message Header, List<Identifier>)

###### When Generated

- A DEREGISTER Request shall be used by the consumer application with the consumer MAL in the Registered State at any time to end a subscription.

- A DEREGISTER Indication shall be generated by the broker MAL in the Registered State upon reception of a DEREGISTER Message, once checked via the Access Control interface, from a consumer.

###### Effect on Reception

- Reception of a DEREGISTER Request shall, once checked via the Access Control interface, cause the consumer MAL in the Registered State to end the set of subscriptions by transmitting a DEREGISTER Message to the broker.

- The consumer MAL shall enter the Deregister Initiated State for each identified subscription.

- On reception of a DEREGISTER Message by the broker MAL, once the message has been checked via the Access Control interface, the broker MAL shall enter the Deregister Initiated State for each of the identified subscriptions and pass a DEREGISTER Indication to the broker.

- The broker shall then remove the specified subscriptions of the consumer.

###### Message Header

- For the DEREGISTER Message the message header fields shall be as defined in 3.4 except for the fields in table 3-41.

- The contents of the subscription Identifier list, as specified in the operation template, shall immediately follow the message header.

Table 3-41:  DEREGISTER Message Header Fields

| Field | Value |
| --- | --- |
| From | Consumer |
| Authentication Id | Consumer Authentication Identifier |
| To | Broker |
| Interaction Type | PUBSUB |
| Interaction Stage | 7 |
| Transaction Id | Provided by consumer MAL |

##### DEREGISTER_ACK

###### Function

- The DEREGISTER_ACK Request primitive shall be used by the broker to acknowledge the termination of a PUBSUB Interaction subscription by the consumer.

- The DEREGISTER_ACK Indication primitive shall be used by the consumer MAL to deliver a DEREGISTER_ACK Message to a consumer.

###### Semantics

DEREGISTER_ACK Request and DEREGISTER_ACK Indication shall provide parameters as follows:

(DEREGISTER_ACK Message Header)

###### When Generated

- A DEREGISTER_ACK Request shall be used by the broker with a broker MAL in the Deregister Initiated State to acknowledge the successful deregistration by a consumer of a set of subscriptions in a PUBSUB Interaction.

- A DEREGISTER_ACK Indication shall be generated by the consumer MAL in the Deregister Initiated State upon reception of a DEREGISTER_ACK Message, once checked via the Access Control interface, from a broker.

###### Effect on Reception

- Reception of a DEREGISTER_ACK Request shall, once checked via the Access Control interface, cause the broker MAL to transmit a DEREGISTER_ACK Message to the consumer.

- The interaction shall end at this point for the broker for each of the identified subscriptions.

- On reception of a DEREGISTER_ACK Message by the consumer MAL in the Deregister Initiated State, once the message has been checked via the Access Control interface, the consumer MAL shall pass the DEREGISTER_ACK Indication to the consumer application.

- The interaction shall end here for the consumer for the set of subscriptions in the initiating DEREGISTER Message.

###### Message Header

For the DEREGISTER_ACK Message the message header fields shall be as defined in 3.4 except for the fields in table 3-42.

Table 3-42:  DEREGISTER_ACK Message Header Fields

| Field | Value |
| --- | --- |
| From | Broker |
| Authentication Id | Broker Authentication Identifier |
| To | Consumer |
| Interaction Type | PUBSUB |
| Interaction Stage | 8 |
| Transaction Id | Transaction Id from initial message |

##### PUBLISH_DEREGISTER

###### Function

- The PUBLISH_DEREGISTER Request primitive shall be used by the provider to end a PUBSUB Interaction.

- The PUBLISH_DEREGISTER Indication primitive shall be used by the broker MAL to deliver a PUBLISH_DEREGISTER Message to a broker and end a PUBSUB Interaction for the specified provider.

###### Semantics

PUBLISH_DEREGISTER Request and PUBLISH_DEREGISTER Indication shall provide parameters as follows:

(PUBLISH_DEREGISTER Message Header)

###### When Generated

- A PUBLISH_DEREGISTER Request shall be used by the provider application with the provider MAL in the Registered State to end the interaction.

- A PUBLISH_DEREGISTER Indication shall be generated by the broker MAL in the Publish Initiated State upon reception of a PUBLISH_DEREGISTER Message, once checked via the Access Control interface, from a provider.

###### Effect on Reception

- Reception of a PUBLISH_DEREGISTER Request shall, once checked via the Access Control interface, cause the provider MAL in the Registered State to request the end of the interaction by transmitting a PUBLISH_DEREGISTER Message to the broker.

- The provider MAL shall enter the Deregister Initiated State.

- On reception of a PUBLISH_DEREGISTER Message by the broker MAL, once the message has been checked via the Access Control interface, the broker MAL shall enter the Publish Deregister Initiated State.

- The broker shall then remove the provider from the list of allowed publishers.

###### Message Header

For the PUBLISH_DEREGISTER Message the message header fields shall be as defined in 3.4 except for the fields in table 3-43.

Table 3-43:  PUBLISH_DEREGISTER Message Header Fields

| Field | Value |
| --- | --- |
| From | Provider |
| Authentication Id | Provider Authentication Identifier |
| To | Broker |
| Interaction Type | PUBSUB |
| Interaction Stage | 9 |
| Transaction Id | Provided by provider MAL |

##### PUBLISH_DEREGISTER_ACK

###### Function

- The PUBLISH_DEREGISTER_ACK Request primitive shall be used by the broker to acknowledge the termination of a PUBSUB Interaction by the provider.

- The PUBLISH_DEREGISTER_ACK Indication primitive shall be used by the provider MAL to deliver a PUBLISH_DEREGISTER_ACK Message to a provider.

###### Semantics

PUBLISH_DEREGISTER_ACK Request and PUBLISH_DEREGISTER_ACK Indication shall provide parameters as follows:

(PUBLISH_DEREGISTER_ACK Message Header)

###### When Generated

- A PUBLISH_DEREGISTER_ACK Request shall be used by the broker with the broker MAL in the Publish Deregister Initiated State to acknowledge the successful deregistration by a provider in a PUBSUB Interaction.

- A PUBLISH_DEREGISTER_ACK Indication shall be generated by the provider MAL in the Deregister Initiated State upon reception of a PUBLISH_DEREGISTER_ACK Message, once checked via the Access Control interface, from a broker.

###### Effect on Reception

- Reception of a PUBLISH_DEREGISTER_ACK Request shall, once checked via the Access Control interface, cause the broker MAL to transmit the supplied acknowledgement as a PUBLISH_DEREGISTER_ACK Message to the provider.

- The interaction shall end at this point for the broker.

- On reception of a PUBLISH_DEREGISTER_ACK Message by the provider MAL in the Deregister Initiated State, once the message has been checked via the Access Control interface, the provider MAL shall pass the PUBLISH_DEREGISTER_ACK Indication to the provider application.

- The interaction shall end here for the provider.

###### Message Header

For the PUBLISH_DEREGISTER_ACK Message the message header fields shall be as defined in 3.4 except for the fields in table 3-44.

Table 3-44:  PUBLISH_DEREGISTER_ACK Message Header Fields

| Field | Value |
| --- | --- |
| From | Broker |
| Authentication Id | Broker Authentication Identifier |
| To | Provider |
| Interaction Type | PUBSUB |
| Interaction Stage | 10 |
| Transaction Id | Transaction Id from provider deregister message |

#### Example

The following example shows a simple example service that contains a single PUBLISH-SUBSCRIBE operation:

| Operation Identifier | testPubSub |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Subscription Keys | Identifier key1 Long key2 |
| Pattern Sequence | Message | Type Signature |
| OUT | PUBLISH/NOTIFY | Boolean field1 Integer field2 TestNotify field3 |

The TestNotify structure is defined below:

| Name | TestNotify |
| --- | --- |
| Extends | Composite |
| Short Form Part | Example Only |
| Field | Type | Nullable | Comment |
| time | Time | Yes | Example Time item |
| value | Integer | Yes | Example Integer item |

To register for this PUBLISH-SUBSCRIBE pattern, a consumer shall send the following message:

It contains a standard pattern body for the register message. This shall result in the following acknowledgement message being sent:

To publish an update on this topic a previously registered provider would send the following message to the message broker. In this example two updates are being generated at the same time:

When an update is required the following notify message will be sent from the message broker to the consumer:

No acknowledgment of the notify message shall be sent by the consumer.

When the consumer wants to deregister, the following message would be sent:

Which would result in the following acknowledgment being received:

NOTE	–	An actual service specification, rather than the example given here, would fully specify the meaning of, and required values of, all structures used by the service.

## Access Control Interface

The MAL Specification does not make any assumption on the applicable security requirements for a concrete deployment. To this end the specification provides a generic Access Control Interface to formalise the interactions with any deployment specific Access Control component.

The security requirements of concrete deployments may vary from none to extremely stringent confidentiality, integrity, and availability requirements. For many legacy and still operational space missions, no authentication, authorization or assurances for confidentiality of the communication between the space and ground have been implemented. For many other space missions various levels of security requirements have been made applicable to the space to ground interface as well as to the ground to ground interactions (e.g. between control centers).

Hence MAL specification needs to support the wide spectrum of  scenarios, in which a simple service may broadcast non-sensitive information to the general public as well as scenarios with elaborate certificate based authentications, rule and content-based authorizations and end-to-end encryption of communication with sophisticated key management systems.

The MO Reference Model [1] and the Mission Operations Concept Green Book [D1] provide a more detailed consideration of the security aspects, examples of typical deployment scenarios for space mission and recommended security profiles.

## The Authentication ID in the MAL header supports accordingly the full ranges of authentication means from none to a simple text based user name and password up to token or certificate based authentications. The MAL is positioned between the transport layer and the application layer. Upon reception of any message from the transport layer and before reaching up to the application layer, MAL passes every MAL message through this specified Access Control interface to the Access Control component. It is the delegated responsibility of the deployment specific implementation of an Access Control component to ensure the enforcement of the necessary security assurances for a particular deployment, using the information provided in the Authentication Id field of every MAL message and the message itself. Only upon an positive check response from the Access Control component through the standardised Access Control Interface, MAL will pass the message to the application layer.

### Check message Interaction

#### Overview

The CHECK pattern is similar to the REQUEST Interaction Pattern: a MAL Message is passed in and the Access Control component responds with a return MAL message. No acknowledgement other than the response is sent:

Figure 3-26:  CHECK Access Control Pattern Message Sequence

#### Description

The CHECK pattern provides a simple request/response message exchange that is used by a MAL implementation to perform Access Control.

NOTE	–	It is not expected that this pattern will be implemented via a message transport, as it is expected to be implemented as a local API used by the MAL.  It is shown here as a pattern for consistency.

#### Usage

- The CHECK pattern shall be used only by the MAL for the checking of incoming and outgoing messages.  It is not used by any other component.

- A compliant MAL implementation shall follow the sequences defined in sections 4 and 5 of reference [1] for interacting with an access control component.

- A broker in a Publish Subscribe pattern shall also submit any NOTIFY and PUBLISH Messages to its Access Control component.

- Access to sensitive data distributed via the PUBSUB pattern shall be filtered at this point if required.

NOTE	–	For the restriction of sensitive data it is legitimate for a broker to integrate the CHECK logic into the subscription matching logic.

#### Error Handling

Figure 3-27:  CHECK Access Control Pattern Error Sequence

- The response shall be replaced with an error message (see section 5) if an error occurs during the processing of the operation (figure ).

- Either the response or the error message shall be returned but never both.

#### Operation Template

The CHECK pattern template is below:

Table 3-45:  CHECK Operation Template

| Interaction Pattern | CHECK |
| --- | --- |
| Pattern Sequence | Message | Type Signature |
| IN | CHECK | MAL message |
| OUT | RESPONSE | MAL message |

#### Primitives

The pattern is not an abstract interface that provides interoperability.  However, it is a function that is required by the MAL.

Table 3-46:  CHECK Primitive List

Primitive

CHECK

RESPONSE

ERROR

#### State Charts

No state charts are provided for this pattern.  The MAL shall initiate the pattern using the CHECK primitive and shall block until either the Response or Error Indication is received.

#### Requests and Indications

##### CHECK

###### Function

The CHECK Request primitive shall be used by the MAL to initiate a CHECK Interaction.

###### Semantics

CHECK Request shall provide parameters as follows:

(MAL Message)

###### When Generated

- CHECK Request shall be generated by the MAL after reception of a message from either the application or from a transport.

- It is implementation and deployment specific what checks an implementation of the Access Control component shall perform upon reception of a CHECK Request.

##### RESPONSE

###### Function

The RESPONSE Indication primitive shall be used by the Access Control component to deliver a RESPONSE Message to the MAL.

###### Semantics

RESPONSE Indication shall provide parameters as follows:

(MAL Message)

###### When Generated

RESPONSE Indication shall be generated upon reception of a RESPONSE Message from the Access Control component.

###### Effect on Reception

- On reception of a RESPONSE Indication the MAL shall end the interaction pattern with success.

- The returned message shall then be used by the MAL from that point onwards.

##### ERROR

###### Function

The ERROR Indication primitive shall be used by the Access Control component to end a CHECK Interaction with an error.

###### Semantics

ERROR Indication shall provide parameters as follows:

(Error Number, Extra Information)

###### When Generated

- An ERROR Indication shall be generated upon reception of an ERROR Message from the Access Control component.

- The Access Control component shall return AUTHENTICATION_FAIL if the supplied message fails authentication checks. These checks are implementation and deployment specific.

- The Access Control component shall return AUTHORISATION_FAIL if the authenticated supplied message fails authorisation checks. These checks are implementation and deployment specific.

###### Effect on Reception

- On reception of an ERROR Indication the MAL shall end the interaction with an error.

- If the Access Control error is to be transmitted to another MAL then the resultant error message shall not be passed to the Access Control component as it originated from that.

- The behaviour of the MAL from this point onwards is defined in reference [1].

# MAL Data Type Specification

## Overview

### General

The specification of the abstract interfaces and services details the structures passed as the message bodies and message returns of the interaction patterns and operations. This section details the MAL data type specification, the rules for its use with the MAL, the types and structures it contains, and the rules allowed for the combination of these.

Other data type specification languages (such as XML Schema [6]) may be used to specify the message bodies in service specifications; however, support for these other data type specification languages in a particular technology mapping may not be universal and may limit use of a specification to specific deployments.

### Abstract and Concrete Types

The MAL type specification allows the definition of two basic categories of types, the first being abstract types, and the second being concrete types.

Abstract types are represented in a table as illustrated below:

| Name | <<Name>> |
| --- | --- |
| Extends | <<Extension Type Name>> |
| Abstract |

The name of the type is given in the Name field and the name of the abstract type that this type extends is given in the ‘Extends’ field.

Concrete types are represented in a table as illustrated below:

| Name | <<Name>> |
| --- | --- |
| Extends | <<Extension Type Name>> |
| Short Form Part | <<Short Form Part>> |

Each concrete type is defined with a numerical short form part that is expected to be used by efficient encodings when required to hold type information. Each specification that defines types shall number each concrete type in the appropriate field starting from 1.

To avoid number conflicts between types defined in different areas, the absolute short form of the type is obtained by combining the area number (as a UShort), the area version (as a UShort), and the short form part from the type definition (as an Integer).

In the context of the MAL specification the area number of ‘1’ is used.

### Fundamentals

The base type for all types and structures is Element. Two other fundamental types exist, Composite and Attribute. Only the MAL specification (this document) is allowed to define fundamental types.

Fundament types are represented in a table as illustrated below:

| Name | Element |
| --- | --- |
| Extends |  |
| Abstract |

### Attributes

Attributes are the simplest MAL type; they cannot be decomposed into any smaller elements and are used to build more complex structures.

Only the MAL specification (this document) is allowed to define attribute types.

Attribute types are represented in a table as illustrated below:

| Name | <<Attribute Name>> |
| --- | --- |
| Extends | Attribute |
| Short Form Part | <<Short Form Part>> |

All attribute types extend the fundamental type ‘Attribute’. They are also defined in 4.2.4, but the actual representation, or encoding, of them is completely dependent on the language and transport/encoding mapping used. However, because the limits and behaviour of the types are constant (defined here), the informational content is preserved when moving between mappings.

For example, a Boolean value may be represented by a single bit in some encodings or by the text strings ‘True/False’ in others; however, the meaning of the value is identical regardless of the encoding used.

### Composites

Composites are represented in a table as illustrated below:

| Name | TestBody |
| --- | --- |
| Extends | Composite |
| Short Form Part | 123 |
| Field | Type | Nullable | Comment |
| FirstItem | String | Yes | Example String item. |
| SecondItem | Integer | Yes | Example Integer item. |

| Name | ExampleStructure |
| --- | --- |
| Extends | Composite |
| Short Form Part | 456 |
| Field | Type | Nullable | Comment |
| first_item | String | Yes | Example String item. |
| second_item | Integer | Yes | Example Integer item. |
| third_item | TestBody | Yes | Contained structure. |

The ExampleStructure would decompose to a sequence of:

| Field | Type | Comment |
| --- | --- | --- |
| first_item | String | from ExampleStructure. |
| second_item | Integer | from ExampleStructure. |
| FirstItem | String | from contained TestBody. |
| SecondItem | Integer | from contained TestBody. |

The Nullable’ column indicates whether the field is permitted to contain a Null value. If the field is set to Yes then it is allowed to contain a Null value, if it is No then it is not.

### Polymorphism - Composite extension

Composite structures can be extended however there are some restrictions:

- An abstract Composite can be extended by another abstract Composite;

- An abstract Composite can be extended by a concrete Composite;

- A concrete Composite can only extend one unique abstract Composite; Therefore, a concrete Composite cannot extend multiple Composites at the same time;

- A concrete Composite cannot be extended further.

NOTE	–	It is not permitted to extend a non-abstract composite as an issue arises when the extended composite is used in place of the base composite (which is not marked as abstract). Because there is no indication to the receiving application that the message contains extra information, it is not possible to decode the message correctly. Some transport encodings may be able to support this, but many will not be able to. Therefore only abstract composites shall be extended.

The following structures presents one example of an abstract Composite being extended by a concrete Composite.

| Name | AbstractComposite |
| --- | --- |
| Extends | Composite |
| Abstract |
| Field | Type | Nullable | Comment |
| FirstItem | String | Yes | Example String item. |
| SecondItem | Integer | Yes | Example Integer item. |

| Name | ComplexStructure |
| --- | --- |
| Extends | AbstractComposite |
| Short Form Part | 345 |
| Field | Type | Nullable | Comment |
| extra_item | Boolean | Yes | Extra Boolean item. |
| second_item | Integer | Yes | Example Integer item. |
| third_item | TestBody | Yes | Contained structure. |

This shows that ComplexStructure can be considered an extension of AbstractComposite and contains all the contents of AbstractComposite plus its own extra items:

| Field | Type | Comment |
| --- | --- | --- |
| FirstItem | String | from AbstractComposite. |
| SecondItem | Integer | from AbstractComposite. |
| extra_item | Boolean | from ComplexStructure. |
| second_item | Integer | from ComplexStructure. |
| FirstItem | String | from ComplexStructure contained TestBody. |
| SecondItem | Integer | from ComplexStructure contained TestBody. |

Good practices for service design:

Note that a sound architectural design favours the “Composition over inheritance” principle (or composite reuse principle). This principle states that polymorphic behaviour and code reuse should be achieved by their composition (by containing other composite structures) rather than inheritance from a base or parent structure. This is an often-stated principle in object-oriented programming. MO Architects are advised to take this principle into consideration when defining new services.

### Polymorphism - Abstract elements in Composites

The MAL data type specification does allow composites to contain an abstract type. The fields within a composite can be abstract or concrete types. Note that by defining an abstract field within a composite, the composite itself does not become abstract.

This includes the containment of the abstract Attribute type, and abstract Composite type. It is also permitted to create composites that have fields defined as Attribute.

For example the following is permitted:

| Name | ConcreteCompositeA |
| --- | --- |
| Extends | Composite |
| Short Form Part | 654321 |
| Field | Type | Nullable | Comment |
| SomeItem | Attribute | Yes | Example attribute item. |

And the following is also permitted:

| Name | ConcreteCompositeB |
| --- | --- |
| Extends | Composite |
| Short Form Part | 123456 |
| Field | Type | Nullable | Comment |
| AnotherItem | TheAbstractComposite | Yes | Example abstract type. |
| FurtherItem | MyAbstractComposite | Yes | Example abstract type. |

### Representing Enumerations

Enumerations are defined sets of possible values. All enumerations are extensions of the fundamental Element type and therefore can only be used to replace abstract Elements in message bodies. They are represented as shown below:

| Name | ExampleEnum |
| --- | --- |
| Short Form Part | 789 |
| Enumeration Value | Numeric Value | Comment |
| FIRST | 1 | First enumeration possible value. |
| SECOND | 2 | Second enumeration value. |
| OTHER | 3 | Etc. |
| LAST | 4 | Last enumeration value. |

The ‘Numeric Value’ field is a simplified numerical version of the enumeration and has the UShort range. It is expected to be used in efficient encodings and transport mappings.

### Representing Lists

A list is an arbitrary-length sequence of items. Lists can be created of any Attribute, Enumeration, or Composite. Lists are represented in the specifications as below:

List<ExampleStructure>

The List is shown as having a ‘type’ of ExampleStructure and is therefore a list of ExampleStructures. A list has a length part, but whether an actual length field is required is dependent on the encoding specification. For example, a binary encoding may include an initial length field to allow correct decommutation, whereas an XML-based encoding would not require this because XML tags denote the end of the list. [6]

The ‘Short Form Part’ for a List is the negative version of the ‘Short Form Part’ of the list type. For example, as the short form part for Integer is ‘11’, the short form part of a list of Integers would be ‘-11’.

### Polymorphism - Abstract elements in Lists

The MAL data type specification allows abstract Lists to be specified. An example is presented:

- elements (List<AbstractBaseType>)

  - element [0] - ConcreteTypeA

  - element [1] - ConcreteTypeB

  - element [2] - ConcreteTypeA

  - element [3] – ConcreteTypeC

- Note that if an abstract list is specified, some Encoders may have to also carry the ‘Short Form Part’ for each of the elements in that list in order to be able to decode them. This is however Encoder-specific.

### Representing Object References

An object reference is a reference to an instance of an MO Object. Object references use the ObjectRef Attribute type as defined in section 4.4.19. When specifying an object reference, the reference shall point to an MO Object (which is defined using MAL::Object). Object references are represented in the service specifications as below:

ObjectRef<ExampleStructure>

The object reference is shown as having a ‘type’ of ExampleStructure and is therefore a reference to an MO Object of ExampleStructure type.

In case the object reference type is unknown, the representation shall use the MAL base type Element as follows:

ObjectRef<Element>

### Representing NULL

In some message structures it may be required to have optional components. To this end it is required to be able to represent, for each type of component, the concept of NULL. This is separate and completely different from the concept of empty.  For example, an empty string (“”) is different from a NULL string which has no value. Language mappings must have the ability to represent NULL in messages, and transport mappings must have the ability to transport NULL.

Each composite structure definition contains an entry for each field denoting whether that field shall be allowed to contain the NULL value.

### Message Bodies

When the message body of an operation is specified using the MAL data type specification, it is permitted to use the concept of multiple part messages, where the body of a message is specified using more than one type (see 4).

Any type in a message body may be an abstract type.

## Fundamentals

### Element

Element is the base type of all data constructs. All types that make up the MAL data model are derived from it.

| Name | Element |
| --- | --- |
| Extends |  |
| Abstract |

### Attribute

Attribute is the base type of all attributes of the MAL data model. Attributes are contained within Composites and are used to build complex structures that make the data model.

| Name | Attribute |
| --- | --- |
| Extends | Element |
| Abstract |

### Composite

Composite is the base structure for composite structures that contain a set of elements.

| Name | Composite |
| --- | --- |
| Extends | Element |
| Abstract |

### Object

Object is the base structure for all objects in the MAL data model. Objects are representations of complex data types with two specific characteristics: Objects have a unique and an immutable identity and can be referenced unambiguously by other objects.

| Name | Object |
| --- | --- |
| Extends | Composite |
| Abstract |

## Objects

### Overview

Objects are representations of complex data types with two specific characteristics: Objects have a unique and an immutable identity and can be referenced unambiguously, using the MAL ObjectRef Type 4.4.19. Objects are used to represent and formally specify the complex data model in service specifications.

Object Type is an extension of the Composite type. All Objects are to be modelled as  specialisations of the Object Type, where the first field shall hold the identity of the object, using the ObjectIdentity MAL data type. The identity of an Object is represented in more detail in the next section.

Objects can be explicitly referenced by other Composite data structures with the use of the ObjectRef MAL data type. The ObjectRef data type is described in section 4.1.7.1.

### Object Identity

Each Object has an immutable and unique Object Identity. The Object Identity is composed of a Domain, an Area, a Type, a Key, and an Object Version. This combination allows the objects to be uniquely identified across the different domain and areas.

Table 4-1:  Object Identity Fields

| Field | Type | Value |
| --- | --- | --- |
| Domain | List<Identifier> | Domain of the object |
| Area | Identifier | Area of the object |
| Type | Identifier | Type of the object |
| Key | Identifier | Key of the Object |
| Object Version | UInteger | Version of the Object, starting at 1 |

An ObjectIdentity MAL Composite is defined in this standard and it includes the exact same fields of the Object Identity as presented above. This allows its direct usage in MAL Composite data structures in order to represent the identity of a certain MO Object.

The Domain shall be formed as follows:

- The Domain shall be defined as a list of identifiers.

- The most significant domain part shall be listed first in the list (for example, Agency), and each subsequent domain identifier in the list narrows the preceding domain.

- Each Identifier part of the Domain shall be allowed the full range of Identifier values with the restriction that it is NOT allowed to contain the ‘.’ character.

The combination of the fields Area and Type shall be used to determine the structure of the Object Body.

The Key field is unique within the scope of the Domain, for a given Area and Type.

If an MO Object does not have versions, then the Version field shall be populated with a ‘1’.

### Representation Example

As previously defined, an MO Object can be defined using the MAL::Object data type. The following table presents an example of how an MO Object is expected to be represented in the specifications.

The MO Object is called ExampleStructure and includes a first field with an ObjectIdentity MAL type, and two additional example fields.

| Name | ExampleStructure |
| --- | --- |
| Extends | Object |
| Short Form Part | 123 |
| Field | Type | Nullable | Comment |
| identity | ObjectIdentity | No | The identity of this MO Object. |
| myField1 | Integer | Yes | An example of a field in the MO Object. |
| myField2 | String | Yes | An example of a field in the MO Object. |

## Attributes

### Blob

The Blob structure is used to hold binary object attributes. It is a variable-length, unbounded, octet array. The distinction between this type and a list of Octet attributes is that this type may allow language mappings and encodings to use more efficient or appropriate representations.

| Name | Blob |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 1 |

### Boolean

The Boolean structure is used to hold Boolean attributes. Possible values are ‘True’ or ‘False’.

| Name | Boolean |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 2 |

### Duration

The Duration structure is used to hold Duration attributes up to milliseconds. It represents a length of time in seconds. Resolutions lower than seconds, shall be contained in a fractional component of this attribute.

| Name | Duration |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 3 |

### Float

The Float structure is used to hold floating point attributes using the IEEE 754 32-bit range. [3]

Three special values exist for this type: POSITIVE_INFINITY, NEGATIVE_INFINITY, and NaN (Not A Number).

| Name | Float |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 4 |

### Double

The Double structure is used to hold floating point attributes using the IEEE 754 64-bit range. [3]

Three special values exist for this type: POSITIVE_INFINITY, NEGATIVE_INFINITY, and NaN (Not A Number).

| Name | Double |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 5 |

### Identifier

The Identifier structure is used to hold an identifier and can be used for indexing. It is a variable-length, unbounded, Unicode string. For some encoding/decoding bindings, the use of a numeric value might be appropriate for this Attribute, for example, via a dictionary. [4]

| Name | Identifier |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 6 |

### Octet

The Octet structure is used to hold 8-bit signed attributes. The permitted range is -128 to 127.

| Name | Octet |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 7 |

### UOctet

The UOctet structure is used to hold 8-bit unsigned attributes. The permitted range is 0 to 255.

| Name | UOctet |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 8 |

### Short

The Short structure is used to hold 16-bit signed attributes. The permitted range is -32768 to 32767.

| Name | Short |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 9 |

### UShort

The UShort structure is used to hold 16-bit unsigned attributes. The permitted range is 0 to 65535.

| Name | UShort |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 10 |

### Integer

The Integer structure is used to hold 32-bit signed attributes. The permitted range is -2147483648 to 2147483647.

| Name | Integer |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 11 |

### UInteger

The UInteger structure is used to hold 32-bit unsigned attributes. The permitted range is 0 to 4294967295.

| Name | UInteger |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 12 |

### Long

The Long structure is used to hold 64-bit signed attributes. The permitted range is -9223372036854775808 to 9223372036854775807.

| Name | Long |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 13 |

### ULong

The ULong structure is used to hold 64-bit unsigned attributes. The permitted range is 0 to 18446744073709551615.

| Name | ULong |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 14 |

### String

The String structure is used to hold String attributes. It is a variable-length, unbounded, Unicode string. [4]

| Name | String |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 15 |

### Time

The Time structure is used to hold absolute time attributes. It represents an absolute date and time to millisecond resolution.

| Name | Time |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 16 |

### FineTime

The FineTime structure is used to hold high-resolution absolute time attributes. It represents an absolute date and time to nanosecond resolution.

| Name | FineTime |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 17 |

### URI

The URI structure is used to hold URI addresses. It is a variable-length, unbounded, Unicode string. [4] [5]

| Name | URI |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 18 |

### ObjectRef

The ObjectRef structure is used to hold references to MO Objects. The ObjectRef type shall be represented in specifications as ObjectRef<T> as presented in section 4.1.7.1.

| Name | ObjectRef |
| --- | --- |
| Extends | Attribute |
| Short Form Part | 19 |

## Data Structures

### InteractionType Enumeration

InteractionType is an enumeration holding the possible interaction pattern types.

| Name | InteractionType |
| --- | --- |
| Short Form Part | 101 |
| Enumeration Value | Numeric Value | Comment |
| SEND | 1 | Used for Send interactions. |
| SUBMIT | 2 | Used for Submit interactions. |
| REQUEST | 3 | Used for Request interactions. |
| INVOKE | 4 | Used for Invoke interactions. |
| PROGRESS | 5 | Used for Progress interactions. |
| PUBSUB | 6 | Used for Publish/Subscribe interactions. |

### SessionType Enumeration

SessionType is an enumeration holding the session types.

| Name | SessionType |
| --- | --- |
| Short Form Part | 102 |
| Enumeration Value | Numeric Value | Comment |
| LIVE | 1 | Used for Live sessions. |
| SIMULATION | 2 | Used for Simulation sessions. |
| REPLAY | 3 | Used for Replay sessions. |

### QoSLevel Enumeration

QoSLevel is an enumeration holding the possible QoS levels.

| Name | QoSLevel |
| --- | --- |
| Short Form Part | 103 |
| Enumeration Value | Numeric Value | Comment |
| BESTEFFORT | 1 | Used for Best Effort QoS Level. |
| ASSURED | 2 | Used for Assured QoS Level. |
| QUEUED | 3 | Used for Queued QoS Level. |
| TIMELY | 4 | Used for Timely QoS Level. |

### AttributeType Enumeration

AttributeType is an enumeration holding the defined MAL Attribute types.

| Name | AttributeType |
| --- | --- |
| Short Form Part | 104 |
| Enumeration Value | Numerical Value | Comment |
| BLOB | 1 | Blob type. |
| BOOLEAN | 2 | Boolean type. |
| DURATION | 3 | Duration type. |
| FLOAT | 4 | Float type. |
| DOUBLE | 5 | Double type. |
| IDENTIFIER | 6 | Identifier type. |
| OCTET | 7 | Octet type. |
| UOCTET | 8 | UOctet type. |
| SHORT | 9 | Short type. |
| USHORT | 10 | UShort type. |
| INTEGER | 11 | Integer type. |
| UINTEGER | 12 | UInteger type. |
| LONG | 13 | Long type. |
| ULONG | 14 | ULong type. |
| STRING | 15 | String type. |
| TIME | 16 | Time type. |
| FINETIME | 17 | FineTime type. |
| URI | 18 | URI type. |
| OBJECTREF | 19 | ObjectRef type. |

### AreaNumber

AreaNumber is an enumeration holding the known existing area numbers in use. Note that the table follows the corresponding MAL Area numbers available on the SANA registry. [7]

| Name | AreaNumber |
| --- | --- |
| Short Form Part | 105 |
| Enumeration Value | Numeric Value | Comment |
| MAL | 1 | The MAL area number. |
| COM | 2 | The COM area number. The COM is deprecated, therefore this area number is reserved for backward compatibility. |
| COMMON | 3 | The Common area number. |
| MC | 4 | The Monitor and Control area number. |
| MPS | 5 | The Mission Planning and Scheduling area number. |
| SM | 7 | The Software Management area number. |
| MDPD | 9 | The Mission Data Product Distribution area number. |

### Subscription

The Subscription structure is used when subscribing for updates using the PUBSUB interaction pattern. It contains a single identifier that identifies the subscription being defined and a set of entities being requested.

| Name | Subscription |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1001 |
| Field | Type | Nullable | Comment |
| subscriptionId | Identifier | No | The identifier of this subscription. |
| domain | List<Identifier> | Yes | Optional domain identifier. If NULL, the subscription shall match with any domain. |
| filters | List<SubscriptionFilter> | Yes | The list of filters that are being selected for this subscription. The list of filters must be ANDed together. If NULL, the subscription will not filter specific keys. |

### SubscriptionFilter

The SubscriptionFilter structure is used when subscribing for updates using the PUBSUB interaction pattern. It contains a single identifier that identifies the subscription key name and the set of values to be registered for the defined key name.

| Name | SubscriptionFilter |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1002 |
| Field | Type | Nullable | Comment |
| name | Identifier | No | The identifier name of the key. |
| values | List<MAL::Attribute> | No | The list of values that are being subscribed for this key. These shall be ORed together. |

### UpdateHeader

The UpdateHeader structure is used by updates using the PUBSUB interaction pattern. It holds information that identifies a single update.

| Name | UpdateHeader |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1003 |
| Field | Type | Nullable | Comment |
| source | Identifier | Yes | The source of the update, usually a PUBSUB provider. |
| keyValues | List<Attribute> | Yes | The values for the PUBSUB keys. The values shall be ordered according to the defined keys. |

### IdBooleanPair

IdBooleanPair is a simple pair type of an identifier and Boolean value.

| Name | IdBooleanPair |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1004 |
| Field | Type | Nullable | Comment |
| id | Identifier | Yes | The Identifier value. |
| value | Boolean | Yes | The Boolean value. |

### Pair

Pair is a simple composite structure for holding pairs. The pairs can be user-defined attributes.

| Name | Pair |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1005 |
| Field | Type | Nullable | Comment |
| first | Attribute | Yes | The attribute value for the first element of this pair. |
| second | Attribute | Yes | The attribute value for the second element of this pair. |

### NamedValue

The NamedValue structure represents a simple pair type of an identifier and abstract attribute value.

| Name | NamedValue |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1006 |
| Field | Type | Nullable | Comment |
| name | Identifier | Yes | The Identifier value. |
| value | Attribute | Yes | The Attribute value. |

### File

The File structure represents a File and holds details about a File. It can also, optionally, hold a BLOB of the file data. The file type is denoted using the internet MIME media types; the list of official MIME types is held in reference [2].

| Name | File |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1007 |
| Field | Type | Nullable | Comment |
| name | String | No | The file name. |
| mimeType | String | Yes | The MIME type of the file, NULL if not known. |
| creationDate | Time | Yes | The creation timestamp of the file, NULL if not known. |
| modificationDate | Time | Yes | The last modification timestamp of the file, NULL if not known. |
| size | ULong | Yes | The size of the file, NULL if not known. |
| content | Blob | Yes | The contents of the file, NULL if not supplied. |
| metaData | List<NamedValue> | Yes | A list of extra metadata for the file. |

### ObjectIdentity

The ObjectIdentity structure represents the object identity of an MO Object.

| Name | ObjectIdentity |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1008 |
| Field | Type | Nullable | Comment |
| domain | List<Identifier> | No | The domain of the MO Object being referenced. |
| area | Identifier | No | The area of the MO Object being referenced. |
| type | Identifier | No | The type of the MO Object being referenced. |
| key | Identifier | No | The key of the MO Object being referenced. |
| version | UInteger | No | The version of the MO Object being referenced. |

### ServiceId

The ServiceId composite represents a specific service in MO.

| Name | ServiceId |
| --- | --- |
| Extends | Composite |
| Short Form Part | 1009 |
| Field | Type | Nullable | Comment |
| serviceArea | UOctet | No | The area of this service taken from the numeric Area identifier of the service specification. |
| serviceNumber | UShort | No | The service taken from the numeric Service identifier of the service specification. |
| keyServiceVersion | UOctet | No | The version of this service taken from the Service Version of the service specification. |

# MAL Errors

Each operation shall list any errors, specific to that operation over and above any standard errors, that can be raised by an implementation. Error codes occupy the UInteger range and for an operation should start at zero ‘0’ and increment; standard errors start at 65536, 0x10000 in hex, and increment; operation-specific errors shall therefore remain inside the inclusive range of 0 to 65535.

The following table lists the standard errors:

Table 5-1:  Standard MAL Error Codes

| Error | Error # | Comment |
| --- | --- | --- |
| DELIVERY_FAILED | 65536 | Confirmed communication error. |
| DELIVERY_TIMEDOUT | 65537 | Unconfirmed communication error. |
| DELIVERY_DELAYED | 65538 | Message queued somewhere awaiting contact. |
| DESTINATION_UNKNOWN | 65539 | Destination cannot be contacted. |
| DESTINATION_TRANSIENT | 65540 | Destination middleware reports destination application does not exist. |
| DESTINATION_LOST | 65541 | Destination lost halfway through conversation. |
| AUTHENTICATION_FAIL | 65542 | A failure to authenticate the message correctly. |
| AUTHORISATION_FAIL | 65543 | A failure in the MAL to authorise the message. |
| ENCRYPTION_FAIL | 65544 | A failure in the MAL to encrypt/decrypt the message. |
| UNSUPPORTED_AREA | 65545 | The destination does not support the service area. |
| UNSUPPORTED_OPERATION | 65546 | The destination does not support the operation. |
| UNSUPPORTED_VERSION | 65547 | The destination does not support the service version. |
| BAD_ENCODING | 65548 | The destination was unable to decode the message. |
| INTERNAL | 65549 | An internal error has occurred. |
| UNKNOWN | 65550 | Operation specific. |
| INCORRECT_STATE | 65551 | The destination was not in the correct state for the received message. |
| TOO_MANY | 65552 | Maximum number of subscriptions or providers of a broker has been exceeded. |
| SHUTDOWN | 65553 | The component is being shutdown. |
| TRANSACTION_TIMEOUT | 65554 | The interaction exceeded a certain timeout duration. |

Only two errors are possible from the MAL and below with regards to Authentication and Authorisation.  They are concerned with message-level issues and do not cover login issues such as an incorrect username/password combination.

NOTE	–	The authentication and authorisation failure messages are very generic in nature; it is possible that a weakness in an underlying protocol or authentication mechanism could be exploited if too much information is returned about the specific nature of an authentication or authorisation failure.

# Service Specification XML

This specification defines a normative XML schema for validating MO service specifications. The use of XML for service specification provides a machine-readable format rather than the text-based document format. [6]

The published specifications and XML Schema are held in an online SANA registry [7] located:

http://sanaregistry.org/r/moschemas/

The XML Schema that is used to validate the actual XML service specifications is located:

http://sanaregistry.org/r/moschemas/ServiceSchema-v.v.xsd

The normative XML for the MAL specification, validated against the XML schema, is located:

http://sanaregistry.org/r/moschemas/ServiceDefMAL-v.v.xml

Where the ‘v.v’ part is replaced with the issue number of the corresponding document.

The latest version of any specification shall always be directly available by removing the ‘-v.v’ part from the address, for example:

http://sanaregistry.org/r/moschemas/ServiceDefMAL.xml

# Conformance Matrix

This section provides the Conformance Matrix for implementations of the MAL. A MAL will be considered to be ‘conformant’ if the mandatory elements identified in the matrix are implemented as described in this Recommended Standard.

Table 7-1:  Conformance Matrix

| Interaction Pattern | Optional/Mandatory |
| --- | --- |
| SEND | Mandatory |
| SUBMIT | Mandatory |
| REQUEST | Mandatory |
| INVOKE | Mandatory |
| PROGRESS | Mandatory |
| PUBSUB | Mandatory |

- Protocol Implementation Conformance 
Statement (PICS) Proforma
(Normative)

  - INTRODUCTION

    - OVERVIEW

This annex provides the Protocol Implementation Conformance Statement (PICS) Requirements List (PRL) for an implementation of the Mission Operations Message Abstraction Layer (MAL) standard.  The PICS for an implementation is generated by completing the PRL in accordance with the instructions below.  An implementation claiming conformance must satisfy the mandatory requirements referenced in the PRL.

An implementation’s completed PRL is called the PICS. The PICS states which protocol features have been implemented.  The following entities can use the PICS:

- the protocol implementer, as a checklist to reduce the risk of failure to conform to the standard through oversight;

- the supplier and acquirer or potential acquirer of the implementation, as a detailed indication of the capabilities of the implementation, stated relative to the common basis for understanding provided by the standard PICS proforma;

- the user or potential user of the implementation, as a basis for initially checking the possibility of interworking with another implementation (while interworking can never be guaranteed, failure to interwork can often be predicted from incompatible PICSes);

- a protocol tester, as the basis for selecting appropriate tests against which to assess the claim for conformance of the implementation.

    - Notation

      - Status Column Symbols

The following are used in the PRL to indicate the status of features:

| Symbol | Meaning |
| --- | --- |
| M | Mandatory |
| O | Optional |

      - Support Column Symbols

The support of every item as claimed by the implementer is stated by entering the appropriate answer (Y, N, or N/A) in the support column.

| Symbol | Meaning |
| --- | --- |
| Y | Yes, supported by the implementation |
| N | No, not supported by the implementation |
| N/A | Not applicable |

  - General Information

    - Identification of PICS

| Ref | Question | Response |
| --- | --- | --- |
| 1 | Date of Statement (DD/MM/YYYY) |  |
| 2 | CCSDS document number containing the PICS |  |
| 3 | Date of CCSDS document containing the PICS |  |

    - Identification of implementation under test (IUT)

| Ref | Question | Response |
| --- | --- | --- |
| 1 | Implementation name |  |
| 2 | Implementation version |  |
| 3 | Machine name |  |
| 4 | Machine version |  |
| 5 | Operating System name |  |
| 6 | Operating System version |  |
| 7 | Special Configuration |  |
| 8 | Other Information |  |

    - User Identification

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation name(s) and Versions |  |
| Other Information Necessary for full identification, e.g., name(s) and version(s) for machines and/or operating systems; System Name(s) |  |

    - Instructions for Completing the PRL

An implementer shows the extent of compliance to the protocol by completing the PRL; the resulting completed PRL is called a PICS.

  - Abstract Service Specifications PICS

There are 6 separate Interaction Patterns in the MAL. All Interaction Patterns are mandatory, and must be implemented according to the specifications defined in this Standard. This section must be completed.

| Interaction Pattern | Optional/Mandatory | Support |
| --- | --- | --- |
| SEND | Mandatory |  |
| SUBMIT | Mandatory |  |
| REQUEST | Mandatory |  |
| INVOKE | Mandatory |  |
| PROGRESS | Mandatory |  |
| PUBSUB | Mandatory |  |

The Access Control Interface includes the CHECK Interaction Pattern. The CHECK Interaction Pattern is mandatory, and must be implemented according to the specifications defined in this Standard. This section must be completed.

| Access Control Interface Pattern | Optional/Mandatory | Support |
| --- | --- | --- |
| CHECK | Mandatory |  |

  - MAL Data Type Specification PICS

All Fundamentals MAL Data Types are mandatory, and must be implemented according to the specifications defined in this Standard. This includes all the defined Attributes and also all the defined data structures in this Standard. This section must be completed.

| Fundamentals | Optional/Mandatory | Support |
| --- | --- | --- |
| Element | Mandatory |  |
| Attribute | Mandatory |  |
| Composite | Mandatory |  |
| Object | Mandatory |  |

  - MAL Errors PICS

All MAL Errors are mandatory, and must be implemented according to the specifications defined in this Standard. This section must be completed.

| Error | Optional/Mandatory | Support |
| --- | --- | --- |
| DELIVERY_FAILED | Mandatory |  |
| DELIVERY_TIMEDOUT | Mandatory |  |
| DELIVERY_DELAYED | Mandatory |  |
| DESTINATION_UNKNOWN | Mandatory |  |
| DESTINATION_TRANSIENT | Mandatory |  |
| DESTINATION_LOST | Mandatory |  |
| AUTHENTICATION_FAIL | Mandatory |  |
| AUTHORISATION_FAIL | Mandatory |  |
| ENCRYPTION_FAIL | Mandatory |  |
| UNSUPPORTED_AREA | Mandatory |  |
| UNSUPPORTED_OPERATION | Mandatory |  |
| UNSUPPORTED_VERSION | Mandatory |  |
| BAD_ENCODING | Mandatory |  |
| INTERNAL | Mandatory |  |
| UNKNOWN | Mandatory |  |
| INCORRECT_STATE | Mandatory |  |
| TOO_MANY | Mandatory |  |
| SHUTDOWN | Mandatory |  |
| TRANSACTION_TIMEOUT | Optional |  |

SECURITY, SANA and patent considerations

(Normative)

SECURITY CONSIDERATIONS

ANALYSIS OF SECURITY CONSIDERATIONS

This annex presents the results of an analysis of security considerations applied to the technologies specified in this Recommended Standard.

CONSEQUENCES OF NOT APPLYING SECURITY TO THE TECHNOLOGY

The current specification (in short MAL) has two aspects, the design time aspect, and the runtime aspect. For the design time aspect, this specification provides an abstract service and data specification language. This language is used in other Blue Book specifications to specify application level services and data model in the domain of mission operations. Hence at the level of this standard, no generally valid assumptions can be made about the nature of the services and data that will be specified in terms of MAL. Accordingly no generally valid consequences can be assumed as a generic statement with regard to not applying “security to the technology”. Same holds for the runtime aspects of MAL. For runtime aspects, MAL specifies a generic Access Control Interface and delegates the responsibilities of implementing the adequate security controls, which are deployment specific, to the implementation of the deployment specific Access Control component .Having said that, regardless of the nature of the services that will be in future specified, using the language provided by this specification, if no security requirements are applied to the application layer, the Access Control component and the transport layer (all out of the scope of this specification) in a concrete implementation of this specification for a given deployment configuration, the confidentiality, integrity and availability of the respected services and data can be compromised.

POTENTIAL THREATS AND ATTACK SCENARIOS

Potential threats or attack scenarios include, but are not limited to, (a) unauthorized access to the programs/processes that generate and interpret the messages, and (b) unauthorized access to the messages during transmission between exchange partners. Protection from unauthorized access during transmission is especially important if the mission utilizes open ground networks such as the Internet to provide ground station connectivity for the exchange of data formatted in compliance with this Recommended Standard. It is strongly recommended that potential threats or attack scenarios applicable to the systems and networks on which this Recommended Standard is implemented be addressed by the management of those systems and networks.

DATA PRIVACY

Privacy of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

DATA INTEGRITY

Integrity of data formatted in compliance with the specifications of this Recommended Standard should be assured by the systems and networks on which this Recommended Standard is implemented.

AUTHENTICATION OF COMMUNICATING ENTITIES

Authentication of communicating entities involved in the transport of data which complies with the specifications of this Recommended Standard should be provided by the systems and networks on which this Recommended Standard is implemented.

DATA TRANSFER BETWEEN COMMUNICATING ENTITIES

The transfer of data formatted in compliance with this Recommended Standard between communicating entities should be accomplished via secure mechanisms approved by the IT Security functionaries of exchange participants.

CONTROL OF ACCESS TO RESOURCES

Control of access to resources should be managed by the systems upon which originator formatting and recipient processing are performed.

AUDITING OF RESOURCE USAGE

Auditing of resource usage should be handled by the management of systems and networks on which this Recommended Standard is implemented.

UNAUTHORIZED ACCESS

Unauthorized access to the programs/processes that generate and interpret the messages should be prohibited in order to minimize potential threats and attack scenarios.

DATA SECURITY IMPLEMENTATION SPECIFICS

Specific information-security interoperability provisions that may apply between agencies and other independent users involved in an exchange of data formatted in compliance with this Recommended Standard should be specified in an ICD.

SANA CONSIDERATIONS

The recommendations of this document request SANA to create a registry named “Mission Operations Service XML” that consists of a set of XML Schemas and XML service specifications.

The registration rule for change to this registry requires an engineering review by a designated expert. The expert shall be assigned by the WG Chair, or in absence, Area Director.

Additionally, the recommendations of this document request SANA to create a registry named “Mission Operations MAL Areas” that consists of a set of entries containing the MAL Area, MAL Area Names, and its corresponding MAL Area Numbers and a comment, as follows:

| Area | Area Name | Area Number | Comment |
| --- | --- | --- | --- |
| MAL | Message Abstraction Layer | 1 | The MAL area number. |
| COM | Common Object Model services | 2 | The COM area number. The COM is deprecated, therefore this area number is reserved for backward compatibility. |
| COMMON | Common services | 3 | The Common area number. |
| MC | Monitor and Control services | 4 | The Monitor and Control area number. |
| MPS | Mission Planning and Scheduling services | 5 | The Mission Planning and Scheduling area number. |
| SM | Software Management services | 7 | The Software Management area number. |
| MDPD | Mission Data Product Distribution services | 9 | The Mission Data Product Distribution area number. |

PATENT CONSIDERATIONS

The recommendations of this document have no patent issues.

Definition of Acronyms

(INFORMATIVE)

ACK		Acknowledgment

API		Application Programming Interface

ASCII		American Standard Code for Information Interchange

BLOB	Binary Large Object

CCSDS	Consultative Committee for Space Data Standards

DNS		Domain Name System

ICD		Interface Control Document

IEEE		Institute of Electrical and Electronics Engineers

IT		Information Technology

IUT		Implementation under Test

MAL		Message Abstract Layer

MO		Mission Operations

NaN		Not a Number

PICS		Protocol Implementation Conformance Statement

PRL		PICS Requirements List

PUBSUB	Publish-Subscribe

QoS		Quality of Service

RPC		Remote Procedure Call

SANA		Space Assigned Numbers Authority

SM&C	CCSDS Spacecraft Monitor & Control

URI		Universal Resource Identifier

WG		Working Group

XML		eXtensible Markup Language

Informative References

(Informative)

[D1]	Mission Operations Services Concept.  Report Concerning Space Data System Standards, CCSDS 520.0-G-3.  Green Book.  Issue 3.  Washington, D.C.: CCSDS, December 2010.

NOTE	–	Normative references are listed in 1.6.

# Comments

This is still vague.  Presumably these are “Data Objects” and not "objects” in some more general sense.  The “two characteristics” are 1) unique identity, and 2) complex data model ???.  Is there a simple data object that is used to create these more complex data objects?

This change removes references to the third, and really important, layer which is the transport.  How can you possibly remove this essential layer, which is where actual bindings among elements take place, from consideration?

A lot of this document used to be, and I suspect still is, about these abstract objects and interfaces.  How can you remove this from consideration?

Where is the figure?

This is a bad example!

We should add a better example showing a composite.

These terms do not exactly align with those used in either Fig 2-5 nor those in Table 2-3.  This is confusing.  I can guess what you mean, but I should not have to guess.

Does this mean that each “Area Identifier” also has a parallel “Area Number”?  Likewise “Service Identifier” and “Operation Identifier”.  Why the duplication in all there service specs?  Isn’t it both redundant and confusing?  And how doe “Service Identifier” in Table 2-3 relate to anything in Fig 2-5?  Is it the same as “Service Area” or as “Service”?  Or is “Service” in Fig 2-5 the same as “Service Number” in Table 2-3?

This statement is really confusing.  Is it possible for one end of the transport pair to select a “service number” and another to select a “service identifier”.  Or how is it that this choice of number vs identifier is made and signalled to each end?  Is this a specific binding choice?  And how is interoperability achieved if these options are both possible?  Is this another matter for specification in an ICD?

I think we agreed to remove this, no?

I fail to understand how leaving out the transport interface adds to the clarity and utility of this document.  No transport, no interoperability.

Session (4.5.2) and Domain (3.5.6.5) have both definitions and sections dedicated to them.  How can you remove them from here?

Add Authentication ID explain it can hold anything from textual username/password, up to a SAML token or a certificate, …and provide a reference to chapter 3.6. Harmonise the name Authentication ID and Auth ID.

Review

So this states, very clearly, that the real interoperability specification for all SM&C MAL deployments is not these specs, nor even the selected bindings, but it is actually an implementation and deployment specific ICD.

The following deletion is an example of information hiding that is really unacceptable. In some sections these fields are “in” and defined.  In others they are “supplements” and left vague, or relegated to “ICD” status.

Or, stated in another way, this specification is is purely abstraction and the only way you get interoperability is to pick some separate encoding, and some separate transport, and document this in an ICD.

What is a “Consumer Entity Name”?   How are they created?  Is there a registry of such names? How are they created” Who manages them?  How do they relate to any sort of transport layer endpoint identifier?

If both of the fields that are used for filtering are optional how does this operate in the case where neither of these optional fields are used?

What is an "Area Version"?  It appears only once in the document, here.

To ask working group, if it makes sense to prescribe the CCSDS 301.0 at the level of MAL?

Define the low/high bounds and also indicate that it can be negative. DM to propose a more precise definition.

# Text boxes

seq PUBLISH SUBSCRIBE

Provider

Consumer

PUBLISH_REGISTER

REGISTER

REGISTER_ACK

*PUBLISH

*NOTIFY

DEREGISTER

DEREGISTER_ACK

PUBLISH_DEREGISTER