Recommendation for Space Data System Standards

Mission Operations Monitor & Control Services

Recommended Standard

CCSDS 522.1-B-1

Blue Book

October 2017

AUTHORITY

|  | Issue: | Recommended Standard, Issue 1 |  |
| --- | --- | --- | --- |
|  | Date: | October 2017 |  |
|  | Location: | Washington, DC, USA |  |

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the e-mail address below.

This document is published and maintained by:

CCSDS Secretariat

National Aeronautics and Space Administration

Washington, DC, USA

E-mail: secretariat@mailman.ccsds.org

STATEMENT OF INTENT

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

Attention is drawn to the possibility that some of the elements of this document may be the subject of patent rights. CCSDS has processes for identifying patent issues and for securing from the patent holder agreement that all licensing policies are reasonable and non-discriminatory.  However, CCSDS does not have a patent law staff, and CCSDS shall not be held responsible for identifying any or all such patent rights.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-4).  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be sent to the CCSDS Secretariat at the e-mail address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- Electronics and Telecommunications Research Institute (ETRI)/Korea.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- Mohammed Bin Rashid Space Centre (MBRSC)/United Arab Emirates.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- South African National Space Agency (SANSA)/Republic of South Africa.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- Swiss Space Office (SSO)/Switzerland.

- United States Geological Survey (USGS)/USA.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 522.1-B-1 | Mission Operations Monitor & Control Services, Recommended Standard, Issue 1 | October 2017 | Original issue |
| CCSDS 522.1-B-2 | Mission Operations Monitor & Control Services, Recommended Standard, Issue 2 | 11 October 2022 | Ongoing revision, services Action, Parameter & ConfigurationManagement |
|  |  | 9 December 2022 | Ongoing revision, services Action, Parameter, Alert, Conversions, after comments from CCSDS Fall’22. |
|  |  | 2 June 2023 | Complete draft for internal review. |
|  |  | 24 July 2023 | Complete draft for WG review. |
|  |  | 19 December 2023 | Final draft for WG review, after comments from CCSDS Fall’23 |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	General	1-1

1.2	Purpose and Scope	1-1

1.3	Applicability	1-1

1.4	Rationale	1-2

1.5	Document structure	1-2

1.6	Definitions	1-2

1.7	NOMENCLATURE	1-3

1.8	Conventions	1-4

1.9	References	1-5

2	Overview	2-1

2.1	General	2-1

2.2	Monitor and Control concept	2-1

2.3	Access Control	2-1

2.4	Concurrency Control	2-2

2.5	M&C services generic Data Model	2-2

2.6	Action Service	2-3

2.7	Parameter service	2-4

2.8	Alert Service	2-5

2.9	Aggregation Service	2-6

2.10	Packet service	2-8

3	Specification: MC	3-1

3.1	Overview	3-1

3.2	Global conventions	3-1

3.3	Service: Action	3-1

3.4	Service: Parameter	3-8

3.5	Service: Alert	3-20

3.6	Service: Aggregation	3-26

3.7	Service: Packet	3-37

4	Data types	4-1

4.1	Area data types: MC	4-1

4.2	Action Service data types	4-3

4.3	Parameter Service data types	4-8

4.4	Alert Service data types	4-12

4.5	Aggregation Service data types	4-15

4.6	Packet Service data types	4-1

5	Error codes	5-2

6	SERVICE SPECIFICATION XML	6-1

ANNEX A	Protocol IMPLEMENTATION CONFORMANCE 
Statement Proforma  (Normative)	A-1

ANNEX B	Security, SANA, and Patent Considerations  (Informative)	B-1

ANNEX C	Definition of Acronyms  (Informative)	C-1

ANNEX D	Informative References  (Informative)	D-1

Figure

2-1	Mission Operations Services Concept Document Set	2-1

2-2	MO Service Layering Using Monitor and Control Services	2-2

2-3	Example Service Consumers and Providers	2-2

2-4	Service Data Augmentation	2-2

2-5	Service Extension	2-2

3-1	Nominal Sequence of Action Submission and Monitoring	3-2

3-3	Flow Chart for Determining the Validity of a Parameter	3-8

3-4	Parameter Service COM Object Relationships	3-11

3-5	Alert Service COM Object and Event Relationships	3-21

3-6	Check Service Nominal Sequence	3-25

3-7	Flow Chart for Determining the Status of a Check	3-25

3-8	Check Service COM Object and Event Relationships	3-25

3-9	Statistic Service Nominal Sequence	3-25

3-10	Example Statistic Interval Reporting	3-25

3-11	Statistic Service COM Object Relationships	3-25

# CONTENTS (continued)

Figure	Page

3-12	Aggregation Delta Time Calculation	3-26

3-13	Aggregation Service COM Object Relationships	3-27

3-14	Conversion Service COM Object Relationships	3-39

3-15	Group Service COM Object Relationships	3-39

Table

1-1	Example Operation Template	1-4

3-1	Action Service Operations	3-2

3-2	Action Service Object Types	3-4

3-3	Action Service Events	3-4

3-2Action Service COM Object and Event Relationships	3-4

3-4	Parameter Service Operations	3-9

3-5	Parameter Service Object Types	3-11

3-6	Alert Service Operations	3-20

3-7	Alert Service Object Types	3-21

3-8	Alert Service Events	3-21

3-9	Check Service Operations	3-25

3-10	Check Service Object Types	3-25

3-11	Check Service Events	3-25

3-12	Statistic Service Operations	3-25

3-13	Statistic Service Object Types	3-25

3-14	Aggregation Service Operations	3-26

3-15	Aggregation Service Object Types	3-27

3-16	Conversion Service Operations	3-39

3-17	Conversion Service Object Types	3-39

3-18	Group Service Operations	3-39

3-19	Group Service Object Types	3-39

5-1	MC Error Codes	5-2

# Introduction

## General

This Recommended Standard defines the Mission Operations (MO) Monitor and Control (M&C) services in conformance with the service framework specified in reference [Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 8,Annex Heading 1 au texte que vous souhaitez faire apparaître ici.1], Mission Operations Services Concept.

The M&C services are a set of services that enables a mission to perform basic monitoring and control of a local or remote mission operations entity. It provides basic monitoring and control services that are expected, but not required, to be used in conjunction with higher level mission operations services, such as Automation and Planning, as identified in reference [Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 8,Annex Heading 1 au texte que vous souhaitez faire apparaître ici.1].

These services are defined in terms of the Message Abstraction Layer (MAL) (see reference [2], Mission Operations Message Abstraction Layer). They have undergone significant changes as a result of the revision of the MAL book, and the discontinuation of the COM book.

## Purpose and Scope

This Recommended Standard defines, in an abstract manner, the M&C services in terms of:

- the operations necessary to provide the services;

- the parameter data associated with each operation;

- the required behaviour of each operation.

It does not specify:

- individual implementations or products;

- the implementation of entities or interfaces within real systems;

- the methods or technologies required for communications.

## Applicability

This specification is applicable to any mission operations component that provides a control interface or provides monitoring information to other mission operations components. Nominally, but not exclusively, this applies to mission operations onboard software across the space link, mission operations ground control systems to external mission operations entities, and between external mission operations entities.

## Rationale

The primary goal of CCSDS is to increase the level of interoperability among agencies. This Recommended Standard furthers that goal by providing a standard service specification for the basic monitor and control of a remote entity. This supports multi-agency missions by providing a single specification for the exchange of basic monitor and control information, which, when combined with the other MO specifications of MAL, and any supported protocol and message transport, provides an interoperable service for the basic monitor and control of a remote entity.

## Document structure

This Recommended Standard is organised as follows:

- section 1 provides purpose and scope, applicability, and rationale of this Recommended Standard and lists the definitions, conventions, and references used throughout the document;

- section 2 presents an overview of the concepts;

- section 3 presents the M&C services specification;

- section 4 is a formal specification of the M&C services data structures;

- section 5 is a formal specification of the M&C services error codes;

- section 6 specifies the internet location of the formal service specification eXtensible Markup Language (XML).

## Definitions

### Terms from CCSDS MO Message Abstraction Layer

This Recommended Standard makes use of a number of terms defined in reference [2]. Those terms are

- service;

- service interface;

- service consumer;

- service provider;

- service capability set;

## Terms from CCSDS Space Packet Protocol

## This Recommended Standard makes use of a number of terms defined in reference [3]. Those terms are

- space packet.

### Terms defined in this Recommended Standard

action: A single executable task of a service provider, a telecommand is an example of an Action.

aggregation: A collection of parameters provided as a set by a service provider.

alert: Any operationally significant event.

argument: A single part of either an action or an alert.

parameter: A single unit of data reported by a service provider.

## NOMENCLATURE

### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## Conventions

### Figures

In figures illustrating this document, Unified Modelling Language (UML) modelling diagrams are used. Reference [1] provides further information regarding diagrams types and their meaning.

### Tables

The table format information presented here is extracted from section 2 of reference [2]. It is repeated here to aid in understanding tables as they are presented in this document. A full description of the table formats presented in this document can be found in section 2 of reference [2].

Each interaction pattern definition contains a table that defines the template for operations that use that pattern.

Table Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 1 au texte que vous souhaitez faire apparaître ici.-1:  Example Operation Template

| Operation Identifier | <<Operation name>> |
| --- | --- |
| Interaction Pattern | <<Interaction pattern name>> |
| Pattern Sequence | Message | Nullable | Type Signature |
| <<Message direction>> | <<Message name>> | <<Nullability>> | <<Message Signature*>> |
| … | … |  | … |

The message direction denotes the direction of the message relative to the provider of the pattern and is either IN or OUT. So all messages directed towards the provider are IN messages, and all messages directed away from the provider are OUT messages.

Blue cells (dark grey when printed on a monochrome printer) contain table headings, light grey cells contain fields that are fixed for a pattern, and white cells contain values that must be provided by the operation or structure.

Where types are required from other MO specifications, the following notation is used to denote the area in which the referenced definition resides:

<area>::<type name>

## References

The following publications contain provisions which, through reference in this text, constitute provisions of this document. At the time of publication, the editions indicated were valid. All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below. The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Mission Operations Reference Model. Issue 1. Recommendation for Space Data System Practices (Magenta Book), CCSDS 520.1-M-1. Washington, D.C.: CCSDS, July 2010.

[2]	Mission Operations Message Abstraction Layer. Issue 2. Recommendation for Space Data System Standards (Blue Book), CCSDS 521.0-B-2. Washington, D.C.: CCSDS, March 2013.

[3]	Space Packet Protocol. Issue 2. Recommendation for Space Data System Standards (Blue Book), CCSDS 133.0-B-2. Washington, D.C.: CCSDS, June 2020.

NOTE	–	Informative references are listed in annex D.

# Overview

## General

- The M&C services provide operations for generic monitoring and control of a remote service provider (e.g., a spacecraft or ground system component).

The MO M&C services build upon the layering concept outlined in reference [Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 8,Annex Heading 1 au texte que vous souhaitez faire apparaître ici.1] and are defined in terms of the MO MAL outlined in reference [2], so it is possible to deploy them over any supported protocol and message transport.

NOTE	–	The services defined in this specification are not dependent on any of the other services, and are complete in their own right. An implementation is free to opt out of any service and also any capability set of these services; however, it may not make sense to support certain services without others.

## Monitor and Control concept

The M&C services provide the basic ability to monitor and control a remote entity. They provide three main concepts:

- Actions allow executable tasks to be invoked and their evolving status to be monitored: spacecraft telecommands are an example of an action.

- Parameters provide status monitoring capability but also may have their value set.

- Alerts provide a mechanism for asynchronous notification of operationally significant events or anomalies by the service provider to the service consumer.

- To be compatible with “classical” operation expectations, Packets are also provided.

In most modern systems the M&C services would be used in conjunction with higher level functionalities such as automation and planning, which would utilise the M&C services to fulfil their high level functions. For example, a planning function may take in requests to perform activities, these may get decomposed into automated procedures executed by the automation system, which in turn may monitor and control the remote entity using the M&C services.

## Access Control

For many situations there may be a deployment or mission specific policy for limiting either access to specific received data or the ability to execute specific operations. This concept of authentication and authorisation is provided by the MAL access control concept and is covered in subsections 3.6, 5.2, and 5.3 of the Reference Model (reference [1]).

## Concurrency Control

The main objective of the M&C services specification is to enable a space agency to open its monitoring and control system to other agencies. The scope of the operations allowed for external agency execution is completely controled by the responsible agency, using the Access control features. However, once the operation has been allowed, then the concurrency issue remains.

A complete specification of a service in a parallel execution environment requires the specification of the concurrent access to the service operations. Whatever the choice of the service provider implementation, this is not part of the current specification of the service.

## M&C services generic Data Model

Most of the M&C services define service primary objects which are modeled as MO Objects. The MAL type of the service specific primary objects is named <Service>Definition. The actual list of the service primary objects is usually fixed for a whole mission, and it may be statically provided as an out of band agreement.

A service primary object is uniquely identified over the whole system using MAL::ObjectRef references.

The content of a service primary object is essentially static, but it may occasionaly evolve when a dependent system component changes. In that case a new Definition object can be created, reusing the values of all the fields but the version field of the object identity/reference. The service object is then properly identified by the (domain, area, type, key) tuple, while the version field identifies the version of the object definition.

Beyond the main type of service objects defined as above, each service may define a secondary type of service objets which are usually mapped as MAL composite objects instead of MO Objects. The service secondary objects are attached to a service primary object, and include an object reference to it. They are identified relatively to this primary object with a specific local identifier (e.g. an index for the ActionExecutionRequest or a timestamp for the ParameterValue). The actual structure of the secondary objects may be dynamic, and depend on the primary object. In such cases the primary object definition will include a description of the dynamic fields of the secondary object.

The M&C services require representing data values (e.g. action argument values or parameter values). This concept is represented by an extended model which includes an engineering unit conversion capability. Values may then be provided and processed as raw values and/or converted values. Converted values are obtained by applying a Conversion to raw values. In the M&C services, Conversions are defined as a background concept and are not explicitly modeled. A data value is then represented by 6 fields (i.e. raw value type, raw value unit, raw value, converted value type, converted value unit, converted value), which are used inline and not as a separate type for simplicity.

## Action Service

### General

Actions enable consumers of the service to control a remote system. Action invocation operations include issuing of action directives by an authorized client to the remote service provider, and the subsequent monitoring of the evolving execution status of that action by both the initiator and other client functions. The action service is concerned with the execution of actions; the control of when that execution happens is a function of an external scheduling service.

### Action service data model

The action service defines two major data structures: the ActionDefinition object type and the ActionExecutionRequest composite type. The ActionDefinition implements the action concept of the M&C services, and identifies an executable action defined by the provider. An ActionExecutionRequest represents a particular execution of the ActionDefinition.

Figure 2-2: Action service data model

### Action verification

The action service reports to consumers the progress and/or verification of actions. The action service does not model the predicted execution state of an action; it only reports on progress when each stage is reached.

If a report of failure has been made there will not be any more execution progress reports for that action.

## Parameter service

### General

The M&C parameter service allows a consumer to monitor and set parameters values from a remote system. This can include raw values, converted (engineering) values and respective validities.

Monitoring parameters are attribute types such as strings or integers. A report containing several parameter values and/or validities is possible by defining an appropriate aggregation (see Aggregation service in 2.9).

The following use case scenario of the service is foreseen.

- subscribe for parameters;

- receive parameter values;

- (optional) modify requested parameter list;

- unsubscribe.

### Parameter service data model

The parameter service defines two major data structures: the ParameterDefinition object type and the ParameterValue composite type. The ParameterDefinition implements the monitoring parameter concept of the M&C services. It uniquely identifies a monitoring parameter in the system, and provides a definition of the parameter and of its values. The ParameterValue is used to represent the evolving value of the monitoring parameter at some time.

Figure 2-3: Parameter service data model

## Alert Service

Alerts are raised asynchronously to report a significant event or anomaly from the remote system. Alerts are characterised by an identifier and a set of arguments.

### Alert service data model

The alert service defines two major data structures: the AlertDefinition object type and the AlertEvent composite type. The AlertDefinition implements the alert concept of the M&C services. It uniquely identifies a type of alert, and describes the arguments required to notify an alert event of that type. The AlertEvent is used to represent a specific occurrence of the alert.

Figure 2-4: Alert service data model

## Aggregation Service

### General

- The aggregation service allows a consumer to get reports containing several parameter values and/or validities (see Parameter service in 2.7). These aggregation can either be predefined on the service provider side or configured at runtime by the consumer.

### Aggregation service data model

The Aggregation service defines two major data structures: the AggregationDefinition object type and the AggregationValue composite type. The AggregationDefinition uniquely identifies an aggregation in the system, and provides a definition of the aggregation including the list of parameters. The AggregationValue object is used to represent the periodic reports of the values of the aggregation parameters.

Figure 2-5: Aggregation service data model

### Automatic publish of Aggregations

In many situations it is expected that basic summary or overview information about the state of a system or spacecraft be published without an initial consumer request. For example, for safety reasons it is normal for a spacecraft to broadcast basic status information when in recovery/safe mode to help diagnose any communication issues that might exist.

In order to achieve this use case, the system designer can deploy an Aggregation service provider on the spacecraft and a broker on ground. The provider would statically know the address of the broker, with an out-of-band agreement, enabling it to initiate the Publish-Subscribe operation. It would also be initially configured through out-of-band agreement with a set of Aggregations, representing the basic summary or overview information required, and would immediately publish value reports of those Aggregations to the broker.

## Packet service

### General

The packet service provides a read only access to the raw space packets (i.e. non decommutated) exchanged by the provider. It enables consumers to subscribe to a subset of the space packets, based on filtering capabilities which may be specific to the packet types.

### Packet service data model

The packet service defines a single data structure: the PacketValue composite type. The PacketValue is used to represent each published packet, together with its metadata. The raw packet itself is structured as a Blob. The metadata are represented as key values used for filtering.

Figure 2-6: Packet service data model

# Specification: MC

## Overview

This section details the M&C services; the structures used by the services are detailed in section 4. Both the services and structures are defined in terms of the MO MAL, which is defined in reference [2], so it is possible to deploy them over any supported protocol and message transport.

To aid comprehension, several tables are included for each service and operation definition. The table formats are briefly described in 1.8.2.

All service specifications in this document are part of the MC area, which has a short form number of ‘4’.

## Global conventions

### Index of elements in lists

## This specification refers to the index of elements in lists. The value 0 shall be used to represent the index of the first element.

## Service: Action

### Overview

The action service allows consumers to submit an action for execution and to subsequently monitor the execution progress of these actions.

An action is represented as an ActionDefinition object. It follows the pattern of a MAL MO Object (ref), i.e. it derives from the MAL::Object type and may be referenced globally by a MAL::ObjectRef. The ActionDefinition object more precisely represents a version of the action definition, while the action itself may be assimilated to the latest version if its definition and may be referenced by a MAL::ObjectRef where the version field is set to 0.

The provider may be requested to execute an action using the requestExecution operation. This specific execution request is represented as an ActionExecutionRequest object. The ActionExecutionRequest object references the ActionDefinition to be executed (field actionRef), and is identified by a numeric identifier (field requestId) relative to the action. The action request identifier must be provided by the consumer, but it must be unique in the system. Coordination may be required between Action service consumers to ensure the action request identifiers are unique. How this is done is outside the scope of this specification. In a distributed command scenario, an ICD may be used to prevent collision of Ids.

If the provider accepts the action execution request, then the ActionExecutionRequest object reference may be subsequently used to monitor the execution progress of the action.

The nominal sequence of action submission and execution monitoring are shown in figure 3-1.

Figure 3-1:  Nominal Sequence of Action Submission and Monitoring

The sequence above shows the activity execution progress events being published to a MAL broker. The sequence does not show the broker passing the events to any subscribed consumers, as that is outside the intent of the figure.

The consumer is responsible for creating the ActionExecutionRequest object, with its unique key, and then using the requestExecution operation to submit it to the Action provider for execution. The Action provider reports the execution progress of the action, through events published by its monitorActionExec operation. Once the supplied action request details have been checked and execution of the action validated by the requestExecution operation, that operation finishes, whilst the execution of the action possibly continues (depends on the actual action).

If the execution of an action fails with an error, the action service provider can publish a progress event with a success status set to false.

Table Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 1 au texte que vous souhaitez faire apparaître ici.-1:  Action Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| MC | Action | 4 | 1 | 2 |
| Interaction Pattern | Operation Identifier | Operation Number | Capability Set |
| SUBMIT | requestExecution | 7 | 1 |
| PUBLISH-SUBSCRIBE | monitorActionExec | 8 | 4 |

### High-Level Requirements

The action service shall provide:

- the capability for submitting execution requests of actions;

- the capability for monitoring the execution progress of actions.

The list of actions (i.e. of ActionDefinition objects) that are supported by the action service shall be declared in an out-of-band agreement.

Each action execution request shall include:

- the action definition object reference;

- the request identifier;

- the ordered list of action arguments;

- the reporting instructions.

The service consumer shall be responsible for choosing the action execution request identifier.

The service consumer shall be able to provide an argument value as either a raw values or a converted value, when enabled in the related ArgumentDefinition.

The service provider shall control the unicity of the action execution request identifier supplied by the service consumer.

The service provider shall accept to monitor the progress of an execution request that has not yet been submitted.

The service provider shall accept an argument value whether provided as a raw value or a converted value, when enabled in the related ArgumentDefinition.

Whenever actions are referenced as MAL::ObjectRef typed parameters in operations, then it shall be possible to use references with a version field set to 0 to reference the latest version of the action definition.

### Functional Requirements

The requestExecution operation shall be used to request the execution of an action.

The monitorActionExec operation shall be used to monitor the execution progress of submitted execution requests with request identifiers that match the subscription, whether the execution requests have been submitted before or after the subscription.

The monitorActionExec operation shall only publish the progress reporting events that have been declared as parameters of the requestExecution operation call that started the action execution.

### OPERATION: requestExecution

#### Overview

The requestExecution operation allows a consumer to request a provider to execute an action.

| Operation Identifier | requestExecution |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No | executionRequest : ActionExecutionRequest |

#### Structures

The executionRequest parameter shall describe the requested action and the modalities for its execution.

The requestId field of the executionRequest parameter shall contain the numeric identifier of the action execution request.

If the numeric identifier of the action execution request is already known by the provider, then a DUPLICATE error shall be returned.

The actionRef field of the executionRequest parameter shall contain the object reference of the action definition.

If the actionRef field of the executionRequest parameter does not match a known ActionDefinition object then an UNKNOWN error shall be returned.

The stageStartedRequired, stageProgressRequired, and stageCompletedRequired fields of the executionRequest parameter shall control the messages actually published by the monitorActionExec operation as regards the progress of the action execution.

The argumentValues field of the executionRequest parameter shall contain the ordered list of arguments to use when starting the action execution.

The size of the argumentValues list of the executionRequest parameter shall be compared to the size of the arguments list in the matched ActionDefinition object and an INVALID error shall be returned if they are not the same.

If a supplied argument value is provided as a converted value while this is not enabled in the related ArgumentDefinition, then an INVALID error shall be returned.

If a supplied argument value does not match the attribute type specified in the action definition for that argument, taking into account the raw or converted nature of the supplied argument, then an INVALID error shall be returned.

A service provider may apply some deployment specific checks to the action execution request and can return an INVALID error if they fail.

If an error is raised then no action shall be executed.

The SUBMIT acknowledgement shall be returned once the action has been accepted for execution but before execution starts.

#### Errors

The operation may return one of the following errors:

- ERROR: DUPLICATE: submitted execution request identifier is already used.

- the provided execution request identifier in a requestExecution operation call is already known by the provider;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | 2 | Not Used |

- ERROR: INVALID:

- the argumentValues list size of the ActionExecutionRequest does not match the arguments definition or it contains one or more invalid argument values;

- if the two lists are not the same length then the extra information field shall contain a singleton list with the first index of the element in the largest list which does not have corresponding element in the other list;

- the extra information field contains a list of the indexes of the erroneous values from the originating list supplied;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | 3 | List<MAL::UInteger> |

- ERROR: UNKNOWN: submitted action definition is unknown.

- the provided action definition reference is not known by the provider;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

#### Discussion

There may be a deployment or mission specific policy for limiting the ability to execute the requestExecution operation. This can be implemented with the concept of authentication and authorisation provided by the MAL access control concept and covered in subsections 3.6, 5.2, and 5.3 of the Reference Model (reference [1]).

### OPERATION: monitorActionExec

#### Overview

The monitorActionExec operation allows a consumer to be informed of the progress in the execution of an action or a set of actions.

The model for monitoring the progress in the execution of an action is simple, as a sequence of stages published as ActionProgressBaseEvents. The first execution stage is a started stage, and shall be published as an ActionProgressStartEvent. The last execution stage in a successful execution is a completed stage, and shall be published as an ActionProgressCompletionEvent. In between the started and completed stages, a variable number of anonymous execution progress stages are allowed, which shall be published as ActionProgressExecutionEvents.

Each execution of an action defines a total number of execution progress stages to be reported. This concerns only the ActionProgressExecutionEvent typed events, and for a nominal execution. This number shall be set to the stageCount field of the corresponding ActionProgressExecutionEvent structure.

A new message shall be published whenever a new execution stage has been reached, and if the reporting of this stage has been required in the ActionExecutionRequest object representing the executed action.

Each actually published execution progress stage is identified by its sequence number, starting at 1.

The message includes a success marker, defined in the base type. If it is false then the sequence is stopped and no further progress message will be issued for that specific execution.

The set of action request executions to monitor is defined by filters provided mainly as subscription keys of the Publish-Subscribe operation.

| Operation Identifier | monitorActionExec |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Subscription Keys | requestId : MAL::Long actionKey : MAL::Identifier actionCategory : MAL::UOctet |
| Pattern Sequence | Message | Nullable | Type Signature |
| OUT | PUBLISH/NOTIFY | No | progressEvent : ActionProgressBaseEvent |

#### Structures

The value of the domain field of the MAL::UpdateHeader of the Publish message shall be set to the domain field of the identity field of the ActionDefinition object representing the executed action definition.

The value of the requestId subscription key shall be set to the requestId field of the ActionExecutionRequest object representing the executed action.

The value of the actionKey subscription key shall be set to the key field of the identity field of the ActionDefinition object representing the executed action definition.

The value of the actionCategory subscription key shall be set to the numeric value of the category field of the ActionDefinition object representing the executed action definition.

The executionStage field of the ActionProgressExecutionEvent typed progressEvent parameter of the successive publish messages published with the same set of subscription key values shall be set to successive numeric values starting at 1.

The executionStage field of the ActionProgressExecutionEvent typed progressEvent parameter shall be less than or equal to the stageCount field.

If the success field of the progressEvent parameter of a publish message is set to False, then this message shall be the last one sent with that set of subscription key values.

## Service: Parameter

### Overview

The parameter service allows the user to subscribe to parameter value report and optionally be able to set new values. A single PUBSUB operation is provided for monitoring and publishing of parameter values.

A parameter value also contains a calculation of the validity of the parameter, which describes how the raw and converted values of the parameter should be interpreted. This standard supports the concept of non-standard invalidity states but the meaning and calculation of these is outside the scope of this document.

The generation of value reports, including effective generation and generation frequency, is initially configured externally to the Parameter service. This initial configuration can then be browsed and changed using a set of dedicated operations.

The parameter service does not include any value checking, this is delegated to the check service.

Table Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 1 au texte que vous souhaitez faire apparaître ici.-2:  Parameter Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| MC | Parameter | 4 | 2 | 2 |
| Interaction Pattern | Operation Identifier | Operation Number | Capability Set |
| PUBLISH-SUBSCRIBE | monitorValue | 1 | 1 |
| REQUEST | getValue | 2 | 2 |
| SUBMIT | setValue | 3 | 3 |
| REQUEST | getReportingConfiguration | 9 | 4 |
| SUBMIT | enableReporting | 10 |  |
| SUBMIT | disableReporting | 11 |  |
| SUBMIT | setReportingPeriod | 12 |  |

### High-Level Requirements

The parameter service shall provide:

- the capability for publishing and receiving periodic reports of the value of a monitoring parameter;

- the capability for setting the raw parameter value of a set of parameters;

- the capability for requesting the current value of a set of parameters;

- the capability for requesting and modifying the configuration of the periodic publication of reports for a parameter;

The list of parameters (i.e. of ParametersDefinition objects) that are supported by the parameter service shall be declared in an out-of-band agreement.

A default configuration for the periodic generation of reports for each parameter shall be defined by the provider of the Parameter service, but this is not part of its interface.

Each parameter value report shall contain:

- The validity of the parameter value;

- The raw value of the parameter, if applicable;

- The converted value of the parameter, if applicable.

The validity of parameter values shall be calculated by implementation specific mechanisms.

### Functional Requirements

The actual generation of reports of a parameter shall be enabled by the enableReporting operation, and disabled by the disableGeneration operation.

If a parameter is required to send periodic reports then the time between these reports shall be controlled using the setReportingPeriod operation.

For onboard parameters, the interval should be a multiple of the minimum sampling interval of those parameters.

If an interval that is not supported by the provider is requested, then an INVALID error shall be returned, and the change rejected.

A default configuration for the generation of reports shall exist for each parameter. It shall be set by implementation specific mechanisms.

The getReportingConfiguration operation shall return the current configuration for the generation of reports for a parameter.

If the parameter is periodic and reported via a periodic aggregation, and a new report has not been received in the aggregation period, then the validity shall be set to EXPIRED by setting the ParameterValueData validityState field to ‘1’ and the rawValue set to the last known parameter raw value.

If the parameter raw value cannot be obtained, or calculated for synthetic parameters, then the validity state shall be INVALID_RAW by setting the ParameterValueData validityState field to ‘2’ and the rawValue set to NULL.

If the parameter raw value is deemed to be valid by the provider, and the ParameterDefinition either allows no conversion or the conversion is successful, then the validity state shall be set to VALID by setting the ParameterValueData validityState field to ‘0’ and the rawValue set to the parameter raw value.

If the parameter raw value is deemed to be valid by the provider, and the conversion of the parameter value fails (for example an unexpected value for a discrete conversion), then the validity state shall be INVALID_CONVERSION by setting the ParameterValueData validityState field to ‘3’, and the rawValue set to the parameter raw value.

If the validity of the raw value cannot be evaluated because of invalid dependant data, then the validity state shall be set to UNVERIFIED by setting the ParameterValueData validityState field to ‘4’, and the rawValue set to the parameter raw value.

If the parameter raw value is deemed to be invalid by the provider, then the validity state shall be set to INVALID by setting the ParameterValueData validityState field to ‘5’, and the rawValue set to the parameter raw value.

If the validity of the parameter is INVALID_CONVERSION then the convertedValue of the ParameterValueData shall be set to NULL.

If the validity of the parameter is either EXPIRED, UNVERIFIED or INVALID and the ParameterDefinition enables a conversion, then the convertedValue of the ParameterValueData shall contain the converted value, or NULL if the conversion fails.

It is supported that other, deployment specific, validityState values be used; however, the meaning of those values is deployment specific and outside the scope of this standard. They must use values greater than 127.

### OPERATION: monitorValue

#### Overview

The monitorValue operation allows a consumer to subscribe for parameter value reports.

| Operation Identifier | monitorValue |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Subscription Keys | parameterKey: MAL::Identifier parameterVersion: MAL::UInteger |
| Pattern Sequence | Message | Nullable | Type Signature |
| OUT | PUBLISH/NOTIFY | No Yes No | timestamp: MAL::Time samplingTime: MAL::Time newValue : ParameterValueData |

#### Structures

The value of the domain field of the UpdateHeader shall be set to the domain field of the identity of the ParameterDefinition object whose value is reported.

The value of the parameterKey subscription key shall be set to the key field of the identity of the ParameterDefinition object whose value is reported.

The value of the parameterVersion subscription key shall be set to the version field of the identity of the ParameterDefinition object whose value is reported.

The newValue parameter of the publish message body shall be set to the new value of the parameter.

The timestamp parameter of the publish message body shall be set to a provider chosen time. The exact semantics of that time is left to the provider.

The timestamp parameter of the publish message body shall uniquely identify the parameter value relatively to the ParameterDefinition.

The samplingTime parameter of the publish message body shall be set to the internal sampling time of the parameter value, as far as it is known by the provider. It may be left undefined and set to NULL.

#### Errors

The operation does not return any errors.

### OPERATION: getValue

#### Overview

The getValue operation returns the latest received value for a requested parameter.

| Operation Identifier | getValue |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | REQUEST | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |
| OUT | RESPONSE | No | parameterValues : List<ParameterValue> |

#### Structures

The domain and keys parameters shall be used to build a list of ParameterDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the ParameterDefinition objects for which values are requested.

If a requested parameter is unknown then an UNKNOWN error shall be returned.

If a parameter is being reported periodically, using the operation shall not reset the reportInterval timer.

The response shall contain a list of returned parameter values matching the input list of references.

The new value shall not be published via the monitorValue operation.

#### Errors

The operation may return the following error: ERROR: UNKNOWN:

- one or more of the requested parameters is unknown;

- a list of the indexes of the error values shall be contained in the extra information field.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: setValue

#### Overview

The setValue operation allows a consumer to set the raw value for one or more parameters.

| Operation Identifier | setValue |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> newRawValues : List<MAL::NullableAttribute> |

#### Structures

The domain and keys parameters shall be used to build a list of ParameterDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the ParameterDefinition objects to set the new value of.

The submitted newRawValues shall hold a matching list of new raw values to be set.

If the two submitted lists do not have the same size, then an INVALID error shall be returned.

The provider shall process each new parameter raw value as any other values, in order to build and publish a new ParameterValueData.

If a raw value is NULL, then the ValidityState of the corresponding ParameterValueData shall be INVALID_RAW.

If a requested ParameterDefinition reference is unknown then an UNKNOWN error shall be returned.

If a requested parameter listed in parameterRefs is not settable because of its being read only, then a READONLY error shall be returned.

If any supplied new parameter raw value does not match the defined type in the matching ParameterDefinition then an INVALID error shall be returned.

If an error is raised then no modifications shall be made as a result of this operation call.

The parameter values shall be set concurrently, by this it is meant that all values are set at the same time without interleaving of other values being (ATOMIC behaviour). How this is implemented is an implementation detail.

The service provider shall publish the new values through the monitorValue operation.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the referenced parameters is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

- ERROR: INVALID:

- one of the supplied parameter values contains an invalid value;

- the extra information field contains a list of the indexes of the erroneous values from the originating list supplied;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | 3 | List<MAL::UInteger> |

- ERROR: READONLY:

- one or more of the parameters being set is read only;

- a list of the indexes of the error values shall be contained in the extra information field.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| READONLY | 1 | List<MAL::UInteger> |

### OPERATION: getReportingConfiguration

#### Overview

The getReportingConfiguration operation allows a consumer to retrieve the current configuration for the generation of reports for a parameter.

| Operation Identifier | getReportingConfiguration |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | REQUEST | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |
| OUT | RESPONSE | No | reportConfigs : List<ReportConfiguration> |

#### Structures

The domain and keys parameters shall be used to build a list of ParameterDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the ParameterDefinition objects for which the report configuration is requested.

If a requested ParameterDefinition reference is unknown then an UNKNOWN error shall be returned.

The response shall contain the matching list of report configurations for each ParameterDefinition object of the input list.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested parameters is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: enableReporting

#### Overview

The enableReporting operation allows a consumer to request the generation of reports for specific parameters.

| Operation Identifier | enableReporting |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |

#### Structures

The domain and keys parameters shall be used to build a list of ParameterDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the ParameterDefinition objects for which reports are requested to be generated.

No error shall be raised if report generation is already enabled for a matched ParameterDefinition object; i.e., enabling an already enabled parameter will not result in an error.

If a requested ParameterDefinition reference is unknown then an UNKNOWN error shall be returned.

If an error is raised then no modifications shall be made as a result of this operation call.

If the generation of reports is being enabled, while it was not before, then the provider shall generate a report immediately and start the report interval from that report.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested parameters is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: disableReporting

#### Overview

The disableReporting operation allows a consumer to stop the generation of reports for specific parameters.

| Operation Identifier | disableReporting |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |

#### Structures

The domain and keys parameters shall be used to build a list of ParameterDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the ParameterDefinition objects for which reports are requested to be stopped.

No error shall be raised if report generation is already disabled for a matched ParameterDefinition object; i.e., disabling an already disabled parameter reporting will not result in an error.

If a requested ParameterDefinition reference is unknown then an UNKNOWN error shall be returned.

If an error is raised then no modifications shall be made as a result of this operation call.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested parameters is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: setReportingPeriod

#### Overview

The setReportingPeriod operation allows a consumer to set the reporting interval for specific parameters.

| Operation Identifier | setReportingPeriod |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> reportInterval : MAL::Duration |

#### Structures

The domain and keys parameters shall be used to build a list of ParameterDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the ParameterDefinition objects for which the report generation period is to be set.

If a requested ParameterDefinition reference is unknown then an UNKNOWN error shall be returned.

If an error is raised then no modifications shall be made as a result of this operation call.

The reportInterval parameter shall contain the new report generation period to set to all the ParameterDefinition objects involved in the operation.

If reportInterval is 0 then the lowest possible value for each parameter shall be used by the provider.

If the provided reportInterval value is not supported by the provider for a parameter, then an INVALID error shall be returned.

The report generation period shall be set to the parameters involved in the operation whatever their reporting status. If the reporting of a parameter is disabled, then the new reporting period shall be used when the reporting of the parameter is enabled again.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested parameters is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

- ERROR: INVALID:

- the report interval value is not supported for one or more of the requested parameters;

- the extra information field contains a list of the indexes of the erroneous values from the originating list supplied;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | 3 | List<MAL::UInteger> |

## Service: Alert

### Overview

The alert service defines the structures and patterns for the publishing and monitoring of alerts. The generation of value reports, including effective generation and generation frequency, is initially configured externally to the Parameter service. This initial configuration can then be browsed and changed using a set of dedicated operations

The generation of alerts is initially enabled or disabled by the provider. This initial configuration can then be browsed and changed using a set of dedicated operations.

Table Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 1 au texte que vous souhaitez faire apparaître ici.-3:  Alert Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| MC | Alert | 4 | 3 | 2 |
| Interaction Pattern | Operation Identifier | Operation Number | Capability Set |
| REQUEST | getAlertConfiguration | 6 | 1 |
| SUBMIT | enableGeneration | 7 |  |
| SUBMIT | disableGeneration | 8 |  |
| PUBLISH-SUBSCRIBE | monitorAlert | 9 | 4 |

### High-Level Requirements

The alert service shall provide:

- the capability for publishing and receiving alerts;

- the capability for controlling reporting of alerts.

The alert reporting service shall provide the capability for requesting and modifying the configuration of the generation of alert reports.

The list of alerts (i.e. of AlertDefinition objects) that are supported by the alert service shall be declared in an out-of-band agreement.

### Functional Requirements

The actual generation of alerts shall be enabled by the enableGeneration operation, and disabled by the disableGeneration operation.

Generation of all alerts shall be initially disabled.

The getGenerationConfig operation shall return the current configuration for the generation of an alert.

### OPERATION: getAlertConfiguration

#### Overview

The getAlertConfiguration operation allows a consumer to retrieve the current configuration for the generation of an alert.

| Operation Identifier | getAlertConfiguration |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | REQUEST | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |
| OUT | RESPONSE | No | alertConfigs : List<AlertConfiguration> |

#### Structures

The domain and keys parameters shall be used to build a list of AlertDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the AlertDefinition objects for which the configuration is requested.

If a requested AlertDefinition reference is unknown then an UNKNOWN error shall be returned.

The response shall contain the matching list of alert configurations for each AlertDefinition object of the input list.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested alerts is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: enableGeneration

#### Overview

The enableGeneration operation allows a consumer to control whether instances of specific alerts are generated or not.

| Operation Identifier | enableGeneration |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Body Signature |
| IN | SUBMIT | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |

#### Structures

The domain and keys parameters shall be used to build a list of AlertDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the AlertDefinition objects for which instances are requested to be generated.

No error shall be raised if alert generation is already enabled for an alert object; i.e., enabling an already enabled alert will not result in an error.

If a requested AlertDefinition reference is unknown then an UNKNOWN error shall be returned.

If an error is raised then no modifications shall be made as a result of this operation call.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested alerts or group objects is unknown;

- a list of the indexes of the error values shall be contained in the extra information field.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: disableGeneration

#### Overview

The disableGeneration operation allows a consumer to stop the generation of instances of specific alerts.

| Operation Identifier | disableGeneration |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |

#### Structures

The domain and keys parameters shall be used to build a list of AlertDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the AlertDefinition objects for which instances generation is requested to be disabled.

No error shall be raised if alert generation is already disabled for a matched AlertDefinition object; i.e., disabling an already disabled alert will not result in an error.

If a requested AlertDefinition reference is unknown then an UNKNOWN error shall be returned.

If an error is raised then no modifications shall be made as a result of this operation call.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested alerts is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: monitorAlert

#### Overview

The monitorAlert operation allows a consumer to subscribe for alerts. The operation conceptually publishes AlertEvent structures, but it actually publishes the fields that are not present in the list of subscription keys.

| Operation Identifier | monitorAlert |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Subscription Keys | alertKey: MAL::Identifier alertVersion: MAL::UInteger alertSeverity: MAL::UOctet |
| Pattern Sequence | Message | Nullable | Type Signature |
| OUT | PUBLISH/NOTIFY | No Yes | timestamp : MAL::Time arguments : List<AttributeValue> |

#### Structures

The value of the domain field of the UpdateHeader shall be set to the domain field of the identity of the AlertDefinition object whose instance is reported.

The value of the alertKey subscription key shall be set to the key field of the identity of the AlertDefinition object whose instance is reported.

The value of the alertVersion subscription key shall be set to the version field of the identity of the AlertDefinition object whose instance is reported.

The value of the alertSeverity subscription key shall be set to the numeric value of the severity field of the AlertDefinition object whose instance is reported.

The timestamp parameter of the publish message body shall be set to the time when the alert has been detected.

The arguments parameter of the publish message body shall be set to the values of the parameters declared in the alert definition.

#### Errors

The operation does not return any errors.

## Service: Aggregation

### Overview

The aggregation service allows the user to acquire several parameter values in a single request.

Aggregations are generated periodically, at a specific and configurable generation interval.

Table Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 1 au texte que vous souhaitez faire apparaître ici.-4:  Aggregation Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| MC | Aggregation | 4 | 6 | 2 |
| Interaction Pattern | Operation Identifier | Operation Number | Capability Set |
| PUBLISH-SUBSCRIBE | monitorValue | 1 | 1 |
| REQUEST | getValue | 2 | 2 |
| REQUEST | getReportingConfiguration | 9 | 3 |
| SUBMIT | enableReporting | 10 |  |
| SUBMIT | disableReporting | 11 |  |
| SUBMIT | setReportingPeriod | 12 |  |
| SUBMIT | addAggregation | 6 | 5 |
| SUBMIT | removeAggregation | 8 |  |

### High-Level Requirements

The aggregation service shall provide:

- the capability for creating and deleting aggregations;

- the capability for periodic reporting of predefined or newly created aggregation values;

- the capability for requesting the current values of the aggregation;

- the capability for controlling reporting of the aggregation values.

Periodic reports for aggregations shall be generated once for each cycle of a specified interval.

An initial list of aggregations (i.e. of AggregationDefinition objects) that are supported by the aggregation service shall be declared in an out-of-band agreement.

### Functional Requirements

The actual generation of reports for an aggregation shall be enabled by the enableReporting operation, and disabled by the disableGeneration operation.

If an aggregation is required to send periodic reports, then the time between these reports shall be controlled using the setReportingPeriod operation.

No periodic reports shall be generated when the reportInterval field is set to ‘0’.

The ordering of the values in the AggregationValue object shall match the ordering of parameters in the AggregationDefinition structure.

### OPERATION: monitorValue

#### Overview

The monitorValue operation allows a consumer to subscribe for aggregation value reports.

| Operation Identifier | monitorValue |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Subscription Keys | aggregationKey: MAL::Identifier aggregationVersion: MAL::UInteger |
| Pattern Sequence | Message | Nullable | Type Signature |
| OUT | PUBLISH/NOTIFY | No No | timestamp : MAL::Time values : List<ParameterValueData> |

#### Structures

The value of the domain field of the MAL::UpdateHeader of the Publish message shall be set to the domain field of the identity field of the AggregationDefinition object representing the aggregation.

The value of the aggregationKey subscription key shall be set to the key field of the identity field of the AggregationDefinition object representing the aggregation.

The value of the aggregationVersion subscription key shall be set to the version field of the identity field of the AggregationDefinition object representing the aggregation.

The timestamp parameter of the publish message body shall be set to the time when the AggregationValue is built.

The values parameter of the publish message body shall be set to the latest known values of the aggregation parameters at the time when the AggregationValue is built.

#### Errors

The operation does not return any errors.

### OPERATION: getValue

#### Overview

The getValue operation returns the latest received value for a requested aggregation.

| Operation Identifier | getValue |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | REQUEST | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |
| OUT | RESPONSE | No | aggregationValue : AggregationValue |

#### Structures

The domain and keys parameters shall be used to build a list of AggregationDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the AggregationDefinition objects whose values are requested.

If the requested aggregation is unknown, or if it has been removed by a call to the removeAggregation operation, then an UNKNOWN error shall be returned.

Using the operation shall have no impact on the periodic reporting of the aggregation.

The parameter values in the aggregationValue returned parameter shall be set to the latest known values of the aggregation parameters at the time of the call, and the timestamp field of the parameter shall be set accordingly to that time.

#### Errors

The operation may return the following error: ERROR: UNKNOWN:

- the requested aggregation is unknown.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | Not Used |

### OPERATION: getReportingConfiguration

#### Overview

The getReportingConfiguration operation allows a consumer to retrieve the current configuration for the generation of reports for an aggregation.

| Operation Identifier | getReportingConfiguration |
| --- | --- |
| Interaction Pattern | REQUEST |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | REQUEST | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |
| OUT | RESPONSE | No | reportConfigs : List<ReportConfiguration> |

#### Structures

The domain and keys parameters shall be used to build a list of AggregationDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the AggregationDefinition objects for which the report configuration is requested.

If a requested AggregationDefinition reference is unknown, or if the corresponding object has been removed by the removeAggregation operation, then an UNKNOWN error shall be returned.

The response shall contain the matching list of report configurations for each AggregationDefinition object of the input list.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested aggregations is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: enableReporting

#### Overview

The enableReporting operation allows a consumer to request the generation of reports for specific aggregations.

| Operation Identifier | enableReporting |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |

#### Structures

The domain and keys parameters shall be used to build a list of AggregationDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the AggregationDefinition objects for which reports are requested to be generated.

No error shall be raised if report generation is already enabled for a matched AggregationDefinition object; i.e., enabling an already enabled aggregation will not result in an error.

If a requested AggregationDefinition reference is unknown, or if the corresponding object has been removed by the removeAggregation operation, then an UNKNOWN error shall be returned.

If an error is raised then no modifications shall be made as a result of this operation call.

If the generation of reports is being enabled for an aggregation, while it was not before, then the provider shall generate a report immediately and start the report interval from that report.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested aggregations is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: disableReporting

#### Overview

The disableReporting operation allows a consumer to stop the generation of reports for specific aggregations.

| Operation Identifier | disableReporting |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |

#### Structures

The domain and keys parameters shall be used to build a list of AggregationDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the AggregationDefinition objects for which reports are requested to be stopped.

No error shall be raised if report generation is already disabled for a matched AggregationDefinition object; i.e., disabling an already disabled aggregation reporting will not result in an error.

If a requested AggregationDefinition reference is unknown, or if the corresponding object has been removed by the removeAggregation operation, then an UNKNOWN error shall be returned.

If an error is raised then no modifications shall be made as a result of this operation call.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested aggregations is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

### OPERATION: setReportingPeriod

#### Overview

The setReportingPeriod operation allows a consumer to set the reporting interval for specific aggregations.

| Operation Identifier | setReportingPeriod |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> reportInterval : MAL::Duration |

#### Structures

The domain and keys parameters shall be used to build a list of AggregationDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the AggregationDefinition objects for which the report generation period is to be set.

If a requested AggregationDefinition reference is unknown, or if the corresponding object has been removed by the removeAggregation operation, then an UNKNOWN error shall be returned.

If an error is raised then no modifications shall be made as a result of this operation call.

The reportInterval parameter shall contain the new report generation period to set to all the AggregationDefinition objects involved in the operation.

If reportInterval is 0, then no report shall be generated for the aggregations involved in the operation.

If reportInterval holds a negative value, then an INVALID error shall be returned.

The report generation period shall be set to the aggregations involved in the operation whatever their reporting status. If the reporting of an aggregation is disabled, then the new reporting period shall be used when the reporting of the aggregation is enabled again.

#### Errors

The operation may return one of the following errors:

- ERROR: UNKNOWN:

- one or more of the requested aggregations is unknown;

- a list of the indexes of the error values shall be contained in the extra information field;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

- ERROR: INVALID:

- the report interval value is negative;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | 3 | Not Used |

### OPERATION: addAggregation

#### Overview

The addAggregation operation allows a consumer to define one or more aggregations that do not currently exist.

| Operation Identifier | addAggregation |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No | newObjects : List<AggregationDefinition> |

#### Structures

The newObjects field shall hold the complete values of the AggregationDefinition objects to be added.

The consumer shall be responsible for allocating the identities of the objects. If the provider considers that an identity is invalid, for example with a wildcard value ‘*’ in a domain part, or with an empty key, then an INVALID error shall be returned.

If one of the supplied aggregation identities is already known by the provider for an existing aggregation, then a DUPLICATE error shall be raised.

If an error is raised then no object shall be created as a result of this operation call.

If a previously existing aggregation has been removed by the removeAggregation operation, then it shall be possible to create a new aggregation with the same identity of the removed one.

The aggregation shall be created with a default value defined by the provider for its generation interval. This value may be 0.

The aggregation reporting shall be enabled as soon as the aggregation is created.

#### Errors

The operation may return one of the following errors:

- ERROR: DUPLICATE:

- one or more of the aggregation objects being added has supplied an aggregation identity that is already known by the provider for an existing object;

- the extra information field contains a list of the indexes of the erroneous values from the originating request list;

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| DUPLICATE | 2 | List<MAL::UInteger> |

- ERROR: INVALID:

- one of the supplied aggregation objects contains an invalid identity according to the rules defined by the provider;

- the extra information field contains a list of the indexes of the erroneous values from the originating list supplied.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| INVALID | 3 | List<MAL::UInteger> |

### OPERATION: removeAggregation

#### Overview

The removeAggregation operation allows a consumer to remove one or more aggregations from the list of aggregations supported by the aggregation provider.

The operation deletes the AggregationDefinition object, allowing its identity to be reused by a new aggregation created by the addAggregation operation.

| Operation Identifier | removeAggregation |
| --- | --- |
| Interaction Pattern | SUBMIT |
| Pattern Sequence | Message | Nullable | Type Signature |
| IN | SUBMIT | No No | domain: List<MAL::Identifier> keys : List<MAL::Identifier> |

#### Structures

The domain and keys parameters shall be used to build a list of AggregationDefinition object references, where the domain field is the domain parameter, the key field is an element of the keys parameter, and the version field is 0.

That list shall identify the AggregationDefinition objects to be removed from the provider.

If a provided aggregation reference is unknown then this operation shall fail with an UNKNOWN error.

Matched AggregationDefinition objects shall be deleted by the provider.

Reusing the object identity of a deleted aggregation shall be allowed in the addAggregation operation to create a new aggregation.

If an error is raised then no aggregations shall be removed as a result of this operation call.

If the operation succeeds then the provider shall not publish aggregation values for the deleted AggregationIdentity objects anymore.

#### Errors

The operation may return the following error: ERROR: UNKNOWN:

- one of the supplied AggregationIdentity object instance identifiers is unknown;

- a list of the indexes of the error values shall be contained in the extra information field.

| Error | Error # | ExtraInfo Type |
| --- | --- | --- |
| UNKNOWN | Defined in MAL | List<MAL::UInteger> |

## Service: Packet

### Overview

The packet service allows a consumer to subscribe to a subset of the space packets, with filtering capabilities based on packets metadata.

The packets metadata are defined by the provider. They consist of a list of keys, which are assigned a value by the provider for each packet. One of the keys is the APID of the packet. The other keys are defined by the provider at deployment time, and they are shared with the consumer through an out of band agreement.

Table Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 1 au texte que vous souhaitez faire apparaître ici.-5:  Packet Service Operations

| Area Identifier | Service Identifier | Area Number | Service Number | Area Version |
| --- | --- | --- | --- | --- |
| MC | Packet | 4 | 9 | 2 |
| Interaction Pattern | Operation Identifier | Operation Number | Capability Set |
| PUBLISH-SUBSCRIBE | deliverPacket | 1 | 1 |

### High-Level Requirements

The packet service shall provide:

- the capability for receiving the packets exchanged by the provider;

- The capability for filtering the received packets;

- The capability to define custom filtering keys specific to a service deployment.

### Functional Requirements

Packets shall be published and received using the deliverPacket operation.

### OPERATION: deliverPacket

#### Overview

The deliverPacket operation allows a provider to publish space packets with associated metadata, and a consumer to receive a filtered set of those packets. The packets metadata translate into subscription keys of the operation.

The published messages semantically correspond to a PacketValue structure. However the fields of that structure are actually splitted into the update header (fields apid and keyValues as subscription keys) and the body (fields payload and timestamp) of the PUBLISH/NOTIFY messages.

A single subscription key named apid is defined in the operation template. However it is very likely that a particular deployment of the service will define additional custom subscription keys.

| Operation Identifier | deliverPacket |
| --- | --- |
| Interaction Pattern | PUBLISH-SUBSCRIBE |
| Subscription Keys | apid: MAL::UShort |
| Pattern Sequence | Message | Nullable | Type Signature |
| OUT | PUBLISH/NOTIFY | No No | timestamp : MAL::Time spacePacket : MAL::Blob |

#### Structures

If the provider chooses to extend the list of subscription keys, then it shall define the ordered list of additional subscription keys in an out of band agreement. This list shall include the name and type of each subscription key.

The list and types of subscription keys declared in the PUBLISH_REGISTER message shall be extended from the operation template by the list of additional subscription keys, if any.

The value of the apid subscription key shall be set to the APID field of the published space packet header.

A value shall be computed by the provider for all the additional subscription keys, if any.

The value of the payload body field shall be set to the full raw content of the published space packet.

NOTE	–	The exact semantics of the domain field of the MAL::UpdateHeader of the Publish message is implementation specific.

NOTE	–	The exact semantics of the timestamp body field is implementation specific. It may or not match the time field of the space packet secondary header.

#### Discussion

The list of additional subscription keys is statically defined at deployment time. It must be used for all the packets published by the provider, even when some of the keys have no meaning for a particular set of packets. In such cases the provider may set the key values to NULL.

This case arises when the provider publishes a flow of packets with meaningfull metadata (apid, A, B), and another flow with meaningful metadata (apid, C). The provider must define the list of additional subscription keys (A, B, C), and set C=NULL for packets in the first flow, and A=B=NULL for packets in the second flow.

An alternative deployment could be to deploy two separate providers of the Packet service, each one dedicated to a single flow of packets. In that case the first provider would define the list of additional subscription keys (A, B), and the second one the list (C). This would limit the use of meaningless subscription keys, at the cost of an additional provider deployed.

# Data types

## Area data types: MC

### ENUMERATION: Severity

The severity enumeration shall be used to hold the possible values for a severity.

NOTE	–	The numerical value represents the increasing severity, and therefore CRITICAL is more severe than ALARM.

| Name | Severity |
| --- | --- |
| Short Form Part | 6 |
| Enumeration Value | Numerical Value | Comment |
| INFORMATIONAL | 1 | Indicates a nominal situation with no consequences. |
| WARNING | 2 | Indicates unexpected behaviour without directly threatening consequences. |
| ALARM | 3 | Indicates behaviour of serious concern requiring the attention of an operator, but not necessarily a malfunction. |
| SEVERE | 4 | Indicates that the monitored item has malfunctioned. Requires operator attention. |
| CRITICAL | 5 | Indicates behaviour with mission threatening consequences. Requires operator attention. |

### Composite: ArgumentDefinition

The ArgumentDefinition structure shall be used to hold the details of an argument definition with a set of associated attributes, such as conversion used.

When a conversion is to be applied to the argument, then the convertedType and convertedUnit fields shall not be NULL.

| Name | ArgumentDefinition |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 1 |
| Field | Type | Nullable | Comment |
| argId | MAL::Identifier | No | Holds the argument definition identifier. |
| description | MAL::String | Yes | Optional argument description. |
| rawType | MAL::AttributeType | No | The raw type of the argument. |
| rawUnit | MAL::String | Yes | The unit for the raw value. |
| convertedType | MAL::AttributeType | Yes | The converted type of the argument. NULL when no conversion is enabled. |
| convertedUnit | MAL::String | Yes | The converted argument units. NULL when no conversion is enabled. |

### Composite: AttributeValue

The AttributeValue structure shall be used to hold an Attribute value. The value may be provided as a raw value or as a converted value.

| Name | AttributeValue |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 2 |
| Field | Type | Nullable | Comment |
| value | MAL::Attribute | Yes | The argument value. May be NULL to represent a NULL AttributeValue. |
| isRawValue | MAL::Boolean | No | If TRUE value is provided as a raw value. If false value is provided as a converted value. |

## Action Service data types

### ENUMERATION: ActionCategory

Contains the default Action category values. It is implementation specific what the meaning of the values are in a particular context.

As allowed by the MAL specification, this list may be extended for a specific deployment. In such a case, an out-of-band agreement would be required for the additional values.

| Name | ActionCategory |
| --- | --- |
| Short Form Part | 10 |
| Enumeration Value | Numerical Value | Comment |
| DEFAULT | 1 | Default category |
| HIPRIORITY | 2 | Category for high priority actions |
| CRITICAL | 3 | Category for critical actions |

### Composite: ActionDefinition

The ActionDefinition structure holds the definition information of an action.

The ActionDefinition object follows the template of the M&C services generic data model (see 2.5). It is mapped onto the MO Object concept defined in the MAL. It is identified by a MAL::ObjectIdentity and may be referenced globally by a MAL::ObjectRef.

| Name | ActionDefinition |
| --- | --- |
| Extends | MAL::Object |
| Short Form Part | 11 |
| Field | Type | Nullable | Comment |
| identity | MAL::ObjectIdentity | No | The Identity of the action. |
| description | MAL::String | No | The description of the action. |
| category | ActionCategory | No | Category of the action. |
| progressStepCount | MAL::UShort | No | Total number of steps that will be reported if PROGRESS reporting is selected in the sent Action. 0 if PROGRESS reporting is not used. |
| arguments | List<ArgumentDefinition> | Yes | The list of argument definitions. If no arguments are defined, then the complete list is replaced with a NULL. |

### Composite: ActionExecutionRequest

The ActionExecutionRequest structure holds the information required for a specific execution of an action such as the argument values to use when requesting a provider to execute the action.

The ActionExecutionRequest structure is a contextual object associated to the ActionDefinition. It is uniquely identified, within the deployment, by the requestId index relative to the ActionDefinition object. This id must be provided by the service consumer, but how uniqueness is ensured is deployment specific.

The ActionExecutionRequest object requires a list of arguments declared as a list of data values. The actual value types, units, and conversion are specified in the associated ActionDefinition object, and may differ for each object. The ActionExecutionRequest structure only holds the actual values.

| Name | ActionExecutionRequest |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 12 |
| Field | Type | Nullable | Comment |
| requestId | MAL::Long | No | A unique id of the action request. It must be provided by the consumer, but how uniqueness is ensured is deployment specific. |
| actionRef | MAL::ObjectRef <ActionDefinition> | No | Refers to the ActionDefinition object of this action request. |
| source | MAL::ObjectRef <Element> | Yes | Generic reference to the entity that created the ActionExecutionRequest. The actual content of this optional field is left to the consumer. |
| stageStartedRequired | MAL::Boolean | No | If TRUE, then a progress event published by the monitorActionExec operation is required for the started stage. |
| stageProgressRequired | MAL::Boolean | No | If TRUE, then progress events published by the monitorActionExec operation are required for the anonymous progress stages. |
| stageCompletedRequired | MAL::Boolean | No | If TRUE, then a progress event published by the monitorActionExec operation is required for the completed stage. |
| argumentValues | List<AttributeValue> | Yes | List containing the values of the arguments. The ordering of the list matches that of the action definition. If a value for a particular entry is not being supplied, then its position is filled with a structure with a NULL value field. If no arguments are defined, then the complete list is replaced with a NULL. |

### Composite: ActionProgressBaseEvent

The ActionProgressBaseEvent is the base type of all events used by the monitorActionExec operation to publish a new execution stage reached by the execution of an action.

| Name | ActionProgressBaseEvent |
| --- | --- |
| Extends | MAL::Composite |
| Abstract |
| Field | Type | Nullable | Comment |
| success | MAL::Boolean | No | True if success, False otherwise. |

### Composite: ActionProgressStartEvent

The ActionProgressStartEvent type is used for publishing an action execution reaching the started stage.

| Name | ActionProgressStartEvent |
| --- | --- |
| Extends | ActionProgressBaseEvent |
| Short Form Part | 13 |
| Field | Type | Nullable | Comment |
| success | MAL::Boolean | No | True if success, False otherwise. |

### Composite: ActionProgressExecutionEvent

The ActionProgressExecutionEvent type is used for publishing an action execution reaching a new execution stage.

| Name | ActionProgressExecutionEvent |
| --- | --- |
| Extends | ActionProgressBaseEvent |
| Short Form Part | 14 |
| Field | Type | Nullable | Comment |
| success | MAL::Boolean | No | True if success, False otherwise. |
| stageCount | MAL::UInteger | No | Total number of expected stages in the nominal execution of the action. |
| executionStage | MAL::UInteger | No | Sequence number of this stage, starting at 1. |

### Composite: ActionProgressCompletionEvent

The ActionProgressCompletionEvent type is used for publishing an action execution reaching the completion stage.

| Name | ActionProgressCompletionEvent |
| --- | --- |
| Extends | ActionProgressBaseEvent |
| Short Form Part | 15 |
| Field | Type | Nullable | Comment |
| success | MAL::Boolean | No | True if success, False otherwise. |

## Parameter Service data types

### ENUMERATION: ValidityState

The ValidityState enumeration shall be used to hold the validity states and their numeric values.

As allowed by the MAL specification, this list may be extended for a specific deployment. However the VALID value shall always be used when the parameter value is in a valid state. Any extended value beyond the standard values shall represent a variant of an invalid state. In such a case, an out-of-band agreement would be required for the additional values.

| Name | ValidityState |
| --- | --- |
| Short Form Part | 20 |
| Enumeration Value | Numerical Value | Comment |
| VALID | 0 | Valid. The raw and converted values of the ParameterValueData structure are valid. |
| EXPIRED | 1 | The parameter has a timeout associated which has expired. The ParameterValueData structure holds formerly valid raw and converted values. |
| INVALID_RAW | 2 | The parameter raw value cannot be obtained, or calculated for synthetic parameters. Both values of the ParameterValueData structure are NULL. |
| INVALID_CONVERSION | 3 | The raw value of the ParameterValueData structure is valid.However the conversion of the parameter value has failed (for example an unexpected value for a discrete conversion), and the converted value of the ParameterValueData structure is NULL. |
| UNVERIFIED | 4 | The validity of the raw value cannot be evaluated because of invalid dependant data. However the value is not NULL and the conversion is applied, if any. |
| INVALID | 5 | The raw value of the ParameterValueData structure is not NULL, however this value is deemed invalid by the provider. The conversion is applied, if any. |

### Composite: ParameterDefinition

The ParameterDefinition structure holds a parameter definition. It follows the template of the M&C services generic data model (see 2.5). It is mapped onto the MO Object concept defined in the MAL. It is identified by a MAL::ObjectIdentity and may be referenced globally by a MAL::ObjectRef.

When a conversion is to be applied to the parameter, then the convertedType field shall not be NULL. The convertedUnit field may be NULL in that case.

| Name | ParameterDefinition |
| --- | --- |
| Extends | MAL::Object |
| Short Form Part | 21 |
| Field | Type | Nullable | Comment |
| identity | MAL::ObjectIdentity | No | The Identity of the parameter. |
| description | MAL::String | No | The description of the parameter. May be empty. |
| rawType | MAL::AttributeType | No | The raw type of the parameter. |
| rawUnit | MAL::String | Yes | The unit for the raw value. If NULL then raw type has no unit. |
| convertedType | MAL::AttributeType | Yes | The converted type of the parameter. NULL when no conversion is enabled. |
| convertedUnit | MAL::String | Yes | The converted parameter unit. NULL when no conversion is enabled. |

### Composite: ParameterValueData

The ParameterValueData structure shall be used to hold a specific value of the parameter.

If rawValue is not NULL, then the type of rawValue shall match the rawType specified in the parameter definition.

If convertedValue is not NULL, then the type of convertedValue shall match the convertedType specified in the parameter definition.

The convertedValue shall be NULL if the convertedType specified in the parameter definition is NULL.

If ValidityState is VALID, EXPIRED, INVALID_CONVERSION, UNVERIFIED or INVALID, then rawValue shall not be NULL.

If ValidityState is INVALID_RAW, then rawValue shall be NULL.

If rawValue is not NULL, and if the convertedType specified in the parameter definition is not NULL, then the provider shall attempt to apply the conversion. If it succeeds, then convertedValue shall not be NULL. If it fails, then convertedValue shall be NULL.

If ValidityState is VALID or EXPIRED, and if the convertedType specified in the parameter definition is not NULL, then convertedValue shall not be NULL.

If ValidityState is INVALID_RAW or INVALID_CONVERSION, then convertedValue shall be NULL.

| Name | ParameterValueData |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 22 |
| Field | Type | Nullable | Comment |
| validityState | ValidityState | No | Holds the validity state for a parameter value. |
| rawValue | MAL::Attribute | Yes | The parameter raw value. The value of NULL is not a valid value, but it is allowed in the structure as an invalid value. |
| convertedValue | MAL::Attribute | Yes | The parameter converted value. |

### Composite: ParameterValue

The ParameterValue structure is a contextual object associated to the ParameterDefinition. It is uniquely identified by the timestamp field, relative to the ParameterDefinition object. It represents a specific time stamped value of the parameter.

| Name | ParameterValue |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 23 |
| Field | Type | Nullable | Comment |
| paramRef | MAL::ObjectRef <ParameterDefinition> | No | The ParameterDefinition object reference. |
| timestamp | MAL::Time | No | The primary timestamp of the value, also called provider time. |
| samplingTime | MAL::Time | Yes | An optional and secondary timestamp of the value, used to capture the sampling time. |
| value | ParameterValueData | No | The actual value of the parameter. |

### Composite: ReportConfiguration

The ReportConfiguration structure is used to retrieve the configuration of the report generation of a parameter. For onboard parameters, the report interval should be a multiple of the minimum sampling interval of that parameter.

| Name | ReportConfiguration |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 24 |
| Field | Type | Nullable | Comment |
| generationEnabled | MAL::Boolean | No | Indicates whether reports for the related parameter are to be generated. |
| reportInterval | MAL::Duration | No | Periodic report interval. |

## Alert Service data types

### Composite: AlertDefinition

The AlertDefinition structure shall be used to provide the definition of an alert including any argument definitions.

The AlertDefinition structure follows the template of the M&C services generic data model (see 2.5). It is mapped onto the MO Object concept defined in the MAL. It is identified by a MAL::ObjectIdentity and may be referenced globally by a MAL::ObjectRef.

| Name | AlertDefinition |
| --- | --- |
| Extends | MAL::Object |
| Short Form Part | 30 |
| Field | Type | Nullable | Comment |
| identity | MAL::ObjectIdentity | No | The Identity of the alert. |
| description | MAL::String | No | The description of the alert. |
| severity | Severity | No | Severity of the alert. |
| arguments | List<ArgumentDefinition> | Yes | The list of argument definitions. |

### Composite: AlertEvent

The AlertEvent structure shall be used to hold the details of an instance of an alert.

The AlertEvent structure is a contextual object associated to the AlertDefinition. It is identified by a timestamp relative to the AlertDefinition object.

The AlertEvent requires a list of arguments declared as a list of data values. The actual value types, and units are specified in the associated AlertDefinition object, and may differ for each object. The AlertEvent object only holds the actual values.

| Name | AlertEvent |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 31 |
| Field | Type | Nullable | Comment |
| alertRef | MAL::ObjectRef <AlertDefinition> | No | The AlertDefinition object reference. |
| timestamp | MAL::Time | No | Time when the alert is generated. |
| argumentValues | List <AttributeValue> | Yes | List containing the values of the arguments. The ordering of the list matches that of the definition. If a value for a particular entry is not being supplied, then its position is filled with a structure with a NULL value field. If no arguments are defined, then the complete list is replaced with a NULL. |

### Composite: AlertConfiguration

The AlertConfiguration structure is used to retrieve the configuration of the generation of an alert.

| Name | AlertConfiguration |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 32 |
| Field | Type | Nullable | Comment |
| generationEnabled | MAL::Boolean | No | Controls whether instances of the related alert are to be generated. |

## Aggregation Service data types

### Composite: AggregationDefinition

The AggregationDefinition structure shall be used to hold definition details of an aggregation. It follows the template of the M&C services generic data model (see 2.5). It is mapped onto the MO Object concept defined in the MAL. It is identified by a MAL::ObjectIdentity and may be referenced globally by a MAL::ObjectRef.

The category field shall hold the category of the aggregation. The current specification defines no standard value. The possible values are deployment specific and shall be defined in an out-of-band agreement.

The list of parameters in the parameters field shall not be empty.

| Name | AggregationDefinition |
| --- | --- |
| Extends | MAL::Object |
| Short Form Part | 60 |
| Field | Type | Nullable | Comment |
| identity | MAL::ObjectIdentity | No | The Identity of the aggregation. |
| description | MAL::String | No | The description of the aggregation. May be empty. |
| category | MAL::Identifier | No | Category of the aggregation. The possible values are deployment specific. |
| parameters | List<ObjectRef <ParameterDefinition>> | No | List containing the parameters which define the aggregation. |

### Composite: AggregationValue

The AggregationValue structure shall be used to hold the values of the aggregation parameters.

The AggregationValue object is a contextual object associated to the AggregationDefinition. It is identified by a timestamp relative to the AggregationDefinition object.

The values shall be held in the same number and order as that defined in the matching AggregationDefinition.

| Name | AggregationValue |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 61 |
| Field | Type | Nullable | Comment |
| aggregationRef | MAL::ObjectRef <AggregationDefinition> | No | The AggregationDefinition object reference. |
| timestamp | MAL::Time | No | The timestamp assigned to all parameter values in the aggregation. |
| parameterValues | List <ParameterValueData> | No | The parameterValues list holds the values of the aggregation parameters. The values must be held in the same order as that defined in the aggregation definition. |

## Packet Service data types

### Composite: PacketValue

The PacketValue structure is used to represent each space packet published by the provider. The structure is actually not used, as the structure fields are actually splitted into the UpdateHeader and the body of the Publish/Notify messages (see 3.7.4).

| Name | PacketValue |
| --- | --- |
| Extends | MAL::Composite |
| Short Form Part | 90 |
| Field | Type | Nullable | Comment |
| payload | MAL:: Blob | No | The payload of the packet. |
| timestamp | MAL::Time | No | Timestamp of the packet. The exact time semantics is provider specific. |
| apid | MAL::UShort | No | The APID of the packet. |
| keyValues | List <MAL::NullableAttribute> | Yes | The list of values representing the packet metadata for the additional subscription keys defined by the provider. |

# Error codes

Errors codes defined in table Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 1 au texte que vous souhaitez faire apparaître ici.-1 shall apply for this specification.

Table Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 1 au texte que vous souhaitez faire apparaître ici.-1:  MC Error Codes

| Error | Error # | Comment |
| --- | --- | --- |
| READONLY | 1 | Operation specific |
| DUPLICATE | 2 | Operation specific |
| INVALID | 3 | Operation specific |

# SERVICE SPECIFICATION XML

The use of XML for service specification provides a machine-readable format rather than the text-based document format. The service specification in XML notation as specified in reference [2] may be accessed at the URLs below.

The published specifications and XML schemas are held in an online SANA registry, located at the following URL:

http://sanaregistry.org/r/moschemas/

The normative XML for this specification, validated against the XML schemas, is located at the following URL:

http://sanaregistry.org/r/moschemas/ServiceDefMC-v.v.xml

where the ‘v.v’ part is replaced with the issue number of the corresponding document.

The latest version of any specification may always be directly addressed by removing the ‘-v.v’ part from the URL; for example:

http://sanaregistry.org/r/moschemas/ServiceDefMC.xml

Protocol IMPLEMENTATION CONFORMANCE Statement Proforma

(Normative)

  - INTRODUCTION

    - OVERVIEW

This annex provides the Protocol Implementation Conformance Statement (PICS) Requirements List (PRL) for an implementation of the Mission Operations M&C Services standard.  The PICS for an implementation is generated by completing the PRL in accordance with the instructions below. An implementation claiming conformance must satisfy the mandatory requirements referenced in the PRL.

An implementation’s completed PRL is called the PICS. The PICS states which protocol features have been implemented. The following entities can use the PICS:

- the protocol implementer, as a checklist to reduce the risk of failure to conform to the standard through oversight;

- the supplier and acquirer or potential acquirer of the implementation, as a detailed indication of the capabilities of the implementation, stated relative to the common basis for understanding provided by the standard PICS proforma;

- the user or potential user of the implementation, as a basis for initially checking the possibility of interworking with another implementation (while interworking can never be guaranteed, failure to interwork can often be predicted from incompatible PICSes);

- a protocol tester, as the basis for selecting appropriate tests against which to assess the claim for conformance of the implementation.

    - Notation

      - Status Column Symbols

The following are used in the PRL to indicate the status of features:

| Symbol | Meaning |
| --- | --- |
| M | Mandatory |
| O | Optional |

      - Support Column Symbols

The support of every item as claimed by the implementer is stated by entering the appropriate answer (Y, N, or N/A) in the support column.

| Symbol | Meaning |
| --- | --- |
| Y | Yes, supported by the implementation |
| N | No, not supported by the implementation |
| N/A | Not applicable |

  - GENERAL INFORMATION

    - IDENTIFICATION OF PICS

| Ref | Question | Response |
| --- | --- | --- |
| 1 | Date of Statement (DD/MM/YYYY) |  |
| 2 | CCSDS document number containing the PICS |  |
| 3 | Date of CCSDS document containing the PICS |  |

    - IDENTIFICATION OF IMPLEMENTATION UNDER TEST (IUT)

| Ref | Question | Response |
| --- | --- | --- |
| 1 | Implementation name |  |
| 2 | Implementation version |  |
| 3 | Machine name |  |
| 4 | Machine version |  |
| 5 | Operating System name |  |
| 6 | Operating System version |  |
| 7 | Special Configuration |  |
| 8 | Other Information |  |

    - USER IDENTIFICATION

| Supplier |  |
| --- | --- |
| Contact Point for Queries |  |
| Implementation name(s) and Versions |  |
| Other Information Necessary for full identification, e.g., name(s) and version(s) for machines and/or operating systems; System Name(s) |  |

    - INSTRUCTIONS FOR COMPLETING THE PRL

An implementer shows the extent of compliance to the protocol by completing the PRL; the resulting completed PRL is called a PICS.

  - MO M&C SERVICES PICS

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1-1 | Action service | 3.3, 4.1 and 4.2 | O |  |
| 1-2 | Parameter Service | 3.4 and 4.3 | O |  |
| 1-3 | Alert Service | 3.5, 4.1 and 4.4 | O |  |
| 1-4 | Aggregation Service | 3.4, 3.6, 4.3 and 4.5 | O |  |
| 1-5 | Packet Service | 3.7 and 4.6 | O |  |

Security, SANA, and Patent Considerations

(Informative)

SECURITY CONSIDERATIONS

The security considerations of this specification are the same as those of reference [2]. Specifically, authentication and authorisation of a participating consumer or provider is provided by the MAL access control concept and is covered in subsections 3.6, 5.2, and 5.3 of the Reference Model (reference [1]).

Security of a communications link is delegated to the transport layer.

SANA CONSIDERATIONS

The recommendations of this document request SANA populate the registry specified in reference [2] with the schema and XML detailed in section 6 of this document.

As stated in reference [2], the registration rule for change to this registry requires an engineering review by a designated expert. The expert shall be assigned by the WG Chair, or in absence, Area Director.

PATENT CONSIDERATIONS

The recommendations of this document have no patent issues.

Definition of Acronyms

(Informative)

API	Application Program Interface

AMS	CCSDS Asynchronous Messaging System

CCS	Central Checkout System

CCSDS	Consultative Committee for Space Data Systems

COM	Common Object Model

MAL	Message Abstract Layer

M&C	Monitor and Control

MCS	Mission Control System

MO	Mission Operations

SPP	[CCSDS] Space Packet Protocol

UML	Unified Modeling Language

XML	eXtensible Markup Language

Informative References

(Informative)

[Erreur ! Utilisez l'onglet Accueil pour appliquer Heading 8,Annex Heading 1 au texte que vous souhaitez faire apparaître ici.1] 	Mission Operations Services Concept. Issue 3. Report Concerning Space Data System Standards (Green Book), CCSDS 520.0-G-3. Washington, D.C.: CCSDS, December 2010.

NOTE	–	Normative references are contained in 1.9.

# Comments

The definition looks more like the definition of a value than the definition of a parameter

TODO : add the nullable parameter formalism

done

To be updated

To be updated

Are the services Check & Aggregation not fundamental ? What about Packet ?

I would remove from « in therms of…” and the 3 examples

done

TODO : retrieve source of the figure

Language API books changed to silver ?

Do we keep/remove/modify this section as MC :Action no longer covers the action forwarding scenario ?

done

I do not fully understand the example. Pre-transmission checking was part of the Action service, but it is no longer the case. Should we consider that it is an example of an extension beyond the standard (as it is defined in the Nomenclature section) ? Or should we remove this whole paragraph ?

Remove

Done

Check references

I do not think that the example is correct, that the access control could be used that way. Should the paragraph be removed entirely ?

It’s a way of using it that I didn’t think of. But it’s interesting => To move or to refrence in “Concurrency Control”: “the access control forbids using operations when concurrent accesses are occurring”.

Removed after discussion

Candidate for either removal or drastic shorten

done

Maybe keep but shorter

done

Data structure ?

done

Do not use “task” but “action”

Done, however « task » was the word used in the definitions part

We do not need to explain why we did this choice.. I would propose to only write : « If this feature is needed, it can achieved by using the automation services, or with deployment specific logics”.

done

The Action service no longer covers the case of action forwarding scenario. Should we keep this section ?

Moreover i twas agreed in the MAL book that the From/To fields are Identifiers, and that mapping to transport addresses is to be specified in an ICD.

done

Should not this be Authorization instead ?

No : we want to be sure that the action comes from a legit consumer.

We use status here, and value afterwards. Is there a need to be more consistent ?

Values everywhere !.

done

In the original document the word « report » is frequently used in place of the word « update » defined here. It seems that « report » is used in the PUS standard, which is very present under the specification of the Parameter service. I believe we should be consistent in this specification, and I have chosen the « report » option.

Good : it’s more close to what operational people will understand/

Data structure

done

We can keep the check as an implementation detail not needed for interoperability or not now. The interoperability part will use Alert.

The monitoring and control of a component includes automatic checks of the parameter values to detect abnormal behaviours. The check service only provides the result of these checks.

The actual definition of the check and how they are executed is not part of the interoperability interfaces.

If this information needs to be exchanged, this can be done either by service extension or deployment specific exchange.

done

I recommend deleting this section

Or move it in 2.2 ? It’s a nice “tip”

To be discussed in WG

Done here

how should this be interpreted ?

This general description must be more precise. It should also used well defined terms.

I am not sure of the SPP reference here.

done

Copy-paste error ?

done

No, the APID is one field among others… the packetValue should hold an objectRef to its definition. The link is defined by the deployment.

The packetValue is {

objRef<PacketDef>

apid

keyValues

value

}

done

I would rather have it exactly like the parameters.

done

No (see above).

I would add a timestamp like parameter

MC ?

Yes : M&C services and MC area

This constraint has been discussed during the Fall meeting ‘22. Simple solutions can be designed such as partitioning of the index range, and need not be fixed in the specification.

Generic usage of the word reference. This is not a MAL::ObjectRef. Actually this refers to the couple :

- requestId field of the ActionRequest

- key field of the actionId field of the ActionDefinition

The current structure does not allow reporting of an error code

During Fall ’22 was discussed the possibility for a new requestExecutionWithReturn operation.

postponed

Agreed during Fall ’22 to renumber the operations as the backward compatibility is not ensured

To be confirmed

check link

This is a UInteger, not a List as declared below.

Check references

Keep or remove ?

done

change

This wording assumes this number is known at start and cannot change, but allows that it may differ from one execution to the other for the same action.

This means that if an execution fails at stage 5/10, then the last message will be (EXECUTION 5/10 False) if stageProgressRequired is true, even if stageCompletedRequired is true. It will be (COMPLETION False) if stageProgressRequired is false.

This formulation prevents a consumer from reusing old ids. This is also true for the next assertions.

The validity expression has been removed from the Parameter definition. We could still keep the concept, making it implementation specific, or remove it also from this flow chart and from the list of  ValidityState.

Source of this diagram ?

It would be great to at least explain what the validityState is for (maybe only with text)

Done, in the comment column of the ValidityState table. Duplicates somehow the requirements in section 3.4.3.

This seems consistent with the assertions related to the UNVERIFIED and INVALID states

The conditions leading to an UNVERIFIED or INVALID_CONVERSION may occur simultaneously. Which status should we keep ?

Explicitly set NULL as converted value. INVALID_CONVERSION means that the raw value is valid.

Add a subscription key related to the validityState ?

We choose to send the timestamps and a ParameterValueData, instead of a ParameterValue, in order to avoid duplication of the ObjectRef<ParameterDefinition>, already known from the subscription keys.

I understand this as : calling the getValue operation has no impact on the values published by the monitorValue operation.

If NULL is a valid raw value, then we should change this into NullableAttribute

done

This structure does not refer to the ParameterDefinition object. As a result the operation cannot accept a wildcard input list.

It might be useful to apply the operation onto parameters from a specific domain. If so the type signature should be changed to a new type ObjectRefFilter.

done

A single value instead of a List keeps the operation simple. It is also possible to make it a List, but we should then declare a Composite {parameterRef, reportInterval} to be consistent with the « no related List » policy.

The original spec allows 0 as a valid value for the reportInterval, and says no report will be generated.

I believe this is confusing to have an enabled parameter with no report.

I suggest this possible use of the 0 value.

Is there an external initial configuration as for the parameter service ?

This should be deployment specific, defined by the asset implementer.

done

This structure does not refer to the AlertDefinition object. As a result the operation cannot accept a wildcard input list.

This structure does not refer to the AggregationDefinition object. As a result the operation cannot accept a wildcar  input list.

What is the index of the first element, 0 or 1 ?

Same question throughout the document.

done

A single value instead of a List keeps the operation simple. It is also possible to make it a List, but we should then declare a Composite {parameterRef, reportInterval} to be consistent with the « no related List » policy.

In a first version of the service, aggregations are actually known by out of band agreement, and their definition cannot change. As a result the only useful operation is getReportingConfiguration which reports the « variable part » of the aggregation.

Lets the provider define its own validity rules

To be confirmed by the WG discussion about MO Object deletion.

done

I believe that the wildcard value was useful before in conjunction with the domain field of the header, acting as a filter. With MAL v2 this field no longer exists. It is also impossible to set wildcard fields in an ObjectRef. As a result the only possible wildcard with the proposed type signature is a NULL parameter, leading to removing all known aggregations from the provider.

If we want the filtering function, then we must define an ObjectRefFilter type.

To be discussed in WG

rejected

DeliverPacket

Done

Could be moved to the Alert service data types section

The severity field has been removed from the Check. Delete this or reset severity in Check ?

done

To be changed with the new MAL List

done

If it’s the requestId, it should be clarify.

The fact that the requestId should be unique within the deployment should be stated here.

done

To move to section 4

done

Move requirements in comment column to the section defining the ParameterValueData type.

done

This state could be removed, and replaced by the INVALID state with a NULL raw value.

This is changed from the original specification to make it consistent with the comment in the ValidityState definition.

Comment from César Coelho:

I suggest to simplify the ParameterValue structure to have just two fields:

- samplingTime (MAL:Time)

- value (MAL:Attribute)

If you think about it, in order to make and plot a Timeseries, all you need to have is a list the above, so basically, a set of points, with time coordinates (for the x-axis), and the values (for the y-axis).

After having this core data structure defined, you can build the rest of the data model around it.

Have a thought about it, I believe that everything would be also simpler.

If you want synthetic data (so called “converted values” in MO), then you can later on generate it out of the raw data in the structure above.

To be discussed in WG

Done, keep it as is, but add a samplingTime

Should we keep this or should we fix 0 as an invalid value ?

With the change proposed in 3.4.10, the value 0 in setReportingPeriod should translate into the smallest valid value for the parameter. That value should be reported here, so 0 should be invalid.

If this change is rejected, then we should add here : No periodic reports to be generated if this is set to ‘0’

To be consistent with the AlertEvent specification

TODO add shall, change into a list of requirements

The timestamp is no longer part of the COM object

Update to new MAL List

done

Could also include a maximum severity level

Note that there is currently no timestamp in the structure

Update codes according to final choice in MAL

done