## Slide 1: CCSDS Delivery Agent
Relay operations scenarios

## Slide 2: Scenario 0 : nominal case
MOC
DTN Network
Asset
The asset and the MOC are connected through a DTN network.
The MOC controls the Asset nominally,
The Delivery Agent service is dormant.

## Slide 3: Scenario 1 : emergency case
MOC
DTN Network
Asset
R
Space Packet / Prox-1 / other
CDA Service interaction
The Asset has an issue (fail-mode ?). It is not DTN enabled anymore.
It is in a non-nominal mode, scanning for a connection from the relay (Space packet? Prox-1? …)
The Relay R provides the Delivery Agent service.
Through the DTN network, the MOC:
(op1) configures the connection between the Relay and the Asset
(op2) sends a command to be relayed to the Asset (last-hop)
(op3) requires the retrieval of the Asset’s telemetry (first-hop)
After that, the asset recovers to nominal mode (i.e Scenario 0)

## Slide 4: Scenario 2 : legacy case
MOC
DTN Network
Asset
R
CDA Service interaction
The Asset was launched before the DTN network was setup. It is not DTN enabled, and therefore called ‘legacy’.
The Relay R provides the Delivery Agent service. It’s connection to the Asset is already configured.
Through the DTN network, the MOC:
(op2) sends commands to be relayed to the Asset (last-hop)
(op3) requires the retrieval of the Asset’s telemetry (first-hop)
This is the nominal way of operating this asset.
Remark: it could make sense that (op2) and (op3) are actually one single « operation » where the telemetry is retrieved automatically, without any explicit request from the MOC
Space Packet / Prox-1 / other

## Slide 5: Scenario 3a : double assets case
MOC
DTN Network
Asset2
R2
R1
A1
SPP
CDA Service interaction
This Scenario builds up on the two previous scenarios, but with 2 assets, commanded by a single MOC.
This highlights the need of addressing the right relay in the DTN network. The expected operations are the same in the previous scenarios.
Space Packet / Prox-1 / other

## Slide 6: Scenario 3b : emergency case, 2 MOCs
DTN Network
MOC Asset
MOC Relay
DTN Network
Asset
R
CDA Service interaction
CDA Service interaction
This Scenario builds up on the two previous scenarios, but with 2 MOCs, one responsible for the Relay, the other for the Asset.
We expect that the MOC responsible for the Asset cannot directly contact the Relay. It has to send a request to the MOC responsible for the Relay (ground-to-ground) that will check the commands and transmit them to the Relay.
Space Packet / Prox-1 / other

## Slide 7: Generalization
DTN Network
Relay
CDA1
CDA2
Legacy / fail-mode Rover
MOC « legacy » part
MOC
Asset
The CCSDS Delivery agent can be generalized as follows:
If the asset is not DTN enabled (legacy or in fail-mode), it can receive command (last hop) and transmit telemetry (first hop) through the Delivery Agent (activated by the MOC).
If the MOC is not DTN enabled, it can be send commands (first hop) and receive telemetry (last hop) through the Delivery agent (activated by… ? the MOC? Something else? To be clarified).
From the system point of view, the MOC is made of the legacy part + the delivery agent CDA2.
Space Packet / Prox-1 / other
HTTP ? Space Packet?