## Slide 1: A Representative Application of a Layered Interface Modeling Pattern
Peter Shames, Marc Sarrel,
Sanford Friedenthal (Affiliate)
Jet Propulsion Laboratory, California Institute of Technology
© 2016. California Institute of Technology. Government Sponsorship Acknowledged.
”meta” version presented in Garlan’s SW Arch class @ JPL

## Slide 2: Meta-Introduction
This paper was originally presented at the 26’th Annual INCOSE International Symposium
  The primary topics in the paper focused on issues involved with accurately representing layered interfaces
  It provides a set of modeling patterns that can be applied to describe various levels of decomposition and detail, from physical down to behavioral
The meta aspects of this paper relate to the use, but not the exposition of, an underlying viewpoint/view methodology and how this method may directly be used to support system architecture modeling and trade studies.
  The meta aspects will be noted like this …

## Slide 3: Introduction
Interfaces define
  How a system interacts with its environment
  How the components of a system interact
Interfaces are specified in many domains
  Electrical, mechanical, thermal, fluid, human, data
System engineers must specify, analyze and verify this range of interfaces
In addition, individual interfaces can be very complex
  Specification for USB 2 is 650 pages
Model Based Systems Engineering offers a method to support accurate interface specification, and allow common representation across disciplines
A profile of SysML is adopted as the MBSE language of choice

## Slide 4: Layered Interface Modeling Approach
Leverage layered interface concepts used to define communication interfaces (e.g., OSI stack, ISO/IEC 7498)
  This layered ISO BRM interface model has functioned well, for decades, to describe the Internet and deployed systems
Specify the interface in terms of what is exchanged
Realize the interface by transforming the exchange from application layer data to physical layer signals
Define interactions between peer entities in the interacting components, and between vertical layers of each component.
This transformation is from abstract view to realized view

## Slide 5: Why Layered Interfaces
Separation of concerns
Each layer of the interface describes it’s own functionality and addresses its own set of concerns
Each layer may be considered separately, or in combination with others
Layers are independent of each other, and can be combined in permissible ways
All layers must function correctly, together, for the interface to work as a whole.
Layering persists from abstract view to realized view

## Slide 6: Why Layered Interfaces (cont.)
Adoption of several different views provides a rich and flexible representation in the model
  Different interface abstractions are provided, from logical flows to complete protocol stacks
  End-to-end data flows, connectivity, and data transformations
  Physical connections
  Protocol specifications
  Message definitions
  Complete interface specifications that span discipline concerns
The generation of these views from a single model ensures their consistency.
Different viewpoints are used to address different concerns

## Slide 7: A Simple Example
The simple view is “boxes and lines”
  What are the interfaces?
  What are the protocols?
End-to-End simple view
  Send a PDF file from A to B.
  This is the requirement, what the user sees.
Interface Specification
  Implemented with HTTP, TCP, IP and Ethernet.
  The protocol stacks in each component are connected both horizontally and vertically.
Simple lists of interface protocols are just not sufficient to understand the architecture.
For some views abstraction works fine and hides details

## Slide 8: Selection of Focus
We can focus on just the TCP layer.
  How it is connected (horizontally).
  How it behaves (horizontally).
We can focus on just the stack.
  How it is connected (vertically).
  How it behaves (vertically).
Data logically flows across the horizontal layers, the TCP spec describes the behavior of the peer protocol entities.
Data actually flows “down the stack” through each successive layer until it gets to the physical layer where the “real” connections occurs.
“On the wire” the whole stack is visible.
The selected view provides the “focus”

## Slide 9: Space Data System Example
Space data systems are composed of a flight segment and a ground segment (including ground stations).
End-to-End Information Systems track data within each segment, and between the segments as an integrated flow.
Systems include both mission-specific and shared multi-mission resources.
So, how to accurately describe, model and characterize these systems and their interfaces?
EEIS is fundamentally a systems-of-systems problem …

## Slide 10: End to End Information Flow
End to End view of whole context
Major physical elements
Coarse-grained decomposition
Elides organizations, ownership and operational details
Does not show interface or protocol details yet…
Abstract view of components, shows only application data flows

## Slide 11: Subsystem Interface Specification
Shows Avionics and Telecom subsystems from End-to-End view
  Shows decomposition, component and hardware-software relationships
Does not show interface details or protocol stacks
Viewpoint still deals in abstractions, but now ports become visible

## Slide 12: Subsystem Interface Realization
Specification
Realization
Details of protocol stack
Ownership split among components between IP and Ethernet layers
Interface Binding Signature
The relationship between specification and realization is exposed

## Slide 13: Typical Communication Interface Layers
Application layer: packet transfer protocol, manages exchange of packet data between applications.
Transport layer: Transmission Control Protocol (TCP), provides end-to-end, once only, in order, complete delivery of data.
Network layer: Internet Protocol (IP), provides network layer routing over any number of intermediate network nodes.
Data link layer: 1 Gb Ethernet, provides data link layer services that may involve a fabric of switches and hubs.
Physical layer: twisted pair cable (Cat-5) and RJ-45 plug terminations.
Layering is a pattern, ISO BRM has seven layers, we seldom define all of them

## Slide 14: Protocol Entity
Every protocol entity at layer (N) has three ports:
  the interface that provides services to the upper (N+1) layer
  the interface that requires services of the lower (N-1) layer
  the interface with the peer protocol entity at the same layer
There may also be a management interface, which can be in-line or separate
Protocol Entity is a basic building block pattern, may include management

## Slide 15: Protocol Entity Behavior
Activity on right is one of many contained in the states on the left
Like system elements, behavior specs may also be decomposed

## Slide 16: Protocol Entity Behavior (cont.)
Describes how a protocol entity behaves when receiving a Protocol Data Unit (PDU) from a peer entity
Describes the exchange(s) of PDUs between peers
May describe the behavior at the required and provided interfaces, such as start-up, connection establishment, and Service Data Unit (SDU) transformation into PDUs
Typically involves describing the dynamics of PDU exchanges, including nominal and error conditions
Peer entity interaction is a protocol behavior pattern

## Slide 17: Protocol Entity Interaction
Constrains the behavior of peer protocol entities
Protocols are defined layer by layer, interfaces are always a stack

## Slide 18: Protocol Entity Interaction (cont.)
Specifies allowable interactions between peer protocol entities
Keeps the peer state machines synchronized
Describes the PDU exchanges you would see on the wire for a single layer
Peer to peer interactions within each protocol layer may be complex

## Slide 19: Behavior Context
Shows all behaviors in context
Shows compliance with RFC 793 spec
  Note that Pkt Xfer entity also complies with RFC 793 spec at the Required Interface
  Interface and behavior
Behavior on vertical SDU links typically implementation specific, i.e. not specified in standards
Only certain aspects of behavior must be specified for interoperability

## Slide 20: Interface Physical Layer
A Trade Study can address which layers are in Transceiver vs software

## Slide 21: Electrical Connection
Interfaces may be further decomposed
Get as specific as your problem demands
Physical layer interfaces may be governed by constraints based on physical laws
  Ohm’s law, Kirchhoff's law, laws of thermodynamics, etc.
  Instead of activities and state machines
Even the Physical layer may be decomposed in its own viewpoint

## Slide 22: Data Packet Structure
Generic Space Packet
Specific Thermal Packet
Shows how packets conform to standard
Left side is generic space packet
  Arrows show typing
  Boxes show constraints
Right side is specific thermal packet
  Show adaptations (redefinition, subsetting and new constraints)
Information in a separate viewpoint, related using correspondence

## Slide 23: Methodology Summary
Nested ports to capture interface details that a component presents
Specification of stacks allows components to be explicit about what combinations of protocols, and in what order, they support
Reference properties for protocol entities in ports allow separation of protocol implementation from all the contexts in which it’s used
Power of the method depends on rigor of model content, rather than visual presentation on SysML diagrams
Meta-summary: viewpoints, views, and abstraction are essential tools

## Slide 24: Summary
Layered Interface Modeling Approach provides a means to model complex interfaces
May be elaborated to include additional details as needed
Ties to standards, and subsections of standards
Compliance of data structures, behavior and physical laws
Layered Approach
  Specification vs Realization
  Layers defined by protocol entities that have peer layer interactions and layer to next layer interactions.

## Slide 25: Summary (cont.)
Allows construction of full set of consistent views at desired level of detail
Development of library components allows re-use of common protocols and standards
Only model what is needed at any given point
Meta-summary, cont: Many architectural methods adopt view/viewpoint terminology. Careful selections of viewpoints, the associated “language” that they use, and the specific representation is essential if models are to be clear and readily understood.

## Slide 26: Acknowledgements
The trade studies that first defined and used this method were chartered and funded by the NASA Space Communications and Navigation (SCaN) Program Office, with strong management support from Phil Librecht and encouragement to adopt OMG SysML™ modeling from Jim Schier. The authors would also like to acknowledge the excellent leadership and guidance of the trade study tasks provided by the co-leads: Wallace Tai from JPL and Nate Wright from GSFC.
Meta-ACK: Use of CCSDS RASDS, 311.0-M-1; ISO RM-ODP, ISO/IEC 10746; and ISO SW Arch, ISO/IEC 42010.