## Slide 1: Plug-and-Play View of SOIS

## Slide 3
Adding/Removing Devices

## Slide 4
Service | Function | Interface/Primitive | Parameter
Device Enumeration Service (DES) | provides table of device names and virtual / physical identifiers – Management of existing devices – Management and user notification of added devices – Management and user notification of removed devices | DEVICE_FOUND DEVICE_LOST ENUMERATE_DEVICES ADD_DEVICE REMOVE_DEVICE QUERY_DEVICES | Transaction Identifier, Result Metadata, Virtual Device Identifier, Physical Device Identifier, Device Serial Number, Device Type, Spacecraft Network Address
Device Discovery Service (DDS) | searches sub-net(s) for devices, recognizes changes to device and sub-net accessibility, provides notifications -discovers initial topology -detects changes to topology -informs management with discovery information -provides notification | DEVICE_DISCOVERY DEVICE_DISCOVERY_LOSS | DDSAP Address, Device Address, Device Metadata
Device Virtualization Service (DVS) | provides virtual device interface, hides physical device mapping – Commanding – Data Acquisition | ACQUIRE_FROM_DEVICE COMMAND_DEVICE | Transaction Identifier, Result Metadata, Virtual Device Identifier, Value Identifier, Value, Timestamp
Device Access Service (DAS) | provides direct physical device access when needed – Acquire value from device – Command a device | ACQUIRE_FROM_DEVICE COMMAND_DEVICE | Transaction Identifier, Result Metadata, Physical Device Identifier, Value Identifier, Value, Timestamp
Packet Service (PS) | provides means to read / write packets to devices providing packet delivery over a single subnetwork | PACKET_SEND PACKET_RECEIVE PACKET_FAILURE | Data, PSSAP, PDSAP, Service Class, Channel, Priority, Failure Metadata
Memory Access Service (MAS) | provides means to read write data to memory providing direct access to device memory | READ, WRITE, READ/MODIFY/WRITE, MEMORY_ACCESS_RESULT | MASAP Address, Destination Address, Transaction ID, Memory ID, Start Memory Address, Size, Mask, Data, Channel, Priority, Acknowledge, Authorization, Verification, Result Metadata
Message Transfer Service (MTS) | provides a standard service for mediating the transfer of discrete data (messages) between onboard software users in a distributed onboard system – send a discrete message; – receive the next queued discrete message; – send a query message and receive a reply message back. – multicast a discrete message (publish-subscribe); – broadcast a discrete message (announce). | SEND, QUERY, REPLY, MESSAGE, FAULT, REGISTER, UNREGISTER, ASSERT_INVITATION, CANCEL_INVITATION, ASSERT_SUBSCRIPTION, CANCEL_SUBSCRIPTION PUBLISH, ANNOUNCE, MODULE_IS_DEAD | Continuum ID, Application Name, Authority Name, Unit ID, Role ID, Meta-AMS Delivery Point (MADP) Specification, Module Number, Subject ID, Delivery Specification, Service Mode, Priority, Flow Label, Context, Application Data Length, Application Data, Term, Fault Expression
Management Information Base (MIB) | stores data about devices in a common format |  | 

## Slide 5: Errors in Documents
871x3m1:
  P2-4: d) Physical Device Identifier (system-wide unique)? In Fig2-3, only Virtual Device ID and S/C Network Addr. are system-wide.
  P3-7: 3.4.4.1 should be DEVICE_FOUND.indication, not ADD_DEVICE.indication.
854x0m1：
  P3-4: 3.2.4.2 DEVICE_DISCOVERY_LOSS.indication (DDSAP, Device Address, Device Metadata (optional))