## Slide 1: Interoperable End-to-End Space Communications Architectures Using CCSDS Building Blocks
Peter Shames
Jet Propulsion Laboratory, California Institute of Technology
SpaceOps 2016, 16-20 May 2016
Daejeon, Korea
© 2016 California Institute of Technology. Government sponsorship acknowledged.

## Slide 2: Introduction – Interoperable End-To-End Space Data Systems
End-to-End space data systems are inherently systems of systems
Typically composed of:
  Spacecraft and mission operations systems (MOS) that belong to one (or more) organizations
  Multi-mission communication assets that belong to another organization.
Interoperability and cross support are essential to:
  Take advantage of expensive, shared, multi-mission assets (DSN, ESTRACK, commercial, …)
  Provide interoperability within and among spacecraft owned by different agencies (e.g. Mars and Lunar exploration)
  Move toward Solar System Internetworking (SSI)
What standard building blocks are available to build such systems?

## Slide 3: Service and Interface Interoperability Considerations
CCSDS has developed a large suite of interoperable, and cross-supportable, protocols and other standards.
Each of these defines a specific “layer” of functionality, such as: RF modulation, space link, error coding, cross support frame delivery, or network layer routing.
What had not been provided was an end-to-end view of how all of these many parts fit together to provide a solution for different missions.
Missions may be “traditional” single space link (called ABA) or may use a relay or network approach (SSI).
The Space Communication Cross Support Architecture document (CCSDS 901.1-M-1) describes best practices for service, system, and protocol building blocks based on more than 80 CCSDS standards.
16-20 May 2016

## Slide 4: Generic End-to-End Space Data System (ABA)
Space User
Node
ABA
ESLT
Earth User
Node
Terrestrial Service Provider Interface
Space-Link Service Provider Interface
Service
Management
Interface
“ABA” configuration
  Agency A develops the spacecraft (Space User Node) and the MOS (Earth User Node).
  Agency B owns/operates the ground station (Earth Space Link Terminal).
Interfaces
  Service interfaces between EUN and ESLT.
  Space Link interfaces between ESLT and SUN
Each of these system building blocks has defined interfaces and component behaviors
Each of these interfaces has an associated set of protocols and protocol behaviors
16-20 May 2016

## Slide 5: Generic End-to-End Space Internetworking Data System (SSI)
Space User
Node
SSI
ESLT
Earth User
Node
Space Link
Interfaces
Terrestrial
WANs
Space
Routing
Node
Terrestrial-Link
Interfaces
Space-Link
Interfaces
Earth
Routing
Node
Service
Management
Interface
“SSI” configuration
  Agency A develops the spacecraft (Space User Node) and the MOS (Earth User Node).
  Agency B owns/operates the Earth and Space Routing nodes.
  Agency C owns/operates the SSI capable ground station (SSI Earth Space Link Terminal).
Interfaces
  Service interfaces between ERN and ESLT.
  Space Link interfaces between ESLT to SRN and SRN to SUN.
  Space internetworking (network layer) interfaces end-to-end,
Each of these system building blocks has defined interfaces and component behaviors.
Each of these interfaces has an associated set of protocols and protocol behaviors.

## Slide 6: Overall Building Block Approach
Service Interfaces
  Describes how missions may plan, schedule, configure, use, and monitor cross supported service interfaces
Component (Physical) Building Blocks
  Shows the major physical elements that are used to compose end-to-end systems
  Describes their typical functions and interfaces
  Supports development of a coarse grained composition of the major system elements
  Shows the nature of the connections and the high level data flows
Protocol (Communications) Building Blocks
  Shows the primary protocol stack assemblies for ABA and SSI configurations
  Shows the protocol configurations as they are intended to be used
  Describes appropriate assemblies for different kinds of services: link layer, radiometric, network layer, application layer, and security
End-to-end Diagrams
  Use the component and protocol building blocks to demonstrate how to construct typical end-to-end ABA and SSI system deployments
The focus is on data transport and related communications services, all user applications, using whatever protocols, are constructed upon these services
16-20 May 2016

## Slide 7: ABA Service Interface View
ABA CSSE
EUN (e.g., User MOC)
Service
Delivery (SD)
Interfaces
SD
I/F
SM
I/F
Service
Management (SM) Interface (I/F)
Service Production
CCSDS Cross Support
Service Management
CCSDS Cross Support
Transfer Services
SD
I/F
SM
I/F
Earth User Node
(Service User)
Space User
Node
ABA ESLT
(CSSE Service Provider)
Space
Link
Service Management
Service Provision
Position & Timing
Services
Radiometric
Services
Return Data
Delivery Services
Forward Data
Delivery Services
16-20 May 2016

## Slide 8: ABA Service Interface Types
Service Management Interfaces (SM)
  Used by the EUN to plan, schedule, configure, use, and monitor cross supported service interfaces
  Defined by a related set of interfaces for exchange of requests and responses between the EUN and the ESLT
Service Delivery Interfaces (SLE & CSTS)
  Two related sets of data delivery interfaces, SLE and CSTS
  SLE includes: forward CLTU, return all frames, and return channel frames
  CSTS includes: a framework and services for radiometric data, monitor data, service control of forward frames built on that framework
16-20 May 2016

## Slide 9: SSI ERN & EUN Service Request and Delivery
SSI CSSE
CSSE (e.g., Router MOC)
Service Delivery
Interfaces
SD
I/F
Service
Management
Interface
Service Production
CCSDS Cross Support
Service Management
CCSDS Cross Support
Transfer Services
SD
I/F
SM
I/F
SSI Earth Routing Node
(CSSE Service Provider)
SSI Space
Routing Node
SSI ESLT
(CSSE Service Provider)
Space
Links
Service Management
Service Provision
Position & Timing
Services
Radiometric
Services
Return Data
Delivery Services
Forward Data
Delivery Services
SSI Space
User Node
EUN (e.g., SSI User MOC)
SSI Service
Interfaces
SSI Earth User Node
(UE Service User)
SM
I/F

## Slide 10: SIS Service Interface Types
Service Management Interfaces (SM)
  Used by the ERN to plan, schedule, configure, use, and monitor cross supported service interfaces
  In the SSI the ERN “owns” the SM interfaces to the ESLT, and the space link interfaces from ESLT to SRN
Service Delivery Interfaces (SLE, CSTS, and SSI)
  The ERN uses the data delivery interfaces, SLE and CSTS when it requires link layer access to the SRN
  At the link layer the ERN to SRN connections look like an ABA mission
  At the network layer the EUN and ERN use SSI services end-to-end to route data through the SSI ESLT and SRN, all may operate as SSI nodes
16-20 May 2016

## Slide 11: Component Building Blocks
ABA Component Building Blocks
  ABA Earth Space Link terminal
  ABA Earth User Node
  ABA Space User Node
SSI Component Building Blocks
  SSI Earth Space Link terminal
  SSI Earth Routing Node
  SSI Earth User Node
  SSI Space Routing Node
  SSI Space User Node
  Wide Area Network (WAN) Routing Node
  Planet Space Link Terminal
  Hybrid Science / Routing Node
16-20 May 2016

## Slide 12: Generic ABA Building Block and Functions
Generic ABA Node
Application 1
Application 2
Element Management
Data
Store
Data Forwarding
Link Type A
Link Type B
Link B Processing
Link A Processing
16-20 May 2016

## Slide 13: Generic ABA Building Block Notes
Not all ABA building blocks will include all functions, user building blocks are often “one-sided”
The functions for link layer processing are well specified in the relevant link layer and related standards
The data forwarding and data storage functions are defined, but typically not in a fully specified form
Some functions, like element management, will be present, but not specified and use interfaces that are not standardized
16-20 May 2016

## Slide 14: Generic SSI Building Block and Functions
Generic SSI Node
Routing
Application 1
Application 2
Element Management
Network A Processing
Network B Processing
Network Management
Data
Store
Link Type A
Link Type B
Link B Processing
Link A Processing
16-20 May 2016

## Slide 15: Generic SSI Building Block Notes
Not all SSI building blocks will include all functions, user building blocks are often “one-sided”
The link layer functions are essentially the same as for ABA configurations, with the exception of the ESLT frame creation, merging, and encoding functions
The SSI networking and routing functions are specified in the relevant SSI standards, some of which are still in development (marked as [Future] in the SCCS-ARD)
Network management functions are identified, but they are not yet in a fully specified form
Some functions, like element management and cross-domain coordination, will be present, but are presently specified only in the SSI conceptual architecture
16-20 May 2016

## Slide 16: ABA Protocol Building Blocks
Describe CCSDS ABA protocol configurations as they are intended to be used
Describe appropriate assemblies for different kinds of services: physical, link layer, radiometric, application layer, and security
Are designed to be used as the interface bindings for the different services and functions within components
The following diagrams include:
  ABA Earth user protocol stacks, forward and return (may be asymmetric)
  ABA ESLT protocol stacks
  ABA Space user protocol stacks
  Specialized “round trip” protocol stacks such as radiometric processing
  An example security protocol deployment
  Many other examples, including security, are in the SCCS-ARD
16-20 May 2016

## Slide 17: ESLT Fwd / Ret Service Provider Protocol Stack Building Blocks
SLE F-CLTU
Processing
RF & Mod
TCP
SLE RAF
Processing
TCP
Frame Sync & De-Code
CSTS F-Frame
Processing
(Frame Muxing)
TCP
Code & Sync
SLE RCF
Processing
(Frame De-Muxing)
TCP
a) SLE F-CLTU
b) SLE RAFs
c) CSTS F-Frame
(multiplex)
d) SLE RCFs
(de-multiplex)
SLE F-CLTU
CSTS F-Frame
SLE RAF
SLE RCF
Frame Sync & De-Code
IP
RF & Mod
IP
RF & De-Mod
IP
RF & De-Mod
IP
16-20 May 2016

## Slide 18: ABA Service-User CLTU & F-Frame Building Blocks
User F-CLTU Application
(CLTU Processing)
IP
Code & Sync
TC Frame
User F-Frame Application
(Frame Processing)
IP
TCP
CSTS F-Frame
a) ABA User SLE F-CLTU
b) ABA User CSTS F-Frame
TCP
SLE F-CLTU
User Application
(Packet Processing)
User Application
(Packet Processing)
AOS/TC Frame
16-20 May 2016

## Slide 19: ABA Service-User Service Management Building Blocks
ESLT Service Management Processing
(Planning & Scheduling)
IP
TCP
HTTPS
SCCS-SM
User Service Management Application
(Planning & Scheduling)
IP
TCP
HTTPS
SCCS-SM
a) ABA ESLT Service Management
b) ABA User Service Management
NDM or ODM
16-20 May 2016

## Slide 20: ESLT Radiometric Service Provider Protocol Stack Building Blocks
CSTS F-Frame
Processing
(Frame Muxing)
TCP
Code & Sync
SLE RCF
Processing
(Frame De-Muxing)
TCP
TD-CSTS Ranging & Radiometric Data
CSTS F-Frame
SLE RCF
Frame Sync & De-Code
IP
IP
TCP
TD-CSTS
IP
Ranging Sequence Recovery
Ranging Sequence Generation
RF & Mod
RF & De-Mod
Ranging Data
Doppler Data
Ranging
Signal
TD-CSTS
Processing
(Real-time Radiometric Data)
16-20 May 2016

## Slide 21: ABA Earth User Secure Forward-Frame / File Building Blocks
Earth User Secure Forward-
Frame Application
(Packet Processing)
IP
TCP
CSTS Forward-Frame
AOS/TC Frame
a) ABA Secure CSTS Forward-Frame User
SDLS Auth./Encrypt
Earth User Secure Forward-
Frame Application
(Packet Processing)
IP
TCP
CSTS Forward-Frame
AOS/TC Frame
b) ABA Secure CDFP file & CSTS Forward-Frame User
SDLS Auth./Encrypt
Encapsulation
Earth User Secure File Application
CFDP
File Validate/Decrypt
16-20 May 2016

## Slide 22: SSI Protocol Building Blocks
Describe CCSDS SSI protocol configurations as they are intended to be used
Describe appropriate assemblies for different kinds of services: network layer, application layer, using underlying link layer protocols
Are designed to be used as the interface bindings for the different SSI services and functions within components
The following diagrams include:
  SSI Earth user and relay protocol stacks, forward and return
  SSI ESLT protocol stacks
  SSI Space user and relay protocol stacks
  Many other examples, including security, are in the SCCS-ARD
16-20 May 2016

## Slide 23: SSI Earth Service User / Provider Building Blocks
CSTS F-Frame
Processing
(Frame Muxing)
RF & Mod
IP
TCP
Code & Sync
LTP
ENCAP
TC/AOS Link Framing
Bundle Agent
(Routing, Store-and-Forward Processing)
BP
BP
a) SSI Earth Bundle Routing
with Frame Multiplexing
CSTS F-Frame
User CFDP Forward-
File Application
IP
TCP
BP
CFDP
b) SSI User CFDP File Delivery
Directly over BP
16-20 May 2016

## Slide 24: SSI Space User / Service Provider Building Blocks
ENCAP
Bundle Agent
(Routing, Store-and-Forward Processing)
BP
a) SSI Space User Relay Link with Bundle Routing
Prox-1 RF & Mod
RF & De-Mod
Frame Sync & De-Code
Prox-1 Code & Sync
LTP
ENCAP
TC/AOS Link
Bundle Agent
(Routing, Store-and-Forward Processing)
BP
BP
Prox-1 Link
ENCAP
b) SSI Space Bundle Routing
Long-Haul and Proximity Links
Prox-1 RF & De-Mod
Prox-1 Sync & De-Code
Prox-1 Link
16-20 May 2016

## Slide 25: End-to-End Deployments
Both ABA and SSI examples are provided in the SCCS-ARD and the companion SCCS Architecture Description Document (911.0-G-1)
The following two examples show the Component building blocks and a typical protocol stack building block configuration
The ABA example shows a very “traditional” forward TC deployment
  Similar examples for return flows, radiometric processing, file delivery, and secured services are possible
The SSI example shows both forward command and forward file using a SSI ESLT and Earth and Space Routing Nodes
  Similar examples for return flows and secured services are possible
16-20 May 2016

## Slide 26: Basic ABA End-to-End Forward CLTU Protocols
VC X
ABA Earth-Space
Link Terminal
ABA Earth User Node
ABA Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
VC X
To VC X
ABA
ABA
ABA
RF & Mod
IP
TCP
F-CLTU
F-CLTU
Production
Space F-Frame
Application
TC
RF & Mod
C & S
User F-CLTU
Application
IP
TCP
F-CLTU
TC
C & S
C & S = Coding & Synchronization
16-20 May 2016
Notes: 26

## Slide 27: SSI End-to-End Forward: All DTN
Earth-Space
Link Terminal
Earth User Node
Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
SSI
SSI
SSI
VC Z
VC X, Y, & Z
Prox-1
UHF
C & S
ENCAP
Space File Application
BP
CFDP
RF & Mod
IP
TCP
C & S
F-Frame
Mux F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
AOS/TC
BP
To
VC Z
User File Application
IP
TCP
BP
CFDP
Space Routing Node MOC
SSI
To
VC X
To
VC Y
User File Application
IP
BP
User Pkt
Application
CMD
CFDP
EP or SP
F-Frame
TCP
Space Routing Node
SSI
UHF
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
Prox-1
RF & Mod
ENCAP
BP
LTP
VC Y
CMD
EP or SP
Space Pkt
Application
C & S
AOS/TC
VC X
Space File Application
CFDP
Proximity Space
CCSDS Protocols
AOS/TC
16-20 May 2016
Notes: 27

## Slide 28: A word about the figures
All of the figures use the viewpoints and methods documented in the Reference Architecture for Space Data Systems (RASDS, CCSDS 311.0-M-1)
These figures use simple Powerpoint drawings and agreed conventions for representing function, components, links, protocols, and other objects
These same viewpoints and the fundamentals of the methods may also be represented using SysML or similar approaches
See a related SpaceOps 2016 paper by Shames, Sarrel, and Friedenthal, 2307501, for a description of this modeling approach
16-20 May 2016

## Slide 29: End-to-End Protocol View using SysML
Shows major communications systems from the End-to-End view
  Shows End-to-End high level protocol flows
  Shows typical CCSDS Standards in relationship to major system elements
Interface Specification
  Shows only the top level ports, types, and data flows
  Does not show interface details nor protocol stacks
16-20 May 2016

## Slide 30: End-to-End Building Block Benefits
The building-block approach presented here provides the means for specifying, analyzing, and designing interoperable, cross-supportable, end-to-end space communications systems.
This approach enhances reuse, consistency, conformance to standards, and provides guidance for adopting CCSDS service, data link, and space internetworking interfaces.
Adopting standard component interfaces and services, complying to CCSDS standards, will support high levels of interoperability and cross support
Using these building blocks supports system connectivity and composition, and will enable re-use of expensive ground communications assets
These building blocks, used appropriately, will support multi-mission and multi-agency space deployments and the development of a Solar System Internet (SSI)
Not all systems deployments require all of these viewpoints
16-20 May 2016

## Slide 31: References
Space Communications Cross Support Architecture Requirements Document (SCCS-ARD, CCSDS 901.1-M-1)
Space Communications Cross Support Architecture Description Document (SCCS-ADD, CCSDS 901.0-G-1)
Reference Architecture for Space Data Systems (RASDS), CCSDS 311.0-M-1, Sept 2008
Shames, Peter M, Sarrel, Marc A, Freidenthal, Sanford A, A Representative Application of a Layered Interface Modeling Pattern, to be published 26th Annual INCOSE International Symposium (IS 2016), Edinburgh, Scotland, UK, July 18-21, 2016
Shames, Peter M, Sarrel, Marc A, A modeling pattern for layered system interfaces, 25th Annual INCOSE International Symposium (IS2015), Seattle, WA, July 13 – 16, 2015
Information technology - Open Systems, Basic Reference Model, ISO/IEC 7498-1, revised June, 1996
Systems and software engineering — Recommended practice for architectural description of software-intensive systems, ISO/IEC 42010, July 2007, revised 2011
And eighty other CCSDS standards as documented in Sec 1.7 References of CCSDS 901.1-M-1
16-20 May 2016