## Slide 1: MOIMS Protocol Viewpoint
Inputs to SEA Reference Architecture
Roger Thompson ESA

## Slide 2: RASDS Graphical Conventions
Organizational Element
Communications Protocol
Data
Store
Data Store
Color Keys:
User Node
Earth Routing Node
Space Routing Node
WAN Node
Application
Element Management
Network Management
Network Layer function
Link Layer function
Routing function
Forwarding function
Data Store
Physical Node
Physical, Logical, & Service Connectors
Physical or
Functional Connection
Logical Link
between Elements
Organizational Domain
Router
Functional Element
Link Layer User
Service Access Point
Peering
Arrangement
DATA
Service Provider
Service Consumer
As all Functions are Application Layer – overload by Functional Group

## Slide 3: Reference Diagram
MO Servce Messages may be carried in files over CFDP.
Ground-Ground may be mapped over terrestrial protocols such as 0MQ/TCP or FTP
SLE may be used to extend space link. This is transparent to application level.
Need to generate RASDS Protocol Stack representation of this.

## Slide 4: SCCS Context
Space Communications Cross Support (SCCS) Architecture
Describes Communications Architecture for two primary cases:
  ABA: a ‘single-hop’ space communications configuration that involves only a single direct to/from Earth space link. Term derives from the notion of an Agency ‘A’ using the ground station of an Agency ‘B’ to communicate between its MOC and its spacecraft, hence ABA.
  SSI: A loose confederation of independent space communications networks that all share a single Network-Layer protocol that allows them to interoperate and exchange Network-Layer PDUs, each often owned and administered by a different space agency.
I
I
User
Applications
User
Applications
SCCS
ABA/SSI

## Slide 5: SCCS Basic ABA Configuration
Space User
Node
ABA
ESLT
Earth User
Node
Terrestrial Service Provider Interface
Space-Link Service Provider Interface
Service
Management
Interface

## Slide 6: SCCS SSI Core Configuration
Space User
Node
SSI
ESLT
Earth User
Node
Space Link
Interfaces
Terrestrial
WANs
Space
Routing
Node
Terrestrial-Link
Interfaces
Space-Link
Interfaces
Earth
Routing
Node
Service
Management
Interface

## Slide 7: MOIMS Services Protocol Binding
MOIMS Concerns Application Level Services, end to end
MOIMS Standards are defined in terms of two principle information exchange paradigms:
  Message Based Interaction
  File Transfer
In terms of Communications Architecture, MOIMS Services may be deployed in 3 principle contexts:
  Across a Space Link, using CCSDS SCCS ARD compliant communications protocol stacks. It should be noted that this includes the use of Space Link Extension services, or SSI protocols deployed over terrestrial networks.
  Across a Terrestrial Network, using industry standard communications protocol stacks
  Within a Spacecraft, using CCSDS SOIS services [TBC]
Bridging between these contexts is performed at application level. Where the MO MAL is used, a generic MAL bridge can provide this as an application independent service

## Slide 8: MOIMS Comms Context: Space Link
Space
User Node
Space Link
Communications Processing
Space or Earth
User Node
MOIMS
User Application
MOIMS
User Application
Space Link
Communications Processing
MOIMS Information Exchange
MOIMS
Any SCCS Architecture
(ABA/SSI)
Space Link

## Slide 9: MOIMS Comms Context: Terrestrial Link
Earth
User Node
Terrestrial Link
Communications Processing
Earth
User Node
MOIMS
User Application
MOIMS
User Application
Terrestrial Link
Communications Processing
MOIMS Information Exchange
MOIMS
Any Terrestrial Network Architecture
Terrestrial Link

## Slide 10: MOIMS Comms Context: On-board Link
Space
User Node
SOIS
Communications Processing
MOIMS
User Application
MOIMS
User Application
SOIS
Communications Processing
MOIMS Information Exchange
MOIMS
SOIS Compatible On-board Architecture
SOIS Link

## Slide 11: MOIMS Generic Protocol Stacks
MOIMS
User Application
MO Language Binding
MALTechnology Binding
MAL
MO Service
Application Protocol
Messaging or File
Transport and Encoding
API Transform
MO Compliant Service
MOIMS File Exchange
MOIMS
User Application
MAL
MAL Encoding
File Transfer Protocol
Optional File Format Specification in terms of MAL
MOIMS File Format
Transport Protocol
Network
Transport/Network Layer
Link Layer
Transport Protocol
Network
Blue layers correspond to Internet/DOD 4 Layer model :
  Application Layer (e.g. FTP or ZeroMQ)
  Transport and Network Layers combined (e.g. TCP/IP or UDP/IP)
  Physical Link Layer or “Network” (e.g. WAN, LAN or WLAN)
Protocol stacks must match between communicating User Applications
MO Language Binding can differ between communicating User Applications
For File Exchange, the transfer must be independently initiated at Communications Protocol level, either directly by the User Application or by a 3rd party.

## Slide 12: MOIMS Over Space Link
MOIMS
User Application
MO Language Binding
MAL SPP
MAL
MO Service
CCSDS Space Packet
Communications Processing
MAL CFDP
CFDP
MO Compliant Service over Space Packet and/or CFDP
Entire Service or Single Message
MOIMS File Exchange
MOIMS
User Application
Communications Processing
CFDP
MOIMS File Format
CCSDS Space Packet
Any SCCS Architecture
(ABA/SSI)
Any SCCS Architecture
(ABA/SSI)
Bidirectional:
TM and TC Packets

## Slide 13: MOIMS Over Space Link (ABA Deployment Example)
Space User Node
MOIMS
User Application
MO Language Binding
MAL SPP
MAL
MO Service
CCSDS Space Packet
MAL CFDP
CFDP
Earth User Node
Coding & Synch
Space Data Link
RF Link
ESLT (Ground Stn)
RF Link
C&S
TCP/IP
Network
CCSDS CSTS/SLE
TCP/IP
Network
Space Data Link
CCSDS CSTS/SLE
MOIMS
User Application
MO Language Binding
MAL SPP
MAL
MO Service
CCSDS Space Packet
MAL CFDP
CFDP
MOIMS
Multiple service options, eg. R-AF + F-CLTU

## Slide 14: MOIMS Over Terrestrial Link
MOIMS
User Application
MO Language Binding
MAL
MO Service
MO Compliant Service over ZeroMQ and/or FTP
MOIMS File Exchange
MOIMS
User Application
FTP
MOIMS File Format
TCP/IP
Network
MAL 0MQ
TCP/IP
MAL FTP
FTP
0MQ
Network
Note that 0MQ and FTP are example protocols – others may be used if MAL binding exists
MO Language Binding can differ between communicating User Applications
For File Exchange, the transfer must be independently initiated at Communications Protocol level, either directly by the User Application or by a 3rd party.

## Slide 15: MOIMS Over Terrestrial Link (Deployment Example)
Earth User Node
MOIMS
User Application (Provider)
MO Language Binding
MAL
MO Service
Earth User Node
MOIMS
User Application
(Consumer)
MO Language Binding
MAL
MO Service
MOIMS
MAL FTP
TCP/IP
MAL 0MQ
0MQ
FTP
Network
TCP/IP
MAL FTP
FTP
0MQ
Network
WAN, LAN or WLAN

## Slide 16: MAL Bridging
MAL Bridge
User Node
MOIMS
User Application (Provider)
MO Language Binding
MAL
MO Service
User Node
MOIMS
User Application
(Consumer)
MO Language Binding
MAL
MO Service
MOIMS
MAL MTA
Transport A
Messaging Tech A
Network A
MAL MTB
Transport B
Messaging Tech B
Network B
MAL
MAL MTA
MAL MTB
Trans A
MTA
Net A
MTB
Trans B
Net B
MAL Bridge supports two technology bindings and translates between them
Example above is for two Messaging Technologies (A and B)
All MO Services defined in terms of MAL can be transferred across the same generic MAL Bridge
Can be used to link different Communications contexts (Space-Ground or Ground-Ground)