## Slide 1: Cross Support and Mission Operations Services & Interfaces
Peter Shames & Erik Barkley
13 October 2014
Updated 10 Nov 2014

## Slide 2: CCSDS CSS & SM&C
CCSDS has two sets of “services & interfaces” that have been identified as having a possible overlap:
  Cross Support Services (CSS: SLE, CSTS, SM)
  Spacecraft Monitor and Control (SM&C: mission operations).
The CSS services are specifically designed for interoperable space link cross support, they are quite mature and the SLE services have been in use for years, implemented by many agencies.
The SM&C services are designed in a general fashion for mission operations. Parts of them have been prototyped over the years, using bi-lateral ICDs, but they do not yet have an interoperable set of specifications and they do not have any application layer services comparable to SLE or SM.
SM&C cannot now directly replace SLE and SM and asking that SLE, CSTS, and SM stop work, and change to this new, not yet mature, framework is problematic for several reasons.
This analysis explores this in more detail.

## Slide 3: Partial Standards Relationship Sketch (CCS Area Point of View – an example)
Specify links to Communicate with
Specify control of on-board activities of
Space Link &
Cross Support
Mission
Operations

## Slide 4: Relationship of SM&C MO to other CCSDS Standards (from CCSDS 520.0-G-3)

## Slide 5: SCCS-ADD Figure 5‑1: Generic ABA Building Block and Functions
Each generic Link-Layer ABA node type contains these functions, Mission Operations functions are inside the pink function ovals.
Generic ABA Node
Application 1
Application 2
Element Management
Data
Store
Data Forwarding
Link Type A
Link Type B
Link B Processing
Link A Processing
Mission
Operations
Space Link &
Cross Support
Notes: 12/12: We reference “Node” in the figure, but the caption/figure title reflects “Building Block”—are we using the terms interchangeably? They should probably at least match between figure and figure title.

## Slide 6: SCCS-ADD Figure 2-2: Basic ABA Configuration
Space User
Node
ABA
ESLT
Earth User
Node
Terrestrial Service Provider Interface
Space-Link Service Provider Interface
Service
Management
Interface
Mission Operations terrestrial services are inside this element
CSS SM & SLE services are inside this element
NOTE: All figures are either directly borrowed from the SCCS-ADD (CCSDS 9021.0-G-1) or are annotated or expanded versions of those figures, as noted
Notes: I changed the lines here from dashed to solid.
7/25: Changed to ESLT now that the term is defined before this graphic.
Note that Earth-Space Link Terminals, while shown here, isn’t mentioned in the document until section 3. In part, that’s why I’ve not adjusted the term to show as “ESLT”.

## Slide 7: CSS Service and Interfaces
Service Management (SM)
  Service Management spec (CCSDS 910.11-B-1)
  Future Extensible Cross Support Service Management spec (CCSDS 902.0-G)
Service Delivery (SD)
  Forward CLTU (CCSDS 912.1-B-3)
  Return (All / Channel) Frames (CCSDS 911.1-B-3 & 911.2-B-2)
  CSTS Framework (CCSDS 921.1-R )
  Monitor Data (CCSDS 922.1-R)
  Radiometric (CCSDS 922.2-R)
  Future Generic File Transfer, Service Control, F-Frame specs

## Slide 8: SCCS-ADD Figure 4‑1: ABA Service View
ABA CSSE
UE (e.g., User MOC)
Service
Delivery (SD)
Interfaces
SD
I/F
SM
I/F
Service
Management (SM) Interface (I/F)
Service Production
CCSDS Cross Support
Service Management
CCSDS Cross Support
Transfer Services
SD
I/F
SM
I/F
Earth User Node
(UE Service User)
Space User
Node
ABA ESLT
(CSSE Service Provider)
Space
Link
Service Management
Service Provision
Position & Timing
Services
Radiometric
Services
Return Data
Delivery Services
Forward Data
Delivery Services
Notes: 12/2012: Removed “(e.g. Network)” from ABA CSSE box per John Pietras/Peter Shames direction (via e-mail).
Unclear why some items are italicized. Suggest removing italics.
Changed to solid lines

## Slide 9: SLE & CSTS use of ASN.1
SLE and CSTS services, PDUs, and data objects are all defined using ASN.1. Each document contains the complete, directly implementable, specification.
Abstract Syntax Notation (ASN.1) is an ISO spec (Information Technology—Abstract Syntax Notation One (ASN.1): Specification of Basic Notation. International Standard, ISO/IEC 8824-1:2008. 4th ed. Geneva: ISO, 2008.)
ASN.1 can describe, in unambiguous terms, specifications for data, structures, syntax, interfaces, and protocol data units
ASN.1 may be directly compiled into executable code using one of several COTS compilers
There are several different, specified, “on-the-wire” bindings from ASN.1 to bit-level data transfer syntax, see Information technology — ASN.1 encoding rules: Specification of Basic Encoding Rules (BER), Canonical Encoding Rules (CER) and Distinguished Encoding Rules (DER), ISO/IEC 8825-1:2008 and also packed and XML encoding rules
Both ESA and JPL have used ASN.1 compiled code to directly create interoperable, validated, service implementations, as have X.400, X.500, LDAP, SNMP & UMTS.

## Slide 10: Cross Support / Mission Operations Interactions using Standard SLE / SM Services
ABA
ESLT
Earth User
Node
User Service Management Application
(Planning & Scheduling)
User Application
(Packet Processing)
User RCF Application
(Frame Processing)
User Radiometric
Data Processing
User Service Monitor Data Processing
User F-CLTU Application
(CLTU Processing)
Service
Delivery (SD)
Interfaces
Service
Management (SM) Interface (I/F)
Flight
Dynamics
Planning
Schedule
Execution
Monitor &
Control
SM over HTTP
F-CLTU over TCP
R-CF over TCP
MD-CSTS over TCP
TD-CSTS over TCP
SLE F-CLTU
Processing
SLE RCF
Processing
(Frame De-Muxing)
TD-CSTS
Processing
(Real-time Radiometric Data)
Service Management Processing
(Monitor Data)
Service Management Processing
(Scheduling)
SM&C MO Applications
(MAL Compliant)
MAL & Transport Adapter for SPP
Notes: I changed the lines here from dashed to solid.
7/25: Changed to ESLT now that the term is defined before this graphic.
Note that Earth-Space Link Terminals, while shown here, isn’t mentioned in the document until section 3. In part, that’s why I’ve not adjusted the term to show as “ESLT”.

## Slide 11: Cross Support / Mission Operations Interactions using Merri’s MAL Service recommendation dated 10 Nov 14
ABA
ESLT
Earth User
Node
User Service Management Application
(Planning & Scheduling)
User Application
(Packet Processing)
User RCF Application
(Frame Processing)
User Radiometric
Data Processing
User Service Monitor Data Processing
User F-CLTU Application
(CLTU Processing)
Service
Delivery (SD)
Interfaces
Service
Management (SM) Interface (I/F)
Flight
Dynamics
Planning
Schedule
Execution
Monitor &
Control
SM over HTTP
F-CLTU over TCP
R-CF over TCP
MD-CSTS over TCP
TD-CSTS over TCP
SLE F-CLTU
Processing
SLE RCF
Processing
(Frame De-Muxing)
TD-CSTS
Processing
(Real-time Radiometric Data)
Service Management Processing
(Monitor Data)
Service Management Processing
(Scheduling)
SM&C MO Applications
(MAL Compliant)
MAL & Transport Adapter for SPP
MAL & Transport Adapter for SM over ???
Network Planning & SchedulingApplications
(MAL Compliant)
Notes: I changed the lines here from dashed to solid.
7/25: Changed to ESLT now that the term is defined before this graphic.
Note that Earth-Space Link Terminals, while shown here, isn’t mentioned in the document until section 3. In part, that’s why I’ve not adjusted the term to show as “ESLT”.

## Slide 12: CSS and MO Interface Alignment
MO Services are uniformly defined to use the MAL as a common data messaging layer.
MAL must be mapped “into a specific and unambiguous encoding of the messages and to a defined and unambiguous mapping to a specific data transport” using a MAL technology mapping and transport adapter.
The key technology mapping relevant for space links is the MAL to SPP adapter.
The standard, interoperable, cross-supported, means for transporting SPP over CCSDS space links is to insert SPP formatted data into TC, TM, or AOS frames and to use the SLE (F-CLTU, RAF, RCF) services to transfer them from a MOC to an ESLT.
The standard, interoperable, cross-supported, means for planning, scheduling, configuring and monitoring CCSDS space link services in an ESLT is to use CCSDS SM (& CSSM)
Other space link related data types (monitor, radiometric, and future service control) have CSTS cross-support service interfaces in process. The CSTS framework is mature.
SM&C may embed CSS service user interfaces within the relevant MO functions, or it may develop interface adapters that conform to CSS service user interfaces on one side and MO/MAL interfaces on the other.
Either approach is completely compliant with CCSDS cross support and interoperability standards and interfaces and provides a straightforward means of interfacing the whole SM&C suite to any agency’s space link services.

## Slide 13
CESG / SEA Materials – 30 Sep 2009

## Slide 14: SMC& Recommendations – Re-visited
The recommendations from CESG Sept 2009 on the relationship of SM&C to the rest of CCSDS are still entirely relevant today.
SM&C MO Services should identify how they will integrate with the existing and planned SLE, CSTS, and CSSM services.
There is no direct benefit to the cross support service providers nor to their users in forcing them to implement the SLE, CSTS, SM suite and also the SM&C, MAL, etc stack and some yet-to-be-defined “SM&C MO compliant” monitor, tracking, and control services.

## Slide 15: Partial Standards Relationship Sketch (SIS Area Point of View – an example)
Specify network & links to Communicate with
Specify control of on-board activities of
Space Link, Network &
Cross Support
Mission
Operations
Network layer services
Network layer Management services
Specify use of space internetworking
Network layer services

## Slide 16: Some Thoughts on SIS and SM&C
SIS needs to develop network management protocols, including monitoring and management of DTN bundle nodes and updates of DTN routes. These are analogous to Internet Standards for SNMP & BGP.
SM&C has some nominal features such as a message abstract layer (MAL) and M&C services (speculative) that could potentially be used to implement SIS NM functions.
However, SIS will need to define the specific DTN M&C services and routing update services, these do not exist in SM&C or in DTN today in any formal specs.
Using SM&C these could be application protocols layered on MAL and using the COM, with some to-be-defined behavior, but they would also require a concrete mapping to some on-the-wire protocol that has suitable addressing and forwarding, such as AMS, and some on-the-wire message content structures.
Creating a specification of a simple DTN M&C protocol directly over BP (much like BGP over TCP in RFC 4271 or SNMP in RFC 3411/3413) would be straight-forward, efficient, and not force a reliance on any other secondary machinery.
  SNMP may be far too “heavy-weight” for our purposes, but separation of concerns between user applications and service provider / service & network management is still important
SIS could directly adopt AMS over DTN if a messaging protocol is really required, but it is not clear that is necessary.
Developing a SIS DTN M&C service using SM&C brings no obvious benefit, adds overhead and coupling where it need not exist, and convolves user application and network/link service management that should remain separate.

## Slide 17: Summary
SM&C Has yet to develop even a fully interoperable messaging framework, let alone application level standards comparable to SLE, CSTS and SM.
CSS / SLE standards already provide a mature, deployed, set of interoperable cross support service interfaces.
CSS/ CSTS is maturing as an interoperable cross support framework for new services: monitor data (MD), tracking data (TD), service control (SC) and forward frame.
CSS / Cross Support Service Management (CSSM) provides an interoperable framework for planning, scheduling, configuring, monitoring and reporting on cross support services.
A service interface and protocol binding for CSSM is needed, but NASA has already adopted a simple HTTP/REST mapping for SCaN.
SCaN has specified these existing and new services in the SCaN Level 2 SRD and SNIP is defining the plan for rolling these out in all three networks, DSN, SN, and NEN.

## Slide 18: BACKUP SLIDES
Service provider protocol stacks from SCCS-ARD
Service user protocol stacks from SCCS-ARD

## Slide 19: High Level Comparison of Cross Support and Mission Operations “Framework” Features
Cross Support
  Focus specifically on space communications cross support for service planning, request, forward / return data delivery and accounting
  Provides direct support for all space link service features
  Concrete specs for SLE/CSTS service interfaces, defined SM messages, interaction patterns, and services, and data transfer services and behavior, including normative XML and ASN.1 bindings
  Rely upon underlying data transport layers, SMTP & HTTP, TCP/IP are being used
  There is a formal data transport binding for SLE / CSTS to TCP/IP
Mission Operations
  Abstract set of services for common mission operations functions, largely terrestrial, but proposed for space
  Specifies an abstract message layer and common object model that may be generally applied in mission operations context
  Does not (yet) include either a concrete message spec, data representation binding, nor a data transport binding, these all must be specified separately
  Require use of space links and cross support services to plan for comm services, transmit commands and data, and receive telemetry, science, radiometric and accounting data

## Slide 20: MOIMS SM&C Standards (core only)
Message Abstraction Layer (MAL, CCSDS 521.0-B-2)
  Abstract interfaces, services, and message types
  Transactions and state transitions
  Abstract message composition
  Message interaction patterns
  Abstract access interface and transport layer interface
  Require a “transport mapping from the abstract MAL data structures into a specific and unambiguous encoding of the messages and to a defined and unambiguous mapping to a specific data transport ”
  XML schema may be used as the “message body type”
Common Object Model (COM, CCSDS 521.1-B-1)
  Abstract common object model (used in MAL) and abstract common services
  Objects have domain, types, relationships, unique identifiers and instances
  Services are event (publish), archive (CRUD), and activity tracking (progress signals)
  Activity / event chaining is described
  COM messages are described in terms of the MAL, and MAL fields are described in the COM
  There is a “normative” XML schema in SANA, but it is in the wrong place and ambiguous
Common Services (CCSDS 522.1-R-2)
  Defined in this draft Blue Book
  Services are: Directory, Login, Service Configuration, Interaction, and Replay
  Abstract services that use MAL messages and COM objects
  There is not yet even a reference XML set of service specifications
Service Management Application
  There is no service management application defined in the MORM (CCSDS 520.1-M-1)
  It might be part of the Planning function as referenced in the MO Service GB (CCSDS 520.0-G-3), but this is not clear and that is a Green Book
Transport Layer
  The only concrete transport layer spec at this point is a draft Red Book (CCSDS 524.1-R-0.1) for the Space Packet Protocol (SPP)
  This provides a concrete binding from the MAL abstractions to the SPP packet structures, this requires a further mapping onto CCSDS space links or some other underlying transport or link protocol

## Slide 21: The Nominal MO / MAL / SPP Mapping (From CCSDS 524.1-R-0.1 )
Produces / consumes SPP packets, requires a transport protocol

## Slide 22: SM&C use of the MAL
The MAL defines abstract interfaces, services, and message types; transactions and associated state transitions; abstract data types & message structures; and message interaction patterns. These are defined abstractly in a tabular form.
The COM defines a common object model (used in MAL) and a few abstract common services. Objects have domain, types, relationships, unique identifiers and instances. The common services are event (publish), archive (CRUD), and activity tracking (progress signals). COM service messages are described in terms of the MAL, and MAL fields are described in the COM.
In order to create an interoperable service a separate “technology mapping” must be defined. The technology mapping translates these abstract messages and data objects into concrete message transfers with an “on-the-wire” bit representation.
The technology mappings must translate the concrete MAL service and message model into a specific protocol tied to specific protocol data units (PDU). The technology mapping recommendation casts the MAL abstract data types and messages into specific bit representations appropriate to that protocol.
There are is only one draft technology mapping that is available and that is to SPP. SPP is a simple data structure suitable for use within a transport or link protocol such as TC or TCP/IP, but there is no spec for this binding.
There are not yet any application services, such as R-AF or SM service request handling, built using the MAL, that could directly substitute for the existing SLE and SM services. The services defined in the COM are defined in abstract terms in just a few pages, behavioral specifications are scant.
There is an XML schema for the MAL, but there is no directly transformable specification for SM&C services as there is for SLE; any service must be programmed by hand based on these three documents.

## Slide 23: Feedback from Merri on CSS Standards
The CSTS specification framework, is envisaged as a generic service specification framework for specification of services in a communication technology (protocol and encoding) agnostic manner. (Not accurate, CSTS has a specific interoperable binding)
The CCSDS MO Framework, has the same objective. Hence it seems there is a conceptual overlap between these two generic CCSDS service frameworks. (Conceptual is the key)
Looking into the concrete envisaged CSTS services such as the Monitoring Data Cross Support Transfer service (currently available as Draft) makes this overlap more evident as it compares very much to CCSDS MO M&C service specifications (Parameter and Aggregation Services). (These services are weakly specified in SM&C).
It is therefore recommended to clarify the relation between the two service frameworks at conceptual level and the relation between the envisaged concrete CSTS services to MO M&C services. (This is already stated, see pgs 3 & 4, including an SM&C relationship chart)
Other materials stated this:
  … this shows that the interfaces for Transfer Services and MD-CSTS are completely different and there is little justification to keep them with the Transfer Services. The same holds true for TD-CSTS.
  Clearly, CCSDS could have specific service definitions for MD and TD, but this will be largely inelegant and not a well engineered solution.
  CCSDS has been on a path to define the CSTS framework, and several services built upon it, for a few years now. The FW spec is mature and MD and TD drafts exist and are out for agency review.
  CCSDS needs the FW spec for these services, for SC, and for Forward frame (and RUFT if desired). Agencies therefor must implement the CSTS FW if they want to be compliant. SMC& cannot do all these jobs. So requiring SM&C is an added burden on the users over and above the CSTS.

## Slide 24: General Recommendations to SM&C
Adopt existing interoperable CCSDS standards, services, and protocols wherever they exist, are in development, or are planned.
  See following page for specific recommendations
  Adoption means to clearly define the relationship between SM&C and existing or planned specifications, such that use of and dependencies on these services and protocols is clearly identified in the SM&C concepts, and in subsequent specs
  Note: adoption may be done by direct integration of these other interfaces and protocols or accomplished by use of proxies at the boundary of SM&C functionality
Work actively to harmonize MOIMS SM&C with other Area and WG activities (CSS, SOIS, SIS, SEA) where overlaps exist
  Harmonize means to bring two different things that already exist into alignment as a negotiation, appropriate when when one or both parties already have solid positions nailed down
Collaborate actively with other WGs to define agreed requirements and to ensure that maturing standards meet agreed requirements
  Collaborate implies some joint work on the parts of both WGs to clarify what was ill specified or unexplored territory, appropriate when all positions are still relatively flexible
Ensure that the SM&C standards have adequately defined interoperability protocols and cross support interfaces

## Slide 25: Pietras’ SM&C and CSS diagram 8 March 2007 Telecon Notes
Onboard Software Management
Onboard Data Product Management
Onboard
M&C
Onboard
Schedule
Execution
Complex
Management
(CM) (CS)
SL Comm & Transfer Services
Time & Location (MO) / Radiometric (CS) & Transfer Services
Flight Dynamics
Planning (MO) / UM (CS)
Schedule Execution
M&C (MO) / UM (CS)
Software Management
Payload Software Management
Data Product Management
Payload
M&C
Payload
Planning
Space Element (CS) /
Flight Segment (spacecraft) (MO)
Ground Element (CS) /
Ground Segment (MO)
Mission Data Operations System (CS)
Payload Operations Centre (MO)
Mission Control Centre (MO)
SLE Complex (MO) /
Ground Station (MO)

## Slide 26: Figure 6-1: ESLT Fwd / Ret Service Provider Protocol Stack Building Blocks
SLE F-CLTU
Processing
RF & Mod
TCP
SLE RAF
Processing
TCP
Frame Sync & De-Code
CSTS F-Frame
Processing
(Frame Muxing)
TCP
Code & Sync
SLE RCF
Processing
(Frame De-Muxing)
TCP
a) SLE F-CLTU
b) SLE RAFs
c) CSTS F-Frame
(multiplex)
d) SLE RCFs
(de-multiplex)
SLE F-CLTU
CSTS F-Frame
SLE RAF
SLE RCF
Frame Sync & De-Code
IP
RF & Mod
IP
RF & De-Mod
IP
RF & De-Mod
IP
Notes: 03 Jan 14 Changed back to Processing for all “function ovals”
11/28/12: Changed only the SLE F-CLTU Production and SLE RAF Production to read “Provision” instead of “Production” per Peter’s 11/25/12 e-mail.

## Slide 27: Figure 6-3: ABA Service-User Service Management Building Blocks
ESLT Service Management Processing
(Planning & Scheduling)
IP
TCP
HTTPS
SCCS-SM
User Service Management Application
(Planning & Scheduling)
IP
TCP
HTTPS
SCCS-SM
a) ABA ESLT Service Management
b) ABA User Service Management
NDM or ODM
Notes: 7/12: Made minor alignment adjustments.//cys

## Slide 28: Figure 6-8: Service User / Provider ABA CSTS Forward-File Building Block
CSTS F-Frame
Delivery Service
(Frame Muxing)
RF & Mod
IP
TCP
Code & Sync
Encapsulation
TC/AOS Link Framing
CSTS Forward-
File Processing
CFDP
a) ABA CSTS Forward-File Service Provider
Using CFDP File Delivery over SPP and CSTS F-Frame
CSTS F-Frame
User CSTS Forward-
File Application
IP
TCP
CSTS Transfer File
b) ABA User CSTS Forward-File
(Requires CSTS Transfer-File in Service Provider)
CSTS Transfer File

## Slide 29: Figure 6-10: ABA Service-User CLTU & F-Frame Building Blocks
User F-CLTU Application
(CLTU Processing)
IP
Code & Sync
TC Frame
User F-Frame Application
(Frame Processing)
IP
TCP
CSTS F-Frame
a) ABA User SLE F-CLTU
b) ABA User CSTS F-Frame
TCP
SLE F-CLTU
User Application
(Packet Processing)
User Application
(Packet Processing)
AOS/TC Frame
Notes: 7/12: Made minor alignment adjustments.//cys

## Slide 30: Figure 6-11: ABA Service-User Protocol Return-Frame & CFDP Building Block
b) ABA User CFDP File Return
over SPP and SLE RCF
User RCF Application
(Frame Processing)
IP
AOS/TM Frame
User RCF Application
(Frame Processing)
IP
TCP
SLE RAF or RCF
a) ABA User Return SLE RAF / RCF
TCP
SLE RAF or RCF
User Application
(Packet Processing)
AOS/TM Frame
User CFDP Return-
File Application
Encapsulation
CFDP
Notes: 7/12: Made minor spacing adjustments.//cys

## Slide 31: Figure 6-12: ABA Service User Radiometric / Monitor & Service Data Protocol Stack Building Blocks
a) User Radiometric Data Processing
User Radiometric
Data Processing
TCP
TD-CSTS
IP
User Service Control Data Processing
TCP
SC-CSTS
IP
User Service Monitor Data Processing
TCP
MD-CSTS
IP
b) User Monitor Data Processing
c) User Service Control Data Processing
Notes: 03 Jan 14 Changed back to Processing for all “function ovals”
11/28/12: Changed only the SLE F-CLTU Production and SLE RAF Production to read “Provision” instead of “Production” per Peter’s 11/25/12 e-mail.

## Slide 32: Cross Support / Mission Operations Interactions using SPP Mapping
ABA
ESLT
Earth User
Node
User Service Management Application
(Planning & Scheduling)
User CSTS Forward-
File Application
User Application
(Packet Processing)
User RCF Application
(Frame Processing)
User Radiometric
Data Processing
User Service Monitor Data Processing
User F-CLTU Application
(CLTU Processing)
Service
Delivery (SD)
Interfaces
Service
Management (SM) Interface (I/F)
Flight
Dynamics
Planning
Schedule
Execution
Monitor &
Control
MAL & Transport Adapter for SPP
SM over HTTP
F-CLTU over TCP
R-CF over TCP
MD-CSTS over TCP
TD-CSTS over TCP
SM&C MO Applications
(MAL Compliant)
Notes: I changed the lines here from dashed to solid.
7/25: Changed to ESLT now that the term is defined before this graphic.
Note that Earth-Space Link Terminals, while shown here, isn’t mentioned in the document until section 3. In part, that’s why I’ve not adjusted the term to show as “ESLT”.

## Slide 33: Specific Recommendations to SM&C From CESG Meeting, Sept 2009
CSS
  Adopt SM WG, SM & request specifications
  Harmonize SM WG and SM&C interaction patterns
  Adopt CSTS WG, Cross Support transfer service interfaces
    Adopt CSTS WG, Radiometric data transfer (using Nav TDM), Monitor Data
    Collaborate with CSTS WG, Proposed service control and file data cross support
  Collaborate with CSA WG, Cross Support Service Architecture
  Collaborate with CSA WG, Service agreements and catalogs
SIS
  Adopt CFDP WG, file transfer standard for space file transfers
  Adopt AMS WG, message transfer standard for space message transfer
  Adopt DTN WG, space internetworking standards
  Collaborate with Time Correlation BoF on protocol standards
SOIS
  Collaborate with App WG, message transfer standards (coordinated with AMS already, use AMS for space / ground xfers)
  Collaborate with Subnet WG on Time and File services
SEA
  Adopt Sec WG, Security Algorithms
  Adopt IA WG, Reference Architecture for Space Information Management
  Collaborate with SANA WG, Standard registries for CCSDS information (& services)
  Collaborate with Registries / Repositories SIG (SEA IA WG & MOIMS IPR WG)
    Emerging interoperable specs for registries & repositories and SOA framework