## Slide 1: Common Mission Operations
Given a goal to enable common ground systems to perform mission operations across spacecraft
And spacecraft subsystem commands and telemetry are contained in CCSDS space packets
And Space packets are transported over several protocols with very different interaction patterns and timings
  CCSDS AOS, COP-1, DTN, as files over CFDP
And Onboard application software must be targeted to the software and avionics architecture
  Software framework, operating system, language (C, C++ …), real-time environment (threads, process, I/O), distributed across processors and/or partitions
  Avionics architectures evolve (Software interfaces can remain )
    Processors improve, multicore, distribution, Integrated Modular Avionics concepts…
    Cubesats are very different than a deep space or human rated vehicle

## Slide 2: Moving MO Onboard (?)
High frequency control loops need to be implemented onboard
Consequently MOIMS has always foreseen implementing services onboard as shown in the following chart 3

## Slide 3: Mission Operations View of Spacecraft
Ground Segment
Space Segment
MCS
TM/TC Device
OBC
MO Applications
Space Data Link
Protocols
Space Data Link
Protocols
Spacecraft Transfer Layer
Subnetwork
Packet
Service
Subnetwork
Packet
Service
CCSDS Packet Router
Subnetwork
Memory Access
Service
Subnetwork
Synchronisation
Service
Subnetwork
Device Discovery
Service
Subnetwork
Test
Service
Space
Network
Protocols
(e.g. Space
Packet)
Space Network
Protocols
(e.g. Space
Packet)
Message Layer
MO Applications
Space Link
Onboard Subnetwork
CCSDS Packets
MO Messages
Thermal
Power
Mode mgmt
FDIR
AOCS
MTL Services
OBT Mgmt
Context mgmt
SSMM mgmt
TM TC
Message Abstraction Layer
MO Applications
Standard MO
Services
Mission MO
Services
SOIS
Message
Transfer
Service
File and
Packet Store
Services
Command
and Data
Acquisition
Services
Time Access
Service
Device
Enumeration
Service
…
TM TC
…
Power
Chart borrowed from Sam Cooper (SciSys), Mario Merri (ESA) presentation

## Slide 4: Proposed CCSDS Layered Reference Model

## Slide 5: SVF Development Example of Proposed CCSDS Layered Reference Model
Parts of SVF code automatically
generated from datasheet by a
code generator based on SECT.

## Slide 6: Moving MO Interfaces Onboard (?)
An alternative is to use the existing flight software and their respective scripting or procedural functions:
  ESA/PUS uses OBCP,
  NASA uses JAVA script, LUA, Store Command Procedure
  CAST uses Store Command Procedure
These could be used by translating interaction patterns from MO to the specific scripting language used and uploading them
MO is common but the software and avionics architectures need not be

## Slide 7: Common MO interfaces Instantiated Onboard
Ground Segment
MCS
TM/TC Device
MO Applications
Space Data Link
Protocols
Space Data Link
Protocols
Subnetwork
Packet
Service
CCSDS Packet Router
Space Network
Protocols
(e.g. Space
Packet)
Space Link
Message Abstraction Layer
…
TM TC
…
Power
SOIS EDS
XML File(s)
MO interface definitions
Code
Generation tools
Spacecraft
Profile/configuration
Thermal
Power
Mode mgmt
FDIR
AOCS
MTL Services
OBT Mgmt
Context mgmt
SSMM mgmt
TM TC
Message
Service
Avionics and Software
Architecture is independent
of MO architecture
PUS,
cFS,
CAST,
…
File and
Packet Store
Services
Command
and Data
Acquisition
Services
Device
Enumeration
Service
Space
Packet
Scripting/
OBCP
MAL
XML File(s)
MAL
translation tools

## Slide 8: Common MO messages Transformed at the Operations Center
Thermal
Power
Mode mgmt
FDIR
AOCS
MTL Services
OBT Mgmt
Context mgmt
SSMM mgmt
TM TC
Ground Segment
MCS
TM/TC Device
MO Applications
Space Data Link
Protocols
Space Data Link
Protocols
Subnetwork
Packet
Service
CCSDS Packet Router
Space Network
Protocols
(e.g. Space
Packet)
Space Link
Message Abstraction Layer
…
TM TC
…
Power
SOIS EDS
XML File(s)
Onboard interface definitions
Message
Service
Spacecraft Configuration
Mission database (XTCE)
Translator/
Formatter
Code
Generation tools
Avionics and Software
Architecture Independent
PUS,
cFS,
CAST,
…
File and
Packet Store
Services
Command
and Data
Acquisition
Services
Device
Enumeration
Service
Space
Packet
Scripting/
OBCP
Avionics and Software Architecture is independent of MO and SOIS architecture

## Slide 9
Backup

## Slide 10: What is SEDS?
SEDS is: …
  SOIS Electronic Data Sheet
  An XML Schema
  Based on the XTCE schema types – but extended and refactored to be more domain specific
    That domain being flight software and devices attached through a subnetwork
  A “FSW meta language” by which a tool will read SEDs XML files and autogenerate portions of the onboard flight software

## Slide 11: Mission Use of SOIS
Current use of SEDS for software components is limited to command and telemetry interfaces over a message service
Device SEDS describes interface to flight software from a subnetworked connected device

## Slide 12: Current SOIS Focus: Definition and Use of EDS

## Slide 13: ARINC 653 System Architecture
Applications are partitioned into separate hardware protected memory
Applications are on fixed schedules with a fixed time allocation
Misbehaving applications cannot affect other applications
Can mix critical and non-critical applications an the same processor
System designers allocate processor MIPS, memory, and I/O to each application partition: