## Slide 1: MOIMS/SOIS Interactions, Case 0, no MO
TM/TC Device, On Board
Mission operations (little ”mo”) software communicates with the device handler across the space link using some SPP (or other) binding.
All S/C functions on-board are typically implemented in an R/T OS and in compliance with Class A/B processes
SOIS device handler is shown here accessed using DACP and DSAP, which provide access to the Device for the Device Handler which accepts SPP.
The Device Handler may be a product of the EDS/DoT tool chain, which makes SOIS device service accessible via Native SPP and space link from ground.
SOIS Packet Service routes packets to/from subnet using convergence layer
Convergence functions match device manufacturer’s functions, if any, or are 1-sided, or are absent.
Space Packet Forwarding in TM/TC Device complies with CCSDS SPP standard and SOIS Subnet Convergence layer.
Ground
Real-Time Computer
Space Link Physical
Subnetwork Link
Subnetwork Physical
Subnetwork Link
mo Applications
Device
Device Logic
Subnetwork Link
Packetizer
Space Packet Forwarding
Spacecraft
TM/TC SCC
TM/TC SCC
AOS
AOS
CCSDS SPP
Convergence
Convergence
Convergence
SOIS Packet
Device Handler
Device DACP
Device DSAP
TMTC DACP
TMTC DSAP
Convergence
CCSDS SPP
R/T OS
“Device Service”

## Slide 2: MOIMS/SOIS Interactions, Case 1
TM/TC Device, On Board
All S/C functions on-board are typically implemented in an R/T OS and in compliance with Class A/B processes
No MO functions on-board
A “Device Service” communicates with the device handler across the space link using an MO to Native SPP binding.
SOIS device service is shown here using DACP and DSAP, which provide access to the devices for MO services.
The Device Handler may be a product of the EDS/DoT tool chain, which makes SOIS device service accessible via Native SPP and space link from ground.
SOIS Packet Service routes packets to/from subnet using convergence layer
Convergence functions match device manufacturer’s functions, if any, or are 1-sided, or are absent.
Space Packet Forwarding in TM/TC Device complies with CCSDS SPP standard and SOIS Subnet Convergence layer.
Ground
Real-Time Computer
Space Link Physical
Subnetwork Link
Subnetwork Physical
Subnetwork Link
MAL
“Device Service”
MO Applications
Device
Device Logic
Subnetwork Link
Packetizer
Space Packet Forwarding
Spacecraft
TM/TC SCC
TM/TC SCC
AOS
AOS
CCSDS SPP
MO Services
Convergence
Convergence
Convergence
SOIS Packet
Device Handler
Device DACP
Device DSAP
TMTC DACP
TMTC DSAP
Convergence
CCSDS SPP
R/T OS

## Slide 3: MOIMS/SOIS Interactions, Case 2
TM/TC Device, On Board
Ground
Real-Time Computer
Device
Spacecraft
All MO functions on-board must be implemented in compliance with R/T OS and Class A/B processes
MO Device Service Proxy makes SOIS device Handler accessible via MAL over SPP and space link from ground.
MO Device Service Proxy converts MO Device Service requests on the ground to SOIS Device Handler on board.
SOIS Device Handler is shown here using DACP and DSAP, which provide access to the devices for MO services.
SOIS Packet Service routes packets to/from subnet using convergence layer.
Convergence functions match device manufacturer’s functions, if any, or are 1-sided, or are absent.
Space Packet Forwarding in TM/TC Device complies with CCSDS SPP standard and SOIS Subnet Convergence layer.
Space Link Physical
Subnetwork Link
Subnetwork Physical
Convergence
SOIS Packet
Subnetwork Link
MAL SPP Binding
MO Services
MO Applications
MO Device Svc Proxy
Device Logic
Subnetwork Link
Packetizer
MAL SPP
Space Packet Forwarding
Device DACP
Device DSAP
TMTC DACP
TMTC DSAP
Convergence
TM/TC SCC
TM/TC SCC
AOS
AOS
CCSDS SPP
CCSDS SPP
Device Handler
Convergence
Convergence
R/T OS

## Slide 4: MOIMS/SOIS Integrated, Case 3-a
TM/TC Device, On Board
Ground
Real-Time Computer
Device
Spacecraft
All MO functions on-board must be implemented in compliance with R/T OS and Class A/B processes
MO Device Service resides in onboard computer and makes SOIS device Handler accessible via MAL over SPP and space link from ground.
MO Device Service converts MO Device Service requests on the ground to SOIS Device Handler on board.
Other MO Services and Applications may reside onboard and on the ground.
SOIS device service is shown here using DACP and DSAP, which provide access to the devices for MO services.
SOIS Packet Service routes packets to/from subnet using convergence layer.
Convergence functions match device manufacturer’s functions, if any, or are 1-sided, or are absent.
Space Packet Forwarding in TM/TC Device complies with CCSDS SPP standard and SOIS Subnet Convergence layer.
Space Link Physical
Subnetwork Link
Subnetwork Physical
Convergence
SOIS Packet
Subnetwork Link
MAL SPP Binding
MO Services
MO Applications
MO Services
Device Logic
Subnetwork Link
Packetizer
MAL SPP
MO Applications
Space Packet Forwarding
Device DACP
Device DSAP
TMTC DACP
TMTC DSAP
Convergence
TM/TC SCC
TM/TC SCC
AOS
AOS
CCSDS SPP
CCSDS SPP
MO Device Service
Device Handler
Convergence
Convergence
R/T OS

## Slide 5: MOIMS/SOIS Integrated, Case 3b
TM/TC Device, On Board
Ground
Real-Time Computer
MO Device
Spacecraft
All MO functions on-board must be implemented in compliance with R/T OS and Class A/B processes
MO Device Service resides in the device and performs all functions previously assigned to SOIS device service.
MO Services on-board use a MAL to SW Bus (and transport/ network) mapping to communicate.
Software Bus, Transport and Network layers reside in the device to communicate with MO Services in onboard computer and on ground.
On-board transport/network mapping uses SOIS Packet and subnet services.
SOIS Packet Service routes packets to/from subnet using convergence layer.
Device manufacturer implements MO Services, MO Device, MAL, SW Bus, SOIS Packet and Convergence functions.
Space Packet Forwarding in TM/TC Device complies with CCSDS SPP standard and SOIS Subnet Convergence layer.
Space Link Physical
Subnetwork Link
Subnetwork Physical
Convergence
SOIS Packet
Subnetwork Link
MAL SPP
MO Services
MO Applications
MO Services
Device Logic
Subnetwork Link
MAL SPP
MO Applications
MAL SW Bus
Space Packet Forwarding
TMTC DACP
TMTC DSAP
TM/TC SCC
TM/TC SCC
AOS
AOS
CCSDS SPP
CCSDS SPP
MAL SW Bus
Transport
Network
Software Bus
Transport
Network
Software Bus
MO Device Service
Convergence
Convergence
SOIS Packet
Convergence
SOIS Packet
R/T OS

## Slide 6: MOIMS/SOIS Integrated, Case 4
TM/TC Device, On Board
Ground
Real-Time Computer
Spacecraft
All MO functions Real-Time Computer must be implemented in compliance with R/T OS and Class A/B processes
MO Functions and framework may be implemented in a separate Ancillary Computer that may not need to comply with Class A/B constraints (and costs)
MO Services on-board either computer may use a MAL to SW Bus (and transport/ network) mapping to communicate.
Software Bus, Transport and Network layers reside in the both Computers to communicate with between both onboard computers and the ground.
On-board transport/network mapping may use SOIS Packet and subnet services.
The Ancillary Computer is separate from the Real-Time Computer, and may have access to all data paths, but the Real-Time Computer is expected to have ultimate control over resource utilization.
Space Link Physical
Subnetwork Link
Subnetwork Physical
Convergence
SOIS Packet
Subnetwork Link
MAL SPP
MO Services
MO Applications
MO Services
MAL SPP
MO Applications
MAL SW Bus
Space Packet Forwarding
TMTC DACP
TMTC DSAP
TM/TC SCC
TM/TC SCC
AOS
AOS
CCSDS SPP
CCSDS SPP
Transport
Network
Software Bus
Convergence
Convergence
SOIS Packet
R/T OS
Ancillary Computer
Subnetwork Link
Convergence
SOIS Packet
MO Services
MAL SPP
MO Applications
MAL SW Bus
TMTC DACP
TMTC DSAP
CCSDS SPP
Transport
Network
Software Bus
Convergence
SOIS Packet
Non R/T OS

## Slide 7: Communication between MOIMS Applications Onboard
Onboard Computer
Onboard Computer
Transport
Subnetwork Link Layer
SOIS Convergence
SOIS Packet Service
Subnetwork Link Layer
Network
Subnetwork Physical
Transport
SOIS Convergence
SOIS Packet Service
Network
Software Bus
Software Bus
MAL
MOIMS Services
MO Applications
MAL
MO Service
MO Application
MAL
MO Service
MO Applications
MO Application
Loopback