## Slide 1
CCSDS System Engineering
Area (SEA): System Architecture WG (SAWG)
RASDS Update Views
Peter Shames, SEA AD
Fred Slane, Ramon Krosley, Costin Radulescu, Christian Stangl
14 February 2022

## Slide 2: Revision of the Reference Architecture for Space Data Systems (RASDS)
Reference Architecture for Space Data Systems (RASDS) CCSDS 311.0-M-1 was published in Sept 2008
  RASDS has been leveraged by a number of CCSDS documents and also by several mission design projects.
  The document is consistently in the top 20-30 documents downloaded from the CCSDS web site, it is being used and referenced.
  RASDS is (over)due for a refresh, the question has been just what to do, and when.
The extensions to RASDS developed in producing the ASL ADD (CCSDS 371.0-G) and the SCCS-ARD and ADD, should be incorporated into the RASDS revision
  ASL ADD and SCCS-ADD examples may be adopted to improve graphics.
  Additional descriptive text on viewpoint & view construction should be added.
  In keeping with current MBSE best practices, an annex should be provided with a set of SysML representations. Published papers, and other CCSDS examples, addressing this already exist.
ISO TC20/SC14 wishes to make use of RASDS and is adopting it as a framework for describing their standards
  A liaison agreement has been agreed by the CMC, CMC-P-2020-03-003, dated 4-7-2020.
  A plan for these revisions has been outlined. See the following pages …

## Slide 3
System Architecture Model Objectives
"Modeling, in the broadest sense, is the cost-effective use of something in place of something else for some cognitive purpose. It allows us to use something that is simpler, safer or cheaper than reality instead of reality for some purpose.
A model represents reality for the given purpose; the model is an abstraction of reality in the sense that it cannot represent all aspects of reality. This allows us to deal with the world in a simplified manner, avoiding the complexity, danger and irreversibility of reality."
  Rothenberg, Jeff. “The Nature of Modeling”, RAND, https://www.rand.org/content/dam/rand/pubs/notes/2007/N3027.pdf
RASDS provides a modeling framework and methodology, a specific Space System Reference Architecture model …
  Provides clear & unambiguous views of systems architectures
  Shows relationship of design to requirements and driving scenarios
  Separates abstract design from implementation concerns in the model to maintain a degree of freedom to do trades
  Details the model & views to the level appropriate for further systems engineering, supports evolution of the design
  Enables concurrent design of spacecraft, ground systems, science operations, control systems, and their components
Notes: 3

## Slide 4: RASDS Revision – ISO 42010-2011 conceptual framework…
We build upon and adopt this system architecture meta-model framework, creating viewpoints aligned with it that are suitable for space system architecture description

## Slide 5: Meta-models: relationships between UML, ISO 42010, RASDS meta-models, and user models
RASDS meta-model defines specific Viewpoints, Objects, and Representations
RASDS conformant Architecture Description adopts specific Views & Model attributes, users may extend
Users adopt / adapt RASDS to describe their specific systems architecture
Copyright 1998-2016 by Rich Hilliard :: http://www.iso-architecture.org/42010
Reference: Jean Bezivin, “On the unification power of models”, 2005
representedBy
conformsTo
conformsTo

## Slide 6
Reference Architecture for Space Data Systems
Enterprise
Business Concerns
Organizational perspective
Connectivity
Physical Concerns
Node & Link perspective
Functional
Computational Concerns
Functional composition
Information
Data Concerns
Relationships and transformations
Communications
Protocol Concerns
Communications stack perspective
Derived from: RM-ODP, ISO 10746
Compliant with IEEE 1471 and ISO 42010
Notes: 6

## Slide 7: A reminder from DoDAF: DoDAF Viewpoints and Models - intro
To assist decision-makers, DoDAF provides the means of abstracting essential information from the underlying complexity and presenting it in a way that maintains coherence and consistency. One of the principal objectives is to present this information in a way that is understandable to the many stakeholder communities involved in developing, delivering, and sustaining capabilities in support of the stakeholder's mission. It does so by dividing the problem space into manageable pieces, according to the stakeholder's viewpoint, further defined as DoDAF-described Models.
Each viewpoint has a particular purpose, and usually presents one or combinations of the following:
  Broad summary information about the whole enterprise (e.g., high-level operational concepts).
  Narrowly focused information for a specialist purpose (e.g., system interface definitions).
  Information about how aspects of the enterprise are connected (e.g., how business or operational activities are supported by a system, or how program management brings together the different aspects of network enabled capability).
However, it should be emphasized that DoDAF is fundamentally about creating a coherent model of the enterprise to enable effective decision-making. The presentational aspects should not overemphasize the pictorial presentation at the expense of the underlying data.
RASDS defines specific objects and representations for different viewpoints and a methodology that may be used to define and aid understanding of different systems technical architectures, information & communications aspects, and deployment approaches.

## Slide 8: Original RASDS Top Level Object Ontology
Function
Behavior
Interfaces
Constraints
Logical structure
Connector
Type
Attributes
Communication
Protocol stack
Standards
Organization
Requirements
Objectives
Goals
Scenarios
Mission
FulfilledBy
Fulfills
IsAllocatedTo
ComposedOf
Composed Of
ComposedOf
ContainsInstances
Produces
Consumes
ConnectVia
ConnectToPort
Uses
ProvidesService
AssociatedWith
ImplementedOn
Information
Data
Metadata
Rules
Owns/Operates
Component
Type
Attributes
Ports
Calls
Environment
Physical Environs
Affects
Location
Attributes
Meta-model
(each Viewpoint)
Defines Objects
Defines Rules
Exposes Concerns
Defines Relations

## Slide 9: RASDS++ Viewpoint Specifications
Each RASDS++ Viewpoint addresses:
  Stakeholder concerns: What does the stakeholder care about (what must views address)
  Objects: The fundamental kinds of objects (functions, data, organizations, physical elements, protocols, etc)
  Relationships: The descriptions of object attributes and how they relate, including correspondences to other objects
  Representation: How objects and relationships of different types are represented in diagrams
MBSE adaptations:
  The primary work that must be done to use RASDS++ with MBSE tools is to:
    Define profiles to represent the different objects and relationships
    Create stereotypes that can be used consistently in the tools
    Use the profiles and methods to develop the MBSE style representations

## Slide 10: RASDS++ Representations (with ASL and SC14 extensions)
Organizational Element
Communications Protocol
Data
Store
Data Store
Color Key for Example Diagrams (from SCCS-ARD):
User Node
Earth Routing Node
Space Routing Node
WAN Node
Application
Element Management
Network Management
Network Layer function
Link Layer function
Routing function
Forwarding function
Data Store
Physical Node
Information
Object
Physical or
Functional Connection
Logical Link
between Elements
Organizational Domain
Router
Functional Element
Link Layer User
Service Access Point
Peering
Arrangement
DATA
Service Provider
Service Consumer
Notes: ASL Fig 3-1, trim headers & footers

## Slide 11: Relationship of ASL & SCCS-ARD/ADD to RASDS
Two documents, the ASL ADD and the SCCS-ARD/ADD, both use the Reference Architecture for Space Data Systems (RASDS) framework
Each used a consistent set of viewpoints and views based on RASDS method and representations
  RASDS provided the baseline set of viewpoints (Enterprise, Functional, Connectivity (deployment), Protocol, and Information.
  The ASL ADD added some useful extensions to the functional viewpoint, improved representation for the information viewpoint, and added a tabular services viewpoint.
  The SCCS-ARD/ADD developed a representative set of physical elements (nodes), extensively used the Connectivity viewpoint featuring deployed functions, and developed a set of protocol stack building blocks, that could be used to compose end-to-end architectures.
  These extensions, and others to meet SC14 needs, are being incorporated into the RASDS++ update.

## Slide 12
Proposed RASDS++ Extensions
(SC 14 Collaboration)
Service Viewpoint
  Already introduced in CCSDS SCCS-ARD/ADD & ASL
  Covers exposed system service interfaces and interface bindings, hardware, software, and people
  Tabular representation, ties to protocol stacks and interface binding signatures
Physical Viewpoint
  Extend present Connectivity Viewpoint, Components and Connectors to add new attributes & types
  Add support for physical aspects of elements, structures, energetic flows, position, attachment, field of view, power, thermal, radiation, other energetic views
Operational Viewpoint
  Create new Operational Viewpoint
  Add support to describe operational processes, procedures, and related behavior
  Propose correlation to / derivation from from UML activity / sequence diagrams

## Slide 13
RASDS Concept Model … and Proposed TC20/SC14 extensions
RASDS++ as Architectural Framework *
Connectivity / Deployment Viewpoint
Connectivity
Components & connectors
RF & optical
Physics of Motion
End to End Views
External Forces
Performance
Physical Viewpoint -Structures:
Power
Mass
Thermal
Orbit
Propulsion
Enterprise Viewpoint (15288)
Organizations
People
Use Case
Contracts Agreements (CONFERS)
Glossary
Augment to Capture:
Capabilities
Mission Design & Drivers (OV-1?)
Requirements
Phases
Engineering Viewpoint
System Design & Construction - realization
Functional allocation
Distribution of functions and trade-offs
Development
Validation & verification & engineering processes
Just use 15288 or agency specs
* Reference Architecture for Space Data Systems (RASDS)
** Reference Model Open Distributed Processing (RMODP, ISO 10746 spec)
Functional Viewpoint
Functional Structure - abstract
Functional Behavior & abstract interfaces
End to End View
Cross Support Services
Protocol Viewpoint
Protocols & comm standards
End to end Information Transfer Mechanisms
Cross Support Services
Service interface bindings
State & Sequence charts ?
Information Viewpoint
Information & information management
Data structures, syntax & semantics
Attributes & constraints (ASN, FRM, EDS)
Mission Assurance Viewpoint ??
Enterprise Risks
Cost
Validation & verification
Safety
Reliability & quality
Operational Viewpoint
Processes
Procedures
Activities, tasks, actions
Scenarios, Events
Modes & states
Services Viewpoint
Tabular views of functions, operations, and related standards
Support system Design & Construction - realization
Correspondence to Protocol stacks and interface binding signature
Functional allocation and distribution of functions and trade-offs (correspondence)
Just use 15288 or agency specs
New Viewpoint
Modified Viewpoint
De-selected Viewpoint
Notes: 13

## Slide 14: Revised RASDS++ (DRAFT) Top Level Object Ontology
Function
Behavior
Interfaces
Constraints
Logical structure
Connector
Type
Communication
Protocol stack
Standards
Organization
Requirements
Objectives
Goals
Use Cases
Mission
FulfilledBy
Fulfills
IsAllocatedTo
ComposedOf
Composed Of
ComposedOf
ContainsInstances
Produces
Consumes
ConnectVia
Uses
ProvidesService
AssociatedWith
ImplementedOn
Information
Data
Metadata
Rules
Develops / Owns
Component
Type
Attributes
(comm, power,
thermal, prop)
Attachment
Calls
Environment
Physical Environs
Affects
Location
Attributes
Meta-model
(each Viewpoint)
Defines Objects
Defines Rules
Exposes Concerns
Defines Relations
Operations
Processes
Activities
Tasks
Modes/states
Scenarios
Performs
Invoke
Service
Svc Behavior
Interface Sig
Svc Constraints
Offers
Defined by
Attributes
(comm, power,
thermal, prop)
Defines Correspondences

## Slide 15: Comments on Engineering and Mission Assurance Viewpoints
Engineering viewpoint concerns are already thoroughly covered by ISO 15288.
  The SE “V”
  Processes and steps
  Also various agency specific standards
Mission Assurance processes are also well covered by ISO 15288 and agency standards.
Since both of these are process oriented in nature, and these processes are well documented, no added Viewpoint in RASDS is required.
What RASDS++ does do, however, is provide a standardized means to document the system architectures themselves.
  This is a capability that these standards call for, but do not provide

## Slide 16
Object
Unified Object Feature Representation
Core Functions
What the object
does
External Interfaces:
How external elements
are controlled
Management Interfaces:
How objects are configured
controlled, and reported upon
Service Interfaces:
How services are
requested & supplied
Concerns:
Issues
Resources
Policies

## Slide 17: Technical Architecture Definitions
System
  A System is a group of interacting or interrelated Elements that act according to a set of rules to form a unified whole. A System, surrounded and influenced by its environment, is described by its boundaries, structure and purpose and expressed in its functioning.
  A collection of interacting components organized to accomplish a specific function or set of functions. A System is composed of Elements, which may be any of: Hardware, Software, People, and Procedures.
Function
  A Function is the purpose for which an Element is intended. This can be an activity performed by the Element or the usage of this Element by other parts of the system.
  A Function is interpreted as a specific process, action or task that a System is able to perform.
Service
  A mechanism to enable access to a set of one or more functions of an Element, where the access is provided using a prescribed interface and is exercised consistent with constraints and policies as specified by the service description.
  A Service is an exposed interface of a Function.
Interface
  An Interface represents a set of mechanical, electrical, signal, or other properties that describe some aspect of a Element’s connection to or interaction with another Element.
  An interface is formed of the ports on two or more elements and the junction that joins them.

## Slide 18: Functional Viewpoint
The Functional Viewpoint describes the functional decomposition of the space data system into abstract objects that interact at interfaces.
Stakeholder Concerns:
  a functional decomposition of the system into objects that interact at interfaces;
  the abstract behavior of the system, its interactions and constraints.
Functional Objects (abstract set of functions, their behaviors, interfaces and configurations);
  Types: data source, data sink, data transformation, control, planning, monitoring, analysis;
  Attributes: role, name, type, behavior, interface signature, data types handled, interaction modes, constraints, allocated requirements;
Logical Links (connections between Functional Objects, connected to associated logical behavior and properties);
Relationships (configuration, precedence, control and data flows, management flows, allocations);
Information (representations of data that are exchanged among Functional Objects, where formal specifications for the objects are found in the Information Viewpoint).

## Slide 19
Functional Object
Functional Viewpoint
(Abstract Functional Object Features)
Attributes
Identifier
Type
Behavior
Interfaces
Performance constraints
External Interfaces:
How other Functional Objects are used to support the performance of this Object
Management Interfaces:
How function is configured,
controlled, and reported upon
Service Interfaces:
How services are
requested by & supplied
to other Functional Objects
Concerns:
Issues
Resources requirements
Constraints

## Slide 20: Extended RASDS Functional View Representation*
Function A
DATA
Logical Link: end-to-end interface between functions
Service Provider
(provided I/F, optional)
Service Consumer
(required I/F, optional arrowhead)
Information Object
(optional)
DATA
Denotes a specific Data Type subject to standardisation by CCSDS / SC14
Italics denotes an Abstract or Generic Data Type
Faded Colour: Data contained within another Data item (to which it is attached)
DATA
DATA
DATA
DATA
DATA
DATA
Unspecified Status (typically used for aggregated or grouped data/services)
Published CCSDS / SC14 Standard (Blue or Magenta Book)
[Future]: CCSDS / SC14 Standard Under Development
[Prospective]: Proposed CCSDS / SC14 Standard (Green Book – future road map)
No CCSDS / SC14 Standard Identified
DATA
Specific and Generic Data Types and Containment:
Standardisation Status:
* Revisions from ASL
Functional Objects are abstract representations of behavior. They may be instantiated or realized in different logical or physical constructs.
Functions may themselves be decomposed into lower level functions, shown by containment.
Different deployments or realizations of the same Functional Object may be expressed in other views and referenced by correspondence.
Functional Objects may explicitly define a service providing interface, but this is not required.
They may explicitly identify the information objects that are exchanged (tied by correspondence to the Information View where they are defined).
Sub-Function B1
Function B
Notes: ASL Fig 3-4, trim headers & footers

## Slide 21
Directive
Generation
Directive
Execution
Alternative Functional VP representation examples
Directive
Management
Directive
Generation
Directive
Execution
Directive
Management
SCEP
SCD
Key:
SCEP - S/C Event Plans
SCD - S/C Directives
SCC - S/C Commands
SCD
SCC
Two different simple Functional Object views, one explicitly showing provided interfaces and data objects, the other just showing flow directions.

## Slide 22: Simplified functional VP example
Mission
Planning
Mission
Analysis
Spacecraft
Analysis
Monitor &
Control
Directive
Generation
Data
Acquisition
Orbit
Determ
Tracking
Radiometric
Data Collect
LT Data
Repository
Data
Repository
Directive
Execution
Directive
Management

## Slide 23: Example: MOIMS top-level Functional Decomposition, Data and Services (from ASL)
Navigation & Timing
Planning & Scheduling
Mission Control
Data Storage and Archiving
Operations Preparation
User Support
TT&C
Spacecraft Development & Maintenance
NAVT
MPS
NAVT
NAVT
MCS
MCS
MCS
OPD
MCS
OPD
MPS
MPS
NAVT
NAVT
MPS
MCS
NAVT
MDP
Functions and Data Colour Coded: Data in Rectangles; Services indicated at Provider End by Circle MDP = Mission Data Product
MCS
MCS
OPD
Mission Data Processing
MCS
MPS
NAVT
MDP
MDP
NAVT
NAVT
MCS
MPS
SLE-Ret
TRM
OPD
CSSM-ES
SC-CSTS
MD-CSTS
CSSM
TD-CSTS
Notes: ASL Figure 4-2, trim top & bottom
The 5 MOIMS Areas are colour coded.
Each application level interaction is annotated with the Data exchanged. At this level all Data generated by each Function is grouped as a single type (the abbreviation reflects the function name).
Potential service interfaces identified by MO are indicated by a colour-coded circle representing the Service Provider
Data formats may be separately defined [NAV, MPS] or specified in the context of the service [MO M&C, MPS].
File Handling is a bit different – there are special services for File Management and File Transfer [the latter delegated to a lower level protocol, such as CFDP or FTP], but the file content my be associated with any of the other Functional Areas. It essentially provides the transport layer for bulk transfer of service messages or data formats. Mission Data Products may also be transferred as files.
Note Planning/Scheduling interactions with the GSTS are greyed out as they are outside the scope of MOIMS standardisation [CSS boundary agreement].

## Slide 24: Information Viewpoint
The Information Viewpoint focuses on the kinds of information handled by the system, the semantics of the information, and the interpretation of that information.
Stakeholder Concerns:
  the structure and semantics of information and information management in a system;
  the rules and constraints on information transformations and permanence in a system.
Information Objects (abstract definitions of information elements, structures, semantics, schema):
  Types: data, metadata, information, package, schema, model, meta-model;
  Attributes: name, type, length, structure, syntax, semantics, permanence, provenance, realized by, rules, policies;
Relationships (information object aggregates, transformations);
Constraints (type checking rules, permanence, policies).

## Slide 25
Information Object
Information Viewpoint
(Information Object Features)
Management Interfaces:
Rules
Schema
Permanence
Element types
Constraints
Concerns:
Rules & Constraints
Resource requirements
Core Capabilities:
Type
Identifier
Structure
Semantics
Relationships
Type conversion
Constraint checking

## Slide 26: Information Representation (ASL version) (Relationships derived from UML)
Information Class B
Information Class A
Relationship
0..1
*
Optional relationship type label
Optional multiplicity specifier
Inheritance
Composition
Aggregation
Association (other relationship, labelled)
Directional Association
Relationship Types (UML derived): Read as sentence with subject = start of arrow, verb = label, and object = end of arrow
DATA
DATA
DATA
DATA
Unspecified Status (typically used for aggregated or grouped data/services)
Published CCSDS / SC14 Standard (Blue or Magenta Book)
[Future]: CCSDS / Sc14 Standard Under Development
[Prospective]: Proposed CCSDS / SC14 Standard (Green Book – future road map)
No CCSDS / SC14 Standard Identified
DATA
Standardisation Status:
Information Objects are abstract representations of information and data structures. They may be referenced in many other views.
The explicit definitions of Information Objects in this Viewpoint are tied by correspondence to the Functional or other Views where they are referenced.
Information objects may themselves be decomposed into lower level objects, shown by containment or relationships.
Specific information object structures will typically be instantiated during design and realized in different forms during development.
Different instantiations or realizations of the same Information Object may occur in different deployments.
Notes: ASL Fig 3-6, trim headers & footers

## Slide 27
Information Viewpoint
Abstract Information Ontology
Information
Data Type
0..*
Representation
described by
Range
Name
Name
Encoding
0..1
0..*
0..*
0..*
Structure
association
ordered

## Slide 28
Information Viewpoint Objects
Showing Instantiation & Realization
Schema &
Structure
Definitions
Concrete
Data
Object
Abstract
Data
Architecture
Data
Models
Actual
Data
Objects
Instantiation
Realization
Conceptualization
Abstract description of information objects
Information
Data Type
0..*
Representation
described by
Range
Name
Name
Encoding
0..1
0..*
0..*
0..*
Structure
association
ordered
Instantiated description of specific data models
Realized actual data objects

## Slide 29: ASL Info model example: SOIS System Model: Concept Diagram
Rounded rectangles represent concepts used by SOIS.
Solid lines represent communication between endpoints.
Dashed lines represent relationships, pointing from subject to object.
Dotted lines represent references, pointing to referenced object.
Dash-dotted lines represent aggregation, pointing to aggregated object.
Mission Application Interfaces
PackageFIle
describes
Application Support Service Interfaces
describes
SO Model
DoT
references
Device Service Interfaces
specifies
Datasheet
Device
describes
references
references
Deployment Description
references
Management Service Interfaces
specifies
Subnetwork
describes
Notes: ASL Figure 5-15, trim top & bottom

## Slide 30: ASL example: SOIS System Model - OWL Dictionary of Terms Diagram
Dictionary of Terms (DOT) Diagram from Protégé using OWL
Inheritance tree for classes of objects
Notes: ASL Figure 5-16, trim top & bottom

## Slide 31: Connectivity Viewpoint
The Connectivity Viewpoint describes the engineered decomposition of the space data system into components (nodes) that exchange data across connectors (links). The Connectivity Viewpoint describes the physical aspects of space data systems communications and the external environment within which they operate, the physical behavior (and motion) of the nodes, and their physical decomposition into communicating elements.
Stakeholder Concerns:
  The mechanisms and functions required to support distributed communications between objects in the system;
  The selected allocation of functions to the nodes of the system, including their implementation choices and constraints on implementation, connections, configuration, and operations imposed by the communication links and the environment;
  The behavior and performance of elements in the system, including their communications capabilities, physical motion, and their interactions with the physical environment.
Engineering Objects (Nodes, Links, Applications):
  Nodes (hardware Engineering Objects, provide communications, processing and other computing and data resources, ports, performance and other associated physical behavior):
    Types: hardware objects, composite hardware objects, ports;
    Attributes: name, type, location (place, trajectory, orbit), laws of motion, available resources, physical interfaces, capabilities (e.g., processor speed, throughput, bandwidth, storage capacity, aperture size, etc.), allocated functions, constraints;

## Slide 32: Connectivity Viewpoint, contd
Engineering Objects (Nodes, Links, Applications), contd:
  Links (communications connections between Nodes, associated physical behavior and properties);
    Types: space link (RF or optical), physical link (e.g., point-to-point, bus, network, copper, fiber, etc.);
    Attributes: name, type, end-points (port on node), physical interfaces, performance (e.g., throughput, bandwidth, frequency band, Round Trip Light Time (RTLT), pointing and view periods, signal attenuation, constraints, environmental effects, etc.), access and ownership;
  Applications (software Engineering Objects, behavior, and processing/resource requirements, may be layered):
    Types: software Engineering Objects, composite software Engineering Objects;
    Attributes: name, type, algorithms, implemented functions, allocation/ deployment to nodes, required resources (e.g., memory, CPU, storage), implemented interfaces (provided and required), implementation language, Operating System (OS)/framework dependencies, constraints;
Relationships (composition, interfaces, constraints, configurations, allocation);
  Environment (physical environs, physical forces [gravity and others], physical interactions and effects);
  Information correspondences (defined representations of data that are exchanged among Engineering Objects, where formal specifications of data architecture are found in the Information Viewpoint).
NOTE – Physical Nodes and Links in any given space system may include many more aspects (physical structures, connections, and flows), types (power, propulsion, thermal) and many more attributes than those shown here. The physical, structural, and energetic flow aspects of Nodes and Links are covered in the new Physical / Structural Viewpoint.

## Slide 33
Connectivity Viewpoint - Physical Object
(Node / Component Features)
Attributes:
Name/identifier
Address
Composition (engineering objects)
Performance
Distribution
Sub-nodes
Communication links and Ports
Physical environment
Configuration
Constraints
External Interfaces:
Communication links to other Nodes
Management Interfaces:
How Nodes are configured,
controlled, and reported upon
Service Interfaces:
Communication links from other Nodes
Node
(Component)
Notes:
Interfaces of Components may be described by an EDS
Specific Components may implement a set of Functional Resources
Physical Environment
Laws of Motion
Communications Geometry

## Slide 34: RASDS Connectivity View Representation
DATA
Physical Link: Node to Node connection
Service Provider I/F *
(provided I/F, optional)
Service Consumer I/F
(required I/F, optional)
Information Object
(optional)
Denotes a specific Node (physical component), may have embedded components
Denotes an implementation of a defined function, may be software or hardware (optional, see Functional Viewpoint)
Denotes a Physical Link (Connector of some sort) between two Nodes
Denotes a physical interface (optional, allows interface type to be characterized)
Denotes a protocol layer at an interface (not shown here, optional, allows interface binding to be characterized, see Communications Viewpoint)
Not shown are Information Objects describing interfaces or connectors which may be described in the Information Viewpoint and referenced by correspondence
Specific and Generic Object Types and Containment:
Related to the Physical Viewpoint, but focus is on data connections not physical connections or energetic flows.
Nodes (Components) will explicitly connect via some Physical Link. This may be free space (RF or optical) or it may be a hardware connection of some sort (cable, twisted pair, fiber optic).
A Node may explicitly define a physical interface, but this is not required. Nodes may have a provider/consumer relationship or they may be peers.
May show allocation of implemented Functions, in hardware (as a sub-node) or in software. These are tied by correspondence to the Functional View where they are defined.
May explicitly identify the information objects exchanged over the link (tied by correspondence to the Information View where they are defined).
May explicitly identify the protocol stack at an interface (tied by correspondence to the Communications View where they are defined).
Node A
Node B
Function A
Function B
Sub-Node B1
Function Deployment
(optional)
*
Notes: ASL Fig 3-4, trim headers & footers

## Slide 35
Science
Instrument
S/C
Transceiver
Attitude
Control
Computer
Command &
Data Handling
Computer
Tracking
Computer
Predict
Generation
Computer
RF & Ant
Systems
Mission
Planning
Computer
Science
Processing
Data
Management
Computer
Spacecraft
Control
Computer
Monitor &
Control
Computer
Flight
Dynamics
Computer
Science Spacecraft
Tracking Station
Spacecraft Control Center
Science
Institute
Simple Connectivity View Example
Nodes & Links

## Slide 36: ASL Connectivity View: Simple ABA Mission example showing application layer function deployment to Nodes
Spacecraft
ESLT
MOC
S/C Manufacturer
Spacecraft Development & Maintenance
TT&C
Planning & Scheduling
Navigation & Timing
Mission
Control
Data Storage & Archiving
Operations
Preparation
Plan Execution
Time/Pos Det
M&C Automation OBCM
OB File Store
CSSM
TRM
TDM
MD-CSTS
ODM
TRP
TDM
PEC
PLN
AUT
OBPM
OBSM
MDP
MPS
SDB
APD
OBSW
FTM
MDP
XTCE
M&C
MCS
NAVT
SLE-Ret
MCS
NAVT
TD-CSTS
SC-CSTS
Notes: ASL Fig 9-2, trim headers & footers
ABA: Spacecraft, ESLT, MOC and SMC (ignore NOC) On-board Functions: Basic M&C; On-board Procedures; On-board Scheduler Tracking done by Dedicated ESLT S/C DB, OBSW and OBCPs from S/C Manufacturer, also supporting performance monitoring and fault diagnosis All other functions in MOC

## Slide 37: ASL Connectivity View with Abstract Protocol Layer (showing corresponding Function and protocol stack deployments)
Node A
Function A (Provider)
Message Abstraction
Service Layer
Node B
Function B
(Consumer)
Message Abstraction
Service Layer
DATA
Technology Binding
Transport Protocol
Network Protocol
Link Layer
Transport Protocol
Network Protocol
Link Layer
Technology Binding
Physical Link
Logical Link
End-to-end Service
Stack of Communications Layer Protocols
Stack of Application Layer Protocols
Service Access Point
Deployment Node
Notes: ASL Fig 3-7, trim headers & footers

## Slide 38: Communications Viewpoint
The Communications Viewpoint focuses on the mechanisms and functions required to engineer and implement the protocols and communications standards for the space data system, including implementation choices and specifications, and relationships among elements in different protocol layers.
Stakeholder Concerns:
  the choice of communications and data transfer standards in the system;
  the end-to-end communications protocol functionality and reliability;
  implementation of the protocol specifications and the services they provide;
  the relevant protocol stacks, interfaces, and interactions;
  interaction of protocol design with environmental constraints;
  support for design, evaluation of suitability, and integration into the rest of the system.
Protocol Entities (elements that implement specific protocols, protocol stacks, with Service Access Point (SAP) and peer interactions optionally shown):
  Types: protocol purpose (e.g., coding, modulation, link, network, transport, middleware, application service);
  Attributes: name, type, capabilities (e.g., in order, once only, bandwidth efficient, error correcting, delay tolerant), applicability (e.g., deep space, near Earth, in situ), constraints, services (offered, required), interface signature (requests, indications, responses, confirmations), API (where appropriate), standard reference identifier, standards organization;
Protocol design specification elements (PDU description), behavior (state machine or table description), reliability (acknowledged, unacknowledged, selectively acknowledged), other design views of the communications protocol or protocol stack;
Correspondences to Nodes and Links (representations of physical elements from the Connectivity Viewpoint, for context);
Correspondences to Software Engineering Objects (representations of implemented functions from the Connectivity Viewpoint, for context).

## Slide 39
Core Functions
Peer behaviors
PDUs
Signaling
Required Interface :
How protocol services are requested from & supplied to this layer by lower layers
Management Interfaces
(may be represented by a MIB):
How protocol is configured
controlled, and reported upon
Provided interface (service access point):
How protocol services are requested of & supplied by this layer
Attributes:
Standards
Functionality
Technology
Applicability
Protocol Entity
Note
Each protocol entity represents a standard
Protocol Entities are usually shown in a stack
Protocol stack at an interface may be described by an EDS
Communications Viewpoint
(Protocol Entity Representation)

## Slide 40: RASDS Protocol View Representation
Protocol Layer n peer
Protocol Layer n
Protocol PDUs
(logical flow)
PDUs may be simplex or bi-directional
Protocol behavior (may be described by state machine or other)
Proto
Proto
Proto
Proto
Unspecified Status (typically used for unknown protocols)
Published CCSDS / SC14 Standard (Blue or Magenta Book)
[Future]: CCSDS / SC14 Standard Under Development
[Prospective]: Proposed CCSDS / SC14 Standard (Green Book – future road map)
No CCSDS / SC14 Standard Identified
Proto
Standardisation Status (if required):
Protocol Layer n-1
Service Provided Interface (n SAP, optional)
Service Required Interface (of n-1 SAP, optional)
Layer type and naming usually follows ISO / IEC 7498 Basic Reference Model (BRM).
Each protocol must have defined behavior, PDUs, and required / provided interfaces. If there is an inter-layer interface mismatch a “shim” or adapter may be required, and this may be complicated enough to be treated as a separate protocol.
Behavior may be defined in a state machine, state table, or narrative form. Usually only defines behavior of sending side, but may define both ends.
May (optionally) formalize the SAP definitions and show Requests and Indications at the SAPs.
physical flow
Protocol Layer n-1 peer
Flow direction arrows (optional)
Notes: ASL Fig 3-6, trim headers & footers

## Slide 41: Simple Communications View example Basic ABA End-to-End Forward CLTU Protocols
VC X
ABA Earth-Space
Link Terminal
ABA Earth User Node
ABA Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
VC X
To VC X
RF & Mod
IP
TCP
F-CLTU
F-CLTU
Production
Space F-CTLU
Application
TC
RF & Mod
C & S
User F-CLTU
Application
IP
TCP
F-CLTU
TC
C & S
C & S = Coding & Synchronization
Notes: 12/12/12: Updated Peter’s version so all lines were the same width, alignment within text boxes was center, general alignment adjustments. Added “C & S” definition to bottom.
41

## Slide 42
SCCS example: SSI Secure End-to-End Forward Protocol Deployment - SSI Agency Supporting SSI Agency
Earth-Space
Link Terminal
Earth User Node
Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
SSI
SSI
SSI
VC X
CMD
VC X
AOS/TC
RF & Mod
C & S
CFDP
ENCAP
Space Msg
Application
Space File Application
BP
AMS
LTP
RF & Mod
IP
C & S
F-Frame
Mux F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
AOS/TC
BP
To VC X
User File Application
IP
TCP
BP
User Msg
Application
CMD
CFDP
AMS
File Secure
BPSec
File Secure
BPSec
BPSec
BPSec
TCP
Notes: ASL Fig 9-16, trim headers & footers
12/12/12: New slide from Peter. Figure title in document is shown above. PPT original figure title is “SSI Secure Single Link Cross Support – Forward
(File, Frame & Message all DTN)
42

## Slide 43: Enterprise Viewpoint - Revised
The Enterprise Viewpoint focuses on the purpose, scope, and policies for the space data system. It describes the organizational entities and relationships; their roles, requirements, goals, objectives, scenarios, constraints; and how to meet them.
Stakeholder Concerns:
  the purpose, scope, and policies for the system;
  the objectives, operations concepts, and scenarios for the system;
  the requirements and constraints on the system;
  roles played by the system elements;
  activities undertaken by the system.
Enterprise Objects:
  Types: Organizations, both formal and informal (missions, projects, communities, with their roles and responsibilities), and Resources (facilities or other elements having enterprise operational or service roles);
  Attributes: name, role, objectives, point of contact, location, members, resources, provided services, types, interfaces and data, interaction modes, requirements, constraints;
Domains (boundaries of responsibility or ownership, requirements);
Relationships (ownership, membership, participation, roles, contractual);
Correspondences of Information (defined instances of documents, agreements, contracts, policies, requirements, objectives, goals, scenarios, membership lists, interface specifications, where formal specifications of the data to be exchanged are found in the Information Viewpoint).

## Slide 44
Enterprise Viewpoint - Enterprise Object
(Organizational Entity Features)
Attributes:
Identifier
Organization
Roles
Objectives
Requirements
Capabilities
Resources
Risk Management
Agreements
Budget
Contracts
External Interfaces:
Scope
Requirements
Policies
Rules
Agreements
Contracts
Funding
Management Interfaces:
Scope
Requirements
Policies
Rules / Laws
Purpose / Mission / mission types
Funding
Service Interfaces:
Requirements
Agreements
Contracts
Funding
Enterprise
Object
Notes:
Interfaces of Enterprise Objects are often described by documents
Specific Enterprise Objects may own / implement / operate a set of Functions or Components

## Slide 45: RASDS Enterprise View Representation
DATA
Logical Link: Node to Node interface
Domain Boundary
(optional)
Organization Object
(Org, Project, Business)
Denotes a specific Organization (org, project, business), may have embedded components
Denotes a function an organization carries out (optional, see Functional Viewpoint)
Denotes a Logical Link (information flow of some sort) between two Organizations
Denotes an information object (optional, allows data to be characterized, see Information Viewpoint)
Denotes an organization / domain boundary (ownership / responsibility)
Specific and Generic Object Types and Containment:
Organizations (Agency, Project, Business) will explicitly connect via a Logical Link. May show the organization domain of control or ownership, or containment (sub-org).
May show allocation of Functions that an organization carries out (tied by correspondence to the Functional View where they are defined).
May explicitly identify the information objects (such as contracts, requirements, agreements) exchanged between organizations (tied by correspondence to the Information View where they are defined).
Org A
Org B
Function A
Function B
Sub-Org B1
DATA
Information Object
(optional)
Notes: ASL Fig 3-4, trim headers & footers

## Slide 46: Enterprise View Single Agency Mission Domain & Enterprise Objects Operations Planning Phase
Agency A
Mission &
Support
Organizations
Mission A
Instrument
Control
Team C
Spacecraft
Control
Org A
Ground
Tracking Network
B
Agency A
Operations
Domain
Instrument
Support
Agreement
Long range
Tracking Plan
Tracking
Configurations
Comm Link
Modes
Enterprise Concerns:
  Objectives
  Roles
  Requirements
  Policies
  Risk Management
  Lifecycle / Phases
  Configuration
  Contracts
Mission A
Spacecraft
Instrument
C

## Slide 47: Enterprise View Multi-Agency Mission Domain & Enterprise Objects Operations Phase
Agency ABC
Instrument
Control Team
Mission Z
Spacecraft Control
Team
Agency ABC
Ground Tracking
Network Ops
Agency ABC
Operations
Domain
Instrument
Observation
Request
Comm Link
Configs
Tracking
Requests
Enterprise Concerns:
  Objectives
  Roles
  Requirements
  Policies
  Risk Management
  Lifecycle / Phases
  Configuration
  Contracts
Mission Z
Spacecraft
Agency ABC
Space Relay
Network Ops
Instrument
ABC
Agency ABC
Science Team
Agency QRS
Science Team
Agency QRS
Operations
Domain
Mission Z
Operations
Domain
Science Planning
Coordination
Relayed
Comm
Data

## Slide 48
Enterprise View - Mars Exploration Program Example
Mars Exploration
Program Federation
MSL Proj
MRO Ops
MMO
Svc Org Z
IND
MRO Proj
NASA/
JPL
S/C Contractor
MEx Proj
Prog S
ExoMars Prog
ESA
Operations
Agreements
Cross- Support
Agreements
Enterprise Concerns:
  Requirements
  Objectives
  Roles
  Policies
  Configuration
  Contracts / agreements
  Lifecycle / Phases
Instr Org S
Instrument
Integration
Science
PI Org
Tracking
Agreements
ICDs

## Slide 49: “Enterprise Architecture” Definitions
Enterprise Capability
  An expression of what an enterprise does and can do. An enterprise capability denotes the “What” an enterprise can do, whereas an enterprise process outlines how a particular activity gets performed by enterprise systems.
  At an elemental level, an enterprise capability is the encapsulation of the underlying functionality expressed abstractly.
System Capability
  An ability that an organization, person, or system possesses. Capabilities are typically expressed in general and high-level terms and typically require a combination of organization, people, processes, and technology to achieve.
Capability
  A set of features implemented by technical, physical, and procedural means. Such features are typically selected to achieve a common organizationally valued purpose.
Pick one (or more) of these definitions …

## Slide 50: “Enterprise Architecture” Definitions, contd
Enterprise (as opposed to Operational …) Process
  An enterprise process is defined as a set of activities and tasks that, once completed, will accomplish an organizational goal.
Activity
  Work, not specific to a single organization, operational system or individual that transforms inputs (Resources) into outputs (Resources) or changes their state. (DoDAF, edited)
Actor
  An actor specifies a role played by a user or any other system that interacts with the subject. It may represent roles played by human users, software, external hardware, or other subjects. (UML)
Application
  An application (app), application program or application software is a computer program designed to help people perform an activity (Wikipedia)
Data
  The representation forms of information that may be stored and/or exchanged by systems and users thereof. (Information)
  Not completely clear what a “data artifact” might be. In some contexts it is defined like this:
    A data artifact is a data flaw caused by equipment, techniques or conditions. Common sources of data flaws include hardware or software errors, conditions such as electromagnetic interference and flawed designs such as an algorithm prone to miscalculations.

## Slide 51: Enterprise Modelling Ontology - Formalized Relationships (Capability / Process Viewpoint, leaves out Systems & Functions)
(enterprise) Process
Capability
Actor
Performed
by
Enterprise
Possess set of 1..
Implemented by 1..
Uses …
Application
Enterprise
Information
Services …
Uses
Department
Member
of
Service
Application*
Data Artifact
Uses …
Accesses
* An “Application” is a set of functions deployed (somehow) on a server as part of a system
  An enterprise capability denotes the “What” an enterprise can do, whereas an enterprise process outlines “how” a particular activity gets done.
  An enterprise process is defined as a set of activities and tasks that, once completed, will accomplish an organizational goal.
Enterprise (financial, contract, success…)
Requirements (L0, L1)

## Slide 52: Formalized Relationships among Terms (System Viewpoint aspects, related to Capability)
System**
System
Element
Hardware
Software
People
Procedures
Function
Has 1..
Composed of 1..
Implement 1..
Environment
Affects
Offers 0..
Service
Technical Process
Action
Task
** A “System” may be de-composed into System Elements.
  System: A collection of interacting components organized to accomplish a specific function or set of functions.
  A System is composed of Elements, which may be any of: Hardware, Software, People, and Procedures.
Capability
Provides 1…

## Slide 53: Formalized Relationships between Enterprise & Technical Architecture (Recolored for the Viewpoint the objects are defined in)
System **
Hardware
Software
People
Procedures
Composed of 1..
Environment
Affects
Function
Implement 1..
Function offers 0.. Service Interfaces
Process
Action
Task
* An “Application” is Software, a set of functions deployed (somehow) on a hardware platform or a server as part of a system, with defined interfaces
(Business) Process
Capability
Actor
Performed
by
Business
Possess set of 1..
Implemented by 1..
Uses …
Application
Business
Information
Services …
Uses
Department
Member
of
Service
Application*
Data Artifact
Uses …
Accesses
“Logical” Enterprise System Boundary **
  The Enterprise Architecture addresses processes, services, and applications, all of which are implemented by the Technical Architecture, but without directly addressing the relationships among functions, HW, SW, and people that are addressed in the Technical Architecture.
Process is an ordered set of Functions
The “Enterprise Architecture”, in actuality, is implemented by the Technical Architecture
“Actors” are People who have assigned identities and roles in a real system.
The “Technical Architecture” implements the systems, services, and processes.
Supports the Enterprise
** The technical aspects of the “Enterprise System” may not be defined as part of the Enterprise Architecture. It may stop at the Service, Application, and Data level.

## Slide 54: Changes for SC14 Perspectives/Viewpoints
  Functional, Enterprise, Physical and Operational: Physical has Hardware and Software Development as sub-viewpoints
  From a non-exhaustive list including:
  Functional Viewpoint: The identification of various abstract functions and their allocation to space domain physical objects (Note: adopt CCSDS RASDS Viewpoint)
  Connectivity Viewpoint: How space domain physical objects are deployed and are connected for communications (RF, optical, cabling) (Note: Adopt CCSDS RASDS Viewpoint)
  Enterprise Viewpoint: How organizations are structured to produce & operate space domain objects, requirements and agreements, governance including laws, regulations, policy, and industry guidance or rules for other Viewpoints
  Physical (Hardware) Viewpoint: How space domain physical objects are deployed and connected from a physical / structural perspective (attachment, mating, umbilicals) (Note: Adapted from CCSDS RASDS Connectivity Viewpoint)
  Operational Viewpoint: How space domain systems objects are operated, tasks, procedures & processes. This Viewpoint also includes end-of-life disposal. (Note: new CCSDS RASDS Viewpoint)
  Communications Viewpoint: How space domain physical and software objects communicate, protocols and end-to-end views (Note: adopt CCSDS RASDS Viewpoint)
  Hardware Development Viewpoint: The development and V&V processes for space domain physical objects
  Software Development Viewpoint: The development and V&V processes for space domain software and firmware objects (Note: uses new CCSDS RASDS Operational/ Process Viewpoints)
  Information Viewpoint: This Viewpoint includes information and data definitions, data structures and relationships, best practices, or a library of Voluntary Consensus Standards. (Note: adopt CCSDS RASDS Viewpoint)

## Slide 55
Proposed RASDS++ Extensions
(including TC20 / SC 14 Joint Effort)
New Service Viewpoint
  Already introduced in CCSDS SCCS-ARD/ADD and ASL
  Covers system service interfaces and interface bindings
  Possibly leverage DODAF Svc’s or other service models
New Operational Viewpoint
  Add support for organizational tasks, activities, processes, procedures, and related behavior
  Effectively extends existing Enterprise Viewpoint, uses Systems
  Possibly leverage DODAF OV’s or other process models
Adapted Physical (Connectivity) viewpoint
  Leverage existing Connectivity Viewpoint (Nodes & Connections) to cover all sorts of physical & energetic aspects, using Nodes & Connections as starting point
  Add new aspects for physical elements (structures, articulation, power, thermal views, propulsion, electro-magnetic) perhaps each with their own View attributes

## Slide 56: Services Viewpoint - New
The Services Viewpoint focuses on the exposed services, formalized functions and interfaces, offered by a space system. It describes the interfaces of systems entities (hardware, software, people, and/or procedures), how to request and provide services, and their operations and interface binding signatures.
Stakeholder Concerns:
  The services provided by the system (H/W, SW, people);
  The interfaces, access points, and protocols for the system;
  The requirements and constraints on the services;
  The required and provided data for the services;
  Any contractual arrangements or agreements for services.
Service Objects:
  Types: Service types, both formal and informal (systems, people, software, etc), data types, and Resources (access to elements having service roles);
  Attributes: service name, type, operations, point of contact, interfaces, interface binding signature, and data, interaction modes, policies, constraints;
Domains (boundaries of responsibility or ownership);
Relationships (ownership, membership, participation, roles, contractual);
Information (defined instances of services, functions, and data specifications, along with documents, agreements, contracts, policies, requirements, objectives, goals, scenarios, membership lists, where formal specifications of all of the data to be exchanged are found in Information Views).

## Slide 57: ASL-style Services Viewpoint Example: Mission Control Service Table and correspondences
Monitoring and Control
M&C
Node A
Function A (Provider)
Message Abstraction
Service Layer
Technology Binding
Transport Protocol
Transfer Protocol
Link Layer
Services Viewpoint Table
Function, Operation, Data
Service View:
Service
Description
Communications
view:
Service Interface
Binding Signature
Information
View:
Information Object
Description

## Slide 58: RASDS Service Protocol Representation
Service Protocol peer
Service Protocol
Service Protocol PDUs
(logical flow)
Service PDUs may be simplex or bi-directional
Service Protocol behavior (may be described by state machine or other)
Proto
Svc
Svc
Svc
Unspecified Status (typically used for unknown protocols)
Published CCSDS / SC14 Standard (Blue or Magenta Book)
[Future]: CCSDS / SC14 Standard Under Development
[Prospective]: Proposed CCSDS / SC14 Standard (Green Book – future road map)
No CCSDS / SC14 Standard Identified
Svc
Standardisation Status (if required):
Protocol Layer n
Service Provided Protocol Interface (Service SAP)
Service Required Interface (of comm protocol SAP)
ISO /IEC 7498 Basic Reference Model (BRM) treats all of this as “Application Layer”. Server, web/cloud, or virtualized deployments fit this same pattern.
Service protocol must have defined behavior, PDUs, and required / provided interfaces. Behavior may be defined in a state machine, state table, or narrative form. Usually only defines behavior of sending side, but may define both ends.
Service Protocol may be built upon a standard protocol such as HTTP/REST, or a protocol like AMS, or accessed via a defined API with a bespoke protocol. Underlying protocol stacks follow normal Communication View rules.
Services may use externally supplied Authentication mechanisms. They may also rely upon security mechanisms (encryption, authentication of data payloads) or security in underlying layers.
physical flow
Protocol Layer n peer
Flow direction arrows (optional)
Reflect on how this pattern can be used to describe Message Bus, Web or Cloud, or AMS Service types
Service User App
Authentication
Protocol Stack
(multiple layers)
Svc Access Authentication (optional)
Notes: ASL Fig 3-6, trim headers & footers

## Slide 59: Relationship of Services to Message Bus, Web or Cloud, or Message Protocols
A service has four properties according to one of many definitions of SOA (Definitions taken from https://en.wikipedia.org/wiki/Service-oriented_architecture):
  It logically represents a business activity with a specified outcome.
  It is self-contained (not well defined).
  It is a black box for its consumers, meaning the consumer does not have to be aware of the service's inner workings.
  It may consist of other underlying services.
The CCSDS use of “Service” is consistent with these definitions
From a protocol / interface signature perspective services may be deployed in many different ways, built upon different underlying protocol stacks: message bus, web services, “cloud”, or other messaging protocols.
  Message Bus: Typically a bespoke protocol implementation, possibly in an on-board context, or using something like JMS. Often uses an API to hide implementation details. Often does not comply with interoperable specs but may be layered on underlying transport/network layer like TCP/IP or a link layer.
  Web or Cloud: Typically use HTTP/REST or related protocols on top of a network/transport layer. Server may be private, or local data center, or “cloud” deployment. Actually End-to-End protocol stack may involve intermediate caching systems for performance.
  Message protocols: Often use an interoperable message protocol spec like AMS and layer upon TCP/IP or DTN network layer.
Services come in many different deployment “flavors”, including: fat client, thin client, browser “app”, virtualized, SaaS, PaaS, IaaS, … All use one flavor or another of application and underlying comm protocol stacks.

## Slide 60: Operations Viewpoint - New
The Operations Viewpoint …
Stakeholder Concerns:
  The operations enabled using the system;
  The activities carried out using the system;
  The requirements on operations and activities (from Enterprise);
  The constraints on operations and activities (from Enterprise);
  How these support enterprise capabilities (from Enterprise);
  How these utilize systems capabilities (from Connectivity/Deployment); .
Operations Objects:
  Types: Capabilities (), Tasks, Processes (), Activities (), Scenarios (), Resources (systems, people, software, etc) having operational roles, data types;
  Attributes: names, types, flows, relationships, requirements, interaction modes, policies, constraints;
Domains: boundaries of responsibility or ownership, related to org/team;
Relationships (implemented by, executed by, satisfies, provides);
Information (defined instances of requirements, plans, processes, resources, objectives, goals, scenarios, where formal specifications of the data to be exchanged are found in the Information Viewpoint).

## Slide 61
Operations Object
Operations Viewpoint
(Abstract Operations Object Representation)
Attributes
Type (task, activity, process)
Properties
Products
Performance constraints
External Interfaces:
How Products are supplied to and requests are made of other Operations Objects
Management Interfaces:
How operations are configured,
controlled, and reported upon
Service Interfaces:
How operations tasks are requested by other Organization or Operations Objects
Concerns:
Issues
Resources requirements
Constraints

## Slide 62: Operational Viewpoint Questions
What are really “Operations Objects”?
  Processes
  Activities
  Tasks
What is the best “Operations Objects” representation?
  Use UML Activity diagram style
  May optionally use something like BPMN as well
What are swimlanes associated with (optional object type references)?
  Function groups
  Systems (sub-systems)
  Organizations/teams

## Slide 63: RASDS Operations View Representation
DATA
Logical Link: Node to Node interface
Domain Boundary
(optional)
Organization Object
(Org, Project, Business)
Denotes a specific Organization (org, project, business), may have embedded components
Denotes a function an organization carries out (optional, see Functional Viewpoint)
Denotes a Logical Link (flow of some sort) between two Organizations
Denotes an information object flow (optional, allows data to be characterized, see Information Viewpoint)
Denotes an organization / domain boundary (ownership / responsibility)
Specific and Generic Data Types and Containment:
Organizations (Agency, Project, Business) will explicitly connect via a Logical Link. May show the organization domain of control or ownership.
May show allocation of Functions that organization carries out (tied by correspondence to the Functional View where they are defined).
May explicitly identify the information objects exchanged between organizations (tied by correspondence to the Information View where they are defined).
Org A
Org B
Function A
Function B
Sub-Org B1
DATA
Information Object
(optional)
Create similar style diagram, but for the Operations model elements … whatever they are
Notes: ASL Fig 3-4, trim headers & footers

## Slide 64: Operational Viewpoint Selected Definitions of Terms
For the Operational Viewpoint we need a self-consistent set of terms and associated definitions.
  Process:
    “set of interrelated or interacting activities which transforms inputs into outputs” NIST
  Activity:
    “Set of cohesive tasks of a process.” NIST
  Procedure:
    “An ordered set of tasks for performing some action.” Wikipedia
    Std Operations Procedure - A set of instructions used to describe a process or procedure that performs an explicit task or explicit reaction to a given event.” NIST
  Task:
    “A Task is a specific defined piece of work that, combined with other identified Tasks, composes the work in a specific specialty area or work role.” NIST
  Action:
    “An action is something that happens within an object, either with or without participation of another object. An interaction is an action performed by an object with participation of another object or with its environment. “ RASDS
  Product:
    “Result of a process. Note: A system as a “product” is what is delivered by systems engineering.” NIST
Process
Activity
(Std Ops)
Procedure
Task
Action
Has 1 .. Inter-related
Has cohesive set of 1 ..
Ordered set of 1 ..
Performs …
Product
Produces
Work
Is …
Systems
Object
Occurs within …
Described by …

## Slide 65: Temporal Aspects of Operational Viewpoint
The Operational Viewpoint may describe any of the following:
  Activity, Procedure and Task all may have stated temporal aspects
    May have start time, stop time, or duration specified
    May have both planning views and actual “as executed” views
  Action:
    An Action may be instantaneous or have some finite duration
    An Action may have both planning estimates and actual “as executed” observations
  Event:
    “Any observable system or natural occurrence.” NIST (modified)
    “The fundamental entity of observed physical reality represented by a point designated by three coordinates of place and one of time in the space-time continuum postulated by the theory of relativity”, Merriam Webster
  Sequence of Events (SOE):
    “a number of events or activities that come one after another in a particular order”
    “the predicted order of events during spacecraft operations”, also
    “the observed order of events during spacecraft operations”
Process
Activity
(Std Ops)
Procedure
Task
Action
Has 1 .. Inter-related with start & stop times.
Has cohesive set of 1 .. with start & stop times.
Ordered set of 1 .. with start & stop times.
Performs … has duration
Product
Produces
Work
Is …
Systems
Object
Occurs within …
Described by …

## Slide 66: Relationships between Functional and Operational views
Functional View
  Shows Functions (and associated Functional Group using color coding)
  Shows Provided Interfaces
  Shows Data that is exchanged (defined in Information Views)
  Does not show any temporal aspects or recursion
Operational View
  Describes how to perform a process to accomplish Tasks
  Shows tasks executed on System Elements (vertical or horizontal swimlanes)
  Shows temporal ordering of flows (starting upper left in this case) between Activities (or Tasks), may show recursion
  May show timing and duration of activities (or tasks)
  Names the Data objects that are exchanged
  May show timing (start/stop or duration) or events
  May show predicted or observed sequence of events

## Slide 67: Functional Viewpoint – Telemetry & Mission Operations Functions & Service Interfaces
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 68: Operations Viewpoint – Mission Control Process Diagram (tasks & data flows)
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive service
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Science Data
    NOTE: All of these may have start time, stop time, or duration specified

## Slide 69: “Singing and Dancing” Views
Shows the relationship between related Functional and Task flows shown using a UML Activity diagram.
UML Activity diagram is better at showing temporal flows
Functional diagram is better at showing relationships, interfaces, and data source / sink behavior
Each step in the flow is marked to show the active functions

## Slide 70: Functional & Operational Diagram Tracking #1
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 71: Functional & Operational Diagram Tracking #2
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 72: Functional & Operational Diagram Tracking #3
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 73: Functional & Operational Diagram Tracking #4
Navigation & Timing
Planning & Sequencing
Maneuver Design
Data Storage and Archiving
Process Telemetry
TT&C
Command Generation
S/C & Trend Analysis
Science Planning
Science
Processing
TCM
Chan
TLM
TDM
Manage Mission Data
Uplink Generation
L0Data
Telem
CLTU
Frames
ODM
L1Data
Telem
L1Data
Telem
Meta
ProcSci
Telem
SciPlan
CorrAct
AppSeq
Cmds
Process Telemetry
Channelized data
S/C and Trend Analysis
Corrective Action
Planning & Sequencing
Approved Sequence
Uplink Generation
Uplink data
Maneuver
Design
TCM and/or Pointing Solution
Science Processing
L0 data
Science Data
Orbit
Data
Science planning
Science Activity Plan
Archive
Manage Mission Data
Sci. Planning
Planning & Seq.
Navigation
Science Data Sys.
Mission Control
Downlink Data
Command Generation
Commands
TT&C Services
Navigation
& Timing
Tracking data
L1 Data &
Metadata
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 74: Research: Operational Viewpoint Identified Definitions of Terms
For the Operational Viewpoint we need a hierarchy of terms and associated definitions. We did some research and found these (not necessarily self-consistent):
  Action:
    “An action is something that happens within an object, either with or without participation of another object. An interaction is an action performed by an object with participation of another object or with its environment. “ RASDS
  Activity:
    “Work, not specific to a single organization, operational system or individual that transforms inputs (Resources) into outputs (Resources) or changes their state.” DoDAF – modified
    “An activity is a specification of behavior described as a sequence of actions” RASDS
    “Set of cohesive tasks of a process.” NIST
    “An Activity is a generic term for work that company performs. An Activity can be atomic or non- atomic (compound). The types of Activities are: Task and Sub-Process.” BPMN
  Procedure:
    “An ordered set of tasks for performing some action.” Wikipedia
  Process:
    “A Process is an activity authorized by a Work Package in support of delivering a Component or producing a Product. “ IMCE
    “Business Process Model is a network of graphical objects, which are activities (i.e., work) and the flow controls that define their order of performance. “ BPMN
    “A logical, systematic sequence of activities, triggered by an event, producing a meaningful output.” DoDAF
    “set of interrelated or interacting activities which transforms inputs into outputs” NIST
  Product:
    “A Product is a concrete output of the design process. It may be a Component or a Document. A Product is any Element that an Authority properly supplies or produces. “ IMCE
    “Result of a process. Note: A system as a “product” is what is delivered by systems engineering.” NIST
  Task:
    “An action, activity or undertaking enabling missions, activities or functions to be performed or accomplished.” DoDAF
    “A Task is a specific defined piece of work that, combined with other identified Tasks, composes the work in a specific specialty area or work role.” NIST

## Slide 75: DRAFT Operations Meta-model (OWL) Replace / Update
Process
Activity
Procedure
Task
Action
Has 1 .. Inter-related
Has cohesive set of 1 ..
Ordered set of 1 ..
Performs …
Product
Produces
Work
Is …
Systems
Object
Occurs within …
If these are the definitions of terms and relationships, does this ontology accurately reflect them?

## Slide 76: Physical Viewpoint - New
The Physical Viewpoint describes the engineered decomposition of the space system into physical components (Nodes) that connect physically or energetically to other Nodes. The Physical Viewpoint describes the physical aspects of the space system and the external environment within which it operates, the physical connections and behavior (fixity or motion) of the nodes, and their physical composition.
Stakeholder Concerns:
  The physical elements (Nodes) that compose the system;
  The physical connections among the physical elements in the system and the structural or energetic flows and functions required to support these connections among objects in the system;
  The characterization of these different physical aspects in their own views, with tailored language for connection modalities: mechanical, electrical, thermal, electro-magnetic, gravitational, propulsive, ..;
  The selected allocation of physical functions to the nodes of the system, including their implementation choices and constraints on implementation, connections, configuration, and features imposed by the nature of the physical connections and the environment;
  The behavior and performance of elements in the system, including their capabilities, fixity or physical motion, and their interactions with the physical environment.
  The impacts and constraints on connections, energy flows, motion, ….

## Slide 77: Physical / Structural Viewpoint - New, contd
Engineering Objects (Nodes, Links, Applications):
  Nodes (hardware Engineering Objects, provide mechanical, power, thermal and other structural or physical resources, connection points, performance and other associated physical behavior):
    Types: hardware objects, composite hardware objects;
    Attributes: name, type, mass/power/orientation, location (place, trajectory, orbit), laws of motion, physical interfaces, capabilities (e.g., attachment type, fixity / motion, connection properties, etc.), allocated functions, constraints;
  Connections between Nodes (associated physical flows, behaviors, and properties);
    Types: connectors / weldments / mating surfaces, joints, waveguides, heat pipes, cables, free-space radiation, …
    Attributes: name, type, end-points (connected nodes), physical interfaces, performance (e.g., capacity, flows, range of motion), constraints, environmental effects, etc.);
Relationships (composition, interfaces/connections, constraints, configurations, allocation);
  Environment (physical environs, physical forces [gravity, electromagnetic, radiation, and others], physical interactions and effects);
  Flows (defined representations of energetic flows that are exchanged among Engineering Objects, where formal descriptions of flows are found in the Information Viewpoint).
NOTE – Physical Nodes and Connections in any given space system may include many more aspects and many more attributes than those shown here. The Data Communications aspects of Nodes and Links are covered in the Connectivity Viewpoint.

## Slide 78
Physical / Structural Viewpoint - Physical Object
(Hardware Component Representation)
Attributes:
Name/identifier
Address
Composition (engineering objects)
Physical attributes (mass, power, moment of inertia, thermal)
Distribution / frame of reference
Sub-nodes
Connection types (flows, energetic, structural,…)
Physical environment
Configuration
Constraints
External Interfaces:
Physical Connections
to other Components
Management Interfaces:
How Components are configured,
controlled, and reported upon
Service Interfaces:
Physical Connections
from other Components
Physical Component
Notes:
Different Connection types will be treated as different aspects of the Nodes.
They may require different descriptors and attributes for the different flows and Connections.
Physical Environment
Laws of Motion
Other energetic inputs, gravity, Solar, radiation,…

## Slide 79: RASDS Physical View Representation
Flow
Physical Link: Node to Node connection
Service Provider
(provider, optional)
Service Consumer
(consumer, optional)
Physical Connection *
Denotes a specific Node (physical component), may have embedded components
Denotes an implementation of a defined function, may be software or hardware (optional, see Functional Viewpoint)
Denotes a Physical Link (Connector of some sort) between two Nodes
Denotes a physical interface (optional, allows interface type to be characterized)
Not shown are Information Objects describing these interfaces or connectors which may be described in the Information Viewpoint and referenced by correspondence
Specific and Generic Object Types and Containment:
Related to the Connectivity Viewpoint, but focus here is on physical characterization, connections and energetic flow, not data.
Nodes (Components) will explicitly connect via some Physical Link. Nodes will have mass, power, thermal, and other properties. A Node may explicitly define a physical interface, but this is not required.
Physical connection (represents energetic constraint). This may be dynamic or static, structural / rigid, flexible, or other energetic (electro-magnetic, thrust, gravitational, thermal radiation).
May show allocation of implemented Functions, in hardware (a sub-node) tied by correspondence to the Functional View where they are defined.
May explicitly identify the flows exchanged by the objects using the link (defined in these views).
May explicitly identify the physical interface or connection type.
Node A
Node B
Function A
Function B
Sub-Node B1
Connection
Energy Flow
(0..n, optional)
Physical I/Fs *
(compatibility, optional)
*
Notes: ASL Fig 3-4, trim headers & footers

## Slide 80: RASDS Physical View Simple Example
This diagram represents connection for on-orbit servicing using structural conduit and fluid flow information.
Servicing Spacecraft
Spacecraft
Fluid Flow
Conduit described in spacecraft manifest
Fluid Tanks
Fluid Storage & Delivery
Fluid Pump
Dynamics of Fluid Flow between elements
Conduit
Physical interface of Conduit to spacecraft
Physical Link: Servicing Spacecraft to “Client” connection

## Slide 81: Physical Viewpoint Ontology

## Slide 82: Physical Viewpoint Ontology
Concern
Aspect
Service
Node
Constrains
Manages Concern
Provides
Interface
System
Required Interface
Provided Interface
Describes
Has
Requires
Is
Is
Is
Composed of
Connects
Flow?

## Slide 83: Physical Viewpoint: Some Aspects
Concern | Aspect | Service
DeltaV | Propulsion | Linear Thrust
Temperature Range | Thermal | Heat Flow
Agility, Pointing Accuracy, Mass Expulsion Control Capacity | Attitude Control | Torque
Power Storage Capacity, Voltage Range, Power Consumption | Electrical | Amperage Supply, Electrical Load
Device Orientation, Device Articulation, Keep Out Zone, Field of View | Structural | Mounting, Articulation Control

## Slide 84
Physical / Structural Viewpoint - Component / Connector Examples
Structural
  Components (S/C bus, physical link, arm/articulation, structural attributes of other components)
  Connectors (joint, bolt (incl explosive), weld)
Power
  Components (solar panel, battery, RTG, switches, power attributes of other components)
  Connectors (power bus, rotational power connectors)
Thermal
  Components (cooler, heater, thermal attributes of other components)
  Connectors (heat pipe, duct, free space radiation)
Propulsion
  Components (motor, wheel, thruster, gyro)
  Connectors (contact patch, gravity, radiation pressure)
Notes: 84

## Slide 85: Physical / Structural View
Command &
Data Handling
Computer
ACS
Computer
S/C Bus
Physical / Structural Concerns:
  Physical connection
  Mass / Power / Thermal
  Physical Environment
  Behaviors
  Constraints
  Configuration
SPACECRAFT
Spacecraft
Transceiver
Science
Instrument
Power
Subsystem

## Slide 86: Comments on Physical / Structural View (and other Physical Views)
Physical / Structural view can be directly related to the Connectivity Views
  Same sets of Nodes, different Connector types, different flows (energetic), different attributes
  The same representation may be used (for crude mechanical drawings)
  The Mechanical Engineering world has its own preferred representations and specialized analyses
Physical / Thermal & Power views may also be similarly crudely modeled
  Nodes are the same, but different attributes are relevant
  Value of these specific representations, except as a way to relate the different views seems questionable
Physical / Propulsion, Magnetic, Gravitational and other views also require different views of these energetic processes

## Slide 87: Proposal for Physical / Structural View (and other Physical Views)
Architecture diagrams that relate Connectivity view objects, essential for communications & protocols, can only weakly support engineering and other detailed Physical views
  Recommend using a common set of simplified 3-D architecture diagrams, where useful, to tie these viewpoints together logically
  Expect to use the engineering domain specific representations that are able to support detailed analyses
    Identify that there are some engineering disciplines that are now coupling various physical aspects, such as thermal and electrical flow from spot welding, or finite element analysis that connects structural, thermal, and other flows.
  Recommend using a single, common, underlying information model, with suitable attribute sets, to model these elements and tie these different aspects together
    Consider use of OML / IMCE approaches

## Slide 88: RASDS Object Hierarchies
In many systems architecture contexts there are different objects, and different hierarchies of objects, that are needed:
  Enterprise: mission phases, org structures, requirements decomposition “levels”
  Functions: high level “functional groups”, “complex functions”, “atomic functions”
  System Elements: systems, subsystems, elements, devices, components …
RASDS cannot create any definitive hierarchies, but it can provide examples and descriptions of how to do this.
Intro notions of Fred’s SC14 hierarchies

## Slide 89: UML System Decomposition Profile
The following is just one possible example of how to do this:
  Created using SysML
  Defines the <<stereotype>> for the top level system elements
  Defines names for successive levels of decomposition of system elements, down to Subsystem
  Splits below that level into a hardware hierarchy (HW) and a software hierarchy (SW)
  Any other hierarchy of terms and levels may be defined, as driven by the project. Just use them consistently.
  Use the same basic process to create other decomposition hierarchies, like SE or RQ Levels.
This example also defines a color palette for different groupings of function types, i.e. kinds of functions, or different ownership.

## Slide 90: SysML Example of System Decomposition

## Slide 91: Mapping RASDS Into SysML
Introduce general approach of mapping RASDS PPT presentation style to SysML / MBSE
  Create Profile
  List diagram type to Viewpoint mapping approaches
Use the following set of “PPT hacked” example diagrams?
Or use example diagrams from Shames, Sarrel, Friedenthal paper?

## Slide 92: Mapping RASDS into SysML
No simple one for one mapping
RASDS uses Viewpoints to expose different concerns of a single system
SysML uses specific diagrams to capture system structure, behavior, parameters and requirements
Several SysML diagrams, focused on different object classes, may be usefully applied to any given RASDS Viewpoint
Extended SysML Views may be used to define the relationships between Viewpoints and Diagrams
SysML will support more accurate fine grained modeling of structure, relationships and behavior than was expected of RASDS

## Slide 93: Mapping RASDS into SysML
Enterprise
  Organizational component & collaboration diagrams
  Use case, interaction overview diagrams
  Requirements & constraints for rules, policies & agreements
Connectivity
  Physical component, composition, collaboration & class diagrams
  Parametric diagram for physical link characterization
Functional
  Logical component, collaboration & class diagrams
  Activity, state chart, parametric, & timing diagrams
Informational
  Information class & parametric diagrams
Communication
  Protocol component & collaboration diagrams
  State machine, sequence, activity & timing diagrams

## Slide 94: Enterprise View Using SysML Use Case Diagram
Preliminary
<<usage>>
Enterprise: Use Case
Mars Exploration
Program Federation
Mission A
Agency ABC
GTN B
Mission Q
Instr C
Agency QRS
Instrument
Integration
Operations
Contract
<<includes>>
<<includes>>
<<includes>>
<<includes>>
<<includes>>
<<includes>>
<<extends>>
Cross Support
Agreement
<<extends>>
<<extends>>
Service Operations
Team
<<Secondary>>
Science
Team
<<primary>>
Science
Team
<<primary>>
Instrument
Team
<<Secondary>>
Relay
Service A
<<extends>>
TT&C
Service B
Mission
Operations
Team
<<Primary>>

## Slide 95: Connectivity View (Nodes & Links) Using SysML Components (Spacecraft)
Preliminary
Derived from: SysML Partners
sciInstr : scienceInstrument
CDH : CmdDataHandlingSystem
dl : DownLink
Spacecraft
s :
Sensor
ic :
InstrControl
ap : Aperture
ap: Mechanical
ObsFin
Port
DataDonePort
dm :
DataManager
ecu : Execution
Control Unit
oc :
ObsControl
InstrCmnd
Port
TelemPort
TakeObs
SensorData
RFAntenna
ul : UpLink
TeleCmndPort
CmndIn
Port

## Slide 96: Connectivity View (Nodes & Links) Using SysML Components (MOS & TT&C Systems)
TT&C : TrackTelemCommand
MOS : MissionOpsSystem
TM :
Telemetry
TC :
Telecommand
Pt : Pointing
Ant: Mechanical
TelemDonePort
dm :
DataManager
MOP : Mission
OpsPlanning
SC :
SendCmnd
Cmnd Port
Telem
Port
PointingData
TelemData
RF
Ant
Tele
Cmnd
Port
ObsReq
Port
ul : UpLink
dl : DownLink
CmndData
Re
Trans
Port
DL
Port
UL
Port

## Slide 97: Connectivity View (Composition) Using SysML Components
Global structure inherited by each kind of Spacecraft …
… and constrained for each kind
Preliminary
TT&C : TrackTelemCommand
MOS : MissionOpsSystem
TM :
Telemetry
TC :
Telecommand
Pt :
Pointing
Ant:
Mechanical
TelemDone
Port
dm :
DataManager
MOP : Mission
OpsPlanning
SC :
SendCmnd
Cmnd Port
Telem
Port
Pointing
Data
TelemData
RF
Ant
Tele
Cmnd
Port
ObsReq
Port
ul : UpLink
dl : DownLink
CmndData
Re
Trans
Port
DL
Port
UL
Port
sciInstr : scienceInstrument
CDH : CmdDataHandlingSystem
dl : DownLink
Spacecraft
S :
Sensor
IC :
InstrControl
Ap :
Aperture
AP:
Mechanical
ObsFin
Port
DataDone
Port
dm :
DataManager
ecu : Execution
Control Unit
oc :
ObsControl
InstrCmnd
Port
TelemPort
Take
Obs
SensorData
RFAnt
ul : UpLink
TeleCmndPort
Cmndin
Port
RF: link [X-band]
RF: link [KaBand]

## Slide 98: Functional View Using SysML Activity Diagram
Preliminary
Showing component allocations (optional)
Spacecraft
Ground System
Instrument
S/C Control
Mission Ops
Prepare
Cmnd
Accept
Data
Finish
ObsSeq
Take Obs
plannedObs
Instr
Cmnd
Plan
ObsSeq
TT&C Network
Xmit
Cmnd
Recv
Data
Transmit
Data
Store
Data
Execute
Cmnd
retransReq
readyCmnd
Recv
Cmnd
obsComplete
retransDataReq

## Slide 99: Informational View Using SysML Class Diagram
Preliminary
Reusable, refinable information structure:
<<info obj>>
InstrCmndFile
1..*
1
describes
Global representation inherited by each kind of Information Object
Derived from: SysML Partners
<<data obj>>
InstrCmndList
<<data obj>>
InstrCmnd
1..*
<<metadata obj>>
InstrCmndMetaData
<<metadata obj>>
InstrCmndSemantics
<<metadata obj>>
InstrCmndStructure

## Slide 100: Communication View (Protocol Objects) Using SysML Component Diagram
Preliminary
Derived from: SysML Partners
TC :
TeleCmnd
<<protocol>>
LL: LinkLayer
SC : SpaceCraft
CmndData:RF
<<protocol>>
PL: PhysLayer
<<protocol>>
IP: InternetLayer
<<protocol>>
TP: TransportLayer
CmndIn
Port
SC :
SendCmnd
<<protocol>>
LL: LinkLayer
MOS : MissionOpsSystem
<<protocol>>
PL: PhysLayer
<<protocol>>
IP: InternetLayer
<<protocol>>
TP: TransportLayer
Cmnd
Port
ECU : Execution
Control Unit
MOP : Mission
OpsPlanning
RF: link [Xband]
<<controls>>

## Slide 101: Communication View Using SysML State Machine Diagram
Preliminary
<<protocol>>
TP: TransportLayer
Derived from: SysML Partners
Idle
Waiting
Sending
evSend /
transmitCount=0
tm(Wait Time)
[transmitCount<LIMIT]
evDoneSend /
++transmitCount
evACK[isValid]
tm(Wait Time)
Throw(“Unable to Send”)
Protocol specifications inherited by each instance of Protocol Objects

## Slide 102
CCSDS / SC14 - RASDS update project
Proposed RASDS update tasks
  Update RASDS, add new viewpoints
    Integrate ASL & SCCS ADD approaches to refine framework
    Work in collaboration with TC20/SC14 SE team to extend framework
    Incorporate published diagrams from ASL and SCCS where appropriate
    Update security view sections, as needed
    => Is a new Engineering / Process Viewpoint needed to deal with SC14 V&V and process considerations? No, leave for ISO 15288 and agency stds.
  Add annex with MBSE / SysML representations
    May use SysML representations or just adopt a uniform set of OWL / ontology diagrams documenting the concepts for each viewpoint
    The methodology is the same for either approach, but the representation differs
    Incorporate representation & figures from published MBSE papers
  With TC20/SC14 refine and extend existing CCSDS Glossary
    Leverage SANA on-line repository for human and machine access
    Add SC14 specific terms where required
    ECSS interests may also be considered

## Slide 103: BACKUP

## Slide 104: Formalized Relationships between Enterprise & Technical Architecture (Enterprise Viewpoint & System Architecture Viewpoint objects)
System **
Hardware
Software
People
Procedures
Composed of 1..
Environment
Affects
Function
Implement 1..
Function offers 0.. Service Interfaces
Process
Action
Task
* An “Application” is Software, a set of functions deployed (somehow) on a server as part of a system, with defined interfaces
(Business) Process
Capability
Actor
Performed
by
Business
Possess set of 1..
Implemented by 1..
Uses …
Application
Business
Information
Services …
Uses
Department
Member
of
Service
Application*
Data Artifact
Uses …
Accesses
“Logical” Enterprise System Boundary **
  The Enterprise Architecture addresses processes, services, and applications, all of which are implemented by the Technical Architecture, but without directly addressing the relationships among functions, HW, SW, and people that are addressed in the Technical Architecture.
Process is an ordered set of Functions
The “Enterprise Architecture”, in actuality, is implemented by the Technical Architecture
“Actors” are People who have assigned identities and roles in a real system.
The “Technical Architecture” implements the systems, services, and processes.
Supports the Enterprise

## Slide 105: Connectivity View Nodes & Links
Mission Planning
Computer
Spacecraft
Control
Computer
Space Link
Internet
Ground
Tracking
Station
Command &
Data Handling
Computer
ACS
Computer
S/C Bus
Science
Instrument
Spacecraft
Transceiver
Connectivity Concerns:
  Distribution
  Communication
  Physical Environment
  Behaviors
  Constraints
  Configuration
SPACECRAFT

## Slide 106: Meta-models: UML relationships among meta-models, user models, and instances

## Slide 107: ASL Connectivity Example: Physical Model (SSI) With representative Functional Deployment
Relay Spacecraft
Lander/Rover
or Habitat
ESLT
TT&C
Spacecraft
NAVT
MCS
DSA
MPS
NAVT
MCS
DSA
MPS
NAVT
MCS
DSA
MPS
MOC
DPC
DAC
POC
PI/User
SCM
NSC
OPS
NAVT
MCS
DSA
MPS
OPS
NAVT
MCS
DSA
MPS
Mission Data Processing
User Support
Spacecraft
Development &
Maintenance
NAVT
DSA
OPS
NAVT
DSA
MPS
Notes: ASL Fig 8-4, trim headers & footers

## Slide 108: ASL Example: Mission Control functional decomposition
Navigation & Timing
Planning & Scheduling
Navigation Interface
Data Storage and Archiving
Operations Preparation
TT&C
Automation
On-board Configuration Management
Monitoring and Control
M&C
ODM
PRM
ADM
NEM
M&C
AUT
M&C
OBSM
OBPM
OBSM
OBPM
APD
SDB
M&C
User Support
Mission Data Processing
Spacecraft Development & Maintenance
M&C
M&C
AUT
OBSM
OBPM
AUT
TCM
OBSW
APD
M&C
SC-CSTS
MD-CSTS
Notes: ASL Figure 4-4, trim top & bottom
M&C: Monitoring & Control
AUT: Automation
OSM: On-board Software Management
OPM: On-board Procedure Management

## Slide 109: Alternate Functional & Protocol Diagram (for a Single Process)
put
get
MIB
Outbound Link PDU
Inbound Link PDU
put
get
database
Outbound App PDU
Inbound App PDU
application
protocol
application
encryption
service
link protocol
Protocol SAP

## Slide 110: DoDAF Operational Viewpoint (for consideration …)
DoDAF-described Models in the Operational Viewpoint describe the tasks and activities, operational elements, and resource flow exchanges required to conduct operations. A pure operational model is materiel independent. However, operations and their relationships may be influenced by new technologies, such as collaboration technology, where process improvements are in practice before policy can reflect the new procedures.
Use of Operational Viewpoint DoDAF-described Models should improve the quality of requirements definitions by:
  Explicitly tying user requirements to strategic-level capability needs, enabling early agreement to be reached on the capability boundary.
  Providing a validated reference model of the business/operations against which the completeness of a requirements definition can be assessed (visualization aids validation).
  Explicitly linking functional requirements to a validated model of the business or operations activities.
  Capturing information-related requirements (not just Information Exchange Requirements [IERs]) in a coherent manner and in a way that really reflects the user collaboration needs.
  Providing a basis for test scenarios linked to user requirements.
  Capturing the activities for Process Engineering or Process Re-engineering.

## Slide 111: DoDAF Operational Viewpoint, contd Possible Model Views
Model | Description
OV-1: High-Level Operational Concept Graphic | The high-level graphical/textual description of the operational concept.
OV-2: Operational Resource Flow Description | A description of the Resource Flows exchanged between operational activities.
OV-3: Operational Resource Flow Matrix | A description of the resources exchanged and the relevant attributes of the exchanges.
OV-4: Organizational Relationships Chart | The organizational context, role or other relationships among organizations.
OV-5a: Operational Activity Decomposition Tree | The capabilities and activities (operational activities) organized in a hierarchal structure.
OV-5b: Operational Activity Model | The context of capabilities and activities (operational activities) and their relationships among activities, inputs, and outputs; Additional data can show cost, performers or other pertinent information.
OV-6a: Operational Rules Model | One of three models used to describe activity (operational activity). It identifies business rules that constrain operations.
OV-6b: State Transition Description | One of three models used to describe operational activity (activity). It identifies business process (activity) responses to events (usually, very short activities).
OV-6c: Event-Trace Description | One of three models used to describe activity (operational activity). It traces actions in a scenario or sequence of events.
Operational Model Descriptions

## Slide 112
RASDS background – from the
IEEE-1471-2000 conceptual framework…
We formalize and adapt this generic conceptual
framework into one for
suitable for space data system design
Notes: 112

## Slide 113: SAWG Observations on Terminology
Some of the terms used in CCSDS documents are not even in the CCSDS Glossary
We only have accurate information models and schema for a small sub-set of the terms in use
Some terminology is defined in multiple different standards, and this is where issues arise
Lack of consistent terminology makes automation and cross use of terms much more difficult
Some terminology is in isolated domains and not an issue
Multiple inconsistencies in use of terminology
  Collisions of usage (same word, two different meanings)
  Specializations (same word, on analysis one derived from another)
  Multiple terms used for the same things
  Internal inconsistencies in usage or definitions
  Inconsistent use of representations (lack of class diagrams)
  Inconsistent references to external standards (ISO BRM and other)
Some differences appear to be easy to resolve (reference the document/namespace), others will require more work

## Slide 114: DoDAF Services Viewpoint
The DoDAF-described Models within the Services Viewpoint describes services and their interconnections providing or supporting, DoD functions. DoD functions include both mission and business functions. The Service Models associate service resources to the operational and capability requirements. These resources support the operational activities and facilitate the exchange of information.
The relationship between architectural data elements across the Services Viewpoint to the Operational Viewpoint and Capability Viewpoint can be exemplified as services are procured and fielded to support the operations and capabilities of organizations. The structural and behavioral models in the OVs and SvcVs allow architects and stakeholders to quickly ascertain which functions are carried out by humans and which by Services for each alternative specification and so carry out trade analysis based on risk, cost, reliability, etc.
Services are not limited to internal system functions and can include Human Computer Interface (HCI) and Graphical User Interface (GUI) functions or functions that consume or produce service data to or from service functions. The external service data providers and consumers can be used to represent the human that interacts with the service.

## Slide 115: DoDAF Services Viewpoint, cont Possible Model Views
Model | Description
SvcV-1 Services Context Description | The identification of services, service items, and their interconnections.
SvcV-2 Services Resource Flow Description | A description of Resource Flows exchanged between services.
SvcV-3a Systems-Services Matrix | The relationships among or between systems and services in a given Architectural Description.
SvcV-3b Services-Services Matrix | The relationships among services in a given Architectural Description. It can be designed to show relationships of interest, (e.g., service-type interfaces, planned vs. existing interfaces).
SvcV-4 Services Functionality Description | The functions performed by services and the service data flows among service functions (activities). (Note: service de-composition into functions)
SvcV-5 Operational Activity to Services Traceability Matrix | A mapping of services (activities) back to operational activities (activities).
SvcV-6 Services Resource Flow Matrix | It provides details of service Resource Flow elements being exchanged between services and the attributes of that exchange. (Note: Explicitly includes security attributes)
SvcV-7 Services Measures Matrix | The measures (metrics) of Services Model elements for the appropriate timeframe(s).
SvcV-8 Services Evolution Description | The planned incremental steps toward migrating a suite of services to a more efficient suite or toward evolving current services to a future implementation.
SvcV-9 Services Technology & Skills Forecast | The emerging technologies, software/hardware products, and skills that are expected to be available in a given set of time frames and that will affect future service development.
SvcV-10a Services Rules Model | One of three models used to describe service functionality. It identifies constraints that are imposed on systems functionality due to some aspect of system design or implementation. (Note: includes components, interfaces, links, I/O, and state)
SvcV-10b Services State Transition Description | One of three models used to describe service functionality. It identifies responses of services to events.
SvcV-10c Services Event-Trace Description | One of three models used to describe service functionality. It identifies service-specific refinements of critical sequences of events described in the Operational Viewpoint.
Service Model Descriptions