## Slide 1
CCSDS System Engineering
Area (SEA): System Architecture WG (SAWG)
RASDS++ Security Views
Edited for: Mark Winstead - coauthor NIST SP 800-160 Vol 1 Rev1
Peter Shames, SEA AD
Fred Slane, Ramon Krosley, Costin Radulescu, Christian Stangl
24 May 2023

## Slide 2: Reference Architecture for Space Data Systems (RASDS)
Reference Architecture for Space Data Systems (RASDS) CCSDS 311.0-M-1 (ISO 13537) was published in Sept 2008
  RASDS included five viewpoints: Enterprise, Functional, Connectivity (nodes & links), Protocols, and Information
  RASDS++ is now being revised to add Services, Physical (components & connectors), and Operations, and to augment Enterprise
RASDS++ aligns with ISO 42010-2022 and also ISO 10746 (RM-ODP)
  Viewpoints, view, correspondence, and related terminology and concepts are direct from ISO 42010
  The initial set of viewpoints were derived from ISO 10746, with adaptations to include protocol stacks and nodes/links suitable for systems that operate terrestrially and in deep space
This presentation introduces the RASDS++ viewpoints, concepts, and terminology
  It adds a focus on the security aspects of a system, or system of systems, architecture
  Each viewpoint is used to address a specific set of security topics in the context of an entire systems architecture
  The materials have been condensed to focus on the security aspects

## Slide 3: ISO 42010-2022 Architecture Definitions
Architecture Viewpoint
  Set of conventions for the creation, interpretation, and use of an architecture view to frame one or more concerns
  Note: a viewpoint is a frame of reference for the concerns determined by the architect as relevant to the purpose of the architecture description.
  Note: The conventions of an architecture viewpoint are included in a specification of this viewpoint. In some communities and architecture frameworks, “view specification” is used to mean the same thing.
Architecture View
  A Information item, governed by an architecture viewpoint, comprising a portion of an architecture description
  Note: An architecture view could include contextual schema, conceptual, logical and physical data models, data dictionary and documents as view components, and entities, relations and attributes as AD elements.
Concern
  Matter of relevance or importance to a stakeholder regarding an entity of interest, or some matter related to that entity.
  Note: Stated concerns are useful when relevant to the purpose of the architecting effort and refer to specific rather than categorical difficulties, problems, or requirements.
Correspondence
  Identified or named relationship between two or more architecture description elements
  Note: A function such that for elements in one viewpoint there is a related element in another viewpoint; the condition of being in conformity from elements in one viewpoint to elements in another.
  Note: Correspondences are used to express a wide range of relationships, such as equivalence, composition, refinement, consistency, traceability, dependency, constraint, satisfaction, and obligation.

## Slide 4
RASDS++ System Architecture Model
Objectives
RASDS++ provides a modeling framework and methodology, a specific Space System Reference Architecture model …
  Provides clear & unambiguous viewpoints for exploring space systems architectures
  Shows relationship of design to requirements and driving scenarios
  Separates abstract design from implementation concerns in the model to maintain a degree of freedom to do trades
  Details the model & views to the level appropriate for further systems engineering, supports evolution of the design
  Enables concurrent design of spacecraft, ground systems, science operations, control systems, and their components
Notes: 4

## Slide 5
Reference Architecture for Space Data Systems
Enterprise
Business Concerns
Capabilities, Organizations, Governance
Physical
Physical Concerns
Component & Connector perspective
Functional
Computational Concerns
Functional composition
Information
Data Concerns
Relationships and transformations
Communications
Protocol Concerns
Communications stack perspective
Derived from: RM-ODP, ISO 10746
Compliant with IEEE 1471 and ISO 42010
Connectivity Derived Viewpoint
Structural Derived Viewpoint
Services
System Service Concerns
Interfaces, protocols, and data exchanged
Operations
Operations Concerns
Processes, Activities, Products
Notes: 5

## Slide 6: Revised RASDS++ (DRAFT) Top Level Object Ontology
Function
Behavior
Interfaces
Constraints
Logical structure
Connector
(Link)
Type
Protocol
Protocol stack
Standards
Enterprise
Requirements
Objectives
Governance
Use Cases
Mission
FulfilledBy
Meets
IsImplementedBy
ComposedOf
Composed Of
ComposedOf
ContainsInstances
Produces
Consumes
ConnectVia
Uses
ProvidesService
AssociatedWith
ImplementedOn
Information
Data
Metadata
Rules
Develops / Owns
Component
(Node)
Type
Attributes
(comm, power,
thermal, prop,
other)
Attachment
Calls
Environment
Physical Environs
Affects
Location
Attributes
Meta-model
(each Viewpoint)
Defines Objects
Defines Rules
Exposes Concerns
Defines Relations
Operations
Processes
Activities
Tasks
Modes/states
Scenarios
Performs
Invoke
Service
Svc Behavior
Interface Sig
Svc Constraints
Offers
Defined by
Flows
(comm, power,
thermal, prop,
other)
Defines Correspondences
Resources

## Slide 7: RASDS++ Viewpoint Specifications
Each RASDS++ Viewpoint addresses:
  Stakeholder concerns: What does the stakeholder care about (what must views address)
  Objects: The fundamental kinds of objects (functions, data, organizations, physical elements, protocols, etc)
  Relationships: The descriptions of object attributes and how they relate, including correspondences to other objects
  Representation: How objects and relationships of different types are represented in diagrams
MBSE adaptations:
  The primary work that must be done to use RASDS++ with MBSE tools is to:
    Define profiles to accurately represent the different classes of objects and relationships
    Create stereotypes that can be used consistently in the tools
    Use the profiles and methods to develop the MBSE style representations

## Slide 8: RASDS++ System Object Representations
Organizational Element
Communications Protocol
Data
Store
Data Store
Color Key for Example Diagrams (from SCCS-ARD):
User Node
Earth Routing Node
Space Routing Node
WAN Node
Application
Element Management
Network Management
Network Layer function
Link Layer function
Routing function
Forwarding function
Data Store
Physical Node
InformationObject
Physical or
Functional Connection
Logical Link
between Elements
Organizational Domain
Router
Functional Element
Link Layer User
Service Access Point
Peering
Arrangement
DATA
Service Provider
Service Consumer
Notes: ASL Fig 3-1, trim headers & footers

## Slide 9: RASDS Relationship Types (UML derived)
Inheritance
Composition
Aggregation
Association (other relationship, labelled)
Directional Association
Read as sentence with subject = start of arrow, verb = label, and object = end of arrow
Inheritance: The ability of one class (child class) to inherit the identical functionality of another class (super class), and then add new functionality of its own. E.g. super class: “round ball”, child classes: “baseball”, “soccer ball”, “basketball”, but not “football”
Composition: A special case of association that describes a relationship between a whole and its existential parts. E.g. a person, with head, arms, legs. Note that the parts cannot exist separate from the rest of the person.
Aggregation: a special type of association in which objects are assembled or configured together to create a more complex object. E.g. a car is assembled from a body, wheels, and an engine. Note that the engine can exist apart from the rest of the car
Association (other relationship, labelled): Association is a relationship between classifiers which is used to show that instances of classifiers could be either linked to each other or combined logically.
Directional Association: Associations that are navigable in only one direction. A directed association indicates that control flows from one classifier to another; for example an actor to a use case.

## Slide 10
Object
Unified Set of Object Features Representation
Core Functions
What the object
does
External Interfaces:
How external elements
are controlled
Management Interfaces:
How objects are configured
controlled, and monitored
Service Interfaces:
How services are
requested & supplied
Concerns:
Issues
Resources
Policies

## Slide 11: Example Ontology - Formalized Relationships among Terms (Functional Viewpoint example with added Correspondences)
Behavior
System
Element
Function
Processes ..
Implemented by 1.. (corr)
Data
Offers 0..
Service
Function : The set of actions or activities performed by some object to achieve a goal; the transformation of inputs to outputs that may include the creation, modification, monitoring, or destruction of elements.
Correspondence: A function such that for elements in one viewpoint there is a related element in another viewpoint; the condition of being in conformity from elements in one viewpoint to elements in another.
Has …
Composed of …
Information
Specified by .. (corr)
Service Table Entry
Specifies aspects .. (corr)
  Correspondence (corr): Colored objects shown with dashed lines are formally defined in other viewpoints and are referenced by correspondence

## Slide 12: Technical Architecture Definitions
System
  A System is a group of interacting or interrelated Elements that act according to a set of rules to form a unified whole. A System, surrounded and influenced by its environment, is described by its boundaries, structure and purpose and expressed in its functioning.
  A collection of interacting components organized to accomplish a specific function or set of functions. A System is composed of Elements, which may be any of: Hardware, Software, People, and Procedures.
Function
  A Function is the purpose for which an Element is intended. This can be an activity performed by the Element or the usage of this Element by other parts of the system.
  A Function is interpreted as a specific process, action or task that a System is able to perform.
Service
  A mechanism to enable access to a set of one or more functions of an Element, where the access is provided using a prescribed interface and is exercised consistent with constraints and policies as specified by the service description.
  A Service is an exposed interface of a Function.
Interface
  An Interface represents a set of mechanical, electrical, signal, or other properties that describe some aspect of a Element’s connection to or interaction with another Element.
  An interface is formed of the ports on two or more elements and the junction that joins them.

## Slide 13: Functional Viewpoint
The Functional Viewpoint describes the functional decomposition of the space data system into abstract objects that interact at interfaces.
Stakeholder Concerns:
  a functional decomposition of the system into objects that interact at interfaces;
  the abstract behavior of the system, its interactions and constraints.
Functional Objects (abstract set of functions, their behaviors, interfaces and configurations);
  Types: data source, data sink, data transformation, control, planning, monitoring, analysis;
  Attributes: role, name, type, behavior, interface types, data types handled, interaction modes, constraints, allocated requirements;
Logical Links (connections between Functional Objects, connected to associated logical behavior and properties);
Relationships (configuration, precedence, control and data flows, management flows, allocations);
Information (representations of data that are exchanged among Functional Objects, where formal specifications for the information objects are found (by correspondence) in the Information Viewpoint).

## Slide 14
Functional Object
Functional Viewpoint
(Abstract Functional Object Features)
Attributes
Identifier
Type
Behavior
Data
External Interfaces:
How other Functional Objects are used to support the performance of this Object
Management Interfaces:
How function is configured,
controlled, and monitored
Service Interfaces:
How services are
requested by & supplied
to other Functional Objects
Concerns:
Performance constraints
Resource requirements
Constraints

## Slide 15: Formalized Relationships among Terms (Functional Viewpoint ontology)
Behavior
System
Element
Function
Produces /
Consumes ..
Implemented by 1.. (corr)
Data
Offers 0..
Service
Has …
Composed of …
Requirement
Fulfilled by 1.. (corr)
Information
Specified by .. (corr)
Function : The set of actions or activities performed by some object to achieve a goal; the transformation of inputs to outputs that may include the creation, modification, monitoring, or destruction of elements.
Behavior: A set of actions performed by an object for some purpose.

## Slide 16: Extended RASDS Functional View Representation*
Function A
DATA
Logical Link: end-to-end interface between functions
Service Provider
(provided I/F, optional)
Service Consumer
(required I/F, optional arrowhead)
Data Object
(optional)
DATA
Denotes a specific Data Type subject to standardisation by CCSDS / SC14
Italics denotes an Abstract or Generic Data Type
Faded Colour: Data contained within another Data item (to which it is attached)
DATA
DATA
DATA
DATA
DATA
DATA
Unspecified Status (typically used for aggregated or grouped data/services)
Published CCSDS / SC14 Standard (Blue or Magenta Book)
[Future]: CCSDS / SC14 Standard Under Development
[Prospective]: Proposed CCSDS / SC14 Standard (Green Book – future road map)
No CCSDS / SC14 Standard Identified
DATA
Specific and Generic Data Types and Containment:
Standardisation Status:
* Revisions from ASL
Functional Objects are abstract representations of behavior. They may be instantiated or realized in different logical or physical constructs.
Functions may themselves be decomposed into lower level functions, shown by containment.
Different deployments or realizations of the same Functional Object may be expressed in other views and referenced by correspondence.
Functional Objects may explicitly define a service providing interface, but this is not required.
They may explicitly identify the information objects that are exchanged (tied by correspondence to the Information View where they are defined).
Sub-Function B1
Function B
Notes: ASL Fig 3-4, trim headers & footers

## Slide 17: RASDS++ Security Aspects Functional Viewpoint
Specific security functions
  Authentication
  Encryption
  Risk assessment
  Threat assessment
  Monitoring
  Identity management / ICAM
  Application management
  Network management
  etc

## Slide 18: Information Viewpoint
The Information Viewpoint focuses on the kinds of information handled by the system, the syntax and semantics of the information, and the interpretation of that information.
Stakeholder Concerns:
  the structure and semantics of information and information management in a system;
  the rules and constraints on information transformations and permanence in a system.
Information Objects (abstract definitions of information elements, structures, semantics, schema):
  Types: data, metadata, information, package, schema, model, meta-model;
  Attributes: name, type, length, structure, syntax, semantics, permanence, provenance, realized by, rules, policies;
Relationships (information object aggregates, transformations);
Constraints (type checking rules, permanence, policies).

## Slide 19
Information Object
Information Viewpoint
(Information Object Features)
Management Interfaces:
Rules (transformations, access)
Schema
Permanence
Element types
Constraints
Concerns:
Rules & Constraints
Resource requirements
Type conversion
Access / security
Core Capabilities:
Type
Identifier
Structure
Semantics
Relationships

## Slide 20: Formalized Relationships among Terms (Information Viewpoint ontology)
Representation
Function
Information
Constrained by ..
Produces / Consumes (corr)
Rules
Has 0.. (corr)
Realizations
Has …
Relationships …
  Information: Data, along with the necessary structure and syntax to allow interpretation and use of that data; may also have associated metadata, including the relationships among Data Objects, rules for their use and transformation, and policies on access.

## Slide 21: Information Representation (ASL version) (Relationships derived from UML)
Information Class B
Information Class A
Relationship
0..1
*
Optional relationship type label
Optional multiplicity specifier
Inheritance
Composition
Aggregation
Association (other relationship, labelled)
Directional Association
Relationship Types (UML derived): Read as sentence with subject = start of arrow, verb = label, and object = end of arrow
DATA
DATA
DATA
DATA
Unspecified Status (typically used for aggregated or grouped data/services)
Published CCSDS / SC14 Standard (Blue or Magenta Book)
[Future]: CCSDS / SC14 Standard Under Development
[Prospective]: Proposed CCSDS / SC14 Standard (Green Book – future road map)
No CCSDS / SC14 Standard Identified
DATA
Standardisation Status:
Information Objects are abstract representations of information and data structures. They may be referenced in many other views.
The explicit definitions of Information Objects in this Viewpoint are tied by correspondence to the Functional or other Views where they are referenced.
Information objects may themselves be decomposed into lower level objects, shown by containment or relationships.
Specific information object structures will typically be instantiated during design and realized in different forms during development.
Different instantiations or realizations of the same Information Object may occur in different deployments.
Notes: ASL Fig 3-6, trim headers & footers

## Slide 22: RASDS++ Security Aspects Information Viewpoint
Specific security information
  Keys
  Passwords
  Risk models
  Threat models
  User device database
  Identity management / ICAM
  Application database
  Network device database
  Data at rest / in transit
  etc

## Slide 23: Connectivity Viewpoint
The Connectivity Viewpoint describes the engineered decomposition of a space data system into components (nodes) that exchange data across connectors (links). The Connectivity Viewpoint describes the physical aspects of space data systems communications and the external environment within which they operate, the physical behavior (and motion) of the nodes, and their physical decomposition into communicating elements.
Stakeholder Concerns:
  The mechanisms and functions required to support distributed communications between objects in the system;
  The selected allocation of functions to the nodes of the system, including their implementation choices and constraints on implementation, connections, configuration, and operations imposed by the communication links and the environment;
  The behavior and performance of elements in the system, including their communications capabilities, physical motion, and their interactions with the physical environment.
Engineering Objects (Nodes, Links, Applications):
  Nodes (hardware Engineering Objects, provide communications, processing and other computing and data resources, ports, performance and other associated physical behavior):
    Types: hardware objects, composite hardware objects, ports;
    Attributes: name, type, location (place, trajectory, orbit), laws of motion, available resources, physical interfaces, capabilities (e.g., processor speed, throughput, bandwidth, storage capacity, aperture size, etc.), allocated functions, constraints;

## Slide 24: Connectivity Viewpoint, contd
Engineering Objects (Nodes, Links, Applications), contd:
  Links (communications connections between Nodes, associated physical behavior and properties);
    Types: space link (RF or optical), physical link (e.g., point-to-point, bus, network, copper, fiber, etc.);
    Attributes: name, type, end-points (port on node), physical interfaces, performance (e.g., throughput, bandwidth, frequency band, Round Trip Light Time (RTLT), pointing and view periods, signal attenuation, constraints, environmental effects, etc.), access and ownership;
  Applications (software Engineering Objects, behavior, and processing/resource requirements, may be layered):
    Types: software Engineering Objects, composite software Engineering Objects;
    Attributes: name, type, algorithms, implemented functions, allocation/ deployment to nodes, required resources (e.g., memory, CPU, storage), implemented interfaces (provided and required), implementation language, Operating System (OS)/framework dependencies, constraints;
Relationships (composition, interfaces, constraints, configurations, allocation);
  Environment (physical environs, physical forces [gravity and others], physical interactions and effects);
  Information correspondences (defined representations of data that are exchanged among Engineering Objects, where formal specifications of data architecture are found in the Information Viewpoint).
NOTE – Physical Nodes and Links in any given space system may include many more aspects (physical structures, connections, and flows), types (power, propulsion, thermal) and many more attributes than those shown here. The physical, structural, and energetic flow aspects of Nodes and Links are covered in the new Physical / Structural Viewpoint.

## Slide 25
Connectivity Viewpoint - Physical Object
(Node / Component Features)
Attributes:
Name/identifier
Address
Composition (engineering objects)
Performance
Distribution / frame of reference
Sub-nodes
Communication links and Ports
Physical environment
Configuration
Constraints
External Interfaces:
Communication links to other Nodes
Management Interfaces:
How Nodes are configured,
controlled, and monitored
Service Interfaces:
Communication links from other Nodes
Node
(Component)
Notes:
Interfaces of Components may be described by an EDS.
Specific Components may implement a set of Functions.
Physical Environment
Laws of Motion
Communications Geometry

## Slide 26: Formalized Relationships among Terms (Connectivity Viewpoint aspects)
Interfaces
System
Element
Node
(Component)
Implements 1..
Is a …
Function
Offers 0..
Service
  Node: A model of a space data system physical entity operating in a physical environment. A Node is a configuration of Engineering Objects forming a single unit for the purpose of location in space, and embodying a set of processing, storage and communication functions.
  Link: A Link provides interconnections between Nodes for communication and coordination. A Link may be implemented by a wired connection or with some RF or optical communications media.
Has 1…
Hardware
Software
People
Composed of 1..
Environment
Affects
Link
(Connector)
Connect via 1…
Composed of / Aggregation of …
Location / Motion
Has
Protocol
Stack
Implemented by (corr)
Offers 0..

## Slide 27: RASDS Connectivity View Representation
DATA
Physical Link: Node to Node connection
Service Provider I/F *
(provided I/F, optional)
Service Consumer I/F
(required I/F, optional)
Information Object
(optional)
Denotes a specific Node (physical component), may have embedded components
Denotes an implementation of a defined function, may be software or hardware (optional, see Functional Viewpoint)
Denotes a Physical Link (Connector of some sort) between two Nodes
Denotes a physical interface (optional, allows interface type to be characterized)
Denotes a protocol layer at an interface (not shown here, optional, allows interface binding to be characterized, see Communications Viewpoint)
Not shown are Information Objects describing interfaces or connectors which may be described in the Information Viewpoint and referenced by correspondence
Specific and Generic Object Types and Containment:
Related to the Physical Viewpoint, but focus is on data connections not physical connections or energetic flows.
Nodes (Components) will explicitly connect via some Physical Link. This may be free space (RF or optical) or it may be a hardware connection of some sort (cable, twisted pair, fiber optic).
A Node may explicitly define a physical interface, but this is not required. Nodes may have a provider/consumer relationship or they may be peers.
May show allocation of implemented Functions, in hardware (as a sub-node) or in software. These are tied by correspondence to the Functional View where they are defined.
May explicitly identify the information objects exchanged over the link (tied by correspondence to the Information View where they are defined).
May explicitly identify the protocol stack at an interface (tied by correspondence to the Communications View where they are defined).
Node A
Node B
Function A
Function B
Sub-Node B1
Function Deployment
(optional)
*
Notes: ASL Fig 3-4, trim headers & footers

## Slide 28: RASDS++ Security Aspects Connectivity Viewpoint
Specific security nodes & links
  Firewalls
  Routers
  Backbone & leaf networks
  Primary & backup network services
  WiFi servers
  VPN servers
  Compute servers / data centers
  User devices
  Identity devices
  Network / security devices (IDS, etc)
  etc

## Slide 29: Communications Viewpoint
The Communications Viewpoint focuses on the mechanisms and functions required to engineer and implement the protocols and communications standards for the space data system, including implementation choices and specifications, and relationships among elements in different protocol layers.
Stakeholder Concerns:
  the choice of communications and data transfer standards in the system;
  the end-to-end communications protocol functionality and reliability;
  implementation of the protocol specifications and the services they provide;
  the relevant protocol stacks, interface bindings, and interactions;
  interaction of protocol design with environmental constraints;
  support for design, evaluation of suitability, and integration into the rest of the system.
Protocol Entities (elements that implement specific protocols, protocol stacks, with Service Access Point (SAP) and peer interactions optionally shown):
  Types: protocol purpose (e.g., coding, modulation, link, network, transport, middleware, application service);
  Attributes: name, type, capabilities (e.g., in order, once only, bandwidth efficient, error correcting, delay tolerant), applicability (e.g., deep space, near Earth, in situ), constraints, services (offered, required), service access point (requests, indications, responses, confirmations), API (where appropriate), standard reference identifier, standards organization;
Protocol design specification elements (PDU description), behavior (state machine or table description), reliability (acknowledged, unacknowledged, selectively acknowledged), other design views of the communications protocol or protocol stack;
Correspondences to Nodes and Links (representations of physical elements from the Connectivity Viewpoint, for context);
Correspondences to Software Engineering Objects (representations of implemented functions from the Connectivity Viewpoint, for context).

## Slide 30
Core Functions
Peer behaviors
PDUs
Signaling
Required Interface (SAP):
How protocol services are requested from & supplied to this layer by lower layers (Layer n SDU)
Management Interfaces
(may be represented by a MIB):
How protocol is configured
controlled, and monitored
Provided interface (service access point):
How protocol services are requested of & supplied by this layer (SAP, Layer n-1 SDU)
Attributes:
Standards
Functionality
Technology
Applicability
Protocol Entity
Note
Each protocol entity represents a standard
Protocol Entities are usually shown in a stack
Protocol stack at an interface may be described by an EDS
Communications Viewpoint
(Protocol Entity Representation)

## Slide 31: Formalized Relationships among Terms (Protocol Viewpoint ontology)
Provided/required
Service
Interfaces
Protocol
Formalizes PDUs …
Protocol Data Units
Specifies 1..
Protocol
Behavior
  Protocol: A set of rules and formats (semantic and syntactic) used to determine the communication behavior of (N-layer)-protocol-entities in the performance of (N-layer)- functions; the description of the state machines within a Protocol Entity and the PDUs that are exchanged between these entities.
Provides
requires 1…
Service Data Units
Formalizes
SDUs …
Standard
Normative
Specification
Protocol
Stack
Participates in …
Interface
Binding
Specifies (corr)

## Slide 32: RASDS Protocol View Representation
Protocol Layer n peer
Protocol Layer n
Protocol PDUs
(logical flow)
PDUs may be simplex or bi-directional
Protocol behavior (may be described by state machine or other)
Proto
Proto
Proto
Proto
Unspecified Status (typically used for unknown protocols)
Published CCSDS / SC14 Standard (Blue or Magenta Book)
[Future]: CCSDS / SC14 Standard Under Development
[Prospective]: Proposed CCSDS / SC14 Standard (some future road map)
No CCSDS / SC14 Standard Identified
Proto
Standardisation Status (if required):
Protocol Layer n-1
Service Provided Interface (n SAP, optional)
Service Required Interface (of n-1 SAP, optional)
Layer type and naming usually follows ISO / IEC 7498 Basic Reference Model (BRM).
PDUs get exchanged between peer entities at the same layer. Service Data Units (SDU) get exchanged between upper layer and lower layer protocol entities.
Each protocol must have defined behavior, PDUs, and required / provided interfaces. If there is an inter-layer interface mismatch a “shim” or adapter may be required, and this may be complicated enough to be treated as a separate protocol.
Behavior may be defined using a state machine, state table, or narrative form. Usually only defines behavior of sending side, but may define both ends.
May (optionally) formalize the SAP definitions and show Requests and Indications at the SAPs. SAPs, APIs, and implementations of protocols are language and deployment specific.
physical flow
Protocol Layer n-1 peer
Flow direction arrows (optional)
Show PDUs &
SDUs???
Notes: ASL Fig 3-6, trim headers & footers

## Slide 33: RASDS++ Security Aspects Protocol Viewpoint
Specific security protocols
  Access control protocols
  2FA protocols
  IPSec
  HTTPS
  Secure DNS
  Application layer encryption & authentication
  Secure application access
  Secure routing updates
  Secure device monitoring
  etc

## Slide 34: Enterprise Viewpoint - Revised
The Enterprise Viewpoint focuses on the purpose, scope, and policies for the space data system. It describes the organizational entities and relationships; their roles, requirements, goals, objectives, scenarios, constraints; and how to meet them.
Stakeholder Concerns:
  the purpose, scope, and policies for the system;
  the objectives, operations concepts, and scenarios for the system;
  the requirements and constraints on the system;
  roles played by the system elements;
  activities undertaken by the system.
Enterprise Objects:
  Types: Organizations, both formal and informal (missions, projects, communities, with their roles and responsibilities), and Resources (facilities or other elements having enterprise operational or service roles);
  Attributes: name, role, objectives, point of contact, location, members, resources, provided services, types, interfaces and data, interaction modes, requirements, constraints;
Domains (boundaries of responsibility or ownership, includes requirements, system elements);
Relationships (ownership, membership, participation, roles, contractual);
Correspondences to Information objects (defined instances of documents, agreements, contracts, policies, requirements, objectives, goals, scenarios, membership lists, interface specifications, where formal specifications of the data to be exchanged are found in the Information Viewpoint).

## Slide 35
Enterprise Viewpoint - Enterprise Object
(Organizational Entity Features)
Attributes:
Identifier
Organization
Assets & Resources (People, Systems, Budget)
Roles
Objectives
Use cases
Requirements
Capabilities
Risk Management
Agreements / contracts
External Interfaces:
Scope
Requirements
Policies
Governance
Agreements / Contracts
Funding / Resources
Management Interfaces:
Scope
Requirements
Policies
Governance
Purpose / Mission / mission types
Funding / Resources
Service Interfaces:
Requirements
Agreements
Contracts
Funding
Enterprise
Object
Notes:
Interfaces of Enterprise Objects are often described as document exchanges
Specific Enterprise Objects may own / implement / operate a set of Functions or Components

## Slide 36: Formalized Relationships among Terms (Enterprise Viewpoint ontology)
Capabilities
Superior
Enterprise
Organization
Perform ..
Provides: Mission, Scope, Requirements, Governance, Resources …
Operations
Consumes / Expends ..
Resources
  Assets: Devices, system components, applications, infrastructure components
  Resource: Anything available to a system that can support the achievement of objectives; any physical or virtual element that may be of limited availability within a system. In the Enterprise Viewpoint a resource is an entity that has some role, offers services, and performs some action within a system.
  Ref: TOGAF, NIST 800-207
Possess set of 1..*
Composed of …
Create ..
Products
System Elements
Data
Services
Any of 1..
Domain
Controls / Operates in 1..*
People
Requirements
Assets
Values…
Specifies…
Constrain …
Produce ..

## Slide 37: RASDS Enterprise View Representation
DATA
Logical Link: Node to Node interface
Domain Boundary
(optional)
Organization Object
(Org, Project, Business)
Denotes a specific Organization (org, project, business), may have embedded components
Denotes a function an organization carries out (optional, see Functional Viewpoint)
Denotes a Logical Link (information flow of some sort) between two Organizations
Denotes an information object (optional, allows data to be characterized, see Information Viewpoint)
Denotes an organization / domain boundary (ownership / responsibility)
Specific and Generic Object Types and Containment:
Organizations (Agency, Project, Business) will explicitly connect via a Logical Link. May show the organization domain of control or ownership, or containment (sub-org).
May show allocation of Functions that an organization carries out (tied by correspondence to the Functional View where they are defined).
May explicitly identify the information objects (such as contracts, requirements, agreements) exchanged between organizations (tied by correspondence to the Information View where they are defined).
Org A
Org B
Function A
Function B
Sub-Org B1
DATA
Information Object
(optional)
Include Use Case in Enterprise view tie to Services view
Notes: ASL Fig 3-4, trim headers & footers

## Slide 38: RASDS++ Security Aspects Enterprise Viewpoint
Specific Enterprise security topics
  Policies
  Rules
  Governance
  Requirements
  Budgets
  Personnel
  Roles
  Resources
  Assets
  Relationships
  Capabilities
  etc

## Slide 39: Services Viewpoint - New
The Services Viewpoint focuses on the exposed services offered by a space system, formalized by functions and interfaces. It describes the interfaces of systems entities (hardware, software, people, and/or procedures), how to request and provide services, and their operations and interface bindings.
Stakeholder Concerns:
  The services provided by the system (H/W, SW, people);
  The interfaces, access points, and protocols for the system;
  The requirements and constraints on the services;
  The required and provided data for the services;
  Any contractual arrangements or agreements for services.
Service Objects:
  Types: Service types, both formal and informal (systems, people, software, etc), data types, and Resources (access to elements having service roles);
  Attributes: service name, type, operations, point of contact, interfaces, interface bindings, and data, interaction modes, policies, constraints;
Domains (boundaries of responsibility or ownership);
Relationships (ownership, membership, participation, roles, contractual);
Information (defined instances of services, functions, and data specifications, along with documents, agreements, contracts, policies, requirements, objectives, goals, scenarios, membership lists, where formal specifications of all of the data to be exchanged are found in Information Views).

## Slide 40
Service Viewpoint - Service Object
(Specialized Functional Entity Features)
Service
Object
Notes:
Interfaces of Service Objects may involve an app (thick or thin client), or expose a service protocol, or they may have their own UI, or they may be deployed in the cloud and use HTTP/REST and a web browser.
Attributes
Identifier
Type
Behavior
Data
External Interfaces:
How other Functional Objects are used to support the performance of this Object
Management Interfaces:
How service is configured,
controlled, and monitored
Service Interfaces:
How services are
requested by & supplied
to “user” Objects

## Slide 41: Formalized Relationships among Terms (Service Viewpoint aspects)
Service
Behavior
System
Element
Service
Processes ..
Implemented by 1..
Data
Offers 0..
Service
Interface
  Service: A provision of an interface of an object to support actions of another object.
  Interface: A set of interactions performed by an object for participation with another object for some purpose, along with constraints on how they can occur. An interface is therefore where the behavior of an object is exposed.
Has …
Composed of …
Interface
Binding
Accessed using 1..
Performs ..
Operations
Implement ..
Function

## Slide 42: RASDS Service Protocol Representation
Service Protocol
Service Protocol PDUs
(logical flow)
Service PDUs may be simplex or bi-directional
Service Protocol behavior (may be described by state machine or other)
Proto
Svc
Svc
Svc
Unspecified Status (typically used for unknown protocols)
Published CCSDS / SC14 Standard (Blue or Magenta Book)
[Future]: CCSDS / SC14 Standard Under Development
[Prospective]: Proposed CCSDS / SC14 Standard (Green Book – future road map)
No CCSDS / SC14 Standard Identified
Svc
Standardisation Status (if required):
Protocol Layer n
Service Provided Protocol Interface (Service SAP)
Service Required Interface (of comm protocol SAP)
ISO /IEC 7498 Basic Reference Model (BRM) treats all of this as “Application Layer”. Server, web/cloud, or virtualized deployments fit this same pattern.
Service protocol must have defined behavior, PDUs, and required / provided interfaces. Behavior may be defined in a state machine, state table, or narrative form. Usually only defines behavior of sending side, but may define both ends.
Service Protocol may be built upon a standard protocol such as HTTP/REST, or a protocol like AMS, or accessed via a defined API with a bespoke protocol. Underlying protocol stacks follow normal Communication View rules.
Services may use externally supplied Authentication mechanisms. They may also rely upon security mechanisms (encryption, authentication of data payloads) implemented within the layer or in underlying layers.
physical flow
Protocol Layer n peer
Flow direction arrows (optional)
Reflect on how this pattern can be used to describe Message Bus, Web or Cloud, or AMS Service types
Service User I/F
Authentication
Interface Binding Protocol Stack
(multiple layers)
Svc Access Authentication (optional)
Service
Provider
Service Protocol peer
Notes: ASL Fig 3-6, trim headers & footers

## Slide 43: RASDS++ Security Aspects Services Viewpoint
Specific Services security topics
  Procured services
  Locally built services
  Development services
  Operations services
  SaaS, etc
  Network, power, HVAC, and other services
  etc

## Slide 44: Operations Viewpoint - New
The Operations Viewpoint …
Stakeholder Concerns:
  The operations enabled by using the system;
  The activities carried out by using the system;
  The requirements on operations and activities (from Enterprise);
  Responding to constraints (e.g. cost, performance, policies) on operations and activities (from Enterprise) and Murphy…;(
  Describing how these support enterprise capabilities (from Enterprise);
  How these utilize systems capabilities (from Connectivity/Deployment); .
Operations Objects:
  Types: Capabilities (), Tasks, Processes (), Activities (), Scenarios (), Resources (systems, people, data, etc) having Operations roles;
  Attributes: names, types, flows, relationships, interaction modes, states (nominal, off-nominal), constraints;
Domains: boundaries of responsibility or ownership, related to org/team;
Relationships (implemented by, executed by, satisfies, provides);
Information (defined instances of requirements, plans, processes, resources, objectives, goals, scenarios, where formal specifications of the data to be exchanged are found in the Information Viewpoint).
Correspondences to Enterprise (requirements, objectives, people, policies), Systems (Connectivity view), Information (defined instances of documents, agreements, contracts, policies, requirements, objectives, goals, scenarios)
Operations viewpoint defines the objects and relations and rules for constructing views
Operations views are used to address specific concerns and represent activities, processes, and behaviors.

## Slide 45
Operations Object
Operations Viewpoint
(Abstract Operations Object Representation)
Attributes
Type (task, activity, process)
Properties
Products
Performance constraints
External Interfaces:
How Products are supplied to and requests are made of other Operations Objects
Management Interfaces:
How operations are configured,
controlled, and reported upon
Service Interfaces:
How operations tasks are requested by other Organization or Operations Objects
Concerns:
Issues
Resources requirements
Constraints

## Slide 46: Formalized Relationships among Terms (Operations Viewpoint ontology)
Operations Process
Operations
Requirements
People
Performed
by
Implemented by 1..
Describes / Uses …
Application
Information
Services …
Specify
Department
Member
of
Operations
Service
Data
Uses …
Accesses
* A System Element includes “Application”, which is a set of functions deployed (somehow) on a server as part of a system
  An enterprise capability denotes the “What” an enterprise can do, whereas an Operations process outlines “how” a particular activity gets done.
Work
Performs
System Element*
Provides …
Product
Produces
Operations Process: An Operations process is defined as a set of activities and tasks that, once completed, will produce a product or perform work

## Slide 47: Formalized Relationships among Terms (Operations Process ontology)
Operations Process
  An enterprise capability denotes the “What” an enterprise can do, whereas an Operations process outlines “how” a particular activity gets done.
An Operations process is defined as a set of activities and tasks that, once completed, will produce a product or perform work
Activity
(Std Ops)
Procedure
Task
Action
Has 1 .. Inter-related
Has cohesive set of 1 ..
Ordered set of 1 ..
Performs …
Product
Produces
Work
Is …
Systems
Element
Occurs within …
Hardware
Software
Person
Composed of 1..
Missing temporal aspects (Event) from recent Costin work

## Slide 48: RASDS Operations View Representation
Swimlane (System B)
Swimlane (System A)
Task A
DATA
Logical Link: flow between tasks
Source Task
(start/stop or duration, optional)
Subsequent Task
(start time or event, optional)
Information Object
(optional)
DATA
Denotes a specific Data Type subject to standardisation by CCSDS / SC14
Italics denotes an Abstract or Generic Data Type
Faded Colour: Data contained within another Data item (to which it is attached)
DATA
DATA
DATA
DATA
DATA
DATA
Unspecified Status (typically used for aggregated or grouped data/services)
Published CCSDS / SC14 Standard (Blue or Magenta Book)
[Future]: CCSDS / SC14 Standard Under Development
[Prospective]: Proposed CCSDS / SC14 Standard (Green Book – future road map)
No CCSDS / SC14 Standard Identified
DATA
Specific and Generic Data Types and Containment:
Standardisation Status:
Operations Objects are Tasks, treated like functions, abstract representations of behavior. For this purpose they are shown within some system context (swimlanes).
Operations Objects may themselves be decomposed into lower level Operations. Different uses of the same Operations Object may be expressed in other views and referenced by correspondence.
Operations views are intended to describe temporal flows among different systems elements.
Operations views may explicitly show timing and/or duration, and are suitable for representing instances, durative events, and sequences of events.
They may explicitly identify the information objects that are exchanged (tied by correspondence to the Information View where they are defined).
Sub-Function B1
Task B
Notes: ASL Fig 3-4, trim headers & footers

## Slide 49: RASDS++ Security Aspects Operations Viewpoint
Specific Operations security topics
  SOC
  System monitoring
  Threat hunting
  ATO assessment
  Red Teaming
  etc

## Slide 50: Physical Viewpoint - New
The Physical Viewpoint describes the engineered decomposition of the space system into physical components (Nodes) that connect physically or energetically to other Nodes. The Physical Viewpoint describes the physical aspects of the space system and the external environment within which it operates, the physical connections and behavior (fixity or motion) of the nodes, and their physical composition.
Stakeholder Concerns:
  The physical elements (Nodes) that compose the system;
  The physical connections among the physical elements in the system and the structural or energetic flows and junctions required to support these connections among objects in the system;
  The characterization of these different physical aspects in their own views, with tailored language for connection modalities: mechanical, electrical, thermal, electro-magnetic, gravitational, propulsive, ..;
  The selected allocation of physical functions to the nodes of the system, including their implementation choices and constraints on implementation, connections, configuration, and features imposed by the nature of the physical connections and the environment;
  The behavior and performance of elements in the system, including their capabilities, fixity or physical motion, and their interactions with the physical environment.
  The impacts and constraints on connections, energy flows, motion, ….

## Slide 51: Physical / Structural Viewpoint - New, contd
Engineering Objects (Nodes, Links, Applications):
  Nodes (hardware Engineering Objects, provide mechanical, power, thermal and other structural or physical resources, connection points, performance and other associated physical behavior):
    Types: hardware objects, composite hardware objects;
    Attributes: name, type, mass/power/orientation, location (place, trajectory, orbit), laws of motion, physical interfaces, capabilities (e.g., attachment type, fixity / motion, connection properties, etc.), allocated functions, constraints;
  Connections between Nodes (associated physical flows, behaviors, and properties);
    Types: connectors / weldments / mating surfaces, joints, waveguides, heat pipes, cables, free-space radiation, …
    Attributes: name, type, end-points (connected nodes), physical interfaces, performance (e.g., capacity, flows, range of motion), constraints, environmental effects, etc.);
Relationships (composition, interfaces/connections, constraints, configurations, allocation);
  Environment (physical environs, physical forces [gravity, electromagnetic, radiation, and others], physical interactions and effects);
  Flows (defined representations of energetic flows that are exchanged among Engineering Objects, where formal descriptions of flows are found in the Information Viewpoint).
NOTE – Physical Nodes and Connections in any given space system may include many more aspects and many more attributes than those shown here. The Data Communications aspects of Nodes and Links are covered in the Connectivity Viewpoint.

## Slide 52
Physical Base Viewpoint - Physical Object
(Hardware Component Representation)
Attributes:
Name/identifier
Composition (engineering objects)
Physical environment
Extensions
  Physical Attributes (mass, power, moment of inertia, thermal, Distribution / frame of reference)
  Connection types (flows, energetic, structural,…)
  Constraints
External Interfaces:
Physical Connections
to other Components
Management Interfaces:
How Components are configured,
controlled, and reported upon
Service Interfaces:
Physical Connections
from other Components
Physical Component
Notes:
Different Connection types will be treated as different aspects of the Nodes.
They may require different descriptors and attributes for the different flows and Connections.
Physical Environment
Laws of Motion
Other energetic inputs, gravity, Solar, radiation,…

## Slide 53: Relationships among Terms (Physical Viewpoint ontology - redrawn)
Interfaces
System
Element
Component
(Node)
Implements 1..
Is a …
Function
Offers 0..
Service
Component (Node): A model of a space data system physical entity operating in a physical environment. A Node is a configuration of Engineering Objects forming a single unit for the purpose of location in space, and embodying a set of processing, storage and communication functions.
Interface: A set of interactions performed by an object for participation with another object for some purpose, along with constraints on how they can occur. An interface is therefore where the behavior of an object is exposed.
Has Provided / Required 1…
Hardware
Software
Person
Composed of 1..
Environment
Affects
Connector
(Link)
Connect via 1…
Composed of …
Location / Motion
Has
Flow
Provides / Conveys

## Slide 54: RASDS Physical View Representation
Flow
Physical Link: Node to Node connection
Service Provider
(provider, optional)
Service Consumer
(consumer, optional)
Physical Connection *
Denotes a specific Node (physical component), may have embedded components
Denotes an implementation of a defined function, may be software or hardware (optional, see Functional Viewpoint)
Denotes a Physical Link (Connector of some sort) between two Nodes
Denotes a physical interface (optional, allows interface type to be characterized)
Not shown are Information Objects describing these interfaces or connectors which may be described in the Information Viewpoint and referenced by correspondence
Specific and Generic Object Types and Containment:
Related to the Connectivity Viewpoint, but focus here is on physical characterization, connections and energetic flow, not data.
Nodes (Components) will explicitly connect via some Physical Link. Nodes will have mass, power, thermal, and other properties. A Node may explicitly define a physical interface, but this is not required.
Physical connection (represents energetic constraint). This may be dynamic or static, structural / rigid, flexible, or other energetic (electro-magnetic, thrust, gravitational, thermal radiation).
May show allocation of implemented Functions, in hardware (a sub-node) tied by correspondence to the Functional View where they are defined.
May explicitly identify the flows exchanged by the objects using the link (defined in these views).
May explicitly identify the physical interface or connection type.
Node A
Node B
Function A
Function B
Sub-Node B1
Connection
Energy Flow
(0..n, optional)
Physical I/Fs *
(compatibility, optional)
*
Notes: ASL Fig 3-4, trim headers & footers

## Slide 55: RASDS++ Security Aspects Physical Viewpoint
Specific Physical security topics
  Venue
  Location
  Perimeter
  Gates, fences, (and physical access control)
  Power, conditioning, and backup
  HVAC and backup
  SCIF
  etc

## Slide 56: BACKUP