SYSTEM ENGINEERING AREA

Time Correlation/Synchronization

BoF

Report and Draft Charter February 2011

Approved:

Ed Greenberg _________________			__________________

### BoF Chair							Date

### Peter Shames_____________				__________________

### Area Director							Date

Executive Summary

This WG will define a set of standards for Time Correlation providing missions with precise approaches to correlate their spacecraft clocks with UTC and laying the foundation for future space networks where synchronized clocks will be an important infrastructural element.

The effort will involve the following:

1)  Develop a Green Book on Time Correlation describing:

- Return (TLM) channel time delay method

- Proposed methodology using PN Ranging

- End to End process for missions using Proximity Links

- Role of the Spacecraft clock and time correlation

- Time keeping on spacecraft

- Space network time service

- Current and future time correlation techniques

2)  Develop a Blue Book to define the parameters and the protocol for the transfer of Time Correlation data, generated in space and on ground, using PN Ranging.

3)  Develop a Magenta Book for Time Correlation documenting the recommended practice for using the approaches identified in the Green Book.

4)  NOTE: Need for developing a Time Synchronization standard for space networks is not yet ripe.  This should be reviewed again in the coming years.

Terminology

Clock correlation 	a method by which we relate the reading on a remote clock with the “master timing source” (i.e. UTC, continuous time scales)

Clock synchronization	a method of adjusting the remote clock/or the clocks frequency source to maintain its integrated time within an acceptable tolerance to the master clock source.

Coordinated time         time keeping that considers relativity (i.e. Barycentric Dynamical Time)

Objectives

- Identify and document in a Green Book the current methods used for time correlation and clock synchronization:

  - Describe approaches for different environments

    - Near Earth using Global Positional Satellite (GNSS)

    - Near Earth Without GNSS

      - Using one way data delay coupled with trajectory data

      - Using two way range signal (similar to Tracking and Data Relay Satellite System (TDRSS))

    - Deep Space

      - Using one way data delay coupled with trajectory data

      - Using two way range signal method that includes time correlation

      - Local area time zones (i.e. rovers and orbiters around Mars)

      - Cislunar space

  - Identify error sources effecting performance

    - One way is limited to orbit knowledge

    - Two way has range time built in.

    - Poorly calibrated factors

  - Determine if there are limiting attributes within the current CCSDS Recommendations (i.e. time tags in SLE services)

- Develop recommendations for use of identified approaches and their expected performance in a Magenta Book

- Review current methods for performance of clock correlation and synchronization to determine a recommendation for mission operations

- Collect and analyze technical literature that can be codified into the proposed Magenta Book or become the subject for new Blue Books

- Develop advocacy material for utilizing CCSDS PN Ranging for time correlation.

- Determine the requirements for time synchronization for emerging mission domains/enterprises.

- Determine the requirements to perform time correlation for each of the documented methodologies.  Document parameters & protocols in a Blue Book.

Schedule

| Date | Milestone |
| --- | --- |
| November 2010 | WG charter submitted to SE Area |
| November 2010 | WG Charter Adopted by CESG |
| January 2011 | Green Book organization prepared and work delegated |
| March. 2011 | List and characterize Error Sources within the end to end path |
| May 2011 | Current Time Correlation approaches documented |
| May 2011 | White paper for new methods to achieve improved time correlation using PN ranging and Transponder upgrades |
| October 2011 | Submit draft of Green Book on Current Time Correlation approaches. |
| October 2011 | White Book on recommended approaches for Time Correlation based for various operational environments. (Magenta book track) |
| January 2012 | White book for exchange of parameters for Time Correlation |
| May 2012 | Submit draft Red Book on recommended approaches for Time Correlation |
| May 2012 | Review the Time Synchronization needs for planned Space Networks, including possible methods and coupling to the recommended Time Correlation practices |
| July 2010 | Interoperability testing, write test report |
| October 2012 | Final draft Magenta book for recommended Time Correlation methods |
| October 2012 | Final draft Blue Book for exchange of parameters for Time Correlation, including interoperability test report |

Risk Management

Schedule relies upon the support of multiple CCSDS Agencies and on the allocation of adequate Agency resources to the WG. This work involves coordination between SLS area and the SE area.  Coordination will also be required between this WG and the MOIMS SM&C WG when they work on MO Time Services.  Use formal risk management approach to formulate risk management plan and identify risks other than schedule and resources.

Note:  JPL has been testing PN ranging and the next generation Transponder has accepted the requirement to time tag their Clock in association with a specified bit in the PN.   Bepi-Columbo is currently building a transponder that performs regenerated ranging using the PN but they have no requirement to use the PN correlation to time tag the PN with the transponder clock.

# Comments

Update

May 2011 Green Book on Time Correlation, started but outcome unknown

Consider using the same terminology used in the IOAG Service Calatog 2, add definitions for time transfer and time code

domains

Inside GNSS service volume

Inside GEO support volume

Catalog best practices for development of Magenta Book.

Update