Factors Considered in Spacecraft Clock Correlation Determination

| Mission | Spacecraft | Downlink | Ground | Correlation |
| --- | --- | --- | --- | --- |
| ACE |  | Not correctly accounted scientists are aware that range delay must be considered | AGRT = DSN's GRT - Ground Delay - Rate Delay | AGRT = DSN's GRT - Ground Delay - Rate Delay |
| Aquarius |  |  |  |  |
| Cassini |  | One-way light time | Tracking station location (dynamic) |  |
| Chandra | Signal delay time on-board spacecraft | Signal-travel time from spacecraft antenna to DSN ground antenna | DSN receipt time DSN time delays sync pulse delay |  |
| CloudSat |  |  |  |  |
| Con. X |  |  |  |  |
| Dawn | Largest uncertainty: short-term and/or long-term instability of onboard oscillator - shifts in oscillator frequency due to voltage variations, temperature variations, radiation, and aging Uncertainties in onboard creation of time correlation packets |  | Uncertainties in earth receipt time of time correlation packets |  |
| Gaia | On-board clock stability Signal delay/jitters Time Code quantization in telemetry | One way ranging errors, Propagation delay/error (Position uncertainty, Troposphere, Ionosphere, etc), | Ground Station Time Stamping Errors (delays, jitters, clock performance |  |
| GFO |  |  |  |  |
| GLAST | Use GPS receiver to determine frequency of on board oscillator & keep one second count delimiters in step with GPS atomic standard. Relativistic correction made in GPS clocks will automatically cause GLAST clock to reduce ticks per second by one tick every several hours so GLAST one second interval will appear to agree with UTC one second interval. This will allow simple calculation to convert the GLAST MET to UTC. |  |  |  |
| GPM | Core and Constellation, spacecraft clock correlation/calibration functions will be performed by on-board GPS receivers. Based on experience with other missions flying GPS technologies, failures are essentially non-credible given the presence of redundant antennas/receivers, as is planned for GPM. |  |  | Ground operations would only perform this activity routinely only if on-board GPS capability is lost. |
| Herschel Space Observatory | Ageing Onboard master-clock drifts onboard time-distribution delays local onboard time delays | Errors in downlinking time information to ground | Errors in ground-infrastructure Errors in decentralized users Time delays |  |
| IMAGE1 |  |  |  | Clock-Corr maintained by syncing onboard MET with Ground Receipt time applied to VCDU’s by DSN, and adding R/F transit time between IMAGE located (using predicted orbit) and DSN antenna. |
| INTEGRAL | On-board delay | Ground – S/C delay Antenna delay |  |  |
| Juno |  |  |  |  |
| LISA |  |  |  | Routine time-of-day synchronization |
| LRO |  |  | Stations required to meet 1 msec accuracy/precision for command time stamp |  |
| Mars Phoenix |  |  |  |  |
| Mars Rovers | clock drift |  |  |  |
| MESSENGER | Environmental effects (temperature, radiation, relativity, oscillator voltage and loading) on the oscillator and also oscillator aging Instrument timing uncertainties Uncertainty in distribution of time to instruments Delays through the spacecraft | One-way-light-time delay | Accuracy of DSN station telemetry frame time tags |  |
| MMS | Because all four spacecraft contain GPS receivers, TAI is maintained on-board all four spacecraft. Therefore, no ground correlation is required under normal conditions |  |  |  |
| Planck | Ageing Onboard master-clock drifts Onboard time-distribution delays Local onboard time delays | Errors in downlinking time information to ground | Errors in ground-infrastructure Errors in decentralized users Time delays |  |
| Pluto New Horizons | Environmental effects (temperature, radiation, relativity, oscillator voltage and loading) on the oscillator and also oscillator aging Instrument timing uncertainties Uncertainty in distribution of time to instruments Delays through the spacecraft | One-way-light-time delay | Accuracy of DSN station telemetry frame time tags, |  |
| Rosetta | On-board delays (TM bit rate dependant) in generating time reference |  | On-board delays (TM bit rate dependant) in generating time reference |  |
| RXTE | Use TT on board |  |  |  |
| STEREO | Environmental effects (temperature, radiation, relativity, oscillator voltage and loading) on the oscillator and also oscillator aging Instrument timing uncertainties Uncertainty in distribution of time to instruments Delays through the spacecraft | One-way-light-time delay | Accuracy of DSN station telemetry frame time tags |  |
| Swift |  |  |  |  |
| Terra |  |  |  |  |
| THEMIS |  | Range is major factor in clock update process |  |  |
| Ulysses | Spacecraft clock imbedded in engineering data | Factored with one way light time |  | Compared to predicted ERT |
| Voyager -1, -2 |  |  |  |  |
| WISE | S/C delays | RTLT TDRSS delays |  |  |