# SYSTEM ENGINEERING AREA

# Timecode

# BoF

# Approved:

Greg J. Kazz_________________			__________________

### BoF Chair							Date

### Peter Shames_____________				__________________

### Area Director							Date

Executive Summary

The T-Field of the CCSDS Unsegmented Timecode (CUC) is unnecessarily constrained. The CCSDS recommendation should pose no limit on the number of octets of course or fine time. This view is consistent with the intent and portions of the existing text. The number of seconds is constrained to approximately 136 years while the resolution of subseconds is constrainted to approximately 40 ns.  Current missions such as Project Constellation is asking for the ability to trace mission history beyond the current limit as well as requiring finer resolution than 40 ns.  The current Timecode blue book contains inconsistencies that lead the reader to believe that the CCSDS timecode is constrained to 4 octets of seconds and 3 octets of sub-seconds. However, the only real limitation is that the timecode must be divided into a seconds and sub-seconds sub-fields.

Furthermore, as currently stated in the recommendation, the timecode can be self-identified by the use of the P-field or not (in which case, the user must supply metadata outside of the timecode to describe the T-field). It should be noted that no missions have, to our knowledge, ever used the P-field. However, if this field is ever used, it makes sense to extend the P-field to meet the needs of current missions in terms of extending the seconds and sub-seconds fields. In addition, provision is made for a new timecode validation field signifying whether or not the time code is within the limits of the metadata specification or not (i.e., montonically increasing or not).

Objectives

The Timecode WG will have the following objectives:

- Extend the T-field of the CCSDS unsegmented timecode due to missions which require a larger counter to count seconds past the existing capability of approximately 136 years (4 bytes of course time) as well as more resolution of subsection time beyond the current approximately 40 ns resolution (3 bytes of fine time).

- Extend the P-field of the CCSDS unsegmented timecode to describe the increase in the number of bytes of course and fine time for timecodes which require self-identification. Also provide an indicator in the P-field to signal that a discontinuity in time has occurred.

Schedule

| Date | Milestone |
| --- | --- |
| April 2007 | BOF chartered by SE Area |
| April 2007 | Draft Pink Sheets created for Unsegmented Timecode |
| April 2007 | Distribute Draft Pink Sheets and BoF charter to participants |
| May-Sept 2007 | Telecon with BoF participants on Issues/Concerns |
| Oct. 2007 | Discuss Timecode changes at CCSDS Fall 2007 Meeting |
| Oct. 2007 | Publish new Timecode Blue Book Version |

Risk Management

Schedule relies upon at least one other CCSDS Agency joining the effort and on the allocation of adequate Agency resources to the WG. This work involves coordination between SLS area and the SE area.