# Ops concepts using the new architecture

The following two scenarios entail examples of how the guidelines presented in this document would be used for future architectures for lunar missions.  The examples are derived from the various end-points described in section 3 and the proposed architecture described in section 7. The first example showcases an architecture consisting of robotic missions and the second is a crewed scenario.  The protocols and technology used in these examples and the links shown are for illustrative purposes only and should not be construed as recommendations.

## Robotic scenario

This scenario describes an established architecture which makes use of a mature lunar communications infrastructure consisting of multiple international missions.  It consists of the spaceborne assets shown in Table 8-1 and the Earth entities shown in Table 8-2.  In the case of the Earth-bound nodes, there may be multiple instances of each.  For instance, each mission may have its own Mission Operations Center (MOC) or a given MOC may control multiple spacecraft.  It is assumed that in all instances there will be greater than one of each type.

| Spacecraft | Location | Quantity | Description |
| --- | --- | --- | --- |
| Science Mission | Lunar Orbit | 3 | Science asset with multiple instruments on-board the spacecraft |
| Lander | Lunar Surface (near and far side) | 2 | Robotic lander with multiple instruments |
| Rover | Lunar Surface (near and far side) | 2 | Robotic rover with multiple instruments |
| Spacecraft (either lander or rover) | En route | 1 | A spacecraft en-route to the either orbit or land on the Moon |
| TDRSS | Earth Orbit | Multiple | Used for relay of communications to/from the Moon |

Figure 8-1: Spaceborne Assets of a Robotic Lunar Architecture

| Node | Description |
| --- | --- |
| Ground Stations | Multiple ground stations. Either the Deep Space Network (DSN) or commercial antennas. |
| Missions Operations Center | Mission operations centers for the various missions. Each MOC may control one or more spacecraft. The MOC is responsible for the health and safety of the spacecraft and coordination of science operations with the SOC |
| Science Operations Center | Science Operations Centers for the various missions. Each SOC may be responsible for one or more instruments on one or more spacecraft. |
| Spacecraft Development Facilities | Spacecraft engineers at commercial/government/university facilities monitor health and safety of the spacecraft |
| Remote locations | These nodes consist of scientists or operations personnel who are not in their home facility. |

Figure 8-2: Earthbound Assets of a Robotic Lunar Architecture

A common denominator of these robotic spacecraft is that they process varying types of input and output either from or to other nodes in the Cislunar network.  Input to a node will typically take the form of commands to control the platform or payload, configuration data for operating the spacecraft or instruments, or data which are destined for another node with the Cislunar network.  Spacecraft output may consist of payload  telemetry consisting of spacecraft status or data, science data in files, video streams, or other formats, and the aforementioned data being relayed to other nodes.  Transmission of this data can be either one-to-one as in Earth ground station to spacecraft or one-to-many such as telemetry which may be received by a single Earth antenna but end in various location such as an operations center, an archiver, and a science workstation.  How this data travels throughout the system may also vary.  Some data, such as real-time housekeeping data or navigation images have an innate timeliness that requires delivery as quickly as possible.  Other types of data may be delay tolerant and can be transmitted in a store-and-forward fashion.  Push, Pull, Multicast.

### Example ApplicationS of cislunar protocols in robotic environment

The following list of examples describe methods and protocol interactions for typical operations and applications that may be seen in a lunar architecture.

#### Real-time Telemetry from a Spacecraft

Spacecraft typically produce some degree of real-time telemetry.  This telemetry could be formatted into CCSDS Space Packets and transported to the ground via UDP and IP.  Upon receipt by the ground, the packet is then routed to various destinations including the SOC, MOC, and an archiver (additional words regarding SLE?)

Figure 8-1: Real-Time Telemetry Transmission

The diagram above is a placeholder.  It should be modified to show include a SOC, MOC, and archiver on the left.

#### CFDP Transmission from Instrument to User

This example uses the transfer of a data file from an instrument to a user on the ground.  The protocol stack for this transfer is shown in Figure 8-1.  In this example, the user initiates a file transfer by contacting the CFDP engine on the spacecraft.  The Acknowledged Mode of CFDP is selected which provides for reliable delivery of CFDP information between endpoints.  Since delivery is ensured by CFDP, UDP is chosen at the next layer and the appropriate IP packets are created with the address of the sender and the address of the instrument on the spacecraft.  This information is then sent within the user’s facility via a physical layer protocol followed by a transmission across the Internet via the same or a different physical layer mechanims to the ground station.  The packet is then placed into the appropriate link layer protocol frames and sent to a lunar orbiter functioning as relay via R/F.  Upon receipt by the spacecraft, the spacecraft determines appropriate communication capability and timing with the lander and initates a transmission by placing the IP packet in a selected link layer frame for transmission to the lander.  When the lander receives this information, it determines the destination of the packet through its routing information and transmits the packet across its internal bus to the instrument.  At this time, the instrument software extracts the CFDP information from the packet.  The CFDP engine determines what was requested, communicates with the CFDP client application, and initiates the appropriate action.  Communication back the sending entity is started in the reverse of what was described but perhaps through a different series of nodes using a different link layers where appropriate.

Figure 8-2: Instrument/User Data Transmission with CFDP Acknowledged Mode

#### Commanding a Spacecraft

Figure 8-3: Spacecraft Commanding

The diagram above is a placeholder.

#### Emergency Commanding of a Spacecraft

Figure 8-4: Spacecraft Commanding

The diagram above is a placeholder.

#### Video Streaming from a Lander

## crewed scenario

### Example ApplicationS of cislunar protocols in crwed environment

#### Internet Access by Astronauts

#### Other crewed examples…

Original Comments in Doc:

How we would do the above scenarios with the new capabilities laid out in section 5.

CFDP goes here?  It’s on the brink between current and future architectures.

Comments:

Keith Hogie, 8/29/2005

Chris,

Going over you list of scenarios I was wondering how they should be grouped.  We probably want a scenario to represent each possibility once we figure out what the categories are.  Here are some of the categories I came up with.  I ‘m not sure these condense into clean categories yet.

Type of end points (unmanned/manned, space/ground)

Space

Unmanned (satellite, lander, rover)

Manned (astronaut in habitat or space suit)

Ground

Unmanned (file servers, data repositories)

Manned (scientist, control center operators)

End point locations and flow

One-to-one

Space-to-Ground and/or Ground-to-Space (does direction matter?)

Space-to-Space (no Earthly involvement)

One-to-many

Combinations of space and ground with 3 or more parties

Timeliness of data delivery

Realtime packet (user assumes packet level forwarding, immediate relay)

File store-and-forward (user assumes files with variable file storage delays)

RF Connectivity path

Direct (only 1 RF link in end-to-end path, multiple wired links?)

(TDRSS looks like 1 RF link for these definitions)

Intermediate relay (2 or more RF links)

Relay protocol level

Packet level relay (immediate forwarding)

File level relay (file level buffering)

Relay mobility

Fixed relay (e.g. cell tower, WiFi access point)

Mobile relay (e.g. TDRSS, other relay satellite)

Link Duplex (during a single contact)

2-way link (less than 10 second round trip time?)

1-way link (only 1-way, or RTT > 10 seconds?)

Type of Data

Telemetry (RT packets or recorded file)

Science (RT packets or recorded file)

Image (file)

Audio (RT packets or recorded file)

Video (RT packets of recorded file)

Data Transfer Initation

Push (space, ground, automated, scheduled)

Pull (space, ground, automated, scheduled)

Multicast (users tune in whenever they want)

Operational Scenario (what is the operational purpose of this data transfer)

Data delivery

Commanding

Telescience

Etc.

Using these categories, your first example would have the following characteristics.

Type of end points (unmanned/manned, S/G) - space unmanned-ground unmanned

End point locations and flow - One-to-One, Space-to-Ground

Timeliness of data delivery - File store-and-forward

RF Connectivity path - Intermediate relay, file level, mobile relay

Link Duplex (during a single contact) - 2-way link

Type of Data - Science data file

Data Transfer Initiation - Push from space-to-ground

Operational Scenario - Deliver science instrument data to end user

While filling in this information, I noticed that the following example starts with space-to-ground and then describes ground-to-space.

Cislunar Meeting: week of 9/12/2005