Draft Report Concerning
Space Data System Standards

SECURITY THREATS AGAINST SPACE MISSIONS

DRAFT INFORMATIONAL REPORT

CCSDS 350.1-G-0.7

DRAFT GREEN BOOK

August 2005

AUTHORITY

|  | Issue: | Draft Green Book, Issue 0.7 |  |
| --- | --- | --- | --- |
|  | Date: | August 2005 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS REPORT IS FINALIZED, IT MAY CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and reflects the consensus of technical panel experts from CCSDS Member Agencies.  The procedure for review and authorization of CCSDS Reports is detailed in Procedures Manual for the Consultative Committee for Space Data Systems.

This document is published and maintained by:

CCSDS Secretariat

Office of Space Communication (Code M-3)

National Aeronautics and Space Administration

Washington, DC  20546, USA

FOREWORD

This document is a CCSDS report that describes the threats that could potentially be applied against space missions.  It characterizes threats against various types of missions and the potential of their likelihood and the results of their having been carried out.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommendation is therefore subject to CCSDS document management and change control procedures which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- British National Space Centre (BNSC)/United Kingdom.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- Deutsches Zentrum für Luft- und Raumfahrt e.V.  (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (Roskosmos)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- Centro Tecnico Aeroespacial (CTA)/Brazil.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- Danish Space Research Institute (DSRI)/Denmark.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- MIKOMTEK:  CSIR (CSIR)/Republic of South Africa.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic & Atmospheric Administration (NOAA)/USA.

- National Space Program Office (NSPO)/Taipei.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

DOCUMENT CONTROL

| Document | Title and Issue | Date | Status |
| --- | --- | --- | --- |
| • |  |  |  |
| • |  |  |  |
| • |  |  |  |
| CCSDS 350.0-G-0.7 | Security Threats against Space Missions, Draft Issue 0.7 | August 2005 | Current draft issue. |

CONTENTS

Section	Page

1	Introduction	1-1

1.1	Purpose	1-1

1.2	scope	1-1

1.3	applicability	1-1

1.4	rationale	1-1

1.5	Document structure	1-1

1.6	definitions	1-1

1.7	references	1-4

2	overview	2-1

3	Threat analysis process	3-1

3.1	Methodology	3-1

3.2	threat analysis and mission planning	3-4

3.3	Activities and expected results	3-5

3.4	threat sources	3-5

4	threats against illustrative mission types	4-1

4.1	active threats	4-1

4.2	passive threats	4-1

4.3	Illustrative Mission threats	4-2

4.4	Threat summary and Security Mechanisms to 
Counter THREATs	4-9

4.5	Communication Architecture and specific threats	4-10

5	Summary	5-1

ANNEX A	ACRONYMS	A-1

Figure

3-1	Generic Threat Analysis Methodology	3-1

3-2	Space Mission Threat Analysis Process	3-2

3-3	Generic Threats to CCSDS Space Missions	3-3

3-4	Classic Network Threats	3-4

4-1	CCSDS Security Communications Threats	4-10

CONTENTS (continued)

Table	Page

4-1	Manned Space Flight—International Space Station Threat Analysis	4-3

4-2	Meteorological Satellite Threat Analysis	4-4

4-3	Communications Satellite Threat Analysis	4-5

4-4	Science Mission Threat Analysis	4-7

4-5	Navigation Satellite Threat Analysis	4-8

4-6	Threat Summary	4-9

# Introduction

## Purpose

This document provides the results of a threat analysis of various categories of civilian space missions and provides security threat data for mission planners.

## scope

In the past, space missions using CCSDS recommendations were typically thought of as ‘civil’ and ‘scientific’ missions that were unlikely targets of malicious attackers, unlike military missions that would be targeted and have traditionally been highly protected.  However this view is now changing.  This document provides threat analysis results for several classes of missions that can be used by mission planners.

## applicability

This document is applicable to mission planners for all space missions.  It provides background data and threat information so that mission planners can be better prepared to understand the security mechanisms and/or policies necessary to counter any perceived threats against the mission.

## rationale

Network connectivity is constantly increasing and is becoming ubiquitous.  As a result, the desire is to take advantage of the existing infrastructure to operate mission payloads across networks.  This opens up many threats against missions that would not have previously existed.  As a result, civil space missions must take into account a wide variety of security threats.

## Document structure

This document is divided into 5 sections.  Section 1 provides this introduction and definitions of commonly used terms.  Section 2 provides an overview of the subject area.  Section 3 describes the threat analysis process.  Section 4 describes the threat analyses of six different classes of civil space missions.  Section 5 is the summary.

## definitions

Access Control: The process of granting access to the resources of a system only to authorized users, programs, processes, or other systems.

Access Control Mechanism: Hardware or software features, operating procedures, management procedures, and various combinations of these designed to detect and prevent unauthorized access and to permit authorized access in an automated system.

Authenticate: (1) To verify the identity of a user, device, or other entity in a computer system, often as a prerequisite to allowing access to resources in a system.  (2) To verify the integrity of data that have been stored, transmitted, or otherwise exposed to possible unauthorized modification.

Authorization: The granting of access rights to a user, program, or process.

Controlled Network: A network that is enforces a security policy.

Confidentiality:  Assurance that information is not disclosed to unauthorized entities or processes.

Configuration Management: Process of controlling modifications to the system’s hardware, firmware, software, and documentation which provides sufficient assurance the system is protected against the introduction of improper modification before, during, and after system implementation.

Data Integrity: Condition that exists when data is unchanged from its source and has not been accidentally or maliciously modified, altered, or destroyed.

Denial of Service: Any action or series of actions that prevent any part of a system from functioning in accordance with its intended purpose.  This includes any action that causes unauthorized destruction, modification, or delay of service.

Identification: The process that enables recognition of an entity by a system, generally by the use of unique machine-readable user names.

Masquerading: Attempts to gain access to a system by posing as an authorized user or as a process.  This is a form of spoofing.

Residual Risk: The portion of risk that remains after security measures have been applied.

Risk: A combination of the likelihood that a threat will occur, the likelihood that a threat occurrence will result in an adverse impact, and the severity of the resulting adverse impact.  Note: Risk is the loss potential that exists as the result of threat and vulnerability pairs. It is a combination of the likelihood of an attack (from a threat source) and the likelihood that a threat occurrence will result in an adverse impact (e.g., denial of service, loss of confidentiality or integrity), and the severity of the resulting adverse impact. Reducing either the threat or the vulnerability reduces the risk.

Risk Analysis: An analysis of system assets and vulnerabilities to establish an expected loss from certain events based on estimated probabilities of the occurrence of those events.  The purpose of a risk assessment is to determine if countermeasures are adequate to reduce the probability of loss or the impact of loss to an acceptable level.

Security Policy: The set of laws, rules, and practices that regulate how information is managed, protected, and distributed.   Note: A security policy may be written at many different levels of abstraction. For example, a corporate security policy is the set of laws, rules, and practices within a user organization; system security policy defines the rules and practices within a specific system; and technical security policy regulates the use of hardware, software, and firmware of a system or product.

Threat: Any circumstance or event with the potential to cause harm to a system in the form of destruction, disclosure, adverse modification of data, and/or denial of service.

Threat Agent: A method used to exploit a vulnerability in a system, operation, or facility.

Threat Analysis: The examination of all actions and events that might adversely affect a system or operation.

Threat Assessment: Formal description and evaluation of threat to a system.

Trap Door: A hidden software or hardware mechanism that can be triggered to permit system protection mechanisms to be circumvented.  It is activated in some innocent-appearing manner; e.g., a special ‘random’ key sequence at a terminal.  Software developers often introduce trap doors in their code to enable them to reenter the system and perform certain functions.  Synonymous with back door.

Trojan Horse: A computer program with an apparently or actually useful function that contains additional (hidden) functions that surreptitiously exploit the legitimate authorizations of the invoking process to the detriment of security or integrity.

Virus: A program that can ‘infect’ other programs by modifying them to include a, possibly evolved, copy of itself.

Vulnerability: Weakness in an information system, or cryptographic system, or components (e.g., system security procedures, hardware design, internal controls) that could be exploited to violate system security policy.

Vulnerability Analysis: The systematic examination of systems in order to determine the adequacy of security measures, identification of security deficiencies, and provide data from which to predict the effectiveness of proposed security measures.

Vulnerability Assessment: A measurement of vulnerability which includes the susceptibility of a particular system to a specific attack and the opportunities available to a threat agent to mount that attack.

## references

[1]	Glossary of INFOSEC and INFOSEC Related Terms.  Corey D. Schou, comp.  Pocatello, Idaho: Idaho State U Simplot Decision Support Center, 1996.

[2]	Capability Maturity Model® Integration (CMMISM), Version 1.1.  CMU-SEI-2002-TR-011.  ESC-TR-2002-011.  Pittsburgh: Carnegie Mellon University, 2002. <http://www.sei.cmu.edu/publications/documents/02.reports/02tr011.html>

[3]	Willis H. Ware, ed.  Security Controls for Computer Systems: Report of Defense Science Board Task Force on Computer Security.  Rand Report, R-609-1.  Reissue.  Santa Monica, California:  Rand Corp., 1979.  <http://www.rand.org/publications/R/R609.1/R609.1.html>

# overview

Security of data communications systems is a very important issue often not given enough attention.  To date, most civil space missions have relied on their uniqueness and obscurity to deter unauthorized access.  Some have ignored the issue entirely.  However, this is changing due to increased international missions with cross-agency support and the potential use of public ground data networks to transfer mission control and monitoring data.  Unprotected civil space mission communications systems are highly vulnerable due to increased reliance on ubiquitous networks.  Furthermore they are a high profile target for malicious attackers to compromise a spacecraft just for fun.  Also, spacecraft data may be sensitive from a commercial or operational perspective (e.g. commercial, space-based imagery; dual-use technologies) and therefore confidentiality, authentication, integrity, and access controls will be important considerations.

CCSDS missions must now address security.  Military space systems have traditionally included a high level of built-in security whereas civil space missions have little, if any security.

With the general increasing level of security awareness in the information technology (IT) community, civil and scientific missions should not wait to act until after a security incident occurs.  The continued expansion of network interconnectivity for data dissemination and science mission scheduling creates new and additional threats against civil space missions.  All threats should be analyzed and protected against to provide protection of assets and critical services.

While this document presents the results of an initial threat analysis, more detailed threat analyses should be carried out by mission planners in order to understand and state their mission’s security requirements.

# Threat analysis process

## Methodology

In order to determine security threats against a mission, a threat analysis methodology should be followed.  Such a methodology is illustrated in figure 3-1.

Figure 3-1:  Generic Threat Analysis Methodology

This figure illustrates a generic process in which one determines the threats against a mission system and then decides whether or not the mission is vulnerable to the threat.  Based on the characteristics of the vulnerability, it then must be determined what the response will be – can the vulnerability be countered by either technical means or by policy?  A cost-benefit analysis must be performed to determine if it is worth countering the threat by technical means.  If the technical means is very expensive, but the likelihood of exploitation of the vulnerability is low, then a policy response would be in order.

If the vulnerability can be countered, it is not exploitable and is no longer a concern.  However, if there is no means to counter it by either technically or by policy, then it remains a concern and is classified as a residual risk.

Taking the generic methodology one step further, it can be refined into a more specific methodology for use in space mission threat analyses.  This is illustrated in figure 3-2.

Figure 3-2:  Space Mission Threat Analysis Process

As a result of applying the threat analysis process, a number of generic threats to CCSDS space missions have been revealed.  Many of the threats are applicable to non-space systems (e.g., generic computer installations) including the ground networks used to support the missions. Threats include hardware and software failures, loss of data confidentiality via data interception, replay of recorded data, loss of data integrity, and unauthorized access.  However, there are some additional threats that are applicable in the space environment that would not necessarily be problems in other environments.  Among these are jamming of radio frequency communications links, ‘hijacking’ of space links (another variation of unauthorized access), and space debris.  And of course, hardware failures in a space environment are much more critical than in a terrestrial environment because of the inability to make repairs.  These generic space mission threats are illustrated in figure 3-3.

Figure 3-3:  Generic Threats to CCSDS Space Missions

In addition to generic threats against space missions, there are a number of network threats, first documented in 1970 that are still meaningful today – and maybe even more meaningful because of the ubiquitous network connectivity that we now see and will see even more of in the future.

Among the network threats documented in 1970 that are still relevant today are:

- unauthorized access,

- theft of information [loss of confidentiality],

- software and hardware failures [denial of service, loss of integrity],

- dishonest maintenance personnel [insider threat],

- dishonest systems personnel [insider threat],

- network taps [loss of confidentiality], and

- communication radiation [loss of confidentiality].

All of these threats are relevant with respect to CCSDS space missions – not only from a space perspective but also from a ground network perspective as well.  Figure 3-4 is a reconstruction of the diagram from the 1970 report shown here to illustrate that network threats are not new problems.

Figure 3-4:  Classic Network Threats

## threat analysis and mission planning

As previously stated in the introduction, this document provides mission planners with a threat overview that can be used to understand and state their mission’s specific security requirements.

If one looks at the way a threat analysis should be conducted, it is very similar, if not identical to a quality assurance process with the following steps:

- Mission start (design): produce recommendations resulting from the threat assessment and the risk analysis,

- Implementation: use standards (CCSDS and others), contingency and disaster recovery planning, conduct conformance testing,

- Operations: Operating procedures, Continuous Contingency Capability, Threat monitoring.

## Activities and expected results

The reasons for integrating security into space activities have already been stated, and if anything, the threats against missions are only increasing with the sophistication of the threat agent.

It is expected that a Common Assessment Methodology will be agreed upon and adopted by all Space Mission Security Officers. Furthermore, a common analysis process will help agreement on common conformance testing and facilitate the agreement on interoperation procedures for multi-agency missions.

Since the threats are constantly evolving and changing, special emphasis has to be put on constant risk awareness and management.  Operational contingency management is a key issue, based on a common (i.e., inter-Agency) organization that would provide all missions with continuous threat monitoring.

## threat sources

The possible sources of threats may be:

- Terrorists and criminals,

- Foreign intelligence services,

- Subversives or political activists,

- Computer hackers,

- Commercial competitors,

- Inadvertent actions of staff members, or

- Disgruntled staff members.

# threats against illustrative mission types

CCSDS space missions threats have been categorized to into two classes: active threats and passive threats.

## active threats

An active threat requires an adversary to initiate a sequence of events to attempt to exploit a vulnerability.  During an active attack, the adversary attempts to probe the system, cause mischief or upsets in order to compromise the system(s).

Active threats include:

- communications system jamming (resulting in denial of service),

- attempting access to an otherwise access controlled system resulting in unauthorized access,

- replay of recorded authentic communications traffic at a later time with the hope that the authorized communications will provide data,

- masquerading as an authorized entity in order to gain access,

- the exploitation of  software vulnerabilities (bugs),

- unauthorized modification or corruption of data, and

- malicious software such as a virus, worm, Distributed Denial-Of-Service (DDOS) agent, or Trojan horse.

Active threats may be carried out against both spacecraft and ground systems.  In the case of ground systems, it is imperative that they are operated as controlled networks.  That is, in general they should not be connected to open, external networks such as the Internet without any safeguard.  If a connection across an open network is required, it should be accomplished through the use of formal risk assessment and technical security controls (e.g., secure Virtual Private Network (VPN), firewalls, anti-virus, anti-spyware).  Only personnel who have been screened (e.g., national agency checks) should be provided access to the closed ground system network.

## passive threats

Passive threats do not require an adversary to do anything other than sit back and take advantage of what is already in place and being used.

An example of this would be the interception of data being sent via radio frequencies.  An adversary would point an antenna and tune a receiver to intercept the data.  Rather than trying to break in or cause an upset, this type of passive threat is performed unbeknownst to the entity under attack.

A passive threat may also take advantage of a software vulnerability such as when a worm infects a system and migrates to other systems, all the while disclosing information to whomever cares to listen.

Another type of passive attack would be traffic analysis – the ability to determine, in loose terms, what is going on between communicating entities simply by virtue of how and when they are communicating without necessarily being able to see or understand the data being communicated.

## Illustrative Mission threats

The following subsections will illustrate the threat analysis of various mission categories that may be of interest to civil space mission planners.  By no means is this an exhaustive or detailed threat analysis but is meant to provide a top level description of the kinds of threats that are possible against these types of missions.  The categories of missions that will be examined are:

- Manned Space Flight

- Meteorological Satellites

- LEO

- GEO

- Communications Satellites

- LEO constellations

- GEO

- Science Missions

- Near earth/earth orbit

- Lunar

- Interplanetary/deep-space

- Navigation Satellites

These classes denote missions in varying orbits.  The threats against each orbit type may be different.  GEO missions, although at a higher altitude requiring more communications power, can be more vulnerable than a low-earth mission because they provide continuous visibility in their coverage area.  LEO missions on the other hand, provide limited view periods but can be reached with low power levels and small antennas.

A special case of LEO mission is the communication constellation (e.g., Iridium).  Whereas each individual LEO spacecraft provides only limited visibility, there are many spacecraft in orbit which provide almost continuous global coverage with satellite cross links creating a space network.  Therefore the LEO communication constellation provides an adversary with more opportunity for attack than does a single LEO mission.

More infrastructure (resulting in higher cost) is required to attack deep-space/interplanetary missions than earth/near-earth orbit missions due to the larger antennas and higher power required to communicate with the spacecraft.

### manned space flight

The International Space Station (ISS) is a good example of a manned space mission with international cross support and cooperation.  Modules aboard the ISS have been built by several different nations and the ISS crews come from a variety of countries.   Table 4-1 illustrates a possible threat analysis for the ISS.

Table 4-1:  Manned Space Flight—International Space Station Threat Analysis

| Applicable Threats | Impacts | Probability (1= Lowest, 5= Highest) | Security Mechanisms to Counter Threat |
| --- | --- | --- | --- |
| Data corruption | Modification of information System damage | 2 | Data integrity schemes (hashing, check values, digital signatures) Resilient hardware (e.g., SOS) |
| Ground facility physical attack | Loss of command, control, and data | 2 | Guards, gates, access controls, backup site(s) |
| Interception | Loss of sensitive data | 3 | Data encryption, spread spectrum, frequency hopping |
| Jamming | Loss of command and telemetry link | 2 | Multiple uplink paths Frequency hopping Spread spectrum |
| Masquerade | Potential to disrupt operations (uplink) Potential to receive false information (downlink) | 3 | Strong authentication of uplinked commands and downlinked data Access control scheme Vetting of staff No use of open networks |
| Replay | System damage (possible safety of life issues | 1 | Authenticated command counter, timestamp |
| Software threats | Undesirable events System damage Enable other threats | 2 | Acceptance testing Independent verification and validation (IVV) Code walkthroughs Automated code analysis Auditing |
| Unauthorized Access | Disruption of operations System damage (possible safety of life issues) | 4 | Encryption of TT&C and mission data Authentication of commands No use of open networks Authentication tokens (e.g., smart card) Auditing |

### meteorological satelliteS

Meteorological satellite systems illustrate a type of mission that is both scientific in nature as well as being a critical national or international asset.  Over the years, these missions have become a necessary part of our climate observation and prediction infrastructure.  Meteorological satellites may be in low earth orbit (LEO) or in geosynchronous earth orbit (GEO).  Table 4-2 illustrates the possible threats against meteorological satellites.

Table 4-2:  Meteorological Satellite Threat Analysis

| Applicable Threats | Impacts | Probability (1=Lowest, 5=Highest) | Security Mechanisms to Counter Threat |
| --- | --- | --- | --- |
| Data Corruption | Modification of information System damage | 4 | Data integrity schemes (hashing, check values, digital signatures) Resilient hardware (e.g., SOS) |
| Ground facility physical attack | Loss of command, control, and data | 2 | Guards, gates, access controls, backup site(s) |
| Interception | Loss of sensitive data Theft of commercial data | 3 (LEO) 3 (GEO) | Protection of archive & distribution systems via encryption |
| Jamming | Loss of command and/or telemetry link Commercial impact | 2 (LEO) 2 (GEO) | Multiple uplink paths Multiple downlink paths Frequency hopping Spread spectrum |
| Masquerade | Potential to disrupt operations (uplink) Potential to receive false information (downlink) | 2 | Strong authentication of uplinked commands and downlinked data Access control scheme Vetting of staff No use of open networks |
| Replay | System damage (possible safety of life issues | 1 | Authenticated command counter, timestamp |
| Software threats | Undesirable events System damage Enable other threats | 2 | Acceptance testing Independent verification and validation (IVV) Code walkthroughs Automated code analysis Auditing |
| Unauthorized Access | Theft of commercial data Disruption of operations System damage | 3 | Encryption of TT&C and mission data Authentication of commands Access control in control and dissemination systems No use of open networks Authentication tokens (e.g., smart card) Auditing |

### communications satellites

Geosynchronous earth orbit (GEO) communications satellites have become one of the most ever-present parts of the international communications infrastructure.  These satellites are relied upon to relay voice, video, data, paging, etc. all over the world.  Outages of these satellites would wreak havoc with the international communications systems (as is best witnessed by the major concerns during periods of high sun-spot activity).

Recently, constellations of communications satellites in low earth orbit (LEO) with satellite cross links, such as Iridium, have been orbited.  The LEO constellations reduce the communications latency experienced with GEO satellites while still providing extensive earth coverage previously only available from GEOs.  However, the reduced threat to LEO satellites, as discussed previously, no longer holds true because of the on-orbit routed network created by the satellite constellation.  While a single LEO satellite is still only visible for a short amount of time, each satellite in the constellation acts as a relay to its neighbor spacecraft which means that the threats against the entire constellation are increased.

A threat analysis of generic communications satellite systems is illustrated in table 4-3.

Table 4-3:  Communications Satellite Threat Analysis

| Applicable Threats | Impacts | Probability (1=Lowest, 5=Highest) | Security Mechanisms to Counter Threat |
| --- | --- | --- | --- |
| Data corruption | Modification of information System damage | 4 (GEO) 2 (LEO) | Data integrity schemes (hashing, check values, digital signatures) |
| Ground facility physical attack | Loss of command, control, and data | 2 | Guards, gates, access controls |
| Interception | Loss of sensitive data Theft of commercial data | 4 (GEO) 2 (LEO) | Protection of traffic (potentially user responsibility) |
| Jamming | Loss of TT&C and/or traffic circuits Commercial impact Possible safety impact | 3 (GEO) 3 (LEO) | Multiple uplink and downlink paths Multiple access points Frequency hopping Spread spectrum |
| Masquerade | Potential to disrupt operations (uplink) Potential to receive false information (downlink) | 2 | Strong authentication of uplinked commands and downlinked data Access control scheme Vetting of staff No use of open networks |
| Replay | System damage (possible safety of life issues) | 1 | Authenticated message counter, timestamp |
| Software threats | Undesirable events System damage Enable other events | 2 | Acceptance testing Independent verification and validation (IVV) Code walkthroughs Automated code analysis Auditing |
| Unauthorized Access | Disruption of operations System damage | 2 | Encryption of TT&C data Authentication of commands Auditing |

### science missionS

Science Missions are a class of missions which are typically not considered operational or part of a national (or international) asset infrastructure.  In as much as this is the case, while the threats against such categories of missions are essentially the same as for other missions, the resulting risks are much less than against those where life or infrastructure may be disrupted.  In the case of science missions, while money was spent to gather the information, only the monetary investment and the data collection will be lost.  Science missions tend to fall into three subclasses:

- Near earth/earth orbit

- Lunar

- Interplanetary/deep-space.

Near earth and earth orbit missions will be similar to other LEO, MEO and GEO missions although because they are not part of an ‘operational infrastructure,’ the resulting risks will be diminished.

Lunar missions and interplanetary/deep-space missions are similar to one another.  However, they take on multiple threat characteristics depending on whether they are in earth-orbit before beginning their cruise phase, in cruise, or in some cases, in a sling-shot trajectory where they leave earth orbit, go into a cruise but come back to near-earth for a sling-shot effect to a more distant encounter.

While in earth orbit or near-earth, these missions are just like the other LEO, MEO, and GEO missions.  However, their threat characteristics change with time since they will move in and out of earth orbit.

When they finally leave earth orbit, they both require more power to communicate with than earth orbit spacecraft, they both have a non-orbit cruise phase while in transit from the Earth to their target destination(s), and they both will have limited viewing from the Earth once in orbit or when landed at their respective destination(s).  However, where these missions differ is in the amount of power and the size of the earth station antennas required for communication.  Interplanetary/deep-space missions require significantly more power and large dishes for reliable communications than do lunar missions.  Likewise, interplanetary/deep-space missions suffer from much longer communications latency than do lunar missions.  As a result, interplanetary missions, with their longer round-trip communications, the increased power, and the size of the dishes required provide immunity from ‘casual’ attack although not from hostile ‘nation-state’ attacks.

But what must be remembered is that both lunar and interplanetary missions also must take into account the threats faced by earth orbit and near-earth missions because they often find themselves in those orbits early in their lives.

A threat analysis for international science category missions is illustrated in table 4-4.

Table 4-4:  Science Mission Threat Analysis

| Applicable Threats | Impacts | Probability (1=Lowest, 5=Highest) | Security Mechanisms to Counter Threat |
| --- | --- | --- | --- |
| Data corruption | Modification of information System damage | 3 | Data integrity schemes (hashing, check values, digital signatures) |
| Ground facility physical attack | Loss of command, control, and data | 2 | Guards, gates, access control |
| Interception | Loss of sensitive data | 1 (deep-space) 3 (lunar) 3 (earth) | Evaluation COTS product use |
| Jamming | Loss of TT&C and/or traffic circuits Commercial impact Possible safety impact | 1 (deep-space) 2 (lunar) 3 (earth) | Multiple uplink and downlink paths Multiple access points Frequency hopping Spread spectrum |
| Masquerade | Potential to disrupt operations (uplink) Potential to receive false information (downlink) | 2 | Strong authentication of uplinked commands and downlinked data Access control scheme Vetting of staff No use of open networks |
| Replay | System damage | 1 | Authenticated message counter, timestamp |
| Software threats | Undesirable events System damage | 2 | Acceptance testing Independent verification and validation (IVV) Code walkthroughs Automated code analysis Auditing |
| Unauthorized Access | Disruption of operations System damage Potential loss of mission | 3 | Authentication of commands Access control in control center Access control in cross support network No use of open networks Auditing |

### Navigation satellites

Navigation satellites such as the Global Positioning System (GPS) are irreplaceable for enterprises such as airlines, maritime, trucking, and the military.  Similarly, navigation satellites are being used for private use in automobile navigation systems, cellular telephones for emergency locating, and via hand-held units in hunting, exploring, and hiking. Like communications satellites, the loss of navigation satellite systems would result in not only loss of investment dollars but there is also the high potential for the loss of life, safety, and infrastructure.  A threat analysis of such a mission category is illustrated in table 4-5.

Table 4-5:  Navigation Satellite Threat Analysis

| Applicable Threats | Impacts | Probability (1=Lowest, 5=Highest) | Security Mechanisms to Counter Threat |
| --- | --- | --- | --- |
| Data Corruption | Modification of information System damage | 3 | Data integrity schemes (hashing, check values, digital signatures) |
| Ground facility physical attack | Loss of command, control, and data | 3 | Guards, gates, access control, backup sites(s) |
| Interception | Loss of sensitive data | 1 | Evaluation COTS product use |
| Jamming | Loss of TT&C and/or traffic circuits Commercial impact Possible safety impact | 3 | Multiple uplink and downlink paths Multiple access points Frequency hopping Spread spectrum |
| Masquerade | Potential to disrupt operations | 2 | Strong authentication Access control scheme Vetting of staff No use of open networks |
| Replay | System damage | 1 | Authenticated message counter |
| Software threats | Undesirable events System damage | 2 | Acceptance testing Independent verification and validation (IVV) Code walkthroughs Automated code analysis Auditing |
| Unauthorized Access | Disruption of operations System damage Potential loss of mission | 3 | Authentication of commands Access control in control center Access control in cross support network No use of open networks Auditing |

## Threat summary and Security Mechanisms to Counter THREATs

Table 4-6:  Threat Summary

| Applicable Threats | Security Mechanisms to Counter Threat |
| --- | --- |
| Data corruption | Data integrity schemes (hashing, check values, digital signatures) |
| Interception | Evaluation COTS product use Protection of traffic (potentially user responsibility) Protection of archive & distribution systems via encryption |
| Jamming | Multiple uplink paths Multiple access points Frequency hopping, spread spectrum |
| Masquerade | Access control scheme Vetting of staff No use of open networks |
| Replay | Data integrity schemes (e.g., encrypted command counter) |
| Software Threats | System evaluation COTS product use Continuous threat Monitoring, continuous risk management Auditing |
| Unauthorized Access | Encryption of TT&C and mission data Authentication of commands No use of open networks Access control in control center Access control in cross support network Access control in control and dissemination systems Multiple access paths Auditing |
| Ground facility physical attack | Guards Gates Access control |

## Communication Architecture and specific threats

Figure 4-1 illustrates threats that are the result of the architecture of the communication links from the principal investigator (or the commercial company selling the satellite product) to the satellite, at each possible link node.

Figure 4-1:  CCSDS Security Communications Threats

# Summary

This document provides a top-level threat analysis of various categories of civil space missions.  From this analysis, it is recognized that there are several high potential threat areas.

Unauthorized access is a potential threat against all mission types.  However, due to the fact that it is also a threat against all information technology infrastructure, there are many existing means by which this threat can be countered (e.g., identification and authentication to mediate access control).

Data corruption, while not entirely a security issue, is a major threat.  Data corruption may occur because of communications problems which can be solved by coding techniques.  However, data corruption may also occur as a result of hostile attacks aimed at denying service.  Various data integrity schemes such as integrity check values and digital signatures help prevent this from occurring.

Interception of data leading to loss of data confidentiality or replay of data is also a major threat.  However, this is also a well recognized threat against other information technology systems – whether communicating via landline or radio frequency.  Encryption technology along with key management and distribution will prevent the disclosure of the data to unauthorized entities.  In addition, the use of spread spectrum and frequency hopping technologies can help to prevent data interception as well as prevent link jamming.

Encryption and authentication also help prevent masquerade attacks.  Sequence counters which are encrypted help prevent replay attacks.

Software problems are also major threats.  Software problems may result from bad design, poor coding practices, lack of reviews, or lack of testing.  While flight-grade software is typically designed, developed, and tested under exacting processes, development methodologies such as promulgated by the Carnegie Mellon University Software Engineering Institute’s Capability Maturity Model Integration (CMMI) help to standardize and formalize the development environments to eliminate such threats.  However, there is another class of software threat which is the result of malicious attackers in the form of such entities as viruses, worms, and attacks against buffer overflows.  These types of threats will continue to be a problem because the ground-based information technology infrastructure has not yet successfully dealt with these to any satisfaction.  But with operational configuration management processes in place and with policies such as prohibiting the use of open networks, this threat can be managed.

Acronyms

CMMI 	Capability Maturity Model Integration

DDOS	Distributed Denial-Of-Service

GEO	geosynchronous earth orbit

ISS	International Space Station

IVV	Independent verification and validation

LEO	low earth orbit

MEO	Medium-Earth Orbit

TT&C	Tracking, Telemetry, and Command

VPN	Virtual Private Network

# Footnotes

By ‘technical means’ it is meant that a security mechanism implemented in hardware or software will be employed to counter the vulnerability.  By ‘policy’ it is meant that a security mechanism will not be employed but instead the vulnerability will be countered by a restriction (a policy) issued by the system managers responsible for ensuring the system’s security.

U.S. Defense Science Board Report on Security Controls for Computer Systems, January 1970.  http://www.rand.org/publications/R/R609.1/R609.1.html

More specifics will be found in the planned-to-be-written CCSDS Mission Planners Guide for Security

These threats, the impacts, and the security mechanisms to counter the threats are illustrative only and do not reflect what is actually being done on the International Space Station.

These probabilities (in this and all subsequent tables) are for illustrative purposes only and will change for specific missions.

Capability Maturity Model Integration (CMMI), version 1.1; CMU/SEI-2002-TR-011

# Text boxes

Identify generic 
threats to space missions

Construct Representative Mission Scenarios

Assess impact of threat on each scenario

Identify candidate security mechanisms to counter each threat

If considered viable and not counterable, threat becomes a vulnerability

1.  Manned space flight
2.  Meteorological satellites 
3.  Communications satellites
4.  Science missions
5.  Navigation satellites

Space Debris

Users

Control

Space Elements

Unauthorised Access 
(virtual or physical) 
(Insider/Outsider)

Interception of Data (theft)

Replay

Software Threats

Hardware Failure

Communications Link Jamming

Traffic Analysis

System/
Network

Files: Theft, Copying, Unauthorized Access

Crosstalk

Radiation

Crosstalk

Radiation

Radiation

Systems People: 
Reveal protective measures, disable protective measures

PROCESSORS

NETWORK SWITCHES

Taps

Radiation

Hardware Failures contributing to software failures

Software Failures: Failure of protection features: access control, bounds control, etc.

Maintenance Personnel:
Disable hardware/software protection

Users: Identification,
Authentication

Comm Lines

Taps