# space internetworking services area

## Unacknowledged-CFDP Working Group

| Title of Group | 6.2 Unacknowledged-CFDP Working Group |
| --- | --- |
| Chair | Scott Burleigh |
| Area Director | Robert Durst |
| Mailing List | sis-uce@mailman.ccsds.org |

### Rationale

In order to operate properly over unit-data transfer (UT) layer implementations that perform their own retransmission, CFDP in unacknowledged mode must better tolerate the routine arrival of metadata and file data after the arrival of the EOF PDU for the same transaction.  A simple solution would be for EOF arrival to trigger a timer cycle, similar to the NAK timer cycle in acknowledged mode, which checks transaction completeness periodically.

### Goals

- Draft the CFDP Recommendation revisions needed to effect this new behavior;

- Modify a CFDP implementation to comply with the revised specification.  Note:  Because the revised procedures are unilateral (there is no reciprocal protocol traffic), there is no interoperability issue;

- Demonstrate the modified implementation;

- Submit the revisions for incorporation into the CCSDS Recommended Standard for CFDP.

### Schedule and Deliverables

| Date | Milestone |
| --- | --- |
| 31 October 2003 | WG established |
| 14 November 2003 | Published proposed revisions to CCSDS 727.0-B-1 as a proposed Standard |
| 19 December 2003 | JPL demonstration of initial implementation of the proposed Standard; WG analyzes results |
| 12 November 2004 | Publish final revisions (“pink sheets”) as a draft Standard |
| 15 November 2004 - 7 February 2005 | Agency Formal Reviews |
| 7 February 2005 | Submit draft Standard for acceptance as a Recommended Standard, revising CCSDS 727.0-B-2 |
| 8 April 2005 | File resolution requesting publication of the revised Recommended Standard. |
| 6 June 2005 | File resolution dissolving the Working Group. |

### Risk Management Strategy

#### Technical Risks

The problem and proposed solution are well understood, as they are derived from existing, tested CFDP functionality.  Technical risk is minimal.

#### Management Risks

Programmatic risks:

- Unavailability of resources could delay achievement of milestones.  Fallback option would be to reschedule the milestones.

- Because the proposed solution is backward-compatible with existing implementations, agency opposition should be minimal.  In the event of unanticipated opposition from one or more member agencies, achievement of consensus on the proposed revisions to CFDP could be delayed.  Fallback option would be to reschedule the milestones or cancel the work item.