IP Over CCSDS Space Links

Concept Paper

August 2, 2005

Keith Hogie

Annex C: IP over Serial Stream Encapsulation

CCSDS provides the VCA and MAPA octet stream transfer services for accommodating serial streams e.g., HDLC bit streams over CCSDS space links.

It is critical for the ground to supply a gated clock along with the VCA or MAPA data stream. The gated clock stops when no data is on the line. This can occur due to data outages at the tracking station or when switching virtual channels. Without the use of a gated clock, fictitious data can be created or data from another virtual channel can be mixed in unexpectedly.

See Figure 3 below.

Figure C-1: IP over Serial Stream/CCSDS Links

ANNEX D: Network Views

Figure D-1: IP over CCSDS/Serial Streams – Network View

Figure D-2: IP over CCSDS/Serial Streams – Network View

A key issue is that IP packets inside HDLC cannot be processed as a byte stream and aligned with any CCSDS data structures.  HDLC frames are not an integral number of bytes and must be treated as a simple bitstream.  This has the advantage that there is no encapsulation information required and the HDLC bitstream has no special relationship to the physical layer it rides on.  The HDLC bitstream can be passed uncoded or with bit or block coding schemes.  The main issue is that whatever coding is added at RF transmission time be removed at RF receipt time and only the data bits passed on.  This isolates coding and modulation details to the equipment directly connected to each end of the RF link and no other equipment needs to know anything about the RF link details.  This sort of isolation becomes very useful when one satellite using one type of coding and modulation wants to communicate with some other system that uses different coding and modulation.  Since the coding and modulation only exist on each RF link, it is easier to pass data between systems.

The following diagrams show options for running IP over an HDLC bitstream over various Physical RF links.  The diagrams show the way that current IP spacecraft are implemented and future ones are being built.  They include various Physical layer forward-error-correction (FEC) schemes including no FEC, convolutional coding, and Reed/Solomon coding.  In all cases the FEC coding or lack thereof is completely independent of the bitstream containing the link level frames.  This model is the standard model that has been used for over 10 years in the commercial world when data is transmitted over satellite links.  The details of the FEC coding and Physical layer RF modulation are completely transparent to the Link layer framing.  This allows the Physical layer FEC coding to be changed completely independent of the Link layer framing.  Commercial satellite modems commonly support many combinations of convolutional coding, R/S coding, Turbo codes, LDPC codes, and other options.  This separation allow for easy insertion of new FEC codes without any modification of the hardware on the sides of the satellite modem away from the RF link.

These architectures do all utilize a gated clock on the receiving sides since the amount of coded bits flowing across the RF link may not be equal to the amount of decoded bits delivered to the routers or end systems on either side.  The gated clock does not matter for no coding or convolutional coding since there is always a constant stream of bits coming out of the receiver.  However, with block codes such as R/S, Turbo, or LDPC, coded bits are flowing into the receiver and the sync pattern and code bits get removed so the output clock must stop during the sync pattern and code bits since only the data bits come out of the modem.

Figure x - IP over HDLC with no FEC coding on RF link

Figure x - IP over HDLC with Convolutional FEC on RF link

Figure x - IP over HDLC with CCSDS R/S FEC coding on RF link

ANNEX E: Acronym List

AOS		Advanced Orbiting Systems

ARQ		Automatic Repeat Request

BOF		Birds Of a Feather

CCSDS	Consultative Committee for Space Data System

ECAP		Encapsulation (Packet Service)

EPI		Encapsulated Protocol Identifier

GMAP	ID	Global Multiplexer Access Point Identifier

GVCID	Global Virtual Channel Identifier

HDLC		High-level Data Link Control (protocol)

IP		Internet Protocol

IPv4		Internet Protocol Version 4

IPv6		Internet Protocol Version 6

MAP ID	Multiplexer Access Point Identifier

MAP_SDU	Multiplexer Access Point Service Data Unit

MAPA		MAP Access (Service)

MAPP		MAP Packet (Service)

MCID		Master Channel Identifier

OSI                 Open Systems Interconnection

Prox-1		Proximity-1

PVN		Packet Version Number

RCF		Return Channel Frame Service (SLE Service)

RFC		Request for Comment

SAP		Service Access Point

SCID		Spacecraft Identifier

SDU		Service Data Unit

SLE		Space Link Extension

TC		Telecommand (pertains to TC Space Data Link Protocol)

TCP		Transmission Control Protocol

TFVN		Transfer Frame Version Number

TM		Telemetry (pertains to TM Space Data Link Protocol)

UDP		User Datagram Protocol

VC		Virtual Channel

VCID		Virtual Channel Identifier

VCA		Virtual Channel Access (Service)

VCA_SDU	Virtual Channel Access Service Data Unit

VCP		Virtual Channel Packet (Service)

VCID		Virtual Channel Identifier