SIS-IPO WG Meeting Minutes

Colorado Springs, CO USA

April 20, 2009

Main Results of this meeting:

1. SIS-IPO will hold off on creating a resolution to progress the IP over CCSDS RED-3 draft magenta book to Blue. Reason is the WG felt it was important to have the SLS-SLP WG create a new project to depreciate IPv4 and SCPS-NP as recognized CCSDS packet versions. By depreciating these IDs, there will no longer be a CCSDS recommendation to directly insert IPv4 and SCPS-NP datagrams into CCSDS transfer frames (AOS, TM, TC, Proximity-1). Therefore, the only was to transfer these datagrams across the space link will be by using the CCSDS Encapsulation Service.

Action Item on Greg Kazz: Work will be undertaken to remove all direct insertion related text of IPv4, SCPS-NP etc in the IP over CCSDS RED-3 book. The book will then be reviewed by the entire WG. The goal is to finish a successful review of the document and generate a resolution to go blue on IP over CCSDS at the Fall 2009 meeting in Noordwijk.

2. Loren Clare gave his report on Interoperability Testing of the CCSDS IPE (Internet protocol extension) i.e., one or more bytes that are pre-pended to the IP PDU before it is placed into a CCSDS Encapsulation packet. As of this meeting, Interoperability testing between GSFC and JPL had not yet been completed. It was recommended that the testing completed within 60 days of this meeting to ensure the CMC adequate time to either approve/disapprove the addition of Annex A to the Space Link Identifiers Blue Book. Action on Loren Clare and Dave Israel to make this happen.

3. The WG recommended that the Encapsulation Pink sheet go forward as a new version of the Blue book.

4. The WG also recommended that the Space Link Identifiers Pink sheets which introduce the CCSDS IPE in Annex A and remove the protocol Ids for IPv4 and IPv6 progress to Blue as well.

5. In parallel with this meeting, NASA and other space agencies have been discussing the need to create new work items for this WG. The new focus will be on the implementation, management and operations of IP internetworking in Space. The idea is to create work projects within this working group to create both a Magenta and a Green book that provide recommendations and concepts and rationale for configuring, managing, and operating IP networks in Space. These draft projects have been added to the CCSDS Framework under IP over CCSDS WG (see http://cwe.ccsds.org/fm/Lists/Projects/AllItems.aspx and look under 6.6). Both projects have been approved by the SIS AD, Bob Durst.