Draft Recommendation for
Space Data System Standards

Digital Motion Imagery

Proposed Draft Recommended Standard

CCSDS 766.1-R-0

Proposed Red Book

January 2013

AUTHORITY

|  | Issue: | Proposed Red Book, Issue 0 |  |
| --- | --- | --- | --- |
|  | Date: | January 2013 |  |
|  | Location: | Not Applicable |  |

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF AUTHORITY:)

This document has been approved for publication by the Management Council of the Consultative Committee for Space Data Systems (CCSDS) and represents the consensus technical agreement of the participating CCSDS Member Agencies.  The procedure for review and authorization of CCSDS documents is detailed in Organization and Processes for the Consultative Committee for Space Data Systems (CCSDS A02.1-Y-3), and the record of Agency participation in the authorization of this document can be obtained from the CCSDS Secretariat at the address below.

This document is published and maintained by:

CCSDS Secretariat

Space Communications and Navigation Office, 7L70

Space Operations Mission Directorate

NASA Headquarters

Washington, DC 20546-0001, USA

STATEMENT OF INTENT

(WHEN THIS RECOMMENDED STANDARD IS FINALIZED, IT WILL CONTAIN THE FOLLOWING STATEMENT OF INTENT:)

The Consultative Committee for Space Data Systems (CCSDS) is an organization officially established by the management of its members. The Committee meets periodically to address data systems problems that are common to all participants, and to formulate sound technical solutions to these problems. Inasmuch as participation in the CCSDS is completely voluntary, the results of Committee actions are termed Recommended Standards and are not considered binding on any Agency.

This Recommended Standard is issued by, and represents the consensus of, the CCSDS members.  Endorsement of this Recommendation is entirely voluntary. Endorsement, however, indicates the following understandings:

o	Whenever a member establishes a CCSDS-related standard, this standard will be in accord with the relevant Recommended Standard. Establishing such a standard does not preclude other provisions which a member may develop.

o	Whenever a member establishes a CCSDS-related standard, that member will provide other CCSDS members with the following information:

--	The standard itself.

--	The anticipated date of initial operational capability.

--	The anticipated duration of operational service.

o	Specific service arrangements shall be made via memoranda of agreement. Neither this Recommended Standard nor any ensuing standard is a substitute for a memorandum of agreement.

No later than five years from its date of issuance, this Recommended Standard will be reviewed by the CCSDS to determine whether it should: (1) remain in effect without change; (2) be changed to reflect the impact of new technologies, new requirements, or new directions; or (3) be retired or canceled.

In those instances when a new version of a Recommended Standard is issued, existing CCSDS-related member standards and implementations are not negated or deemed to be non-CCSDS compatible.  It is the responsibility of each member to determine when such standards or implementations are to be modified.  Each member is, however, strongly encouraged to direct planning for its new standards and implementations towards the later version of the Recommended Standard.

FOREWORD

This document identifies which television and video industry standards should be utilized for interoperability between spacecraft, spacecraft-to-ground, ground-to-spacecraft, and ground-to-ground applications.  The international television and video industries have many standards and interfaces for acquiring, recording and distributing live and recorded video.  That flexibility can lead to complexity when attempting to share or monitor video from acquisition to monitoring or recording locations.  This document provides system designers a sub-set of the larger industry set of standards to choose from, depending on the application and purpose of the video system.

Through the process of normal evolution, it is expected that expansion, deletion, or modification of this document may occur.  This Recommended Standard is therefore subject to CCSDS document management and change control procedures, which are defined in the Procedures Manual for the Consultative Committee for Space Data Systems.  Current versions of CCSDS documents are maintained at the CCSDS Web site:

http://www.ccsds.org/

Questions relating to the contents or status of this document should be addressed to the CCSDS Secretariat at the address indicated on page i.

At time of publication, the active Member and Observer Agencies of the CCSDS were:

Member Agencies

- Agenzia Spaziale Italiana (ASI)/Italy.

- Canadian Space Agency (CSA)/Canada.

- Centre National d’Etudes Spatiales (CNES)/France.

- China National Space Administration (CNSA)/People’s Republic of China.

- Deutsches Zentrum für Luft- und Raumfahrt e.V. (DLR)/Germany.

- European Space Agency (ESA)/Europe.

- Federal Space Agency (FSA)/Russian Federation.

- Instituto Nacional de Pesquisas Espaciais (INPE)/Brazil.

- Japan Aerospace Exploration Agency (JAXA)/Japan.

- National Aeronautics and Space Administration (NASA)/USA.

- UK Space Agency/United Kingdom.

Observer Agencies

- Austrian Space Agency (ASA)/Austria.

- Belgian Federal Science Policy Office (BFSPO)/Belgium.

- Central Research Institute of Machine Building (TsNIIMash)/Russian Federation.

- China Satellite Launch and Tracking Control General, Beijing Institute of Tracking and Telecommunications Technology (CLTC/BITTT)/China.

- Chinese Academy of Sciences (CAS)/China.

- Chinese Academy of Space Technology (CAST)/China.

- Commonwealth Scientific and Industrial Research Organization (CSIRO)/Australia.

- CSIR Satellite Applications Centre (CSIR)/Republic of South Africa.

- Danish National Space Center (DNSC)/Denmark.

- Departamento de Ciência e Tecnologia Aeroespacial (DCTA)/Brazil.

- European Organization for the Exploitation of Meteorological Satellites (EUMETSAT)/Europe.

- European Telecommunications Satellite Organization (EUTELSAT)/Europe.

- Geo-Informatics and Space Technology Development Agency (GISTDA)/Thailand.

- Hellenic National Space Committee (HNSC)/Greece.

- Indian Space Research Organization (ISRO)/India.

- Institute of Space Research (IKI)/Russian Federation.

- KFKI Research Institute for Particle & Nuclear Physics (KFKI)/Hungary.

- Korea Aerospace Research Institute (KARI)/Korea.

- Ministry of Communications (MOC)/Israel.

- National Institute of Information and Communications Technology (NICT)/Japan.

- National Oceanic and Atmospheric Administration (NOAA)/USA.

- National Space Agency of the Republic of Kazakhstan (NSARK)/Kazakhstan.

- National Space Organization (NSPO)/Chinese Taipei.

- Naval Center for Space Technology (NCST)/USA.

- Scientific and Technological Research Council of Turkey (TUBITAK)/Turkey.

- Space and Upper Atmosphere Research Commission (SUPARCO)/Pakistan.

- Swedish Space Corporation (SSC)/Sweden.

- United States Geological Survey (USGS)/USA.

PREFACE

This document is a draft CCSDS Recommended Standard.  Its ‘Red Book’ status indicates that the CCSDS believes the document to be technically mature and has released it for formal review by appropriate technical organizations.  As such, its technical contents are not stable, and several iterations of it may occur in response to comments received during the review process.

Implementers are cautioned not to fabricate any final equipment in accordance with this document’s technical content.

Recipients of this draft are invited to submit, with their comments, notification of any relevant patent rights of which they are aware and to provide supporting documentation.

# DOCUMENT CONTROL

| Document | Title | Date | Status |
| --- | --- | --- | --- |
| CCSDS 766.1-R-0 | Digital Motion Imagery, Proposed Draft Recommended Standard, Issue 0 | January 2013 | Current draft |

# CONTENTS

Section	Page

1	Introduction	1-1

1.1	Purpose and Scope	1-1

1.2	applicability	1-1

1.3	NOMENCLATURE	1-1

1.4	References	1-2

2	Overview	2-1

3	Specification	3-1

3.1	Overview	3-1

3.2	General	3-1

3.3	INTERFACE STANDARDS	3-1

3.4	VIDEO FORMAT AND CHARACTERISTICS	3-3

3.5	Audio	3-10

3.6	Real-Time Video Encapsulation AND Transmission	3-11

3.7	ReCorded Video and Audio	3-12

3.8	Distribution of video data	3-13

ANNEX A	Protocol Implementation  Conformance 
Statement (PICS) Proforma  (normative)	A-1

ANNEX B	Security, SANA, and Patent Considerations  (Informative)	B-1

ANNEX C	DTN Bundle Protocol for Video Transmission  (Informative)	C-1

ANNEX D	Informative References  (Informative)	D-1

ANNEX E	Abbreviations  (Informative)	E-1

Figure

3-1	Video System Elements—Non-Compressed Video Design	3-9

3-2	Video System Elements—Compressed Video Design	3-10

# Introduction

## Purpose and Scope

The purpose of this document is to provide a common reference and framework of standards for digital motion video and imagery, and to provide recommendations for utilization of international standards for sharing or distributing motion video and imagery between spacecraft elements and ground systems.

The scope of this document includes traditional real-time streaming video and television, including spacecraft-to-spacecraft and spacecraft-to-ground systems, as well as video recorded and streamed later, either in real time or as a file transfer.  In this context, real-time streaming includes all modes where video is sent from a spacecraft in a contiguous stream and is intended for immediate use when it is received, regardless of the latency of the transmission path.  Other specialized motion imagery applications, such as high-speed scientific motion imagery and multi-spectral motion imagery, are not addressed in this document.  However, if a specialized imagery camera system has a requirement to interface to spacecraft systems in a video mode, it would be required to match these interfaces.

Ground systems-to-ground systems video distribution is obviously a key component of the entire video distribution system.  However, this is not the primary focus of this document.  Presently, there are significant differences in the ways mission video products are exchanged between the various space agencies.  This is the result of differences in agreements for video sharing and networks between the space agencies.  Those differences preclude there being a standard methodology for delivering video imagery between agencies.  Prior to the commencement of video transmission between space agencies, system design reviews and performance testing should be done between the ground systems in use to assure operability when video imagery comes from spacecraft.

## applicability

This document is a CCSDS Recommended Standard.  It is intended for all missions that produce, consume, or transcode video imagery in the scope of web streaming through high-definition imagery.

## NOMENCLATURE

### Normative Text

The following conventions apply for the normative specifications in this Recommended Standard:

- the words ‘shall’ and ‘must’ imply a binding and verifiable specification;

- the word ‘should’ implies an optional, but desirable, specification;

- the word ‘may’ implies an optional specification;

- the words ‘is’, ‘are’, and ‘will’ imply statements of fact.

NOTE	–	These conventions do not imply constraints on diction in text that is clearly informative in nature.

### Informative Text

In the normative sections of this document, informative text is set off from the normative specifications either in notes or under one of the following subsection headings:

- Overview;

- Background;

- Rationale;

- Discussion.

## References

The following publications contain provisions which, through reference in this text, constitute provisions of this document.  At the time of publication, the editions indicated were valid.  All publications are subject to revision, and users of this document are encouraged to investigate the possibility of applying the most recent editions of the publications indicated below.  The CCSDS Secretariat maintains a register of currently valid CCSDS publications.

[1]	Studio Encoding Parameters of Digital Television for Standard 4:3 and Wide Screen 16:9 Aspect Ratios.  ITU-R BT.601-7.  Geneva: ITU, 2011.

[2]	Television—SDTV Digital Signal/Data—Serial Digital Interface.  SMPTE ST 259:2008.  White Plains, New York: SMPTE, 2008.

[3]	Digital Interfaces for HDTV Studio Signals.  ITU-R BT.1120-8.  Geneva: ITU, 2012.

[4]	1.5 Gb/s Signal/Data Serial Interface.  SMPTE ST 292-1:2012.  White Plains, New York: SMPTE, 2012.

[5]	Serial Digital Interface-Based Transport Interface for Compressed Television Signals in Networked Television Production Based on Recommendation ITU-R BT.1120.  ITU-R BT.1577.  Geneva: ITU, 2002.

[6]	Television—Serial Data Transport Interface (SDTI).  SMPTE ST 305:2005.  White Plains, New York: SMPTE, 2005.

[7]	Teletext Systems.  ITU-R BT.653-3.  Geneva: ITU, 1998.

[8]	Television—Time and Control Code.  SMPTE ST 12-1:2008.  White Plains, New York: SMPTE, 2008.

[9]	Television—Transmission of Time Code in the Ancillary Data Space.  SMPTE ST 12-2:2008.  White Plains, New York: SMPTE, 2008.

[10]	Ancillary Data Packet and Space Formatting.  SMPTE ST 291:2011.  White Plains, New York: SMPTE, 2011.

[11]	Vertical Ancillary Data Mapping of Caption Data and Other Related Data.  SMPTE ST 334-1:2007.  White Plains, New York: SMPTE, 2007.

[12]	Metadata Element Dictionary Structure.  SMPTE ST 335:2012.  White Plains, New York: SMPTE, 2012.

[13]	Metadata Dictionary Registry of Metadata Element Descriptions.  SMPTE RP 210.10:2007.  White Plains, New York: SMPTE, 2007.

[14]	1280×720, 16:9 Progressively-Captured Image Format for Production and International Programme Exchange in the 60 Hz Environment.  ITU-R BT.1543.  Geneva: ITU, 2001.

[15]	1280 x 720 Progressive Image 4:2:2 and 4:4:4 Sample Structure—Analog and Digital Representation and Analog Interface.  SMPTE ST 296:2012.  White Plains, New York: SMPTE, 2012.

[16]	Parameter Values for the HDTV Standards for Production and International Programme Exchange.  ITU-R BT.709-5.  Geneva: ITU, 2002.

[17]	Television—1920 x 1080 Image Sample Structure, Digital Representation and Digital Timing Reference Sequences for Multiple Picture Rates.  SMPTE ST 274:2008.  White Plains, New York: SMPTE, 2008.

[18]	Dual Link 1.5 Gb/s Digital Interface for 1920 x 1080 and 2048 x 1080 Picture Frames.  SMPTE ST 372:2011.  White Plains, New York: SMPTE, 2011.

[19]	Television—3 Gb/s Signal/Data Serial Interface.  SMPTE ST 424:2006.  White Plains, New York: SMPTE, 2006.

[20]	Information Technology—Coding of Audio-Visual Objects—Part 10: Advanced Video Coding.  International Standard, ISO/IEC 14496-10.  7th ed.  Geneva:  ISO, 2012.

[21]	Advanced Video Coding for Generic Audiovisual Services.  ITU-T H.264.  Geneva: ITU, 2012.

[22]	Data Services in Digital Television Broadcasting.  ITU-R BT.1301-1.  Geneva: ITU, 2011.

[23]	Interface for Digital Component Video Signals in 525-Line and 625-Line Television Systems Operating at the 4:2:2 Level of Recommendation ITU-R BT.601.  ITU-R BT.656-5.  Geneva: ITU, 2007.

[24]	Information Technology—JPEG 2000 Image Coding System: Motion JPEG 2000.  International Standard, ISO/IEC 15444-3:2007.  2nd ed.  Geneva:  ISO, 2007.

[25]	Information Technology—Generic Coding of Moving Pictures and Associated Audio Information—Part 7: Advanced Audio Coding (AAC).  International Standard, ISO/IEC 13818-7.  4th ed.  Geneva:  ISO, 2006.

[26]	Digital Audio Interface—Part 3: Consumer Applications.  Ed. 3.1 Consol. with am1.  IEC 60958-3.  Geneva: IEC, 2009.

[27]	IP over CCSDS Space Links.  Recommendation for Space Data System Practices, CCSDS 702.1-B-1.  Blue Book.  Issue 1.  Washington, D.C.: CCSDS, forthcoming.

[28]	J. Postel.  User Datagram Protocol.  STD 6.  Reston, Virginia: ISOC, August 1980.

[29]	Licklider Transmission Protocol (LTP) for CCSDS.  Draft Recommendation for Space Data System Standards, CCSDS 734.1-R-2.  Red Book.  Issue 2.  Washington, D.C.: CCSDS, February 2012.

[30]	CCSDS Bundle Protocol Specification.  Draft Recommendation for Space Data System Standards, CCSDS 734.2-R-1.  Red Book.  Issue 1.  Washington, D.C.: CCSDS, February 2012.

[31]	CCSDS File Delivery Protocol (CFDP).  Recommendation for Space Data System Standards, CCSDS 727.0-B-4.  Blue Book.  Issue 4.  Washington, D.C.: CCSDS, January 2007.

# Overview

In the early days of human spaceflight, motion imagery was accomplished with motion picture cameras, set at varying frame rates depending on lighting conditions.  Upon safe return the film was processed and eventually shared with the world via documentaries or television.  Inevitably live video became operationally desirable for situational awareness and to satisfy the public’s interest in high-profile events such as the Moon landings or the Apollo-Soyuz test project.  Compromises were made with those first video systems to fit within the constraints of bandwidth, avionics, and transmission systems.  Even in the modern era, video systems on spacecraft are a hybrid of analog and digital systems, typically made to work within the existing spacecraft’s avionics, telemetry, and command/control systems.

With the advent of digital cameras, encoding algorithms, and modulation techniques, it is desirable to treat video as data and utilize commercially available technologies to capture and transmit live and recorded motion imagery, possibly in High Definition (HD) or even better.  Thus the Recommended Standard addresses:

- Video Interfaces and Characteristics

- Video Formats and Characteristics

Video data has a number of characteristics which need definitions such as frame rate, aspect ratio, bandwidth and compression standards, color sampling, the inclusion of audio, etc.

- Encapsulation and Transmission Protocols

Video data needs to be encapsulated, transported, and distributed.  Although the choice of mechanisms and protocols may not be specific to video data, certain aspects need addressing because of the high bandwidth typically required of video.  Thus this part will address encapsulation schemes (e.g., IP), transport protocols, and use of CCSDS Encapsulation Packets.

- Interoperability of Standards

Future Human Spaceflight endeavors are expected to be collaborations between many agencies, with complex interactions between spacecraft, and Lunar/Mars surface systems, with intermediate locations (EVA crew, habitats, etc.) requiring the ability to view video generated by another agency’s systems.  Therefore interoperability between these systems will be essential to mission success and in some cases crew safety.  Such interoperability will only be achieved by use of common references and joint agreement on international standards, either commercial or CCSDS or a combination of the two.

This Recommended Standard does not cover video quality.  The intention of this document is to provide a framework of standards to ensure interoperability, not define a level of quality.  What is acceptable video quality varies widely with the application and requirements of users.  A science experiment, for example, may have video quality requirements beyond what is available, or practical, within a spacecraft avionics system.  The science team for that experiment might elect to record video on board at a high quality level and transfer video files after the conclusion of the experiment run.  They might elect to do that and have a real-time downlink of lesser quality as a confirmation the experiment is working properly.  A requirement for real-time video to support a docking event might sacrifice spatial resolution to lower the latency of the real-time video feed.  Within the parameters listed in this document and the capabilities of any given spacecraft, users and controllers will determine how equipment should be configured for the best match to requirements.

# Specification

## Overview

There are many system configurations that can be implemented in spacecraft video systems.  Choices of interface standards, resolutions, and frame rates are based on the application, user requirements, available equipment, and spacecraft capability.  Referencing the two figures following 3.4.5, it can be seen there are multiple ways for signals to flow from the image source through to the spacecraft avionics system and on to the ground.  Application of this Recommended Standard limits the overall number of options by limiting the interfaces to those that are in most common use.  It should be noted that while scientific imaging systems are excluded from this Recommended Standard, should one of those users need to interface to the spacecraft video system, the same interfaces would apply to them.  It would be incumbent upon the user to provide a matching interface from the user’s imaging system.

## General

Users shall select from the following interfaces and standards when designing and implementing new video systems for spacecraft.

## INTERFACE STANDARDS

### NON-COMPRESSED STANDARD DEFINITION TELEVISION SIGNALS

The interface for non-compressed standard definition television signals shall be Serial Digital Interface (SDI), conforming to

- ITU-R BT.601-7 (reference [1]);

- SMPTE ST 259:2008 (reference [2]).

### NON-COMPRESSED HIGH DEFINITION TELEVISION SIGNALS

The interface used for non-compressed high definition television signals shall be one of the following:

- High Definition-Serial Digital Interface (HD-SDI), conforming to

- ITU-R BT.1120-8 (reference [3]);

- SMPTE ST 292-1:2012 (reference [4]);

- High Definition Multimedia Interface (HDMI) 1.4 or higher, as defined by the HDMI Founders and licensed by HDMI Licensing, LLC;

- Camera Link Low Voltage Differential Signaling (LVDS) Interface Standard, as defined by the Camera Link Participating Companies.

### COMPRESSED DIGITAL TELEVISION SIGNALS

The interface used for compressed digital television signals shall be Digital Video Broadcasting-Asynchronous Interface (DVB-ASI), conforming to

- ITU-R BT.1577 (reference [5]);

- SMPTE ST 305:2005 (reference [6]).

NOTE	–	DVB-ASI would be used with compressed digital video while still in the serial digital domain.  For interfacing to spacecraft systems, Internet Protocol (IP) (see 3.6) is the preferred interface.

### Television Time Code and Metadata

Television time code and metadata may be inserted in non-compressed video.  Applicable standards for television time code and metadata are:

- ITU-R BT.653-3 (reference [7]);

- SMPTE ST 12-1:2008 (reference [8]);

- SMPTE ST 12-2:2008 (reference [9]);

- SMPTE ST 291:2011 (reference [10]);

- SMPTE ST 292-1-2012 (reference [4]);

- SMPTE ST 334-1:2007 (reference [11]);

- SMPTE ST 335:2012 (reference [12]);

- SMPTE RP 210.10:2007 (reference [13]).

NOTE	–	The standards listed above are primarily concerned with the serial digital standard-definition and high-definition interfaces listed in 3.3.1 and 3.3.2.  Metadata inserted at a camera conforming to HDMI or Camera Link interfaces conform to the serial digital interfaces when those signals are converted.

Compressed video signals in 3.3.3, per the standards listed in 3.3.3, shall carry all television time code and metadata information inserted into a non-compressed video stream.

## VIDEO FORMAT AND CHARACTERISTICS

### Video RESOLUTIONS

#### Overview

Traditionally, video resolution has been categorized as low resolution, standard definition, high definition, or high resolution.  Low resolution is generally defined as less than 640 × 480, standard definition as 640 × 480 and 768 × 576, high definition as 1280 × 720 and 1920 × 1080, and high resolution as anything beyond 1920 × 1080.  Low resolution was used for streamed Internet video.  Standard definition was used for broadcast (pre-HD) and security camera systems.  High definition was limited to high-end television broadcast.  High resolution was practically non-existent unless it was film based.  Now, however, the distinctions are less clear.  Laptop computer cameras are now often high definition, with options to stream from 320 × 240 up to 1280 × 720.  Standard-Definition is now leftover broadcast television, web streaming, and monitoring applications.  High definition has become the norm for broadcast and cable television.  High resolution cameras are replacing 35mm motion picture film for imaging requirements beyond HD.  Therefore, it is more difficult to classify video in terms of resolutions than in terms of application.  A given application can have a broad range of resolutions, depending upon the requirements of the user, available equipment, and bandwidth constraints.  The specifications below reflect the diversity of choices available for video systems.  Higher resolution applications, e.g., ‘public affairs’, can be used to fulfill lower resolution applications, e.g., ‘personal video conferencing’.

#### Personal Video Conferencing

Personal video conferencing video resolution should be selected from the following range:

- 320 × 240 to 1280 × 720, progressive scan.

NOTE	–	Selection of resolution is dependent on immediate requirement and available bandwidth.

#### Medical Conferencing

Medical conferencing video resolution should be selected from the following range:

- 320 × 240 to 1280 × 720, bandwidth-dependent progressive or interlace scan:

- standard definition legacy systems may be 525 or 576 interlace;

- 640 × 480 and 768 × 576 systems shall conform to ITU-R BT.601-7 (reference [1]) or SMPTE ST 259:2008 (reference [2]).

NOTE	–	Lower resolution personal video conferencing and medical conferencing applications are most likely to be performed using a personal computer or tablet-type device.  All video encoding would be handled internally.  Connection to the spacecraft avionics system would be through wired or wireless data connections independent of any video systems.  Transmission to the ground would also be handled as part of standard data protocols and also independent of dedicated video transmission.

#### Situational Awareness

Situational awareness video resolution should be selected from the following range:

- 640 × 480 to 1280 × 720, bandwidth dependent:

- interlace scan for legacy Standard Definition (SD) systems shall conform to

- ITU-R BT.601-7 (reference [1]); or

- SMPTE ST 259:2008 (reference [2]);

- progressive scan for HD systems shall conform to:

- ITU-R BT.1543 (reference [14]); or

- SMPTE ST 296:2011 (reference [15]).

NOTE	–	Situational awareness may be required in situations where only low-bandwidth transmission is available, such as S-Band, which would likely limit resolution to as low as 320 × 240.  In cases such as this, best effort is acceptable.  The requirement to have visual confirmation of events may be higher than a specific resolution.  This should be considered the exception and not the norm.

#### Public Affairs

Public affairs video resolution should be selected from the following range:

- 640 × 480 to 1280 × 720, bandwidth dependent:

- Interlace scan for legacy SD systems shall conform to

- ITU-R BT601-7 (reference [1]); or

- SMPTE ST 259:2008 (reference [2]);

- Progressive scan for HD systems shall conform to:

- ITU-R BT.1543 1280 (reference [14]); or

- SMPTE ST 296:2011 (reference [15]).

Multiple resolutions may be used to accommodate mission requirements.

NOTE	–	There are situations where HD formats are not required.  It saves considerable bandwidth to use SD systems.  Whether these are US or European standard resolutions and frame rates is not an issue.  Regardless of the actual video format, the interface standards allow virtually all current equipment to route and encode the video.  Once encoded and packetized, it is not an issue for spacecraft avionics as it is IP packets with a payload.  That part of the system is format agnostic.  Regardless of the interface chosen for a particular spacecraft, routing and encoding utilize the same components.

#### High Resolution Digital Imaging

High resolution digital imaging video resolution should have a minimum resolution of 1920 × 1080, progressive scan:

- 1080 HD systems shall conform to

- ITU-R BT.709-5 (reference [16]); or

- SMPTE ST 274:2008 (reference [17]);

- Up to 30 FPS shall conform to

- ITU-R BT.1120-8 (reference [3]); or

- SMPTE ST 292-1:2012 (reference [4]);

- Above 30 FPS shall conform to

- ITU-R BT.1120-8 (reference [3]); or

- SMPTE ST 372:2011 (reference [18]); or

- SMPTE ST 424:2006 [19].

NOTE	–	1920 × 1080 and above is to accommodate users with special requirements.  Typically, these systems will have on-board recording and downlink video as file transfers.  Any real-time requirement will entail the payload having to provide a compatible signal.

#### Spacecraft to Spacecraft

Spacecraft-to-spacecraft video resolution should follow 3.4.1.2-3.4.1.6.

NOTE	–	Selection of spacecraft-to-spacecraft video resolution is dependent on mission requirements.

### Frame Rate

Video frame rates shall be selected from the following ranges for the following applications:

- personal video conferencing: 10 – 60 Frames Per Second (FPS);

- medical video: 10 – 60 FPS;

- situational awareness: 25 – 60 FPS;

- public affairs: 24, 25, or 60 FPS;

- high resolution digital imaging: 24 – 60 FPS.

NOTE	–	These are considered optimum frame rates for these applications.  However, bandwidth constraints may not allow even the lower frame rates to be utilized.  In these cases, best effort should be made to accommodate the recommendations based on available bandwidth for imaging applications.

Spacecraft-to-spacecraft frame rates should be selected from 3.4.2.1 a)-e), above, depending on application.

NOTES

- Spacecraft-to-spacecraft frame rates are dependent on mission requirements.

- The listing of specific video applications above does not necessarily imply discrete equipment sets dedicated for each application. Most cameras, for example, can be used at multiple resolutions and frame rates allowing them to be used for multiple applications.

### Aspect Ratio

Aspect ratio of original material shall be maintained from origination through delivery to end-user.

NOTE	–	By definition within industry standards, HDTV resolution video has an aspect ratio of 16:9.

### Video Compression

#### Overview

The two compression standards listed have different applications.  MPEG-4 Part 10 is intended for real-time applications where live, or nearly live, video needs to be monitored at a ground location during an event or experiment.  JPEG2000 is intended for requirements for higher quality or where each individual frame needs to be maintained intact.  The data rate required for JPEG2000 would normally preclude JPEG2000 from being used for live transmission.  The normal operating mode for JPEG2000 is to record the video and downlink it later as a data file.

#### Compression Standards

The following video compression standards shall be used as indicated:

- MPEG-4 Part 10 (references [20] and [21]) for real-time transmission:

- 0.5 to 25 Mb/s—application and user requirement-driven data rates;

- 8-bit sampling;

- constant bit rate or variable bit rate acceptable—defined by interface to spacecraft system;

- Group of Pictures (GOP) from 1 – 30—defined by user requirement;

- metadata as required by user,

- shall conform to:

- ITU-R BT.1301-1 (reference [22]); or

- SMPTE ST 291:2011 (reference [10]); or

- ITU-R BT.656-4 (reference [23]) for ancillary data; or

- SMPTE ST 335:2001 (reference [12]); or

- SMPTE RP 210.10:2007 (reference [13]);

- shall be read and passed by encode/decode systems;

- may include system status and control feedback data;

- may include embedded television time code conforming to

- ITU-R BT.1301-1 (reference [22]); or

- SMPTE ST 12-1:2008 (reference [8]); or

- SMPTE ST 12-2:2008 (reference [9]).

NOTE	–	Per specification and established practice, embedded television time code is used as the time reference for the MPEG transport stream time code value.

- JPEG2000 (reference [24]) for analysis and high-quality recording requirements:

- 50 to 140+ Mb/s—application and user requirement-driven data rates limited to file transfer (non-real time);

- 10-bit Sampling;

- metadata as required by user

- shall conform to:

- SMPTE ST 291:2011 (reference [10]); or

- ITU-R BT.653-3 (reference [7]) for ancillary data; or

- SMPTE ST 335:2001 (reference [12]); or

- SMPTE RP 210.10:2007 (reference [13]).

- shall be read and passed by encode/decode systems;

- may include system status and control feedback data;

- may include embedded television time code.

NOTES

- JPEG2000, while normally considered a recording format with later file streaming, should be considered for real-time use in cases where latency is a critical factor.   JPEG2000 encodes one frame at a time, dividing the frame into sections.  While not as bandwidth efficient as MPEG-4, it has significantly lower encoding and decoding latency, typically 1 video frame.  In certain situations, such as situational awareness, this may be the more critical factor as compared to overall image quality.

- JPEG2000 may also be considered in situations where service interruptions of the video stream are common.  As JPEG 2000 does not use a GOP, interruptions are more easily tolerated than the same condition with MPEG-4 streams.

### Color Sampling

Color sampling should be as follows:

- 4:2:0 for real-time requirements;

- 4:2:2 for high resolution digital imaging:

- science and engineering;

- production and digital cinema applications;

- 4:4:4 for special applications.

### Discussion—Video System Block Diagrams

The diagrams below illustrate typical video system connectivity and what interfaces are associated with each stage in the system.  These diagrams assume separate components for each of these functions.  While the same functions occur with the use of a laptop or tablet based video system used for medical or personal video conferencing, they are internal with an IP connection to the spacecraft avionics system for transmission.

Figure 3-1:  Video System Elements—Non-Compressed Video Design

Figure 3-2:  Video System Elements—Compressed Video Design

## Audio

### Audio as part of video stream

Audio as part of a video stream should conform to the following standards:

- Advanced Audio Codec (AAC) (reference [25]) for compressed audio;

- AES/EBU-3 (reference [26]) for uncompressed audio.

NOTE	–	Generally, audio as part of a compressed bit-stream for live applications (MPEG-4) will be compressed.  There are several different audio codecs available.  AAC was chosen as the highest quality, most widely used audio codec for this application.  Non-compressed AES/EBU-3 is another possibility supported by a number of audio/video codecs.  It is less common, but might be a requirement based on user needs.

### Discussion—Audio Separate from Video Stream

For those applications where audio is distributed separately from video, audio/video synchronization (lip sync) is handled on the ground.  Time stamps in the audio stream, corresponding to time stamps in the video stream, are recommended to aid in synchronization.

## Real-Time Video Encapsulation AND Transmission

### Internet Protocol Transport Stream

MPEG-4-encoded video shall be formatted as Transport Stream (TS) with Packet Identification (PID) for transport in IP datagrams.

JPEG2000 encoded video for transmission shall be directly formatted into IP datagrams.

IP datagrams shall be encapsulated for transmission over the CCSDS space link as specified in reference [27].

### Elementary Stream

Real time video and audio elementary streams may be transmitted via User Datagram Protocol (UDP) (reference [28]).

### JITTER AND BIT ERROR RATES

Real-time video delivery jitter and Bit Error Rate (BER) shall be limited as follows:

- jitter (packet delay variation) not to exceed 10 ms (assumes 300 ms decoder buffer);

- BER not to exceed 1 × 10-6.

NOTES

- Use of elementary streams is possible for lower bandwidth video applications, such as personal video conferencing.  However, commercial hardware decoders do not recognize elementary streams, so transport stream should be used exclusively for video systems interfacing directly to spacecraft avionics.  Also, audio cannot be embedded with video when using elementary stream for compressed video transport.  Audio and video in an elementary stream are not synchronized for transmission.

- Real Time Protocol (RTP) and Hypertext Transfer Protocol (HTTP) are commonly used for video transmission.  HTTP is common for computer-based applications, such as family video conferencing.  In this application it is not only acceptable, but may be the only methodology available on that type of platform.  However, for higher bandwidth video transmission where transport streams are utilized, HTTP is not efficient.  RTP is acceptable, but UDP offers better performance over space based networks.  The use of TCP for video over space based networks is also not recommended.

## ReCorded Video and Audio

### Acquisition and Storage of video data

Recordings shall be file based to allow for transfer of recorded video data via established file transfer methodologies.

Encoding shall be MPEG-4 or JPEG 2000, dependent upon the application.

NOTE	–	Specific file formats will change based on systems being used.

### File Transfer of Recorded Video

#### Recorded File Transmission

Recorded video shall be transmitted as files via the CCSDS File Delivery Protocol (CFDP) Class 1 or Class 2 (reference [31]), and Delay Tolerant Networking (DTN) protocol (references [29] and [30]).

#### Discussion

##### CFDP

CFDP supports four classes that are distinct from the three video classes.  Each of the classes can be supported over the DTN Bundle Protocol (reference [30]) and DTN Licklider Transport Protocol (LTP) (reference [29]).

- Class 1—Unreliable CFDP Transfer (if over reliable DTN "UT layer" stack);

- Class 2—Reliable CFDP Transfer (if over unreliable DTN "UT layer" stack);

- Class 3—Unreliable Transfer Via One Or More Waypoints In Series;

- Class 4—Reliable Transfer Via One Or More Waypoints In Series.

Of these, only Class 1 and Class 2 are considered acceptable for use to perform file transfers of recorded video.

#### DTN

There are three classes of video transmission under DTN:

- File Transfer of Recorded Video;

- Mode 1 – Real Time Delivery, Best Effort;

- Mode 2 – Delayed Delivery, With Packet Restoration.

Annex C presents a narrative of the classes of real-time video transmission still under development by the DTN working group.

## Distribution of video data

### Real-Time Distribution

Real-time video shall be distributed as MPEG-4 program streams with resolution and frame rate dependent on available bandwidth and user requirements.

### Delayed Distribution

Video files should be distributed on the ground via established file distribution methodologies.

NOTE	–	For file transfer of video, this will likely be recorded JPEG 2000, as MPEG-4 will be used for real-time distribution.

### end user capabilities

End user capabilities should include:

- decoding capability for real-time video distribution:

format conversion as required to meet local user requirements for display (i.e., conversion from 525i to 625i and vice versa, 50/60 Hz frame rate conversion, up-conversion or down-conversion);

- ability to record data stream from real-time applications;

- ability to participate in and store video files from transfer operations;

- ability to decode and play the stored files.

Protocol Implementation 
Conformance Statement (PICS) Proforma

(normative)

Instructions for completing the PICS proforma

Overview

Columns

General

In order to reduce the size of tables in the PICS proforma, notations have been introduced that have allowed the use of a multi-column layout, where the columns are headed ‘Status’ and ‘Support’. The definition of each of these follows.

Status Column

The ‘Status’ column indicates the level of support required for conformance to the standard. The values are as follows:

M		Mandatory support is required.

O		Optional support is permitted for conformance to the standard.  If implemented, it must conform to the specifications and restrictions contained in the standard.  These restrictions may affect the optionality of other items.

O.n		The item is optional, but support of at least one of the options labeled with the same number n is mandatory.  The definitions for the qualification statements used in this annex are written under the tables in which they first appear.

C.n		The item is conditional (where n is the number which identifies the applicable condition). The definitions for the conditional statements used in this annex are written under the tables in which they first appear.

n/a		The item is not applicable.

Support Column

The ‘Support’ column is completed by the supplier or implementer to indicate the level of implementation of each feature. The proforma has been designed such that the only entries required in the ‘Support’ column are:

Y		Yes, the feature has been implemented.

N		No, the feature has not been implemented.

–		The item is not applicable.

Item Reference Numbers

Within the PICS proforma, each line that requires implementation detail to be entered is numbered at the left hand edge of the line. This numbering is included as a means of uniquely identifying all possible implementation details within the PICS proforma. The need for such unique referencing has been identified by the testing bodies.

The means of referencing individual responses is to specify the following sequence:

- a reference to the smallest subclause enclosing the relevant item;

- a solidus character, ‘/’;

- the reference number of the row in which the response appears;

- if, and only if, more than one response occurs in the row identified by the reference number, then each possible entry is implicitly labeled a, b, c, etc., from left to right, and this letter is appended to the sequence.

Completion of the PICS

The implementer shall complete all entries in the column marked ‘Support’. In certain clauses of the PICS proforma, further guidance for completion may be necessary. Such guidance shall supplement the guidance given in this clause and shall have a scope restricted to the clause in which it appears. In addition, other specifically identified information shall be provided by the implementer where requested. No changes shall be made to the proforma except the completion as required. Recognizing that the level of detail required may, in some instances, exceed the space available for responses, a number of responses specifically allow for the addition of appendices to the PICS.

REFERENCED BASE STANDARDS

Motion Imaginery and Applications (MIA, this document) is the only base standard referenced in the PRL. In the tables below, numbers in the Reference column refer to applicable subsections within this document.

GENERAL INFORMATION

IDENTIFICATION OF the PICS

| Date of statement (yyyy-mm-dd) |  |
| --- | --- |
| PICS version |  |
| System Conformance Statement cross-reference |  |
| Other information |  |

Identification of the system supplier / test laboratory client

| Organization name |  |
| --- | --- |
| Contact name |  |
| Address |  |
| Telephone |  |
| E-mail |  |
| Other information |  |

IDENTIFICATION OF the IMPLEMENTATION UNDER TEST

| Implementation name |  |
| --- | --- |
| Implementation version |  |
| Encoder name |  |
| Decoder name |  |
| Camera |  |
| Software viewer |  |
| Special configuration |  |
| Other information |  |

Equipment Configuration for Video format In details (encoder/Decoder)

| Source Device IP address |  |
| --- | --- |
| Source Device Netmask |  |
| Source Device Gateway |  |
| Destination IP Addresses |  |
| Network Protocol |  |
| Source /destination UDP ports |  |
| Bandwidth |  |

Global statement of conformance

| Are all mandatory features implemented? (Yes or No) |  |
| --- | --- |

NOTE	–	If a positive response is not given to this box, then the implementation does not conform to the standard.

SIGNAL INTERFACES

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | Non-Compressed Standard Definition Television Signals | 3.3.1 | O.1 |  |
| 2 | Non-Compressed High Definition Television Signals | 3.3.2 | O.1 |  |
| 3 | Compressed Digital Television Signals | 3.3.3 | O |  |

Supported video Resolutions

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | Personal Video Conferencing | 3.4.1.2 | O.2 |  |
| 2 | Medical Conferencing | 3.4.1.3 | O.2 |  |
| 3 | Situational Awareness | 3.4.1.4 | O.2 |  |
| 4 | Public Affairs | 3.4.1.5 | O.2 |  |
| 5 | High Resolution Digital Imaging | 3.4.1.6 | O.2 |  |

Interoperability

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | Acquisition and storage of video data | 3.7.1 | M |  |
| 2 | Real time distribution | 3.8.1 | C |  |
| 3 | Delayed distribution | 3.8.2 | O |  |
| 4 | End User Capabilities | 3.8.3 | M |  |

Compression

| MPEG-4 | High Definition 720p |  |  |  |
| --- | --- | --- | --- | --- |
| Item | Protocol Feature | Reference | Status | Support |
| 1 | Mpeg 2 /TS stream (7 TS packet /UDP Frame) | 3.6.1 | O.3 |  |
| 2 | Elementary Stream | 3.6.2 | O.3 |  |
| 3 | Codec Mpeg-4, part 10 | 3.4.4 | M |  |
| 4 | Color code 4:2:0 | 3.4.5 | O.2 |  |
| 5 | Video Format (720 p) | 3.4.1.2-3.4.1.5 | O.2 |  |
| 6 | HD H.264 High profile. Level 4.0 | 3.4.4.2 | O |  |
| 7 | GOP < 31 | 3.4.4.2 | O |  |
| 8 | Constant Bit Rate (CBR) | 3.4.4.2 | O |  |
| 9 | Embedded audio | 3.5.1 | O |  |
| JPEG2000 | High Definition 720p |  |  |  |
| Item | Protocol Feature | Reference | Status | Support |
| 1a | IP Datagram Encapsulation | 3.6.1.3 | M |  |
| 2b | Color Code 4:2:0 | 3.4.5 | O.2 |  |
| 3c | Video Format (720p) | 3.4.1.2-3.4.1.5 | O.2 |  |
| 4d | CBR | 3.4.4.2 | O |  |
| 5e | Embedded Audio | 3.5.1 | O |  |

Supported Operations

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | Personal Video Conferencing | 3.4.1.2 | O.1 |  |
| 2 | Medical Conferencing | 3.4.1.3 | O.1 |  |
| 3 | Situational Awareness | 3.4.1.4 | O.1 |  |
| 4 | Public Affairs | 3.4.1.5 | O.1 |  |
| 5 | High Resolution Digital Imaging | 3.4.1.6 | O.1 |  |

PRIVACY

General

| Item | Protocol Feature | Reference | Status | Support |
| --- | --- | --- | --- | --- |
| 1 | Data Privacy | B1.3 | M |  |
| 2 | Data Integrity | B1.4 | M |  |
| 3 | Authentication of communicating entities | B1.5 | M |  |
| 4 | Control of access of resources | B1.6 | M |  |

Encryption Procedures FOR PRIVATE VIDEO

Encryption procedures are applicable for private or medical video.  Encryption is typically peer-to-peer based on the application being used.  Tests are not required for PICS proforma.  Tests of individual application are to be performed prior to use in flight.

Security, SANA, and Patent Considerations

(Informative)

Security Considerations

Introduction

Aside from the generic security needs of computing systems, security concerns are applicable to motion imagery where there are specific requirements to ensure that transmitted imagery not be disclosed, altered, spoofed, nor redistributed without authorization.

Unmanned space systems that transmit imagery frequently need the capability to control access to the imagery, whether for proprietary reasons or for national security.  Manned space applications frequently have the additional requirements to provide private video teleconferencing capabilities for communications with families, physicians, ground operations personnel, and/or news media outlets.  Ground systems that receive and/or redistribute motion imagery have additional threats and countermeasures as well.

The focus of this a is on the specific protocols and methods recommended earlier in this document.  It may be necessary to implement security services at other layers within the protocol stack, to account for distributed processing and cross support, to account for different classes of data or end users, or to account for protection of data during unprotected portions of the complete end-to-end transmission (e.g., across ground networks).  The specification of security services at other layers is outside the scope of this document.

Security Concerns With Respect To The CCSDS Document

The most common method of applying security to digital video and audio streams is through the use of multimedia container formats. Containers provide a file-based mechanism for exchanging, processing, and storing interleaved fragments of video, audio, metadata, and/or other data such as subtitles and still images.  Most container files may be read or written by ordinary computer systems in the same manner as other files.

The ‘MP4’ standard, ISO/IEC 14496-14 (reference [D6]), is a multimedia container format standard specified as a part of MPEG-4.  The ‘Secure JPEG 2000’ standard, ISO/IEC 15444-8 (reference [D7]), is a multimedia container format standard specified as a part of JPEG 2000.

Data Privacy

The first major area of security concern is privacy, the requirement that the imagery not be disclosed to any other than the intended recipient(s).  Limited privacy can be achieved through the use of data scrambling, which weakly obfuscates the data stream using a reversible non-cryptographic mechanism, or through employment of protected data transport at lower layers and restricting distribution.

Better privacy can be achieved using cryptographic techniques, which may be applied to all or part of a container format.  Since any transcoding or decoding system must be able to read and pass metadata in order to process the stream,  imagery metadata must be visible at these points.  It is therefore highly desirable to have the capability to perform selective encryption of container file fields (e.g., imagery but not metadata, or imagery and imagery metadata but not cryptographic metadata).  ‘Secure JPEG 2000’ includes mechanisms for selective encryption of JPEG 2000 image content and metadata.  Various proprietary methods also exist for encrypting MP4 streams.

Data Integrity

The second major area of security concern is data integrity, the requirement that the imagery not be altered, whether to introduce false imagery or to interfere with decoding.  Integrity verification mechanisms can be used for data validation to prevent security problems due to non-compliant malignant data. Like privacy, data integrity is commonly provided at other layers of the protocol stack or through a container format.  ‘Secure JPEG 2000’ includes mechanisms for cryptographic verification of JPEG 2000-compliant data.

Authentication of Communicating Entities

Source authentication is the requirement that the imagery be attributable to a known origin.  Closely related to data integrity, it can also be used for data validation.  Source authentication, if provided, is commonly provided at other layers of the protocol stack or through a container format.  ‘Secure JPEG 2000’ includes digital signature mechanisms for authentication of JPEG 2000-compliant data.

Control of Access to Resources

The third major area of security concern is access control, the requirement that the imagery be restricted from unauthorized further use by the recipient(s).  Access control is commonly provided at other layers of the protocol stack.  Various methods also exist for attempting access control through the inclusion of proprietary metadata in a container format, although it should be noted that many similar techniques in the past have been defeated by determined attackers.  As discussed in B1.3 above, some protocols provide for selective encryption of imagery (e.g., high-resolution imagery encrypted while metadata or a low-resolution preview is unencrypted).  This method may be used to provide controlled access to imagery.

Auditing of Resource Usage

Auditing of imagery usage falls under the controversial category of so-called Digital Rights Management (DRM), i.e., ‘copy protection’.  As discussed with respect to access control in B1.6 above, copy protection is commonly an application of proprietary techniques to container formats.  A more robust mechanism is the use of digital watermarking to embed identifying data within imagery or metadata in order to provide legally actionable evidence of the data’s origin that is difficult to remove from second- or later-generation copies.  ‘Secure JPEG 2000’ includes digital watermarking mechanisms for JPEG 2000-compliant data.

Potential Threats and Attack Scenarios

It is possible to interfere with the decoder at the receiving end by injecting non-compliant data streams.  This attack can result in a denial of service (if the decoder crashes) or a system compromise (if the decoder is software-based).  Deliberate overflow of receiving buffers is a widespread attack method in ground-based computing systems.

With some digital imagery formats, it is possible to embed arbitrary data within the metadata sent as part of the overall imagery stream, and thereby use the ancillary data as a covert channel for transmitting other, unrelated information.  This technique is called Steganography.

Consequences of Not Applying Security to the Technology

If confidentiality is not implemented, imagery might be visible to unauthorized entities resulting in disclosure of sensitive or private information.

Without source authentication or integrity verification, valid imagery could be corrupted or invalid imagery substituted in its place.  Without access controls, authorized entities might be able to redistribute sensitive or proprietary information to unauthorized third parties.

SANA Considerations

The recommendations of this document do not require any action from SANA.

NOTE	–	The systems described in this document are either standalone or connect to existing communications facilities.  Those communication facilities, however, would require a SANA registry entry.  Motion Imagery is another service among many utilizing a given spacecraft’s communication system and therefore does not require an additional SANA entry.

Patent Considerations

[A statement regarding patent considerations will be included here.]

DTN Bundle Protocol for Video Transmission

(Informative)

Mode 1 Real Time Delivery, Best Effort

Mode 1 provides best-effort delivery of data and should be used for unicast or multicast data delivery when the data is to be utilized immediately upon arrival (perhaps for near–real-time decision making).  The data will be forwarded using the DTN Bundle Protocol without custody transfer and will be available to the receiving CODEC/application on a best-effort basis.  Therefore the data will be ‘played’ in the order it is received.  Missing, damaged, or out-of-order packets will be ignored with subsequent CODEC responses being typical.  Additional items such as excessive latency or jitter may be deleterious to the CODEC response.

Mode 2 DELAYED Delivery, WITH Packet RESTORATION

Mode 2 provides delivery of data with the prospect of no packets dropped and should be used for single or multi-transport of data when the data can be utilized after a sufficient latency to allow reassembly of the data.  The data will be available to a CODEC/application once the underlying protocol has sufficient time to reassemble the data stream.

Therefore the data will be ‘played’ in its entirety subject to data being wholly lost on a frame basis.  Missing and damaged bundles will be forwarded prior to reassembly with out-of-order bundles to be made available to the end CODEC/application.  Additional items such as excessive latency or jitter will not affect CODEC/application response.

Store and Forward Issues

The Delay Tolerant Networking Bundle Protocol (DTN-BP) enables store and forward operation when multiple hops or links are required to send data from source to receiver. There is an additional space link reliability protocol available known as Licklider Transmission Protocol (LTP), which will note loss of DTN bundles (which would contain 1-n video frames depending on system design) and request retransmission of missing bundles.

Use of the LTP reliability mechanism will result in delivery of out-of-order video frames to the application layer (because of the lag in retransmitting missing bundles). This may or may not be acceptable to the end-user application, and consideration of this out-of-order condition must be made.

In current lab experiments, it has been seen that an effective use of DTN to transmit video is to transmit bundles unreliably, accept the consequences of missing data for the real-time viewing of the video stream, and use another mechanism for recovery of missing data. This mechanism could be an application buffer to store retransmitted bundles separately for later reconstruction of the video stream in non–real time, or to record the video on board and later transmit as a video file for playback after the file is completely received without errors.  Further experimentation is required to provide definite parameters for the transmission of video using DTN.

Informative References

(Informative)

[D1]	Motion Imagery and Applications.  Report Concerning Space Data System Standards, CCSDS 706.1-G-1.  Green Book.  Issue 1.  Washington, D.C.: CCSDS, November 2010.

[D2]	J. Postel.  Internet Protocol.  STD 5.  Reston, Virginia: ISOC, September 1981.

[D3]	Hypertext Transfer Protocol -- HTTP/1.1.  RFC 2616.  Reston, Virginia: ISOC, June 1999.

[D4]	H. Schulzrinne, et al.  RTP: A Transport Protocol for Real-Time Applications.  STD 64.  Reston, Virginia: ISOC, July 2003.

[D5]	J. Postel.  Transmission Control Protocol.  STD 7.  Reston, Virginia: ISOC, September 1981.

[D6]	Information Technology—Coding of Audio-Visual Objects—Part 14: MP4 File Format.  International Standard, ISO/IEC 14496-14:2003.  Geneva:  ISO, 2003.

[D7]	Information Technology—JPEG 2000 Image Coding System: Secure JPEG 2000.  International Standard, ISO/IEC 15444-8:2007.  Geneva:  ISO, 2007.

Abbreviations

(Informative)

AAC	Advanced Audio Codec

BER	Bit Error Rate

CBR	Constant Bit Rate

CFDP	CCSDS File Delivery Protocol

DRM	Digital Rights Management

DTN	Delay Tolerant Networking

DTN-BP	Delay Tolerant Networking Bundle Protocol

DVB-ASI	Digital Video Broadcasting-Asynchronous Interface

EVA	Extra-Vehicular Activity

FPS	Frames Per Second

GOP	Group of Pictures

HD	High Definition

HDMI	High Definition Multimedia Interface

HD-SDI	High Definition-Serial Digital Interface

HTTP	Hypertext Transfer Protocol

IP	Internet Protocol

LTP	Licklider Transport Protocol

LVDS	Low Voltage Differential Signaling

PID	Packet Identification

RTP	Real Time Protocol

SD	Standard Definition

SDI	Serial Digital Interface

TS	Transport Stream

UDP	User Datagram Protocol

UT	Unitdata Transfer

# Footnotes

It is anticipated the Voice Working Group standard will address this issue with standard practices to be employed for audio/video synchronization.

As this is refined, it will be added to the MIA specifications.