## Slide 1
Generic Frame Procedure
Jon Hamkins
February 26, 2020
This research was carried out by the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration.
© 2020 California Institute of Technology. U.S. Government sponsorship acknowledged.

## Slide 2
Previous Discussion
May 7, 2019 meeting in Mountain View
  “Flexible Frame Interfaces for Optical Communications,” presented (available in CWE)
  Proposed use of Generic Frame Procedure (GFP, ITU T G.7041/Y.1303) to adapt higher layer frame formats to fixed rate octet transport service
  There was general agreement in the Optical Working Group that this was a good approach to support these desired features
October 21, 2019 meeting in Darmstadt
  “Pink Sheets for Generic Frame Procedure” and “Summary of CNES/JAXA/NASA/ NICT High Data Rate (1550 nm) Orange Book Updates” presented (available in CWE)
  Description of how GFP would interface to the existing optical standard
  Supplied and discussed proposed Pink Sheets to 142.0. Optical Working Group reached consensus.
  Work was identified in SLS plenary as requiring broader CCSDS discussion

## Slide 3
Outline
The CCSDS Optical Standards
Description of the Generic Frame Procedure (GFP)
Proposed use of GFP for Optical Standards

## Slide 4
Outline
The CCSDS Optical Standards
Description of the Generic Frame Procedure (GFP)
Proposed use of GFP for Optical Standards

## Slide 5
Status of CCSDS Optical Standards
High Photon Efficiency (HPE) – Blue Books (physical layer, coding & sync)
Optical On-Off Keying (O3K) – Pink sheets (physical layer). Channel coding is under study.
High Data Rate (HDR) – Orange Books for 1064 nm and 1550 nm (each includes both physical layer and coding & sync layer)
HPE, O3K
HDR
Free-Space Optical Channel
CCSDS Transfer Frames
(TM, AOS, USLP)

## Slide 6
Outline
The CCSDS Optical Standards
Description of the Generic Frame Procedure (GFP)
Proposed use of GFP for Optical Standards

## Slide 7
Overview of Generic Frame Procedure (GFP)
GFP is an ITU standard
ITU-T G.7041/Y.1303 (2016) Amd. 1 defines a Generic Frame Procedure to delineate octet-aligned, variable-length payloads from higher-level client signals for subsequent mapping into octet-synchronous path.
This ITU standard is available at:
https://www.itu.int/rec/dologin_pub.asp?lang=e&id=T-REC-G.7041-201908-I!Amd1!PDF-E&type=items

## Slide 8
GFP Relationship of Client Signals
to Transport Paths
client signals
GFP functions
Octet-synchronous path
Client signals (frames) may be:
  Variable length
  Variable rate / sporadic
  An arbitrary frame types
  Potentially multiplexed

## Slide 9
Two modes of GFP
Frame-mapped GFP (GFP-F)
  The GFP function has access to frames of the data link layer (Protocol Data Units (PDUs))
  PDUs are received and processed by the GFP function
  This is specified in ITU G.7041/Y.1303 (2016) Amd. 1 clause 7
  Possible to mulitiplex several streams
  This is the mode that is relevant to application of GFP to CCSDS
Transparent GFP (GFP-T)
  GFP operates on the coded character stream (physical channel) rather than on PDUs
  The channel clock is derived from the client clock
  This is specified in ITU G.7041/Y.1303 (2016) clause 8
  This mode is not relevant to application of GFP to CCSDS

## Slide 10
GFP Frame Structure

## Slide 11
The GFP Core Header (CH) is a 32 bit field.
It is composed of:
  A 16 bit Payload length indicator (PLI)
  A 16 bit CRC, the core header error control (cHEC)
  The CH is scrambled by XORing with B6AB31E0.
The Function of the CH is to provide:
  The length of the frame
  A sync marker for the frame (so start of a frame data block can be found)
  4 octet Fill Units for matching frame production to output data rate as necessary
  Note that the use of the cHEC is designed to guard against random bit errors (not a feature useful for a decoded bit stream)
Payload Length
Indicator (PLI)
16 bits
CRC
(cHEC)
16 bits
GFP Core Header (CH)
Entire CH is scrambled
GFP Core Header (CH) and its Role

## Slide 12
GFP Payload Area

## Slide 13
Type
  2 octets
  Indicates the content and format of the GFP payload information field
  Distinguishes GFP frame types between different services
Type header error control field (tHEC)
  2 octets
  CRC-16 that protects GFP Type field
Extension headers
  0 to 60 octets
  Supports technology-specific data link headers such as virtual link identifiers, source/destination address, port numbers, etc.
Extension header error check field
  2 octets
  CRC-16 that protects extension headers.
GFP Payload Header (PH)

## Slide 14
Payload type identifier (PTI)
  3-bit subfield
  Identifites type of GFP client frame
Payload frame check sequence indicator (PFI)
  1-bit subfield
  Indicates the presence or absence of the pFCS field
Extension header identifier (EXI)
  4-bit subfield
  Identifies the type of extension header GFP
User payload identifier (UPI)
  8-bit subfield
  Identifies the type of payload conveyed in the GFP payload information field.
GFP Payload Header (PH) Type Field

## Slide 15
GFP User Payload Identifier
* “The proprietary codes allow non-standard payload mappings to be supported. These proprietary codes are not subject to international standardization and can be used by any vendor and/or operator as needed. The selection of a code from any of the reserved proprietary codes is left for the user.” [ITU-T G.806, Annex A]
*

## Slide 16
Contains the framed PDU
It is a variable-length field, from 0 to 65 535 – X octets, where X is the size of the payload header.
Octet-aligned
May include an optional payload frame check sequence (pFCS) field
GFP Payload Information Field and Check Sum

## Slide 17
All octets of the payload area are scrambled with 1 + x^43 self-synchronous scrambler:
GFP Payload Area Scrambling

## Slide 18
CH
PH
Payload
CH
PH
Payload
CH
CH
CH
CH
CH
CH
CH
PH
Payload
CH
CH
PH
Payload
GFP Frame
Idle Frames
GFP Rate Matching
Client supplies frames (payload)
When frame is available, GFP prepends a Core Header and Payload Header to it
When no frame is available, GFP generates a Core Header for 0-length Payload. This is an idle frame, and enables an octet-synchronous service on the physical channel.

## Slide 19
GFP Multiplexing of Multiple
Client Sources and Idle Frames

## Slide 20
Outline
The CCSDS Optical Standards
Description of the Generic Frame Procedure (GFP)
Proposed use of GFP for Optical Standards

## Slide 21
Current Optical Standard Frame Interface
Current optical standard requires:
CCSDS transfer frames (TM, AOS, or USLP)
Fixed length transfer frames (variable length USLP not handled)
Fixed rate transfer frames (no rate matching in standard)

## Slide 22
The Proposed Use of Generic Frame Procedures
Normally, SMTFs are created by attaching sync markers to transfer frames.
New content
Normally, SMTFs are created by attaching sync markers to transfer frames
As an alternative option, instead we may generate SMTFs by using GFP.
GFP enables:
  Variable length frames
  Variable rate frames
  Arbitrary frame types (not just CCSDS)
There are two proposed GFP modes:
  Short GFP mode
  Full GFP mode
SMTF: sync-marked transfer frame.

## Slide 23
Proposed “Short GFP mode”
Replace the attached sync marker (ASM) with an alternate marker
The alternate marker is the GFP Core Header
GFP idle frames may be used
Incorporate no other features of GFP
Benefits:
  The overhead is the same as the ASM
  Variable length and rate frames can be handled
  Rate matching (between frame generation and channel transmission rates)
  CCSDS and non-CCSDS frame types can be handled
Payload Length
Indicator (PLI)
16 bits
CRC
(cHEC)
16 bits
GFP Core Header (CH)
Entire CH is scrambled

## Slide 24
Proposed “Full GFP mode”
Replace the attached sync marker (ASM) with the full GFP standard
  Core header
  Payload header
GFP idle frames may be used
Set payload type identifier (PTI) to 000, to indicate user data
Denote the CCSDS frame type using the user payload identifier (UPI) 1111 0000. CCSDS frame types may be distinguished using transfer frame fields.
Benefits:
  Enables multiplexing of different frame types, as might be needed for a trunk link application.
  Variable length and rate frames can be handled
  Rate matching (between frame generation and channel transmission rates)
  CCSDS and non-CCSDS frame types can be handled
Payload Length
Indicator (PLI)
16 bits
CRC
(cHEC)
16 bits
GFP Core Header (CH)
Entire CH is scrambled

## Slide 25
Proposed “Pink Sheets” for GFP
3.3.2.1 Short GFP mode
When the short GFP mode is used, SMTFs shall be formed by preceding each transfer frame with the core header as defined in section 6.1.1 of reference [9], where the term “payload area” in reference [9] is to be understood as referring to the transfer frame.
NOTE – The short GFP mode has the same overhead as the ASM approach in subsection 3.3.1.
3.3.2.2 Full GFP mode
When the full GFP mode is used, each STMF shall be the GFP client data frame that results from designating a transfer frame as the GFP payload information field and applying the frame-mapped GFP encapsulation methods defined in sections 6 and 7 of reference [9].
NOTES:
The full GFP mode may be useful for multiplexed trunk lines with fixed or variable length transfer frames, with the added overhead present in the payload headers.
Reference [9] describes two modes of GFP: frame-mapped (GFP-F) and transparent-mapped (GFP-T). This Recommended Standard utilizes only the GFP-F mode.
3.3.2.2.1 Payload frame check sequence (pFCS)
The payload frame check sequence (pFCS) field of GFP shall not be used.
3.3.2.2.2 User payload identifier
When CCSDS frames are used, the user payload identifier within the payload header shall be set to 1111 0000.
NOTE – as provided for by the GFP standard, this setting can be used to indicate data types not enumerated in the GFP standard, such as the CCSDS client data type.
3.3.2.3 GFP idle frame
In either the short or long GFP modes, when a transfer frame is not available an SMTF may be formed using a GFP idle frame, i.e., a core header only with no payload area, as defined in section 6.2.1 of reference [9].
NOTE – The use of GFP idle frames will cause there to be more than A SMTFs. For simplicity in the description below, the notation A is still used to refer to the number of SMTFs.

## Slide 27
Backup

## Slide 28
CCSDS Optical Recommended Standards
The first CCSDS Recommended Standards for optical communications have been published. One standard relates to the physical layer signaling characteristics, and the other to the coding and modulation.
  https://public.ccsds.org/Pubs/141x0b1.pdf
  https://public.ccsds.org/Pubs/142x0b1.pdf
This is the culmination of a multiyear effort.
The standard is designed for photon-starved free space optical communications, as may occur for missions to deep space, the Moon, and low-power Earth orbiting missions.

## Slide 29
Codeword(s)
Codeword
Sync Marker
(CSM)
Frame
Frame and
Codeword Aligned
(CCSDS 131.0)
ASM
Frame
codeword
ASM
Frame
codeword
ASM
Frame
codeword
Attached
Sync
Marker
(ASM)
Randomization
SMTF
Fixed Length Frame and
Codeword Unaligned
(CCSDS 131.2, 131.3,
and
Sec. 8 of 131.0)
CSM
codeword
CSM
codeword
CSM
codeword
SMTF A
SMTF B
SMTF C
CSM
Existing RF Frame and Codeword Relationships
Not supported by 131.x CCSDS standards:
Variable length frames
Fill/Idle

## Slide 30
Codeword(s)
Codeword
Sync Marker
(CSM)
Frame
Variable length Frame
and Codeword Unaligned
CSM
SMTF 1
codeword
CSM
codeword
CSM
codeword
GFP
Core
Header
(CH)
CSM
Fill/Idle
Randomization
SMTF
Fixed Length Frame and
Codeword Unaligned
CSM
codeword
CSM
codeword
CSM
codeword
SMTF A
SMTF B
CH
CH
SMTF 2
SMTF 3
SMTF 4
CH
CH
Fill/Idle
SMTF C
CSM
Proposed Optical Frame and Codeword Relationships

## Slide 31
Coding sublayer
  Codewords are synchronized using the CSM, and decoded as defined in the existing CCSDS standards.
  A serial output data stream is formed from the error free data codewords. This bitstream is error free but it can have gaps caused by those erred and discarded codewords.
  Frame delineation is performed following standard GFP methods, e.g.:
    A search is made for a core header. This is done by checking if a cHEC is a valid check on the preceding 16 bits.
    Once a match is found, the PLI is extracted.
    Additional validation against one or more subsequent CHs may be performed, if necessary, to achieve the desired false positive rate.
    If PLI=0, the fill unit will be discarded.
  Frames are extracted and provided, with validation, to the protocol sublayer
Implementation Aspects (Receive Side)