## Slide 1
SEA: Analysis of
Space Link Services
Inter Satellite Link (ISL) Proposal
Ignacio Aguilar (Area Chair)
Gilles Moury (Area Deputy Chair)
30 Aug 2022
This version adds new “CCSDS vs Commercial” deployment figures, pgs 28-32. These were modified during the special CESG “Luna ISL” session on 30 Aug.
This whole package starts with the SLS input to CESG Chair and then evaluates several options leveraging existing IOAG, SIS, and SCCS-ARD/ADD materials. SEA AD: Peter Shames
Notes: 1
1
1

## Slide 2: IOAG Lunar Comm Architecture WG Background
IOAG created a Lunar Comm Architecture Working Group (LCAWG)
They published their “The Future Lunar Communications Architecture” document, IOAG v 1.3, on 31 Jan 2022.
The following figures are from that document and provide a sort of DoDAF OV-1 overview and one of the prototypical end-to-end protocol stack diagrams
These diagrams are included for context

## Slide 3
DTN BP/LTP over AOS/USLP
over Trunk Link (X-band,
Ka-band-22/26 GHz, Optical)
Lander
Geophysical Network
Lander
Rover
Habitat
EVA
Comm
Station
Mobile
Habitat
Low orbit
Science Orbiter
Exploration Zone
Lunar Gateway
Earth Stations
Lunar Relay Network
DTN BP/LTP over AOS/USLP
over Proximity Link (S-band, Ka-22/26 GHz, or optical)
DTN BP/LTP over AOS/USLP over
Cross Link (Ka-band-22/26GHz,or Optical)
Lunar
Relay Orbiter
Lunar Surface Network
Wireless LAN
Earth Network
DTN nodes
DTN nodes
DTN nodes
DTN nodes
DTN nodes
DTN nodes
DTN BP/LTP over AOS/USLP over
Trunk Link (X-band, Ka-band-22/26 GHz, Optical)
DTN BP/LTP over AOS/USLP
over Proximity Link (S-band)
Science/Relay Orbiter
Artemis
orbiter
DTN BP/LTP over AOS/USLP over Proximity Link (S-band)
DTN BP/LTP over AOS/USLP over
Direct Earth Link (X-band, Ka-band 26 GHz)
To/from Earth Network
MOC
MOC
DTN nodes
Moon-to/from-Earth trunk link:
Between relay orbiter and Earth station
Moon-to/from-Earth link:
Between Lunar orbiter/landed vehicle and Earth station
Proximity link:
Between relay orbiter and landed vehicle/orbital vehicle
Cross link:
Between two relay orbiters
Lunar surface-to-surface link:
Wireless link between surface elements
Lunar Relay Network;
Lunar Surface Network;
Earth Network
NME

## Slide 4
Earth Station
Mission Operations Center
Lunar surface vehicle
Lunar Relay Orbiter
CCSDS File
Delivery
Protocol (CFDP)
Asynchronous
Messaging
Service (AMS)
User applications
CCSDS Space
Packet
Ethernet
CCSDS Bundle Protocol (BP)
Transmission Control Protocol (TCP)
Cat-5/Cat-6
Internet Protocol (IP)
User applications
CCSDS File
Delivery
Protocol (CFDP)
Asynchronous
Messaging
Service (AMS)
CCSDS Space
Packet
CCSDS Unified Space Link Protocol (USLP)
CCSDS Bundle Protocol (BP)
Licklider Transmission Protocol (LTP)
Radio Frequency Links – Near Earth Ka-, S-Bands;
Optical Link - CCSDS High Photon Efficiency (HPE)
CCSDS Encapsulation Packet (ENCAP)
CCSDS Bundle Protocol (BP)
Cat-5/Cat-6
TCP
Internet Protocol (IP)
RF - Near Earth Ka-, X-Bands
Optical - CCSDS HPE
Encapsulation Packet (ENCAP)
Licklider Transmission Protocol (LTP)
CCSDS Unified Space Link Protocol (USLP)
Ethernet
RF - Near Earth Ka-, S-, X-Bands
Optical - CCSDS HPE
Encapsulation Packet (ENCAP)
Licklider Transmission Protocol (LTP)
CCSDS Unified Space Link Protocol (USLP)
CCSDS Bundle Protocol (BP)
Lunar orbiter
Lunar Gateway
Lunar Proximity link
Terrestrial link
Earth-Moon link
Lunar Space Internet – End-to-End Protocols
Notes: 7/12: Again, I pasted in a fuzzy version of the Space User Node since it’s all I could get from one of the figures in the Word file; otherwise, there was just an empty placeholder for the graphic. //cys

## Slide 5: SEA: Comments on IOAG LCAWG Protocol Diagram
There is a large set of these protocols stack diagrams, all of which focus on the end-to-end concerns of DTN data flow from the User Applications in the MOC to the User Application in the Lunar Orbiter or Lunar Surface Vehicle, using the services of an Earth Station and one or more Lunar Relays.
Different configurations of node types and protocols are shown.
All contain the same, simplified but inaccurate diagram, including undocumented and non-standard protocol stacks, in the Earth Station (dashed lines on pg 4).
The issues:
  There are no CCSDS standards documents that describe this Earth Station configuration and the typical Earth Station service production does not support what is shown
  This configuration does not include the required SLE/CSTS service elements to support the “normal” TT&C services that all CCSDS Earth Stations include, as well as DTN
  Without these SLE/CSTS services there is no standard DTE/DFE link layer comms to/from the S/C
  There are two standardized CCSDS Earth Station configurations that be used: one that uses standard SLE F-CLTU & R-CF (SSI Stage 1, limited to TC) and one that uses FF-CSTS & R-CF (SSI Stage 2)
  Only the documented SSI Stage 2 configuration provides the kinds of services shown in these diagrams and provides support for forward USLP (or AOS) as well as normal TT&C, the Stage 1 F-CLTU does not
  The documented SSI Stage 1 configuration only supports forward TC (not USLP nor AOS), cannot support DTN deployment in the Earth Station, and requires the User MOC for the Relay Nodes to handle all DTN traffic flows and data stream merging
    Failure to include the required features and standards means that what is presented is an unsupported, and undocumented Earth Station configuration
  There is no MOC shown to operate the Lunar Relay Orbiter nor Lunar Gateway

## Slide 6
Activity for the implementation of a Open ISL standard
Prepared by Andrea Modenini, on behalf of SLS C&S, RFM, and SLP WGs
20/04/2022
ESA ESTEC

## Slide 7: SLS: Introduction
Today, there are no standards or recommended practices for inter satellites links (ISL)
  SEA: This is not quite accurate, since the latest C&S and link layer updates specifically include space to space links, and the SCCS-ARD/ADD already have relevant diagrams and text.
ESA had an activity from QinetiQ and Goonhilly Earth Station for the definition of a possible ISL standard (denoted as OpenISL) by using CCSDS standards
During CCSDS Spring 2022 meeting, ESA presented the main outcomes in SLS during the joint C&S, SLP, and RFM Working Groups (SLS-CS_22-07)
The WGs expressed interest in defining an ISL standard architecture, since it would support the definition of the future lunar architectures, especially those on-going in IOAG
However, it would be a CCSDS across area project, hence it requires coordination at CESG level
SEA: This extended version of the SLS ISL proposal provides SEA views across end-to-end (and local) interfaces

## Slide 8: SLS: Brief Summary of the ESA Study
Definition of Scenarios
  LEO: the Proba-3 mission adopted as reference
    Exchange of the formation flying status vector
    Autonomy demonstration
    Additional distance and collision avoidance mode, via ranging
  Mars Missions
    Taking into account NASA’s Human Exploration of Mars Design Reference Architecture 5.0
  Lunar Missions
    IOAG interested in inte-operability
    Meet SFCG and ITU constraints
    Need of Proximity (relay to vehicle) and cross links (between spacecrafts)

## Slide 9: SLS: Brief Summary of the ESA Study
Following a detailed analysis of CCSDS (and also non-CCSDS) standards, the ESA activity came out with the following proposal for an OpenISL:
  Bundle Protocol– CCSDS 734.2-B
    BP requires Convergence Layer Adapter (CLA) to connect BP and LTP
  LTP – CCSDS 734.1-B
  Encap – CCSDS 133.1-B-3, integrates LTP data frames into USLP data link
  USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
  Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
  Proximity 1 Physical Layer, CCSDS 221.4-B (*)
(*) with possible extension of blue books, in particular use of LDPC, and S-Band (with interest also in X- and K-Band). These possible changes will be discussed in SLS by means of a dedicated and separated project.

## Slide 10: SLS: Proposed way forward to CESG
Currently, SLS WGs (C&S, SLP, RFM) is already planning a Concept Paper for extending Proximiy-1 C&S and RFM layers for future Lunar applications (thus, a separated SLS project, not objective of this presentation)
For the OpenISL the SLS proposal to CESG is to have an across-area project for the definition of a Magenta Book, that defines the set of standards to be adopted
In fact, Magenta Books are a way to capture "best" or "state of the art" approaches for applying or using standards. They may include references to sets of standards selected to perform certain applications
  Depending on the level of directly implementable specificity this might best be characterized as a “Utilization Profile” style Blue Book.
In light of this, CESG is invited to provide its view and, in case of positive feedback, to agree with SLS the CCSDS Areas/WGs to be involved for such project

## Slide 11: SEA: SCCS-ARD Context for OpenISL
”OpenISL” appears to just focus on the Inter Satellite Link portion of an end-to-end flow (based on slide 8)
  This is only a small fraction of the total end-to-end path
  But parts of the proposed protocol stack, like DTN, only seem to make sense and provide real value in an end-to-end context
SCCS-ARD / ADD provides several views of cross support deployments relevant to this OpenISL discussion
  Services, Node types, protocol stacks, end-to-end protocols
  The following diagrams are just some of the possible end-to-end protocol views
These diagrams, derived from the SCCS-ARD / ADD, show the OpenISL concepts in the context of an end-to-end flow
  At least three different end-to-end architectures are explored for SSI Stage 1 & Stage 2 approaches

## Slide 12: SEA: Stated Assumptions
OpenISL states that it is focused on “Inter Satellite Links”, but it includes DTN and therefore looks like an “Inter Satellite Network” (ISN)
The ISL must accept data from somewhere else (ground, other space assets) and it must deliver data to a related set of assets in space
  There seems to be a strong desire to start “at the middle” and build outward
  The complexities of ground system integration cannot be “wished away”
The upper layers are DTN (including LTP and possibly BPSec), the bottom layers can be any of:
  USLP everywhere, including Prox-1 “tail circuit” signaling at UHF, or even S-Band, X-band, K/Ka-band (the latter are not yet standardized)
  Tail circuits could also be WiFi and 3GPP (standardized in SOIS docs)
  The ISL’s could be optical instead of RF (so could the long haul links from Earth)
  BUT – some down selected subset of standards appears to be desirable for any given deployment to minimize complexity and better support interoperability
At the DTN layer the assumption is that there is more than one terrestrial asset and more than one space asset that wish to interoperate
  There are two different types of terrestrial ground station and Relay MOC deployments documented now, SSI Stage 1 or SSI Stage 2, these will be distinguished to aid understanding
  We are leaving security, identity, and network management topics out of the discussion for now

## Slide 13: IOP/IOAG: Solar System Internet (SSI) Concepts
Support for DTN in the IOAG arose in the 2008 Interoperability Plenary (IOP-2) that published a report supporting:
  “The IOAG’s Space Internetworking Strategy Group (SISG) should formalize a draft Solar System Internetwork (SSI) Operations Concept and candidate architectural definition in time for IOAG-13 and should prepare a mature architectural proposal for review and endorsement at the third Inter-Operability Plenary meeting (IOP-3). “
This led to the IOAG Space Internetworking Strategy Group (SISG), developing an SSI architecture:
  “The IOAG resolves to form a Space Internetworking Strategy Group to reach international consensus on a recommended approach for transitioning the participating agencies towards a future “network centric” era of space mission operations. The group will focus on the extension of internetworked services across the Solar System, including multi-hop data transfer to and from remote space locations and local networked data interchange within and among the space end systems.”

## Slide 14: SISG Study Results => CCSDS Standards
The SISG study resulted in the Operations Concept for a Solar System Internetwork (SSI), IOAG.T.RC.001.V1, dated 15 Oct 2010, which defined:
  End-to-end architecture, SSI concepts and Principles
  Terminology such as provider & user nodes, ESLT/PSLT, relay spacecraft (including hybrid), and WANs (on Earth and off)
And this led directly to work in CCSDS (and the IETF) to define:
  SSI Architecture document, CCSDS 730.1-G-1
  BP document, CCSDS 734.2-B-1
  Other supporting documents like LTP, SBSP, SABR, …
  All of these are now in the process of being updated and extended
The typical CCSDS “one document, one protocol” approach required a “picture” of how all of these Blue colored puzzle pieces could fit together
  The CCSDS Architecture document, SCCS-ARD, CCSDS 901.1-M-1, provides that picture

## Slide 15: SSI Architecture Stages Quoted from CCSDS 730.1-G-1
The SSI architecture, therefore, encompasses three broad grades of functionality to support participating organizations in their transition through these stages toward full deployment of the SSI. The three stages of transition are:
  – Stage 1 (Mission Functionality)—introduction of the SSI protocols within MOCs and spacefaring vehicles to automate the mission data communications (command and telemetry) conducted within the simple mission communications model described in the first paragraphs of this section. The SSI architecture supports this stage by providing mission functionality (as described in section 3), which automates basic communication processes for individual space flight missions without requiring that Earth station service providers implement the SSI protocols.
  – Stage 2 (Internetwork Functionality)—introduction of the SSI protocols into Earth station service providers to enable Network-Layer cross support. The SSI architecture supports this stage by providing internetwork functionality (as described in section 4), which enables the SSI protocols to operate across multiple space flight missions, possibly managed by different national space agencies (interagency cross support). The coordination of mission data communications is still manual at this stage.
  – Stage 3 (Advanced Functionality)—automation of the coordination of mission data communications in the unified cross-support environment. The SSI architecture supports this stage by providing advanced functionality (as described in section 5), which provides automated support for the internetwork topologies, implementing a unified solar-system-wide communication network that can scale up to the complex space exploration programs of the future.
Organizations participating in the SSI may initially operate at any of the three stages, as long as they have implemented the functionality required in order to operate at all preceding stages: i.e., the stages are cumulative in functionality but need not be entered in sequence.

## Slide 16: Comments on Core “OpenISL” Sat to Sat relay
The following figures show the Core OpenISL in a vacuum, no sources of data, no sinks for data, no end-to-end guidance.
The only stated assumption is that data flowing in and out uses DTN at the network layer.
It only states how one relay satellite could talk to another and exchange link layer, network layer (DTN), and carry application data of various sorts.
There is no indication of whether the source(s) of data nor the destination(s), nor any given parts of the surrounding deployment uses consistent, or varying, protocols.
There is no guidance as to how to configure ground stations, mission systems, nor “user” systems in space to work with this “core”.
There are many open questions and options at the ISL data link layer (layer 2) and physical (layer 1).
  These could be the focus of a down selection process to provide guidance for interoperability.
OpenISL concept, as stated, is “simple”, but woefully incomplete and provides inadequate guidance to ground systems and space systems developers.

## Slide 17: Core “OpenISL” Sat to Sat relay – Forward (no security shown)
Inter Satellite
Link
Space Routing Node - B
SSI
Some Space-Ground
CCSDS Protocols
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
BP
Bundle Agent (Router/S&F)
X-Band
ENCAP
BP
C & S
USLP
LTP
LTP
BP
Some “tail circuit” protocol stack
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Prox-1 tail circuits not shown in this view
NOTE 2: AOS, or TC, could be substituted for USLP
NOTE 3: Optical physical and coding layers could replace these RF versions
End-to-end notes :
OpenISL does not live in a vacuum.
Ground Station services and protocols that get data to the OpenISL link are not shown.
The Bundle Protocol (BP) is the binding layer, the Space-Ground segment could even be bespoke / commercial protocols.
NOTE: DTN traffic from terrestrial sources (not shown) may flow directly to a Ground Station (SSI Stage 2) or through the terrestrial node that manages the Space Routing Node A (SRN-A).
Some Space-End Node
CCSDS Protocols
Some “deep space” protocol stack
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
17

## Slide 18: Core “OpenISL” Sat to Sat relay – Return (no security shown)
Inter Satellite
Link
Space Routing Node - B
SSI
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
BP
Bundle Agent (Router/S&F)
X-Band
ENCAP
BP
C & S
USLP
LTP
LTP
BP
Some Space-Ground
CCSDS Protocols
Some “tail circuit” protocol stack
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Prox-1 tail circuits not shown in this view.
NOTE 2: AOS, or TM, could be substituted for USLP
NOTE 3: Optical physical and coding layers could replace these RF versions
End-to-end notes:
OpenISL does not live in a vacuum.
Ground Station services and protocols that get data from the OpenISL link are not shown.
The Bundle Protocol (BP) is the binding layer, the Space-Ground segment could even be bespoke / commercial protocols.
NOTE: DTN traffic from terrestrial sources (not shown) may flow directly to a Ground Station (SSI Stage 2) or through the terrestrial node that manages the Space Routing Node A (SRN-A).
Some Space-End Node
CCSDS Protocols
Some “deep space” protocol stack
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
18

## Slide 19: Comments on SSI Stage 1 Deployment w/ Sat to Sat relay
The following figures show the OpenISL along with a Stage 1 ESLT configuration (and basic end-to-end guidance), but show no sources of data, nor sinks for data.
The stated assumptions are that data flowing in and out of the ESLT uses standard CCSDS data link and SLE services and that the ESLT offers no SSI services.
This documents how to use a set of existing CCSDS protocols to deploy a fully functioning SSI Stage 1 ESLT, which is essentially an unmodified ABA ESLT.
There is specific guidance in the SCCS-ARD as to how to configure ground stations, mission systems, and “user” systems in space to work with this “Stage 1 ESLT”.
A Stage 1 ESLT (as documented in the SCCS-ARD) offers two specific services:
  SLE F-CLTU, which only supports use of TC forward links from one source
  No multiplexing nor encoding of data frames, only encoded CLTUs are accepted from the source
There is the assumption that any other source(s) of BP data must direct traffic to the SRN-A MOC which hosts the Bundle Agent. The SRN-A must handle all BP processing, bundle fragments, encapsulation, TC frame creation, merging, and encoding.
There are no assumptions that the destination(s), nor any given parts of the surrounding deployment use consistent, or varying, link layer protocols.
As with the ”Core” there are many open questions and options at the ISL data link layer (layer 2) and physical (layer 1). This could be the focus of a down selection process to provide guidance for link layer interoperability.

## Slide 20: “OpenISL” Sat to Sat relay with SSI Stage 1 ESLT – Forward (no security shown)
Inter Satellite
Link
Terrestrial
WAN
Space Routing Node - B
SSI
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
ABA
RF & Mod
IP
TCP
SLE F-CLTU
SLE F-CLTU
Production
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
TC
Bundle Agent (Router/S&F)
X-Band
ENCAP
BP
C & S
USLP
RF & Mod
LTP
LTP
BP
End-to-end notes:
An SSI Stage 1 ESLT is an unmodified ABA ESLT that does not host a BP bundle agent nor other DTN services.
The ESLT offers all standard SLE/CSTS TT&C cross support services.
The SLE-F-CLTU service only allows TT&C using TC data link from one node, the SRN-A MOC (not shown).
All of the other Earth User Nodes must send their BP traffic to the SRN-A MOC, which must process BP, create and encapsulate bundle fragments for all DTN data, and then create, merge, and encode the TC frames for all data.
The ESLT to SRN-A link layer must be TC which is all that SLE F-CLTU supports. C&S and RF & Mod may be selected from all CCSDS supported options.
NOTE: All other user traffic using DTN/BP must be handled by the SRN-A MOC that controls the SRN-A.
Some “tail circuit” protocol stack
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Prox-1 tail circuits not shown in this view
NOTE 2: Only TC can be used on the ESLT to SRN-A link
NOTE 3: Optical physical and coding layers could replace these RF ISL versions
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
20

## Slide 21: “OpenISL” Sat to Sat relay with SSI Stage 1 ESLT – Return (no security shown)
Inter Satellite
Link
Terrestrial
WAN
Space Routing Node - B
SSI
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
ABA
RF & Mod
IP
TCP
C & S
R-CF
SLE R-CF
Production
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
Bundle Agent (Router/S&F)
X-Band
ENCAP
BP
C & S
USLP
RF & Mod
LTP
LTP
BP
Some “tail circuit” protocol stack
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Prox-1 tail circuits not shown in this view
NOTE 2: AOS, or TM, could be substituted for USLP
NOTE 3: Optical physical and coding layers could replace these ISL RF versions
End-to-end notes:
An SSI Stage 1 ESLT is an unmodified ABA ESLT that does not host a BP bundle agent nor other DTN services.
The ESLT offers all standard SLE/CSTS TT&C cross support services.
The SLE R-CF service allows multiple delivery paths of TT&C data to more than one node. This could be the SRN-A MOC (not shown) and a separate USLP/AOS/TM to BP node that could then serve other users.
All of the other Earth User Nodes must get their BP traffic from the SRN-A MOC (or other BP node) that extracts DTN data from the link layer frames.
The SRN-A to ESLT link layer may be any of USLP/AOS/TM. C&S and RF & Mod may be selected from all CCSDS supported options.
NOTE: All DTN/BP user traffic must be handled by the SRN-A MOC or another link layer to BP processing node.
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
21

## Slide 22: Comments on SSI Stage 2 Deployment w/ Sat to Sat relay
The following figures show the OpenISL along with a Stage 2 ESLT configuration (and basic end-to-end guidance), but show no sources of data, nor sinks for data.
The stated assumptions are that data flowing in and out uses DTN at the network layer and that the ESLT offers SSI Stage 2 services.
This documents how to use a set of existing CCSDS protocols to deploy a fully functioning SSI Stage 2 ESLT.
There is specific guidance in the SCCS-ARD as to how to configure [Future] ground stations, mission systems, and “user” systems in space to work with this “Stage 2 ESLT”.
A Stage 2 ESLT (as documented in the SCCS-ARD) offers four specific services:
  FF-CSTS, which supports use of either AOS or USLP forward links (SLE F-CLTU does not)
  Multiplexing and encoding data frames from more than one source (other BP compliant MOCs)
  Creating properly encapsulated and formed data link frames from Bundles
  Allowing the SRN-A MOC (not shown) to use all standard TT&C link layer & ranging features as well as BP
There is the assumption that other source(s) of BP data may direct traffic to the ESLT Bundle Agent. There are no assumptions that the destination(s), nor any given parts of the surrounding deployment use consistent, or varying, link layer protocols.
As with the ”Core” there are many open questions and options at the ISL data link layer (layer 2) and physical (layer 1). This could be the focus of a down selection process to provide guidance for link layer interoperability.

## Slide 23: “OpenISL” Sat to Sat relay with SSI Stage 2 ESLT – Forward (no security shown)
Inter Satellite
Link
Terrestrial
WAN
Space Routing Node - B
SSI
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
SSI
RF & Mod
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
Bundle Agent (Router/S&F)
X-Band
ENCAP
BP
C & S
USLP
RF & Mod
LTP
LTP
BP
End-to-end notes:
SSI Stage 2 ESLT hosts a BP bundle agent, and the ability to form bundle fragments into USLP data link frames
The ESLT also offers all standard SLE/CSTS TT&C cross support services.
CSTS-FF is the only CCSDS standard that supports USLP and AOS forward links, SLE F-CLTU is only for TC and single user.
SSI Stage 2 ESLT also hosts frame multiplexing that supports BP traffic from multiple terrestrial source and allows TT&C to SRN-A.
All of the Earth User Nodes may just send BP traffic to the ESLT.
The ESLT to SRN-A link layer (USLP in this view), C&S and RF & Mod may be selected from all CCSDS supported options
NOTE: CSTS FF supports other user traffic using DTN/BP and TT&C direct to the SRN-A from the MOC that controls it.
Some “tail circuit” protocol stack
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Prox-1 tail circuits not shown in this view
NOTE 2: AOS, or TC, could be substituted for USLP
NOTE 3: Optical physical and coding layers could replace these RF ISL versions
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
23

## Slide 24: “OpenISL” Sat to Sat relay with SSI Stage 2 ESLT – Return (no security shown)
Inter Satellite
Link
Terrestrial
WAN
Space Routing Node - B
SSI
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
SSI
RF & Mod
IP
TCP
C & S
R-CF
SLE R-CF
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
Bundle Agent (Router/S&F)
X-Band
ENCAP
BP
C & S
USLP
RF & Mod
LTP
LTP
BP
Some “tail circuit” protocol stack
End-to-end notes :
SSI Stage 2 ESLT hosts a BP bundle agent, and the ability to extract bundle fragments from USLP data link frames
The ESLT also offers all standard SLE/CSTS TT&C cross support services.
SSI Stage 2 ESLT also hosts frame de-multiplexing that supports BP traffic to multiple terrestrial sources and allows TT&C from SRN-A.
All of the Earth User Nodes may just receive BP traffic from the ESLT.
The ESLT from SRN-A link layer (USLP in this view), C&S and RF & Mod may be selected from all CCSDS supported options
NOTE: SLE-RCF Production demux supports other user traffic using DTN/BP and TT&C direct from the SRN-A to the MOC that controls it.
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Prox-1 tail circuits not shown in this view
NOTE 2: AOS, or TM, could be substituted for USLP
NOTE 3: Optical physical and coding layers could replace these ISL RF versions
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
24

## Slide 25: Comments on Bespoke ESLT Deployment w/ Sat to Sat relay
The following figures show the OpenISL along with a Bespoke ESLT and SRN-A configuration (and basic end-to-end guidance), but show no sources of data, nor sinks for data.
The stated assumptions are that data flowing in and out of the commercially (or other) provided bespoke service uses DTN at the network layer and that the ESLT offers DTN store and forward services at the interfaces that are the equivalent of SSI Stage 2.
Note that the Bespoke ESLT may not provide any standard SLE/CSTS TT&C cross support services, or it may only provide its own, bespoke, TT&C link layer service interfaces.
This documents, at a normative level, how to integrate a non-compliant set of bespoke link layer protocols to deploy a SSI Stage 2 ESLT and SRN-A that support DTN (but not standard CCSDS TT&C services).
There is no specific guidance in the SCCS-ARD as to how to configure Bespoke ground stations, mission systems, and “user” systems in space to work with this “Bespoke Stage 2 ESLT”.
This Bespoke SSI Stage 2 ESLT and SRN-A should offer three specific services:
  Multiplexing and encoding data frames from more than one source (the BP compliant MOCs)
  Creating properly encapsulated and formed Bespoke data link frames from Bundles
  Delivering Bundles via the SRN-A and returning them from the SRN-A, using private / bespoke means at the link layer
As with the ”Core” there are many open questions and options at the ISL data link layer (layer 2), tail ciruits from SRN to and physical (layer 1). This could be the focus of a down selection process to provide guidance for link layer interoperability.

## Slide 26: “OpenISL” Sat to Sat relay with Bespoke ESLT & SRN-A – Forward (no security shown)
Inter Satellite
Link
Terrestrial
WAN
Space Routing Node - B
SSI
Earth-Space
Link Terminal
Space-Ground
Bespoke Protocols
Bespoke
RF & Mod
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
Bundle Agent (Router/S&F)
X-Band
ENCAP
BP
C & S
USLP
RF & Mod
LTP
LTP
BP
Some “tail circuit” protocol stack
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Prox-1 tail circuits not shown in this view
NOTE 2: AOS, or TC, could be substituted for USLP
NOTE 3: Optical physical and coding layers could replace these RF ISL versions
Bespoke ESLT to SRN-A
protocol stack
End-to-end notes:
This diagram shows a possible “Commercially provided” ESLT and SRN-A that meets the “Core ISL” spec and also offers BP services.
The Bespoke ESLT offers a BP compliant routing & forwarding service interface to any user MOC.
The Bespoke ESLT may not provide any standard SLE/CSTS TT&C cross support services.
The SRN-A MOC (not shown) uses its own bespoke services to do TT&C to the SRN-A routing node.
All of the other Earth User Nodes must send their BP traffic to the ESLT, which must process BP, create and encapsulate bundle fragments for all DTN data, and then create, merge, and encode the data using its own bespoke reliability and link protocols.
The ESLT to SRN-A link layer uses bespoke protocols that carry what is otherwise normal BP traffic, possibly using LTP (or other) reliability protocols.
NOTE: All user traffic using DTN/BP must be handled by the ESLT BP interface.
Bespoke ESLT
protocol stack
& processing
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
26

## Slide 27: “OpenISL” Sat to Sat relay with Bespoke ESLT & SRN-A – Return (no security shown)
Inter Satellite
Link
Terrestrial
WAN
Space Routing Node - B
SSI
Earth-Space
Link Terminal
RF & Mod
IP
TCP
C & S
R-CF
SLE R-CF
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
Bundle Agent (Router/S&F)
X-Band
ENCAP
BP
C & S
USLP
RF & Mod
LTP
LTP
BP
Some “tail circuit” protocol stack
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Prox-1 tail circuits not shown in this view
NOTE 2: AOS, or TM, could be substituted for USLP
NOTE 3: Optical physical and coding layers could replace these ISL RF versions
Space-Ground
Bespoke Protocols
Bespoke
Bespoke SRN-A to
ESLT protocol stack
End-to-end notes:
This diagram shows a possible “Commercially provided” ESLT and SRN-A that meets the “Core ISL” spec and also offers BP services.
The Bespoke SRN-A and ESLT offers a BP and “ISL” compliant return service interface to any user space asset.
The Bespoke ESLT may not provide any standard SLE/CSTS TT&C cross support services.
The SRN-A provides ISL compliant services to other S/C and uses its own bespoke services to return data to the Bespoke ESLT.
All of the other Earth User Nodes must get their BP traffic from the ESLT, which must process the bespoke link data and create and forward all DTN data.
The SRN-A to ESLT link layer uses bespoke protocols that carry what is otherwise normal BP traffic, possibly using LTP (or other) reliability protocols.
NOTE: All user DTN/BP traffic from ESLT to User MOCs (not shown) must be handled by the ESLT BP interface.
Bespoke ESLT
protocol stack
& processing
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
27

## Slide 28: Comments on End-to-End ESLT Deployment Figures
The following figures show the OpenISL in the context of a complete, standards-based, ESLT and End-to-End configuration, including all sources and sinks of data.
The stated assumptions are that all data shown flowing in and out of the service elements and users adopt DTN at the network layer, and that the ESLT offers DTN compliant store and forward services that meet SSI Stage 2 functionality.
Note that the compliant Stage 2 ESLT continues to provide a full suite of standard SLE/CSTS TT&C cross support services which may be used by the relay or user spacecraft.
This documents, at a normative level, how to integrate a fully standards-compliant set of network and link layer protocols to deploy a SSI Stage 2 ESLT and SRN-A that support DTN and standard CCSDS TT&C services.
There is concrete guidance in the SCCS-ARD as to how to configure such ground stations, SRN, BP compliant mission systems, and “user” systems in space will work with this “Stage 2 ESLT” and the SRN-A.
A Stage 2 ESLT (as documented in the SCCS-ARD) offers four specific services:
  FF-CSTS, which supports use of either AOS or USLP forward links (SLE F-CLTU does not)
  Multiplexing and encoding data frames from more than one source (other BP compliant MOCs)
  Creating properly encapsulated and formed data link frames from Bundles
  Allowing the SRN-A MOC (not shown) to use all standard TT&C link layer & ranging features as well as BP
There is the assumption that other source(s) of BP data may direct traffic to the ESLT Bundle Agent. There are no assumptions that the destination(s), nor any given parts of the surrounding deployment use consistent, or varying, link layer protocols.
As with the ”Core” there are many open questions and options at the ISL data link layer (layer 2), at the “tail circuits” from SRN to SRUN, and physical (layer 1). This could be the focus of a down selection process to provide guidance for link layer interoperability.

## Slide 29: Bespoke Forward, SSI Stage 2 ESLT (no security shown)
Inter Satellite Link
Cross Support Interface
Terrestrial
WAN
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
SSI
RF & Mod
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
SSI
Prox Phy
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
Prox Link
ENCAP
BP
LTP
C & S
USLP
RF & Mod
To
VC X&Z
LTP
Space User Node
SSI
From
VC Z
Prox Link
Prox Phy
C & S
Space Msg Application
BP
AMS
IP-based Network
Terrestrial
WAN
Space to Planet
Relay Link
SSI
To
VC X
User File Application
File
IP
BP
CFDP
TCP
Earth User Node
SSI
To
VC Z
User Msg Application
IP
TCP
BP
AMS
Space Routing Node MOC
From
VC X
File
Space File Application
CFDP
Msg
Space to Planet Link:
Could use USLP with Prox-1 controls from SRN-A to Node on Planet Surface
Could use Prox-1 from SRN-A to surface
SRN-A could be on Planet surface (treated like PSLT)
PSLT to Space Relay User Node could use WiFi or 3GPP for Space to Planet Relay Link instead of Prox
Terrestrial User Node:
Space Routing Node MOC (controlling one or more ISL Nodes) can use DTN / BP to do monitor & control of traffic flow, or it may use link layer TT&C via CSTS-FF direct to the Relay S/C, SRN-A (or B, not shown explicitly)
Earth User Node shown using AMS and BP via ESLT that offers DTN services.
EUN MOC just uses BP end to end unless “Last Hop” emergency mode is required.
Bespoke EUN to ESLT
protocol stack
Bespoke ESLT
protocol stack
& processing
Bespoke ESLT
protocol stack
& processing
ENCAP
LTP
ESLT / MOC
Cross Support Interface (including Svc Mgmt)
Msg
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
29

## Slide 30: CCSDS Forward, SSI Stage 2 ESLT (no security shown)
Terrestrial
WAN
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
SSI
RF & Mod
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
SSI
Prox Phy
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
Prox Link
ENCAP
BP
LTP
C & S
USLP
RF & Mod
To
VC X&Z
LTP
Space User Node
SSI
From
VC Z
Prox Link
Prox Phy
C & S
Space Msg Application
BP
AMS
IP-based Network
Terrestrial
WAN
Space to Planet
Relay Link
SSI
To
VC X
User File Application
IP
BP
CFDP
TCP
Earth User Node
SSI
To
VC Z
User Msg Application
IP
TCP
BP
AMS
Space Routing Node MOC
From
VC X
Space File Application
CFDP
ENCAP
LTP
ESLT / MOC
Cross Support Interface (including Svc Mgmt)
Space to Planet Link:
Could use USLP with Prox-1 controls from SRN-A to Node on Planet Surface
Could use Prox-1 from SRN-A to surface
SRN-A could be on Planet surface (treated like PSLT)
PSLT to Space Relay User Node could use WiFi or 3GPP for Space to Planet Relay Link instead of Prox
Terrestrial User Node:
Space Routing Node MOC (controlling one or more ISL Nodes) can use DTN / BP to do monitor & control of traffic flow, or it may use link layer TT&C via CSTS-FF direct to the Relay S/C, SRN-A (or B, not shown explicitly)
Earth User Node shown using AMS and BP via ESLT that offers DTN services.
EUN MOC just uses BP end to end unless “Last Hop” emergency mode is required.
File
File
Msg
Msg
Inter Satellite Link
Cross Support Interface
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
30

## Slide 31: Bespoke – Return, SSI Stage 2 ESLT (no security shown)
Terrestrial
WAN
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
SSI
RF & Mod
IP
TCP
C & S
SLE - RCF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
RF & Mod
From
VC X&Z
LTP
Space User Node
SSI
To
VC Z
C & S
BP
IP-based Network
Terrestrial
WAN
Space to Planet
Relay Link
SSI
From
VC X
User File Application
IP
BP
CFDP
TCP
Earth User Node
SSI
From
VC Z
User Video Application
IP
TCP
BP
Space Routing Node MOC
To
VC X
Space File Application
CFDP
Planet to Space Link:
Could use USLP with Prox-1 controls from User Node on Planet Surface to SRN
Could use Prox-1 from surface to SRN
Space Routing Node could be on Planet surface (treat link PSLT)
Space User Node to PSLT could use WiFi or 3GPP for Space to Planet Relay Link
Space User Node could send messages via AMS (shown) or Files using CFDP
Terrestrial User Nodes:
Space Routing Node MOC (controlling one or more ISL Nodes) can use DTN / BP to receive monitor & data traffic, or it may do DFE/DTE and link layer via Bespoke Protocols direct from Relay S/C (not shown explicitly)
Earth User Node shown receiving messages (AMS) and BP via ESLT that offers Bespoke services.
EUN MOC just uses BP end to end unless “First Hop” mode is required.
Prox Phy
Prox Link
Prox Link
Prox Phy
C & S
AMS
AMS
ENCAP
LTP
Bespoke EUN to ESLT
protocol stack
Bespoke ESLT
protocol stack
& processing
Bespoke ESLT
protocol stack
& processing
Space Msg Application
User File Application
User Msg Application
File
File
Msg
Msg
ESLT / MOC
Cross Support Interface (including Svc Mgmt)
Inter Satellite Link
Cross Support Interface
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
31

## Slide 32: CCSDS – Return, SSI Stage 2 ESLT (no security shown)
Terrestrial
WAN
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
SSI
RF & Mod
IP
TCP
C & S
SLE - RCF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
Space Routing Node - A
SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
RF & Mod
From
VC X&Z
LTP
Space Relay User Node
SSI
To
VC Z
C & S
BP
IP-based Network
Terrestrial
WAN
Space to Planet
Relay Link
SSI
From
VC X
User File Application
IP
BP
CFDP
TCP
Earth Relay User Node
SSI
From
VC Z
User Video Application
IP
TCP
BP
Space Routing Node MOC
To
VC X
Space File Application
CFDP
Planet to Space Link:
Could use USLP with Prox-1 controls from User Node on Planet Surface to SRN
Could use Prox-1 from surface to SRN
Space Routing Node could be on Planet surface (treat link PSLT)
Space User Node to PSLT could use WiFi or 3GPP for Space to Planet Relay Link
Space User Node could send messages using AMS (shown) or Files using CFDP
Terrestrial User Nodes:
Space Routing Node MOC (controlling one or more ISL Nodes) can use DTN / BP to receive monitor & data traffic, or it may do DFE/DTE and link layer via SLE R-CF direct from Relay S/C (not shown explicitly)
Earth User Node shown receiving messages (AMS) and BP via ESLT that offers DTN services.
EUN MOC just uses BP end to end unless “First Hop” mode is required.
Prox Phy
Prox Link
Prox Link
Prox Phy
C & S
AMS
AMS
ENCAP
LTP
Space Msg Application
User File Application
File
User Msg Application
Msg
Msg
ESLT / MOC
Cross Support Interface (including Svc Mgmt)
Inter Satellite Link
Cross Support Interface
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
32

## Slide 33: Bundle Protocol Security Considerations
BPv7 and BPSec do have some "security hooks" built it.
  Nodes have IDs, and BPSec uses keys, and provides the ability to use them to do encryption and authentication.
  The new draft network management standards have the same sorts of features as well.
But the existing SANA Node ID registry just says "This agency has this range of numbers to do with what they want."
  There is no formal relationship between a Node ID and a specific S/C or ground station or user MOC.
  Therefore, without a solid definition of node identity, anyone can say "I'm node 3.".
So the "hooks are in”, but what is hanging on them right now is a bunch of local (or implementation specific) assigned and managed data elements.
  These IDs and keys may be in project specific tables, or in some implementation specific tables using, in some cases, locally defined means / protocols to exchange and manage them.
There are not yet standards for network-wide security, routing, updates, identities, authentication / access control nor management from the PoV of multi-mission, multi-agency, interoperability.
We can start to define a set of "cottage industry" guidelines that can be used in any specific coordinated set of deployments, but we need more...
  Work must be done to provide guidance as to approaches to use at different stages of deployment …
  From "mission private", to "cottage industry", to "fully interoperable".

## Slide 34: “OpenISL” Sat to Sat relay with SSI Stage 1 ESLT – Forward With “private”, mission specific, security & management
CP
Inter Satellite
Link
Terrestrial
WAN
Earth-Space
Link Terminal
Space-Ground
CCSDS Protocols
ABA
RF & Mod
IP
TCP
SLE F-CLTU
SLE F-CLTU
Production
Space Routing Node - A
ABA/SSI
UHF-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP/BPSec
Prox-1
ENCAP
BP/BPSec
LTP
C & S
TC
RF & Mod
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Prox-1 tail circuits shown in this view
NOTE 2: Only TC can be used on the ESLT to SRN-A link (F-CLTU limitation)
NOTE 3: Optical physical and coding layers could replace the RF ISL versions
ABA/SSI
To
VC X
SRN Cmnd Application
CMD
IP
TCP
Earth Relay User Node
SSI
To
VC Z
User File Application
IP
TCP
BP/BPSec
CFDP
Space Relay User Node
SSI
From
VC Z
C & S
Space File Application
BP/BPSec
CFDP
UHF-Band
ENCAP
Prox-1
Space Routing Node MOC
ENCAP
BP/BPSec
LTP
C & S
TC
SLE F-CLTU
From
VC X
CMD
SRN Cmnd
Proc
From
VC Z
From
VC X & Z
End-to-end notes:
An SSI Stage 1 ESLT is an unmodified ABA ESLT that does not host a BP bundle agent nor other DTN services.
The SRN-A MOC uses standard TT&C and also handles all DTN traffic.
The SRN-A MOC must create some local, private, mechanisms for managing routing, assigning identities, and handling keys, for itself and the ERUN/SRUN.
Private protocols (implementation specific) are used to manage routing (may use SABR), nodes, and keys.
Assume that every BP / BPSec entity shown is a Bundle Agent as well
May use E2E file encryption at App layer
Need: Agreed Contact Plan (CP) definition, some approach for shared keys, agreed identity mechanism
Pvt Routing - A
Pvt Keystore - A
Pvt Routing - A
Pvt Keystore- A
Private Protocols
(May be BP or other, or out of band key dist)
From
VC Z
Pvt Routing - B
Pvt Keystore - B
Pvt Routing - B
Pvt Keystore - B
SABR
Link Schedule (SSF)
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
34

## Slide 35: Notes: SSI Stage 1 ESLT With “private”, mission specific, security & management
Frequencies are assigned by SFCG, link layer SCIDs by the CCSDS SANA, BP Node numbers are defined by each Agency within their assigned range.
The ESLT offers no DTN services nor support. The SRN MOC must provide all terrestrial DTN services.
There must be some agreed method and format to send Contact Plan (CP) info from SRN MOC to ERUN MOC.
Routing calculations and routing updates for both SRN and ERUN Earth & Space nodes are a private matter, may use SABR.
The end user nodes must agree on private means to manage their own identities.
Identities may be self-assigned or assigned using some agreed, potentially local, mechanism / authority. This may involve certificates, or not.
Both SRN and ERUN may (separately) use BPSec to secure data transfers.
Either may also use application layer data encryption / authentication.
There may not be any shared keys, and both the SRN and the ERUN may create their own keys and manage them using their own, private, in band, out of band, or pre-emplaced means.
SRN MOC could use SDLS link layer security too, with its own private keys (not shown).

## Slide 36: “OpenISL” Sat to Sat relay with SSI Stage 2 ESLT – Forward With “private”, deployment specific, security & management
Inter Satellite
Link
Terrestrial
WAN
Space-Ground
CCSDS Protocols
Space Routing Node - A
ABA/SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
RF & Mod
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Updated USLP / Prox-1 tail circuits shown in this view
NOTE 2: AOS, or TC, could be substituted for USLP fwd link
NOTE 3: Optical physical and coding layers could replace these RF ISL versions
ABA/SSI
To
VC X
SRN Cmnd Application
CMD
IP
TCP
Earth Relay User Node
SSI
To
VC Z
User File Application
IP
TCP
BP
CFDP
Space Relay User Node
SSI
From
VC Z
C & S
Space File Application
BP
CFDP
X-Band
ENCAP
USLP
Space Routing Node MOC
ENCAP
BP
LTP
USLP
CSTS-FF
From
VC X
CMD
SRN Cmnd
Proc
From
VC Z
End-to-end notes:
SSI Stage 2 ESLT hosts a BP bundle agent, and the ability to form bundle fragments into USLP data link frames and merge with other CSTS-FF traffic
The ESLT also offers all standard SLE/CSTS TT&C cross support services.
The SRN-A MOC must create some local, private, mechanisms for managing routing, assigning identities, and handling keys, for itself and the ERUN/SRUN.
Private protocols (implementation specific) are used to manage routing (may use SABR), nodes, and keys.
Assume that every BP / BPSec entity shown is a Bundle Agent as well
May use E2E file encryption at App layer
Need: Agreed Contact Plan (CP) definition, some approach for shared keys, agreed identity mechanism
Earth-Space
Link Terminal
SSI
RF & Mod
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
From
VC X
From
VC Z
LTP
LTP
Pvt Routing - E
Pvt Keystore - E
Pvt Routing - A
Pvt Keystore - A
Pvt Routing - A
Pvt Keystore- A
Private Protocols
(May be BP or other, or out of band key dist)
Pvt Routing - B
Pvt Keystore - B
Pvt Routing - B
Pvt Keystore - B
CP
SABR
Link Schedule (SSF)
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
36

## Slide 37: Notes: SSI Stage 2 ESLT With “private”, deployment specific, security & management
Frequencies are assigned by SFCG, link layer SCIDs by the CCSDS SANA, BP Node numbers are defined by each Agency within their assigned range.
The ESLT offers full DTN services and support. May coordinate Contact Plan for all supported users. Stage 2 coordination is done by whatever ad hoc means are agreed among participants.
There must be some agreed method and format to send Contact Plan (CP) info from ESLT and SRN MOC to ERUN MOC.
Routing calculations and routing updates for ESLT, SRN and ERUN Earth & Space nodes are a private matter, may use SABR.
The ESLT and end user nodes must agree on private means to manage their own identities.
Identities may be self-assigned or assigned using some agreed, potentially local, certificate mechanism / authority. The ESLT might offer such services.
Common implementations may be adopted across a deployment, with common, implementation specific, protocols. Absent this, interoperability may be a challenge.
ESLT, SRN, and ERUN may (separately) use BPSec to secure data transfers.
Either SRN or ERUN may also use application layer data encryption / authentication.
There may not be any shared keys, and both the SRN and the ERUN may create their own keys and manage them using their own, private, in band, out of band, or pre-emplaced means.
SRN MOC could use SDLS link layer security too, with its own private keys. ESLT could also support SDLS, using shared keys. (Not shown)

## Slide 38: “OpenISL” Sat to Sat relay with SSI Stage 3 ESLT – Forward With Standard security & management
Inter Satellite
Link
Terrestrial
WAN
Space-Ground
CCSDS Protocols
Space Routing Node
ABA/SSI
X-Band
C & S
Bundle Agent (Router/S&F)
ENCAP
BP
USLP
ENCAP
BP
LTP
C & S
USLP
RF & Mod
OpenISL:
Bundle Protocol– CCSDS 734.2-B
Bundle CLA left out …
LTP – CCSDS 734.1-B
Encap has been added
USLP – CCSDS 732.1-B, as allowed by Proximity-1 data link CCSDS 211.0-B)
Proximity-1 Coding and Synch layer, CCSDS 221.3-B (*)
Proximity 1 Physical Layer, CCSDS 221.4-B (*)
NOTE 1: Updated USLP / Prox-1 tail circuits shown in this view
NOTE 2: AOS, or TC, could be substituted for USLP fwd link
NOTE 3: Optical physical and coding layers could replace these RF ISL versions
ABA/SSI
To
VC X
SRN Cmnd Application
CMD
IP
TCP
Earth Relay User Node
SSI
To
VC Z
User File Application
IP
TCP
BP
CFDP
Space Relay User Node
SSI
From
VC Z
C & S
Space File Application
BP
CFDP
X-Band
ENCAP
USLP
Space Routing Node MOC
ENCAP
BP
LTP
USLP
CSTS-FF
From
VC X
CMD
SRN Cmnd
Proc
From
VC Z
End-to-end notes:
SSI Stage 3 ESLT hosts a BP bundle agent, and the ability to form bundle fragments into USLP data link frames and merge with other CSTS-FF traffic
The ESLT also offers all standard SLE/CSTS TT&C cross support services.
The interoperable agencies must use some agreed, standard, mechanisms for managing routing, assigning identities, and handling keys, for all member of the Enterprise.
Standard protocols are used to manage nodes, routing, and keys.
SANA w/ IGCA may be used to manage S/C ID, Identities, keys
ESLT or SRN MOC may manage / coordinate routing or a separate org may handle that task
Earth-Space
Link Terminal
SSI
RF & Mod
IP
TCP
C & S
CSTS-FF
CSTS F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
USLP
BP
From
VC X
Standard Rtng, Key, Mgmt Protocols
From
VC Z
LTP
LTP
Std Identites & Keystore
Std Routing - E
Std Keystore - E
Std Routing
Std Keystore
Std Routing
Std Keystore
Std Routing
Std Keystore
Std Routing
Std Keystore
CP
SABR
Link Schedule (SSF)
Rtng Agent
IGCA Agent
Notes: 12/12/12: Figure title here is from document; in original PPT file, the title is “ABCBPA PSLT Return -
SSI Agency supported by SSI Agency”
38

## Slide 39: Notes: SSI Stage 2 ESLT With Standard security & management
Frequencies are assigned by SFCG, link layer SCIDs by the CCSDS SANA, BP Node numbers are defined by each Agency within their assigned range and registered in a “DTN DNS”.
The ESLT offers full DTN services and support. Contact Plans for all supported users are generated by some central entity (ESLT shown in that role here). Stage 3 coordination is done by formal peering and cross support agreements among participants.
There is a standard protocol and format to send Contact Plan (CP) info and routing updates from ESLT and SRN MOC to ERUN MOC.
Routing calculations and routing updates for ESLT, SRN and ERUN Earth & Space nodes are standardized and use SABR.
The ESLT and end user nodes all use an agreed formal method to manage their identities and certificates, shown here as the IGCA. A standard protocol is used to keep distributed caches, for local performance, up to date.
All DTN nodes that provide services are registered in the SANA Service Site and Aperture registry. These, and all other DTN nodes, are registered as user nodes in the equivalent of a DTN DNS registry.
Common implementations may be adopted across a deployment, but all support the standard protocols.
ESLT, SRN, and ERUN use BPSec to secure data transfers, with public and/or private certificates as desired.
Standard, secure, network management protocols are used to do routing updates, network management, monitoring, and reporting. One (or more) nodes are assigned responsibility for the global enterprise.
Application data may be secured using public (or private) keys. SRN MOC could use SDLS link layer security too, with its own private keys. ESLT could also support SDLS, using shared keys.

## Slide 40: Final Thoughts about “Open-ISL”
OpenISL concept is good as far as it goes, but it is missing the end-to-end context that justifies some of the features.
Configurations for cross supported satellite links would benefit from being documented, but ideally this would be in an end-to-end context where full value of DTN would be realized.
Configurations for the ESLT’s must be accurately described since the two defined for Stage 1 and Stage 2 differ significantly in functionality and the burden placed on the relay MOC.
  Stage 1, “mission functionality” can be deployed now using ABA ESLTs, but this only supports TC forward links, places a burden on the Earth Relay Node, and does not align with the IOAG defined Earth Station functionality.
  Stage 2, “internetwork functionality”, and AOS or ULSP forward links, cannot be deployed until we have ESLTs that implement full FF-CSTS services, DTN bundle agents, and frame creation, encoding, and merging.
  This is an essential set of features that are required to achieve the IOAG vision, and cannot be overlooked since it has not yet been deployed in current ESLTs.
Deployment of USLP in all the situations where it can be applied is excellent, but some (orbiting or landed) relay to surface element tail circuits might be better handled by 3GPP or WiFi, and the architecture ought to accommodate that.
  Extensions to Prox-1 coding, modulation, and frequency sets that would support other frequencies, modulations, and codes are already underway
  CCSDS has published standards for these WiFi and 3GPP tail circuits. They should be adopted where they will be useful.
A more complete description of a “DTN ecosystem” will need to address monitor, control, routing, coordination, security, multi-agency identities, and domain interoperability.
  In a multi-agency context some agreed methods of security, identity, network, and key management will surely be required
  Other considerations like governance, policies, integration with non-DTN missions, and last hop / first hop features also need to be addressed
  Frequency assignment and and use policies for Service User to Service Provider must be formulated and managed
In alignment with CCSDS document types this sort of interoperable architecture, which is intended to be directly implementable, would normally be documented as a Utilization Profile, which is a Blue Book.
An Orange Book, or Experimental Specification, could provide a rapid way forward to get the core concepts published in the short term, while the more complicated DTN ecosystem aspects are worked out.

## Slide 41: BACKUP

## Slide 42: Figure 7-11: SSI End-to-End Forward: DTN Agency Supporting ABA Agency, Including Last-Hop Service and CSTS Forward File
Earth-Space
Link Terminal
ABA Earth
User Node
ABA Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
SSI
VC Z
VC X, Y, & Z
UHF RF
Space Reboot
Processing
RF & Mod
IP
C & S
F-Frame
Mux F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
AOS/TC
BP
To
VC Z
IP
TCP
Space Routing Node MOC
SSI
To
VC X
User File Application
IP
BP
CFDP
TCP
Space Routing Node
SSI
UHF RF & Mod
Bundle Agent (Router/S&F)
ENCAP
BP
Prox-1 Link
RF & Mod
ENCAP
BP
LTP
C & S
AOS/TC
CFDP
Proximity Space
CCSDS Protocols
(UDD SAP)
ABA
ABA
User Forward
Delivery Package Application
TC
Blocks
Deliv.
Instr.
Link
Config.
F-File
CFDP
F-File
'Last-Hop'
Delivery Agent Application
TC
Blocks
Prox UDD
C & S
TCP
Prox UDD
C & S
TC
Blocks
VC X
VC Z
Notes: 12/12/12: Original PPT figure title: “: ABCBA ABA Agency supported by SSI Agency – “Last Hop” Commanding - Forward TC Coded Blocks” Title above is how the figure is labeled in the document.
42

## Slide 43: Figure 7-12: SSI End-to-End Return: DTN Agency Supporting ABA Agency, Including First-Hop Service and CSTS Return File
Earth-Space
Link Terminal
Earth User Node
Space User Node
Ground-Space
CCSDS Protocols
Terrestrial
WAN
SSI
VC Z
VC X, Y, & Z
RF & Mod
Safe Mode
Processing
RF & Mod
IP
C & S
R-CF
Mux F-Frame
Production
Bundle Agent (Router/S&F)
ENCAP
BP
LTP
AOS/TM
BP
From
VC Z
IP
TCP
Space Routing Node MOC
SSI
From
VC X
User File Application
IP
BP
CFDP
TCP
Space Routing Node
SSI
UHF
Bundle Agent (Router/S&F)
ENCAP
BP
Prox-1 Link
RF & Mod
ENCAP
BP
LTP
C & S
AOS/TM
CFDP
Space Link
CCSDS Protocols
ABA
ABA
User Return
Delivery Package Application
TM
Frames
Deliv.
Instr.
Link
Config.
R-File
CFDP
R-File
'First Hop'
Delivery Agent Application
TM
Frames
C & S
TCP
Eng
Eng
C & S
RF & Mod
C & S
AOS/TM
AOS/TM
EP or SP
VC Z
VC X
Notes: 12/12/12: Original PPT slide title is “ABCBA ABA Agency supported by SSI Agency – “First Hop” Return TM Essential Telemetry; however, the actual figure title is what is shown here.
43

## Slide 44: Figure 6-15: Last-Hop Delivery Package Structure
BCH Code Block
BCH Code Block
BCH Code Block
Use Proximity-1 UDD SAP
Configure Proximity Link
On Next Possible Pass
Extract BCH Code Blocks
Transmit until ACK Received
Delivery metadata include:
  instructions on:
    when to provide the service (if required);
    how to configure the last-hop link (UDD or packet SAP);
    how to extract data (data structures);
    how to deliver the data (once, continuously);
    when to terminate (# of retries, time out, signal);
  Configuration of the last-hop link, mode, data rate, other parameters.
Data to be delivered:
  could be telecommand frames, BCH code blocks, space packets, AOS frames, or other well-defined link artifacts.
  UDD = User-Defined Data
  SAP = Service Access Point
  BCH = Bose, Chaudhuri, Hocquenghem
Notes: I had to do a call-out for UDD here, since the call-out doesn’t show up until section 7 in the document.
I’ve adjusted the colors to match the figures in 6-14 and 6-15, after this figure 4-7 was referenced section 6.5.3.
Don’t we need to be sure we don’t introduce new colors here w/o having them somehow referenced in figure 1-1?
BCH isn’t called out ANYWHERE in the document, and isn’t even referenced until section 5, so… what’s it stand for? We should insert the call-out in this figure.
SAP isn’t referenced until section 7 in the document; so it needs to be called out here as well. It’s not called out anywhere in the document.

## Slide 45: Figure 6-16: Data Exchanges for Forward Last-Hop and Return First-Hop Service
Forward
Return
Space User
Node
Space Routing Node
with Delivery Agent
Earth User
Node
Last-Hop Data Items
Service Report
Service Report
Last-Hop Data Items
Service Report
Service Report
Space User
Node
Space Routing Node
with Delivery Agent
Earth User
Node
Service Request
Service Request
Proximity Link Config.
Proximity Link Config.
Last-Hop Data File
Last-Hop Data File
Service Request
Service Request
Proximity Link Config.
Proximity Link Config.
Last-Hop Data File
Last-Hop Data File
ESLT
ESLT
Notes: Do these colors match ONLY the color scheme found in figure 1-1???

## Slide 46: Figure 6-17: End-to-End Generic Protocol for Forward Last-Hop Service
Uses standardized SSI relay processes & file handling
Uses Space Internetworking between Lander MOC and the Last-Hop delivery agent
Adopts standardized Last-Hop Delivery Agent on orbiter
SLE is still used “under” SI protocols on the Orbiter MOC to ground station path to establish the Ground Station to Orbiter link
NOTE: Orbiter MOC may be an SSI node, but it may not handle or route all of the data, see Ground Support study for details
Last hop delivery agent may also support legacy missions, not just emergency
Last-Hop Delivery
Agent
LH App = Last-Hop Application
SI = Space Internetwork
SI
SI
Space Routing
Node
Space Routing
Node
ESLT
Link
Application Data Transfer #2
Terrestrial Internetwork
User LH
App
Link-Layer
App
Link
Link
Link
CFDP
Earth User
Node
Space User Node
SI
Space Link Extension
Space Link 1
Space Link 2
Application Data Transfer #1
CFDP
SI
SI
Notes: 12/30: What’s “LH” in the orange box at the upper right?? I don’t want to assume it’s “last hop,” since the box’s info doesn’t match up to the other orange box’s info.

## Slide 47: Figure 6-32: Last-Hop Delivery Package Assembly
User Forward
Delivery Package Application
IP
TCP
CSTS Transfer File
Files
Space
Packets
Direct
TC Frames
Delivery
Instructions
Link
Configuration
ABA Last-Hop Delivery Package Assembly and CSTS Transfer-File Delivery
Notes: 7/12: made minor adjustments to spacing.//cys